Europa Surface Radiation Environment for Lander Assessment

John F. Cooper

Space Physics Data Facility, Code 612.4, Laboratory for Solar and Space Physics

NASA Goddard Space Flight Center

8800 Greenbelt Road, Greenbelt, MD 20771

U.S.A.

John.F.Cooper@nasa.gov

Steven J. Sturner

USRA, Code 661.0, Astroparticle Physics Laboratory

NASA Goddard Space Flight Center

U.S.A.

The Jovian magnetospheric particle environment at Europa’s surface is critical to assessment of landed astrobiological experiments in three respects: (1) the landing site must be chosen for the best prospects for detectable organic or inorganic signs of life, e.g. regions of freshly emergent flows from the subsurface; (2) lander systems must reach the surface through the Jovian magnetospheric environment and operate long enough on the surface to return useful data; (3) lander instrumentation must be capable of detecting signs of life in the context of the local environmental radiation and associated chemistry. The Galileo, Voyager, and Pioneer missions have provided a wealth of data on energetic particle intensities throughout the Jovian magnetosphere including from many flybys of Europa. Cumulative radiation dosages for spacecraft enroute to Europa can be well characterized, but knowledge of the surface radiation environment is very limited. Energetic electrons should primarily impact the trailing hemisphere with decreasing intensity towards the center of the leading hemisphere and are the most significant radiation component down to meter depths in the surface regolith due to secondary interactions. Observed surface distribution for sulfates is suggestive of electron irradiation but may have alternative interpretations. Having much larger magnetic gyroradii than electrons, energetic protons and heavier ions irradiate more of the global surface. The particular orientations of electron, proton, and ion gyromotion would project into corresponding directional (e.g., east-west) anisotropies of particle flux into the surface. Particular topographic features at the landing site may therefore offer shielding from part of the incident radiation.