| NWS FORM E-5 U.S. DEPARTMENT OF COMMERCE NOAA, NATIONAL WEATHER SERVICE MONTHLY REPORT OF RIVER AND FLOOD CONDITIONS TO: NATIONAL WEATHER SERVICE HYDROMETEOROLOGICAL INFO CENTER, W/OS31 SSMC 2 – Room 13468 1325 EAST-WEST HIGHWAY SILVER SPRING, MD 20910-3283 | HSA OFFICE: LINCOLN, ILLINOIS |
| --- | --- |
|  | REPORT FOR (MONTH / YEAR): January 2005 |
|  | DATE: February 16, 2005 |
|  | SIGNATURE: Daniel F. Smith – HPM Dan Kelly – Asst HPM |
| When no flooding occurs, include miscellaneous river conditions, such as significant rises, record low stages, ice conditions, snow cover, droughts, and hydrologic products issued (NWSPD 10-9). |

All river forecast points in the central Illinois HSA reached or exceeded Flood Stage during the month of January 2005. These rivers include:

Illinois River:		Henry (HNYI2), Peoria(PIAI2), Havana (HAVI2) and Beardstown (BEAI2)

Spoon River:		London Mills (LNMI2) and Seville (SEVI2)

Mackinaw River:	Congerville (CNGI2)

Salt Creek:		Greenview (GREI2)

Sangamon River:	Monticello (MNTI2), Riverton (RVTI2), Petersburg (PETI2) and Oakford (OKFI2)

Kaskaskia River:	Shelbyville Dam (SBYI2)

Vermilion River:	Danville (DNVI2)

Little Wabash River:	Clay City (CLAI2)

Embarras River:	Ste Marie (STMI2) and Lawrenceville (LAWI2)

In addition…the southeastern part of the Central Illinois Forecast Area (KILX CWA) was significantly impacted by flooding along the Wabash River (eastern parts of Clark, Crawford and Lawrence Counties).

January 2005 was a very busy month in the hydro department across the Central Illinois (KILX) Hydrologic Service Area. Temperatures during January 2005 were 4 to 6 degrees above normal, and precipitation was up to 4.5 inches above normal! In fact, it was the 2nd wettest January on record in Lincoln (Jan 2005 precipitation = 6.18”…Departure from normal = +4.48”) and the 3rd wettest on record in Urbana (Jan 2005 precipitation = 6.20”…Departure from normal = +4.31”). Some stations in the southeastern part of the Central Illinois HSA received over 9 inches of precipitation during the month! (The Jan 2005 Precipitation in: Hidalgo (Jasper Co) = 10.07”, Palestine (Crawford Co) = 9.43”, Effingham SE (Effingham Co.) = 9.29” and Flora 5NW (Clay Co) = 9.27”)

A nearly stationary frontal boundary remained in the vicinity of central Illinois for the first week of the new year. This front marked the boundary between warm, very moist air to the south, and very cold air to the north. This warm and moist air fueled showers, and even some thunderstorms, across the Central Illinois HSA, especially across southeastern Illinois. In the 5 day period between Jan 2nd and the 6th, many stations picked up well over half their monthly rainfall (see jan02-06 05rain.gif). Rivers across eastern and southeastern Illinois responded quickly to all of this rain. The Sangamon River in Monticello went above flood stage on the 5th and crested nearly 2 feet above flood stage (13 feet) at 14.94 feet on the 7th. In Danville, the Vermilion River crested just barely above flood stage (18 feet) at 18.05 feet on the 6th. The Embarras River also responded quite rapidly to this rainfall. In Ste Marie (FS=19 feet), the river exceeded flood stage on the 5th, and crested nearly 5 feet above flood stage on the 7th. Two additional crests would take place in Ste Marie before the river finally fell below flood stage on the 17th. Further downstream in Lawrenceville, after going above flood stage (30 feet) on the 4th, the Embarras River finally crested 10.5 feet above flood stage, at 40.50 feet on the 9th. Pictures of the flooding in Lawrenceville on Jan 5th and 6th are available on the Lawrenceville Daily Record Website at: http://www.lawdailyrecord.com/main.asp?SectionID=30 . Unfortunately there was 1 fatality due to the river/flash flooding. A woman was swept away in her car, by flood waters, in the North Fork Creek near the Crawford/Jasper County Line. On the Little Wabash River, the Clay City Gauge (FS = 16 feet) shot up from 8 feet at 1145 UTC on the 3rd, to 18 feet by 2300 UTC on the 3rd. The Little Wabash River finally crested at 25.27 feet (the 6th highest crest on record) on the morning of the 7th.

On the 12th, a warm front lifted north through the central Illinois HSA. Very warm and moist air was transported into the state behind this front, with dew points in the middle to upper 50s. By the evening of the 12th, a strong cold front collided with this warm and moist air, as it slowly drifted across the state. Showers and thunderstorms erupted ahead of this front, and deposited 1 to 2 inches of rain and liquid equivalent precipitation across central and southeastern Illinois, with a swath of over 2 inches from Petersburg (Menard County) to Lincoln to Bloomington. (see 011305ilpcn.gif) This heavy rainfall, on already saturated ground, resulted in widespread flash flooding, and later river flooding, across the central Illinois Hydrologic Service Area. In fact, Flash Flood Warnings were issued for each one of the 35 counties in the KILX County Warning Area on the evening of the 12th and the morning of the 13th, as this heavy precipitation moved through the area. Numerous roads across central and southeastern Illinois were closed due to flood waters. Some of the more significant reports of flash flooding include: Car stalled on country road 2000N near Oblong (Crawford Co.), which was under 2 to 3 feet of water. US Route 150 west of Mahomet (Champaign Co.) was closed due to flowing water. West of Fisher (Champaign Co.), a half mile stretch of US Route 136 was under up to 2 feet of water. Near Newton, in Jasper County, water closed State Highway 33. Unfortunately there were 2 fatalities that were indirectly related to the flash flooding, a man (24) and his mother (45) were electrocuted in their flooded basement in Shirley (southwestern McLean County).

Very cold air poured into Illinois behind this strong cold front, resulting in a changeover from rain to snow. In addition, the cold air caused the flooded creeks, streams, farm fields and road ditches to freeze, turning much of central Illinois into an ice skating rink. The attached pictures were taken by Dan Smith (HPM at KILX) in Lawndale (northeast of Lincoln in Logan Co.). By the afternoon of the 13th, Clinton Lake (DeWitt County) was rising rapidly due to all of this water (normal stage at Clinton Lake is 690 feet), and there was concern that the Clinton Dam would be overtopped (The dam is overtopped at a height of 697 feet MSL). A failure of this dam would result in the flooding of Illinois Route 10 just below the dam, as well as the Salt Creek in western Dewitt and southern Logan Counties. Lake Clinton came up to 695.5 feet (1.5 feet below the overtop stage) by 0130 CST on the 14th, before slowly receding. Downstream along the Salt Creek, the stage at Greenview began to rapidly fall, and there was some concern of a levee failure. After an emergency visit by NWS personnel, it was determined to be a gauge failure. The Greenview gauge was back on line later that day, however went out just as the river was about to crest, so the crest had to be estimated. Lake Shelbyville also rose to near record levels, and the US Army Corps of Engineers had to release slowly to get the lake down, and to prevent flooding in Shelbyville downstream. The Kaskaskia River crested right at flood stage on the 22nd. According to the US Army Corps of Engineers St. Louis District, the record level of Lake Shelbyville since it’s creation in 1971, was 620.26 feet on Jun. 29, 1974. The peak level of the Lake was 618.08 feet pm the 18th, just 2 feet below the record.

Across southeastern Illinois, the Wabash River climbed to record or near record levels as a result of heavy rainfall across Indiana. Although the Wabash River is not a part of the central Illinois Hydrologic Service Area, 3 of our counties border the river (Clark, Crawford and Lawrence). The flooding of the Wabash River required the evacuation of around 100 people from the town of Hutsonville (Crawford County). On the 14th at about 1630 CST, a levee breach was observed just north of Darwin, in eastern Clark County. Water from the Wabash River surrounded the towns of York and Darwin, and the only way to get to these towns was by boat. Residents of York and Darwin were encouraged to evacuate, however several residents remained in their homes. A major levee failure on the Indiana side of the Wabash River spared many communities on the Illinois side. According to the Robinson Daily News, the river came to within 9 inches of overtopping a levee in eastern Lawrence County.  Had this levee failed, extensive flooding would have occurred in parts of eastern Lawrence County. Flood waters washed out a bridge on Robinson-Marshall Road in Crawford County which will need to be completely replaced. Pictures of the flooding along the Wabash River are available on the Robinson Daily News internet site at: http://www.robdailynews.com/ . To get to the pictures, click on the yellow box on the right side of the window that states “New local photos  Browse and order here!”

Monthly Statement Summary

(CHIFLWILX) Flood Warnings - 45

(CHIFLSILX) Flood Statements - 220

(CHIRVSILX) River Statements - 14

(CHIESFILX) Hydrologic Outlooks - 3

(CHIESFILX) Snowmelt River Flood Outlook - 0

(CHIFFWILX) Flash Flood Warnings - 35

(CHIFFSILX) Flash Flood Statements - 15

(CHIFFAILX) Flood Watches – 27

Total January 2005 hydro Statements…359!!!!

CC: OHRFC NCRFC  W/CR2