# Beam Heating in the Accumulator

#### Valeri Lebedev

FNAL, May 13, 2002.

# Contents

- Heating mechanisms

- Review of gas scattering

- Review of IBS theory

- Comparison of the theory with experimental data

- Conclusions

Heating Mechanisms

  - Scattering on residual gas

    - Dominates at small beam current

  - Intrabeam scattering (IBS)

    - Presently is major heating mechanism at high current (~100 mA)

  - Non-linear resonances

    - Tunes should not be to close to resonances. Harmful effects of resonances (up to 18-th order) have been observed

  - Instabilities

    - An instability driven by ions originated from the residual gas heats the beam at currents above ~20 mA

  - Noise on electrodes

    - We do not have any evidence of beam heating due to noise on electrodes

# Scattering on the residual gas

Beam lifetime

where

- Total beam lime time measured with low intensity protons   ~1400 hour

- Coulomb scattering ~2800 hour

- Nuclear absorption ~2700 hour

Emittance growth rate is closely related to the beam life time

Presuming that the relative gas composition is proportional to a single point measurement performed 2 years ago we obtain the vacuum and the emittance growth rates

- Measured minimum vertical emittance growth time coincides well with the calculations

- The horizontal one is usually above predictions and grows fast with beam current

Twiss parameters for the old and new accumulator lattices

# Intrabeam scattering theory

If in the beam frame the longitudinal momentum spread is much less than the transverse one the IBS formulas can be significantly simplified

##### The IBS growth rate for longitudinal degree of freedom

- IBS transfers the energy from the transverse degrees of freedom to the longitudinal one and the growth rate can be approximated by the following formula

,

where averaging is performed along the beam orbit,

,

Lc - is the Coulomb logarithm,

C – is the ring circumference,

the beam sizes and local angular spreads along the ring are determined by

and

##### The IBS growth rate for transverse degree of freedom

- The heating of the longitudinal degree of freedom causes cooling for both transverse degrees of freedom;

- Additional mechanism heats the horizontal degree of freedom

  - At regions with non-zero dispersion, changes in the longitudinal momentum change the particles reference orbits, which additionally excites the horizontal betatron motion,

,

where

Coefficient ½ is related to the fact that the beam is unbunched

- Finally, one can write for the emittance growth rates

where

.

Comparison of the old and new accumulator lattices from the horizontal emittance growth rate due to IBS

Old lattice

New lattice

# Comparison with experiment

Protons, I.beam=13.5 mA, Lifetime = 1400 hour, beam is scraped from 100 mA, Apr.30.02

Antiprotons, I.beam=12.1 mA, Lifetime=900 hour, beam is scraped from 24 mA,Apr.30.02

- Green line shows the emittance growth from the gas scattering only

- X-Y coupling causes additional growth for vertical emittance, = 0.04

Beam scraping makes distribution non-Gaussian. It affects the growth rates but we do not have a clear answer how much

- Protons, I.beam=48.2 mA, Lifetime = 800 hour, Mar.26.02

Antiprotons, I.beam=50.8 mA, Lifetime = 650 hour, Mar.27.02

- Green line shows the emittance growth from the gas scattering only

- X-Y coupling causes additional growth for vertical emittance, = 0.04

- Presence of ions in the antiproton beam causes decrease of beam lifetime due to worsening of the effective vacuum and drives additional emittance growth due to ion instability

Antiprotons, I.beam=100 mA, Lifetime = 550 hour, Mar.27.02

Remarks about measurements and theory

- Both IBS and residual scattering are taken into account in the theoretical model

  - Both models have logarithmic accuracy with expected accuracy of about 10%

- IBS theoretical model is build for the Gaussian distribution function

  - It is not quite accurate for the proton beam and not always true for the antiproton beam

  - That brings additional uncertainty but it is difficult to say how much

- Longitudinal momentum spread for all presented date sets was fudged by factor of 1.15 to get coincidence between theory and measurements for the momentum spread growth rate.

  - Momentum spreads reported by A:SIGMAP and A:FRWDTH is different by ~40% and the are not always proportional to each other in the both cases of proton and antiproton beams

  - We need to investigate the reason of this discrepancies

Conclusions

- Vacuum lifetime in the Accumulator is about 1400 hours

  - Single intrabeam scattering (Touschek effect) affects the lifetime for both proton and antiproton beams

  - Ions stored in the antiproton beam cause additional drop of the antiproton lifetime

- In the absence of ion instability summed effects of the residual gas scattering and the IBS describe well the observed emittance growth rates

- In the case of antiproton beam the ions cause the two stream (ion-antiproton) instability above ~20 mA beam current.

  - The instability can be monitored at lowest (1-Q) betatron sideband.

  - This instability causes additional emittance growth comparable to the growth rate due to IBS

- We do not have any indications of the external noise causing the emittance growth

- We plan to change operation of the accumulator.

  - After stacking is completed the present optics (optimized for stacking) will be dynamically changed to the “low IBS optics”.

  - After about 30 min cooling the beam will be ready for extraction

- This optics change will bring

A decrease of the horizontal heating by more than two times, which, consequently, yields smaller beam emittances. Together with the core cooling upgrade we expect the emittance decrease by

  - Decreasing of beta-functions in the extraction aria additionally decreases beam size of the extracted beam and will prevent scraping at the beam extraction. Presently, we lose 5-10% at the beginning of the accumulator-to-MI beam line

- Ion instability is expected to be the major heating mechanism after new optics is introduced

# Text boxes

- Both lattices are not designed to have small IBS

- New lattice amplifies IBS by more than factor of two in comparison with the old one

|  | Old | New |
| --- | --- | --- |
| x[m] | 15.3 | 20.9 |
| y[m] | 13.4 | 12.5 |