SPECIAL SPECIFICATION

SECTION 05211

STEEL JOISTS

Page

PART 1 - GENERAL

1.01	Description Of Work 	2

1.02	Quality Assurance  	2

1.03  	Design	2

1.04	Delivery, Storage And Handling	 3

PART 2 - PRODUCTS

2.01	Materials	3

2.02	Fabrication 	4

PART 3 - EXECUTION

3.01	Erection 	 5

SPECIAL SPECIFICATION

SECTION 05211

STEEL JOISTS

PART 1 - GENERAL

1.01	DESCRIPTION OF WORK

A.	Extent of steel joists is shown on the drawings, including basic layout and type of joists required.

B.	Produce joists to configuration shown on Drawings.

1.02	QUALITY ASSURANCE

A.	Provide joists fabricated in compliance with the following, and as herein specified.

Steel Joists Institute (SJI) "Standard Specifications".

B.	Qualification of Field Welding.  Qualify welding processes and welding operators in accordance with American Welding Society AWS "Standard Qualification Procedure".

1.03	DESIGN

A.	Design special joists to safely support loading shown on Drawing 104740/A2.

B.	Special joists shall be designed in accordance with the provisions of the Amerian Institute of Steel Construction Manual of Steel Construction Allowable Stress Design, Specifications for Structural Steel Buildings, June 1989.

C.	Design shall be performed by a registered structural engineer and his seal shall appear on detail (shop) drawings and calculations.

D.	Detail drawings and calculations shall be submitted to Owner for review.

1.04	DELIVERY, STORAGE AND HANDLING

Deliver, store and handle steel joists as recommended in SJI "Specifications". Handle and store joists in a manner to avoid deforming members and to avoid excessive stresses.

PART 2 -- PRODUCTS

2.01	MATERIALS

A.	Steel.  Comply with SJI "Specifications".

B.	Unfinished Threaded Fasteners.  ASTM A 307, Grade A, regular hexagon type, low carbon steel.

C.	Steel Prime Paint.  Comply with SJI "Specifications".

2.02	FABRICATION

A.	General.  Fabricate steel joists in accordance with SJI "Specifications".

Fabricate special joists to configuration shown on Drawings.

Holes in Chord Members:  Provide holes in chord members where shown for securing other work to steel joists; however, deduct area of holes from the area of chord when calculating strength of member.

B.	Extended Ends.  Provide extended ends of joists where shown, complying with manufacturer's standards and requirements of design and applicable SJI "Specifications".

C.	Bridging.  Provide horizontal and diagonal type bridging for special joists according to design requirements and in compliance with SJI "Specifications".

Provide bridging anchors for ends of bridging lines terminating at walls or beams.

D.	End Anchorage.  Provide end anchorages to secure joists to adjacent construction complying with SJI "Specifications" and design requirements.

E.	Shop Painting.  Remove loose scale, heavy rust, and other foreign materials from fabricated joists and accessories before application of shop paint.

Apply one shop coat of primer paint to all steel joists and accessories, by spray, dipping, or other method to provide a continuous dry paint film thickness of not less than 0.50 mil.

PART 3 -- EXECUTION

3.01	ERECTION

A.	Placing Joists.  Do not start placement of steel joists until supporting work is in place and secured.  Place joists on supporting work, adjust and align in accurate locations and spacing before permanently fastening.

B.	Bridging.  Install bridging simultaneously with joist erection, before construction loads are applied.  Anchor ends of bridging lines at top and bottom chords where terminating at walls or beams.

C.	Field weld joists to supporting steel framework as indicated on drawings and in accordance with SJI "Specifications" for type of joists used.  Coordinate welding sequence and procedure with placing of joists.

D.	Touch-Up Painting.  Cleaning and touch-up painting of field welds, abraded areas, and rust spots of shop painting is included in Section 09900, which is hereby included in the contract documents via reference.

END OF SECTION