Project Number:  AW-2271

Contract Number:  TW-0663

November 4, 1994

SPECIAL SPECIFICATION

SECTION 07600

FLASHING AND SHEET METAL

Page

PART 1 - GENERAL

1.01	Job Conditions	2

1.02	Submittals	2

1.03	Product Delivery, Storage And Handling	2

PART 2 - PRODUCTS

2.01	Materials	2

PART 3 - EXECUTION

3.01	General	3

3.02	Fabrication And Installation	4

SPECIAL SPECIFICATION

SECTION 07600

FLASHING AND SHEET METAL

PART 1 - GENERAL

1.01	JOB CONDITIONS

Coordinate metal flashing and trim work with the installation of roofing, piping, blocking, nailing, framing at openings, curbs, and other adjoining and substrate work.

1.02	SUBMITTALS

A.	Samples:  Submit two 12" samples of formed metal products.  Submit full range of manufacturer's color samples for color selection.

B.	Manufacturer's Literature:  Copies indicating instruction for installation and shop drawings.

C.	Shop Drawings:  Submit shop drawings of flashing, sheet metal, and accessories showing layout, joining, profiles and anchorages.  Layouts at 1/4" scale, details at 3" scale.

D.	Provide manufacturer's 20 year warranty on prefinished coating.

1.03	PRODUCT DELIVERY, STORAGE AND HANDLING

A.	Store and handle all flashing and sheet metal items so as to prevent damage to edges and surfaces.

B.	Do not install damaged items.

PART 2 - PRODUCTS

2.01	MATERIALS

A.	General:  All materials used shall not contain asbestos fibers.

B.	Galvanized metal shall be commercial quality carbon steel sheets having no less than .20% copper content, hot dip galvanized to comply with ASTM A525, 1.25 oz., Commercial Class, gauge as shown or specified, or 24 gauge if not otherwise required.

C.	Factory finished cap flashing shall be custom formed in 8'-0" lengths minimum, with flared continuous front and back edge cleats.

D.	Materials used for fastenings, hangers, brackets, and similar usage shall be suitable for the purpose and compatible with adjacent materials.  Use only galvanized steel or corrosion resisting steel nails and screws for securing galvanized items.  For cleats and similar items, use the same material as used for the item being secured.

E.	Precoated metal shall meet manufacturer's requirements for Dry Film Thickness 0.85-1.05 mils; Pencil Hardness Test - F Pencil Hardness minimum; Cure Test; Adhesion Test; Flexibility Test; Class Test; and Color Uniformity.  Material shall also meet ASTM tests as follows:  Weatherometer Test ASTM D2244; Humidity Test - ASTM D2247; Salt Spray Test - ASTM B117; Pollution Resistance Test -ASTM D1308, Formability Test - ASTM D1737; and Impact Resistance Test -ASTM D2794.  Prefinished galvanized steel shall be coated with Kynar 500 finish, or equal.  Provide 20 year warranty.

F.	Flashing and Trim:  All steel brake form flashings/trim shall be factory formed in 24 gauge steel.

G.	Cap flashing chair (seat) shall be 20 ga. galvanized steel, as shown on drawings.

H.	Splice plate shall be 24 ga. steel minimum, of 11" long shaped to conform to the coping cover; prefinish all exposed edges to match coping.

PART 3 - EXECUTION

3.01	GENERAL

A.	Comply with applicable recommendations and details of the "Architectural Sheet Metal Manual" by SMACNA, except as otherwise shown or specified.

B.	Manufacturer's Recommendations:  Except as otherwise shown or specified comply with the recommendations and instructions of the manufacturer of the sheet metal being installed.  Separate dissimilar metals from each other by painting each metal surface in the area of contact with a heavy application of bituminous coating or by other permanent separation as recommended by the manufacturers of the dissimilar metals.  Provide for thermal expansion of running trim, flashing, and other items exposed for more than 15 feet continuous length. Maintain a watertight installation at expansion seams.  Locate expansion seams at 10 feet intervals, and two feet each side of corners and intersections.

3.02	FABRICATION AND INSTALLATION

A.	Fabricate and install work with lines and corners of exposed units true and accurate.  Form exposed faces flat and free of buckles, excessive waves and avoidable tool marks, considering the temper and reflectivity of the metal. Provide uniform, neat seams with minimum exposure of folder, welds, and sealant. Except as otherwise shown, fold back the sheet metal to form a hem on the concealed side of exposed edges.  Conceal fasteners and expansion provisions wherever possible in exposed work, and locate so as to minimize the possibility of leakage.  Cover and seal work as required for a watertight installation.  Provide cleat-type anchorage for metal flashing and trim wherever practical, arranged to relieve stresses from building movement and thermal expansion.  On vertical surfaces lap 2-piece flashings a minimum of three inches.  For embedment of metal flashing, flanges in roofing or composition flashing or stripping, extend flanges for a minimum of four inches embedment.

B.	Provide flashings at intersection of roofing materials with vertical surfaces, at projections through the roof, at curbs for roof mounted equipment, at terminal edges of roofing, and elsewhere as shown by the drawings.

C.	Installation of Parapet Cap Flashings:  Install manufacturer's standard anchor plates, cap flashing chairs and splice plates with the cap flashing snapped on the front anchor plate and screwed to the rear anchor.  Top of cap flashing shall slope front to back a minimum of 1/2".  Front and rear of cap flashing shall be a minimum of 3-1/2" in depth.  Width of cap flashing shall be sized to accommodate the wall construction with no greater than 5/8" variance.

D.	Installation of Mechanical Equipment Supports and Roof Curbs:  	Except as otherwise shown or specified, comply with the recommendations and instructions of the manufacturer.  Anchor to deck with 3/8" expansion or toggle bolts at 32" o.c. with a minimum of 2 per side, or as shown on the drawings.

E.	Clean all cap flashing and flashings according to manufacturer's directions.

END OF SECTION