Central Subway

San Francisco, California

(November 2004)

The San Francisco Municipal Railway (Muni) and the San Francisco County Transportation Authority (SFCTA) are planning the Central Subway project, a 1.7-mile extension of the Third Street light rail transit (LRT) line (currently under construction) from its termini at Fourth and King Streets, north under Market Street and into Chinatown.  Five stations would be constructed along the Central Subway alignment and four light rail vehicles would be purchased to augment the existing fleet.  The current Third Street LRT project extends 5.4 miles south from Fourth and King Streets along Third Street and Mission Bay Boulevard to the Bayshore Caltrain Station in Visitacion Valley.  Taken together, the Third Street LRT, scheduled to open in December 2005, and the Central Subway project would provide a continuous 7.1-mile light rail system serving the heavily transit-dependent communities of Bayshore and Chinatown.

The Financial District, Union Square, and Chinatown have a very high level of existing transit service.  Bus routes that serve the project corridor operate on two-minute headways during peak hours and typically carry passenger loads which are at or above capacity.  Currently, commuter rail passengers from the south must board these crowded buses or walk over a mile from the CalTrain Station to reach the San Francisco central business district (CBD).  The Central Subway project would provide high-capacity rail service, with 2.5-minute peak headways, to an area of San Francisco that has demand for transit which exceeds the extensive existing bus service.  Additionally, implementation of the Central Subway project would restore a continuous transportation link from the communities of Visitacion Valley, Bayshore, and South of Market (SOMA) area to Union Square and Chinatown that was lost when the Embarcadero Freeway was destroyed by the Loma Preita earthquake in 1989.   This restored connection is anticipated to improve transit service between these areas, accommodate redevelopment of SOMA, and serve large crowds attending events at the Moscone Center and SBC Park (home of the San Francisco Giants).

| Summary Description |
| --- |
| Proposed Project: | Light Rail Transit |
|  | 1.7 Miles 5 Stations |
| Total Capital Cost ($YOE): | $994.4 Million ($1,594.4 Million of combined |
|  | Central Subway and Third Street LRT) |
| Section 5309 New Starts Share ($YOE): | $762.2 Million (76.6%; 47.8% of combined projects) |
| Annual Forecast Year Operating Cost: | $24.6 Million |
| Ridership Forecast 2025: | 61,000 Average Weekday Boardings |
|  | 20,500 Daily New Riders |
| FY 2006 Finance Rating: | Medium |
| FY 2006 Project Justification Rating: | Medium-High |
| FY 2006 Overall Project Rating: | Recommended |

Division H of the Consolidated Appropriations Act, 2005, includes language directing FTA to permit Muni to use local funding expended for the construction of the Third Street LRT project as match for the Central Subway.  This action reduces the overall New Starts share from 77 percent for the Central Subway project alone to less than 48 percent of the cost of the combined projects, and renders FTA’s rating of the project’s proposed New Starts share as inapplicable.

Project Development History and Current Status

In October 1996, FTA authorized the initiation of preliminary engineering and the preparation of a Draft Environmental Impact Statement (EIS)/Draft Environmental Impact Report for both the Third Street and Central Subway light rail lines.  Muni is currently constructing the Third Street light rail line project using local, State, and non-New Starts Federal funding.  In December of 2001, the Metropolitan Transportation Commission (MTC, the region’s metropolitan planning organization) adopted the Central Subway project into the region’s financially constrained long-range plan as a priority for future FTA funding.  Because of the different schedules for the Third Street light rail and the Central Subway, they are considered separate projects.   FTA approved the Central Subway project to advance into preliminary engineering in July of 2002.  Muni is currently examining alternative alignments which would extend the environmental review period and likely delay final design on the project until 2006.

Significant Changes Since Last Evaluation (November 2003)

The project capital cost has increased from $763.9 million to $994.4 million.  Muni’s financial plan has been updated to reflect the revised cost.  Additionally, Muni has refined the travel forecasts for the project, which includes the incorporation of improved results from the MTC’s and San Francisco County Transportation Authority’s travel demand models, as well as special events forecasts for SBC Park

Project Justification Rating: Medium-High

The project is rated Medium-High based on a Medium-Low rating for cost effectiveness and a High rating for transit-supportive land use.

Cost Effectiveness Rating: Medium-Low

The Medium-Low cost effectiveness rating reflects a sufficient level of travel-time benefits (9,700 hours each weekday) relative to the project’s annualized costs.   Muni is considering some significant changes to the project alignment and construction methodology, which places the current cost effectiveness estimate at some risk.

| Cost Effectiveness |
| --- |
| Cost per Hour of Transportation System User Benefit Incremental Cost per Incremental Trip | New Start vs. Baseline $22.45* $11.17 |

* Indicates that measure is a component of Cost Effectiveness rating.

The Central Subway provides a new direct transit link between the San Francisco CBD and southeastern San Francisco, and provides an improved connection between these areas and CalTrain and other commuter services from the region’s South Bay area.  Without the Central Subway, commuters from Mission Bay, Bayview, and the South Bay destined for Chinatown and Union Square must travel along the circuitous Embarcadero alignment to reach Market Street on the far eastern end of the CBD, or transfer to local bus service at King Street.  The proposed New Start provides a more direct connection to downtown and eliminates transfers for riders originating within the City; fully one-third of work trip benefits are attributable to this market.  The project also generates a significant level of travel time benefits for reverse commute trips to industrial areas in the Third Street corridor.  Approximately 85 percent of forecast benefits are attributable to San Francisco residents; the remainder of benefits accrue to residents from other jurisdictions in the region taking advantage of improved LRT connections to CalTrain and BART.  Over 40 percent of benefits accrue to low-income households.

The project’s revised capital cost estimate reflects a 30 percent increase in costs since last year.  While the estimate is improved, some uncertainties continue to exist.  Muni is considering various horizontal and vertical alignment options under 3rd or 4th Street, with either a deep or shallow tunnel, which, if advanced, would result in a revised estimate of project costs, ridership, travel time benefits, and cost effectiveness.

Transit-Supportive Land Use Rating: High

The High land use rating is based upon the High ratings assigned to existing land use and performance of land use policies, and the Medium-High rating for transit-supportive land use plans and policies.

Existing Land Use: High

- Population density is approximately 35,300 people per square mile, and total employment in the corridor is over 250,000 jobs.

- The San Francisco CBD is the densest and most transit accessible downtown on the west coast.  Union Square is the primary retail district in the city with dense pedestrian and transit-oriented development.  Chinatown has extremely dense concentrations of residential units, retail, and some office and small-scale industrial uses.

- Available parking in the corridor is generally on-street, with some off-street parking for commuters and city-owned parking garages for commuters and shoppers.  The daily cost to park in city-owned lots in the corridor is high, ranging from $20 to $30 per day.

Transit-Supportive Plans and Policies: Medium-High

- While the city and entire Bay Area have a number of physical constraints to growth such as topographical limitations, it does not have a unified or enforceable growth management policy.

- San Francisco’s General Plan has long encouraged higher-density and transit-oriented development.  The city is undertaking additional planning initiatives to focus higher-intensity growth in transit corridors. The city is considering zoning changes that would require residential community-oriented retail development near transit nodes.

- The city’s zoning regulations are intended to maintain a medium to high-density profile and scale, with a mixture of land uses in many areas.  The city’s plan generally supports transit-supportive densities. There are no minimum parking requirements or off-street parking provisions in the CBD and other major employment areas.

- The City of San Francisco Redevelopment Agency employs a number of special tools to help implement land use policies contained in the city’s General Plan such as tax increment financing, special land acquisition rules, and special land assembly abilities.

- San Francisco’s existing land use pattern includes the densest development along its major transportation corridors.  The objective of the City Planning Department and directing codes and ordinances is to reinforce this pattern of development along corridors that have high transit capacity such as the Central Subway corridor.  Thus, land use planning in the Central Subway corridor is focused more on the corridor and neighborhood level than around individual stations or stops.

Performance and Impacts of Policies: High

- The existing high-density development and pedestrian accessibility in the City of San Francisco demonstrates the strength of city policies and market forces at achieving transit-oriented intensities and urban design.  The number of jobs in the San Francisco CBD has doubled since the 1970s with no increase in the volume of traffic entering the area.

- The South of Market area within the New Central Subway corridor is expected to experience strong growth over the next two decades, with high density residential, high-tech office, and a variety of retail uses continuing to fill in sites formerly occupied by industrial uses.

Other Project Justification Criteria

| Mobility Improvements Rating: High |
| --- |
| Within ½-mile radius of boarding areas: Existing Employment Projected Employment (2025) Low Income Households (% of total HH) Average Per Station: Employment Low Income Households Transportation System User Benefit Per Project Passenger Mile (Minutes) | 254,500 268,700 6,000 (18%) 50,900* 1,200* New Start vs. Baseline 4.30* |
| Environmental Benefits Rating: High |
| Criteria Pollutant (Reduction in tons) Carbon Monoxide (CO) Nitrogen Oxide (NOx) Volatile Organic Compounds (VOC) Particulate Matter (PM10) Carbon Dioxide (CO2) Criteria Pollutant Status Carbon Monoxide 1-Hour Ozone (O3) 8-Hour Ozone Annual Energy Savings (million British Thermal Units) | New Start vs. Baseline 1 9 3 0 429 EPA Designation Maintenance Area* Other * Marginal Non-Attainment Area* 4,079 |
| Operating Efficiencies Rating: Medium |
| System Operating Cost per Passenger Mile (current year dollars) | Baseline $0.736* | New Start $0.753* |

* Indicates that measure is a component of rating for each criterion.

N/A indicates information was not available for this entry.

# Local Financial Commitment Rating: Medium

The Medium rating is based upon the Medium ratings assigned to both the capital and operating financial plans.

Section 5309 New Starts Share of Total Project Costs: 77%

Rating: Not Applicable

Division H of the Consolidated Appropriations Act, 2005, permits Muni to use non-New Starts funds expended for the Third Street LRT project as match to the Central Subway.  This lowers the non-New Starts share of project costs from approximately 77 percent for the Central Subway project alone ($994.4 million) to approximately 48 percent of the total costs of the combined Third Street/Central Subway project ($1,594.4 million).  However, due to the Appropriations Act provision, the New Starts share of project costs is not applicable to FTA’s rating process.

| Locally Proposed Financial Plan |
| --- |
| Source of Funds | Total Funds ($million) | Percent of Total |
| Federal: Section 5309 New Starts STIP Funds | $762.2 $92.2 | 76.6% 9.3% |
| State: Traffic Congestion Relief Plan | $14.0 | 1.4% |
| Local: Proposition B/K Sales Tax Funds | $126.0 | 12.7% |
| Total: | $994.4 | 100.0% |

NOTE:  The financial plan reflected in this table has been developed by the project sponsor and does not reflect a commitment by DOT or FTA.  The sum of the figures may differ from the total as listed due to rounding.

*STIP funds are state-administered Federal flexible funds augmented by state gas tax and other revenues.  These funds are passed from the state to local transportation agencies as STIP funds, but all Federal requirements apply.

# Capital Finance Plan Rating: Medium

The capital finance plan is rated Medium, based upon the average of the ratings assigned to each of the subfactors listed below.  The commitment of capital funds subfactor was rated High; agency capital condition was rated Medium-High; plan completeness was rated Medium; and the remaining subfactors were rated Medium-Low.

#### Agency Capital Condition: Medium-High

- The average age of Muni’s bus fleet is 3.8 years, which is significantly younger than the industry average.

- The agency’s good bond ratings, which were issued in May 2004, are as follows: Moody’s Aa3, Standard & Poor’s AA, and Fitch AA-.

#### Completeness of Capital Plan: Medium

- The submission was generally complete but lacked a sensitivity analysis and information regarding the project’s very modest financing costs.

#### Commitment of Capital Funds: High

- A majority (60 percent of the Central Subway only; 89 percent of the combined project) of the non-New Starts funding has been committed.

#### Capital Funding Capacity: Medium-Low

- The project’s financial plan shows projected cash balances, reserve accounts, and/or access to credit that would allow Muni to cover cost increases or funding shortfalls equal to approximately 10 percent of project costs.

#### Capital Cost Estimate and Planning Assumptions: Medium-Low

### The assumed inflation rate is considered optimistic, while project contingencies are small.

- Muni is currently reviewing alternatives to the project’s current alignment along 3rd Street, placing the current cost estimate at some risk.

#### Operating Finance Plan Rating: Medium

The operating finance plan is rated Medium, based upon the averaged ratings of the five subfactors listed below.  All subfactors were rated Medium except for completeness, which was rated Medium-High.

#### Agency Operating Condition: Medium

- Muni is in average operating condition, having weathered a challenging economic environment with limited or no service cuts and the requirement to balance its budget.

- Muni’s current ratio of assets to liabilities as reported in its most recent audited financial statement is 1.42, which is considered good.

#### Completeness of Operating Plan: Medium-High

- The operating plan contains a moderate level of detail and a sensitivity analysis.  The main weakness is the plan’s failure to identify which of the possible funding source(s) will support the project’s small incremental increase in operating costs.

#### Commitment of Operating Funds: Medium

- Over 25 percent of operating funding is committed.  The main revenue sources are fares, parking fees, General Fund contributions, and sales tax and fuel assistance revenues.

#### Operating Funding Capacity: Medium

- The project’s financial plan shows projected cash balances, reserve accounts, and/or access to credit exceeding 12 percent of annual operating expenses.

#### Operating Cost Estimates and Planning Assumptions: Medium

- The rating is a balance between the plan’s assumption of frequent fare increases that differ from history and the minimal of the line on operating costs and Muni’s extensive light rail operations experience.

Map