Interagency Trail Data Standards (ITDS) Version 2

Trail Planning and Management Fundamentals

Trail Type  ( Trail Class ( Managed Use (  Designed Use

Updated:  1/2004

Note: The management concepts incorporated in the ITDS Trail Fundamentals are currently undergoing public notice and comment via the Federal Register under the leadership of the US Forest Service. Once this is complete and the final version published in the Federal Register, the ITDS Trail Planning and Management Fundamentals will be revised as needed to reflect the final published version of these management concepts. (August, 2007)

The Interagency Trail Fundamentals include four fundamental concepts that are cornerstones of effective trail planning and management:

Trail Type

Trail Class

Managed Use

Designed Use

Although not entirely new, these interagency concepts provide an integrated means to consistently record and communicate the intended design and management guidelines for trail design, construction, maintenance and use.

Trail Type

A fundamental trail category that indicates the predominant trail surface or trail foundation, and the general mode of travel the trail accommodates.

Trail Types are exclusive, that is there can only be one Trail Type assigned per trail or trail segment.  This allows managers to identify specific trail Design Parameters (technical specifications), management needs and the cost of managing the trail for particular uses and/or seasons by trail or trail segment.

When one Trail Type “overlaps” another, identify each trail or trail segment with its respective Trail Type as a separate route, with its own Trail Name and Trail Number.  The ITDS “Shared System” data attribute will allow you to flag the route as also being used as a different type of route or Trail Type, (presumably during a different time of the year).  For example, Canyon Ridge Trail 106 may be categorized as a Standard/Terra Trail from MP 0.0 to its end termini at MP 7.4.   The first three miles of that same route may also function as a Snow Trail during the winter, in which case a separate record would be established for Canyon Creek Snow Trail #206 from MP 0.0 to MP 3.0.  The actual naming and numbering of trails (i.e. Standard/Terra Trails versus Snow Trails) should be consistent with local unit identification protocols.

The three fundamental Trails Types include:

Standard/Terra Trail:  The predominant foundation of the trail is ground (as opposed to snow or water); and that is designed and managed to accommodate ground-based trail use.

Snow Trail:  The predominant foundation of the trail is snow (as opposed to ground or water); and that is designed and managed to accommodate snow-based trail use.

Water Trail:  The predominant foundation of the trail is water (as opposed to ground or snow); and that is designed and managed to accommodate trail use by water craft.  There may be ground-based Portage segments of Water Trails.

Trail Class

The prescribed scale of trail development, representing the intended design and management standards of the trail.

There is only one Trail Class identified per trail or trail segment.

The National Trail Classes provide a chronological classification of trail development on a scale ranging from Trail Class 1 to Trail Class 5:

Trail Class 1:  Minimal/Undeveloped Trail

Trail Class 2:  Simple/Minor Development Trail

Trail Class 3:  Developed/Improved Trail

Trail Class 4:  Highly Developed Trail

Trail Class 5:  Fully Developed Trail

Each Trail Class is defined in terms of applicable Tread and Traffic Flow, Obstacles, Constructed Feature and Trail Elements, Signs, Typical Recreation Environment and Experience.

Trail Class descriptions define “typical” scenarios or combined factors, and exceptions may occur for any factor.  In applying Trail Classes, choose the one that most closely matches the managed objective of the trail.

Trail prescriptions describe the desired management of each trail, based on  land management plan direction.  These prescriptions take into account actively managed trail uses, user preferences, setting, protection of sensitive resources, and other management activities.  To meet prescription, each trail is assigned an appropriate Trail Class.

There is a direct relationship between Trail Class and Managed Use (defined below), and one cannot be determined without consideration of the other.

These general categories can be used to identify applicable construction and maintenance specifications and to identify basic indicators used for determining the cost to meet national quality standards.

Managed Use

Modes of travel that are actively managed and appropriate, considering the design and management of the trail.

There may be more than one Managed Use per trail or trail segment.

Managed Use indicates a management decision or intent to accommodate and/or encourage a specified type of trail use.

Designed Use

The intended use that controls the desired geometric design of the trail, and determines the subsequent maintenance parameters for the trail.

There is only one Designed Use per trail or trail segment.

Although the trail may be actively managed for more than one use, and numerous uses may be allowed, only one use is identified as the critical design driver.  The Designed Use determines the technical specifications for the design, construction and maintenance of the trail or trail segment.    For each Designed Use and applicable Trail Class, a corresponding set of standardized construction and maintenance specifications or Design Parameters can then be identified and applied.

Of the actively Managed Uses that the trail is developed and managed for, the Designed Use is the single design driver that determines the technical specifications for the trail.  This is somewhat subjective, but the Designed Use is most often the Managed Use that requires the highest level of development.  (ie: Pack & Saddle stock require higher and wider clearance than a trail designed for Hikers).  In addition to Designed Use, managers must also determine the desired development scale or Trail Class, with Trail Class 1 being the lowest level of development and Trail Class 5 the highest.  On a Trail Class 1 Hiker trail, the trail is basically a deer path and in places may disappear and be reacquired later. Trail Class 5 is most often paved, or at least hardened, and is associated with a highly developed Recreation Opportunity Spectrum classification (ROS).

Designed Use / Managed Use Types

All Terrain Vehicle

Snow All Terrain Vehicle

Bicycle

Dogsled

Hiker / Pedestrian

Motorcycle

Pack and Saddle

Snowmobile

Snowshoe

Watercraft

Motorized Watercraft

Non-Motorized Watercraft

Cross Country Ski