# Appendix A

# Blaster Training Requirements § 850.13(b)

The following is a list of potential  topics to be covered in blaster training and testing based of the Federal rules.

1(i)  Explosives – selection of type to be used

- ANFO

- Emulsions

- Cast Primers

- Blends 25/75  50/50  75/25

- Detonating Cord

- Initiators

- Dynamite

- Pre-split

1(ii)  Explosives – determination of the properties which will produce desired results at an acceptable level of risk

- Water Resistance

- Gas Pressure (Detonation)

- Detonation Velocity

- Sensitivity

- Coupling

- see IC 8925

- Density

- Fume class

- Sensitiveness

- Relative Bulk strength

1(iii)  Explosives – handling, transportation, and storage

- MSHA Rules

- ATF

- US DOT

- Possessor License

- RESPA Registration

- Internal Controls/ Accountability

- Vehicle requirements

- Magazine requirements

- Handling requirements

2(i)  Blast designs – geologic and topographic considerations

- Rock Type

- Rock Integrity

- Structure/Dip

- Fractures

- Voids

- Phreatic Surfaces

- Outcrops

- Drilling – Logs

- Equipment requirements

- Overburden type, amount and placement

- Steepness of slope

- Old mine works

- Auger holes

2(ii)  Blast designs – design of a blast hole, with critical dimensions

- Site Selection

- Burden

- Stemming

- Spacing

- Depth

- Sub Drill

- Decking

- Geology

- Explosive Column

- Hole diameter

- Deck stemming

- Bench Height to burden ratio

- Air decks

- Drill selection

- Angle holes

- Guide holes / line drilling

- Powder factor

- Loading factor

2(iii)  Blast designs – pattern design, field layout, and timing of blast holes

- Drill Patterns

- Location Holes (Tapes, Surveys, GPS)

- Chevron, Echelon, Square, Row by Row

- Left, Box-Cuts, Presplit, Coal, Conventional, Cast

- Timing – Rock Response Time

- Delay Intervals

- Cushion blasting

- Left Lift (sinking, center pull, drop cut, sump shot)

- V-Cut

- Adverse effects to expect (pros and cons) and address different

- Terminology for the different types

- Contour

- Pattern Layout Methods

- Step Benches

- Binder / Inner Burden / Parting Shots

- Face Velocity

- Boulders (block holing / mud capping)

- Air Gapping

- Bench Preparation

2(iv)  Blast designs – field applications

- Keeping blasts inside permit area

- Keep within blast area

- Blast for equipment type

- Sediment Ponds

- Haul Roads

- DO NOT – rock in culvert or stuck silos

- Reclamation

- Secondary Blasting

- Nearest Protected Structures

- Design Application

- Coal Blasts

- Confinement of Material

- Confinement Factors

- Burden Pole / Laser Profiler

- Free Face Conditions

- Hole Deviation

# Loading blastholes, including priming and boostering

- Review Drill Logs

- Communication with Driller

- Direct vs. Indirect (Primer Location)

- Taping the Holes

- Decking

- Boosters – When and Where

- Primer Makeup

- Primer Diameter – Optimum

- Primer Location

- Size of Primers

- Stemming Material / Type

- Selection of Primer

- Tamping Methods and Applications

- Secondary Priming (Insurance)

- Auger vs. Re-Pump

- Loading Methods

- Bulk Bag

# 4  Initiation systems and blasting machines

Initiation Systems

- Electric (Electronic)

- Non-electric

  - Det. Cord

  - Shell Tube

- Energy Distribution

- Delay Types

- Lead-in Line

- Remote / Wireless Systems

- Site-Specific Conditions

- Pros and Cons of Applications

- Circuit Testing Methods

- Failure Mode Analysis and Prevention

- Electricity

Blasting Machines

- Plunger

- Twister

- Capacitor Discharge

- Sequential

- Cap Fuse

- Shot Gun Primer

5.  Blasting vibrations, airblast, and flyrock

- ISEE “Field Practice Guidelines for Blasting Seismographs”

- Capability of the machine / interpretation of the data

- Utilization of Data

- Documentation and Proper Location Based on Conditions

- Scale Distance Calculations

- Frequency Determination

- Ground Vibration Prediction and Limitations

- Waveform Interpretation – Blast Identification

- Weather Effects

5(i)  Blasting vibrations, airblast, and flyrock – monitoring techniques

Flyrock Monitoring

- Video

- Photographs

- Evaluation Tools (Seismogram)

- Post Blast inspections

Ground Vibration Monitoring

- Sensor placements/coupling

- Sensor location

- Blasting Seismograph

  - Record duration and calibration

  - Trigger levels

  - Waveforms

  - Frequency

Airblast Monitoring

- Microphone placement

- Microphone location

5(ii)  Blasting vibrations, airblast, and flyrock – methods to control adverse affects

Flyrock - Methods to Control

  - Require Drill Logs

  - Laser Profile Face / Burden Poles

  - Stemming Type, Amount, Delivery, and Placement

  - Proper Shot Performance Documentation

  - Bench Height to Burden Ratio

  - Shot Size

  - Powder Factor

  - Face Orientation

  - Unconsolidated Material

  - Matting / Backfill / Burming

  - Confinement

  - Partial Misfires

  - Geology

  - Hole Deviation

  - Timing

  - Explosive Type

  - Pre-inspection of blast site

  - Excessive toe

  - Back break

  - Weathered surface rock

Ground vibrations - Methods to Control

- Rules

- Distance/Charge weight

- Confinement

Airblast - Methods to Control

- Rules

- Distance/Charge weight

- Stemming type

- Initiation system

- Decking weak zones

# 6  Secondary blasting applications

- Big rocks into small rocks

- Airblast/Flyrock

- Mud Capping/ Confinement

- Drilling

- Limit # of holes

- Cover with blast first

- Specialty products

- Other Options

  - RAM hoe

  - Headache ball

  - Jack hammer

# 7  Current Federal and State rules applicable to the use of explosives

- MSHA

- State specific information

- ATF

- OSHA

- EPA

- Placards (addressed by MSHA and in the ATF regulations)

# 8  Blast records

# Focus on:

- Location of blast

- Accurate sketch/Dimensions

- Distance reported

  - Closest hole in pattern to nearest corner of house

  - Calculating distances from blasts to homes with various coordinate systems (State plane, local, UTM, Lat-Long)

- Amount of explosive/Hole

- Timing/Sequence of detonation

- Seismograph location at house

- Initiation system

Other items:

- Name of operator conducting the blast

- Location, date, and time of the blast

- Name, signature, and certification number of the blaster conducting the

- blast

- Identification, direction, and distance in feet, from the nearest blast

- hole to the nearest dwelling, public building, school, church, community of institutional building outside the permit area, except those described in 816.67.

- Weather conditions, including those that may cause possible adverse

- blasting effects

- Type of material blasted

- Sketches of the blast pattern including number of holes, burden, spacing, decks, and delay pattern

- Show special relationship of blast site to surrounding area

- Freeface

- Resulting highwall

- North arrow

- Previous shot material (muck pile)

- Azimuth of primary freeface

- Diameter and depth of  holes

- Types of explosives used and amounts

- Total weight of explosives used per hole

- The maximum weight of explosives detonated in an e-millisecond period

- Initiation system

- Type and length of stemming

- Mats or other protections used

- Seismographic and airblast records, if required, which shall include

  - Type of instrument, sensitivity, and calibration signal or certification of annual calibration

  - Exact location of instrument and the date, time, and distance from the blast

  - Name of the person and firm taking the reading

  - The vibration and/or airblast level recorded

- Reasons and conditions for each unscheduled blast

- Detonator quantities

- Booster quantities

- Timing of the actual hole

- Delay time sequence

- Cap firing time

- Hole-to-hole and in-hole delays

- Explosive column / hole cross section

- Firing times

- Coal seam shooting down to

- 3-D location

- Direction to protected structures

- Exact location of blast and methods of obtaining location

- Document coordinates and method

- Use of a blasting map / pit map

- GPS

- Survey

- Record time (duration of the shot) for seismograph

- Site security measures

- Verification of what was done and the crew present for the shot

- In comments document misfires

- Seismograph operation should be documented

- Attach the printout from the seismograph if available

- Trigger levels of the seismograph

- Attach the full wave form printout

- Document the seismograph set up

- Label multiple pages with shot number and date or some unique number

# 9  Schedules

- Distribute annually

- Utilities, residents.

- Warning signals

- Mail to all within ½ mile of permit area

- Audible outside ½ mile of the blast

- Awareness of permit blast plan

- MSHA joint approvals with underground mines

- Include public safety – outdoor activity, school schedule, welfare considerations

- If beyond the blast schedule, list reasons and conditions in the blast record

- State specific regulations

- Optimum blasting times (nuisance awareness and annoyance)

- Safety considerations

- Atmospheric or weather conditions (fumes / dust)

- Wind direction and temperature

10 Preblasting surveys

- How to conduct surveys

10(i)  Preblasting surveys – availability

Letter (certified)

- ½ Mile of permit area

- Free to owner

- Get copy to owner

- Proof of offering

- Right of review/Comment

10(ii)  Preblasting surveys – coverage

- ½ Mile of permit area

10(iii)  Preblasting surveys – use of in-blast design

- Historic structures/ Sensitive structures

- Changing vibration limits

# 11  Blast-plan requirements

- Address all the performance standards 816.61-68 in permit

- Public safety issues

- Active underground mine issues w/ MSHA

- Public utilities – Consultation

- Recognize site-specific requirements

- Blast plan development

- Prepared by a certified blaster – state specific

# 12  Certification and training

- Rules

- State specific regulations and/or federal regulations

- Revocation

- Time frames

- Application fees

- Continuing education requirements

- Renewals

- What a certified blaster should be training the crew on – OJT

- Reinstatement

# 13  Signs, warning signals, and site control

Warning Signals

- Horns

  - Truck

  - Air

  - Bugle

  - Air compressor

- Conditions affecting audibility

  - Wind – direct

  - Atmospheric conditions

  - Ambient noises

- Adequate blast area

- Location – all access points

- Define responsible parties for each aspect

- Training of flag personnel

- Individual notification before each blast (phone or in-person)

- Public notification

- Communication methods for site security personnel

- Pre-project meeting with the mine

- Public roads

- ATV’s

14.  Unpredictable hazard including Lightening, Stray currents, Radio waves and Misfires

- Stray gas – CO, NOx

- Cell phones

- Lightening

- Stray currents

- Radio waves/RF

- Misfires

- Power lines

- Underground voids

- Gas wells/lines

- Radar sites (airport)

- Untrained helpers / assistants

- Recognition

- Ways to deal with them

- Avoidance

- Reporting

- Remedy