96M03/29/06

S101-96M.doc

Use on all projects.

Section 101. - TERMS, FORMAT, AND DEFINITIONS

101.02  Specifications Format.  Delete the third and fourth paragraphs and substitute the following:

Division 150 consists of project contract requirements that are applicable to all contracts.  Work under Division 150 is paid for directly or indirectly according to Subsection 109.05 and the Section ordering the work.  When there is no pay item in the bid schedule, no direct payment is made.

Divisions 200 through 600 consist of construction contract requirements for specific items of work.  Work under these Divisions is paid for directly or indirectly according to Subsection 109.05 and the Section ordering the work.

101.04  Definitions.

Suitable Material - Add the following:

Suitable material may necessitate drying, the addition of moisture, reduction in size, screening, or other common methods of manipulation prior to use.  Suitable material includes the classification(s) of materials, resulting R-values and other characteristics, for which the project was designed.

Unsuitable Material - Delete the text and substitute the following:

Material which the CO determines to be unsuitable for use in the construction of foundations, embankments, or roadbeds.  Unsuitable materials generally include muck and soils with high organic contents.