UNITED STATES ENVIRONMENTAL PROTECTION AGENCY

WASHINGTON, D.C.  20460

OFFICE OF

PREVENTION, PESTICIDES AND

TOXIC SUBSTANCES

July 27, 2006

Memorandum

SUBJECT:	TCMTB [2-(Thiocyanomethylthio)benzothiazole]: Second Revision of the Occupational and Residential Exposure Assessment for the Reregistration Eligibility Decision Document.

PC Code: 035603 (TCMTB)

DP Barcode: D324013

FROM:	Charles Smith

Reregistration Branch 2

Health Effects Division (7509C)

THROUGH:	Alan Nielsen, Senior Scientist

Reregistration Branch 2

Health Effects Division (7509C)

TO:		Kathryn Avivah Jakob, Chemical Review Manager

Regulatory Management Branch 2

Antimicrobials Division (7510C)

and

Deborah Smegal, Risk Assessor

Reregistration Branch 1

Health Effects Division (7509C)

The attached assessment is the occupational and non-occupational (residential) exposure and risk estimates for TCMTB to support the Antimicrobial Division’s reregistration eligibility decision (RED) document.  The assessment was reviewed by HED’s Science Council for Exposure (ExpoSAC) to ensure compliance with current HED policy as well as ExpoSAC standard operating procedures (SOPs) for conducting occupational and residential exposure (ORE) assessments.

Table of Contents

Executive Summary	4

1.0	Occupational and Residential Exposure/Risk Assessment	5

1.1	Purpose	5

1.2	Criteria for Conducting Exposure Assessments	5

1.3       Summary of Hazard Concerns for TCMTB	5

1.4	Incident Reports	8

1.5	Summary of Physical and Chemical Properties of TCMTB	8

1.6.1	End-Use Products	9

1.6.2	Registered Use Categories and Sites	9

1.6.3	Application Methods	9

2.0	Occupational Exposures and Risks	10

2.1	Occupational Handler Exposures and Risks	10

2.1.1	Data and Assumptions for Handler Exposure Scenarios	12

2.1.1.1	Assumptions for Handler Exposure Scenarios	12

2.1.1.2	Exposure Data for Handler Exposure Scenarios	13

2.1.2	Noncancer TCMTB Handler Exposure and Assessment	16

2.1.2.1	Noncancer TCMTB Handler Exposure and Risk Calculations	16

2.1.2.2	TCMTB Noncancer Risk Summary	17

2.1.3 	Cancer TCMTB Handler Exposure and Risk Assessment	22

2.1.4 	Summary of Risk Concerns/Data Gaps for Occupational Handlers	22

2.1.4.1	Summary of Risk Concerns	22

2.1.4.2	Summary of Data Gaps	22

2.1.5	Recommendations For Refining  Handler Risk Assessment	22

# Executive Summary

TCMTB is a broad spectrum biocide used in commercial and on-farm seed treatment settings.  It is formulated as a liquid concentrate.

Hazard Concerns:  The toxicological endpoints used to complete the occupational and residential risk assessment were based on the best professional judgment of AD toxicologists.  Adverse effects were identified at durations of exposure ranging from short-term (up to 30

days) to intermediate-term durations (> 30 days up to 6 months) and long-term durations (> 6 months).  No cancer endpoint was identified, therefore, cancer risks are not assessed.

The short- and intermediate-term (noncancer) dermal risk assessment for TCMTB is based on an NOAEL of 25 mg/kg/day from a dermal study.  The NOAEL was based on decreased body weight gain and food consumption in males, in addition to significant hematalogical (increased neutrophils, decreased hemoglobin, hematocrit and erythrocytes) and clinical chemistry changes (increased urea nitrogen, glucose and globulins).  Long-term exposures to TCMTB (i.e., greater than 6 months) are not expected for current registered uses.   HED’s level of concern (LOC) for occupational TCMTB dermal exposures is 100.  The short- and intermediate-term (noncancer) inhalation risk assessment for TCMTB is based on an NOAEL of 16 mg/kg/day, which is based on an oral rabbit development study.  The NOAEL was based on reduced body weight gain and food consumption.  Long-term exposure to TCMTB (i.e., greater than 6 months) is not expected for current registered uses.  HED’s level of concern (LOC) for short- and intermediate-term occupational (and residential) TCMTB inhalation exposures is 100.  The dermal and inhalation margins of exposure were combined for the TCMTB risk assessment because the toxicity endpoints for the dermal and inhalation routes of exposure are based on the same toxicological effects.

The Health Effects Division Carcinogenicity Peer Review Committee (CPRC) met on June 28, 1995 to discuss and evaluate the weight-of-the-evidence on 2-(Thiocyanomethylthio) benzothiazole (TCMTB) with particular reference to its carcinogenic potential.  The CPRC concluded that TCMTB should be classified as Group C - possible human carcinogen - and recommended that for the purpose of risk characterization, the Reference Dose (RfD) approach should be used for quantitation of human risk.  This was based on statistically significant increases in tumors in both sexes of the Sprague-Dawley rat: testicular interstitial cell adenomas in males and thyroid c-cell adenomas in females.

Use Patterns: TCMTB is a fungicide used for treating seeds in the United States.  It is used in commercial and on-farm settings.

Occupational Handler Risks:	For commercial and on-farm seed treatment scenarios, all dermal and inhalation MOEs met or exceeded the required uncertainty factor of 100 at some level of mitigation.  For commercial and on-farm seed treatment scenarios, all combined dermal and inhalation risks met or exceed the required uncertainty factor of 100 at some level of mitigation.

# 1.0	Occupational and Residential Exposure/Risk Assessment

## 1.1	Purpose

This document is the occupational and residential non-dietary exposure and risk assessment for TCMTB from its use as a fungicide.  In this document, which is for use in EPA's development of the Antimicrobials Division (AD) chapter of the TCMTB RED Document, EPA presents the results of its review of the potential human health effects of occupational and residential/non-occupational exposure to TCMTB.

## 1.2	Criteria for Conducting Exposure Assessments

An occupational and/or residential exposure assessment is required for an active ingredient if (1) certain toxicological criteria are triggered and (2) there is a potential for exposure to handlers (mixers, loaders, applicators) during use or to persons entering treated sites or exposed to vapors after application is complete.  Toxicological endpoints were selected for short- and intermediate-term dermal and inhalation exposures to TCMTB.  There is a significant potential for exposure in a variety of occupational agricultural and commercial seed treatment settings.  There are no residential uses currently registered for TCMTB.   Therefore, risk assessments are required for occupational handlers that can occur as a result of TCMTB use.

## 1.3    	Summary of Hazard Concerns for TCMTB

2-(Thiocyanomethylthio) benzothiazole (TCMTB) - Report of the Antimicrobials Division Toxicity Endpoint Selection Committee (ADTC).  M. McMahon and M. Centra dated January 12, 2006.

The toxicological endpoints used to complete the occupational and residential risk assessment were based on the best professional judgment of AD toxicologists.  Adverse effects were identified at durations of exposure ranging from short-term (up to 30 days) to intermediate-term durations (> 30 days up to 6 months) and long-term durations (> 6 months).  No cancer endpoint was identified, therefore, cancer risks are not assessed.

TCMTB is a fungicide where the use patterns can vary widely ranging from short-term through intermediate-term exposure durations.  As such, when the Antimicrobials Division Toxicity Endpoint Selection Committee (ADTC) evaluated the TCMTB hazard database, endpoints were selected to address the various durations of exposure.  TCMTB exposures are expected to occur only to occupational users.

Dermal Route (noncancer)

The short- and intermediate-term (noncancer) dermal risk assessment for TCMTB is based on an NOAEL of 25 mg/kg/day from a dermal study.  The NOAEL was based on decreased body weight gain and food consumption in males, in addition to significant hematalogical (increased neutrophils, decreased hemoglobin, hematocrit and erythrocytes) and clinical chemistry changes (increased urea nitrogen, glucose and globulins).  Long-term exposures to TCMTB (i.e., greater than 6 months) are not expected for current registered uses.

Inhalation Route (noncancer)

The short- and intermediate-term (noncancer) inhalation risk assessment for TCMTB is based on an NOAEL of 16 mg/kg/day, which is based on an oral rabbit development study.  The LOAEL was based on reduced body weight gain and food consumption.  Long-term exposure to TCMTB (i.e., greater than 6 months) is not expected for current registered uses.

Incidental Oral Route (noncancer)

The short- and intermediate-term (noncancer) incidental oral risk assessment for TCMTB is based on an NOAEL of 16 mg/kg/day, which is based on an oral rabbit development study.  The LOAEL was based on reduced body weight gain and food consumption.

Noncancer Level of Concern (LOC)

HED’s level of concern (LOC) for occupational TCMTB dermal and inhalation exposures is 100 (i.e., a margin of exposure (MOE) less than 100 exceeds HED’s level of concern).  The level of concern is based on a 10x for interspecies extrapolation and a 10x for intraspecies extrapolation.

Aggregation

The dermal and inhalation margins of exposure were combined for the TCMTB risk assessment because the toxicity endpoints for the dermal and inhalation routes of exposure are based on the same toxicological effects.

Cancer

The Health Effects Division Carcinogenicity Peer Review Committee (CPRC) met on June 28, 1995 to discuss and evaluate the weight-of-the-evidence on 2-(Thiocyanomethylthio) benzothiazole (TCMTB) with particular reference to its carcinogenic potential.  The CPRC concluded that TCMTB should be classified as Group C - possible human carcinogen - and recommended that for the purpose of risk characterization, the Reference Dose (RfD) approach should be used for quantitation of human risk.  This was based on statistically significant increases in tumors in both sexes of the Sprague-Dawley rat: testicular interstitial cell adenomas in males and thyroid C-cell adenomas in females.

Acute Toxicity

TCMTB is classified as category II for acute oral toxicity, category III for acute dermal toxicity, and category I for inhalation toxicity.  It is classified as category I for primary eye irritation potential and category II for primary skin irritation potential.  Results were positive for dermal sensitization.  The acute toxicity profile for TCMTB is presented in Table 1.

Body Weight

The adverse effects for the dermal and inhalation endpoint are observed in the general population.  Therefore, the body weight of an average adult (i.e., 70 kg) was used to estimate dermal dose.

| Table 1. Acute Toxicity Profile - TCMTB |
| --- |
| Guideline No. | Study Type | MRID(s) | Results | Toxicity Category |
| 81-1 | Acute Oral | 41583801 | LD50 = 750 mg/kg | II |
| 81-2 | Acute Dermal | 41515401 | LD50 > 2000 mg/kg | III |
| 81-3 | Acute Inhalation | 41640601 | LC50 = 0.07 mg/L | I |
| 81-4 | Primary Eye Irritation | Acc no. 111991 |  | I |
| 81-5 | Primary Skin Irritation | 41583701 | Severe erythema at 72 hrs. | II |
| 81-6 | Dermal Sensitization | 42349201 |  | Sensitizer |

| Table 2. Summary of Toxicological Doses and Endpoints for TCMTB |
| --- |
| Exposure Scenario | Dose Used in Risk Assessment, UF | Special FQPA SF* and Level of Concern for Risk Assessment | Study and Toxicological Effects |
| Acute Dietary (general population) | NOAEL = 25.1 mg/kg/day UF = 100 Acute RfD = 0.25 mg/kg/day | FQPA SF = 1X aPAD = acute RfD FQPA SF aPAD = 0.25 mg/kg/day | Rat Developmental Study LOAEL = 76.5 mg/kg/day based on clinical signs of ventral toxicity (alopecia, rough coat, dyspnea/wheezing, oral discharge, diarrhea/loose stool, urine staining, piloerection and hunched gait). |
| Chronic Dietary (all populations) | LOAEL = 3.8 mg/kg/day UF = 300 Chronic RfD = 0.013 mg/kg/day | FQPA SF = 1X PAD = chronic RfD FQPA SF cPAD = 0.013 mg/kg/day | One-year Dog Study LOAEL = 3.8 mg/kg/day based on decreased body weight gain, white cells, monocytes and plasma ALT in males and decreased plasma ALT and uterine weight in females. |
| Incidental Oral Short- and Intermediate-Term (1 - 30 days) | NOAEL = 16 mg/kg/day UF = 100 | MOE = 100 | Rabbit Developmental Study LOAEL = 32 mg/kg/day based on reduced body weight gain and food consumption. |
| Dermal Short-, Intermediate-, and Long-Term (1 - 30 days) | Dermal NOAEL = 25 mg/kg/day | MOE = 100 | 21-Day Dermal toxicity study in Rats LOAEL = 100 mg/kg/day for systemic toxicity based on decreased body weight gain and food consumption in males, in addition to significant hematalogical (increased neutrophils, decreased hemoglobin, hematocrit and erythrocytes) and clinical chemistry changes (increased urea nitrogen, glucose and globulins). |
| Inhalation Short-and Intermediate-Term (1 - 30 days) | NOAEL = 16 mg/kg/day (Inhalation absorption rate = 100%) | MOE = 100 | Rabbit Developmental Study LOAEL = 32 mg/kg/day based on reduced body weight gain and food consumption. |
| Inhalation Long-Term (> 6 months) | LOAEL = 3.8 mg/kg/day (Inhalation absorption rate = 100%) | MOE = 1000 | One-year Dog Study LOAEL = 3.8 mg/kg/day based on decreased body weight gain, white cells, monocytes and plasma ALT in males and decreased plasma ALT and uterine weight in females. |

## 1.4	Incident Reports

An analysis of incidence reports will be included in a separate memo.

## 1.5	Summary of Physical and Chemical Properties of TCMTB

TCMTB (CAS registry number 21564-17-0) is a dark orange liquid with a molecular formula of C9H6N2S3 and a molecular weight of 238.3 g/mole.  It is has a faint, mild odor.  TCMTB is miscible with most organic solvents and can be formulated with a range of surface active agents which can form stable emulsions when diluted further with water.

1.6	Summary of Use Patterns and Formulations

### 1.6.1	End-Use Products

TCMTB is a fungicide used for treating seeds in the United States.  It is used in agricultural and commercial settings.  TCMTB is formulated as a liquid.

### 1.6.2	Registered Use Categories and Sites

An analysis of the current labeling and available use information was completed by HED.  TCMTB is registered for use in agricultural and commercial seed treating (see Table 3).

| Table 3: Summary of Maximum Application Rates for Registered TCMTB Commercial and Agricultural Uses |
| --- |
| Crop | Target | Formulationa | Maximum Application Rate | Application Equipment (Area Treated or Amount Handled Daily) |
| Barley Seed, Oat Seed, Rice Seed, Wheat Seed | Seed | L | 0.026 lbs ai/100 lbs of seed | commercial treater |
| Cotton Seed | Seed | L | 0.13 lbs ai/100 lbs of seed | commercial treater |
|  |  |  | 0.051 lbs ai/100 lbs of seed | on-farm treater |
| Safflower Seed, Sugar beet Seed | Seed | L | 0.041 lbs ai/100 lbs of seed | commercial treater |

a	L = Liquid concentrate

### 1.6.3	Application Methods

TCMTB is applied to seeds during both on-farm and commercial seed treatment.  The following descriptions of seed treatment and planting methods and equipment are based primarily on information provided in HED’s seed treatment SOP (SOP 14), which was developed in consultation with industry specialists.

Commercial Seed Treatment:  Commercial seed treaters are designed to apply accurately measured quantities of pesticides to a given weight of seed.  There are two primary methods for treating seeds: the batch system and the continuous flow system.  The batch system is less automated and generates lower production volume than the continuous flow system.  Seed treatment in commercial facilities occurs primarily via the highly automated continuous flow system.   Treated seed is bagged by a machine which picks up a bag, opens it, and lets it fill to a predetermined weight.  The bagger then folds the top of the bag, and attaches the seed grade certificates and treatment tags.  The sewer then sews the bag shut using an automated sewing machine.  The bag is then moved by a conveyer belt to a pallet area where it is stacked for shipping.  Seed treatment workers may rotate duties to other areas.  In the smaller, less automated facilities in particular, one worker will often have multiple duties within the plant.

On-farm Seed Treatment & Planting of Treated Seed:  There are various pieces of equipment used for on-farm seed treatment, such as drum mixers, homemade devices using augers, cement mixers, hand cranked revolving drums, and gravity feed systems.  The more sophisticated on-farm treaters are essentially miniature versions of the commercial treaters.  Simpler units consist of reusable chemical containers, a power source (vehicle battery), valve and pump or compressed air, and tubing spray nozzles.  These units are mounted directly on a truck box or wagon to dispense seed treatment directly into an auger conveyance system.  Seed may be treated as it is augered from the grower’s truck to the storage bin or seeder or from the storage bin to the farmer’s truck or seeder.  This type of enclosed on-farm treatment system is available only for liquid formulations.

The treated seed can be planted with a wide range of equipment.  Common equipment types include: specialized drills with a box for small seeds and disk openers with depth bands to place the seeds at the appropriate depth followed by packer wheels to firm soil over and around seeds; double corrugated roller seeders, which drop the seed between the rollers followed by a second roller, which covers the seed and firms the soil; and booms, delivery tubes, and air pressure that blow seed onto the soil at properly spaced intervals followed by light packing, dragging a chain or harrowing to cover the planted seed.  Seeding rate is determined by factors such as machine wear, seed size and shape, and crop variety.

# 2.0	Occupational Exposures and Risks

There is a potential for exposure to TCMTB in occupational scenarios from handling TCMTB products during the seed treating process (both commercial and on-farm) and a potential for postapplication worker exposure from handling seed previously treated with TCMTB.  As a result, risk assessments have been completed for occupational handler scenarios as well as occupational postapplication scenarios.

## 2.1	Occupational Handler Exposures and Risks

HED uses the term “handlers” to describe those individuals who are involved in the pesticide application process.  HED believes that there are distinct job functions or tasks related to applications and that exposures can vary depending on the specifics of each task. Job requirements (e.g., amount of chemical to be used in an application), the kinds of equipment used, the target being treated, and the level of protection used by a handler can cause exposure levels to differ in a manner specific to each application event.

HED uses exposure scenarios to describe the various types of handler exposures that may occur for a specific active ingredient. The use of scenarios as a basis for exposure assessment is very common as described in the U.S. EPA Guidelines for Exposure Assessment (U.S. EPA; Federal Register Volume 57, Number 104; May 29, 1992).  Information from the current labels, use and usage information, toxicology data, and exposure data were all key components in the development of the exposure scenarios.  HED has developed a series of general descriptions for tasks that are associated with pesticide applications.  Tasks associated with occupational pesticide handlers are categorized using one of the following terms:

On-farm Loader/Applicator: The possible points of operator exposure for an on-farm treatment are; transport of pesticide in mobile containers, moving pesticide from storage in to seed treatment equipment, introduction of pesticide into seed treatment equipment, and equipment cleaning and maintenance.  On-farm seed treatment with liquid formulations is generally done with more automated equipment, essentially miniature versions of commercial treaters.  Seed may be treated as it is augured from the grower’s truck to the storage bin (at the farmstead), or from the truck to the seeder (field) or from the grower’s storage bin into either a truck or seeder.

- On-farm Planting of Treated Seed: Planting exposures occur during both the loading of hoppers and driving the equipment.

- Commercial Mixer/Loader/Applicator for Seed Treatments: This scenario involves loading/applying of all formulations in a commercial operation.

- Commercial Bagger for Seed Treatments: Seed is bagged by a machine which picks up a bag, opens it, slips it over a spout and lets it fill to a predetermined weight.  The bagger then folds the top of the bag, attaches the seed grade certificates and treatment tags.

- Commercial Sewer for Seed Treatments: After bagging the treated seed the sewer shuts the bag using an automatic sewing machine.  The bag is then moved by a conveyer belt to a pallet area where it is stacked for shipping.

- Multiple Commercial Activities for Seed Treatments: The SOP contains a scenario labeled “Multiple Activities” to address the potential for multiple types of exposure in small commercial operations.

A chemical can produce different effects based on how long a person is exposed, how frequently exposures occur, and the level of exposure.  HED classifies exposures up to 30 days as short-term and exposures greater than 30 days up to several months as intermediate-term.  HED completes both short- and intermediate-term assessments for occupational scenarios in essentially all cases, because these kinds of exposures are likely and acceptable use/usage data are not available to justify deleting intermediate-term scenarios.  Based on use data and label instructions, HED believes that occupational TCMTB exposures may occur over a single day or up to weeks at a time for many use-patterns and that intermittent exposure over several weeks also may occur.  Some applicators may apply TCMTB over a period of weeks, because they are commercial seed treaters.  Long-term handler exposures are not expected to occur for TCMTB.

Other parameters are also defined from use and usage data such as application rates and application frequency.  HED always completes noncancer risk assessments using maximum application rates for each in order to ensure there are no concerns for each specific use.

Occupational handler exposure assessments are completed by HED using different levels of risk mitigation.  Typically, HED uses a tiered approach.  The lowest tier is designated as the baseline exposure scenario (i.e., long-sleeve shirt, long pants, shoes, socks, and no respirator).  If risks are of concern at baseline attire, then increasing levels of personal protective equipment or PPE (e.g., gloves, double-layer body protection, and respirators) are evaluated.  If risks remain a concern with maximum PPE, then engineering controls (e.g., closed mixing/loading systems) are evaluated.  This approach is used to ensure that the lowest level of risk mitigation that provides adequate protection is selected, since the addition of PPE and engineering controls involves an additional expense to the user and – in the case of PPE – also involves an additional burden to the user due to decreased comfort and dexterity and increased heat stress and respiratory stress.

### 2.1.1	Data and Assumptions for Handler Exposure Scenarios

#### 2.1.1.1	Assumptions for Handler Exposure Scenarios

A series of assumptions and exposure factors served as the basis for completing the occupational handler risk assessments.  Each assumption and factor is detailed below on an individual basis. The assumptions and factors used in the risk calculations include:

- Occupational handler exposure estimates were based on surrogate data from: the Health Effects Division Science Advisory Committee on Exposure (HED ExpoSAC) SOP #15: Amount of Seed Treated or Planted per Day, which was completed on March 2, 2004.

- The toxicological endpoint of concern for dermal risks is from a dermal study; with the effects seen in males and females, therefore, the average body weight of an adult handler (i.e., 70 kg) is used to complete the dermal noncancer risk assessment.  The toxicological endpoint of concern for inhalation risks is from an oral study; with the effects seen in males and females, therefore, the average body weight of an adult handler (i.e., 70 kg) is used to complete the inhalation noncancer risk assessment.

- Generic protection factors (PFs) were used to calculate exposures when data were not available.  For example, an 80 percent protection factor was assumed for the use of a respirator equipped with a quarter-face dust/mist filter.

- On-farm treaters and planters are expected to have short-term exposure duration (less than 30 days) for all seed crops.

- Personal protective equipment for on-farm and commercial mixer/loader/applicators and planter includes a single layer and gloves.  Personal protective equipment for commercial baggers and sewers includes baseline attire only - no gloves. Personal protective equipment for performing multiple activities in a commercial operation includes a single layer of clothing and gloves

- Exposure factors used to calculate daily exposures to handlers are based on applicable data, if available.  For lack of appropriate data, values from a scenario deemed similar enough by the assessor might be used.

- For noncancer assessments, HED assumes the maximum application rates allowed by labels in its risk assessments (see Table 3).

- The average occupational workday is assumed to be 8 hours.

- The daily pounds of seed treated per day were defined for each handler scenario by determining the amount that can be reasonably treated in a single day. These assumptions are taken from the HED’s ExpoSAC SOP #15.  The standard values in this SOP are based on the information obtained from the registrants, seed treatment equipment manufacturers, and Agency experts. The values listed are considered to be typical-to-high-end values.  The default values may be modified by pesticide-specific knowledge that affects the amount of seed that can be treated or planted in a day (e.g., high amount of seed required per acre) but in the case of TCMTB, no such data is available.  The values are as follows:

- for commercial seed treatment facilities it is assumed that for barley, rice, safflower, and wheat seed – 718,000 lb seed is treated per day; for cotton seed – 160,000 lb seed is treated per day; and for sugar beet seed – 88,000 lb seed is treated per day.

- for on farm treatments it is assumed that 200 acres is planted per day for cotton (18 lbs of seed per acre), oats (128 lbs of seed per acre), rice (150 lbs of seed per acre), and wheat (150 lbs of seed per acre) seeds;  80 acres is planted per day for safflower (100 lbs of seed per acre) and sugar beet (8 lbs of seed per acre) seeds; and 35 acres is planted per day for barley (100 lbs of seed per acre) seeds.

There are data gaps that have been identified for some TCMTB applications.  Each is identified in the calculation tables and is also noted in the summary of risk calculations.

#### 2.1.1.2	Exposure Data for Handler Exposure Scenarios

HED uses unit exposure to assess handler exposures to pesticides.  Unit exposures are estimates of the amount of exposure to an active ingredient a handler receives while performing various handler tasks and are expressed in terms of micrograms or milligrams of active ingredient per pounds of active ingredient handled.  HED has developed a series of unit exposures that are unique for each scenario typically considered in our assessments (i.e., there are different unit exposures for different types of application equipment, job functions, and levels of protection).  The unit exposure concept has been established in the scientific literature and also through various exposure monitoring guidelines published by the U.S. EPA and international organizations such as Health Canada and OECD (Organization for Economic Cooperation and Development).

Exposure data used for the TCMTB seed treatment assessment are taken primarily from HED’s recently developed seed treatment standard operating procedure (SOPs for Seed Treatment, 6/1/03) and also are based on professional judgment.  The seed treatment SOP contains representative scenarios for worker exposure associated with seed treatment facilities and planting treated seed.  The data contained in the SOP are mostly generated by industry sources.  Exposure estimates are from actual seed treatment studies and are based on exposure factors associated with occupational handler scenarios (i.e., commercial seed treatment, on-farm seed treatment, planting of treated seed).  Eight seed treatment studies were used in developing the SOP.  Given the high level of variance in the data, multiple statistical analyses were undertaken to help ensure derivation of a statistically sound exposure value for the different scenarios evaluated.  For all selected seed treatment studies, replicates were combined into sets of equivalent job functions.  This process resulted in four categories of commercial seed treatment activities (loader/applicator, sewer, bagger, and multiple activities), and two categories for on-farm activities (treater and planter).

On-farm Seed Treatment and Planting

On-farm Loader/Applicator: No studies were available to address exposure to liquid formulations in an on-farm facility.  On-farm seed treatment with liquid formulations is generally done with more automated equipment, essentially miniature versions of commercial treaters.

On-farm Planting of Treated Seed:  Exposure estimates for loading and planting of treated seed are based on 2 exposure studies (MRID # 42251901, 45654503).  In one study, workers loaded and drilled seed treated with Baytan at 13 different sites in the UK.  The seed was loaded into the drill hoppers from 0.5 or 1 ton super sacks or 50 kg bags. The amount of seed handled ranged from 1100 to 12,100 lbs and the amount of ai handled ranged from 0.35 to 4.72 lbs.   The loading time ranged from 19 to 83 minutes, while the planting time ranged from 155 to 487 minutes.  The seed planting rate per acre was not given.  The same worker performed both the loading and planting.  Dermal exposure was measured with inner and outer whole body dosimeters which included a cap, a jacket and trousers over a long sleeve T-shirt and long johns and two sets of cotton gloves.  The gloves were changed at the end of loading.  Inhalation exposures were measured with 37 mm glass fiber filters and the filters were changed after loading.  The dermal results were adjusted by a clothing protection factor to account for the fact that 5% of the outer residues were found on the inner dosimeters.

In the second study workers loaded and drilled canola seed treated with Oftanol, which forms a hard shell coating.  The 13 replicates for this study were located at one site in Manitoba using four different planting rigs.  Four workers participated in the study and the replicates averaged 3.2 hours in duration.  The seed was loaded into the drill hoppers from 25 kg bags.   The amount of seed handled per replicate averaged 360 pounds and the amount of ai handled averaged 4.33 lbs.  The seed was planted at a rate of 6 to 8 pounds per acre.   The same worker performed both the loading and planting.  Dermal exposure was measured with patches located both inside and outside the worker’s coverall.  Hand exposures were measured by hand rinse.   Inhalation exposures were measured with 37 mm quartz microfiber filters.

Commercial Seed Treatment

Commercial Loader/Applicator: Exposure estimates are based on a subset of 3 exposure studies (MRID Nos. 43080049, 42251902, 44904526).  The loader/applicator activities in these 3 exposure studies encompass a wide range of seed treaters, amounts of seed and amounts of pesticides handled for seed treatment scenarios.  The three studies monitored an open loading/applying activity for various seed treatment facilities. There is an average of 9 replicates per study (ranging from 1 to 20 replicates per study).  Two of the three studies monitored dermal exposures with patch dosimetry, hand rinses, and face wipes.  The methodology in the third study was whole body dosimetry, hand rinses and face wipes.

Commercial Bagger: Exposure estimates for bagging activities for all formulations are based on data from 3 exposure studies (MRID Nos. 43080049, 42251902, and 44904526).  The studies monitored bagging treated seed in various seed treatment facilities and encompassed a wide range of bagging equipment, and amount of seed and pesticides handled.  The number of replicates ranged from 1 to 20 per study. Two of the studies monitored dermal exposures with whole body dosimeters, and face, neck and hand rinses.  The third used dermal patches and hand rinses to monitor exposure.

Commercial Sewer: Exposure estimates for sewing activities for all formulations are based on data from 2 exposure studies (MRID # 430800-49, and449045-26).  The two studies monitored sewing various bags of treated seed in a number of seed treatment facilities. The number of replicates ranges from 1 to 20 per study.  Both of the studies monitored dermal exposures with whole body dosimeters, and face, neck and hand rinses.

Multiple Commercial Activities: Exposure estimates for multiple activities for all formulation are based on data from 4 exposure studies (MRID #s, 454427-01, 422519-02, 449045-26 and 447315-01).  These studies encompass a variety of seed treatment activity and a wide range of amount of seed pesticides handled.  The four studies in this scenario monitored multiple activities for various seed treatment facilities. The number of replicates ranges from 3 to 45 per study.  Three of the five studies monitored dermal exposures with whole body dosimeter, face and neck and hand rinses.  The methodology in the other studies was dermal patches and hand rinses.

TCMTB Handler Exposure Scenarios

It has been determined that exposure to pesticide handlers is likely during the occupational use of TCMTB in a variety of occupational environments.  The anticipated use patterns and current labeling indicate several occupational exposure scenarios based on the types of equipment and techniques that can potentially be used for TCMTB applications.  The quantitative exposure/risk assessment developed for occupational handlers is based on the following scenarios.

Seed treatment:

(S-1) loading and applying liquid formulations with commercial seed-treatment equipment,

(S-2) commercial sewer stitching bags of seed,

(S-3) bagging and otherwise handling treated seeds with commercial equipment,

(S-4) multiple commercial seed treatment activities,

(S-5) on-farm loading/applying seed treatment, and

(S-6) on-farm loading/planting previously treated seeds.

### 2.1.2	Noncancer TCMTB Handler Exposure and Assessment

#### 2.1.2.1	Noncancer TCMTB Handler Exposure and Risk Calculations

Daily Exposure: Daily dermal or inhalation handler exposures are estimated for each applicable handler task with the application rate, the area treated in a day, and the applicable dermal or inhalation unit exposure using the following formula:

Daily Exposure (mg ai/day)	= 	Unit Exposure (mg ai/lb ai handled) * Application Rate (lbs ai/area) *

Daily Area Treated (area/day)

Where:

Daily Exposure		=	Amount (mg ai/day) deposited on the surface of the skin that is 	available for dermal absorption or amount inhaled that is available for 	inhalation absorption;

Unit Exposure		=	Unit exposure value (mg ai/lb ai handled) derived from August 1998 	PHED data, from ORETF data;

Application Rate		=	Normalized application rate based on a logical unit treatment, such as 	acres, square feet, or gallons. Maximum values are generally used (lb 	ai/cut weight); and

Daily Area Treated	=	Normalized application area based on a logical unit treatment such as 	acres (A/day).

Daily Dose:  The daily dermal or inhalation dose is calculated by normalizing the daily exposure by body weight and adjusting, if necessary, with an appropriate dermal or inhalation absorption factor.  For all exposure scenarios for TCMTB, an average adult body weight of 70 kilograms was used, since the toxicological endpoint of concern was gender-specific.  For dermal exposures, no dermal absorption factor was necessary, since the toxicological endpoint is from a dermal study.  For inhalation exposures, an absorption factor of 100% was assumed.

Daily dose was calculated using the following formula:

Average Daily Dose (mg/kg/day)	=	(Daily Exposure (mg ai/day) * (Absorption Factor (%)

Body Weight (kg)

Where:

Average Daily Dose 	=	Absorbed dose received from exposure to a pesticide in a given 						scenario (mg pesticide active ingredient/kg body weight/day);

Daily Exposure 		=	Amount (mg ai/day) deposited on the surface of the skin that is 	available for dermal absorption or amount inhaled that is available for 	inhalation absorption;

Absorption Factor	= 	A measure of the amount of chemical that crosses a biological 	boundary such as the skin or lungs (% of the total available absorbed); 	and

Body Weight 		= 	Body weight determined to represent the population of interest in a risk

assessment (kg).

Margins of Exposure:  Noncancer dermal and inhalation risks for each applicable handler scenario are calculated using a Margin of Exposure (MOE), which is a ratio of the daily dose to the toxicological endpoint of concern. All MOE values were calculated separately for dermal and inhalation exposure levels using the formula below:

MOE	=	(NOAEL (mg/kg/day) / Average Daily Dose (mg/kg/day)

Where:

MOE 			= 	Margin of Exposure, value used by HED to represent risk or how close a

chemical exposure is to being a concern (unitless);

ADD 			= 	Average Daily Dose or the absorbed dose received from exposure to a pesticide

in a given scenario (mg pesticide active ingredient/kg body weight/day); and

NOAEL			= 	Dose level in a toxicity study, where no observed adverse effects (NOAEL) occurred in the study

It is important to present risk estimates for each route of exposure (i.e., dermal or inhalation) in each scenario because it makes determining appropriate risk mitigation measures easier.  For example, if overall risks are driven by dermal exposures and not inhalation, it is inadvisable to require respirators even though they may marginally reduce overall risks.

A total MOE was calculated for TCMTB because common toxicity endpoints were used to calculate dermal and inhalation risks for each exposure duration.  The dermal and inhalation MOEs were combined using the formula below:

MOE TOTAL	=	[1/((Dermal MOE ) + (1/Inhalation MOE))]

#### 2.1.2.2	TCMTB Noncancer Risk Summary

All of the noncancer risk calculations for occupational TCMTB handlers completed in this assessment are included in the appendices.  A summary of the short- and intermediate-term risks for each exposure scenario are presented below in Tables 4 - 7.

Short- and Intermediate-term Dermal and Inhalation Risks

For commercial and on-farm seed treatment scenarios, all dermal and inhalation MOEs met or exceeded the required uncertainty factor of 100 at some level of mitigation.

Short- and Intermediate-term Total Risks

For commercial and on-farm seed treatment scenarios, all combined dermal and inhalation risks met or exceed the required uncertainty factor of 100 at some level of mitigation.

| Table 4. Estimated Worker Exposure and Risk from Commercial Seed Treatment |
| --- |
| Crop | Exposure Scenario | Application Rate (lb ai/100 lb)a | Amount Handled per Day (lb ai/day)b | Short- and Intermediate-term MOEs c |
|  |  |  |  | Baseline | Personal Protective Equipment | Engineering Controls |
|  |  |  |  | Dermal | Inhalation | Dermal | Inhalation | Dermal | Inhalation |
|  |  |  |  |  |  | SL w/ gloves | DL w/ gloves | 80% R | 90% R |  |  |
| Barley, Oats Rice, Wheat Seeds | Loader/Applicator | 0.026 | 187 | ND | 18000 | 410 | 520 | 88000 | 180000 | 1100 | 72000 |
|  | Sewer |  |  | 1500 | 26000 | ND | ND | 13000 | 260000 | NF | NF |
|  | Bagger |  |  | 1000 | 37000 | ND | ND | 190000 | 370000 | NF | NF |
|  | Multiple Activities |  |  | ND | 3700 | 220 | ND | 19000 | 37000 | NF | NF |
| Cotton Seeds | Loader/Applicator | 0.13 | 208 | ND | 16000 | 370 | 470 | 79000 | 160000 | 980 | 65000 |
|  | Sewer |  |  | 1400 | 23000 | ND | ND | 120000 | 230000 | NF | NF |
|  | Bagger |  |  | 920 | 34000 | ND | ND | 170000 | 340000 | NF | NF |
|  | Multiple Activities |  |  | ND | 3400 | 200 | ND | 17000 | 34000 | NF | NF |
| Safflower Seeds | Loader/Applicator | 0.041 | 294 | ND | 11000 | 260 | 330 | 56000 | 110000 | 690 | 46000 |
|  | Sewer |  |  | 960 | 17000 | ND | ND | 83000 | 170000 | NF | NF |
|  | Bagger |  |  | 650 | 24000 | ND | ND | 120000 | 240000 | NF | NF |
|  | Multiple Activities |  |  | ND | 2400 | 140 | ND | 12000 | 24000 | NF | NF |
| Sugar Beet Seeds | Loader/Applicator | 0.041 | 36 | ND | 91000 | 2100 | 2700 | 460000 | 910000 | 5600 | 370000 |
|  | Sewer |  |  | 7800 | 130000 | ND | ND | 670000 | 1300000 | NF | NF |
|  | Bagger |  |  | 5300 | 190000 | ND | ND | 970000 | 1900000 | NF | NF |
|  | Multiple Activities |  |  | ND | 19000 | 1200 | ND | 97000 | 190000 | NF | NF |

ND  =  No Data; NF  =  Not Feasible

a	Application rates are the maximum application rates determined from EPA registered labels for TCMTB

b	Amount handled per day calculated from the maximum application rate and the lbs of seed treated or planted/day and:  for barley, rice, safflower, and wheat seed - 718000 lb/day; for cotton seed – 160000 lb/day; and sugar beet seed – 88000 lb/day.

c	Baseline Dermal:  Long-sleeve shirt, long pants, no gloves.

Baseline Inhalation: no respirator.

PPE Dermal SL with gloves: Single layer plus chemical-resistant gloves.

PPE Dermal DL and gloves: Coveralls worn over long-sleeve shirt and long pants plus chemical-resistant gloves.

PPE 80% R inhalation: assumes a dust/mist removing filtering face piece style respirator providing an 80% protection factor.

PPE 90%R inhalation: assumes a dust/mist removing half-face style respirator providing a 90% protection factor.

Eng Controls Dermal and Inhalation: Closed System.

| Table 5. Combined Estimated Worker Dermal and Inhalation Risk from Commercial Seed Treatment |
| --- |
| Crop | Exposure Scenario | App Ratea (lb ai/lb) | Amount Handled per Day b (lb ai/day) | Combined MOEs c |
|  |  |  |  | Baseline | SL, G + NR | DL, G + NR | SL + 80% R | SL, G + 80% R | SL + 90% R | SL, G+ 90% R | Eng Control |
| Barley, Oats, Rice, Wheat Seeds | Loader/Applicator | 0.026 | 187 | ND | 400 | 510 | ND | 410 | ND | 410 | 1000 |
|  | Sewer |  |  | 1400 | ND | ND | 1500 | ND | 1500 | ND | NF |
|  | Bagger |  |  | 970 | ND | ND | 990 | ND | 1000 | ND | NF |
|  | Multiple Activities |  |  | ND | 210 | ND | ND | 220 | ND | 220 | NF |
| Cotton Seeds | Loader/Applicator | 0.13 | 208 | ND | 360 | 450 | ND | 360 | ND | 360 | 920 |
|  | Sewer |  |  | 1300 | ND | ND | 1400 | ND | 1400 | ND | NF |
|  | Bagger |  |  | 900 | ND | ND | 910 | ND | 920 | ND | NF |
|  | Multiple Activities |  |  | ND | 190 | ND | ND | 200 | ND | 200 | NF |
| Safflower Seeds | Loader/Applicator | 0.041 | 294 | ND | 250 | 320 | ND | 260 | ND | 260 | 650 |
|  | Sewer |  |  | 910 | ND | ND | 950 | ND | 950 | ND | NF |
|  | Bagger |  |  | 630 | ND | ND | 650 | ND | 650 | ND | NF |
|  | Multiple Activities |  |  | ND | 130 | ND | ND | 140 | ND | 140 | NF |
| Sugar Beet Seeds | Loader/Applicator | 0.041 | 36 | ND | 2100 | 2600 | ND | 2100 | ND | 2100 | 5300 |
|  | Sewer |  |  | 7400 | ND | ND | 7700 | ND | 7800 | ND | NF |
|  | Bagger |  |  | 5200 | ND | ND | 5300 | ND | 5300 | ND | NF |
|  | Multiple Activities |  |  | ND | 1100 | ND | ND | 1100 | ND | 1100 | NF |

ND  =  No Data; NF  =  Not Feasible

a	Application rates are the maximum application rates determined from EPA registered labels for TCMTB

b	Amount handled per day calculated from the maximum application rate and the lbs of seed treated or planted/day and:  for barley, rice, safflower, and wheat seed - 718000 lb/day; for cotton seed – 160000 lb/day; and sugar beet seed – 88000 lb/day.

c	Baseline		=	No gloves and no respirator

SL, G		=	Single layer w/gloves is baseline attire plus chemical-resistant gloves.

DL, G		=	Double layer w/gloves is coveralls worn over long-sleeve shirt and long pants, plus chemical-resistant gloves.

80% R		=	80% Respirator is dust/mist removing filtering face piece style respirator (that provides an 80% protection factor).

90% R		=	90% Respirator is half-face dust/mist respirator (that provides a 90% protection factor).

Eng Control	=	Engineering control is closed mixing/loading system, enclosed cab, or enclosed cockpit.

| Table 6. Estimated Worker Exposure and Risk from On-farm Seed Treatment |
| --- |
| Crop | Acres treated/ day | App Rate (lb ai/ 100 lb)a | Amount Handled per dayb (lb ai/day) | Unit Exposures | Short- and Intermediate-term MOEs |
|  |  |  |  | Baseline | Personal Protective Equipment | Engineering Controls | Baseline | Personal Protective Equipment |
|  |  |  |  | Dermalc (mg/lb ai) | Inhalationd (g/lb ai) | Dermal (mg/lb ai) | Inhalation (ug/lb ai) | Dermalh (mg/lb ai) | Inhalationi (ug/lb ai) | Inhalation | Dermal | Inhalation |
|  |  |  |  |  |  | SL w/ glovese | 80% Rf | 90% Rg |  |  |  | SL w/ gloves | 80% R | 90% R |
| LOADING/APPLYING LIQUID SEED TREATMENTS |
| Cotton | 125 | 0.051 | 0.64 | NDj |
| LOADING/PLANTING PREVIOUSLY TREATED SEEDS |
| Barley | 35 | 0.026 | 0.64 | ND | 3.4 | 0.25 | 0.68 | 0.34 | NF | NF | 360000 | 7700 | 1800000 | 3600000 |
| Beet; Sugar | 80 | 0.041 | 0.26 |  |  |  |  |  |  |  | 1300000 | 27000 | 6300000 | 13000000 |
| Cotton | 200 | 0.13 | 4.68 |  |  |  |  |  |  |  | 70000 | 1500 | 350000 | 700000 |
| Oats | 200 | 0.026 | 6.66 |  |  |  |  |  |  |  | 49000 | 1100 | 250000 | 490000 |
| Rice | 200 | 0.026 | 7.80 |  |  |  |  |  |  |  | 42000 | 900 | 210000 | 420000 |
| Safflower | 80 | 0.041 | 3.28 |  |  |  |  |  |  |  | 100000 | 2100 | 500000 | 1000000 |
| Wheat | 200 | 0.026 | 7.80 |  |  |  |  |  |  |  | 42000 | 900 | 210000 | 420000 |

ND  =  No Data; NF  =  Not Feasible

a	Application rates are the maximum application rates determined from EPA registered labels for TCMTB.

b	Amount handled per day calculated from the acres treated/day and the maximum lb of seed planted per acre.

c	Baseline Dermal:  Long-sleeve shirt, long pants, no gloves.

d	Baseline Inhalation: no respirator.

e	PPE Dermal SL with gloves: Single layer plus chemical-resistant gloves.

f	PPE 80% R inhalation: assumes a dust/mist removing filtering face piece style respirator respirator providing an 80% protection factor.

g	PPE 90%R inhalation: assumes a dust/mist removing half-face style respirator providing a  90% protection factor.

h	Eng Controls Dermal: Closed System.

i	Eng Controls Inhalation: Closed System.

j	On-farm seed treatment with liquid formulations is generally done with automated equipment, essentially miniature versions of commercial treaters.

| Table 7. Combined Estimated Worker Dermal and Inhalation Risk from On-farm Seed Treatment |
| --- |
| Crop | Acres treated/day | App Ratea (lb ai/lb) | Amount Handled per dayb (lb ai/day) | Combined MOEs c |
|  |  |  |  | Baseline | SL, G + NR | SL + 80% R | SL, G + 80% R | SL + 90% R | SL, G+ 90% R | Eng Control |
| LOADING/APPLYING LIQUID SEED TREATMENTS |
| Cotton | 125 | 0.051 | 0.64 | NDd |
| LOADING/PLANTING PREVIOUSLY TREATED SEEDS |
| Barley | 35 | 0.026 | 0.64 | ND | 7500 | ND | 7700 | ND | 7700 | NF |
| Beet; Sugar | 80 | 0.041 | 0.26 | ND | 26000 | ND | 27000 | ND | 27000 | NF |
| Cotton | 200 | 0.13 | 4.68 | ND | 1500 | ND | 1500 | ND | 1500 | NF |
| Oats | 200 | 0.026 | 6.66 | ND | 1100 | ND | 1100 | ND | 1100 | NF |
| Rice | 200 | 0.026 | 7.80 | ND | 880 | ND | 900 | ND | 900 | NF |
| Safflower | 80 | 0.041 | 3.28 | ND | 2100 | ND | 2100 | ND | 2100 | NF |
| Wheat | 200 | 0.026 | 7.80 | ND | 880 | ND | 900 | ND | 900 | NF |

ND  =  No Data; NF  =  Not Feasible

a	Application rates are the maximum application rates determined from EPA registered labels for TCMTB

b	Amount handled per day calculated from the acres treated/day and the maximum lb of seed planted per acre.

c	Baseline		=	No gloves and no respirator

SL, G		=	Single layer w/gloves  is baseline attire plus chemical-resistant gloves.

DL, G		=	Double layer w/gloves is coveralls worn over long-sleeve shirt and long pants, plus chemical-resistant gloves.

80% R		=	80% Respirator is dust/mist removing filtering face piece style respirator (that provides an 80% protection factor).

90% R		=	90% Respirator is half-face dust/mist respirator (that provides a 90% protection factor).`

Eng Control	=	Engineering control is closed mixing/loading system, enclosed cab, or enclosed cockpit.

d	On-farm seed treatment with liquid formulations is generally done with automated equipment, essentially miniature versions of commercial treaters.

2.1.3 	Cancer TCMTB Handler Exposure and Risk Assessment

The Health Effects Division Carcinogenicity Peer Review Committee (CPRC) met on June 28, 1995 to discuss and evaluate the weight-of-the-evidence on 2-(Thiocyanomethylthio) benzothiazole (TCMTB) with particular reference to its carcinogenic potential.  The CPRC concluded that TCMTB should be classified as Group C - possible human carcinogen - and recommended that for the purpose of risk characterization, the Reference Dose (RfD) approach should be used for quantitation of human risk.  This was based on statistically significant increases in tumors in both sexes of the Sprague-Dawley rat: testicular interstitial cell adenomas in males and thyroid c-cell adenomas in females.

### 2.1.4 	Summary of Risk Concerns/Data Gaps for Occupational Handlers

There are several occupational handler scenarios for TCMTB that have risks associated with them that are above HED’s level of concern for noncancer risk assessments, even at the highest level of risk mitigation.  However, there are also some occupational handler scenarios for TCMTB that have data gaps.

#### 2.1.4.1	Summary of Risk Concerns

The short- and intermediate-term dermal and inhalation handler risk assessment for TCMTB indicates risk concerns for a number of seed treatment scenarios, even with maximum risk mitigation.  See Section 2.1.3.2 for a detailed summary.

#### 2.1.4.2	Summary of Data Gaps

One data gap was identified for TCMTB.  On-farm seed treatment with liquid formulations is generally done with automated equipment, essentially miniature versions of commercial treaters.  Currently, HED has no exposure data to assess this particular exposure scenario.

### 2.1.5	Recommendations For Refining  Handler Risk Assessment

The values presented in the Health Effects Division Science Advisory Committee on Exposure SOP #15: Amount of Seed Treated or Planted per Day are most relevant to commercial seed treaters and growers planting treated seed.  When assessing growers who do on-farm seed treatment, the values may, in some cases, be overestimates or underestimates, depending on the crop type, geographic location and toxicity endpoint.  Likewise, because of limitations on farm size/crop type specific to the pesticide being assessed, the volume given in the tables may not be appropriate.  These are cases when more detailed information regarding the pesticide application rates, geographical/cultural characteristics of the crop and other relevant information should be considered and modifications made to the table values on a case-by-case basis.  For TCMTB, no chemical specific data regarding applications to seeds is currently available.  In order to refine this occupational risk assessment, data on actual use patterns including rates, timing, and seeds treated per day would better characterize TCMTB risks.