RENEWABLE ENERGY IN PAKISTAN

1	(2x50) MW Wind Power Generation Project at Gharo, Sindh

On commercial grid connected electricity generation program, the Government of Pakistan has decided to install 100 MW Wind Power Farm by June 2009. This program initiated by the Alternative Energy Development Board (AEDB), involves financing through private sector, land from Government of Sindh and power purchase by NTDC for HESCO. The Government of Pakistan guarantees are backed through NEPRA. The Board has recently issued LOIs to 30 national and international companies for generation of 1500 MW power through wind energy.

A wind corridor at Gharo-Keti Bandar, Sindh has been identified with an actual potential of 50,000 MW. The pre-feasibility study of the site has been done by AEDB. AEDB drafted the Power Purchase Agreement (PPA) and the Implementation Agreement. 8 companies with financial and technical viability have been short-listed. OEMs/Suppliers like GE, VESTAS and GAMESA have been short-listed for the project. Three companies have submitted applications to NEPRA for obtaining Generation License. NTDC has submitted the request for Power Acquisition Permission to NEPRA for procuring power from the proposed wind plants. HESCO has agreed to purchase the initial 100 MW Wind Power generated through this project. Private investors have entered the PPA negotiations with NTDC/WAPDA. Sindh Government has leased out approximately 5000 Acres of land for the project. AEDB has allocated 1000 acres of land each to five (5) investors, namely M/s New Park Energy Ltd., M/s Green Power, M/s Zephyr Ltd., M/s Win Power Ltd. and M/s Tenaga. Tariff would be determined by NEPRA in consultation with the IPP and the Power Purchaser i.e. NTDC, as per Government of Pakistan’s Policy for Power Generation 2002, and under the Section 7(6) of the Regulation Generation, Transmission and Distribution of Electric Power Act (XL of) 1997 (NEPRA Act). New Transmission Network from Mirpur Sakro to Thatta is to be constructed by NTDC in order to sustain the load generated by 100 MW Wind Power. PC-I for the project has been approved by the CDWP.

Once the initial target of generating 100 MW through Wind Energy is achieved, it will be upgraded to 700 MW by the year 2010 and 9700 MW by the year 2030.

2	PSDP Projects undertaken by AEDB

2.1	100 Solar Homes Program Narian Khorian, Islamabad

The project was successfully executed and implemented by AEDB. The Honorable Prime Minister of Pakistan inaugurated it on 19th June 2005. Each of the 100 households has been provided with 88-Watt Solar Panels, 4 LED lights, a 12 Volt DC fan and a TV socket. In addition, a Solar Geyser and a Solar Cooker have also been provided to each household.

As part of the community welfare, a Solar Water Desalination Plant has also been installed and commissioned at the village ensuring the availability of clean drinking water to the villagers. A Children’s Playground with Solar Powered Lights has also been developed at the Village. Two Solar Powered Computers have been provided to the village Mosque/Community Center, which has been air-conditioned using Solar Energy as well. In addition, an electric vehicle has also been developed which will act as the first ever Electric Rickshaw in Pakistan. The batteries of this vehicle are charged with Solar Energy.

2.2	100 Solar Homes Program per Province:

The project was executed and implemented in the following villages:

- Allah Baksh Bazar Dandar, District Kech, Balochistan,

- Bharo Mal, District Thar, Sindh,

- Janak, District Kohat, N.W.F.P.,

- Lakhi Bher, Distrcit D.G. Khan, Punjab.

Each of the 100 households in each village has been provided with 88-Watt Solar Panels, 4 LED lights, a 12 Volt DC fan and a TV socket. In addition, a Solar Disinfecting Unit and a Solar Cooker have also been provided to each household.

2.3	Pilot Project for Development and Installation of 02 Micro Hydro Kaplan Turbines:

A 40 kW Kaplan type micro hydel Turbine has been imported from China to reverse engineer the technology. An R&D lab is being setup for this purpose.

Another 40 kW Kaplan type micro hydel turbine has been indigenously manufactured and installed at the Khanpur Dam Canal near the village of Mohra Morado, Taxila. This turbine is being used to provide electricity to the village.

2.4	Pilot Project for Installation of Indigenously Developed Micro Wind Turbines:

A total of 140 Micro Wind Turbines have been installed at various sites within Sindh and Balochistan, for providing electricity to the rural households, as well as for water pumping. Details have been provided in Table 3.

2.5	Pilot Project for Emerging Alternative Energy Technologies Demonstration in Pakistan:

Fuel Cell: The Project clearly emphasizes on the research and development of Fuel Cells in the country and in this regard most of the initial work has already been completed. 03 No Fuel Cells along with accessories were imported from the international market for carrying out research in this field. UET Lahore and NED University Karachi have been contacted for establishment of Fuel Cell Laboratories in their premises so that the youth and intellectual class of students can benefit out of this cutting edge technology to the most. The Laboratories would be established and the equipment would be handed over to the concerned after proper training. Training Workshop by a Foreign Consultant has also been arranged so that the final part of the Project under the present scope could be finalized. The Monitoring and Evaluation team of AEDB would be in continuous operation for the success of the said project, its development and indigenization in the country in near future.

Bio Diesel: The initial research on bio-diesel resources in Pakistan is complete. As much as 10 oil resources have been subjected to oil extraction, transesterification and chemical analysis. After iterative experiments, a number of potential resources have been identified including Pongamia Pinnata (Sukh Chane), Rape Seed, and Castor Bean.

Out of these, Pongamia Pinnata, being a natural tree and with no other usage of its seed is considered to be the most promising source with an average yield of 40-90 kg seed per tree and 25% oil content in de-shelled seed.

The bio-diesel resources have been subjected to oil production. The practical yields have been found and chemical properties have been compared with those of HSD. The bio-diesel in neat form, as well as B5, B10, B20 has been subjected to road run.

The experiments so far have revealed that performance of bio-diesel, produced through indigenous means, remains same as that of HSD, when used as a blend. One just has to start off the engine and operate. However, for use of neat bio-diesel, production processes require slight iteration to reduce the viscosity of oil. This is achievable but should only be done when use of neat bio-diesel is required.

Basic research on supply chain mechanism is also complete. The infrastructure requirements, the raw material availability and deployment models have been primed.

Still in progress is laboratory set-up for advance research on bio-diesel. This includes installation of seed press in Quaid-i-Azam University to study the productivity and economic aspects vis-à-vis botanical aspect. Secondly, installation of a CL engine test bed at University of Engineering & Technology Taxila, to calculate and compare the performance indicators when operated on HSD and various blends of bio-diesel.

In addition, Pakistan Railways has been involved in plantation of Sukh Chane trees along the railway tracks. Once the performance parameters are finalized and test run of the locomotive’s engine is done, the oil extracted from the Sukh Chane seed will be used in the locomotive engine, saving sufficient volumes of imported HSD.

Innovative Lighting Systems: LED Lights, Solar Lanterns, Pedal Generators, Hand Generators and Solar Mobile Phone Chargers have been indigenously developed by the private sector with AEDB’s facilitation. These products have also been provided to the rural areas that have been electrified with Solar Energy.

3.	Activities of Pakistan Council for Renewable Energy Technologies (PCRET)

  - Photovoltaic (PV) Technology

- Solar-Wind-Diesel High hybrid system installed to provide electricity to two villages in Balochistan through M/s Empower International, New Zealand.

- Two other villages in Balochistan were electrified using PV system.

- 3000 Laser Detectors were designed and fabricated for incorporating in the laser land leveling system of Pakistan Atomic Energy Commission (PAEC).

- 4000 Solar Cells and 300 Solar Modules of different sizes were fabricated indigenously.

  - Solar Thermal Appliances

A number of appliances including solar water heaters, solar fruit and vegetable dryers, solar distillation stills for producing clean water, solar room heating systems and solar cookers have been developed and disseminated for domestic and commercial applications.

3.3	Fuel Saving / Efficient Cooking Stoves

PCRET has developed five different models of efficient cooking stoves for use in different parts of the country. Their efficiency varies from 20% to 25% vis-à-vis 10% efficiency of conventional cooking stoves. So far, 70,000 such cooking stoves have been disseminated, 400 training programs conducted and 20 cooking stoves manufacturing units/shops established and 200 sale points have been opened by the private sector.

3.4	Biogas Technology

- 1500 family size biogas plants have been installed, which are meeting the domestic needs of 1500 households in the rural area of the country.

- 3 community size biogas plants have been installed in rural areas of Islamabad, which are meeting domestic fuel needs of 20 houses.

- A 1000 m3 biogas plant is being designed for installation near Cattle Colony, Karachi. This plant will work under thermophillic conditions.

3.5	Micro Hydro Power (MHP) Plants

- 300 MHP plants (5-50 kW each) installed on cost sharing basis in the hilly terrain of NWFP.

- Under Malakand Rural Development Project, 5 MHP plants have been installed and civil works of another 20 MHP plants have been completed. The Government of NWFP has funded this project.

3.6	Electrification through Micro Wind Turbines

- 600 houses have been electrified in the remote coastal areas of Sindh and Balochistan through installation of small wind turbines (stand alone) systems.

- 4 Coast Guard Check Posts at Lasbela have been electrified.

- 5 villages have been provided with battery charging facilities through a wind-powered battery-charging center.

- 500-Watts Wind Turbine has been manufactured locally. The second (improved) model is under field test.

- A reverse osmosis unit is being installed near village Mubarak, Kemari Town, Karachi for desalination of brackish water.

*****

Medium Term Wind Energy Development Plan 2011-2020

| Year | Capacity Installed (MW) | Cumulative MW of Wind Energy Installed by Year End |
| --- | --- | --- |
|  | 700 | Short Term Plan (2005-2010) 700 |
| 2011 | 100 | 800 |
| 2012 | 100 | 900 |
| 2013 | 150 | 1,050 |
| 2014 | 200 | 1,250 |
| 2015 | 250 | 1,500 |
| 2016 | 250 | 1,750 |
| 2017 | 300 | 2,050 |
| 2018 | 300 | 2,350 |
| 2019 | 350 | 2,700 |
| 2020 | 300 | 3,000 |

Source:  Board of Investment, Government of Pakistan

DETAILS OF MICRO WIND TURBINES INSTALLED IN SINDH & BALOCHISTAN

SINDH - District Thatta

| S.No | Name of Village | Homes Electrified | Turbines Installed |
| --- | --- | --- | --- |
| 1 | Goth Gul Muhammad Khaskheli – Thakani, Mirpur Sakro | 16 | 04 |
| 2 | Goth Haji Jumo Khaskheli – Thakani, Mirpur Sakro | 23 | 06 |
| 3 | Goth Ismail Khaskheli 1 – Thakani | 15 | 04 |
| 4 | Goth Ismail Khaskheli 2 – Thakani | 05 | 01 |
| 5 | Goth Mohd Hasan Khaskheli – Thakani, Mirpur Sakro | 18 | 05 |
| 6 | Goth Haji Abdullah Channo – Thakani, Mirpur Sakro | 07 | 02 |
| 7 | Goth Jamot Hussain Khaskheli – Thakani, Mirpur Sakro | 11 | 03 |
| 8 | Goth Baboo Pahwar – Thakani, Mirpur Sakro | 06 | 02 |
| 9 | Goth Sher Muhammad Hamaiti – Gujjo | 40 | 10 |
| 10 | Goth Daandaari – Ghorabari, U.C. Udaasi | 250 | 40 |
| 11 | Goth Lukman – Ghorabari, U.C. Udaasi | 16 | 04 |
| 12 | Goth Sammo – Ghorabari, U.C. Udaasi | 14 | 03 |
|  | Total | 356 | 85 |

| 13 | Daandaari – Ghorabari, U.C. Udaasi | 01 (10 kilo Watts) – Water Pumping |
| --- | --- | --- |

Source:  Board of Investment, Government of Pakistan

BALOCHISTAN - Kund Malir, District Lasbela

| S.No | Name of Village | Homes Electrified | Turbines Installed |
| --- | --- | --- | --- |
| 1 | Goth Meer Isa – Kund Malir, Lasbela | 03 | 01 |
| 2 | Goth Ramzan – Kund Malir, Lasbela | 15 | 02 |
| 3 | Goth Haji Sher Muhammad – Kund Malir, Lasbela | 35 | 05 |
| 4 | Goth Yaaqoob – Kund Malir, Lasbela | 18 | 02 |
| 5 | Goth Mir Abdullah – Kund Malir, Lasbela | 08 | 01 |
| 6 | Goth Haji Washi / Daghari – Kund Malir, Lasbela | 32 | 04 |
|  | Totals | 111 | 15 |

Source:  Board of Investment, Government of Pakistan

BALOCHISTAN - Quetta

| S.No | Name of Recipient | Location | Turbines | Current Status |
| --- | --- | --- | --- | --- |
| 7 | Governor Balochistan on behalf of the Government of Balochistan | F.C. Warehouse Quetta | 39 | To be installed as per the direction and advice of the Irrigation & Power Department Balochistan |

Source:  Board of Investment, Government of Pakistan

VILLAGES ELECTRIFIED THROUGH SOLAR PHTOVOLTAIC DURING 2004-05

| Village Name | District | Province | No. of Houses |
| --- | --- | --- | --- |
| Narian | Rawalpindi | Punjab | 53 |
| Khorian | Rawalpindi | Punjab | 57 |
| Allah Baksh Bazar Dandar | Turbat | Balochistan | 121 |
| Lakhi Bhair | D.G. Khan | Punjab | 135 |
| Bharomal | Chachro | Sindh | 115 |
| Jhanak | Kohat | N.W.F.P | 120 |
|  |  | Total | 601 |

Source:  Board of Investment, Government of Pakistan

VILLAGES TO BE ELECTRIFIED THROUGH SOLAR PHTOVOLTAIC DURING 2005-06

| Village name | District | Province | No. of Houses |
| --- | --- | --- | --- |
| Khirzaan | Khuzdar | Balochistan | 100 |
| Basti Bugha | D.G. Khan | Punjab | 100 |
| Pinpario | Chachro | Sindh | 100 |
| Shnow Garri | Kohat | N.W.F.P | 100 |
|  |  | Total | 400 |

Renewable Energy ProjectS FOR 2005-06

| No. | Project Title |
| --- | --- |
| 1. | Roshan Pakistan: National Rural Electrification Programe through Alternative / Renewable Energy Technologies |
| 2. | Solar Homes Project in Each Province |
| 3. | Development of Supply Chain Mechanism for Pedal Generators, Hand Generators and LED Lanterns |
| 4. | Pilot Project of Production Plant of Bio-Diesel |
| 5. | Research on Development of 1 kW Fuel Cell Electric Vehicle in Pakistan using Existing Fuel Cell |
| 6. | Solar Water Pumping & Desalination |
| 7. | Solar Thermal Power Plant Technologies (Demonstration Units) |
| 8. | Electrification of Villages through Micro Wind Turbines |
| 9. | Pilot project for Development and Installation of 02 Micro Hydro Kaplan Turbines |
| 10. | Pilot project for Emerging Alternative Energy Technologies Demonstration in Pakistan |

# Footnotes

Alternative Energy Development Board (AEDB), Prime Minister’s Secretariat, Islamabad has provided the Material for this report.

Blends of 5%, 10%, 20% bio-diesel, respectively, with HSD.