# ATLAS Cathode Strip Chamber

Radiation Hardness Assurance Progress Report

Date : 				December 1, 2000

Report made by :	P. O’Connor

Institute:			BNL

Email:				poc@bnl.gov

1 General information on CSC boards

Name of the board: ASM-PACK (consists of a sandwich of two ASM 1 and one ASM 2 board)

Location: all boards to be interchangeable. Worst location: Z = 718cm, R = 89.4cm

Simulated Radiation Levels and Safety Factors[Nov. 18 draft of ATLAS Policy on Rad Hard Electronics]

|  | TID | NIEL | SEE |
| --- | --- | --- | --- |
| SRL | 126 (Gy/10yr) | 5.4 x 10^12 (1MeV n/cm2/10yr) | x 10^12 (>20MeV h/cm2/10yr) |
| SFsim | 3.5 | 5 | 5 |
| SFldr, COTS | 5 | 1 | 1 |
| SFldr, Rad-hard | 1.5 | 1 | 1 |
| SFlot, COTS | 4 | 4 | 4 |
| SFlot, ASIC | 2 | 2 | 2 |
| SFlot, Rad-hard ASIC | 1 | 1 | 1 |

2. Electronics components on each board

| Name/function | Part No. | Manufacturer/technology | Qty/ASM-PAK | Qty/system (incl. 10% spares) (one endcap only) | Status |
| --- | --- | --- | --- | --- | --- |
| Preamp/shaper | IC50 rev. 2 | HP/ 0.5um CMOS | 16 | 2816 | Prelim. TID qual done |
| 3.3V regulator | -- | -- | 2 | 352 | Not selected |
| SCA | HAMAC rev. 4 | DMILL | 16 | 2816 | Being qualified by LAr |
| Dual op-amp | AD8042 | Analog Devices | 32 | 5632 | Being qualified by LAr |
| 12-b ADC | AD9042 | Analog Devices | 16 | 2816 | Being qualified by LAr |
| PECL translator | MC10H116 | Motorola | 6 | 1056 | Being qualified by LAr |
| 5V regulator | -- | -- | 2 | 352 | Being qualified by LAr |
| 850nm transceiver | MDX-19-4-1-8 | Methode | 3 | 528 | Partially qualified by LAr |
| Glink serializer | HDMP1022 | HP | 2 | 352 | Being qualified by LAr |
| Glink de-serializer | HDMP1024 | HP | 1 | 176 | Qualification started |
| Multiplexer | -- | Technology not chosen | 2 | 176 | Not selected |

IC50: custom preamp/shaper, 16-channel chip, designed at BNL, uses HP 0.5um CMOS triple metal process

HAMAC rev. 4: custom analog memory, 12-channel chip, designed at Nevis/Saclay, fabricated in DMILL

3. Radiation test reports

No devices yet qualified