# IEEE P1451.3 Proposal

| Proposal Title: | Miscellaneous Modifications |
| --- | --- |
| Proposal Number: | 03-006 |
| Revision Number: | A |
| Date: | 2/19/2003 |
| Name: | Mark Slack |
| Company: | Boeing Commercial Airplanes |
| Phone Number: | 206-662-4771 |
| Fax Number: |  |
| Email Address: | mark.b.slack@boeing.com |
| Proposal Status: | Initial Draft X Revised Draft Ready for Vote |
| Impacts: | __ __ |
| Action: | __ Approved _X_ Approved with changes __ Rejected __ Returned for revision |

# Background:

The changes proposed herein are a direct result of anticipating how a Transducer Block will interpret information in various TEDS. These changes were originally included in Part B of P03-004.  That proposal was rejected by the Working Group with the expectation that Part B would be advanced as an independent proposal.

Among other minor fixes, we have recognized that the original definition of Channel Groups was actually two semantically distinct categories of Channel Groups.  Herein, we propose to separate the specification into Control Groups and Vector Group.

# Proposal:

# Clause 3 -- Definitions

3.2.11 Code-Division Multiple Access: Code-Division Multiple Access (CDMA) uses …

3.2.12 CommunicationsChannel: For the purposes of this standard, ...

3.2.13 ControlGroup: ControlGroups are manufacturer specifications that define the inherent relationships between the TransducerChannels of a multi-channel TBIM. This ControlGrouping information is not normally used by the TBIM itself. This information is used to identify TransducerChannels that are used to control some characteristic of another TransducerChannel. For example, a ControlGroup could be used to identify an actuator that is used to set the threshold of an analog event sensor.

3.2.67 VectorGroup: VectorGroups are manufacturer specifications that define the inherent relationships between the TransducerChannels of a multi-channel TBIM. This VectorGrouping information is not normally used by the TBIM itself. This information is normally used by bus controller applications to properly compose human readable displays or in formulating other computations. For example, VectorGroupings may be used to indicate which TransducerChannels represent the three vector axes of a three-axis vector measurement.

# Clause 4 -- Data types

Break Table 1 into 2 components to assign manifest constant. No change to textual description

# Table 1—Physical units data type structure

| Field | Description | Data Type | Number of octets |
| --- | --- | --- | --- |
| 1 | Physical units interpretation -- see Table 2 | U8E | 1 |
| 2 | (2 * <exponent of radians>) + 128 | U8C | 1 |
| 3 | (2 * <exponent of steradians>) + 128 | U8C | 1 |
| 4 | (2 * <exponent of meters>) + 128 | U8C | 1 |
| 5 | (2 * <exponent of kilograms>) + 128 | U8C | 1 |
| 6 | (2 * <exponent of seconds>) + 128 | U8C | 1 |
| 7 | (2 * <exponent of amperes>) + 128 | U8C | 1 |
| 8 | (2 * <exponent of kelvins>) + 128 | U8C | 1 |
| 9 | (2 * <exponent of moles>) + 128 | U8C | 1 |
| 10 | (2 * <exponent of candelas>) + 128 | U8C | 1 |

# Table 2—Physical units interpretation

| Value | Manifest constant | Definition |
| --- | --- | --- |
| 0 | PUI_SI_UNITS | Unit is described by the product of SI base units, plus radians and steradians, raised to the powers recorded in fields 2 through 10. Units for some quantities, such as the number of people through a turnstile, cannot be represented using these units. Enumeration zero, with fields 2-10 set to 128, is the appropriate enumeration for these cases when a quantity is being defined. |
| 1 | PUI_RATIO_SI_UNITS | Unit is U/U, where U is described by the product of SI base units, plus radians and steradians, raised to the powers recorded in fields 2 through 10. |
| 2 | PUI_LOG10_SI_UNITS | Unit is log10(U), where U is described by the product of SI base units, plus radians and steradians, raised to the powers recorded in fields 2 through 10. |
| 3 | PUI_LOG10_RATIO_SI_UNITS | Unit is log10(U/U), where U is described by the product of SI base units, plus radians and steradians, raised to the powers recorded in fields 2 through 10. |
| 4 | PUI_DIGITAL_DATA | The associated quantity is digital data (e.g. a bit vector) and has no unit. Fields 2-10 shall be set to 128. The "digital data" type applies to data that does not represent a quantity, such as the current positions of a bank of switches. |
| 5 | PUI_ARBITRARY | The associated physical quantity is represented by values on an arbitrary scale (e.g. hardness). Fields 2-10 are reserved, and shall be set to 128. |
| 6-255 | — | Reserved |

# Clause 5 -- Functional spec

New sub-clause, inserted before 5.6 (TransducerChannel Proxy)

5.6	TransducerChannel groups

There are two types of TransducerChannel groups defined in this standard. They are ControlGroups and VectorGroups. They are similar in implementation but are used for two different functions.

5.6.1	ControlGroups

# ControlGroups are used to define collections of TransducerChannels when one TransducerChannel is the primary channel and the remaining TransducerChannels in the group provide either additional information about the primary TransducerChannel or are used to control some aspect of the primary TransducerChannel. For example, a ControlGroup can be used to define up to three additional TransducerChannels associated with an analog event sensor. One is a sensor that is used to measure the analog input to the event sensor. The second is an actuator that is used to set the threshold for the event sensor. The third is an actuator that can be used to set the hysteresis for the event sensor.5.6.2	VectorGroups

VectorGroups are used to define relationships between TransducerChannels within a single multi-channel TBIM that imply a display or mathematical relationship between the TransducerChannels. For example, they can be used to identify the relationships between the components of a three-axis accelerometer. VectorGroups are used by the software in the TBC/NCAP or host processor to group the outputs of the individual TransducerChannels into vectors for display or computational purposes.

Note: VectorGroups are in some ways similar to TransducerChannel proxies. TransducerChannel proxies are used to identify TransducerChannels that are grouped together for reasons such as efficient transmission of the data and/or simultaneous triggering. Proxies may or may not represent a vector for display or computational purposes. However, it is recommended that all vectors be implemented as proxies, especially in spatial vector applications (like velocity or acceleration), where the measurements of the three components at different points in time could lead to misinterpretation.

# Change Meta-TEDS

7.3.2	Data block

Table 37 summarizes the content of the data block. Subordinate subclauses explain each data field in this data block.

# Table 37—Structure of the Meta-TEDS data block

| Field | Description | Type | # octets |
| --- | --- | --- | --- |
| — | Length | U32L | 4 |
| 1 | TEDS identifier | U8E | 1 |
| 2 | IEEE P1451 standards family number | U8E | 1 |
| 3 | TEDS version number | U8E | 1 |
| — | Timing related information | — | — |
| 4 | TEDS hold-off time (tth) | F32 | 4 |
| 5 | Operational hold-off time (toh) | F32 | 4 |
| 6 | Load current drawn from the transducer bus | F32 | 4 |
| 7 | Multi-range Capability | U8E | 1 |
| — | ControlGroup information sub-block | — | — |
| 8 | Number of ControlGroups (Nc) | U8C | 1 |
| — | Fields 9, 10, and 11 comprise a structure that defines one ControlGroup. All ControlGroup structures (Nc occurrences) shall be specified consecutively. | — | — |
| 9 | ControlGroup type | U8E | 1 |
| 10 | Number of TransducerChannels in the ControlGroup (NTc) | U8C | 1 |
| 11 | ControlGroup member list | array of U8E | NTc |
| — | VectorGroup information sub-block | — | — |
| 12 | Number of VectorGroups (Nv) | U8C | 1 |
| — | Fields 13, 14, and 15 comprise a structure that defines one VectorGroup. All VectorGroup structures (Nv occurrences) shall be specified consecutively. | — | — |
| 13 | VectorGroup type | U8E | 1 |
| 14 | Number of TransducerChannels in the VectorGroup (NTv) | U8C | 1 |
| 15 | VectorGroup member list | array of U8E | NTv |
| — | TransducerChannel proxy definition sub-block | — | — |
| 16 | Number of TransducerChannel proxies (Np) | U8C | 1 |
| — | Fields 17, 18, 19, and 20 comprise a structure that defines one TransducerChannel proxy. All proxy definition structures (Np occurrences) shall be specified consecutively. | — | — |
| 17 | TransducerChannel number of the TransducerChannel proxy | U8E | 1 |
| 18 | TransducerChannel proxy data set organization | U8E | 1 |
| 19 | Number of TransducerChannels represented by this proxy (NTp) | U8C | 1 |
| 20 | TransducerChannel proxy member list | array of U8E | NTp |
| — | Checksum | U16C | 2 |

7.3.2.8	Number of ControlGroups

Data type: unsigned octet integer used for enumeration (U8C, 1 octet)

This field identifies the number of ControlGroups that follow.

# 7.3.2.9	ControlGroup type

Data type: unsigned octet integer used for enumeration (U8E, 1 octet)

This field contains the relationship between the TransducerChannels comprising the specific ControlGroup. It is defined by the enumeration in Table 40.

# Table 40—Enumeration of ControlGroup types

| Value | Entry | Meaning |
| --- | --- | --- |
| 0 |  | Reserved |
| 1 | 1 2 3 4 | Analog event sensor TransducerChannel, Analog input sensor TransducerChannel Upper threshold embedded actuator TransducerChannel Hysteresis embedded actuator TransducerChannel |
| 2 | 1 2 3 4 | Sensor TransducerChannel (any type) High pass filter embedded actuator TransducerChannel Low pass filter embedded actuator TransducerChannel Scale factor embedded actuator TransducerChannel |
| 3 | 1 2 | TransducerChannel (any type) Sample interval embedded actuator TransducerChannel |
| 4 | 1 2 3 | Digital event sensor TransducerChannel Digital input sensor TransducerChannel Event pattern embedded actuator TransducerChannel |
| 5 | 1 2 | Time interval sensor TransducerChannel TransducerChannel number of the transducer that causes the output of the time interval sensor to be latched. |
| 6 | 1 2 | Time-of-day sensor TransducerChannel TransducerChannel number of the transducer that causes the output of the time-of-day sensor to be latched. |
| 7 | 1 2 — | TransducerChannel number of an event sensor used to trigger other transducers. The number, N, of transducers triggered by the event sensor. The remaining N entries give a list of TransducerChannels triggered by the event |
| 8 | 1 2 | TransducerChannel (any type), Embedded time delay actuator TransducerChannel |
| 9-127 |  | Reserved for future expansion |
| 128-255 |  | open to manufacturers |

Enumerations 1 and 4 may be used to identify the embedded actuator TransducerChannels used to set up an event sensor. They also identify a sensor TransducerChannel that may be used to read the level of the signal in an analog event sensor or the current pattern input to a digital event sensor.

Enumeration 2 may be used to identify the embedded actuator TransducerChannels used to set the high pass filter, low pass filter, and scale factor associated with a sensor of any type.

Enumeration 3 is used to identify an embedded actuator TransducerChannel that may be used to set the TransducerChannel sampling period.

7.3.2.10	Number of TransducerChannels in the ControlGroup

Data type: unsigned octet integer used for enumeration (U8C, 1 octet)

This field identifies the number of TransducerChannels in the group, which is the number of entries required in the list described in 7.3.2.11.

# 7.3.2.11	ControlGroup member list

Data type: an array of unsigned octet integers used for enumeration (U8E, 0 to 255 octets)

This field contains a one-dimensional array (list) of 1-octet elements. Each element is the TransducerChannel number for a member in the specific ControlGroup. The values of the elements in this list shall be in the sequence specified by the ControlGroup type field.

An element with value zero shall indicate that the TransducerChannel does not implement this particular element of the enumerated relationship. For example, a ControlGroup describing an analog event sensor that implements the ability to change the threshold and hysteresis but does not implement a sensor to read the analog input could be specified by (1,0,2,3), where the TransducerChannel number for the event sensor is 1, for the threshold actuator is 2 and the hysteresis actuator is 3.

NOTE—a TransducerChannel may be represented in multiple ControlGroups.

# 7.3.2.12	Number of VectorGroups

Data type: unsigned octet integer used for enumeration (U8C, 1 octet)

This field identifies the number of VectorGroups that follow.

# 7.3.2.13	VectorGroup type

Data type: unsigned octet integer used for enumeration (U8E, 1 octet)

This field contains the relationship between the TransducerChannels comprising the specific VectorGroup. It is defined by the enumeration in Table 41.

# Table 41—Enumeration of VectorGroup types

| Value | Entry | Meaning |
| --- | --- | --- |
| 0 | — | an arbitrary relation |
| 1 | 1 2 3 | x component of a right hand rectangular spatial vector y component of a right hand rectangular spatial vector z component of a right hand rectangular spatial vector |
| 2 | 1 2 3 | ( component of a right hand cylindrical spatial vector ( component of a right hand cylindrical spatial vector z component of a right hand cylindrical spatial vector |
| 3 | 1 2 3 | r component of a right hand spherical spatial vector ( component of a right hand spherical spatial vector ( component of a right hand spherical spatial vector |
| 4 | 1 2 3 | latitude component of a planetary coordinate system longitude component of a planetary coordinate system altitude component of a planetary coordinate system |
| 5 | 1 2 | in-phase component of a 2-dimensional vector quadrature component of a 2-dimensional vector |
| 6 | 1 2 3 | red component in a color vector green component in a color vector blue component in a color vector |
| 7-127 |  | Reserved for future expansion |
| 128-255 |  | open to manufacturers |

The arbitrary relation, when the enumeration value is equal to zero, shall be used to convey VectorGroup semantics not specifically enumerated by this subclause, but deemed necessary by the TransducerChannel manufacturer, for the correct operation or interpretation of the data related to the TransducerChannels that are members of the VectorGroup.

The arbitrary relation may be used to convey that correct behavior of TransducerChannels with coupling terms in the calibration assumes that all TransducerChannels involved are triggered at the same time.

7.3.2.14	Number of TransducerChannels in the VectorGroup

Data type: unsigned octet integer used for enumeration (U8C, 1 octet)

This field identifies the number of TransducerChannels in the group, which is the number of entries required in the list described in 7.3.2.15.

# 7.3.2.15	VectorGroup member list

Data type: an array of unsigned octet integers used for enumeration (U8E, 0 to 255 octets)

This field contains a one-dimensional array (list) of 1-octet elements. Each element is the TransducerChannel number for a member in the specific VectorGroup. The values of the elements in this list shall be in the sequence specified by the VectorGroup type field.

An element with value zero shall indicate that the TransducerChannel does not implement this particular element of the enumerated relationship. For example, a two axis vector measurement implemented by TransducerChannels 1 (x) and 2 (y) may be specified by designating the VectorGroup type (7.3.2.13) as 1 (x, y, z) with the VectorGroup member list of (1, 2, 0). The value zero shall not appear in the VectorGroup member list for a VectorGroup of VectorGroup type ‘arbitrary relation.’

A TransducerChannel may not be represented in multiple VectorGroups.

7.3.2.16	Number of TransducerChannel proxies

No change to text for the remainder of 7.3.  Paragraph numbers and Table/Figure numbers ripple.

# Incidental change TransducerChannel TEDS

7.4.2.2	Calibration key

Data type: unsigned octet integer used for enumeration (U8E, 1 octet)

This field contains an enumeration that denotes the calibration capabilities of this TransducerChannel. Table 43 provides the list of enumerated values and their meanings. The column labeled “Name” defines manifest constants to symbolize the enumerated values, and these names are used throughout the remainder of this standard.

# Table 43—Enumeration of calibration keys

| Value | Calibration capability | Name |
| --- | --- | --- |
| 0 | No calibration information needed or provided by the TBIM. This implies that there is no Calibration TEDS associated with this TransducerChannel. See Note. | CAL_NONE |
| 1 | Calibration information provided as a Calibration TEDS, as specified in 7.5. Correction is performed outside of the TBIM. | CAL_SUPPLIED |
| 2 | (reserved) | - |
| 3 | Calibration information is provided but in a form that is not described in this standard. Correction is performed outside of the TBIM. See Note. | CAL_CUSTOM |
| 4 | Calibration information is provided as a Calibration TEDS, as specified in 7.5. Correction is applied in the TBIM. See 7.5.1.2 for additional details. | TBIM_CAL_ SUPPLIED |
| 5 | Calibration information is provided as a Calibration TEDS, as specified in 7.5, and is applied in the TBIM. The calibration is adjusted by a self-calibration capability. See 7.5.1.2 for additional details. | TBIM_CAL_SELF |
| 6 | Calibration information is provided but in a form that is not described in this standard. It may be a manufacturer-defined TEDS. Correction is performed in the TBIM. See Note. | TBIM_CAL_CUSTOM |
| 7-255 | Reserved | — |
| Note—If the Calibration TEDS is accessed, the Calibration TEDS Length shall be zero |

7.4.2.2.1	System corrections

Calibration key enumerations CAL_SUPPLIED or CAL_CUSTOM are to be used when the correction is performed in the NCAP, a host processor or elsewhere in the system.

7.4.2.2.2	TBIM corrections

Calibration key enumerations TBIM_CAL_SUPPLIED and TBIM_CAL_SELF are to be used when the correction is performed in the TBIM using the correction method specified in 7.5.1.1 and information stored in the Calibration TEDS (7.5.3). TBIM_CAL_CUSTOM is used when the correction method is not the one specified in 7.5.1.1.

7.4.2.3	TransducerChannel type key	<<No change>>

7.4.2.4	Physical units

Data type: physical units (UNITS, 10 octets).

The physical units that apply to the TransducerChannel data. If the Calibration key is CAL_SUPPLIED or CAL_CUSTOM, the physical units apply only to the TransducerChannel data after correction for the case of sensors, or before correction for the case of actuators.

See 4.11 for details on how to construct the value placed in the Physical units fields.

7.4.2.5	Design operational lower range limit	<<No change>>

7.4.2.6	Design operational upper range limit	<<No change>>

7.4.2.7	Worst case uncertainty	<<No change>>

7.4.2.8	Self-test key	<<No change>>

7.4.2.9	Data model

Data type: unsigned octet integer used for enumeration (U8E, 1 octet)

This field describes the data model used when issuing Read TransducerChannel data or Write TransducerChannel data commands to this TransducerChannel. Values are enumerated in Table 46.

# Table 46—Enumeration of data models

| Value | Model | Constraint on data model length |
| --- | --- | --- |
| 0 | N-octet integer (unsigned) | 0(N(8 |
| 1 | Single precision real | N=4 |
| 2 | Double precision real | N=8 |
| 3 | N-octet fraction (unsigned) | 0(N(8 |
| 4 | Bit sequence | 0(N(255 |
| 5 | Long integer (unsigned) | 9(N(255 |
| 6 | Long fraction (unsigned) | 9(N(255 |
| 7 | Time of day | N=8 |
| 8 - 255 | Reserved for future expansion | — |

There are two differences between the integer forms (enumeration zero and five) and fractional forms (enumeration three and six):

The radix point (which divides integer from fractional bits) is to the right of the least significant bit for N-octet integer. It is immediately to the right of the most significant bit for N-octet fraction.

Justification of the significant bits differs, as explained in the Model significant bits field (xxx).

The use of enumerations 5 and 6 is expected to be rare. An NCAP is not expected to process data with these enumerations but may pass them on unprocessed to the entity requesting the data.

The N-octet fraction type may be used to keep the multinomial coefficients (see xxx) within representable bounds and to avoid overflows when converting the data to physical units.

The bit sequence data model is for collections of bits that have no numeric value. An example of this type is the position of each switch in a bank of switches. Bit significance is user defined.

Boolean data (such as {0,1} or {false, true}) shall be represented as a bit sequence with a length of one octet, in which the data resides in the least significant bit.

The Time of day data model supports Time-of-day (ToD) data types defined in 4.13.

7.4.2.10	Data model length	<<No change>>

7.4.2.11	Model significant bits

Data type: unsigned 16-bit integer used for counting (U16C, 2 octets)

When the Data model is N-octet integer (enumeration 0 or 5) or N-octet fraction (enumeration 3 or 6), the value of this field is the number of bits that are significant.

For example, if data from a TransducerChannel comes from a 12-bit ADC, then:

Data model	= 0	(N-octet integer)

Data model length	= 2	(the number of octets needed to hold 12 bits)

Model significant bits	= 12

When the Data model is N-octet integer, N-octet fraction, long integer or long fraction, the Model significant bits shall not exceed eight times the Data model length.

When the Data model is N-octet integer or long integer, the data bits shall be right justified within the octet stream. Model significant bits specifies the number of bits that are significant. A value of zero is illegal.

When the Data model is N-octet fraction or long fraction, the data bits shall be left justified within the octet stream. Model significant bits is ignored.

When the Data model is single or double precision real (enumerations one or two), the value of this field is the number of bits in the TransducerChannel’s signal converter.

When the Data model is Time of day, Model significant bits is ignored.

# Incidental change Calibration TEDS

7.5.1.2	Application

If the value of the Calibration key field (7.4.2.2) in the TransducerChannel TEDS is CAL_SUPPLIED, the correction algorithm shall be performed in the NCAP, a host processor or elsewhere in the system. It is recommended that it be performed in the NCAP.

If the value of the Calibration key field is TBIM_CAL_SUPPLIED or TBIM_CAL_SELF, then the correction algorithm shall be performed in the TBIM.

All remaining text in 7.5.1.2 remains unchanged.

# Incidental change Commisioning TEDS

# 7.10.2	Data block

Table 63 shows the structure of the data block for this TEDS. The content is user defined.

# Table 63—Structure of the Commissioning TEDS data block

| Field | Description | Type | # octets |
| --- | --- | --- | --- |
| — | TEDS length | U32L | 4 |
| 1 | Character set | U8E | 1 |
| 2 | Character code | U8E | 1 |
| 3 | Language | U8E | 1 |
| 4 | Length, in octets | U8C | 1 |
| 5 | Parameter name | U8E | N |
| — | Checksum | U16C | 2 |

The manufacturer shall determine the size of this TEDS, but as a minimum, the TEDS shall be at least 42 octets to accommodate a 32-character parameter name.

# Incidental change to text that was located at 5.8.6 in D2.02, but moved to Appendix J by Proposal P03-002

J.4	Trigger logic based on event recognition

The functional block diagram in Figure J.4 depicts a TransducerChannel that is triggered by an event sensor. An event sensor may have additional embedded actuators to implement features such as a programmable analog threshold and hysteresis or a programmable digital pattern.

# Figure J.4

The event sensor has a special hardware relationship to one or more TransducerChannels. This should be identified as a ControlGroup with enumeration 7 in the Meta TEDS. A trigger message issued to the event sensor causes the event sensor to begin monitoring. The occurrence of the event, which may cause the Data Transport Logic to issue a trigger acknowledgment (if appropriate), may also be used to trigger the associated TransducerChannel(s).

The manufacturer may not honor a trigger message addressed to the TransducerChannels so configured.

# Comments

In order to properly fill out this form, you MUST do the following:

- Click on the CUSTOM tab, under FILE,PROPERTIES.

- Click on the PropTitle property, enter your proposal name, click on MODIFY.

- Click on the PropDate property, enter the date, click on MODIFY.

- Click on the PropRev property, enter your revision symbol (space is OK, empty is not), click on MODIFY.

- In NORMAL view, click on SELECT ALL under the EDIT menu.

- Press the F9 key to update fields.