#### Pixel Trigger

### Current or Permanent:

- Implemented in FPGA.

- FO Links between detector area and trigger and DAQ upstairs.

### Options that need more info:

- Hold raw data or translated data in L1 buffer.

- Simple or CENTER-OF-MASS cluster finder? Some analog or all digital data?

- Combine columns data into cluster processing?

- Need to simulate pattern-matching algorithms to select between BB33 and sweep.

- Where to split the hardware upstairs and downstairs?

- Define the dividing line between the pixel and trigger groups’ efforts.

### Current or Permanent:

- Implemented in a floating point Digital Signal Processor.

### Options that need more info:

- Microprocessor, DSP or neural net?

- Partition as quadrants or in Z?

- Cut segments first or after track finding?

- Remove quadrant segmentation at this step?

### Current or Permanent:

- Implemented in a floating point Digital Signal Processor.

### Options that need more info:

- Could this be done in the same fixed point DSP as the track processing?

- What information must the trigger output contain?

### Current Efforts:

- Simulations of segment algorithms – Erik & Penny

- Data flow and queuing analysis - ESE

- Pixel processor subgroup - Gustavo

- DSP software investigation – Erik.

# Text boxes

XY

XY

Pixels In

…

…

Station-7 Quad-1

Pixel Processor

Station-6 Quad-1

Pixel Processor

Station-5 Quad-1

Pixel Processor

XY

Segments Out

##### BB33 Algorithm

Y-Doublets  +     X Hits Out

8

XY

7

XY

6

XY

…

Station-7/8 Quad-1

Station-6/7 Quad-1

Station-5/6 Quad-1

…

Pixels In

Segments Out

##### Combined Algorithm

5

XY

Triplet

Finder &

X verifier

Triplet

Finder &

X verifier

Triplet

Finder &

X verifier

##### Sweep Algorithm

Segments Out

XY

XY

XY

Pixels In

…

…

Station-7 Quad-1

Pixel Processor

Station-6 Quad-1

Pixel Processor

Station-5 Quad-1

Pixel Processor