Removal of Regulations Allowing for Polished Frost on Wings of Airplanes

As it currently stands with flights being allowed to operate with polished frost on their wings upon takeoff, the industry is finding itself with unnecessary safety hazards.  Overall the practice of polishing wings is unsafe and unnecessary to have in the Federal Aviation Regulations. The reasons behind these beliefs are the lack of information regarding polished frost, the immense hazards caused by frost on the wings and control surfaces, and the lack of available resources	regarding the actual polishing.

Although polished frost is mentioned in the FAR’s as being an acceptable way of removing frost from the control surfaces and wings this is basically the extent of the information given on the subject.  If a pilot was to realize they were allowed to take off with polished frost on their plane, but they could not find any other information on the subject, how would they know how to do this procedure? Therefore the practice of flying with polished frost becomes even more dangerous due to the lack of knowledge known about it by the pilots.

While researching this NPRM as well as polished frost itself I surveyed ten of the local flight instructors and none of them even knew of the regulation allowing polished frost or what was meant by polished frost.   Since there is an obvious lack of knowledge and teaching practices of polished frost, the need to keep this rule the way it is does not make sense.

From what I believe to be some of the most important facts that prove polished frost should be removed from the FAR’s is the deaths due to frost on the wings, as well as how drastically it changes the aerodynamics.  In the NPRM itself it is stated that 11 accidents have occurred due to people attempting to polish or smooth frost.  Although I’m sure there have been other accidents due to frost that people did not try to polish, but these accidents occurred due to something the regulations specifically state to do.  There should not be a regulation so vague that no one knows the exact specifications of how to perform it and be safe while doing it.

Frost can be very detrimental to the characteristics of flight of the aircraft you are flying. As was stated in the NPRM there is many different ways your plane can be affected. A contaminated wing's maximum lift may be reduced by 30 percent or more.  Any loss of lift can change the characteristics flight greatly, especially if it was an inexperienced pilot who has only flown one type of plane and they were unable to recognize the change. The angle of attack for maximum lift may be reduced by several degrees and could lead to panic with the pilot if they are unaware this is going to happen. Upon takeoff roll an increase of drag could greatly increase the distance for lift off.  Even if the frost is polished smooth the increase in drag could be drastic. Finally the airplane's handling qualities and performance may change unexpectedly from that of the uncontaminated aircraft.

For anyone who is trying to fly a plane which has frost on it, whether polished or not, should know the risks of flying with frost.  Although I’m sure that most of the people do not take time to think of the associated risks of flying with frost on their plane, but if someone does not take the time to learn about these consequences, then they should not be attempting to polish the frost smooth anyway.

In dealing with the severity of the changes of aerodynamic principles of the plane with frost, one must take into consideration the amount of area covered as well as the thickness of the frost on the wing. Also stated in the NPRM the location of the roughness in accordance with the surface leading edge where significant variations greatly affect the airspeed and the surface air loads.

One major problem with the polishing of frost on the planes is just as the NPRM states that the manufacturer’s guidelines are to be used in referring to the procedure of how to go about it, but no manufacturers list how.  This just leads to more confusion in regards to the polishing of frost.  How can someone recommend checking the manufacturer’s guidelines in reference to polishing frost if none of the manufacturers provide guidelines on how to do it? Also while looking through many supplemental materials for information on the polishing of  frost on aircraft I was unable to find any information on the process or even that it existed outside of the FAR’s at all.

In conclusion polished frost procedures should be removed from the FAR’s. The practice of polishing frost on airplanes is dangerous because of the lack of a definition of what polished frost is.  Also the effect that frost alone can have on the aerodynamic principles of an aircraft is dangerous and can be fatal.  Finally no sources are available to gain information on the actual polishing of the frost, or the procedures on how to perform this task.  Therefore a regulation should not be kept in place that makes flying less safe because of its lack of structure.