PART I - SECTION B

SUPPLIES/SERVICES

SCOPE:  ITEMS 0001, 0002, 0003, & 0004 :  Furnish all labor, material, supplies, and equipment (except for specified FAA furnished materials) for (1) the construction of a Runway End Identifier Light (REIL) System to serve Runway 15 (Item 0001) at North Central State Airport, Pawtucket, Rhode Island; (2) for the construction of a REIL System to serve Runway 23 (Item 0002) at North Central State Airport, Pawtucket, Rhode Island; (3) for the construction of a Precision Approach Path Indicator (PAPI) to serve Runway 15 (Item 0003) at North Central State Airport, Pawtucket, Rhode Island; and (4) for the construction of a PAPI to serve Runway 23 (Item 0004) at North Central State Airport, Pawtucket, Rhode Island.  All work shall be in accordance with the attached Technical Specifications and Drawings, as identified in PART I – SECTION C.  The Drawings are attachments to the Technical Specifications.

Work associated with the construction of the facilities includes, but is not limited to:

- Layout,

- Site Preparation,

- Excavation,

- Installation of cast in-place (or pre-cast) reinforced concrete foundations,

- Pull box/hand hole installations,

- Electrical power service work,

- Underground electrical conduit/duct bank installation,

- Electrical cable installation and testing,

- Electrical grounding,

- Equipment assembly,

- Associated site work and cleanup,

- PAPI and REIL System acceptance.

ITEM #0001:  Construction of REIL on Runway 15 at North Central State Airport, Pawtucket, Rhode Island

ITEM #0002:  Construction of REIL on Runway 23 at North Central State Airport, Pawtucket, Rhode Island

ITEM #0003:  Construction of PAPI on Runway 15 at North Central State Airport, Pawtucket, Rhode Island

ITEM #0004:  Construction of PAPI on Runway 23 at North Central State Airport, Pawtucket, Rhode Island.

PART I - SECTION C

SPECIFICATIONS/DRAWINGS

1.  Technical Specifications for the Installation of Two Precision Approach Path Indicator (PAPI) Systems and Two Runway End Identifier Light (REIL) Systems to Serve Runways 15 & 23 at North Central State Airport, Pawtucket, Rhode Island, May 2006.

2. Appendix A – Advisory Circular – 150/5370.2E, Operational Safety on Airports During Construction & A Guide to Airport Ground Vehicle Operations.

3. Appendix B – FAA STD-019e, Lightning and Surge Protection, Grounding, Bonding and Shielding Requirements for Facilities and Electronic Equipment & FAA-C-1217f, Electrical Work, Interior.

4. Appendix C – Cable Test Data Forms.

5. Appendix D – Pre-construction/Maintenance Project Safety and Health Checklist.

6. Airport Ground Vehicle Operations/An FAA Guide.

7.  List of Drawings:

Item #0001:  Runway 15 REIL

| Cover Sheet | SFZ-D-REIL15-G101 |
| --- | --- |
| Index Sheet | SFZ-D-REIL15-G102 |
| General Notes & GFM List | SFZ-D-REIL15-G103 |
| General Airport Layout | SFZ-D-ALD-C101-PC02 |
| System Layout & Details | SFZ-D-REIL15-C101 |
| Foundation Details | SFZ-D-REIL15-S101 |
| Power and Control Station Equipment Installation | SFZ-D-REIL15-Q101 |
| System Wiring Diagram & Cable Schematic | SFZ-D-REIL15-E101 |
| Site Plan Power to Runway 15 REIL | SFZ-D-REIL15-E102 |

Item #0002:  Runway 23 REIL

| Cover Sheet | SFZ-D-REIL23-G101 |
| --- | --- |
| Index Sheet | SFZ-D-REIL23-G102 |
| General Notes & GFM List | SFZ-D-REIL23-G103 |
| Airport Layout | SFZ-D-ALD-C101-PC01 |
| General Power Service Layout | SFZ-D-REIL23-C101 |
| System Layout and Details | SFZ-D-REIL23-C102 |
| Foundation Details | SFZ-D-REIL23-S101 |
| Power and Control Station Equipment Installation | SFZ-D-REIL23-Q101 |
| System Wiring Diagram & Cable Schematic | SFZ-D-REIL23-E101 |

Item #0003:  Runway 15 PAPI

| Cover Sheet | SFZ-D-PAPI15-G101 |
| --- | --- |
| Index Sheet | SFZ-D-PAPI15-G102 |
| General Notes & GFM List | SFZ-D-PAPI15-G103 |
| General Airport Layout | SFZ-D-ALD-C101-PC03 |
| PAPI Site Plan | SFZ-D-PAPI15-C101 |
| Site Details | SFZ-D-PAPI15-C102 |
| Site Grounding Details | SFZ-D-PAPI15-C103 |
| Power and Control Station Foundation Design | SFZ-D-PAPI15-S101 |
| Lamp Housing Assembly (LHA) Foundation Design | SFZ-D-PAPI15-S102 |
| Power and Control Station Equipment Installation | SFZ-D-PAPI15-Q101 |
| Lamp Housing Assembly (LHA) Equipment Installation | SFZ-D-PAPI15-Q102 |
| System Block Diagram | SFZ-D-PAPI15-E101 |
| System Wiring Diagram | SFZ-D-PAPI15-E102 |

Item #0004:  Runway 23 PAPI

| Cover Sheet | SFZ-D-PAPI23-G101 |
| --- | --- |
| Index Sheet | SFZ-D-PAPI23-G102 |
| General Notes & GFM List | SFZ-D-PAPI23-G103 |
| General Airport Layout | SFZ-D-ALD-C101-PC04 |
| PAPI Site Plan | SFZ-D-PAPI23-C101 |
| Site Details | SFZ-D-PAPI23-C102 |
| Site Grounding Details | SFZ-D-PAPI23-C103 |
| Power and Control Station Foundation Design | SFZ-D-PAPI23-S101 |
| Lamp Housing Assembly (LHA) Foundation Design | SFZ-D-PAPI23-S102 |
| Power and Control Station Equipment Installation | SFZ-D-PAPI23-Q101 |
| Lamp Housing Assembly (LHA) Equipment Installation | SFZ-D-PAPI23-Q102 |
| System Block Diagram | SFZ-D-PAPI23-E101 |
| System Wiring Diagram | SFZ-D-PAPI23-E102 |

PART I - SECTION D

WAGE RATE DETERMINATION

In accordance with Clause No. 3.6.2-18 entitled “Davis-Bacon Act”, for any laborer or mechanic that is employed in a classification that is not listed in the following wage determination, after contract award the contractor is required to submit to the Contracting Officer, Standard Form 1444, Request for Authorization of Additional Classification and Rate.  The request shall contain the proposed additional classification and minimum wage rate including any fringe benefit payments.

The applicable wage rate determination is U.S. Department of Labor General Decision No. RI030001, dated January 5, 2007 for Pawtucket, Rhode Island, in Providence County, attached hereto, and made a part thereof.

PART I - SECTION E

INSPECTION AND ACCEPTANCE

3.10.4-10     Inspection of Construction (July 2001)

- 'Work' includes, but is not limited to, materials, workmanship, and manufacture and fabrication of components.

(b) The Contractor shall maintain an adequate inspection system and perform such inspections as will ensure that the work performed under the contract conforms to contract requirements. The Contractor shall maintain complete inspection records and make them available to the Government. All work shall be conducted under the general direction of the Contracting Officer and is subject to Government inspection and test at all places and at all reasonable times before acceptance to ensure strict compliance with the terms of the contract.

(c) Government inspections and tests are for the sole benefit of the Government and do not--

(1) Relieve the Contractor of responsibility for providing adequate quality control measures;

(2) Relieve the Contractor of responsibility for damage to or loss of the material before acceptance;

(3) Constitute or imply acceptance; or

(4) Affect the continuing rights of the Government after acceptance of the completed work under paragraph (i) below.

(d) The presence or absence of a Government inspector does not relieve the Contractor from any contract requirement, nor is the inspector authorized to change any term or condition of the specification without the Contracting Officer's written authorization.

(e) The Contractor shall promptly furnish, without additional charge, all facilities, labor, and material reasonably needed for performing such safe and convenient inspections and tests as may be required by the Contracting Officer. The Government may charge to the Contractor any additional cost of inspection or test when work is not ready at the time specified by the Contractor for inspection or test, or when prior rejection makes reinspection or retest necessary. The Government shall perform all inspections and tests in a manner that will not unnecessarily delay the work. Special, full size, and performance tests shall be performed as described in the contract.
(f) The Contractor shall, without charge, replace or correct work found by the Government not to conform to contract requirements, unless the Government determines that it is in the public interest to accept the work with an appropriate adjustment in contract price. The Contractor shall promptly segregate and remove rejected material from the premises.

(g) If the Contractor does not promptly replace or correct rejected work, the Government may:

(1) by contract or otherwise, replace or correct the work and charge the cost to the Contractor or 

(2) terminate for default the Contractor's right to proceed.

(h) If, before acceptance of the entire work, the Government decides to examine already completed work by removing it or tearing it out, the Contractor, on request, shall promptly furnish all necessary facilities, labor, and material. If the work is found to be defective or nonconforming in any material respect due to the fault of the Contractor or its subcontractors, the Contractor shall defray the expenses of the examination and of satisfactory reconstruction. However, if the work is found to meet contract requirements, the Contracting Officer shall make an equitable adjustment for the additional services involved in the examination and reconstruction, including, if completion of the work was thereby delayed, an extension of time.

(i) Unless otherwise specified in the contract, the Government shall accept, as promptly as practicable after completion and inspection, all work required by the contract or that portion of the work the Contracting Officer determines can be accepted separately. Acceptance shall be final and conclusive except for latent defects, fraud, gross mistakes amounting to fraud, or the Government's rights under any warranty or guarantee.

(End of clause)

PART I - SECTION F

DELIVERIES OR PERFORMANCE

3.1-1      	Clauses and Provisions Incorporated by Reference (December 2005)

This screening information request (SIR) or contract, as applicable, incorporates by reference the provisions or clauses listed below with the same force and effect as if they were given in full text. Upon request, the Contracting Officer will make the full text available, or offerors and contractors may obtain the full text via Internet at:

http://www.asu.faa.gov/conwrite/ (on this web page, select "Search and View Clauses").

3.2.2.3-51 	Operations and Storage Areas (July 2004)

3.2.2.3-53 	Cleaning Up and Roadway Maintenance (July 2004)

3.2.2.3-54 	Preventing Accidents  (July 2004)

3.2.2.3-58 	Layout of Work (July 2004)

3.2.2.3-60 	Specifications, Drawings, and Material Offers (July 2004)

3.2.2.3-68 	Safety and Health (July 2004)

3.10.1-11  	Government Delay of Work (April 1996)

F.1     Starting, Performing, and Completing Work (July 2004)

The Contractor (you) must 
(a) begin work under this contract within five (5) calendar days after the effective date of the Notice to Proceed, 
(b) perform the work diligently, and 
(c) complete the entire work ready for use not later than sixty (60) calendar days after the effective date of the Notice to Proceed.  The time allowed for completion must include final cleanup of the premises.

3.2.2.3-41 	Performing Work  (July 2004)

The Contractor (you) must perform, using your own organization, work equivalent to at least fifteen (15) percent of the total amount of work under the contract on the site. The CO may modify this contract to reduce this percentage if you request a reduction and the CO determines that it would be to the Government's advantage to do so.

(End of clause)

3.2.2.3-42 	Differing Site Conditions (July 2004)

(a) Before the conditions are disturbed, the Contractor (you) must promptly notify the Contractor Officer (CO) in writing of either or both of the following conditions:

(1) Subsurface or latent physical conditions at the site which differ materially from those described in this contract.

(2) Unknown physical conditions at the site, of an unusual nature, which differ materially from those ordinarily encountered and generally recognized as inherent to the type of work the contract covers.

(b) FAA (we) will investigate the site conditions promptly after receiving the notice. If the CO determines that the conditions do materially differ and cause an increase or decrease in your cost of, or the time required for, performing any part of the work under this contract, the CO will make an equitable adjustment under this clause and modify the contract accordingly in writing.

(c) The CO will not accept your request for an equitable adjustment to the contract unless you give the written notice. However, the CO may extend the time for giving written notice.

(d) The CO will not accept your request for an equitable adjustment for differing site conditions after we make final payment under this contract.

(End of clause)

3.2.2.3-43 	Site Investigation and Conditions Affecting the Work (July 2004)

(a) The Contractor (you) acknowledges that you have taken reasonable steps to determine the nature and location of the work, and you have investigated and are satisfied about the general and local conditions which can affect the work or its cost, including but not limited to:

(1) Conditions bearing upon transportation, disposal, handling, and storage of materials;

(2) The availability of labor, water, electric power, and roads;

(3) Uncertainties of weather, river stages, tides, or similar physical conditions at the site;

(4) The conformation and conditions of the ground; and

(5) The character of equipment and facilities needed before and during the work.

You also acknowledge that you are satisfied as to the character, quality, and quantity of surface and subsurface materials or obstacles you might find, to the extent you can, from an inspection of the site, including all exploratory work done by FAA (we, us), as well as from the drawings and specifications that are a part of this contract. If you do not take the actions described and acknowledged in this paragraph, you will still be responsible for properly estimating the difficulty and cost of successfully performing the work, and for proceeding to successfully perform the work without additional expense to us.

(b) We are not responsible for your conclusions or interpretations of information we provided before contract award.  We are not responsible for your understanding of conditions you get from any of our officers or agents before contract award.  You can rely on representations we make about conditions that we put into the contract.

(End of clause)

3.2.2.3-45 	Material and Workmanship (July 2004)

(a)  The Contractor (you) must incorporate equipment, material, and articles that are new and of the most suitable grade for the purpose intended to do the work this contract covers, unless the contract provides otherwise. The FAA (we) encourages you to use recycled materials to manufacture the products. If the contract specifies equipment, material, or articles by trade name, make, or catalog number, you must use those specific items.  We will not accept equivalent items unless the specification authorizes it.

(b) You must perform all work under this contract in a skillful and workmanlike manner. The Contracting Officer (CO) may require, in writing, that you remove employees whom the CO determines are incompetent, careless, or otherwise objectionable.

(End of clause)

3.2.2.3-46 	Supervising the Contract Work (July 2004)

At all times while the Contractor (you) performs this contract, and until you complete the work and FAA accepts it, you must directly supervise the work or assign and have on the worksite a competent supervisor who the Contracting Officer (CO) is satisfied with and who has authority to act for you.

(End of clause)

3.2.2.3-47 	Permits and Responsibilities (July 2004)

The Contractor (you) must get any necessary licenses and permits, and comply with any Federal, state, and municipal laws, codes, and regulations applicable to the work, at no additional expense to FAA (we). You are also responsible for all damages to persons or property that happen due to your fault or negligence, and you must take proper safety and health precautions to protect the work, the workers, the public, and the property of others. You are also responsible for all materials delivered and work performed until you complete and we accept the entire work, except for any completed unit of work that may have already been accepted under the contract.

3.2.2.3-48 	Other Contracts (July 2004)

FAA (we, our) may undertake or award other contracts for additional work, or may use in-house construction resources that are at or near the work site. The Contractor (you) must cooperate fully with those other contractors and with our employees, and carefully adapt scheduling the work under this contract to accommodate simultaneous work, following any direction from the Contracting Officer (CO). You must not commit or permit any act that will interfere with the work of any other contractors or FAA employees.

(End of clause)

3.2.2.3-50 	Property Protection (July 2004)

(a) The Contractor (you) must construct and maintain any temporary fences, gates and other facilities needed to preserve crops, control livestock, and protect property. Before cutting a fence, you must take necessary precautions to prevent livestock from straying.  You must also prevent loss of tension in or damage to adjacent portions of the fence.  You must immediately replace all fencing and gates you cut, remove, damage, or destroy with new materials to the original standard.  You may reuse undamaged gates.

(b) You must comply with the property owner's requests to leave gates open or closed.

(c) You must use all necessary precautions to avoid destroying surveying markers such as section corners, witness trees, property corners, mining claim markers, bench markers, triangulation stations, and the like.  If you must destroy any marker, you must first notify the agency responsible for the marker, as well as the Contracting Officer's (CO) technical representative, and replace the markers.

(d) You must use care to prevent unnecessary damage to property in or near the work area caused by your work. Unnecessary damage is that which you can avoid through efficient and careful performance of the work, taking into account the land rights you have.  If you damage any property, you must at once notify the owner or custodian and make or arrange to make prompt and full restitution.

(e) Maps and specifications FAA (we, us) provides may not give the location of all water supply, drainage, irrigation, and other underground facilities. Before entering a tract of land for contract purposes, you must find out from the property owner (or other reasonably available source) the location of any irrigation system, domestic water system, source of water, and drainage system existing on the property, whether serving that property or other property. You must avoid damaging or obstructing these facilities or polluting water supplies.

(f) You must hold us harmless from any and all suits, actions, and claims for damages, including environmental impairment, to property arising from any of your acts or omissions, your subcontractors, or any of your employees or subcontractor employees, in any way related to the work or operations under this contract.

(g) You must indemnify and hold harmless the property owners or parties lawfully in possession against all claims or liabilities asserted by third parties, including all governmental agencies, resulting directly or indirectly from your wrongful or negligent acts or omissions.

(End of clause)

PART I - SECTION G

CONTRACT ADMINISTRATION DATA

3.1-1      	Clauses and Provisions Incorporated by Reference (December 2005)

This screening information request (SIR) or contract, as applicable, incorporates by reference the provisions or clauses listed below with the same force and effect as if they were given in full text. Upon request, the Contracting Officer will make the full text available, or offerors and contractors may obtain the full text via Internet at:

http://www.asu.faa.gov/conwrite/ (on this web page, select "Search and View Clauses").

3.2.2.3-62     Preconstruction Conference (July 2004)

The successful offeror must attend a pre-construction conference at a site the Contracting Officer designates before starting the work.

(End of clause)

3.10.1-22     Contracting Officer's Technical Representative (July 1996)

(a) The Contracting Officer may designate other Government personnel (known as the Contracting Officer's Technical Representative) to act as his or her authorized representative for contract administration functions which do not involve changes to the scope, price, schedule, or terms and conditions of the contract. The designation will be in writing, signed by the Contracting Officer, and will set forth the authorities and limitations of the representative(s) under the contract. Such designation will not contain authority to sign contractual documents, order contract changes, modify contract terms, or create any commitment or liability on the part of the Government different from that set forth in the contract.

(b) The Contractor shall immediately contact the Contracting Officer is there is any question regarding the authority of an individual to act on behalf of the Contracting Officer under this contract.

(End of clause)

PART I - SECTION H

SPECIAL CONTRACT REQUIREMENTS

NOT APPLICABLE

PART II - SECTION I

CONTRACT CLAUSES

3.1-1      	Clauses and Provisions Incorporated by Reference (December 2005)

This screening information request (SIR) or contract, as applicable, incorporates by reference the provisions or clauses listed below with the same force and effect as if they were given in full text. Upon request, the Contracting Officer will make the full text available, or offerors and contractors may obtain the full text via Internet at:

http://www.asu.faa.gov/conwrite/ (on this web page, select "Search and View Clauses").

3.2.2.3-33 	Order of Precedence (July 2004)

3.2.2.7-6  	Protecting the Government’s Interest when Subcontracting with Contractors Debarred, Suspended, or Proposed for Debarment (April 1996)

3.2.5-1    	Officials Not to Benefit (April 1996)

3.2.5-3    	Gratuities or Gifts (January 1999)

3.2.5-4    	Contingent Fees (October 1996)

3.2.5-5    	Anti-Kickback Procedures (October 1996)

3.2.5-7    	Disclosure Regarding Payments to Influence Certain Federal Transactions (June 1999)

3.2.5-8    	Whistleblower Protection for Contractor Employees (April 1996)

3.3.1-15   	Assignment of Claims (April 1996)

3.3.1-19   	Prompt Payment for Construction Contracts (August 1998)

3.3.2-1    	FAA Cost Principles (October 1996)

3.4.2-6    	Taxes--Contracts Performed in U.S. Possessions or Puerto Rico (October 1996)

3.6.2-2    	Convict Labor (April 1996)

3.6.2-9    	Equal Opportunity (August 1998)

3.6.2-12   	Affirmative Action for Special Disabled and Vietnam Era Veterans (January 1998)

3.6.2-13   	Affirmative Action for Workers With Disabilities (April 2000)

3.6.2-14   	Employment Reports on Special Disabled Veterans and Veterans of Vietnam Era (January 1998)

3.6.2-16   	Notice to the Government of Labor Disputes (April 1996)

3.6.2-18   	Davis Bacon Act (April 1996)

3.6.2-19   	Withholding--Labor Violations (April 1996)

3.6.2-20   	Payrolls and Basic Records (June 1999)

3.6.2-21   	Apprentices, Trainees, and Helpers (April 1996)

3.6.2-22   	Subcontracts (Labor Standards) (April 1996)

3.6.2-23   	Certification of Eligibility (April 1996)

3.6.3-1    	Clean Air and Water Certification (April 2000)

3.6.3-2    	Clean Air and Clean Water (April 1996)

3.6.3-13   	Recycle Content and Environmentally Preferable Products (January 2002)

3.6.3-14   	Use Of Environmentally Preferable Products (January 2002)

3.10.1-7   	Bankruptcy (April 1996)

3.10.1-8   	Suspension of Work (August 1998)

3.10.1-19  	Modification Cost Proposal - Price Breakdown (Construction) (April 1996)

3.10.1-25  	Novation and Change-Of-Name Agreements (January 2003)

3.10.6-1   	Termination for Convenience of the Government (Fixed Price) (October 1996)

3.10.6-6   	Default (Fixed Price Construction) (October 1996)

3.2.2.3-49 	Protecting of Existing Vegetation, Structures, Equipment, Utilities, and Improvements (July 2004)

(a) The Contractor (you) must preserve and protect all structures, equipment, and vegetation (such as trees, shrubs, and grass) on or adjacent to the work site that are not to be removed and which do not unreasonably interfere with the work required under this contract. You must remove trees only when specifically authorized to do so, and must avoid damaging vegetation that will remain in place. If any tree limbs or branches break while you work, you must trim those limbs or branches with a clean cut.

(b) You must protect from damage all existing improvements and utilities at or near the work site and on a third party's adjacent property, if you are or should be aware of them.  You must repair any damage to those facilities, including those that are a third party's property, resulting from your failure to comply with the contract requirements or to exercise reasonable care in performing the work. If you fail or refuse to repair the damage promptly, the Contracting Officer (CO) may have another vendor perform the work and charge you for it.

(End of clause)

3.2.2.3-67 	Special Precautions for Work at Operating Airports (July 2004)

(a) When the Contractor (you) performs work at an operating airport, you must arrange your work schedule so it will not interfere with flight operations. Those operations take precedence over construction convenience. You must perform work that would otherwise interfere with or endanger the operations of aircraft only at times and in the manner the Contracting Officer (CO) directs. The FAA will make every effort to reduce the disruption of your operation.

(b) Unless otherwise specified by local regulations, you must mark all areas in which construction operations are underway with yellow flags during daylight hours and with red lights at other times. The red lights along the edge of the construction areas within the existing aprons must be the electric type of not less than 100 watts intensity, placed and supported as required. All other construction markings on roads and adjacent parking lots may be either electric or battery type lights. You must place these lights and flags to outline the construction areas, and the distance between any two flags or lights must not be greater than 25 feet. You must provide adequate watch to maintain the lights in working condition at all times other than daylight hours. The CO will determine the hour daylight begins and ends.

(c) All equipment and material in the construction areas or when moved outside the construction area must be marked with airport safety flags during the day and at other times the CO directs, and with red obstruction lights at nights. You must have clearance lights conforming with the CO's instructions for all equipment operating on the apron, taxiway, runway, and intermediate areas after dark. You must not operate construction equipment within 50 feet of aircraft undergoing fuel operations. You must not have open flames on the ramp except at times the CO authorizes.

(d) Your trucks and other motorized equipment must enter the airport or construction area only over routes the CO identifies.  You must not use runways, aprons, taxiways, or parking areas as truck or equipment routes unless specifically authorized for such use. You must provide flag personnel at points on apron and taxiway to safely guide your equipment over these areas to assure right of way to aircraft.  You must return areas and routes you used during the contract to their original condition. You must not exceed the airport management's maximum speed at the airport.  Your vehicles must be under safe control at all times, weather and traffic conditions considered. Vehicles must have with head and tail lights when it's dark.

(End of clause)

3.2.2.3-75 	Requests for Contract Information (July 2004)

Any contract resulting from this SIR is a public document, subject to release under the Freedom of Information Act (FOIA), 5 U.S.C. Section 552. Unless covered by an exemption described in the Act, the Contracting Officer (CO) may release all information contained in the contract, including unit price, hourly rates and their extensions, to the public on request. Offerors (you) are urged to mark any sensitive documents you submit in response to this SIR that you consider to be trade secrets, proprietary information, or privileged or confidential financial information.

[End of Provision]

3.3.1-33   	Central Contractor Registration (April 2006)

(a) Definitions.  As used in this clause

"Central Contractor Registration (CCR) database" means the primary Government repository for Contractor information required for the conduct of business with the Government.

"Data Universal Numbering System (DUNS) number" means the 9-digit number assigned by Dun and Bradstreet, Inc. (D&B) to identify unique business entities.

"Data Universal Numbering System +4 (DUNS+4) number" means the DUNS number assigned by D&B plus a 4-character suffix that may be assigned by a business concern. (D&B has no affiliation with this 4-character suffix.) This 4-character suffix may be assigned at the discretion of the business concern to establish additional CCR records for identifying alternative Electronic Funds Transfer (EFT) accounts for the same parent concern.

"Registered in the CCR database" means that the Contractor has entered all mandatory information, including the DUNS number or the DUNS+4 number, into the CCR database.

(b)(1) By submission of an offer, the offeror acknowledges the requirement that a prospective awardee shall be registered in the CCR database prior to award, during performance, and through final payment of any contract, basic agreement, basic ordering agreement, or blanket purchasing agreement resulting from this solicitation.

(2) The offeror shall enter, in Representations, Certifications and Other Statements of Offerors Section of the solicitation, the DUNS or DUNS +4 number that identifies the offeror's name and address exactly as stated in the offer. The DUNS number will be used by the Contracting Officer to verify that the offeror is registered in the CCR database.

(c) If the offeror does not have a DUNS number, it should contact Dun and Bradstreet directly to obtain one.

(1) An offeror may obtain a DUNS number

(i) If located within the United States, by calling Dun and Bradstreet at 1-866-705-5711 or via the Internet at http://www.dnb.com/; or

(ii) If located outside the United States, by contacting the local Dun and Bradstreet office.

(2) The offeror should be prepared to provide the following information:

(i) Company legal business.

(ii) Tradestyle, doing business, or other name by which your entity is commonly recognized.

(iii) Company Physical Street Address, City, State, and ZIP Code.

(iv) Company Mailing Address, City, State and ZIP Code (if different from physical street address).

(v) Company Telephone Number.

(vi) Date the company was started.

(vii) Number of employees at your location.

(viii) Chief executive officer/key manager.

(ix) Line of business (industry).

(x) Company Headquarters name and address (reporting relationship within your entity).

(d) If the offeror does not become registered in the CCR database in the time prescribed by the Contracting Officer, the Contracting Officer may proceed to award to the next otherwise successful registered offeror.

(e) Processing time, which normally takes 48 hours, should be taken into consideration when registering. Offerors who are not registered should consider applying for registration immediately upon receipt of this solicitation.

(f) The Contractor is responsible for the accuracy and completeness of the data within the CCR database, and for any liability resulting from the Government's reliance on inaccurate or incomplete data. To remain registered in the CCR database after the initial registration, the Contractor is required to review and update on an annual basis from the date of initial registration or subsequent updates its information in the CCR database to ensure it is current, accurate and complete. Updating information in the CCR does not alter the terms and conditions of this contract and is not a substitute for a properly executed contractual document.

(g)(1)(i) If a Contractor has legally changed its business name, "doing business as" name, or division name (whichever is shown on the contract), or has transferred the assets used in performing the contract, but has not completed the necessary requirements regarding novation and change-of-name agreements in AMS Procurement Guidance T3.10.1.A-8, the Contractor shall provide the responsible Contracting Officer a minimum of one business day's written notification of its intention to:

(A) change the name in the CCR database;

(B) comply with the requirements of T3.10.1.A-8; and

(C) agree in writing to the timeline and procedures specified by the responsible Contracting Officer. The Contractor must provide the Contracting Officer with the notification, sufficient documentation to support the legally changed name.

(ii) If the Contractor fails to comply with the requirements of paragraph (g)(1)(i) of this clause, or fails to perform the agreement at paragraph (g)(1)(i)(C) of this clause, and, in the absence of a properly executed novation or change-of-name agreement, the CCR information that shows the Contractor to be other than the Contractor indicated in the contract will be considered to be incorrect information within the meaning of the "Suspension of Payment" paragraph of the electronic funds transfer (EFT) clause of this contract.

(2) The Contractor shall not change the name or address for EFT payments or manual payments, as appropriate, in the CCR record to reflect an assignee for the purpose of assignment of claims. Assignees shall be separately registered in the CCR database. Information provided to the Contractor's CCR record that indicates payments, including those made by EFT, to an ultimate recipient other than that Contractor will be considered to be incorrect information within the meaning of the "Suspension of payment" paragraph of the EFT clause of this contract.

(h) Offerors and Contractors may obtain information on registration and annual confirmation requirements via the internet at http://www.ccr.gov/ or by calling 1-888-227-2423, or 269-961-5757.

(End of clause)

3.3.1-34   	Payment by Electronic Funds Transfer/Central Contractor Registration (October 2005)

(a) Method of payment.

(1) All payments by the Government under this contract shall be made by electronic funds transfer (EFT), except as provided in paragraph (a)(2) of this clause. As used in this clause, the term "EFT" refers to the funds transfer and may also include the payment information transfer.

(2) In the event the Government is unable to release one or more payments by EFT, the Contractor agrees to either?

(i) Accept payment by check or some other mutually agreeable method of payment; or

(ii) Request the Government to extend the payment due date until such time as the Government can make payment by EFT (but see paragraph (d) of this clause).

(b) Contractor's EFT information. The Government shall make payment to the Contractor using the EFT information contained in the Central Contractor Registration (CCR) database. In the event that the EFT information changes, the Contractor shall be responsible for providing the updated information to the CCR database.

(c) Mechanisms for EFT payment. The Government may make payment by EFT through either the Automated Clearing House (ACH) network, subject to the rules of the National Automated Clearing House Association, or the Fedwire Transfer System. The rules governing Federal payments through the ACH are contained in 31 CFR Part 210.

(d) Suspension of payment. If the Contractor's EFT information in the CCR database is incorrect, then the Government need not make payment to the Contractor under this contract until correct EFT information is entered into the CCR database; and any invoice or contract financing request shall be deemed not to be a proper invoice for the purpose of prompt payment under this contract. The prompt payment terms of the contract regarding notice of an improper invoice and delays in accrual of interest penalties apply.

(e) Liability for uncompleted or erroneous transfers.

(1) If an uncompleted or erroneous transfer occurs because the Government used the Contractor's EFT information incorrectly, the Government remains responsible for?

(i) Making a correct payment;

(ii) Paying any prompt payment penalty due; and

(iii) Recovering any erroneously directed funds.

(2) If an uncompleted or erroneous transfer occurs because the Contractor's EFT information was incorrect, or was revised within 30 days of Government release of the EFT payment transaction instruction to the Federal Reserve System, and?

(i) If the funds are no longer under the control of the payment office, the Government is deemed to have made payment and the Contractor is responsible for recovery of any erroneously directed funds; or

(ii) If the funds remain under the control of the payment office, the Government shall not make payment, and the provisions of paragraph (d) of this clause shall apply.

(f) EFT and prompt payment. A payment shall be deemed to have been made in a timely manner in accordance with the prompt payment terms of this contract if, in the EFT payment transaction instruction released to the Federal Reserve System, the date specified for settlement of the payment is on or before the prompt payment due date, provided the specified payment date is a valid date under the rules of the Federal Reserve System.

(g) EFT and assignment of claims. If the Contractor assigns the proceeds of this contract as provided for in the assignment of claims terms of this contract, the Contractor shall require as a condition of any such assignment, that the assignee shall register separately in the CCR database and shall be paid by EFT in accordance with the terms of this clause. Notwithstanding any other requirement of this contract, payment to an ultimate recipient other than the Contractor, or a financial institution properly recognized under an assignment of claims, is not permitted. In all respects, the requirements of this clause shall apply to the assignee as if it were the Contractor. EFT information that shows the ultimate recipient of the transfer to be other than the Contractor, in the absence of a proper assignment of claims acceptable to the Government, is incorrect EFT information within the meaning of paragraph (d) of this clause.

(h) Liability for change of EFT information by financial agent. The Government is not liable for errors resulting from changes to EFT information made by the Contractor's financial agent.

(i) Payment information. The payment or disbursing office shall forward to the Contractor available payment information that is suitable for transmission as of the date of release of the EFT instruction to the Federal Reserve System. The Government may request the Contractor to designate a desired format and method(s) for delivery of payment information from a list of formats and methods the payment office is capable of executing. However, the Government does not guarantee that any particular format or method of delivery is available at any particular payment office and retains the latitude to use the format and delivery method most convenient to the Government. If the Government makes payment by check in accordance with paragraph (a) of this clause, the Government shall mail the payment information to the remittance address contained in the CCR database.

(End of clause)

3.4.1-4    	Performance Bond Requirements (April 1996)

(a)  The  contractor is required to submit a performance bond in a penal amount equal to 100 percent of the contract price, unless another amount is specified in the contract "Schedule," within the time specified by the Contracting Officer.

(b)  The bond must be executed on specified forms, and sureties must be acceptable to the Federal Aviation Administration.  Corporate sureties must appear on the list in Treasury Circular 570, and the amount of the bond may not exceed the underwriting limit stated for the surety on that list.

(c)  Failure to submit an acceptable bond may be cause for termination of the contract for default.

3.4.1-5    	Payment Bond Requirements (April 1996)

(a)  The contractor is required to submit a payment bond in the penal amount set forth in the "Schedule," within the time required by the Contracting Officer.

(b)  The bond must be executed on the forms attached to this SIR, and sureties must be acceptable to the Federal Aviation Administration.  Corporate sureties must appear on the list in Treasury Circular 570, and the amount of the bond may not exceed the underwriting limit stated for the surety on that list.

(c)  Failure to submit an acceptable bond may be cause for termination of the contract for default.

NOTE:  Payment bond shall be in a penal amount equal to 100 percent.

3.4.1-6    	Additional Bond Security (April 1996)

If any surety furnishing a bond in connection with this contract becomes unacceptable to the Federal Aviation Administration or fails to furnish reports on its financial condition as requested by the Contracting Officer, or if the contract price increases to the point where the security furnished becomes inadequate in the Contracting Officer's opinion, the contractor must promptly furnish additional security as required to protect the interests of the Federal Aviation Administration and of persons supplying labor or materials in performance of this contract.

(End of clause)

3.4.1-7    	Notice to Proceed (April 1996)

The contractor shall not initiate work under this contract until it has received a notice to proceed in writing from the Contracting Officer.

(End of clause)

3.4.1-11   	Insurance--Liability to Third Persons (October 1996)

(a)

(1)  Except as provided in subparagraph (a)(2) of this clause, the Contractor shall provide and maintain workers' compensation, employer's liability, comprehensive general liability (bodily injury), comprehensive automobile liability (bodily injury and property damage) insurance, and such other insurance as the Contracting Officer may require under this contract.

(2)  The Contractor may, with the approval of the Contracting Officer, maintain a self-insurance program; provided that, with respect to workers' compensation, the Contractor is qualified pursuant to statutory authority.

(3)  All insurance required by this paragraph shall be in a form and amount and for those periods as the Contracting Officer may require or approve and with insurers approved by the Contracting Officer.

(b)  The Contractor agrees to submit for the Contracting Officer's approval, to the extent and in the manner required by the Contracting Officer, any other insurance that is maintained by the Contractor in connection with the performance of this contract and for which the Contractor seeks reimbursement.

(c) The Contractor shall be reimbursed:

(1)  For that portion

(i) of the reasonable cost of insurance allocable to this contract, and

(ii) required or approved under this clause; and

(2)  For certain liabilities (and expenses incidental to such liabilities) to third persons not compensated by insurance or otherwise without regard to and as an exception to the limitation of cost or the limitation of funds clause of this contract.  These liabilities must arise out of the performance of this contract, whether or not caused by the negligence of the Contractor or of the Contractor's agents, servants, or employees, and must be represented by final judgments or settlements approved in writing by the Government.  These liabilities are for:

(i)  Loss of or damage to property (other than property owned, occupied, or used by the Contractor, rented to the Contractor, or in the care, custody, or control of the Contractor); or

(ii)  Death or bodily injury.

(d)  The Government's liability under paragraph (c) of this clause is subject to the availability of appropriated funds at the time a contingency occurs.  Nothing in this contract shall be construed as implying that the Congress will, at a later date, appropriate funds sufficient to meet deficiencies.

(e)  The Contractor shall not be reimbursed for liabilities (and expenses incidental to such liabilities)-

(1)  For which the Contractor is otherwise responsible under the express terms of any clause specified in the "Schedule" or elsewhere in the contract;

(2)  For which the Contractor has failed to insure or to maintain insurance as required by the Contracting Officer; or

(3)  That result from willful misconduct or lack of good faith on the part of any of the Contractor's directors, officers, managers, superintendents, or other representatives who have supervision or direction of:

(i)  All or substantially all of the Contractor's business;

(ii)  All or substantially all of the Contractor's operations at any one plant or separate location in which this contract is being performed; or

(iii)  A separate and complete major industrial operation in connection with the performance of this contract.

(f)  The provisions of paragraph (e) of this clause shall not restrict the right of the Contractor to be reimbursed for the cost of insurance maintained by the Contractor in connection with the performance of this contract, other than insurance required in accordance with this clause; provided, that such cost is allowable under the "Allowable Cost and Payment" clause of this contract.

(g)  If any suit or action is filed or any claim is made against the Contractor, the cost and expense of which may be reimbursable to the Contractor under this contract, and the risk of which is then uninsured or is insured for less than the amount claimed, the Contractor shall:

(1)  Immediately notify the Contracting Officer and promptly furnish copies of all pertinent papers received;

(2)  Authorize Government representatives to collaborate with counsel  for the insurance carrier in settling or defending the claim when the amount of the liability claimed exceeds the amount of coverage; and

(3)  Authorize Government representatives to settle or defend the claim and to represent the Contractor in or to take charge of any litigation, if required by the Government, when the liability is not insured or covered by bond.  The Contractor may, at its own expense, be associated with the Government representatives in any such claim or litigation.

(End of clause)

3.4.1-12   	Insurance (July 1996)

(a)  During the term of this contract and any extension, the contractor shall maintain at its own expense the insurance required by this clause.  Insurance companies shall be acceptable to the Federal Aviation Administration.  Policies shall include all terms and provisions required by the Federal Aviation Administration.

(b)  The contractor shall maintain and furnish evidence of the following insurance, with the stated minimum limits:

(1)  Worker's Compensation and Employer's Liability.  The contractor shall comply with applicable Federal and State workers' compensation and occupational disease statutes.  The contractor shall maintain employer's liability coverage of at least $100,000, except in States with exclusive or monopolistic funds that do not permit worker's compensation to be written by private carriers.

(2)  General Liability.  The contractor shall maintain bodily injury general liability insurance written on a comprehensive form of policy of at least $100,000* per person and $500,000* per occurrence.  Property damage limits, if any, will be set forth elsewhere in the "Schedule."

(3)  Automobile Liability.  If automobiles will be used in connection with performance of this contract, the contractor shall maintain automobile liability insurance written on a comprehensive form of policy with coverage of at least $200,000* per person and $500,000* per occurrence for bodily injury and $20,000* per occurrence for property damage.

(4)  Aircraft Liability.  If aircraft will be used in connection with performance of this contract, the contractor shall maintain aircraft public and passenger liability insurance with coverage of at least $200,000* per person and $500,000* per occurrence for bodily injury other than passenger liability, and $200,000* per occurrence for property damage.  Coverage for passenger liability bodily injury shall be at least $200,000* multiplied by the number of seats or passengers, whichever is greater.

(5)  Watercraft Liability.  When watercraft will be used in connection with performing the contract, the contractor shall provide watercraft liability insurance.  Limits shall be at least $1,000,000* per occurrence.  The policy shall include coverage for owned, non-owned and hired watercraft.

(6)  Environmental Impairment Liability.  When the contract may involve hazardous wastes, the contractor shall provide environmental impairment liability insurance with coverage of at least $1,000,000* bodily injury per occurrence and $1,000,000* property damage per occurrence.  Such insurance shall include coverage for the clean up, removal, storage, disposal, transportation, and use of pollutants.

(7)  Medical Malpractice.  When the contract will involve health care services, the contractor shall maintain medical malpractice liability insurance with coverage of at least $500,000* per occurrence.

(c)  Each policy shall include substantially the following provision:

"It is a condition of this policy that the company furnish written notice to the U.S. Federal Aviation Administration 30 days in advance of the effective date of any reduction in or cancellation of this policy."

(d)  The contractor shall furnish a certificate of insurance or, if required by the Contracting Officer, true copies of liability policies and manually countersigned endorsements of any changes, including the FAA's contract number to ensure proper filing of documents.  Insurance shall be effective, and evidence of acceptable insurance furnished, before beginning performance under this contract.  Evidence of renewal shall be furnished not later than five days before a policy expires.

(e)  The maintenance of insurance coverage as required by this clause is a continuing obligation, and the lapse or termination of insurance coverage without replacement coverage being obtained will be grounds for termination for default.

*Unless modified in the "Schedule"

(End of clause)

3.4.2-8    	Federal, State, and Local Taxes--Fixed Price Contract (April 1996)

(a)  Definitions:

(1)  'Contract date,' as used in this clause, means the effective date of this contract or modification.

(2)  'All applicable Federal, State, and local taxes and duties,' as used in this clause, means all taxes and duties, in effect on the contract date, that the taxing authority is imposing and collecting on the transactions or property covered by this contract.

(3)  'After-imposed Federal tax,' as used in this clause, means any new or increased Federal excise tax or duty, or tax that was exempted or excluded on the contract date but whose exemption was later revoked or reduced during the contract period, on the transactions or property covered by this contract that the Contractor is required to pay or bear as the result of legislative, judicial, or administrative action taking effect after the contract date.  It does not include social security tax or other employment taxes.

(4)  'After-relieved Federal tax,' as used in this clause, means any amount of Federal excise tax or duty, except social security or other employment taxes, that would otherwise have been payable on the transactions or property covered by this contract, but which the Contractor is not required to pay or bear, or for which the Contractor obtains a refund or drawback, as the result of legislative, judicial, or administrative action taking effect after the contract date.

(b)  The contract price includes all applicable Federal, State, and local taxes and duties.

(c)  The contract price shall be increased by the amount of any after-imposed Federal tax, provided the Contractor warrants in writing that no amount for such newly imposed Federal excise tax or duty or rate increase was included in the contract price, as a contingency reserve or otherwise.

(d)  The contract price shall be decreased by the amount of any after-relieved Federal tax.

(e)  The contract price shall be decreased by the amount of any Federal excise tax or duty, except social security or other employment taxes, that the Contractor is required to pay or bear, or does not obtain a refund of, through the Contractor's fault, negligence, or failure to follow instructions of the Contracting Officer.

(f)  No adjustment shall be made in the contract price under this clause unless the amount of the adjustment exceeds $250.

(g)  The Contractor shall promptly notify the Contracting Officer of all matters relating to any Federal excise tax or duty that reasonably may be expected to result in either an increase or decrease in the contract price and shall take appropriate action as the Contracting Officer directs.

(h)  The Government shall, without liability, furnish evidence appropriate to establish exemption from any State, or local tax when the Contractor requests such evidence and a reasonable basis exists to sustain the exemption.

(End of clause)

3.6.1-1    	Notice of Total Small Business Set-Aside (July 2006)

(a)  Definition.  Small business concern, as used in this clause, means a concern, including its affiliates, that is independently owned and operated, not dominant in the field of operation in which it is bidding on Government contracts, and qualified as a small business under the North American Industry Classification System (NAICS) standards in this Screening Information Request (SIR).

(b)  General.

(1)  Information and/or offers are requested only from small business concerns.  Information and/or offers received from concerns that are not small business concerns shall be considered nonresponsive and will be rejected.

(2)  Any award resulting from this SIR will be made to a small business concern.

(c)  Agreement.  A manufacturer or regular dealer submitting information and/or an offer in its own name agrees to furnish, in performing the contract, only end items manufactured or produced by small business concerns inside the United States, its territories and possessions, the Commonwealth of Puerto Rico, the Trust Territory of the Pacific Islands, or the District of Columbia.  However, this requirement does not apply in connection with construction or service contracts.

(End of clause)

3.6.3-12   	Asbestos-Free Construction (August 1998)

In performing this contract, the Contractor shall not use asbestos or asbestos-containing building materials during construction, renovation, and/or modernization of this facility and shall provide to the Contracting Officer (CO) a signed statement [CO state due date of statement here related to completion of the project] indicating that to the best of its knowledge, no asbestos or asbestos-containing building materials were used during construction,  renovation, and/or modernization of this facility.  The Contractor's certification under this clause is considered to be a material requirement of the contract and the FAA may withhold payment pending submittal and receipt of an acceptable certification.

The FAA CO may authorize sample testing of contractor  building materials used during construction, renovation, and/or modernization of this facility to verify that they are asbestos-free.  The FAA will bear the expense of this testing unless the testing reveals that the Contractor used asbestos-containing building material in performing this contract.  If asbestos-containing material is found, the Contractor shall remove and replace the asbestos-containing material and decontaminate the site of asbestos contamination caused by the Contractor at no additional cost to the Government.  In addition, the Contractor shall bear the expense of the original testing and retesting to determine that the asbestos removal and site decontamination are satisfactorily completed.

(End of clause)

3.9.1-1    	Contract Disputes (November 2002)

(a) All contract disputes arising under or related to this contract shall be resolved through the Federal Aviation Administration (FAA) dispute resolution system at the Office of Dispute Resolution for Acquisition (ODRA) and shall be governed by the procedures set forth in 14 C.F.R. Parts 14 and 17, which are hereby incorporated by reference. Judicial review, where available, will be in accordance with 49 U.S.C. 46110 and shall apply only to final agency decisions. A contractor may seek review of a final FAA decision only after its administrative remedies have been exhausted.

(b) The filing of a contract dispute with the ODRA may be accomplished by mail, overnight delivery, hand delivery, or by facsimile. A contract dispute is considered to be filed on the date it is received by the ODRA.

(c) Contract disputes are to be in writing and shall contain:

(1) The contractor's name, address, telephone and fax numbers and the name, address, telephone and fax numbers of the contractor's legal representative(s) (if any) for the contract dispute;

(2) The contract number and the name of the Contracting Officer;

(3) A detailed chronological statement of the facts and of the legal grounds for the contractor's positions regarding each element or count of the contract dispute (i.e., broken down by individual claim item), citing to relevant contract provisions and documents and attaching copies of those provisions and documents;

(4) All information establishing that the contract dispute was timely filed;

(5) A request for a specific remedy, and if a monetary remedy is requested, a sum certain must be specified and pertinent cost information and documentation (e.g., invoices and cancelled checks) attached, broken down by individual claim item and summarized; and

(6) The signature of a duly authorized representative of the initiating party.

(d) Contract disputes shall be filed at the following address:

(1) Office of Dispute Resolution for Acquisition, AGC-70,

Federal Aviation Administration,

800 Independence Ave, S.W., Room 323,

Washington, DC 20591,

Telephone: (202) 267-3290,

Facsimile: (202) 267-3720; or

(2) other address as specified in 14 CFR Part 17.

(e) A contract dispute against the FAA shall be filed with the ODRA within two (2) years of the accrual of the contract claim involved. A contract dispute by the FAA against a contractor (excluding contract disputes alleging warranty issues, fraud or latent defects) likewise shall be filed within two (2) years after the accrual of the contract claim.  If an underlying contract entered into prior to the effective date of this part provides for time limitations for filing of contract disputes with the ODRA which differ from the aforesaid two (2) year period, the limitation periods in the contract shall control over the limitation period of this section.  In no event will either party be permitted to file with the ODRA a contract dispute seeking an equitable adjustment or other damages after the contractor has accepted final contract payment, with the exception of FAA claims related to warranty issues, gross mistakes amounting to fraud or latent defects.  FAA claims against the contractor based on warranty issues must be filed within the time specified under applicable contract warranty provisions.  Any FAA claims against the contractor based on gross mistakes amounting to fraud or latent defects shall be filed with the ODRA within two (2) years of the date on which the FAA knew or should have known of the presence of the fraud or latent defect.

(f) A party shall serve a copy of the contract dispute upon the other party, by means reasonably calculated to be received on the same day as the filing is to be received by the ODRA.

(g) After filing the contract dispute, the contractor should seek informal resolution with the Contracting Officer.

(h) The FAA requires continued performance with respect to contract disputes arising under this contract, in accordance with the provisions of the contract, pending a final FAA decision.

(i) The FAA will pay interest on the amount found due and unpaid from (1) the date the Contracting Officer receives the contract dispute, or (2) the date payment otherwise would be due, if that date is later, until the date of payment. Simple interest on contract disputes shall be paid at the rate fixed by the Secretary of the Treasury that is applicable on the date the Contracting Officer receives the contract dispute and then at the rate applicable for each 6-month period as fixed by the Treasury Secretary until payment is made.

(j) Additional information and guidance about the ODRA dispute resolution process for contract disputes can be found on the ODRA Website at http://www.faa.gov.

(End of clause)

3.9.1-2    	Protest After Award (August 1997)

(a)  Upon receipt of a notice that a protest has been filed with the FAA Office of Dispute Resolution, or a determination that a protest is likely, the Administrator or his designee may instruct the Contracting Officer) to direct the Contractor to stop performance of the work called for by this contract.  The order to the Contractor shall be in writing, and shall be specifically identified as a stop-work order issued under this clause.  Upon receipt of the order, the Contractor shall immediately comply with its terms and take all reasonable steps to minimize the incurrence of costs allocable to the work covered by the order during the period of work stoppage.  Upon receipt of the final decision or other resolution of the protest, the Contracting Officer shall either--

(1)  Cancel the stop-work order; or

(2)  For other than cost-reimbursement contracts, terminate the work covered by the order as provided in the "Default" or the "Termination for Convenience of the Government" clause(s) of this contract; or

(3)  For cost-reimbursement contracts, terminate the work covered by the order as provided in the "Termination" clause of this contract.

(b)  If a stop-work order issued under this clause is canceled either before or after the final resolution of the protest, the Contractor shall resume work.  The Contracting Officer shall make for other than cost-reimbursement contracts, an equitable adjustment in the delivery schedule or contract price, or both; and for cost-reimbursement contracts, an equitable adjustment in the delivery schedule, the estimated cost, the fee, or a combination thereof, and in any other terms of the contract that may be affected; and the contract shall be modified, in writing, accordingly, if--

(1)  The stop-work order results in an increase in the time required for, or in the Contractor's cost properly allocable to, the performance of any part of this contract;  and

(2)  The Contractor asserts its right to an adjustment within 30 days after the end of the period of work stoppage; provided, that if the Contracting Officer decides the facts justify the action, the Contracting Officer may receive and act upon a proposal submitted at any time before final payment under this contract.

(c)  If a stop-work order is not canceled and the work covered by the order is terminated for the convenience of the Government, the Contracting Officer shall allow reasonable costs resulting from the stop-work order in arriving at the termination settlement.

(d)  If a stop-work order is not canceled and the work covered by the order is terminated for default, the Contracting Officer shall allow, by equitable adjustment or otherwise, reasonable costs resulting from the stop-work order.

(e)  The Government's rights to terminate this contract at any time are not affected by action taken under this clause.

(End of clause)

3.10.1-16  	Changes and Changed Conditions (April 1996)

(a)  The Contracting Officer may, in writing, order changes in the drawings and specifications within the general scope of the contract.

(b)  The Contractor shall promptly notify the Contracting Officer, in writing, of subsurface or latent physical conditions differing materially from those indicated in this contract or unknown unusual physical conditions at the site before proceeding with the work.

(c)  If changes under paragraph (a) or conditions under paragraph (b) increase or decrease the cost of, or time required for performing the work, the Contracting Officer shall make an equitable adjustment (see paragraph (d)) upon submittal of a proposal for adjustment (hereafter referred to as proposal) by the Contractor before final payment under the contract.

(d)  The Contracting Officer shall not make an equitable adjustment under paragraph (b) unless-

(1)  The Contractor has submitted and the Contracting Officer has received the required written notice; or

(2)  The Contracting Officer waives the requirement for the written notice.

(e)  Failure to agree to any adjustment shall be a dispute under the "Disputes" clause.

(End of clause)

3.10.1-20  	Warranty--Construction (April 1996)

(a)  In addition to any other warranties in this contract, the Contractor warrants, except as provided in paragraph (i) of this clause, that work performed under this contract conforms to the contract requirements and is free of any defect in equipment, material, or design furnished, or workmanship performed by the Contractor or any subcontractor or supplier at any tier.

(b)  This warranty shall continue for a period of 1 year from the date of final acceptance of the work. If the Government takes possession of any part of the work before final acceptance, this warranty shall continue for a period of 1 year from the date the Government takes possession.

(c)  The Contractor shall remedy at the Contractor's expense any failure to conform, or any defect. In addition, the Contractor shall remedy at the Contractor's expense any damage to Government owned or controlled real or personal property, when that damage is the result of :

(1)  The Contractor's failure to conform to contract requirements; or

(2)  Any defect of equipment, material, workmanship, or design furnished by the Contractor.

(d)  The Contractor shall restore any work damaged in fulfilling the terms and conditions of this clause. The Contractor's warranty with respect to work repaired or replaced will run for 1 year from the date of repair or replacement.

(e)  The Contracting Officer will notify the Contractor, in writing, within a reasonable time after the discovery of any failure, defect, or damage.

(f)  If the Contractor fails to remedy any failure, defect, or damage within a reasonable time after receipt of notice, the Government shall have the right to replace, repair, or otherwise remedy the failure, defect, or damage at the Contractor's expense.

(g)  With respect to all warranties, express or implied, from subcontractors, manufacturers, or suppliers for work performed and materials furnished under this contract, the Contractor shall:

(1)  Obtain all warranties that would be given in normal commercial practice;

(2)  Require all warranties to be executed, in writing, for the benefit of the Government, if directed by the Contracting Officer, and

(3)  Enforce all warranties for the benefit of the Government if directed by the Contracting Officer.

(h)  In the event the Contractor's warranty under paragraph (b) of this clause has expired, the Government may bring suit at its expense to enforce a subcontractor's, manufacturer's, or supplier's warranty.

(i)  Unless a defect is caused by the negligence of the Contractor or subcontractor or supplier at any tier, the Contractor shall not be liable for the repair of any defects of material or design furnished by the Government nor for the repair of any damage that results from any defect in Government furnished material or design.

(j)  This warranty shall not limit the Government's rights under the Inspection and Acceptance clause of this contract with respect to latent defects, gross mistakes, or fraud.

(End of clause)

3.13-5     	Seat Belt Use by Contractor Employees (January 1999)

In accordance with Executive Order 13043 entitled "Increasing Seat Belt Use in the U.S.," the contractor is encouraged to implement, communicate and enforce on the job seat belt policies and programs for their employees and subcontractors when operating company-owned, rented or personally-owned vehicles.

(End of clause)

3.14-2     Contractor Personnel Suitability Requirements (July 2006)

(a) This clause applies to the extent that this contract requires contractor employees, subcontractors, or consultants to have unescorted access to FAA:

(1) Facilities;

(2) Sensitive information; and/or

(3) Resources regardless of the location where such access occurs, and none of the exceptions of FAA Order 1600.72A, Contractor and Industrial Security Program, Chapter 5, paragraphs 4, 6, 7 and 8 pertains.

Definitions of applicable terminology are contained in the corresponding guidance and Order 1600.72A, appendix A.

(b) Consistent with FAA Order 1600.72A, the FAA Servicing Security Element (SSE) has approved designated risk levels for the positions under the contract.

Position Risk Level 1 – Low Risk  		FAA Escort Required (refer to paragraph o)

(c) Not later than five (5) business days, not to exceed a maximum of 30 days, after contract award (or date of modification, if this provision is included by modification to an existing contract), for each employee in a listed position requiring access, provided, no previous background investigations can be supported as described below, the contractor will submit the following documentation to the SSE for an employment suitability determination:

- Standard Form (SF) 85P, Questionnaire for Public Trust Positions as designated by the Contractor Position Risk/Sensitivity Level Designation Record, FAA Form 1600-77, will be completed (all questions answered) in accordance with the instruction sheet.
- One fingerprint card (FD-258). Fingerprints will be taken by those individuals who have been identified as either a Trusted Agent or a Personal Identity Verification (PIV) registrar (SSE). 

In some instances, the fingerprint only may be required and an OF-306 Declaration for Federal Employment, most current edition, will also be submitted.

The applicant will appear in person and provide two forms of identity source documents in original form to the PIV Registrar (SSE) or the authorized Trusted Agent. The identity source documents must come from the list of acceptable documents included in Form I-9, OMB No. 1115-0136, Employment Eligibility Verification or version of the DOT F 1681 containing the list of acceptable identity verification documents. At least one document will be a valid State or Federal Government-issued picture Identification. A signed I-9 Form may be used but must indicate the two source documents that were verified.

The type of investigation conducted will be determined by the position risk level designation for all duties, functions, and/or tasks performed and will serve as the basis for granting a favorable employment suitability authorization as described in FAA Order 1600.72A. If an employee has had a previous U. S. Government conducted background investigation which meets the requirements of Chapter 5 of FAA Order 1600.72A and Homeland Security Presidential Directive 12 (HSPD-12), it will be accepted by the FAA. However, the FAA reserves the right to conduct further investigations, if necessary. For each contractor employee for which a previous background investigation was completed, the contractor will provide, in writing to the SSE, the name, date of birth, place of birth, and social security number of the employee, the name of the investigating entity, type of background investigation conducted, and approximate date the previous background investigation was completed. For all contracts over six (6) months in duration, the minimum background investigation requirement will be a National Agency Check with Inquiries (NACI). Please check with your SSE for final determination as to OPM background investigation type required. The contract may include positions that are temporary, seasonal, or under escort only. In such cases, a FAA Form 1600-77 for each specific position will be established as the investigative requirements may differ from the NACI.

The contractor must submit the required information with a transmittal letter referencing the contract number and this request to:

The transmittal letter must also include a list of all of the names of contractor employees and their positions for which completed forms will be submitted to the SSE pursuant to this Clause. A copy of the transmittal letter must also be provided to the Contracting Officer/Contracting Officer's Technical Representative (COTR) minus any privacy act information. 

(d) The contractor must submit the information required by Section (c) of this Clause for any new employee not listed in the Contractor's initial submission who is hired into any position identified in Section (c) of this Clause.

(e) The Contracting Officer will provide notice to the contractor when any contractor employee is found to be unsuitable or otherwise objectionable, or whose conduct appears contrary to the public interest, or inconsistent with the best interest of national security. The contractor must take appropriate action, including the removal of such employee from working on this FAA contract, at their own expense. The Contracting Officer will confirm to the SSE that the action has been taken.

(f) No contractor employee will work in a high, moderate, or low risk position unless the SSE has received all forms necessary to conduct any required investigation and has authorized the contractor employee to begin work.
(g) As applicable, the contractor must submit quarterly/bi-annual reports to the Contracting Officer with a copy to the SSE and the Operating Office on or before the fifth (5th) business day following each report period. This report must include a complete alphabetical listing of all current contractors who are currently supporting the contract and a separate listing of all terminated contractors.

(h) The contractor must notify the CO within one (1) business day after any employee identified pursuant to Section (c) of this Clause is terminated from performance on the contract.

(i) The Contracting Officer may also, after coordination with the SSE and other security specialists, require contractor employees to submit any other security information (including additional fingerprinting) deemed reasonably necessary to protect the interests of the FAA. In this event, the contractor must provide, or cause each of its employees to provide, such security information to the SSE, and the same transmittal letter requirements of Section (c) of this Clause applies.

(j) The contractor and/or subcontractor(s) must immediately contact the Servicing Security Elements (Regional and/or Center Security Divisions) or AIN-400 at Headquarters in the event an employee is arrested (detained by law enforcement for any offenses, other than minor traffic offenses) or is involved in theft of government property or the contractor becomes aware of any information that may raise a question about the suitability of a contractor employee.

(k) Failure to submit information required by this clause within the time required may be determined by the Contracting Officer a material breach of the contract.

(l) If subsequent to the effective date of this contract, the security classification or security requirements under this contract are changed by the Government and if the changes cause an increase or decrease in direct contract costs or otherwise affect any other term or condition of this contract, the contract will be subject to an equitable adjustment.

(m) The contractor agrees to insert terms that conform substantially to the language of this clause, including this paragraph (l) but excluding any reference to the Changes clause of this contract, in all subcontracts under this contract that involve access and where the exceptions under Chapter 5, FAA Order 1600.72A do not apply.

(n) The Contracting Officer will ensure the SSE receives a list of all proposed contractor employees, the name of the contracting company, contract number, duty location, identification of the funding line of business, and the names of the contracting officers and COTR for each contract within five (5) business days of contract award. If the Contracting Officer provided the SSE a solicitation number during pre-award, the contracting officer will ensure the SSE is notified of the contract number.

(o) Contractor employees who have not undergone a background investigation must be escorted at all times. In some instances, a contractor employee may be required to serve as an escort. In this situation, the contractor employee must have a completed and favorably adjudicated National Agency Check with Inquiries (NACI).

(End of clause)

PART III - SECTION J

LIST OF ATTACHMENTS

1.  Technical Specifications for the Installation of Two Precision Approach Path Indicator (PAPI) Systems and Two Runway End Identifier Light (REIL) Systems to Serve Runways 15 & 23 at North Central State Airport, Pawtucket, Rhode Island, May 2006.

2. Appendix A – Advisory Circular – 150/5370.2E, Operational Safety on Airports During Construction & A Guide to Airport Ground Vehicle Operations.

3. Appendix B – FAA STD-019e, Lightning and Surge Protection, Grounding, Bonding and Shielding Requirements for Facilities and Electronic Equipment & FAA-C-1217f, Electrical Work, Interior.

4. Appendix C – Cable Test Data Forms.

5. Appendix D – Pre-construction/Maintenance Project Safety and Health Checklist.

6. Airport Ground Vehicle Operations/An FAA Guide.

7.  Drawings as listed in PART I - SECTION C, Pages 4 & 5.

8.  Department of Labor General Decision Number RI030001, dated October 6, 2006.

PART IV - SECTION K

REPRESENTATIONS, CERTIFICATIONS, AND OTHER STATEMENTS OF OFFERORS

3.2.2.3-10 	Type of Business Organization (July 2004)

By checking the applicable box, the offeror (you) represents that--

(a) You operate as [ ] a corporation incorporated under the laws of the State of ____________________ , [ ] an individual, [ ] a partnership, [ ] a nonprofit organization, [ ] a joint venture or [ ] other ____________[specify what type of organization].

(b) If you are a foreign entity, you operate as [ ] an individual, [ ] a partnership, [ ] a nonprofit organization, [ ] a joint venture, or [ ] a corporation, registered for business in _____________________________________________.

(country)

(End of provision)

3.2.2.3-15 	Authorized Negotiators (July 2004)

The offeror states that the following persons are authorized to negotiate on your behalf with the FAA in connection with this offer:

Name:_______________________

Title:_________________________

Phone number:_________________

3.2.2.3-70 	Taxpayer Identification (July 2004)

(a) Definitions.

(1) "Common parent," as used in this clause, means a corporate entity that owns or controls an affiliated group of corporations that files an offeror's (you, your) Federal income tax returns on a consolidated basis, and of which you are a member.

(2) "Corporate status," as used in this clause, means a designation as to whether you are a corporate entity, an unincorporated entity (for example, sole proprietorship or partnership), or a corporation providing medical and health care services.

(3) "Taxpayer Identification Number (TIN)," as used in this clause, means the number the Internal Revenue Service (IRS) requires you use in reporting income tax and other returns.

(b) All offerors must submit the information required in paragraphs (c) through (e) of this provision to comply with reporting requirements of 26 U.S.C. 6041, 6041A, and 6050M and implementing regulations issued by IRS. The FAA will use this information to collect and report on any delinquent amounts arising out of your relation with the Federal Government, under Public Law 104 -134, the Debt Collection Improvement Act of 1996, Section 31001(I)(3). If the resulting contract is subject to the reporting requirements and you refuse or fail to provide the information, the Contracting Officer (CO) may reduce your payments 31 percent under the contract.

(c) Taxpayer Identification Number (TIN).

[ ] TIN: ______________________________

[ ] TIN has been applied for.

[ ] TIN is not required because:

[ ] Offeror is a nonresident alien, foreign corporation, or foreign partnership that does not leave income effectively connected with the conduct of a trade or business in the U.S. and does not have an office or place of business or a fiscal paying agent in the U.S.;

[ ] Offeror is an agency or instrumentality of a foreign government;

[ ] Offeror is an agency or instrumentality of a Federal, state, or local government;

[ ] Other--State basis. ___________________________________.

(d) Corporate Status.

[ ] Corporation providing medical and health care services, or engaged in the billing and collecting of payments for such services;

[ ] Other corporate entity

[ ] Not a corporate entity

[ ] Sole proprietorship

[ ] Partnership

[ ] Hospital or extended care facility described in 26 CFR 501(c)(3) that is exempt from taxation under 26 CFR 501(a).

(e) Common Parent.

[ ] A common parent does not own or control the offeror as defined in paragraph (a).

[ ] Name and TIN of common parent:

Name _______________________________________________________

TIN _______________________________________________________

3.2.2.3-76 	Representation- Release of Contract Information (July 2004)

(a) Any contract resulting from this SIR may be subject to release under the Freedom of Information Act (FOIA), 5 U.S.C. Section 552.

(b) The offeror's (you, your) position regarding the possible release of information you provide in response to this SIR is as follows:

(c) REPRESENTATION CONCERNING RELEASE OF CONTRACT INFORMATION--

The offeror (you) represents that--(1)[ ] You have made a complete review of your offer(s) in response to this SIR and no exemption from mandatory release under FOIA exists, and, (2)[ ] You have no objection to the release of any contract you may be awarded in whole or in part resulting from this SIR.

OR

The offeror (you) represents that [ ] your offer(s) in response to this SIR contains information that is exempt from mandatory release under FOIA. Accordingly, you represent that--(1)[ ] You have identified any sensitive documents you submitted in response to this SIR by placing restrictive markings on them.  This may include trade secrets, proprietary information, or commercial or financial information that is privileged or confidential, and (2)[ ] As the party that provided the information, you have provided the Contracting Officer (by separate letter concurrent with this offer) detailed information listing the page(s) to be withheld complete with any and all legal justifications which would permit the FAA to invoke a FOIA exemption.

[End of Provision]

3.2.2.7-7  	Certification Regarding Debarment, Suspension, Proposed Debarment, and Other Responsibility Matters (April 1996)

(a)  The Offeror certifies, to the best of its knowledge and belief, that--

(i)  The Offeror and/or any of its Principals--

(A)  Are [ ] are not [ ] presently debarred, suspended, proposed for debarment, or declared ineligible for the award of contracts by any Federal agency;

(B)  Have [ ] have not [ ] within a three-year period preceding this offer, been convicted of or had a civil judgment rendered against them for: commission of fraud or a criminal offense in connection with obtaining, attempting to obtain, or performing a public (Federal, state, or local) contract or subcontract; violation of Federal or state antitrust statutes relating to the submission of offers: or commission of embezzlement, theft, forgery, bribery, falsification or destruction of records, making false statements, or receiving stolen property; and

(C)  Are [ ] are not [ ] presently indicted for, or otherwise criminally or civilly charged by a governmental entity with, commission of any of the offenses enumerated in subdivision (a)(1)(i)(B) of this provision.

(ii)  The Offeror has [ ] has not [ ] within a three-year period preceding this offer, had one or more contracts terminated for default by any Federal agency.

'Principals,' for the purposes of this certification, means officers; directors; owners; partners; and, persons having primary management or supervisory responsibilities within a business entity (e.g., general manager; plant manager; head of a subsidiary, division, or business segment, and similar positions).  THIS CERTIFICATION CONCERNS A MATTER WITHIN THE JURISDICTION OF AN AGENCY OF THE UNITED STATES AND THE MAKING OF A FALSE, FICTITIOUS, OR FRAUDULENT CERTIFICATION MAY RENDER THE MAKER SUBJECT TO PROSECUTION UNDER SECTION 1001, TITLE 18, UNITED STATES CODE.

(b)  The Offeror shall provide immediate written notice to the Contracting Officer if, at any time prior to contract award, the Offeror learns that its certification was erroneous when submitted or has become erroneous by reason of changed circumstances.

(c)  A certification that any of the items in paragraph (a) of this provision exists will not necessarily result in withholding of an award under this SIR.  However, the certification will be considered in connection with a determination of the Offeror's responsibility.  Failure of the Offeror to furnish a certification or provide such additional information as requested by the Contracting Officer may render the Offeror nonresponsible.

(d)  Nothing contained in the foregoing shall be construed to require establishment of a system of records in order to render, in good faith, the certification required by paragraph (a) of this provision.  The knowledge and information of an Offeror is not required to exceed that which is normally possessed by a prudent person in the ordinary course of business dealings.

(e)  The certification in paragraph (a) of this provision is a material representation of fact upon which reliance was placed when making award.  If it is later determined that the Offeror knowingly rendered an erroneous certification, in addition to other remedies available to the Government, the Contracting Officer may terminate the contract resulting from this SIR for default.

3.3.1-35   	Certification of Registration in Central Contractor Registration (CCR)  (April 2006)

In accordance with Clause 3.3.1-33, Central Contractor Registration, offeror certifies that they are registered in the CCR Database and have entered all mandatory information including the DUNS or DUNS+4 Number.

Name:    ______________________________

Title:  ________________________________

Phone Number:   _______________________

(End of provision)

3.6.2-5    	Certification of Nonsegregated Facilities (April 1996)

(a)  'Segregated facilities,' as used in this provision, means any waiting rooms, work areas, rest rooms and wash rooms, restaurants and other eating areas, time clocks, locker rooms and other storage or dressing areas, parking lots, drinking fountains, recreation or entertainment areas, transportation, and housing facilities provided for employees, that are segregated by explicit directive or are in fact segregated on the basis of race, color, religion, or national origin because of habit, local custom, or otherwise.

(b)  By the submission of this offer, the offeror certifies that it does not and will not maintain or provide for its employees any segregated facilities at any of its establishments, and that it does not and will not permit its employees to perform their services at any location under its control where segregated facilities are maintained.  The offeror agrees that a breach of this certification is a violation of the "Equal Opportunity" clause in the contract.

(c)  The offeror further agrees that (except where it has obtained identical certifications from proposed subcontractors for specific time periods) it will--

(1)  Obtain identical certifications from proposed subcontractors before the award of subcontracts under which the subcontractor will be subject to the "Equal Opportunity" clause;

(2)  Retain the certifications in the files; and

(3)  Forward the following notice to the proposed subcontractors (except if the proposed subcontractors have submitted identical certifications for specific time periods):

NOTICE TO PROSPECTIVE SUBCONTRACTORS OF REQUIREMENT FOR CERTIFICATIONS OF NONSEGREGATED FACILITIES

A Certification of Nonsegregated Facilities must be submitted before the award of a subcontract under which the subcontractor will be subject to the "Equal Opportunity" clause.  The certification may be submitted either for each subcontract or for all subcontracts during a period (i.e., quarterly, semiannually, or annually).

Note:  The penalty for making false statements in offers is prescribed in 18 U.S.C. 1001.

(End of provision)

3.6.2-6    	Previous Contracts and Compliance Reports (April 1996)

The offeror represents that--(a) It [ ] has, [ ] has not, participated in a previous contract or subcontract subject either to the "Equal Opportunity" clause of this solicitation, the clause originally contained in Section 310 of Executive Order No. 10925, or the clause contained in Section 201 of Executive Order No. 11114; (b) It [ ] has, [ ] has not, filed all required compliance reports; and (c) Representations indicating submission of required compliance reports, signed by proposed subcontractors, will be obtained before subcontract awards.

(End of provision)

3.13-4     	Contractor Identification Number--Data Universal Numbering System (DUNS) Number (April 2006)

(a)  Definitions.  As used in this clause

"Contractor Identification Number," as used in this provision, means "Data Universal Numbering System (DUNS) number, which is a nine-digit number assigned by Dun and Bradstreet Information Services, to identify unique business entities (taken from CCR clause)

"Data Universal Numbering System +4 (DUNS+4) number" means the DUNS number assigned by D&B plus a 4-character suffix that may be assigned by a business concern. (D&B has no affiliation with this 4-character suffix.) This 4-character suffix may be assigned at the discretion of the business concern to establish additional CCR records for identifying alternative Electronic Funds Transfer.

(b) Contractor identification is essential for receiving payment and  complying with statutory contract reporting requirements. Therefore, the offeror shall provide its DUNS or DUNS+4 number below.  The DUNS number will be used by the Contracting Officer to verify that the offeror is registered in the CCR database.

DUNS OR DUNS+4 NUMBER:  _________________________

(c)  If the offeror does not have a DUNS number, it should contact Dun and Bradstreet directly to obtain one.

(1)  An offeror may obtain a DUNS number

(i) If located within the United States, by calling Dun and Bradstreet at 1-866-705-5711 or via the Internet at http://www.dnb.com/; or

(ii) If located outside the United States, by contacting the local Dun and Bradstreet office.

(2)  The offeror should be prepared to provide the following information:

(i) Company legal business.

(ii) Tradestyle, doing business, or other name by which your entity is commonly recognized.

(iii) Company Physical Street Address, City, State, and ZIP Code.

(iv) Company Mailing Address, City, State and ZIP Code (if different from physical street address).

(v) Company Telephone Number.

(vi) Date the company was started.

(vii) Number of employees at your location.

(viii) Chief executive officer/key manager.

(ix) Line of business (industry).

(x) Company Headquarters name and address (reporting relationship within your entity).

(End of provision)

PART IV - SECTION L

INSTRUCTIONS, CONDITIONS, AND NOTICES TO OFFERORS

3.1-1      	Clauses and Provisions Incorporated by Reference (December 2005)

This screening information request (SIR) or contract, as applicable, incorporates by reference the provisions or clauses listed below with the same force and effect as if they were given in full text. Upon request, the Contracting Officer will make the full text available, or offerors and contractors may obtain the full text via Internet at:

http://www.asu.faa.gov/conwrite/ (on this web page, select "Search and View Clauses").

3.2.2.3-1  	False Statements in Offers (July 2004)

3.2.2.3-12 	Amendments to Screening Information Requests (July 2004)

3.2.2.3-14 	Late Submissions, Modifications, and Withdrawals of Submittals (July 2004)

3.2.2.3-16 	Restricting, Disclosing and Using Data (July 2004)

3.2.2.3-17 	Preparing Offers (July 2004)

3.2.2.3-19 	Contract Award (July 2004)

L.1		Past Performance Submittal

Prospective Offerors shall provide references for three (3) contracts performed over the past five (5) years that are of similar size and complexity to this requirement.  In no case shall the contract value of a referenced contract be less than $100,000.00.  Each reference shall include a contact point name, phone number, title, job title, and contract amount.

The prospective contractor shall have a minimum of five (5) years experience in the construction of/or renovation of navigational aid facilities, FAA electrical facilities, or buildings of similar size and complexity to this requirement, as identified.

3.2.2.3-20 	Electronic Offers  (July 2004)

(a) The offeror (you) may submit responses to this SIR by the following electronic means:  Facsimile. Your offer must arrive at the place and by the time specified in the SIR. 

(b) Electronic offers must refer to this SIR and include, as applicable, the item or sub-items, quantities, unit prices, time and place of delivery, all representations and other information required and a statement specifying the extent of your agreement with all the FAA's (we) terms, conditions, and provisions..

(c) We may decline to consider electronic offers that do not include required information, or that reject any of the terms, conditions and provisions of the SIR.

(d) We reserve the right to make award solely on the electronic offer. However, if the CO requests, you must promptly submit the complete original (hard copy) signed proposal.

(e) Send your offer electronically to 781-238-7654.

(f) If you chose to send your offer electronically, we will not be responsible for any failure attributable to transmitting or receiving the offer.

(End of Clause)

3.2.2.3-63 	Site Visit (Construction) (July 2004)

(a) AMS clauses 3.2.2.3-42, Differing Site Conditions, and 3.2.2.3-43, Site Investigations and Conditions Affecting the Work, will be included in any contract awarded under this SIR. Accordingly, FAA urges and expects offerors to inspect the site where the work will be performed.

(b) Site visits may be arranged during normal duty hours by contacting:

Name:  Cecilia Eichel

Telephone:  603-881-1255

(End of provision)

3.2.4-1    	Type of Contract (April 1996)

The FAA contemplates award of a Firm Fixed-Price contract resulting from this Screening Information Request.

(End of provision)

3.9.1-3    	Protest (November 2002)

AS A CONDITION OF SUBMITTING AN OFFER OR RESPONSE TO THIS SIR (OR OTHER SOLICITATION, IF APPROPRIATE), THE OFFEROR OR POTENTIAL OFFEROR AGREES TO BE BOUND BY THE FOLLOWING PROVISIONS RELATING TO PROTESTS:

(a) Protests concerning Federal Aviation Administration Screening Information Requests (SIRs) or awards of contracts shall be resolved through the Federal Aviation Administration (FAA) dispute resolution system at the Office of Dispute Resolution for Acquisition (ODRA) and shall be governed by the procedures set forth in 14 C.F.R. Parts 14 and 17, which are hereby incorporated by reference. Judicial review, where available, will be in accordance with 49 U.S.C. 46110 and shall apply only to final agency decisions. A protestor may seek review of a final FAA decision only after its administrative remedies have been exhausted.

(b) Offerors initially should attempt to resolve any issues concerning potential protests with the Contracting Officer.  The Contracting Officer should make reasonable efforts to answer questions promptly and completely, and, where possible, to resolve concerns or controversies. The protest time limitations, however, will not be extended by attempts to resolve a potential protest with the Contracting Officer.

(c) The filing of a protest with the ODRA may be accomplished by mail, overnight delivery, hand delivery, or by facsimile. A protest is considered to be filed on the date it is received by the ODRA.

(d) Only an interested party may file a protest.  An interested party is one whose direct economic interest has been or would be affected by the award or failure to award an FAA contract.  Proposed subcontractors are not "interested parties" within this definition.

(e) A written protest must be filed with the ODRA within the times set forth below, or the protest shall be dismissed as untimely:

(1) Protests based upon alleged improprieties in a solicitation or a SIR that are apparent prior to bid opening or the time set for receipt of initial proposals shall be filed prior to bid opening or the time set for the receipt of initial proposals.

(2) In procurements where proposals are requested, alleged improprieties that do not exist in the initial solicitation, but which are subsequently incorporated into the solicitation, must be protested not later than the next closing time for receipt of proposals following the incorporation.

(3) For protests other than those related to alleged solicitation improprieties, the protest must be filed on the later of the following two dates:

(i) Not later than seven (7) business days after the date the protester knew or should have known of the grounds for the protest; or

(ii) If the protester has requested a post-award debriefing from the FAA Product Team, not later than five (5) business days after the date on which the Product Team holds that debriefing.

(f) Protests shall be filed at:

(1)   Office of Dispute Resolution for Acquisition, AGC-70,

Federal Aviation Administration,

800 Independence Ave., S.W.,

Room 323,

Washington, DC 20591,

Telephone: (202) 267-3290,

Facsimile: (202) 267-3720; or

(2) other address as specified in 14 CFR Part 17.

(g) At the same time as filing the protest with the ODRA, the protester shall serve a copy of the protest on the Contracting Officer and any other official designated in the SIR for receipt of protests by means reasonably calculated to be received by the Contracting Officer on the same day as it is to be received by the ODRA. The protest shall include a signed statement from the protester, certifying to the ODRA the manner of service, date, and time when a copy of the protest was served on the Contracting Officer and other designated official(s).

(h) Additional information and guidance about the ODRA dispute resolution process for protests can be found on the ODRA Website at http://www.faa.gov.

(End of provision)

PART IV - SECTION M

EVALUATION FACTORS FOR AWARD

Award will be made to the prospective Offeror providing the best value as determined by the requirements associated with Past Performance identified below, and lowest price.  Specifically, a Pass grade will be given to prospective Offerors who meet the past performance requirements.  A Fail grade will be given to prospective Offerors who do not meet the past performance requirements.  Award will be made to the Offeror with the lowest price among those Offerors receiving a passing grade.

All prospective Offerors shall have a minimum of five (5) years experience in the construction or renovation of navigational aid facilities, FAA electrical facilities, or buildings of similar size and complexity to this requirement, and demonstrate successful completion of at least three (3) contracts over $100,000.00 for similar facilities.  Value of previously performed contracts shall not be less than $100,000.00 (See L.1, Past Performance Submittal, page 35).

Offerors with less than five (5) years experience and/or less than three (3) contracts of similar size and complexity will not be considered for award.