New Britain – Hartford Busway

Hartford, Connecticut

(November 2006)

The Connecticut Department of Transportation (ConnDOT) is proposing to construct the New Britain-Hartford Busway, an 11-station, 9.4-mile exclusive bus rapid transit (BRT) system operating primarily in an existing and abandoned railroad right-of-way (ROW) on a new two-way roadway between downtown New Britain and downtown Hartford’s Union Station.  The busway would run parallel to Interstate 84

(I-84), the primary transportation link between New Britain, West Hartford, and downtown Hartford.  The project’s operating plan calls for a number of bus routes to operate on the Busway, including services that enter and exit the facility to reach destinations well outside of the immediate corridor without the need for a transfer.  The project scope includes the procurement of 30 new buses and construction of five small park-and-ride lots along the alignment.

I-84 is currently, and is forecast to remain, the region’s most congested highway.  In addition, the combined population of New Britain and Hartford account for just under 50 percent of the entire  metropolitan area’s zero-car households. The proposed busway project is intended to provide faster transit travel times between major activity centers throughout the corridor, improve mobility and accessibility for the corridor’s relatively large transit-dependent population, and promote redevelopment opportunities in older urban centers along the project alignment.

| Summary Description |
| --- |
| Proposed Project: | Bus Rapid Transit |
|  | 9.4 Miles 11 Stations |
| Total Capital Cost ($YOE): | $458.78 Million (includes $11.16 million in finance charges) |
| Section 5309 New Starts Share ($YOE): | $275.27 Million (60.0%) |
| Annual Forecast Year Operating Cost: | $10.0 Million |
| Ridership Forecast (2030): | 15,200 Average Weekday Boardings |
|  | 4,500 Daily New Riders |
| Opening Year Ridership Forecast (2012): | 13,700 Average Weekday Boardings |
| FY 2008 Local Financial Commitment Rating: | Medium |
| FY 2008 Project Justification Rating: | Medium |
| FY 2008 Overall Project Rating: | Medium |

ConnDOT has demonstrated significant progress over the last year.  ConnDOT must resolve outstanding design and ROW issues, gain full commitments of non-New Starts funding, and maintain sufficient New Starts ratings before FTA considers a Full Funding Grant Agreement (FFGA) for the New Britain-Hartford Busway project.

Project Development History and Current Status

The 1994 regional transportation plan prepared by the Capitol Region Council of Governments identified the I-84 corridor west of Hartford as one of the metropolitan area’s high priority corridors in need of improvement.  A major investment study in the corridor was completed in 1999; it resulted in the selection of a BRT system between New Britain and Hartford as the locally preferred alternative.  FTA approved the New Britain - Hartford Busway’s entrance into preliminary engineering (PE) in January 2000.  The project received a NEPA Record of Decision (ROD) in March 2002.  In order to address changes in project scope since issuance of the ROD, ConnDOT completed supplementary environmental work, which FTA approved in June 2006.  FTA approved final design for the project in October 2006.

Significant Changes Since FY 2007 Evaluation (November 2005)

ConnDOT prepared and submitted an updated cost estimate (reflecting an increase of $120 million) and financial plan reflecting anticipated sources and uses of capital and operating funds for transit.  ConnDOT’s updated capital cost estimate reflects revised finance costs, construction unit price and quantity increases, a higher contingency percentage, new work elements, and a revised annual escalation factor.  The updated cost also reflects a revised project implementation schedule which delays revenue operations from December 2011 to January 2012.   Minor updates were made to the project travel forecasts to exclude tangential trips (riders who use a busway station, but do not actually travel over a segment of the busway).

Project Justification Rating: Medium

The project is rated Medium based on the Medium rating for cost effectiveness and the Medium rating for transit-supportive land use.

Cost Effectiveness Rating: Medium

The Medium cost effectiveness rating reflects the level of travel time-benefits (3,800 weekday hours) relative to the project’s annualized costs.

| Cost Effectiveness |
| --- |
| Cost per Hour of Transportation System User Benefit Incremental Cost per Incremental Trip | New Start vs. Baseline $22.07* $19.63 |

* Indicates that measure is a component of Cost Effectiveness rating.

The New Britain-Hartford Busway project is anticipated to result in travel-time benefits not only to residents living within the corridor, but to suburban commuters who take advantage of the flexibility of BRT service.  Specifically, ConnDOT’s operating plan for the Busway allows several routes to exit the facility and circulate through neighborhoods to reach destinations far removed from the alignment.  This reduces the number of transfers required, allows more riders access to more trip origins and destinations with a single-seat ride, and contributes to higher ridership levels.  Approximately 40 percent of travel-time benefits accrue to suburban travel markets, with Hartford and New Britain residents splitting the remainder of time savings.  In addition, zero-car households generate nearly 40 percent of the project’s travel-time benefits.

Based on a cost review and risk assessment conducted by FTA, several risk factors were identified that must be mitigated in order to maintain the current cost.  These factors include both the lack of agreements with Amtrak and a detailed assessment of contamination associated with the Amtrak ROW; the need for more sufficient ROW plans; and the need for detailed utility surveys and utility relocation plans.  Resolution of these issues will be the focus of ongoing FTA oversight of the project.

###### Transit-Supportive Land Use Rating:  Medium

The Medium project rating is based on the Medium-Low rating assigned to existing land use combined with Medium ratings for plans and policies and their performance.

##### Existing Land Use:  Medium-Low

- The project spans four jurisdictions between the downtown areas of Hartford and New Britain.  Intermediate stations serve residential neighborhoods of varying urban and suburban character, with low to medium densities, as well as a mix of auto-oriented commercial and industrial development and undeveloped land. The busway is in a transportation corridor and the stations are adjacent to I-84, additional major roadways, Amtrak ROW, and large, formerly industrial buildings.

- Average population density for all station areas is 5,600 per square mile.  A total of 64,800 employees work in areas to be served by the system.

- Parking rates are modest in downtown Hartford and New Britain, while parking is free and generally available at other station areas.

Transit-Supportive Plans and Policies: Medium

- The State of Connecticut has established Transportation Investment Areas, including the area to be served by this project, in which to focus development and investment in transportation infrastructure.  State legislation passed over the last year requires designation of areas for compact, transit accessible, pedestrian-oriented mixed-use development and permits the use of several state sources to fund transit-oriented development.  The State of Connecticut’s 2005 Master Transportation Plan reinforces these principles.

- A rigorous land use planning effort, the New Britain-Hartford Station Planning Project, was conducted for the busway and has produced conceptual transit-oriented station area plans, although progress in implementation has been slow. The City of Hartford is implementing infrastructure improvements to enhance pedestrian circulation.

- All municipalities are in the process of adopting transit-oriented overlay zoning in response to the project.  The Town of West Hartford and the City of Hartford have adopted overlay zones that support various aspects of transit-supportive development.  An additional TOD Overlay District that would remove restrictions on residential density, height, and lot occupancy was proposed in 2003 but has not yet been adopted.

Performance and Impacts of Policies: Medium

- Significant redevelopment is under way in downtown Hartford, reflecting recovery from a long period of economic decline.  Major components have been completed of the 30-acre Adriaen's Landing site project, which includes a new Connecticut Convention Center, Downtown Marriott Hotel, an entertainment district, residential development, and the Connecticut Center for Science and Exploration.

- Multiple development projects are either newly completed or under construction in downtown Hartford station areas and rehabilitation of existing structures to support new uses is under way at two additional stations.

- The project is conceived as a linchpin for the economic revival of urban areas in Hartford and New Britain, as well as growth throughout the entire corridor.

Other Project Justification Criteria

| Mobility Improvements Rating: Medium-High |
| --- |
| Within ½-mile radius of boarding areas: Existing Employment Projected Employment (2030) Low Income Households (% of total HH) Average Per Station: Employment Low Income Households Transportation System User Benefit Per Project Passenger Mile (Minutes) | 64,800 80,900 4,600 (27)% 5,900* 420* New Start vs. Baseline 3.60* |
| Environmental Benefits Rating: High |
| Criteria Pollutant (Reduction in tons) Carbon Monoxide (CO) Nitrogen Oxide (NOx) Volatile Organic Compounds (VOC) Particulate Matter (PM10) Carbon Dioxide (CO2) Criteria Pollutant Status 8-Hour Ozone (O3) Carbon Monoxide (CO) Annual Energy Savings (million British Thermal Units) | New Start vs. Baseline 254 5 5 N/A 13,850 EPA Designation Moderate Non-Attainment Area* Maintenance Area* 179,124 |
| Operating Efficiencies Rating: Medium |
| System Operating Cost per Passenger Mile (current year dollars) | Baseline $0.732* | New Start $0.663* |

* Indicates that measure is a component of rating for each criterion.

N/A indicates information was not available for this entry.

# Local Financial Commitment Rating: Medium

The Medium local financial commitment rating is based on Medium ratings for the New Starts share of project costs and for both the operating and capital finance plans.

Section 5309 New Starts Share of Total Project Costs: 60%

Rating: Medium

ConnDOT is requesting a 60 percent New Starts share of total project costs, which equates to a Medium rating for this measure.

| Locally Proposed Financial Plan |
| --- |
| Source of Funds | Total Funds ($million) | Percent of Total |
| Federal: Section 5309 New Starts Section 5307 Urbanized Area Formula Funds Section 5309 Fixed Guideway Modernization Funds Section 5309 Bus Discretionary Flexible Funds (CMAQ and STP) FHWA NHS Funds | $275.27 $12.98 $13.06 $22.06 $38.85 $6.00 | 60.0% 2.8% 2.9% 4.8% 8.5% 1.3% |
| State: Special Transportation Fund (STF) STF/Public Act 06-136 | $38.56 $52.00 | 8.4% 11.3% |
| Total: | $458.78 | 100.0% |

NOTE:  The financial plan reflected in this table has been developed by the project sponsor and does not reflect a commitment by DOT or FTA.  The sum of the figures may differ from the total as listed due to rounding.

# Capital Finance Plan Rating: Medium

The capital finance plan is rated Medium.  This reflects a Medium rating each subfactor.

#### Agency Capital Condition: Medium

- The average age of ConnDOT’s Statewide bus fleet is 7.1 years; the average age of the Hartford Division’s bus fleet is 6.6 years, which is younger than the industry average.

- ConnDOT’s Special Tax Obligation bond ratings, which were issued in December 2005, are as follows: Moody’s Investors Service A1 and Fitch AA-.

#### Completeness of Capital Plan: Medium

- The capital plan was reasonably complete and included cash flow statements specifying the sources and uses of capital funds for transit and highway projects Statewide, five years of historical data, bus fleet replacement schedules, and a limited sensitivity analysis.

- The plan was missing some explanatory details.  The sensitivity analysis examined the potential for project cost increases, but did not include an accompanying analysis demonstrating how ConnDOT would address such cost increases.

#### Commitment of Capital Funds: Medium

- Almost 60 percent of non-New Starts funding is committed or budgeted.  Federal funding sources include Section 5307 Formula funds, Section 5309 Fixed Guideway Modernization funds, Section 5309 Bus Discretionary funds, flexible funds including CMAQ and STP, and FHWA National Highway System funds.  State funding sources include revenues from the State Transportation Fund and the funds newly-committed in Public Act 06-136.

#### Capital Funding Capacity: Medium

- The project’s financial plan shows projected cash balances, reserve accounts, and/or access to credit based on the State Transportation Fund that would allow ConnDOT to cover cost increases or funding shortfalls equal to approximately 10 percent of project costs.

#### Capital Cost Estimate and Planning Assumptions: Medium

- Most assumptions in the capital plan are generally consistent with historical experience, although a few are slightly optimistic.

- The capital cost estimate of the project is considered current and reliable.

#### Operating Finance Plan Rating: Medium

The operating finance plan is rated Medium, based upon the average of the ratings of the five subfactors listed below. The operating condition subfactor received a High rating; the completeness subfactor received a Medium rating; the commitment of funds and operating cost estimates and planning assumptions subfactors received Medium-Low ratings; and the operating capacity subfactor received a Low rating.

#### Agency Operating Condition: High

- The ratio of current assets to liabilities as reported in the most recent financial statements for the Special Transportation Fund is 5.8.

- ConnDOT is in good condition with no bus service cutbacks in recent years and a history of being able to draw funds as required from the State Transportation Fund.

#### Completeness of Operating Plan: Medium

- The operating plan was reasonably complete and included a 20-year cash flow statement for the project, the Hartford Bus Division and for transportation Statewide, historical data, identification of key assumptions, and a limited sensitivity analysis.  The plan was missing some explanatory detail including a description of how busway operating costs were estimated.  The sensitivity analysis did not address how ConnDOT would cover unexpected cost increases.

#### Commitment of Operating Funds: Medium-Low

- Less than 50 percent of operating funding is committed.  Planned sources of funds include the State Transportation Fund and farebox revenues.

#### Operating Funding Capacity: Low

- The project’s financial plan shows annual deficits in the State Transportation Fund beginning in 2010, and a negative fund balance beginning in 2019. Although the Legislature is compelled to maintain a minimum positive fund balance for a rolling five-year horizon, the financial plan did not describe any means by which these deficits would be eliminated.

#### Operating Cost Estimates and Planning Assumptions: Medium-Low

- Assumptions regarding the sources of operating funds tend to be conservative, while the assumptions regarding operating costs, uses of funds, and subsidy needs appear optimistic.

MAP