| Company Name: | Equipment/Job Identification: Surface Mechanic Type of Equipment: Make: Model: Year: Use: |
| --- | --- |
| Mine Name: |  |
| Date of Analysis: |  |

# Pre-Assessment:

### List pre-requisites here:

### HazCom Training,

### Hand tool Training

- Part 48 Training

- Basic Hydraulic Training

- Handling Material Training (Proper lifting)

- Personal Protective Equipment Training

- Prevention of slips and falls

# Duty 1: Start-of-shift Activities

Learner will explain the importance of start-of-shift activities.  The learner will explain each job step, why it is conducted, any associated risk, and how to implement appropriate controls.  Start-of-shift activities include the following job steps:

| Job Steps | Importance Narrative (Consider Safety, Production, Maintenance) | Importance Ranking 1=Important 2=Very Important 3=Critical | Satisfactory or Needs Work | Procedures/Risk Resolution/ Notes/Comments |
| --- | --- | --- | --- | --- |
| Attend Pre-shift meeting | To receive the correct information on work assignments |  |  |  |
| Discuss equipment down |  |  |  |  |
| Obtain copy of down sheet |  |  |  | Be sure the trainee gets the appropriate information at the beginning of the shift |
| Obtain assignments |  |  |  | Teams of two, if possible |
| Check trucks |  |  |  |  |
| Check dozers |  |  |  |  |
| Check shovels |  |  |  |  |
| Check graders |  |  |  |  |
| Check loaders |  |  |  |  |
| Self assessment | Ensure fitness for work: mental, physical, attitude, etc. for safety of self & others |  |  |  |

# Duty 2: Examine equipment for preventive maintenance

Learner will demonstrate how to safely and thoroughly examine equipment for preventive maintenance.  Learner will also explain the job steps, why they are conducted, any associated risk, and how to implement appropriate controls.  A safe and thorough equipment examination for preventive maintenance includes the following job steps:

| Job Steps | Importance Narrative (Consider Safety, Production, Maintenance) | Importance Ranking 1=Important 2=Very Important 3=Critical | Satisfactory or Needs Work | Procedures/Risk Resolution/ Notes/Comments |
| --- | --- | --- | --- | --- |
| Examine Shovel |  |  |  |  |
| Conduct visual inspection of the following: |  |  |  | Maintain communication with equipment operator For the 1800, inspect front-to-back instead of side-to-side |
| Ladders | Cause serious personal injury, slips and falls are the number three causes of fatalities in the mining industry |  |  | When you drive up to the shovel these are the first things you would observe |
| Handrails | Cause serious personal injury, slips and falls are the number three causes of fatalities in the mining industry |  |  |  |
| Bucket | Damaged bucket could be very costly and could cause additional damage to machine |  |  |  |
| Grease lines | Insufficient lubrication could cause costly repairs |  |  |  |
| Start at left side of shovel |  |  |  |  |
| Inspect pump room |  |  |  |  |
| Check for: bad hoses & leaks |  |  |  |  |
| Check mainframe for cracks | Early detection is critical to avoid future failure |  |  |  |
| Inspect engine for: leaks, hoses, belts, and guarding | Critical to prevent engine failure and major down time |  |  |  |
| Cross top of machine |  |  |  |  |
| Inspect fire suppression canisters | To ensure fire protection |  |  |  |
| Inspect Sheet metal for debris & build-up across top of machine |  |  |  |  |
| Inspect Air intake hoses for engine | Critical to prevent engine failure and major down time |  |  |  |
| Inspect Handrails | Cause serious personal injury, slips and falls are the number three causes of fatalities in the mining industry |  |  |  |
| Examine air compressor for the following: oil leaks, guards, pressure gauge, pressure relief valve, and drain plugs | May cause hydraulic failure and/or personal injury |  |  |  |
| Open cab door |  |  |  |  |
| Inspect the instrument panels for warning lights | Gives early indication of failures |  |  |  |
| Cross down to right side |  |  |  |  |
| Inspect Engine for leaks, hoses, belts, and guarding | Critical to prevent engine failure and major down time |  |  |  |
| Inspect Pump room for: bad hoses & leaks |  |  |  |  |
| Report problems for Possible hold over | Helps make an informed decision. |  |  | Common problems include: Broken grease lines, hydraulic and engine leaks, missing tooth tip, missing bucket guard, damage to sheet metal and handrails |
| Examine Trucks |  |  |  | Ensure all trucks are in the ditch and operators exited cab before examination All maintenance employees must be out ditch by 15 minutes prior to start of shift |
| Inspect visually the left side of truck engine for the following: |  |  |  |  |
| Inspect intake air boots | Critical to prevent engine failure and major down time |  |  |  |
| Inspect the Fan, alternator, AC belts and guards | Possible engine failure and down time. Personal injury. |  |  | Guards secured/bolts intact |
| Inspect fuel filter and fuel lines for leaks. |  |  |  |  |
| Inspect Steering hoses | Loss of operator control, property damage and personal injury/death |  |  |  |
| Inspect Radiator hoses | Could lose an engine, down time |  |  |  |
| Check clamps |  |  |  |  |
| Inspect wheel for the following: |  |  |  |  |
| Inspect seals | Equipment damage, down time, possible personal injury |  |  | Oil in wheel, look for oil starting to pour. Contact supervisor if conditions are found. |
| Inspect brake pad | Equipment damage, down time, possible personal injury |  |  | cracks in discs, wear |
| Check for missing or loose lug nuts and wedges | Equipment damage, down time, possible personal injury |  |  | Check for spun (shiny metal) |
| Inspect the Tire for: |  |  |  |  |
| Check for inflation/bulging | High cost, damage, replacement availability |  |  | A low tire will bulge on the bottom |
| Check for Damage which includes the following: |  |  |  |  |
| Cuts |  |  |  |  |
| Sidewall cuts | Possible safety issue |  |  | If sidewall cuts bulge all the time, contact supervisor |
| Inspect Rim | Possible failure or safety issue |  |  | Check for cracks, bending |
| Inspect Rings (bead & lock) | Possible failure or safety issue |  |  |  |
| Inspect Front trailing arm for cracks | could cause property damage and personal injury |  |  | Lock and tag out of service and Notify supervisor immediately |
| Inspect Tie rod end | Could lose control of truck; could cause multiple serious injuries and property damage |  |  | Show trainee a loose tie rod for reference |
| Inspect Struts |  |  |  |  |
| Check for Leaks in cylinders |  |  |  | Oil leaks indicates damage |
| Check for broken bearings |  |  |  |  |
| Examine Steering cylinders |  |  |  |  |
| Check pins/bearings |  |  |  |  |
| Check for oil leaks |  |  |  |  |
| Underneath - Middle of truck |  |  |  |  |
| Check Drive shaft for U-Joints, Caps, & Damage |  |  |  |  |
| Examine Truck body/frame & cracks | Early detection is important to prevent down time and high costs |  |  | Notify supervisor immediately |
| Examine for Hydraulic leaks |  |  |  | Look for Hoses rubbing against each other or metal |
| Inspect transmission visually for leaks and loose bolts |  |  |  |  |
| Examine Wish Bone bearing |  |  |  | Look for bearing broken or bolts missing |
| Rear of truck |  |  |  |  |
| Inspect Strut for the following: |  |  |  |  |
| Check Pins coming out | Could cause the truck to roll over causing major property damage and possible serious injury |  |  | Lock and tag out of service; immediately contact supervisor |
| Check for Bearings and leaks |  |  |  |  |
| Examine Bed pins | Could cause the truck to roll over causing major property damage and possible serious injury |  |  | Lock and tag out of service; immediately contact supervisor Remember to check for cracks on bed ears. |
| Check for Broken lens/camera |  |  |  |  |
| Check visually for physical damage to back-up alarm |  |  |  |  |
| Check all Lights |  |  |  |  |
| Go back to rear of truck |  |  |  |  |
| Inspect the Tire for: |  |  |  |  |
| Check for inflation/bulging | High cost, damage, replacement availability |  |  | A low tire will bulge on the bottom |
| Check for Damage which includes the following: |  |  |  |  |
| Cuts |  |  |  |  |
| Sidewall cuts | Possible safety issue |  |  | If sidewall cuts bulge all the time, contact supervisor |
| Inspect Rim | Possible failure or safety issue |  |  | Check for cracks, bending |
| Inspect Rings (bead & lock) | Possible failure or safety issue |  |  |  |
| Inspect visually the right side of truck engine for the following: |  |  |  |  |
| Inspect intake air boots | Critical to prevent engine failure and major down time |  |  |  |
| Inspect the Fan, alternator | Possible engine failure and down time. Personal injury. |  |  | Bolts intact |
| Inspect fuel filter and fuel lines for leaks |  |  |  |  |
| Inspect Steering hoses | Loss of operator control, property damage and personal injury/death |  |  |  |
| Inspect Radiator hoses | Could lose an engine, down time |  |  |  |
| Check clamps |  |  |  |  |
| Inspect wheel for the following: |  |  |  |  |
| Inspect seals | Equipment damage, down time, possible personal injury |  |  | Oil in wheel, look for oil starting to pour. Contact supervisor if conditions are found. |
| Inspect brake pad | Equipment damage, down time, possible personal injury |  |  | cracks in discs, wear |
| Check for missing or loose lug nuts and wedges | Equipment damage, down time, possible personal injury |  |  | Check for spun (shiny metal) |
| Inspect the Tire for: |  |  |  |  |
| Check for inflation/bulging | High cost, damage, replacement availability |  |  | A low tire will bulge on the bottom |
| Check for Damage which includes the following: |  |  |  |  |
| Cuts |  |  |  |  |
| Sidewall cuts | Possible safety issue |  |  | If sidewall cuts bulge all the time, contact supervisor |
| Inspect Rim | Possible failure or safety issue |  |  | Check for cracks, bending |
| Inspect Rings (bead & lock) | Possible failure or safety issue |  |  |  |
| Inspect Front trailing arm for cracks | could cause property damage and personal injury |  |  | Lock and tag out of service and Notify supervisor immediately |
| Inspect Tie rod end | Could lose control of truck; could cause multiple serious injuries and property damage |  |  | Show trainee a loose tie rod for reference |
| Inspect Struts |  |  |  |  |
| Check for Leaks in cylinders |  |  |  | Oil leaks indicates damage |
| Check for broken bearings |  |  |  |  |
| Examine Steering cylinders |  |  |  |  |
| Check pins/bearings |  |  |  |  |
| Check for oil leaks |  |  |  |  |
| Check Hoist cylinders on both sides of truck |  |  |  |  |
| Front of truck |  |  |  |  |
| Check Grill for damage |  |  |  |  |
| Check Handrails | Could contribute to slip and falls, and other injuries |  |  |  |
| Check Steps and Ladder | Could contribute to slip and falls, and other injuries |  |  |  |
| Check Head lights in place | Could result in poor visibility, property damage, and/or personal injury |  |  |  |
| Check Strobe lights in place |  |  |  |  |
| Check actuator on fire suppression system |  |  |  | Ensure red plunger is intact |
| Examine Dozers |  |  |  | Do not work on dozer if operator is in the cab – company policy |
| Ensure blade and ripper are on the ground | Unplanned motion of blade/ripper could result in personal injury |  |  |  |
| Check the push arm on the left side for cracks and ball wear | Major maintenance problems could occur, lose cylinders, etc.; Major $ |  |  |  |
| Check tracks-left side |  |  |  |  |
| Check for broken/missing pads | Fall hazards could result in personal injury |  |  |  |
| Check bushings for wear |  |  |  |  |
| Check pins for stretch |  |  |  |  |
| Check for missing bolts |  |  |  |  |
| Check bottom roller bolts |  |  |  |  |
| Check Front and rear idler bolts |  |  |  |  |
| Check final drives for heat |  |  |  |  |
| Check Segment bolts |  |  |  |  |
| Check cylinder pins (upper and lower) |  |  |  |  |
| Examine for Missing or broken bearings |  |  |  |  |
| Check fire extinguisher | Limits your fire fighting |  |  | All mobile equipment must have a fire extinguisher – company policy |
| Check blade yoke and pins for missing bushings/pins and wear | Major maintenance problems could occur, lose cylinders, etc.; Major $ |  |  |  |
| Check grab rail | Mounting/Dismounting safety; fall prevention |  |  |  |
| Walk to front to dozer |  |  |  |  |
| Check for missing bolts in cutting edge |  |  |  |  |
| Check skin on blade |  |  |  |  |
| Walk to right side |  |  |  |  |
| Check tracks-right side |  |  |  |  |
| Check for broken/missing pads | Fall hazards could result in personal injury |  |  |  |
| Check bushings for wear |  |  |  |  |
| Check pins for stretch |  |  |  |  |
| Check for missing bolts |  |  |  |  |
| Check bottom roller bolts |  |  |  |  |
| Check Front and rear idler bolts |  |  |  |  |
| Check final drives for heat |  |  |  |  |
| Check Segment bolts |  |  |  |  |
| Walk to rear of dozer |  |  |  |  |
| Check ripper pins, bushings, cylinder leaks, and missing ripper tooth (teeth) |  |  |  |  |
| Ensure fire suppression canisters are intact | Control fire |  |  |  |
| Crawl underneath dozer |  |  |  |  |
| Check for major oil leaks | Equipment damage; fire hazard |  |  | Immediately shut down, lock & tag out and report it to supervisor |
| Check belly pan bolts are in place | Belly Pan falling off could result in equipment damage |  |  |  |
| Check seals on pivot shaft |  |  |  |  |
| Check roller and idler bolts (left and right) |  |  |  |  |
| Check equalizer bar (E-Bar), center pin, left & right outer pins |  |  |  | Check for tightness |
| Crawl out the front of the dozer |  |  |  |  |
| Check stabilizer arm | Equipment damage and $ |  |  |  |
| Mechanic Truck |  |  |  | This is the MSHA required safety exam for your service truck |
| Conduct Pre-shift |  |  |  |  |
| Check Seat Belt | Potential for serious bodily injury |  |  | Refer to company policy |
| Check back up alarm while in cab | Potential for serious bodily injury and property damage |  |  | Must be audible – company policy |
| Check cab for extraneous materials | Could cause personal injury and property damage |  |  |  |
| Check parking brake | Potential for serious bodily injury and property damage |  |  |  |
| Check forward horn while in cab | Potential for serious bodily injury and property damage |  |  |  |
| Check radio/communication |  |  |  |  |
| Check all lights |  |  |  |  |
| Check glass for cleanliness and damage |  |  |  |  |
| Check Fire extinguishers | Limits fire fighting ability |  |  |  |
| Check bay doors |  |  |  |  |
| Chock Tires | Required every time you are under truck to prevent unplanned motion |  |  | Chock tires before crawling under truck. Chock tires when parked on incline; refer to company policy |
| Check tires |  |  |  | Tap with hammer |
| Look underneath |  |  |  |  |
| Check Oil leaks |  |  |  |  |
| Check Drive shafts |  |  |  |  |
| Ensure acetylene and oxygen tanks are secured and stored upright | To prevent injury and property damage |  |  |  |
| Check gauges and gauge guards | To prevent injury and property damage |  |  |  |
| Ensure hoses are rolled up | Slip and tripping hazard |  |  |  |
| Ensure crane is cradled and electrical wires are connected |  |  |  |  |
| Check bumper for loose materials | Loose materials can fall off bumper and could be struck by company or public vehicles |  |  | Refer to Company policy |
| Remove extraneous materials from bed of truck | Slip/Trip Hazards resulting in injuries |  |  |  |
| Remove chocks and store in truck |  |  |  |  |
| Complete and turn in inspection sheet | Company/location policy |  |  |  |
| Put on seat belt | To prevent injury |  |  | Company policy |
| Sound horn before moving | To prevent injury |  |  | Company policy |
| Drive defensively | To prevent injury and property damage |  |  |  |

# Duty 3: Examine Work Areas

Learner will demonstrate how to conduct a safe and thorough work area examination.   Learner will also explain the job steps, why they are conducted, any associated risk, and how to implement appropriate controls.  A safe and thorough work area examination includes the following steps:

| Job Steps | Importance Narrative (Consider Safety, Production, Maintenance) | Importance Ranking 1=Important 2=Very Important 3=Critical | Satisfactory or Needs Work | Procedures/Risk Resolution/ Notes/Comments |
| --- | --- | --- | --- | --- |
| Establish communications |  |  |  |  |
| CB channels |  |  |  | Demonstrate use |
| Company FM radios |  |  |  | Demonstrate use |
| Examine Pit areas |  |  |  |  |
| Examine Haul Roads for Congestion & traffic patterns (English/American) | Prevent collisions causing personal injury and property damage |  |  |  |
| Examine Intersections |  |  |  |  |
| Mine | Prevent collisions causing personal injury and property damage |  |  |  |
| Public | Prevent collisions causing personal injury and property damage |  |  | Stop/Yield Right of way to public vehicles |
| Check for Equipment |  |  |  |  |
| Check for Pick-up trucks |  |  |  |  |
| Check for Persons on the ground/in area | To prevent injuries |  |  |  |
| Observe Condition of haul roads |  |  |  |  |
| Check for Debris(rocks), Soft Spots, & Holes |  |  |  |  |
| Observe Wet/dry and visibility conditions | To maintain control of vehicle and prevent collisions causing personal injury and property damage |  |  |  |
| Observe berms |  |  |  | Report berm defects to supervisor |
| Maintain Spacing | To prevent collisions causing personal injury and property damage |  |  | Keep safe distance between mobile equipment; use three second rule |
| Enter the pit |  |  |  |  |
| Examine ramp and look ahead for drop offs | To maintain control of vehicle and prevent collisions causing personal injury and property damage |  |  |  |
| Communicate with trucks or other equipment as to where you are going | Prevent collisions with other vehicles; could get ran over |  |  |  |
| Examine Shop area |  |  |  |  |
| Examine Inside shop |  |  |  |  |
| Use Required PPE | To prevent injuries |  |  | Company policy: hard hats, steel toe shoes, & safety glasses with side shields |
| Look for slip & fall hazards | Slip & Fall hazards are major contributing factors to mining injuries |  |  | Use oil dry to clean up all Oil, grease, water, & hydraulic fluids |
| Remove other housekeeping hazards | Slip, Trip, & Fall hazards are major contributing factors to mining injuries |  |  | Maintain supervisor policy, Trash, shop rags, flammable storage, pallets, Used parts and materials |
| Look for Trip & Fall Hazards | Slip, Trip, & Fall hazards are major contributing factors to mining injuries |  |  | Air hoses, Cables, tools, parts, cribbing and extraneous materials Roll up all cables, cords, & hoses and pick up cribbing, tools, and extraneous materials |
| Observe if clear access is provided to Fire Extinguishers, and electrical boxes | Provides access to fire equipment and electrical components |  |  | If these areas are obstructed, you are to Immediately provide clear access |
| Maintain clear access to first aid equipment and supplies | Provides access to emergency equipment |  |  | Keep eye wash station clean; keep supplies stocked |
| Maintain clear access to all exits | Could result in death or serious injury |  |  |  |
| Maintain proper illumination | Helps avoid personal injury and property damage |  |  |  |
| Check ventilation controls |  |  |  |  |
| Observe compressed gas cylinders | Pressured tanks could become rockets and bombs |  |  | All unguarded valves must be protected and secured |
| Examine Outside of Shop |  |  |  |  |
| Keep area clean | Slip, Trip, & Fall hazards are major contributing factors to mining injuries |  |  | Pick up cribbing, blocks, trash, & used parts; use dumpster where provided |
| Secure compressed gas cylinders, use storage area provide, and observe the no smoking rule | Pressured tanks could become rockets and bombs |  |  | All unguarded valves must be protected and secured |
| Observe metal rack for material storage and cleanliness |  |  |  | Be aware of sharp points |
| Adjust your work based on weather conditions to avoid slip and fall hazards | Slip, Trip, & Fall hazards are major contributing factors to mining injuries |  |  | Be aware of snow accumulation on roof, Rain/snow/ice, ground conditions (mud), & Dust |
| Observe traffic and equipment in the area | Sometimes area is congested |  |  | Including vendors |
| Park service trucks in specific area |  |  |  | North and East sides of Building |
| Check fuel storage area |  |  |  | Water inside of containment area |
| Tank leaks & Fire Extinguishers | Environmental and fire hazards are possible and expensive to clean up |  |  | Two extinguishers required |

# Duty 4:  Working on Equipment in Pit and Shop

Learner will demonstrate how to safely and efficiently work on equipment in the pit and shop areas.  Learner will also explain the job steps, why they are conducted, any associated risk, and how to implement appropriate controls.  Safe and efficient maintenance and repair of equipment in the pit and shop includes the following steps:

| Job Steps | Importance Narrative (Consider Safety, Production, Maintenance) | Importance Ranking 1=Important 2=Very Important 3=Critical | Satisfactory or Needs Work | Procedures/Risk Resolution/ Notes/Comments |
| --- | --- | --- | --- | --- |
| Determine if downed equipment can be moved, move to another location, and coordinate maintenance work with pit boss. | Reduce exposure to hazards |  |  | Maintain safe work area; Estimated time to repair equipment; ask about blasting times & locations |
| Have operators position equipment in a safe area to be worked on | To prevent property damage and serious personal injury |  |  | Refer to company policy |
| Park equipment away from highwalls and spoil area | To prevent property damage and serious personal injury |  |  | Refer to company policy |
| Park equipment out of traffic pattern | To prevent property damage and serious personal injury |  |  | Refer to company policy |
| Have operators exit equipment (unless needed for testing) | To prevent property damage and serious personal injury |  |  | Refer to company policy |
| Attach keys to tag out and place on steering controls | To prevent property damage and serious personal injury |  |  | Refer to company policy |
| Examine immediate work area |  |  |  |  |
| Look for slip, fall and falling materials hazards | Slip & Falls are leading cause of mining injuries |  |  | Clean up immediate work area of Grease, Oil, Mud, Water, Hydraulic fluid, Anti-freeze, Snow/ice/rain, & Rocks. Check the underside of the equipment. Be sure to look up to see if there may be material that could fall onto you from equipment that has been operated in adverse weather conditions, i.e. ice, mud, etc. |
| Examine Highwall/spoil | Prevent being struck by falling material |  |  | Check for Loose material, Major cracks, Mud slides, Movement, Overhangs, Slips, Water running off highwall, and Weather conditions If at all possible, do not work between highwall/spoil and equipment. If you must work in pit, keep equipment as far away from highwall/spoil as possible. |
| Determine if equipment is loaded or unloaded, especially trucks | Prevent being struck by falling material |  |  | Truck may have to be unloaded with a different piece of equipment. |
| Barricade work area if necessary for traffic control or falling materials | Prevent exposure to traffic & falling materials hazards |  |  |  |

# Duty 5: Mounting & Dismounting Equipment

Learner will demonstrate how to properly mount and dismount equipment.  Learner will also explain the job steps, why they are conducted, any associated risk, and how to implement appropriate controls.  Proper mounting and dismounting of equipment includes the following job steps:

| Job Steps | Importance Narrative (Consider Safety, Production, Maintenance) | Importance Ranking 1=Important 2=Very Important 3=Critical | Satisfactory or Needs Work | Procedures/Risk Resolution/ Notes/Comments |
| --- | --- | --- | --- | --- |
| Ensure equipment is blocked/chocked from unplanned movement | Unexpected movement can cause personal injury or death |  |  | Company policy |
| Visually examine ladders, steps, and handholds | Slips and falls are the number three cause of accidents |  |  | Oil, grease, mud and make sure steps/ladders are in good shape Clean if needed |
| Use the three points of contact | Slips and falls are the number three cause of accidents |  |  | Use ropes to raise up supplies if necessary, do not hurry climbing ladder, use all steps in sequence, do not jump, and face machine |
| Check and clean the bottom of shoes |  |  |  | Wear proper footwear Consider the surface you are going to be working on Company policy |

# Duty 6: Working from Elevated Areas

Learner will demonstrate how to work safely in elevated areas.  Learner will also explain the job steps, why they are conducted, any associated risk, and how to implement appropriate controls.  The proper procedures for working safely in elevated areas include the following job steps:

| Job Steps | Importance Narrative (Consider Safety, Production, Maintenance) | Importance Ranking 1=Important 2=Very Important 3=Critical | Satisfactory or Needs Work | Procedures/Risk Resolution/ Notes/Comments |
| --- | --- | --- | --- | --- |
| Determine if you need to steam/clean area | Could be oil covered |  |  |  |
| Inspect and put on your fall protection equipment | To detect any defects and ensure that you are wearing the fall protection properly |  |  | Demonstrate the right way to put on fall protection Discuss lanyard length |
| Use fall protection | To prevent serious injury or fall |  |  | Company policy |
| Determine if you need a man-lift, ladder, or additional help | Important to use the right equipment for the job and basic work procedures |  |  |  |
| Communicate with co-worker |  |  |  |  |
| Operating the manlift |  |  |  | Do not operate man lift until you have completed task training on the lift |
| Ensure handrails/guardrails are in place and in good condition on the manlift | Falls occur because of the lack of adequate handrails and guardrails |  |  |  |
| Use fall protection (required) | Manlift can fail and people can still fall |  |  |  |
| Follow company policy on operating manlift | Require to be task trained before operating the manlift |  |  |  |
| Using ladders |  |  |  |  |
| Use the right ladder for the job | Falls has happen because of use of wrong ladder |  |  | Never climb on top step Secure ladder if needed Refer to ladder safety sheet |

# Duty 7:  Equipment Cribbing

Learner will demonstrate how to safely and thoroughly crib equipment.  Learner will also explain the job steps, why they are conducted, any associated risk, and how to implement appropriate controls.  Safe and thorough cribbing of equipment includes the following job steps:

| Job Steps | Importance Narrative (Consider Safety, Production, Maintenance) | Importance Ranking 1=Important 2=Very Important 3=Critical | Satisfactory or Needs Work | Procedures/Risk Resolution/ Notes/Comments |
| --- | --- | --- | --- | --- |
| Ensure stable foundation for cribbing and jacking | Without stable foundation cribbing and jacking will not be stable |  |  | Weather conditions |
| Determine method of lifting equipment prior to cribbing | State of machine could determine lifting method |  |  | Hydraulic equipment and/or jacks are used for lifting only – cannot be used as cribbing. |
| Using hydraulic jack | Prevent personal injury or death |  |  | Know jack and hose rating and check gauge |
| Using machine hydraulics | Prevent personal injury or death |  |  | Check machine hoses Test the machine drift from hydraulic leaking off prior to cribbing |
| Determine cribbing needs for the equipment being worked on | Prevent personal injury or death |  |  | Spacing, weight, and type of repair to be performed |
| Obtain cribbing materials | Use proper lifting and handling techniques |  |  | Improper lifting and handling causes injuries. Get additional help if needed |
| Use solid cribbing such as straight-grained hardwood | Hardwood provides strength and durability/splitting/crushing |  |  | Check condition of cribbing material and discard damage or defected material |
| Use rated or approved metal jack stands on solid surface | Accidents happen using underrated stands and unstable foundation |  |  | Use only proper pins (not bolts) Use rated or approved stands Know the capacity of stand |
| Lower machine weight onto cribbing | Lets you know if the cribbing will hold the weight of the machine |  |  | Recheck the stability of cribbing |
| Lower and lock all machine components to ground | Prevents movement of machine and provides additional support |  |  |  |

# Duty 8:  Replacing a Hydraulic Hose

Learner will demonstrate how to safely and efficiently replace a hydraulic hose.  Learner will also explain the job steps, why they are conducted, any associated risk, and how to implement appropriate controls.  Safe and efficient replacement of a hydraulic hose includes the following job steps:

| Job Steps | Importance Narrative (Consider Safety, Production, Maintenance) | Importance Ranking 1=Important 2=Very Important 3=Critical | Satisfactory or Needs Work | Procedures/Risk Resolution/ Notes/Comments |
| --- | --- | --- | --- | --- |
| Make sure all implements are at rest | Prevent personal injury or death |  |  |  |
| Shut down machine | Ensures that hydraulics are off |  |  |  |
| Block against motion | Prevent unexpected movement when you unhook the hydraulics |  |  |  |
| Relieve tank pressure | This reduces hydraulic fluid flow (line is still pressurized) |  |  | Be aware of hot hydraulic oil Wear PPE – Glasses & Gloves |
| Hold vacuum on tank when needed | Prevents loss of oil |  |  | If in question, ask experience help because this does not apply to all applications |
| Clean work area and hose connections | Prevents slips, falls and contamination |  |  |  |
| Cover hose end with shielding material | This helps prevent exposure from hot or pressurized oil |  |  | Wrap in rags, etc. |
| Wiggle until fluid flows | This helps prevent exposure from hot or pressurized oil |  |  |  |
| Remove hose |  |  |  |  |
| Install new hose |  |  |  |  |
| Use hose that meets manufacturer specification | Prevents personal injury and property damage $ |  |  | Refer to parts manual or ask |
| Ensure new hose is clean | Prevent machine damage |  |  | Clean ends and inside of hose to prevent contamination |
| Reinstall all factory clamps | Prevent personal injury from hose failure Many equipment fires are due to improper routing of hydraulic hoses |  |  | Prevent premature failure due to rubbing, pinching, kinking |
| Leave area of repair | Because hose may rupture when machine is started |  |  |  |
| Restart machine | Beware of people in area |  |  | Check hydraulic fluids level and bleed system if necessary |
| Check for leaks |  |  |  |  |
| Clean up work area | Machine may require steam cleaning before put back into service |  |  |  |

# Duty 9:  Changing Dozer Rollers

Learner will demonstrate how to safely and efficiently change dozer rollers.  Learner will also explain the job steps, why they are conducted, any associated risk, and how to implement appropriate controls.  Safe and efficient changing of dozer rollers includes the following steps:

| Job Steps | Importance Narrative (Consider Safety, Production, Maintenance) | Importance Ranking 1=Important 2=Very Important 3=Critical | Satisfactory or Needs Work | Procedures/Risk Resolution/ Notes/Comments |
| --- | --- | --- | --- | --- |
| Place machine on clean, level spot | Prevent personal injury and makes job easier |  |  |  |
| Clean off the top of the roller frame |  |  |  |  |
| Chain major bogey to the side frame while machine is setting on ground | Prevent movement and personal injury |  |  | Visual check chain |
| Relieve track tension |  |  |  |  |
| Raise the machine using the blade and/or ripper |  |  |  | Test hydraulics for drift |
| Insert beam or spacing tool between rollers on minor bogey and track | You could lose a finger, hand, and/or arm |  |  | Refer to diagram Use the right tooling |
| Lower dozer back down | Make sure dozer is resting on tooling |  |  |  |
| Obtain and use proper lifting device | Prevent personal injury |  |  | Use saddle beam or fork truck Refer to mfg’s manual Caution on hotness of roller |
| Ensure two inside bolts are in place | Because when we remove the two outside bolts nothing will hold the roller in place if these bolts are missing |  |  |  |
| Remove the outside two bolts first |  |  |  | Must be removed before installing the tooling |
| Install lifting device |  |  |  |  |
| Go under tractor to loosen two inside bolts | To ensure tooling is supporting the roller |  |  | Make sure the roller stays against frame |
| Remove inside two bolts |  |  |  |  |
| Lower from under machine | Could roll off on your foot or cause injury |  |  |  |
| Reverse procedure to install new roller |  |  |  |  |

# Duty 10:  Replacing Shovel Crowd or Level Cylinder

Learner will demonstrate how to safely and efficiently replace a shovel crowd and level cylinder.  Learner will also explain the job steps, why they are conducted, any associated risk, and how to implement appropriate controls.  Safe and efficient replacement of a shovel crowd and level cylinder includes the following job steps:

| Job Steps | Importance Narrative (Consider Safety, Production, Maintenance) | Importance Ranking 1=Important 2=Very Important 3=Critical | Satisfactory or Needs Work | Procedures/Risk Resolution/ Notes/Comments |
| --- | --- | --- | --- | --- |
| Place shovel in a safe and level location | Level location is important for support equipment use to do this job |  |  |  |
| Use man-lift or bucket truck | Using the manlift or bucket truck makes this job easier and safer |  |  | Refer to company policy on manlift use. MSHA task training required for each machine operated. |
| Secure cylinder by chaining bottom of boom | Prevents the cylinder from unwanted movement |  |  | Use minimum 3/8 chain Ton and half come along |
| Remove stick end pin using a pry bar and sledge hammer | Caution must be taken when pulling this pin |  |  | Check with lead man |
| Retract and secure cylinder rod completely with chains | This must be done for safety and balancing cylinder |  |  |  |
| Lock controls |  |  |  |  |
| Shut machine down |  |  |  |  |
| Bleed hydraulic system using valve and auto shut down switch | This reduces hydraulic fluid flow (line is still pressurized) |  |  | Be aware of hot hydraulic oil Wear PPE – Glasses & Gloves Leave key on for shut down switch to work |
| Remove hydraulic hoses | Prevent personal injury |  |  | Refer to procedures |
| Cap hoses | Prevent contamination |  |  |  |
| Position forklift under cylinder | To support the cylinder |  |  | Check for clearance/balance Use special forks and cradle |
| Secure cylinder to the forklift with rated come-alongs | This is critical because we are in an elevated position with people in the area |  |  |  |
| Remove second pin | Caution must be taken when pulling this pin |  |  | Check with lead man |
| Lower cylinder slowly and beware of surroundings | Prevent personal injury and property damage |  |  |  |
| Remove old cylinder with mechanic crane truck |  |  |  |  |
| Replace cylinder |  |  |  |  |
| Reverse procedure for installing new cylinder | Same dangers exist installing as removing |  |  |  |
| Close bleed off valves |  |  |  |  |
| Charge the system (start shovel) | People are in the area |  |  |  |
| Bleed air from cylinder at bleeder ports | Prevent cavitations and ensures smooth operation |  |  | Warranty requires this |
| Remove the specific forks off forklift |  |  |  |  |

# Duty 11: Using Cutting Torch (from service truck at equipment)

Learner will demonstrate how to inspect the cutting torch before use, thoroughly inspect and prepare the work area/site for cutting, and safely use the cutting torch.  Learner will also explain the job steps, why they are conducted, any associated risk, and how to implement appropriate controls.  Safe and thorough equipment and work area/site inspections, preparation, and safe use of the cutting torch include the following job steps:

| Job Steps | Importance Narrative (Consider Safety, Production, Maintenance) | Importance Ranking 1=Important 2=Very Important 3=Critical | Satisfactory or Needs Work | Procedures/Risk Resolution/ Notes/Comments |
| --- | --- | --- | --- | --- |
| Use required PPE | Protects you from materials that may be hot |  |  | Face shield, gloves, leather welding vest, safety glasses, footwear, secure pant legs |
| Remove all personal combustible items | Eliminates possible explosion causing injury |  |  | Matches and lighters Check clothing for combustibles |
| Inspect (visual) equipment and area | Equipment has been destroyed |  |  | Accumulation of flammable/combustible materials |
| Wash down or wet area | Help prevents fire |  |  |  |
| Identify and inform personnel exposed to worksite | Protects you and others working on equipment |  |  |  |
| Barricade area affected if necessary | Prevents people walking into hazards areas |  |  |  |
| Maintain proper ventilation | Health hazards (fumes/oxygen deficiency) |  |  | Use confined space guidelines |
| Examine work area for hazards near the cutting site | People have cut into or through things that have caused fires or explosions |  |  | Refer to examine work areas Fuel tanks, hydraulic tanks, hoses, electrical wires |
| Establish fire watch | Safeguard against fire |  |  |  |
| Use fire blanket when needed | Protects other machine components |  |  | To protect electrical harness, cylinder rods, glass, hoses |
| Hook up torch |  |  |  |  |
| Stand to side while pressurizing the gauges | Gauge or regulator could blow out causing personal injury or death |  |  |  |
| Observe gauges for operating pressures |  |  |  | Acetylene pressure should not exceed 15 PSI Oxygen-40lbs |
| Check tip condition |  |  |  |  |
| Check for installation of flash back arrestor | Prevents explosions and flashbacks |  |  | Mandatory-company policy |
| Check hoses for damages | Prevents fires and personal injuries |  |  | Burn spots, cuts, holes, kinks |
| Locate and position fire equipment | Small fires become big fires quickly |  |  | Fire extinguisher and fire suppression cart |
| Disable automatic mode of fire suppression system | Prevents accidental discharge of fire suppression system |  |  | Refer to disarming procedures Make sure you rearm the system after the work is complete |
| Light torch |  |  |  | See JTA for Burning and Welding |
| Re-arm the fire suppression system on equipment |  |  |  |  |
| Return fire extinguishers and cart |  |  |  |  |

# Duty 12:  Dropping the Belly Pan

Learner will demonstrate how to safely and efficiently drop the belly pan.  Learner will explain the job steps, why they are conducted, any associated risk, and how to implement appropriate controls.  Safe and efficient dropping of the belly pan includes the following job steps:

| Job Steps | Importance Narrative (Consider Safety, Production, Maintenance) | Importance Ranking 1=Important 2=Very Important 3=Critical | Satisfactory or Needs Work | Procedures/Risk Resolution/ Notes/Comments |
| --- | --- | --- | --- | --- |
| Obtain sheet steel for field installations | Provides stable base for handling belly pan |  |  | Company policy |
| Determine a level, dry and remote location to perform work | Provides stable base and keeps you away from other mining activities |  |  |  |
| Place pan cradle on jack |  |  |  |  |
| Position jack and metal for field work | Provides for safe handling of belly pan |  |  |  |
| Position dozer over jack and metal | Eliminates strains and sprains |  |  |  |
| Lower all implements | Prevents unexpected movements |  |  |  |
| Lock out and tag equipment | Prevents unexpected movements |  |  | Company policy |
| Center jack under pan to be removed | Centered for proper balance |  |  | Weight of pan on jack and wear kneepads |
| Ensure that all pan bolts are in place | Ensure that you don’t lose control of pan |  |  | Accidents have occurred |
| Pull hinge pin on pan |  |  |  |  |
| Loosen until one full nut thread remains on all four bolts | Maintain control of pan |  |  |  |
| Lower jack to check to ensure pan is free-resting on nuts, jack, and cradle | Allows pan to break free from the machine |  |  |  |
| Raise jack back up to take the weight of pan | Ensure that the pan does not fall when nuts are removed |  |  |  |
| Remove all four nuts |  |  |  |  |
| Stand clear | Prevents pan from falling on you |  |  |  |
| Lower jack |  |  |  |  |
| Reinstalling belly pan |  |  |  |  |
| Reverse procedure | You are exposed to the same hazards that you were exposed to taking the pan down |  |  | Pan may not align with bolts. In this case manual alignment maybe necessary. Try to get one bolt down through the pan; install nut with all the thread you can get. Finish aligning pan. Pull bolts through pan. Install nuts and tighten. |
| Store jack |  |  |  |  |
| Clean work area |  |  |  |  |

# Duty 13:  Hinging Belly Pan

Learner will demonstrate how to safely and efficiently hinge the belly pan.  Learner will explain the job steps, why they are conducted, any associated risk, and how to implement appropriate controls.  Safe and efficient hinging of the belly pan includes the following job steps:

| Job Steps | Importance Narrative (Consider Safety, Production, Maintenance) | Importance Ranking 1=Important 2=Very Important 3=Critical | Satisfactory or Needs Work | Procedures/Risk Resolution/ Notes/Comments |
| --- | --- | --- | --- | --- |
| Determine a level, dry, and remote location to perform work | Provides stable base and keeps you away from other mining activities |  |  |  |
| Position your service truck |  |  |  |  |
| Dig out roller frame |  |  |  |  |
| Run crane cable between roller frames and track |  |  |  |  |
| Center cable under pan |  |  |  |  |
| Secure cable to track pad on opposite side | If not hook well, the cable may come off |  |  |  |
| Tighten tension on crane cable | Maintain control of pan |  |  |  |
| Place blocking in desired area |  |  |  |  |
| Make sure all hinge pins and brackets are in place | Serious injuries have occurred because hinge pins were missing or damaged and someone removed nuts |  |  |  |
| Make sure all four nuts are in place |  |  |  |  |
| Loosen all nuts until one full nut thread remains on each bolt |  |  |  |  |
| Release cable tension slowly until pan is free |  |  |  |  |
| Tighten tension on crane cable so nuts can be removed |  |  |  |  |
| Remove nuts opposite of the hinge first |  |  |  |  |
| Remove hinge side nuts last |  |  |  |  |
| Remove yourself from area | Prevent yourself from being struck by pan |  |  |  |
| Release cable tension slowly until pan is resting on block |  |  |  |  |
| Make repairs |  |  |  |  |
| Tighten crane cable |  |  |  | Start raising pan in position |
| Install hinge side nuts first |  |  |  |  |
| Install opposite side nuts last |  |  |  |  |
| Tighten all nuts |  |  |  |  |
| Unhook crane cable |  |  |  |  |
| Retract crane cable |  |  |  |  |
| Clean area |  |  |  |  |