# IEEE P1451.3 Proposal

| Proposal Title: | Comments Catlin-39 and -43 |
| --- | --- |
| Proposal Number: | 02-026 |
| Revision Number: | A |
| Date: | 10/19/02 |
| Name: | Lee Eccles/Steve Smith |
| Company: | Boeing Commercial Airplanes/ORNL |
| Phone Number: | 206-655-2824/ |
| Fax Number: | 206-655-7724 |
| Email Address: | Lee.h.eccles@boeing.com |
| Proposal Status: | Initial Draft Revised Draft X Ready for Vote |
| Impacts: | __ __ |
| Action: | _X_ Approved _ _ Approved with changes _ _ Rejected _ _ Returned for revision |

Background:

Catlin-39

8.4.6 – Is Table 70 required or is it a normative summary. Parameters in Table do not seem to appear anywhere in this document.

Catlin-43

8.5 – There is no reference to the required input impedance of a TBIM or TBC.

Table 70 was originally supposed to be a listing of requirements that were taken from G.989.1 and .2. As such it is Normative.

Proposal:

### 10.4.6	Communication parameters

The following table summarizes the physical parameters required by ITU Recommendations G.989.1 and G989.2.

Table 1—Summary of physical parameters

| Peak-to-average power ratio | compliant with Paragraph 5.1 of ITU Recommendation G.989.1 |
| --- | --- |
| RF Data Channel Bandwidth | 6 MHz |
| RF Data Input Tuning Range | 7 MHz (fixed) |
| RF Sync Channel Bandwidth | 150 KHz |
| RF Sync Input Tuning Range | 2 MHz (fixed) |
| RF Input Return Loss | 20 dB |
| RF Input Impedance | 100  |
| Spurious Emissions | see Figure 22 and Figure 23 |
| Signal Leakage/RFI | see Figure 22 and Figure 23 |
| Device Input Impedance | 100  |

### 10.5.5  Electrical isolation

Electrical isolation shall not be required by this standard.

Note: Due to the adoption of the HomePNA™ standard, electrical isolation is provided for the data signals at each and all of the equipment interfaces. However, the DC power is not necessarily isolated. To provide complete isolation, an isolated power converter must be supplied either in the TBIM or in a coupler. See 10.5.8 for coupler recommendations.

Note: Good phone-line engineering practice would include the use of components, wiring, connectors, circuit-board traces, in addition to transient suppressor devices, designed to stand off at least 200 volts on a short-term basis (~ 1 sec) to reliably handle transient-voltage events on the line. Typical HPNA magnetics (i.e., transformer/filter modules) are rated at 1500 V standoff; typical small RF transformers are rated to at least 250 V. Both should serve to interrupt ground loops and provide reasonable isolation in the absence of DC power on the bus.