Survey (Topographic) and Surveyor’s Report Instructions

Surveyor’s Report (form HUD-2457)

- The first date, in paragraph one, shall be the same date as shown in the Surveyor’s Certification on the survey map, and shall be the date of the “on the ground” survey(s).

- Items 1-10 on the form shall be addressed with comments or “N/A”.  These items should correspond with the encumbrances, easements and encroachments listed in the title policy and as shown on the survey map.

- The report must include the surveyor’s signature and have his/her professional seal affixed.

- The re-inspection date(s) shall be all of the subsequent visits to the property by the surveyor in order to confirm that site status is still in conformance with the “on the ground” survey.

- To be considered current, the last inspection of the property, as indicated by the re-inspection date in the report, must have occurred within 120 days of the scheduled closing date.

Survey Map

- The following must be shown on the transit survey map:

- Scale 1” = 40’-0”

- Contours at no more than two-foot intervals.  For steeply sloping site, intervals may be five feet.

- Name of city, county and state.

- Project number and name.

- North arrow, magnetic and true.

- Lot and block numbers of property and names of adjacent property owners.

- Distance to nearest street

- Dimension, length and direction, of each boundary and physical indication of boundary (monuments, markers, fences, etc.).

- All easements, right-of-way, set-back lines, and other restrictions.

- Existing streets, alleys, drives and walks.

- Provide street names or designations.

- Indicate surfacing, curbs and other pertinent data.

- Location and size of all utilities including water, electric, telephone, storm sewer, sanitary sewer and gas lines on and adjacent to the subject property. Include sewer invert elevations and direction of flow.

- Location of natural features such as preservable trees, streams, rock outcropping, etc.

- Available information about subsoil, ground water, fill, and buried foundations, tanks, debris, etc.

- Legal description of the property (must match legal description word for word on the title policy. If it is a metes and bounds description, the legal description and survey map must coincide.)

- Total square feet and acreage.

- All encroachments or deviations from the description of the property or conflicts with descriptions of adjoining properties.

- Point of beginning.

- Point of bearing.

- Legend.

- Width and names of adjacent streets.

- Surveyor’s Certification as noted on HUD-2457. The surveyor’s Certification on the map must correspond with the wording in form HUD-2457 (current ALTA/ASCM standards should be used). Surveyor must sign and seal map directly under the Certification.

- To be considered current, the date of the survey map must be within 120 days of the scheduled closing date.  This would be the last map revision date, unless the “on the ground” is within the 120 day time period.

  - For Air Rights Projects, add the following to the list above:

- Provide a 3 dimensional map.

- Show vertical ways to the ground for required services, e.g. utility and fire suppression lines, chimneys, trash chutes, elevators and emergency exit stairs.

- Show acceptable discharge to a public way from all building egresses, including emergency exits, and services, e.g. trash removal.

  - For “as-built” surveys, add the following to the above list:

- Show the exact location of each building by dimension in relation to other buildings and the property lines.

- Show site improvements such as topographic changes, grading, drainage, etc.

- Show overall dimensions of each building on footprint.

- Show the finish floor elevation of each building.

- Describe each building (i.e. 2-story wood frame; 10-story concrete block, etc.)

- Show the exact location and size of all utilities on or adjacent to the site from the public connection point to each of the buildings.

- Show all paved areas.

- Show all offsite improvements.

References:  Handbook 4460.1 REV-2, Architectural Analysis and Inspections for Project Mortgage Insurance; Handbook 4430.1 REV-1, Initial Closing for Project Mortgages; Multifamily Accelerated Processing Guide