Report #0616

DIGHEMV Conductivity Survey

Everglades National Park

Site Characterization

Dighem, A division of CGG Canada Ltd.	Douglas L. McConnell, P.Eng.

Mississauga, Ontario	Geophysicist

February 1, 1995

A0616FEB.95R

SUMMARY

This report describes the logistics and results of a DIGHEMV airborne geophysical survey carried out for the U.S. Geological Survey over 398 square miles of the Florida Everglades.  Total survey coverage amounted to 1718 miles.  The survey was flown from December 9 to December 14, 1994.

The purpose of the survey was to map resistivity variations due to changes in salt water salinity.  The results are being used to map the fresh-water/salt-water interface in the Everglades National Park, as well as salinity variations.  This is a follow up survey to a an earlier DIGHEMV survey flown in April 1994.  An additional objective is to asses whether the EM system is capable of mapping resistivity variations due to changes in fresh-water runoff.  The previous survey was flown during the dry season.  It was expected that there should be an increased amount of fresh-water runoff due to higher rainfall late in the year.

A DIGHEMV multi-coil, multi-frequency electromagnetic system was used.  The information  from this system was processed to produce maps which display the conductive properties of the survey area.  A GPS electronic navigation system, utilizing a UHF link, ensured positioning of the geophysical data with an accuracy of 3 m.  Visual flight path recovery techniques were used to confirm the location of the helicopter where visible topographic features could be identified on the ground.

The fresh-water/salt-water interface (FWSWI) is clearly mapped.  The three coplanar frequency resistivities and resistivity sections provide qualitative information as to the layering and changes in the FWSWI interface with depth.  	The maps show sufficient detail to identify near surface influences on fresh-water and salt-water.  Additional conclusions follow:

*	Highway 9336 (State Highway 27) from Florida City to Flamingo appears to be acting as a barrier to fresh water.  This is particularly evident on the 56,000 Hz resistivity.

*	An east-west canal, adjacent to a road which connects with Highway 9336, is associated with conductivity which is higher than that of the surrounding, relatively fresh water.

*	In the western portion of the survey area, salt water encroachment appears to be associated with drainage.  For example, a series of creeks which converge at Tarpon Bay are associated with higher conductivity than the surrounding marsh.

*	In the eastern portion of the survey area, Taylor Slough is the main source of fresh water.  A similar feature exists parallel and to the east of Taylor Slough.

*	Shark Valley Slough, in the western portion of the survey area, does not appear to contain as thick a layer of fresh-water float as Taylor Slough, as Shark Valley Slough is more conductive.

*	A similar feature to Taylor Slough may exist near the bend in Highway 9336, centred at 800 49' W Lat., 250 21' N Long.

A comparison of the results of this survey with the April results shows that near surface conductivities are very similar except for the following main differences:

*	The FWSWI appears to have moved to the south by approximately 1/2 mile in the northeast portion of the survey area.  This is consistent with an increase in fresh-water runoff.

*	The 900 Hz resistivities are generally more conductive by about 20% on this recent survey.  As this occurs in both resistive, fresh-water, and conductive, saline-water, portions of the survey area, the difference is probably the result of the lack of an absolute calibration of the EM system.  In future surveys, calibration of the system over a half space of sea water may be useful.

CONTENTS

Section

INTRODUCTION		1.1

SURVEY EQUIPMENT		2.1

PRODUCTS AND PROCESSING TECHNIQUES		3.1

SURVEY RESULTS		4.1

APPENDICES

A.  List of Personnel

INTRODUCTION

A DIGHEMV resistivity survey was flown for The U.S. Geological Survey from December 9 to December 14, 1994 over 398 square miles of the Florida Everglades.  The survey area can be located on map sheet Miami 25080-A1 (see Figure 1).

Survey coverage consisted of approximately 1718 line-miles, including tie lines.  Flight lines were flown in an azimuthal direction of 0( with a line separation of 1/4 mile (400 metres).

The survey employed the DIGHEMV electromagnetic system. Ancillary equipment consisted of a radar altimeter, video camera, analog and digital recorders and an electronic navigation system.  Details on the survey equipment are given in Section 2.  Section 2 also provides details on the data channels, their respective sensitivities, and the navigation/flight path recovery procedure.

SURVEY EQUIPMENT

The instrumentation was installed in an Aerospatiale AS350B turbine helicopter (Registration N350LE) which was provided by Bulldog Helicopters Ltd.  The helicopter flew at an average airspeed of 100 km/h with an EM bird height of approximately 30 m.

Electromagnetic System

Model:	DIGHEMV

Type:	Towed bird, symmetric dipole configuration operated at a nominal survey altitude of 30 metres.  Coil separation is 8 metres for all coil-pairs except for the 56,000 Hz coil-pair which has a 6.3 metre coil separation.

Coil orientations/frequencies:	coaxial	/	900 Hz

coplanar	/	900 Hz

coaxial	/	5,500 Hz

coplanar	/ 	7,200 Hz

coplanar	/	56,000 Hz

Channels recorded:	5 inphase channels

5 quadrature channels

4 monitor channels

Sensitivity:		0.1 ppm at	900 Hz

0.2 ppm at	5,500 Hz

0.2 ppm at	7,200 Hz

0.5 ppm at	56,000 Hz

Sample rate:		10 per second

The electromagnetic system utilizes a multi-coil coaxial/coplanar technique to energize conductors in different directions.  The coaxial coils are vertical with their axes in the flight direction.  The coplanar coils are horizontal.  The secondary fields are sensed simultaneously by means of receiver coils which are maximum coupled to their respective transmitter coils.  The system yields an inphase and a quadrature channel from each transmitter-receiver coil-pair.

Radar Altimeter

Manufacturer:	Honeywell/Sperry

Type:	AA 220

Sensitivity:	1 ft

The radar altimeter measures the vertical distance between the helicopter and the ground.  This information is used in the processing algorithm which determines conductor depth.

The altimeter is calibrated by checking the reading when the helicopter lifts-off and reaches the end of the 100 ft EM bird cable.

Analog Recorder

Manufacturer:	RMS Instruments

Type:	DGR33 dot-matrix graphics recorder

Resolution:	4x4 dots/mm

Speed:	1.5 mm/sec

The analog profiles are recorded on chart paper in the aircraft during the survey.  Table 2-1 lists the geophysical data channels and the vertical scale of each profile.

Table 2-1.  The Analog Profiles

| Channel Name | Parameter | Scale units/mm | Designation on digital profile |
| --- | --- | --- | --- |
| 1XI | coaxial inphase (900 Hz) | 2.5 ppm | CXI (900 Hz) |
| 1XQ | coaxial quad (900 Hz) | 2.5 ppm | CXQ (900 Hz) |
| 3PI | coplanar inphase (900 Hz) | 2.5 ppm | CPI (900 Hz) |
| 3PQ | coplanar quad (900 Hz) | 2.5 ppm | CPQ (900 Hz) |
| 2PI | coplanar inphase (7200 Hz) | 5 ppm | CPI (7200 Hz) |
| 2PQ | coplanar quad (7200 Hz) | 5 ppm | CPQ (7200 Hz) |
| 4XI | coaxial inphase (5500 Hz) | 5 ppm | CXI (5500 Hz) |
| 4XQ | coaxial quad (5500 Hz) | 5 ppm | CXQ (5500 Hz) |
| 5PI | coplanar inphase (56000 Hz) | 10 ppm | CPI (56 kHz) |
| 5PQ | coplanar quad (56000 Hz) | 10 ppm | CPQ (56 kHz) |
| ALTR | altimeter | 3 m | ALT |
| CXSP | coaxial sferics monitor |  | CXS |
| 4XSP | coaxial sferics monitor |  |  |
| CPSP | coplanar sferics monitor |  | CPS |
| 3PSP | coplanar sferics monitor |  |  |
| CXPL | coaxial powerline monitor |  | CXP |
| CPPL | coplanar powerline monitor |  | CPP |
| 3PPL | coplanar powerline monitor |  |  |

Digital Data Acquisition System

Manufacturer:	Picodas

Type:	PDAS 1000

The PDAS 1000 has a built-in hard drive for digital data storage, and two internal magnetometer counters.  The data are downloaded from the hard drive to a DC2120 cassette at the end of each flight.

The digital data are used to generate several computed parameters.  Both measured and computed parameters are plotted as "multi-channel stacked profiles" during data processing.  These parameters are shown in Table 2-2.  In Table 2-2, the log resistivity scale of 0.06 decade/mm means that the resistivity changes by an order of magnitude in 16.6 mm.  The resistivities at 0, 33 and 67 mm up from the bottom of the digital profile are respectively 1, 100 and 10,000 ohm-m.

Table 2-2.  The Digital Profiles

| Channel Name (Freq) | Observed parameters | Scale units/mm |
| --- | --- | --- |
| ALT | bird height | 6 m |
| CXI (900 Hz) | vertical coaxial coil-pair inphase | 8 ppm |
| CXQ (900 Hz) | vertical coaxial coil-pair quadrature | 8 ppm |
| CPI (900 Hz) | horizontal coplanar coil-pair inphase | 8 ppm |
| CPQ (900 Hz) | horiztonal coplanar coil-pair quadrature | 8 ppm |
| CXI (5500 Hz) | vertical coaxial coil-pair inphase | 16 ppm |
| CXQ (5500 Hz) | vertical coaxial coil-pair quadrature | 16 ppm |
| CPI (7200 Hz) | horizontal coplanar coil-pair inphase | 16 ppm |
| CPQ (7200 Hz) | horiztonal coplanar coil-pair quadrature | 16 ppm |
| CPI (56 kHz) | horizontal coplanar coil-pair inphase | 40 ppm |
| CPQ (56 kHz) | horiztonal coplanar coil-pair quadrature | 40 ppm |
| CXS | coaxial sferics monitor |  |
| CXP | coaxial powerline monitor |  |
|  | Computed Parameters |  |
| RES (900 Hz) | log resistivity | .06 decade |
| RES (7200 Hz) | log resistivity | .06 decade |
| DP (900 Hz) | apparent depth | 6 m |
| DP (7200 Hz) | apparent depth | 6 m |
| DP (56 kHz) | apparent depth | 6m |

Tracking Camera

Type:     	Panasonic Video

Model:    	AG 2400/WVCD132

Fiducial numbers are recorded continuously and are displayed on the margin of each image.  This procedure ensures accurate correlation of analog and digital data with respect to visible features on the ground.

Navigation System (RT-DGPS)

Model:	Sercel NR106, Real-time differential positioning

Type:	SPS (L1 band), 10-channel, C/A code, 1575.42 MHz.

Sensitivity:  	-132 dBm, 0.5 second update

Accuracy:   	< 5 metres in differential mode,

± 50 metres in S/A (non differential) mode

The Global Positioning System (GPS) is a line of sight, satellite navigation system which utilizes time-coded signals from at least four of the twenty-four NAVSTAR satellites.  In the differential mode, two GPS receivers are used.  The base station unit is used as a reference which transmits real-time corrections to the mobile unit in the aircraft, via a UHF radio datalink.  The on-board system calculates the flight path of the helicopter while providing real-time guidance.  The raw XYZ data are recorded for both receivers, thereby permitting post-survey processing for accuracies of approximately 2 metres.

Although the base station receiver is able to calculate its own latitude and longitude, a higher degree of accuracy can be obtained if the reference unit is established on a known benchmark or triangulation point.  The GPS records data relative to the WGS84 ellipsoid, which is the basis of the revised North American Datum (NAD83).

Conversion software is used to transform the WGS84 coordinates to the system displayed on the base maps.

Field Workstation

Manufacturer:	Dighem

Model:	FWS: V2.41

Type:	80386 based P.C.

A portable PC-based field workstation is used at the survey base to verify data quality and completeness.  Flight tapes are dumped to a hard drive to permit the creation of a database.  This process allows the field operators to display both the positional (flight path) and geophysical data on a screen or printer.

PRODUCTS AND PROCESSING TECHNIQUES

The following products are available from the survey data.  Those which are not part of the survey contract may be acquired later.  Refer to Table 3-1 for a summary of the maps which accompany this report, some of which may be sent under separate cover.  Most parameters can be displayed as contours, profiles, or in colour.

Base Maps

Base maps of the survey area have been produced from the 1:100,000 scale Cape Sable, Everglades City, Miami and Homestead topographic map sheets.  These were joined and photographically reproduced to a scale of 1:48,000.  The topographic base maps were hand digitized to produce the skeletal topography for the colour maps.

Resistivity

The apparent resistivity in ohm-m was generated from the inphase and quadrature EM components for the 900 Hz, 7,200 Hz and 56,000 Hz frequencies, using a pseudo-layer halfspace model.  A resistivity map portrays all the EM information for that frequency over the entire survey area.  The large dynamic range makes the resistivity parameter an excellent mapping tool.

Table 3-1    Survey Products

Final Transparencies @ 1:48,000

900 Hz resistivity contours

7,200 Hz resistivity contours

56,000 Hz resistivity contours

The final prints display the geophysical parameter combined with the flight path on a screened topographic base.  Two sets of black and white prints are supplied.

Final Colour maps @ 1:48,000

900 Hz resistivity colours

7,200 Hz resistivity colours

56,000 Hz resistivity colours

The colour maps display superimposed contours, flight path, skeletal topography, Lat/Long's and UTM coordinates.  Two sets of colour maps are supplied.

Other Products

Digital XYZ archives with documentation

Digital grid archives

Multi-channel 'stacked' geophysical profiles

Sengpiel and differential resistivity sections for four lines

Note:	The XYZ archives are supplied on a DOS compatible CD-ROM in Geopak ASCII format.

Multi-channel Stacked Profiles

Distance-based profiles of the digitally recorded geophysical data are generated and plotted by computer.  These profiles also contain the calculated parameters which are used in the interpretation process.  These are produced in the final corrected form after interpretation.

Contour and Colour Displays

The geophysical data are interpolated onto a regular grid using a modified Akima spline technique.  The resulting grid is suitable for generating contour maps of excellent quality.

Colour maps are produced by interpolating the grid down to the pixel size.  The parameter is then incremented with respect to specific amplitude ranges to provide colour "contour" maps.

Conductivity-depth Sections

The apparent resistivities for all frequencies can be displayed simultaneously as coloured conductivity-depth sections.  Usually, only the coplanar data are displayed as the quality tends to be higher than that of the coaxial data.

Conductivity-depth sections can be generated in two formats:

(1)	Sengpiel resistivity sections, where the apparent resistivity for each frequency is plotted at the depth of the centroid of the inphase current flow; and,

(2)	Differential resistivity sections, where the differential resistivity is plotted at the differential depth.

Both the Sengpiel and differential methods are derived from the pseudo-layer halfspace model.  Both yield a coloured conductivity-depth section which attempts to portray a smoothed approximation of the true resistivity distribution with depth.  The Sengpiel method is most useful in conductive layered situations, but may be unreliable in areas of moderate to high resistivity where signal amplitudes are weak.  In areas where inphase responses have been suppressed by the effects of magnetite, the computed resistivities shown on the sections may be unreliable.  The differential technique was developed by Dighem to overcome problems in the Sengpiel technique.  The differential resistivity section is more sensitive than the Sengpiel section to changes in the earth's resistivity and it reaches deeper.

SURVEY RESULTS

Resistivity maps, which display the conductive properties of the survey area, were produced from the 900 Hz, 7,200 Hz and 56,000 Hz coplanar data.  The conductivity units, in mS/m, are calculated from the resistivity units in ohm-m as: mS/m = 1000/ohm-m.

The maximum resistivity value, which is calculated for each frequency, is approximately 1.15 times the numerical value of the frequency.  This cutoff eliminates the meaningless higher resistivities which would result from very small EM amplitudes.  The minimum resistivity value is .0000054 times the frequency.  This cutoff eliminates errors due to the lack of an absolute phase control for the EM data.  This cutoff only affected the 56,000 Hz data.

Several points of interest, which appear on the coplanar resistivity maps, in addition to those identified in the report of the April 1994 survey results, are as follows:

*	A red-orange to green-blue resistivity contrast is obvious on all three resistivity colour maps.  It undoubtedly reflects a major salinity contrast, and indicates relatively saline water dominates the western and southern portions of the survey area.  This contrast, which is characterized by resistivities below 10 ohm-m (100 mS/m) to the south and west and resistivities over 10 ohm-m to the north and east, is

almost identical in its location on the 7,200 and 900 Hz maps, but differs in location on the 56,000 Hz maps, east of 800 33' W, in that for the most part the 10 ohm-m contour does not go north of 250 18' N.  This contrast on the 56,000 Hz maps, which is less obvious on the other frequencies, may reflect a secondary salinity interface due to some controlling source that is not indicated on the topographic maps.

*	A comparison of the results from the April survey with this recent survey shows that the main interface mentioned above has moved about 1/2 mile to the south, north of 250 20' and east of 800 31'.  This may reflect an influx of fresh-water.

*	The 900 Hz is consistently more conductive in this recent survey than in the April survey.  This occurs in both fresh-water, high resistivity areas, and salt-water low resistivity areas.  The difference between the resistivity values in any one location for the two surveys is about 20%.  This is probably due to the lack of an absolute calibration of the EM system.  A calibration test over a salt-water half space would allow post-survey phase rotation to ensure that all EM parameters were giving the same value for salt-water.  Assuming that the resistivity of the salt-water did not change over time, this calibration would allow season to season comparisons.

*	Highway 9336 (State Highway 27) from Florida City to Flamingo appears to be acting as a barrier to fresh water.  This is particularly evident on the 56,000 Hz resistivity.

*	A relatively resistive feature, which is similar to Taylor Slough, may exist near the bend in Highway 9336, centred at 800 49' W Lat., 250 21' N Long.  The shape of this resistive area may be affected by the road.

*	An east-west canal, adjacent to a road which connects with Highway 9336, is associated with conductivity which is higher than that of the surrounding, relatively fresh water.

*	In the western portion of the survey area,  the area hosting a series of creeks that converge at Tarpon Bay is associated with higher conductivity than the surrounding marsh.  This indicates that saline water encroaches more where there is existing drainage channels.

*	Shark Valley Slough, in the western portion of the survey area, does not appear to contain as thick a layer of fresh-water float as Taylor Slough, as Shark Valley Slough is more conductive.

Respectfully submitted,

DIGHEM

Douglas L. McConnell, P.Eng.

Geophysicist

APPENDIX A

LIST OF PERSONNEL

The following personnel were involved in the acquisition, processing, interpretation and presentation of data, relating to a DIGHEMV airborne geophysical survey carried out for the U.S. Geological Survey of a selected area of the Florida Everglades.

Don Ellis          		Senior Geophysical Operator

Jordan Cronkwright		Second Geophysical Operator

Steve Alexander		Pilot (Bulldog Helicopters Ltd.)

Gordon Smith		Data Processing Supervisor

Dak Darbha   		Computer Processor

Doug McConnell		Interpretation Geophysicist

Lyn Vanderstarren 		Drafting Supervisor

Mike Armstrong   		Draftsperson (CAD)

Susan Pothiah		Word Processing Operator

Albina Tonello		Secretary/Expeditor

All personnel are employees of Dighem, A Division of CGG Canada Ltd., except for the pilot who is an employee of Bulldog Helicopters Ltd.

DIGHEM

Douglas L. McConnell, P.Eng.

Geophysicist

# Footnotes

Approximate Inversion of Airborne EM Data from Multilayered Ground: Sengpiel, K.P., Geophysical Prospecting 36, 446-459, 1988.

The Differential Resistivity Method for Multi-frequency Airborne EM Sounding: Huang, H. and Fraser, D.C., presented at Intern. Airb. EM Workshop, Tucson, Ariz., 1993.