### SPECIFICATIONS

### for

### MAGNETIC NANOPARTICLE CHARACTERIZATION SYSTEM

Solicitation 1-057-RCA.1380

A magnetic nanoparticle characterization system is needed having, as a minimum, the following specifications:

- Real-time hardware image zoom

- Solid base with automatic tip approach (motor-driven)

- Scan head with isotopic focal system that utilizes laser-on-probe tracking and allows for 90° view of probe/sample area

- Video subsystem required for probe alignment, having a minimum of 200X top view alignment

- Scan modes must include:

  - Standard contact mode

  - Lateral force mode

  - Intermittent contact (wave) mode

  - Phase shift mode

  - Force-distance curves

- Computer-controlled features required with system-specific software, having data acquisition and analysis capabilities

- Several 10-16 bit D/A and A/D converters must be included

- Several magnetic probes must be provided to allow characterization of magnetic nanoparticles

- System must have an acoustic/vibration isolation enclosure

- Cost must include system installation and training