Oakland County PM2.5

Attainment Analysis:

Supplemental Report

.	Prepared for

Pepper Hamilton LLP

600 Fourteenth Street, N.W.

Washington, DC  20005-2004

Prepared by

Gradient Corporation

20 University Road

Cambridge, MA  02138

September 9, 2005

Table of Contents

Page

Executive Summary	ES-1

1	Introduction	1

2	Oakland County PM2.5 Data Analysis	2

2.1	2004 PM2.5 Data	2

2.2	Wind Speed Influence	1

2.3	Meteorological Data from Other Stations	2

3	Does Oakland County Affect Wayne County PM2.5 Levels?	6

4	Weighted Emissions Analysis	9

5	Conclusions	11

6	References	12

Appendix A	Qualifications of Authors

Appendix B	MDEQ Analysis (Weidner, 2005)

Executive Summary

We have been retained by Pepper Hamilton LLP, on behalf of Oakland County, Michigan, to assess the attainment status of Oakland County with regard to the National Ambient Air Quality Standards for PM2.5.  On March 7, 2005, we submitted a technical report entitled "Oakland County PM2.5 Attainment Analysis."  We later discussed the findings of this original report in a meeting with USEPA personnel at Research Triangle Park, North Carolina, on July 14, 2005.  In response to questions and comments received from USEPA during that meeting, and to supplement to the original report, we have prepared this report to address several additional technical issues relating to the Oakland County PM2.5 attainment analysis.

In its initial designation, USEPA contended that, although Oakland County is meeting both the 24-hour and annual PM2.5 standards, the transport of Oakland County emissions contributes to the PM2.5 violations recorded in Wayne County.  To address this issue, we have further analyzed the PM2.5 data taken at the Oakland County monitor in Oak Park, Michigan, from 2000 to 2004, and have compared that data with 2000-2004 data from two Wayne County monitoring locations, Dearborn and Livonia.  We have also made additional meteorological analyses that examine data from other airports and the effect of low wind speeds, and have examined the contribution of emissions from counties near Toledo, Ohio.

Based upon our further analysis of the available PM2.5 and meteorological data, Oakland County should clearly be designated as in PM2.5 attainment, for the following reasons:

- When the Oak Park PM2.5 data are compared with local meteorological data, almost all the Oak Park PM2.5 values above 15 (g/m3 over the last five years have occurred with winds blowing from the south (i.e., indicative of transport from Wayne County and other potential emission sources to the south).  This result is very consistent with both high and low wind speeds.

- The Dearborn monitor in Wayne County records the highest PM2.5 concentrations of any monitor in Wayne County.  When winds are blowing from the north (i.e., from Oakland County towards Wayne County), the annual-average PM2.5 values at the Dearborn monitor over the 2000-2004 time period ranged from 12 to 13.5 (g/m3, which are well below the 15 (g/m3 PM2.5 standard and similar to regional background levels.  Thus, the transport of potential emissions or precursors from Oakland County is not contributing to the PM2.5 violations at the Dearborn monitor.

- Likewise, the Livonia monitor, which is located in Wayne County very close to the southern border of Oakland County, records extremely low annual average PM2.5 values of 8 to 11 (g/m3 when winds are blowing from Oakland County.  These values are well below the regional background levels estimated by USEPA.  Again, the transport of emissions from Oakland County does not contribute to high PM2.5 concentrations at the Livonia monitor.

- The subjective technique applied by EPA of the "weighted emissions score" (Factor 1), which compares emission levels of PM2.5 precursors in Oakland County with other counties, is highly uncertain and depends strongly on the choice of a regional background monitoring location and which counties are included in the analysis.

The use of actual PM2.5 monitoring data and meteorological data should take precedence over any subjective factors.  The meteorological analysis clearly shows that the transport of potential emissions or precursors from Oakland County does not contribute to any PM2.5 violations in Wayne County, but actually improves the PM2.5 air quality in Wayne County.  The PM2.5 monitoring data and meteorological factors document why Oakland County deserves a PM2.5 attainment designation.

# 1	Introduction

We have been retained by Pepper Hamilton LLP, on behalf of Oakland County, Michigan, to assess the attainment status of Oakland County with regard to the National Ambient Air Quality Standards for PM2.5.  On March 7, 2005, we submitted a technical report entitled "Oakland County PM2.5 Attainment Analysis."  We later discussed the findings of this original report in a meeting with USEPA personnel at Research Triangle Park, North Carolina on July 14, 2005.  In response to questions and comments received from USEPA during that meeting, and to supplement the original report, we have prepared this report to address several additional technical issues relating to the Oakland County PM2.5 attainment analysis.

Section 2 of this report presents a more detailed analysis of the PM2.5 data taken at the Oakland County monitor in Oak Park, Michigan, from 2000 to 2004, and includes additional meteorological analyses that examine data from other airports and the effect of low wind speeds.  Because EPA contends that transport of Oakland County emissions contributes to the PM2.5 violations recorded in Wayne County, Section 3 of this report presents a meteorological analysis of the 2000-2004 PM2.5 data for two Wayne County monitoring locations, Dearborn and Livonia.  Section 4 of this report presents a more detailed analysis of the uncertainties involved in the EPA "weighted emissions score" (Factor 1) analysis.  We summarize our conclusions in Section 5 of this report.

This document was prepared by Dr. Peter Drivas and Dr. Chris Long of Gradient Corporation.  The qualifications of the authors are presented in Appendix A.

# 2	Oakland County PM2.5 Data Analysis

## 2.1	2004 PM2.5 Data

In our original March 7, 2005 report, we presented figures for each of the years 2000 through 2004, where 24-hour PM2.5 measurements from the Oakland County Oak Park monitor were segregated by general wind direction into "north" (blowing from the northwest and northeast quadrants) and "south" (blowing from the southwest and southeast quadrants).  Due to the unavailability of PM2.5 data beyond July 2004 from USEPA's Air Quality System (AQS) at the time we prepared these figures, the graph for 2004 was incomplete in our original report.

PM2.5 data for the entire 2004 year are now available on the EPA AQS website, and Figure 1 below updates our original report to include the 24-hour PM2.5 measurements at Oak Park for all of 2004.  This figure confirms our prior conclusions regarding PM2.5 trends at the Oak Park monitor, namely that significantly higher PM2.5 measurements at Oak Park occur when winds are from the south (i.e., indicative of transport from Wayne County).

Figure 2 below updates the summary graph from our original March 7, 2005 report that presents the annual-average PM2.5 values at the Oak Park monitor by wind direction for the years 2000 to 2004.  Figure 2 clearly shows that when winds were blowing from the north towards Wayne County, representing transport across the majority of the Oakland County area (given that the Oak Park monitor is on the southern border of the county), the annual average PM2.5 values were less than 10 g/m3 for every year.  Further, Figure 2 shows that PM2.5 levels measured at the Oak Park monitor, for winds from the north, are on average less than those from rural sites, such as MK Goddard, Pennsylvania (11.9 g/m3) or Bondville, Illinois (12.3 g/m3), that USEPA has selected as representative of regional background PM2.5 levels.

Figure 1.  Daily PM2.5 Levels at Oak Park vs. Daily Average Wind Direction: Complete 2004 Data

Figure 2.  Summary of Annual Average PM2.5 Concentrations at Oak Park by Wind Direction. Dashed line is 12.1 (g/m3, average of MK Goddard (11.9 (g/m3) and Bondville (12.3 (g/m3).

## 2.2	Wind Speed Influence

In response to USEPA comments at our July 14, 2005 meeting regarding the potential influence of low wind speeds on our meteorological analysis of Oak Park PM2.5 data, we further segregated the Oak Park PM2.5 data by low and high wind speed days.  The USEPA comments suggested that changes in wind direction during the day (i.e., a "sloshing" effect) at low wind speeds might result in uncertain 24-hour average resultant wind directions.  Based on the average wind speed at the Detroit City Airport of 3 m/sec, we defined a "low" wind speed day to have an average resultant wind speed of less than 3 m/sec and a "high" wind speed day to have an average resultant wind speed of greater than 3 m/sec.

Figures 3 and 4 below present the results of this further segregation by wind speed.  Figure 3 shows calculated annual average PM2.5 values at the Oak Park monitor by wind direction for low (< 3 m/sec) wind speed days, while Figure 4 shows calculated annual average PM2.5 values at the Oak Park monitor by wind direction for high (> 3 m/sec) wind speed days.

Figure 3.  Oak Park PM2.5 Data by Wind Direction on Low (<3 m/sec) Wind Speed Days.  Dashed line is 12.1 (g/m3, average of MK Goddard (11.9 (g/m3) and Bondville (12.3 (g/m3).

Figure 4.  Oak Park PM2.5 Data by Wind Direction on High (>3 m/sec) Wind Speed Days.  Dashed line is 12.1 (g/m3, average of MK Goddard (11.9 (g/m3) and Bondville (12.3 (g/m3).

Figures 3 and 4 confirm the findings from the prior analyses, namely that when the Oak Park PM2.5 data are compared with local meteorological data, the annual average PM2.5 values above 15 (g/m3 over the last five years are associated with winds blowing from the south (i.e., indicative of transport from Wayne County and other potential emission sources to the south).  This result remains very consistent with both high and low wind speeds from year to year.  The main influence of wind speed is that slightly higher PM2.5 concentrations occur at the Oak Park monitor with lower wind speeds for both the "north" and "south" directions.

## 2.3	Meteorological Data from Other Stations

As discussed in our original March 7, 2005 report, we used hourly meteorological data for the years 2000-2004 for the National Weather Service (NWS) station at the Detroit City Airport for our meteorological analyses of the Oak Park PM2.5 measurement data.  Figure 5 shows the five-year average wind rose summarizing 2000-2004 wind speed and wind direction measurements at the Detroit City Airport.  As shown in this wind rose, the most frequent winds are from the southwest quadrant, with significantly less frequent winds from the northeast and southeast quadrants.

Figure 5.  2000-2004 Wind Rose for Detroit City Airport

In response to comments from USEPA at our July 14, 2005 meeting regarding whether the Detroit City data are representative of meteorological conditions at other Detroit-area weather stations, we obtained meteorological data for the Detroit Metro Airport and the Flint/Bishop Airport from the USEPA air modeling website.  Five-year wind roses representative of long-term meteorological conditions at the Detroit Metro Airport and the Flint/Bishop Airport are shown in Figures 6 and 7. Using meteorological data that we obtained from the Michigan Department of Environmental Quality (MDEQ) for the on-site weather station at the Oak Park PM2.5 monitoring location, we created a five-year wind rose for the Oak Park station, which is shown in Figure 8.

Figure 6.  1988-1992 Wind Rose for Detroit Metro Airport

Figure 7.  1988-1992 Wind Rose for Flint/Bishop Airport

Figure 8.  2000-2004 Wind Rose for Oak Park Weather Station

Each of these additional wind roses is consistent with the wind rose for Detroit City Airport, showing predominant winds from the southwest quadrant, with significantly less frequent winds from the northeast and southeast quadrants.  The primary difference among the wind roses is that the Oak Park monitor in Figure 8 recorded lower wind speeds than the three airport monitors in Figures 5, 6, and 7.  However, the wind direction frequencies at Oak Park (refer to Figure 8) are almost identical to the wind directions recorded at Detroit City Airport (refer to Figure 5).  Based on wind roses for these additional meteorological stations, we conclude that the Detroit City Airport meteorological data are representative of wind flow in the Detroit area.

# 3	Does Oakland County Affect Wayne County PM2.5 Levels?

In order to address whether transport from Oakland County contributes to PM2.5 exceedances in Wayne County, we conducted a similar meteorological analysis of PM2.5 data for two monitoring locations in Wayne County, Dearborn and Livonia.  The Dearborn monitoring location, located within the heavily industrialized Rouge corridor in Wayne County, typically records the highest PM2.5 levels in Wayne County.  The most recent three-year PM2.5 average (2002-2004) at the Dearborn monitor is 18.6 (g/m3 (Chester, 2005).  In addition, we conducted a meteorological analysis of PM2.5 data for the Livonia monitoring location in the northwestern corner of Wayne County, to investigate the potential transport from Oakland County at the monitor in Wayne County that is closest to Oakland County.

Figure 9 presents a summary graph of annual-average PM2.5 concentrations by resultant wind direction for the Dearborn monitor during the five-year period 2000 to 2004.  As shown in Figure 9, when winds were blowing from the north (i.e., from Oakland County towards Wayne County), the annual-average PM2.5 values at the Dearborn monitor in Wayne County were 12 to 13.5 (g/m3 over the 2000-2004 time period.  These PM2.5 concentrations at Dearborn, when winds are blowing from Oakland County, are very similar to those from rural sites, such as MK Goddard, Pennsylvania (11.9 g/m3) and Bondville, Illinois (12.3 g/m3), that USEPA has selected as representative of regional background PM2.5 levels.

In contrast, as shown in Figure 9, the elevated PM2.5 values at Dearborn, with annual average concentrations ranging from 21 to 26 (g/m3, occur with winds from the south.  Thus, the transport of potential emissions or precursors from Oakland County is not contributing to any PM2.5 violations at the Dearborn monitor.  The source of the PM2.5 non-attainment in Dearborn is not Oakland County, but emission sources to the south of Dearborn.  It is clear from Figure 9 that transport from Oakland County actually improves the PM2.5 air quality at the Dearborn monitor.

Figure 9.  Summary of Annual Average PM2.5 Concentrations at Dearborn by Wind Direction.  Dashed line is 12.1 (g/m3, average of MK Goddard (11.9 (g/m3) and Bondville (12.3 (g/m3).

Likewise, as shown in Figure 10 below, the Livonia monitor, which is the closest monitor in Wayne County to the Oakland County border, recorded extremely low annual-average PM2.5 values of 8 to 11 (g/m3 when winds were blowing from the north (i.e., representative of transport across Oakland County).  As shown in Figure 10, these values are well below average PM2.5 levels at either the MK Goddard, Pennsylvania or Bondville, Illinois sites.  The higher PM2.5 values at Livonia, which have annual averages ranging from 16 to 20 (g/m3, occur with winds from the south.  Thus, both Figures 9 and 10 conclusively demonstrate that the transport of potential emissions or precursors from Oakland County does not contribute to PM2.5 violations in Wayne County, but actually improves the PM2.5 air quality in Wayne County.

Figure 10.  Summary of Annual Average PM2.5 Concentrations at Livonia by Wind Direction.  Dashed line is 12.1 (g/m3, average of MK Goddard (11.9 (g/m3) and Bondville (12.3 (g/m3).

# 4	Weighted Emissions Analysis

As discussed in our original March 7, 2005 report, the subjective technique applied by USEPA of the "weighted emissions score" (Factor 1), which compares emission estimates of PM2.5 precursors in Oakland County with those in other counties, is inherently an unreliable methodology for assessing "contribution" due to its reliance on uncertain data inputs and questionable assumptions.  In particular, we previously highlighted the uncertainties associated with the pairing of measured single-site concentration data with estimated county-wide emissions inventories.  We also previously demonstrated the sensitivity of this metric for a change in just one of the parameters (the regional background site) employed in the calculation.

Table 1 demonstrates that this methodology is also sensitive to which counties are included in the analysis.  Relying upon MDEQ (Chester, 2004) information indicating that monitors in Wayne County are impacted by Toledo emissions, the composite emissions score for the Detroit CMSA was recalculated to include the three nearby Toledo, Ohio counties (Lucas, Wood, and Fulton Counties).  Using the more appropriate Bondville, Illinois regional site and adding the three Toledo counties, Table 1 shows that the composite emissions scores for many of the Michigan counties changed significantly from the USEPA analysis, with Oakland County decreasing by 19%.

Table 1

Uncertainty in Composite Emission Scores

| County | Composite Emission Scores | % Change |
| --- | --- | --- |
|  | USEPA, 2004 | With Toledo Counties and Bondville, IL Background Site |  |
| Wayne | 29.8 | 24.8 | -17 |
| Monroe | 15.1 | 15.6 | 3 |
| Oakland | 13.6 | 11.0 | -19 |
| St. Clair | 10.4 | 10.5 | 1 |
| Lucas (OH) | -- | 8.5 | -- |
| Macomb | 9.5 | 7.0 | -26 |
| Genesee | 7.5 | 6.4 | -14 |
| Washtenaw | 5.3 | 4.4 | -16 |
| Livingston | 4.0 | 3.7 | -6 |
| Lenawee | 2.5 | 2.4 | -5 |
| Wood (OH) | -- | 2.2 | -- |
| Lapeer | 2.1 | 1.8 | -16 |
| Fulton (OH) | -- | 1.6 | -- |

Table 1, as well as our original March 7, 2005 analysis, clearly demonstrate that the weighted emissions score is an uncertain and flawed metric for assessing PM2.5 attainment status.  The overall lack of credibility of this metric has been demonstrated by showing significant impacts on the composite emissions scores with slight (but justified) changes in the calculation methodology.  The selection of which counties to include in the metric, which USEPA based upon census areas, rather than on analysis of wind direction and air transport of pollutants, skews the analysis significantly.  Importantly, this metric does not provide any information on whether local PM2.5 contributions in counties such as Oakland County have any impacts in the portions of Wayne County where PM2.5 standards have been exceeded.

# 5	Conclusions

Based upon our further analysis of the available PM2.5 and meteorological data, Oakland County should clearly be designated as in PM2.5 attainment.  In particular:

- When the Oak Park PM2.5 data are compared with local meteorological data, almost all the Oak Park PM2.5 values above 15 (g/m3 over the last five years have occurred with winds blowing from the south (i.e., indicative of transport from Wayne County and other potential emission sources to the south).  This result is very consistent with both high and low wind speeds.

- The Dearborn monitor in Wayne County records the highest PM2.5 concentrations of any monitor in Wayne County.  When winds are blowing from the north (i.e., from Oakland County towards Wayne County), the annual-average PM2.5 values at the Dearborn monitor over the 2000-2004 time period ranged from 12 to 13.5 (g/m3, which are well below the 15 (g/m3 PM2.5 standard and similar to regional background levels.  Thus, based on monitoring and meteorological data, the transport of potential emissions or precursors from Oakland County is not contributing to the PM2.5 violations at the Dearborn monitor.

- Likewise, the Livonia monitor, which is located in Wayne County very close to the southern border of Oakland County, records extremely low annual average PM2.5 values of 8 to 11 (g/m3 when winds are blowing from Oakland County.  These values are well below the regional background levels estimated by USEPA.  Again, the data document that transport of emissions from Oakland County does not contribute to high PM2.5 concentrations at the Livonia monitor.

- The subjective technique applied by EPA of the "weighted emissions score" (Factor 1), which compares emission levels of PM2.5 precursors in Oakland County with other counties, is highly uncertain and depends strongly on the choice of a regional background monitoring location and which counties are included in the analysis.

The use of actual PM2.5 monitoring data and meteorological data should take precedence over any subjective factors such as the "weighted emissions score."  The meteorological analysis clearly shows that the transport of potential emissions or precursors from Oakland County does not contribute to any PM2.5 violations in Wayne County, but actually improves the PM2.5 air quality in Wayne County.  The PM2.5 monitoring data and meteorological factors document why Oakland County deserves an attainment designation for PM2.5.

# 6	References

Chester, S.E. 2004.  Letter from Steven E. Chester, Michigan DEQ to Bharat Mathur, EPA Region V, dated September 1, 2004.

Chester, S.E. 2005.  Letter from Steven E. Chester, Michigan DEQ to Bharat Mathur, EPA Region V, dated February 22, 2005.

U.S. Environmental Protection Agency (USEPA). 2004. Technical Support for State and Tribal Air Quality Fine Particle (PM2.5) Designation. Office of Air Quality Planning and Standards, Integrated Policy and Strategies Group, Research Triangle Park, NC.  December.

Weidner, J.  2005.  Personal Communication.  Senior Transportation Planner, Southeast Michigan Council of Governments (SEMCOG).  August.

Appendix A

Qualifications of Authors

| Peter J. Drivas, Ph.D. Principal Consultant |  |
| --- | --- |
| Dr. Drivas has over 20 years experience in the fields of air quality modeling, pesticide drift, reactive chemical modeling, hazardous spill assessments, and indoor air pollution. He has managed numerous air quality and multimedia modeling programs; has been an expert witness on air quality modeling; and has developed many innovative environmental models, which can predict ozone and photochemical smog formation, soil gas infiltration from buried liquid chemicals into houses, evaporation from oil spills, and the consequences of hazardous spills of toxic materials. He is an expert on numerous Agency-approved and industry standard models including ISC, CALPUFF, AERMOD, RPM-IV, PLUVUE-II, and others. He has published two books and over 30 technical articles in the environmental field. | Practice Areas & Expertise: Air Quality Modeling Emission Source Characterization Soil-Gas Modeling Chemical Engineering Processes Accidental Releases |
| Education: Ph.D., Chemical Engineering, California Institute of Technology M.S., Chemical Engineering, Massachusetts Institute of Technology B.S., Chemical Engineering, Massachusetts Institute of Technology |  |

| Christopher M. Long, Sc.D. Senior Project Manager |  |
| --- | --- |
| Dr. Long is an environmental health scientist with experience in the areas of exposure assessment, indoor air pollution, human health risk assessment, and statistical data analysis. Dr. Long has several years consulting experience in the risk assessment field. At Gradient, Dr. Long has been involved in fate and transport analyses, litigation support, and exposure modeling. Prior to joining Gradient, Dr. Long completed his doctorate in environmental science and engineering at the Harvard School of Public Health. While at Harvard, Dr. Long conducted a comprehensive study investigating the sources and toxicity of indoor particulate matter in residential homes. He received a U.S. EPA graduate fellowship for this work, and he is first author on several recent papers on indoor and outdoor particulate matter. | Practice Areas & Expertise: Indoor/Outdoor Air Quality Airborne Toxicants Exposure Assessment/Modeling Human Health Risk Assessment Epidemiology |
| Education: Sc.D., Environmental Science & Engineering, Harvard School of Public Health M.S., Environmental Engineering, MIT A.B., Chemistry and Environmental Studies, Bowdoin College |  |

| Areas of Expertise |  |
| --- | --- |
|  | Air quality modeling, chemically reactive pollutants, accidental releases, multi-media modeling, chemical process analysis, visibility, indoor air pollution, program management. |
| Education |  |
|  | Ph.D., Chemical Engineering, California Institute of Technology, 1974. S.M. and S.B., Chemical Engineering, Massachusetts Institute of Technology, 1970. |
| Professional Experience |  |
|  | 1996 – present GRADIENT CORPORATION, Cambridge, MA Principal Consultant. Chief scientist for air quality modeling, multi-media modeling, indoor air modeling, hazardous spill assessments, modeling of reactive pollutants, emissions characterization, and chemical process analysis. |
|  | 1989 – 1996 GRADIENT CORPORATION, Cambridge, MA Principal. Chief scientist for air quality modeling practice, hazardous spill assessments, modeling of reactive pollutants, and chemical process analysis. Director of multi-media modeling, emissions characterization, and indoor air pollution studies. |
|  | 1983 – 1989 THERMO ELECTRON CORPORATION, Waltham, MA Environmental Director. Consultant to all Thermo Electron divisions on air quality monitoring and modeling, including the use of EPA dispersion models, photochemical models, and hazardous spill models. |
|  | 1982 – 1983 ENERGY RESOURCES COMPANY, La Jolla, CA Principal Scientist. Directed development of accidental release models and managed air quality modeling activities related to permitting. Designed fluidized bed reactors to minimize emissions. |
|  | 1979 – 1981 ENVIRONMENTAL RESEARCH & TECHNOLOGY, Concord, MA Senior Consultant. Directed air quality modeling studies, including the use of EPA UNAMAP and photochemical models for permitting of new sources. Developed visibility degradation models for compliance with PSD regulations. |
|  | 1975 – 1978 PACIFIC ENVIRONMENTAL SERVICES, Santa Monica, CA Manager, Atmospheric Modeling Division. Responsible for model development, group management, and business development. Project manager for environmental permitting and research studies, including ozone and mobile source modeling. |
|  | 1974 – 1975 CALIFORNIA INSTITUTE OF TECHNOLOGY, Pasadena, CA Research Fellow. Studied indoor air pollution and infiltration rates in buildings by means of a tracer gas technique. |

| Professional Activities |  |
| --- | --- |
|  |  Chairman of AWMA national technical committee on accidental releases. ( Expert witness testimony experience for air quality modeling topics. ( Author of approximately 30 journal articles, books, and conference presentations. |
| Professional Affiliations |  |
|  | American Institute of Chemical Engineers, Consultant to Environmental Division ( Air and Waste Management Association, Chairman of AT-4 Accidental Release Committee ( American Chemical Society ( American Meteorological Association |
| Projects |  |
| project # (hidden text) | Martin Marietta Energy Systems: Technical consultant on reactive chemistry modifications to the HGSYSTEM model to account for UF6 chemistry and thermodynamics. The chemistry involved UF6 flashing to a mixture of vapor and solid particles if accidentally released, reacting with water vapor to form HF and UO2F2, and the HF continuing to react with water vapor. UF6 chemistry and thermodynamic algorithms were combined with the HF chemistry and algorithms in HGSYSTEM. The solutions were obtained by solving a set of 14 simultaneous differential equations involving chemistry, dispersion, and thermodynamics. |
| project # | American Institute of Chemical Engineers, Center for Chemical Process Safety: Co-authored a guideline book describing the latest techniques to calculate the source emissions, transport, and dispersion of hazardous vapor clouds. Source emission techniques that were described included gas and liquid jet releases, pool evaporation, pipeline breaks, and cryogenic releases. Topics included two-phase flow, reactive components, and calculation of multi-component releases. |
| project # | State of Alaska, Department of Environmental Conservation: Managed study to evaluate health and environmental impacts on animals and plants in Prince William Sound, Alaska, caused by hydrocarbon evaporative emissions from the Exxon Valdez oil spill. Developed evaporative emission model for individual air toxics such as benzene, toluene, and xylene from oil spills. Air concentrations resulting from the evaporative emissions were used to assess the risk of adverse environmental impacts in the vicinity of Prince William Sound. |
| project # | Amoco Corporation: Managed study to determine impacts of a proposed chemical plant expansion on ozone concentrations and visibility in a nearby national park, in support of a Prevention of Significant Deterioration (PSD) operating permit. A reactive plume model was used to evaluate ozone concentrations, and a visibility screening technique was used to determine the worst-case visibility impairment caused by the plant emissions. |
| project # | Browning-Ferris Industries: Developed a health risk exposure assessment of stack emissions from a proposed medical waste incinerator. Estimated emission rates of possible hazardous substances released into the air from the incinerator stack, including metals, dioxins, furans, acid gases, pathogens, hydrocarbons, and radioisotopes. Conducted air dispersion modeling using the ISCST model for five years of meteorological data to predict short-term and long-term concentrations and resulting health risks at nearby resident receptor sites. |
| project # | State of California, Air Resources Board: Managed an improved emission inventory for oil production and refining emission sources in the San Joaquin Valley in California, for use as input to a photochemical grid model. All available emission factor models and equations applicable to oil production facilities and refineries were reviewed and compared, and an estimate was made of the statistical accuracy of the most appropriate emission factor. Hydrocarbon emissions were apportioned into individual chemical species for use in photochemical modeling. |
| project # | Major Oil Company: Developed a mathematical model for the prediction of air quality concentrations resulting from the accidental releases of hazardous components. A new algorithm was developed for multicomponent evaporation from a liquid spill mixture. Also, techniques for calculating the evaporation heat balance were evaluated, and a method was developed to determine the phase partitioning of boiling compounds. |
| project # | Insurance Company: Directed scientific investigation into historical chemical manufacturing and waste disposal processes. Relevant patents and process flow sheets were reviewed to determine the basic process chemistry and the amount and type of waste material created. Based on the process chemistry, chemical reaction calculations were performed to determine the composition of the waste stream by-products. |
| project # | Thermo Electron: Developed a mathematical model to predict evaporation and transport of pollutants at high temperatures through porous media. The model included the effects of cylindrical as well as rectangular geometry, considered the addition of a layer that inhibits diffusion, and included the effects of variable pore size and geometry in the porous medium. |
| project # | EPA Region II: Evaluated potential human risks due to implementation of recommended remedial actions at a hazardous waste site. Calculated emissions and air concentrations resulting from five different remedial activities, including soil excavation, incineration, site capping, and sediment dredging. Exposure and resulting health risks due to emission of PCB vapors and dust were examined using EPA-recommended air quality dispersion and deposition models. |
| project # | Major Chemical Company: Developed an innovative model for evaluating the air emissions from buried hazardous waste material, resulting in a presentation at the 1990 Air and Waste Management Association meeting. The new model showed that typical techniques used to calculate buried waste emissions may overpredict air concentrations by an order of magnitude. Conducted air quality dispersion modeling to estimate downwind exposures and concentrations. |
| project # | Browning Ferris Industries: Investigated air quality issues associated with the expansion of a landfill in Minnesota. Calculated the air exposures of nearby populations to potential releases of air toxics emissions from the site by using EPA-recommended air quality models. Investigated the effects on the air quality modeling results of variability in terrain, year-to-year changes in site meteorology, and the use of rural vs. urban dispersion coefficients. |
| project # | Law Firm: Developed a general indoor air pollution model that can predict indoor concentrations, as a function of time, of gases, particulates, or fibers such as asbestos. A Gaussian puff dispersion model was combined with a flow field and general building decay parameters for a comprehensive model of indoor air transport and dispersion of a point source of emissions. |
| project # | General Electric: Provided chemical process analysis development for the manufacture of a solid-state energy conversion device. Developed time and temperature process parameters for manufacturing, both theoretically and experimentally, and calculated chemical formation and degradation rates as a function of temperature. |
| project # | Government of China: Trained representatives from Beijing and Lanzhou, China, on the theory, operation, and practical application of Gaussian and photochemical air quality models. Developed a microcomputer version of the OZIPM-2 photochemical model to determine ozone control strategies in China. |
| project # | Consortium of Oil Companies: Developed numerical modeling techniques for predicting the air quality impact of spills of cryogenic materials from storage tanks and pipelines, and two-phase (gas and liquid) flow from high-pressure liquid pipelines. A comprehensive modeling system was developed for handling any type of hazardous spill. |
| project # | U.S. Department of Energy: Designed a fluidized bed combustion reactor to minimize air pollutant emissions of SO2 and NOx. A numerical model was developed to calculate fluid flow, mixing, and chemical reactions inside a fluidized bed reactor, and the results of the calculations were used to guide pilot plant experimental development. |
| project # | Texaco: Managed the successful air quality permitting of an expansion of oil production operations in California. Met with state and local representatives and conducted emissions and air dispersion modeling to demonstrate compliance with current regulations. |
| project # | Consolidated Edison of New York: Directed the successful air quality permitting of a change in power plant fuel from oil to coal, involving very detailed air dispersion modeling that considered "street canyon" effects in New York City. Also, developed environmental and economic analyses of currently available and possible future types of burners and control equipment for reducing pollutants from coal-fired power plants. |
| project # | State of Maine, Department of Environmental Protection: Developed a liquid spill evaporation model to predict time-dependent multicomponent air pollution concentrations resulting from oil spills. Results of the model were used to analyze the health risks to residents near a liquid spill waste facility. |
| project # | Northern Tier Pipeline Company: Developed an improved visibility degradation model, and used this model to predict the impact of a proposed marine terminal on visibility impacts in Washington's Olympia National Park. Ten scenic views, selected by the National Park Service, were modeled to determine the amount of visibility impairment due to emissions from the proposed marine terminal. |
| project # | EPA, Office of Air Quality Planning and Standards: Directed a major atmospheric tracer study to develop basic experimental data on dispersion in complex terrain. Dual atmospheric tracers (SF6 and Freon-11) were released from different heights over a small hill with over 50 sampling locations. Responsible for the experimental analysis and database development for thousands of air samples. Results from this study were used to develop EPA's Complex II air quality model. |
| project # | Aluminum Association: Managed a comprehensive SF6 tracer study at an aluminum plant to develop basic experimental data for the line-source type of releases characteristic of aluminum plants. Results from this study were used to develop EPA's Buoyant Line and Plume (BLP) model. |
| project # | EPA, Region I: Used the city-specific version of the OZIPP photochemical model to estimate hydrocarbon emission reductions necessary to attain the ozone air quality standard in Massachusetts, Connecticut, and Rhode Island. The city-specific ozone model was run with the specific UV intensity, transported ozone, dilution rate, and emission parameters for each of five major urban areas to determine the emission reductions necessary in each area to attain the ozone standard. |
| project # | EPA, Office of Air Quality Planning and Standards: Developed procedures for the acquisition and compilation of emission information into the form required for input into photochemical air quality simulation models. Emission methods were applicable to both grid and trajectory photochemical models. Techniques were developed for obtaining the necessary spatial and temporal resolution, and for segregating hydrocarbon emissions into the reactive species required by the photochemical model. |
| project # | State of Arizona, Highway Department: Used a photochemical trajectory model to analyze the impact on ambient ozone levels of a proposed new highway in Phoenix. Nine worst-case air trajectories were modeled that would maximize the ozone impact of the new highway in major residential communities in and near Phoenix. The highway was built after our study concluded that there would be only minor ozone impacts. |
| project # | Zinc Galvanizing Company: Directed an emissions monitoring and air quality dispersion modeling study for a zinc galvanizing facility in Los Angeles. The basic galvanizing process was studied to determine emission parameters, stack testing was conducted, and the emission results were used as input to an air quality model. Provided expert witness testimony on emissions and air modeling. |
| project # | United Airlines: Performed an air quality dispersion modeling study for a proposed United Airlines food waste incinerator at Los Angeles International Airport. Provided expert witness testimony on air quality modeling and the impact of the incinerator on nearby residents. The incinerator was successfully permitted and is currently operating. |
| project # | ASARCO: Monte Carlo air modeling and risk assessment at operating smelter. |
| Publications & Presentations |  |
|  | Brody, J.G., D.J. Vorhees, S.J. Melly, S.R. Swedis, P.J. Drivas, and R.A. Rudel. 2002. "Using GIS and Historical Records to Reconstruct Residential Exposure to Large-Scale Pesticide Application." Journal of Exposure Analysis and Environmental Epidemiology, 12: 64-80. |
|  | Drivas, P.J., P.A. Valberg, B.L. Murphy, and R. Wilson. 1996. " Modeling Indoor Air Exposure from Short-term Point Source Releases." Indoor Air 6:271-277. |
|  | Valberg, P.A., P.J. Drivas, S.M. McCarthy, and A.Y. Watson. 1996. "Evaluating the Health Impacts of Incinerator Emissions." J. Hazardous Material, 47:205-227. |
|  | Hanna, S.R., P.J. Drivas, and J.C. Chang. 1996. Guidelines for Use of Source Emissions and Atmospheric Dispersion Models for Accidental Releases. Center for Chemical Process Safety, American Institute of Chemical Engineers, New York. |
|  | Drivas, P.J. 1995. "A Review of Source Emission Models for Accidental Releases." Paper No. 95-TP54A.03. Proceedings: The 88th Annual Meeting of the Air and Waste Management Association, San Antonio, TX, June 19-23. |
|  | McCarthy, S.M., P.J. Drivas, and R.J. Yamartino. 1994. "The Design and Evaluation of Oil Production Emission Database Files for Input to the SARMAP Modeling System." Proceedings: Regional Photochemical Measurement and Modeling Studies Conference, San Diego, CA, November 8-12. |
|  | Murphy, B.L. and P.J. Drivas. 1993. "Migration of Volatile Contaminants into Buildings." Proceedings: Eighth Annual Conference on Contaminated Soils, Amherst, MA. |
|  | Drivas, P.J., K. Raabe, L.C. Daly, and L.K. Zuke. 1993. "Air Toxics Modeling of Excavation and Landfilling Activities." Paper 93-RA-114A.03, 86th Annual Air and Waste Management Association Meeting, Denver, Co. |
|  | Hanna, S.R. and P.J. Drivas. 1993. "Modeling VOC Emissions and Air Concentrations from the Exxon Valdez Oil Spill." Journal of the Air and Waste Management Association, 43:298-309. |
|  | Drivas, P.J., B.L. Murphy, and P.A. Valberg. 1992. "Exposure Modeling of Indoor Sources of Particulates or Fibers." Proceedings: Society for Risk Analysis - 1992 Annual Meeting, San Diego, CA. |
|  | Drivas, P.J., P.A. Valberg, and T.D. Gauthier. 1991. "Health Assessment of Air Toxics Emissions from Alternative Fuels." Paper 91-107.6, 84th Annual Air and Waste Management Association Meeting, Vancouver, BC. |
|  | Drivas, P.J. and L.C. Daly. 1991. "Calculation of Evaporative Emission Rates of Air Toxics from a Multicomponent Liquid Spill." Paper 91-84.7, 84th Annual Air and Waste Management Association Meeting, Vancouver, BC. |
|  | Drivas, P.J. 1991. "Validation of Hazardous Spill Emission Models." Invited Paper, International Conference and Workshop on Mitigating the Consequences of Accidental Releases of Hazardous Materials, New Orleans. |
|  | Drivas, P.J., A.P. Toole, and S.C. Gnewuch. 1990. "The Effects of Global Warming and Increased UV Radiation on Urban Ozone Concentrations." Paper 40C, American Institute of Chemical Engineers, Summer National Meeting, San Diego, CA. |
|  | Drivas, P.J., D.H. Bass, and B.L. Murphy. 1990. "Atmospheric Emissions from Buried Hazardous Waste." Paper 90-74.4, 83rd Annual Air and Waste Management Association Meeting, Pittsburgh, PA. |
|  | Hanna, S.R., and P.J. Drivas. 1987. Guidelines for Use of Vapor Cloud Dispersion Models. Center for Chemical Process Safety, American Institute of Chemical Engineers. |
|  | Drivas, P.J. 1986. "Two-dimensional Resistance Analysis in a Thermoelectric Multicouple." Proceedings: 21st Intersociety Energy Conversion Engineering Conference, San Diego, CA, pp. 1353-1356. |
|  | Drivas, P.J. 1985. "Prediction of Multicouple Performance." Proceedings: Fifth Working Group Meeting on Thermoelectrics, Pasadena, CA. |
|  | Drivas, P.J., J.S. Sabnis, and L.H. Teuscher. 1983. "Simulation of Pipeline and Tank Storage Failures." Oil and Gas Journal: 162-169 (September). |
|  | Drivas, P.J. 1982. "Calculation of Evaporative Emissions from Multicomponent Liquid Spills." Environmental Science and Technology, 16:726-728. |
|  | Heinold, D.W., P.J. Drivas, D.A. Hansen, and T.F. Lavery. 1982. "Acid Rain Impact Assessment: From Stack to Stream." Proceedings: AMS/APCA Third Joint Conference on Applications of Air Pollution Meteorology, San Antonio, TX. |
|  | Drivas, P.J. and D.W. Heinold. 1981. "Visibility Impact Analysis of a Marine Oil Terminal." Proceedings: Fifth Symposium on Turbulence, Diffusion, and Air Pollution. Atlanta, GA. |
|  | Drivas, P.J., A. Bass, and D.W. Heinold. 1981. "A Plume Blight Visibility Model for Regulatory Use." Atmospheric Environment 15:2179-2184. |
|  | Drivas, P.J., K.H. Wilson, and L.W. Wayne. 1979. "A Case Study: Use of City-Specific EKMA in Massachusetts, Connecticut, and Rhode Island." Proceedings: Specialty Conference on Ozone/Oxidants, Houston, TX. |
|  | Drivas, P.J. 1978. "Emission Inventory Requirements for Photochemical Air Quality Simulation Models." Proceedings: Specialty Conference on Emission Factors and Inventories, Anaheim, CA. |
|  | Wayne, L.W. and P.J. Drivas. 1978. "Sensitivity of the Empirical Kinetic Modeling Approach to Input Data and Local Conditions." Paper 78-72.2, 71st Annual APCA Conference, Houston, TX. |
|  | Drivas, P.J. and L.W. Wayne. 1977. "Sensitivity Tests of a Lagrangian Photochemical Air Quality Simulation Model." Paper 78-10.3, 71st Annual APCA Conference, Houston, TX. |
|  | Drivas, P.J., M. Chan, and L.W. Wayne. 1977. "Validation of an Improved Photochemical Air Quality Simulation Model." Proceedings: AMS/APCA Joint Conference on Applications of Air Pollution Meteorology, Salt Lake City, UT. |
|  | Drivas, P.J. 1976. Emissions from Hot-Dip Galvanizing Processes. EPA Report No. EPA-905/4-76-002, USEPA, Region V, Chicago, IL. Available as Document PB251910, U.S. Dept. of Commerce, National Technical Information Service, Springfield, VA. March. |
|  | Drivas, P.J. 1975. "On the Measurement of Ambient Halogenated Hydrocarbons." Proceedings: Caltech Air Quality Symposium, Pasadena, CA. |
|  | Drivas, P.J. and F.H. Shair. 1974. "Probing the Air Flow Within the Wake Downwind of a Building by Means of a Tracer Technique." Atmospheric Environment 8:1165-1175. |
|  | Drivas, P.J. and F.H. Shair. 1974. "A Tracer Study of Pollutant Transport and Dispersion in the Los Angeles Area." Atmospheric Environment 8:1155-1163. |
|  | Griffith, G.A., P.J. Drivas, and F.H. Shair. 1974. "An Inexpensive Remote Sequential Air Sampler." Journal of the Air Pollution Control Association 24:776-777. |
|  | Drivas, P.J. and F.H. Shair. 1974. "Dispersion of an Instantaneous Crosswind Line Source of Tracer Released from an Urban Highway." Atmospheric Environment 8:475-484. |
|  | Drivas, P.J., P.G. Simmonds, and F.H. Shair. 1972. "Experimental Characterization of Ventilation Systems in Buildings." Environmental Science and Technology 6:609-614. |
| Patent |  |
|  | Shair, F.H., P.G. Simmonds, R.B. Leighton, and P.J. Drivas. 1975. "Technique and System for Coding and Identifying Materials." |

| Areas of Expertise |  |
| --- | --- |
|  | Public health and exposure assessment, with expertise in indoor/outdoor air pollution and particulate matter; air dispersion modeling; epidemiology; human health risk assessment; risk communication; statistical data analysis. |
| Education |  |
|  | Sc.D., Environmental Science & Engineering, Harvard School of Public Health, 2000. M.S., Environmental Engineering, Massachusetts Institute of Technology, 1995. A.B., Chemistry and Environmental Studies, summa cum laude, Bowdoin College, 1993. |
| Professional Experience |  |
|  | 2000 – Present GRADIENT CORPORATION, Cambridge, MA Senior Project Manager. Evaluate human exposure and health effects of environmental pollutants, specializing in airborne gases and particles. Investigate indoor and outdoor air quality problems, and perform air dispersion and exposure modeling. Conduct human health risk assessments and worker safety evaluations, and review and interpret epidemiological and toxicological studies. Prepare technical analyses, expert reports, and risk communication materials. |
|  | 1997 – 2000 HARVARD SCHOOL OF PUBLIC HEALTH, Boston, MA Research/Teaching Assistant. Designed and conducted indoor air particle characterization study of nine Boston-area homes. Also served as teaching assistant for two graduate courses: Seminar in Risk Analysis, Management, and Communication and Air Pollution: Particles and Gases. |
|  | 1995 – 1997 MENZIE-CURA & ASSOCIATES, INC., Chelmsford, MA Environmental Scientist/Risk Assessor. Conducted human health and ecological risk assessments for state and federal hazardous waste sites. Modeled fate and transport of organic and inorganic contaminants in all environmental media. Responsibilities also included project management, proposal writing, and litigation support. Participated in environmental site assessments and field sampling activities of aquatic and terrestrial habitats. OSHA-certified 40-hour training. |
|  | 1993 – 1995 MASSACHUSETTS INSTITUTE OF TECHNOLOGY, Cambridge, MA Research Assistant. Conducted research in trace organic pollutant laboratory. Modeled the fate and transport of sewage-derived linear alkylbenzenes (LABs) in the Gulf of Maine. |
|  | 1992 NASA GODDARD SPACE FLIGHT CENTER, Greenbelt, MD Research Assistant. Selected as summer intern in Summer Institute on Atmospheric and Hydrospheric Sciences; worked with atmospheric scientists in GSFC’s Atmospheric Chemistry and Radiation Branch. Used a photochemical box model to explore the potential for ozone depletion in the Northern Hemisphere stratosphere at middle and low latitudes. |

| Professional Activities |  |
| --- | --- |
|  |  Invited technical peer reviewer for the Journal of the Air & Waste Management Association, Environmental Science & Technology, Environmental Health Perspectives, and Journal of Exposure Analysis and Environmental Epidemiology. |
| Awards/Honors |  |
|  |  U.S. EPA STAR Graduate Fellow, 1998-2000  Phi Beta Kappa  Student abstract/presentation award at 1999 ISEA/ISEE Annual Conference in Athens, Greece |
| Professional Associations |  |
|  | American Chemical Society (ACS) ( International Society of Exposure Analysis (ISEA) ( Air & Waste Management Association (AWMA) (Boston Risk Analysis Group |
| Projects |  |
| project # | State of Maine: Assisted in the development of a trial guideline for protecting residents from inhalation exposure to indoor petroleum vapors released from home fuel oil spills. Wrote indoor sampling guidance. |
| project # | Metropolitan District Commission (MDC): Performed mass balance calculations for mercury in Wachusett and Quabbin Reservoirs. Conducted extensive literature review on environmental Hg cycling. Wrote technical report. |
| project # | Private Client: Provided technical analysis of fate and transport of zinc and fluoride emissions in subsurface environment for an aluminum manufacturing facility. Evaluated fluoride toxicity to aquatic organisms and livestock and developed ambient water quality criteria based on U.S. EPA guidelines. |
| project # | Law Firm: Reviewed extensive body of epidemiological studies of ozone health effects and helped develop technical document for litigation support. |
| project # | Private Client: Managed and conducted MCP Method 3 risk characterizations for a chain of Massachusetts gas stations. Contaminants of interest included BTEX and MTBE. Modeled indoor air concentrations and collected indoor VOC samples using Summa canisters to validate model findings. Conducted wetland sampling and performed screening-level ecological risk assessments |
| project # | Private Client: Wrote scope of work, managed, and performed MCP Method 3 human health risk assessment for a former electronics manufacturer with subsurface dissolved-phase chlorinated hydrocarbon contamination. Indoor air modeling performed using vapor intrusion model. Risk to town drinking water wells assessed. |
| project # | Private Client: Developed risk-based soil cleanup levels for BTEX and PAH compounds at a site with pervasive asphalt contamination. Provided technical support during site remedial actions. |
| project # | Massachusetts Bays Program: Assisted in a project designed to quantify point and nonpoint sources of nitrogen to Massachusetts harbors and coastal embayments and to evaluate the potential for eutrophication. Delineated watersheds and subwatersheds using topographic maps. |
| project # | ASTM Committee E-50: Authored sections on chemical properties and contaminant behavior in ASTM Standard Provisional Guide for Risk-Based Corrective Action (PS 104-98). |
| project # | Private Client: Performed U.S. EPA screening-level ecological risk assessments for two former submarine manufacturing facilities. Extensive list of contaminants of concern including metals, PAHs, and PCBs. |
| Publications |  |
|  | Long, C.M. and J.A. Sarnat. 2003. Assessing Indoor-Outdoor Relationships and Infiltration Behavior of Elemental Components of Ambient PM2.5. Manuscript submitted to Aerosol Science & Technology. |
|  | Sarnat, J.A., C.M. Long, P. Koutrakis, B.A. Coull, J. Schwartz, and H.H. Suh. 2002. Using Sulfur as a Tracer of Outdoor Fine Particulate Matter. Environ. Sci. Technol. 36: 5305-5314. |
|  | Long, C.M., H.H. Suh, L Kobzik, P.J. Catalano, Y. Ning, and P. Koutrakis. 2001. A Pilot Investigation of the Relative Toxicity of Indoor and Outdoor Fine Particles: In-vitro Effects of Endotoxin and Other Particulate Properties. Environ. Health Perspect. 109: 1019-1026. |
|  | Long, C.M., H.H. Suh, and P. Koutrakis. 2001. Using Time- and Size-Resolved Particulate Data to Quantify Penetration and Deposition Behavior. Environ. Sci. Technol. 25: 2089-2099. |
|  | Gustafsson, Ö, C.M. Long, J. MacFarlane, and P.M. Gschwend. 2001. Fate of Linear Alkylbenzenes (LABs) Released to the Coastal Environment near Boston Harbor. Environ. Sci. Technol. 25: 2040-2048. |
|  | Long, C.M., H.H. Suh, and P. Koutrakis. 2000. Characterization of indoor particle sources using continuous mass and size monitors. J. Air & Waste Manage. Assoc. 50: 1236-1250. |
|  | Menzie, C.A., J.S. Freshman, and C.M. Long. 1997. Developing Environmentally Acceptable Endpoints for Soil Based on Ecological Considerations. In Proceedings for the Air & Waste Management Association's 90th Annual Meeting & Exhibition, Toronto, Ontario, June 8-13. |
| Presentations |  |
|  | Long, C.M. and B.D. Beck. 2002. An Evaluation of Potential Human Exposures to Trace Metals and Radionuclides in Construction and Building Materials Containing Coal Combustion Products. Poster presentation at 2002 International Society of Exposure Assessment (ISEA)/International Society of Environmental Epidemiology (ISEE) Annual Conference, Vancouver, August 11-15, 2002. |
|  | Long, C.M., H.H. Suh, and P. Koutrakis. 2001. Understanding Indoor Exposures to Ambient Particulate Matter: Estimates of Penetration Efficiencies and Deposition Rates for Residential Homes. Poster Platform Presentation at the 2001 Society for Risk Analysis Annual Meeting, Seattle, WA, December 2-5, 2001. |
|  | Sarnat, J.A., C.M. Long, P. Koutrakis, and H.H. Suh. 2001. Evaluating Tracers of Ambient PM2.5. Platform Presentation at the ISEA 2001 Conference, Charleston, SC, November 4-8, 2001. |
|  | Long, C.M., H.H. Suh, and P. Koutrakis. 2000. Using Time- and Size-resolved Particulate Data to Investigate Infiltration and Deposition Behavior. Platform presentation at the ISEA 2000 Conference, Monterey Peninsula, CA, October 24-27. |
|  | Long, C.M., H.H. Suh, and P. Koutrakis. 2000. Using Time- and Size-resolved Particulate Data to Investigate Infiltration and Deposition Behavior. Platform presentation at the AWMA PM2000 Specialty Conference, Charleston, SC, January 24-28. |
|  | Long, C.M., H.H. Suh, and P. Koutrakis. 2000. Characterization of Indoor Particle Sources Using Continuous Mass and Size Monitors. Poster presentation at the AWMA PM2000 Specialty Conference, Charleston, SC, January 24-28. |
|  | Long, C.M., H.H. Suh, and P. Koutrakis. 1999. Characterization of Indoor Particulate Source Strengths Using Continuous Mass and Size Monitors. Platform presentation at 1999 Annual ISEE/ISEA Conference, Athens, Greece, September 5-8. |
|  | Bernays, W.H., D.J. Vorhees, C.M. Long, and P. Eremita. 1997. Trial Guideline for Protecting Residents from Inhalation Exposure to Petroleum Vapors. Poster presentation at 1997 Annual Meeting of the Society for Risk Analysis, Washington, DC, December 7-10. |
| Invited Talks |  |
|  | Long, C.M. and J.A. Sarnat. 2003. Infiltration Behavior of PM2.5 Chemical Components: Implications for Exposure Assessment and Epidemiological Associations. Platform Presentation at the Particulate Matter: Atmospheric Sciences, Exposure and the Fourth Colloquium on PM and Human Health, Pittsburgh, PA, March 31-April 4, 2003. |

Appendix B

MDEQ Analysis (Weidner, 2005)

# Footnotes

After completion of the analysis set forth in this report, the authors received an additional examination of PM2.5 data prepared by the Michigan Department of Environmental Quality (MDEQ), in conjunction with the Southeast Michigan Council of Governments (SEMCOG) (Weidner, 2005).  This additional MDEQ study analyzed PM2.5 data in the context of wind direction at five monitoring locations, including Dearborn and Oak Park, and relevant graphics from this MDEQ analysis are attached as Appendix B to this report.  Although the MDEQ findings have not been independently verified by the authors, the data presented in Appendix B strongly support the conclusions in this report.

http://www.epa.gov/ttn/airs/airsaqs/detaildata/downloadaqsdata.htm

Refer to Appendix A of our original March 7, 2005 report for a description of the calculations of 24-hour resultant wind speeds and directions.

http://www.epa.gov/ttn/scram/

As before, "from the north" includes winds blowing from both the northwest and northeast quadrants.

Despite the "contribution" of the three Ohio counties to the USEPA's designated Southeast Michigan non-attainment area (shown in Table 1), USEPA has designated Lucas, Wood, and Fulton Counties in Ohio as attainment for  PM2.5.