Table of Contents:

1. Entities

IfcActuator

IfcAirFilter

IfcAirTerminal

IfcAirTerminalBox

IfcBoiler

IfcChiller

IfcCoil

IfcCompressor

IfcControlElement

IfcController

IfcCoolingTower

IfcDamper

IfcDiscreteElement

IfcDistributionFlowElement

IfcFan

IfcFlowController

IfcFlowFitting

IfcFlowSegment

IfcFluidFlowProperties

IfcFluidMovingDevice

IfcHydronicHeater

IfcHygroscopicMaterialProperties

IfcOpticalMaterialProperties

IfcPump

IfcSanitaryTerminal

IfcSensor

IfcSpaceThermalLoad

IfcTank

IfcThermalMaterialProperties

IfcTreatmentDevice

IfcTubeBundle

IfcUnitHeater

IfcValve

2. PropertySets

Pset_AggregateLoadInformation

Pset_AirHandler

Pset_AirSideSystemInformation

Pset_BackdraftDamper

Pset_ControlDamper

Pset_DuctDesignCriteria

Pset_DuctFitting

Pset_DuctSegment

Pset_DuctSystemDesignCriteria

Pset_ElectricActuator

Pset_FireDamper

Pset_FireSmokeDamper

Pset_GlazingType

Pset_GutterSegment

Pset_HandOperatedActuator
Pset_HardwareGroup

Pset_HvacSensor

Pset_HydraulicActuator

Pset_Insulation

Pset_LinearActuator

Pset_LoadDesignCriteria

Pset_Louver

Pset_ManufactureOccurrence

Pset_OpeningShadingType

Pset_OutsideDesignCriteria

Pset_PipeFitting

Pset_PipeSegment

Pset_PipeSystemDesignCriteria

Pset_SiteWeatherData

Pset_SmokeDamper

Pset_SoundPowerLevels

Pset_SoundPressureLevels

Pset_SpaceHvacInformation

IfcActuator

Definition from IAI: This class defines properties of an actuating device typically used in a control system such as a building automation control system.

Attribute definitions:

| PredefinedType | : | Predefined generic types are specified in an Enumeration. A TypeDefinition is available for each generic type (as the required attributes differ). Use Type Definition corresponding to this generic type. Type Definitions Type driven PropertySets PreDefined Type Associated PropertySet ElectricActuator Pset_ElectricActuator PneumaticActuator Pset_PneumaticActuator HydraulicActuator Pset_HydraulicActuator HandOperatedActuator Pset_HandOperatedActuator UserDefined NotDefined |
| --- | --- | --- |
| FailPosition | : | Enumeration defining the types of fail positions for the actuator. |

IfcAirFilter

Definition from IAI: An IfcAirFilter is an apparatus used to remove particulate or gaseous matter from air. It is typically used in conjunction with another device, such as an AirHandler or PackagedACUnit.

Attribute definitions:

| DirtyPressureDrop | : | Pressure drop at the maximum air flowrate across the filter when the filter needs replacement per ASHRAE Standard 52.1. |
| --- | --- | --- |
| CleanPressureDrop | : | Pressure drop at the maximum air flowrate across the filter when the filter is new per ASHRAE Standard 52.1. |
| Efficiency | : | Efficiency value. |

IfcAirTerminal

Definition from IAI: An IfcAirTerminal is a terminating or origination point for the transfer of air between distribution system(s) and one or more space. Air terminals can be any one of the following:

- Diffuser - An outlet discharging supply air in various directions and planes.

- Grille - A covering for any area through which air passes.

- Register - A grille typically equipped with a damper or control valve.

- Supply opening or Outlet - Any opening through which air is being delivered into a ventilated or conditioned space. or control valve.

Attribute definitions:

| AirFlowType | : | Enumeration of possible AirTerminal types (e.g., Supply, Return, Exhaust, etc.). |
| --- | --- | --- |
| Throw | : | The horizontal or vertical axial distance an airstream travels after leaving an AirTerminal before the maximum stream velocity is reduced to a specified terminal velocity. |
| AirDiffusionPerformanceIndex | : | The Air Diffusion Performance Index (ADPI) is used for cooling mode conditions. If several measurements of air velocity and air temperature are made throughout the occupied zone of a space, the ADPI is the percentage of locations where measurements were taken that meet the specifications for effective draft temperature and air velocity. |
| FinishType | : | The type of finish for the AirTerminal. |
| FinishColor | : | The finish color for the air terminal. |
| MountingType | : | The way the AirTerminal is mounted to the ceiling, wall, etc. |
| FaceType | : | Identifies how the terminal face of an AirTerminal is constructed. |
| CoreType | : | Identifies the way the core of the AirTerminal is constructed. |
| CoreSetVertical | : | Degree of blade set from the centerline. |
| CoreSetHorizontal | : | Degree of blade set from the centerline. |
| IntegralControl | : | If TRUE, a self powered temperature control is included in the AirTerminal. |

IfcAirTerminalBox

Definition from IAI: This class defines properties of an air terminal box, which participates in an HVAC duct distribution system. An air terminal box is typically used to control or modulate the amount of air delivered to its downstream ductwork.

| TerminalBoxType | : | Enumeration that identifies the type of terminal box (e.g., VariableAirVolume, ConstantVolume, VariableAirVolumeReheat, ConstantVolumeReheat, FanPowered, VariableAirVolumeDualDuct, etc.) |
| --- | --- | --- |
| SoundLevel | : | Design sound power level defined in decibels with a reference quantity of picowatts. |

IfcBoiler

Definition from IAI: An IfcBoiler is a device which converts stored energy to heat which is added to a fluid; typically used to heat water.

Attribute definitions:

| BoilerType | : | Defines boiler types by heat transfer medium. |
| --- | --- | --- |
| HeatOutput | : | Total nominal heat output as listed by the Boiler manufacturer. |
| PressureRating | : | Nominal pressure rating of the boiler as rated by ASME Boiler and Pressure Vessel Code Section IV, Rules for Construction of Heating Boilers, and Section I, Rules for Construction of Power Boilers. |
| EnergyInputRate | : | Nominal fuel consumption rate required to produce the total boiler heat output. |

IfcChiller

Definition from IAI: An IfcChiller is a device used to implement a refrigeration cycle for cooling a fluid.

| ChillerType | : | Defines the typical types of chillers (e.g., air-cooled, water-cooled, etc.). |
| --- | --- | --- |
| NominalCoolingCapacity_ | : | Nominal cooling capacity of chiller at standardized conditions per ARI Standards 550-92, Centrifugal and Rotary Screw Water-Chilling Packages, and ARI Standards 590-92, Positive Displacement Compressor. |

IfcCoil

Definition from IAI: An IfcCoil is a device used to provide heat transfer between non-mixing media. This is typically used in conjunction with an AirHandler or PackagedACUnit and often will use a TubeBundle.

| CoilType | : | Defines typical types of coils (e.g., Cooling, Heating, etc.) |
| --- | --- | --- |
| BypassFactor | : | Coil bypass factor |
| FaceVelocity | : | Air velocity through the coil. |
| FlowArrangement | : | Coil flow arrangement. |

IfcCompressor

Definition from IAI: An IfcCompressor is a device that compresses a fluid typically used in a refrigeration circuit.

Attribute definitions:

| CompressorType | : | Defines the type of compressor (e.g., hermetic, reciprocating, etc.). |
| --- | --- | --- |
| HotGasBypass | : | Whether or not hot gas bypass is provided for the compressor. TRUE = Yes, FALSE = No. |

IfcControlElement

Definition from IAI: This class defines elements of a building automation control system that are used to impart control over elements of a distribution system.

This class defines elements of a building automation control system. These are typically used to control distribution system elements to maintain temperature, humidity, pressure, flow, power, lighting levels, etc., through the modulation, staging or sequencing of mechanical or electrical devices. The three general functional categories of ControlElements as defined for this release of the IFC model are as follows:

- Impart control over flow control elements (IfcFlowController) in a distribution system such as dampers, valves, relays, etc., typically through the use of actuation (IfcActuator: See IfcHvacDomain schema).

- Sensing elements (IfcSensor: See IfcHvacDomain schema) that measure changes in the controlled variable (e.g., temperature, humidity, pressure, flow, etc.).

- Controllers (IfcController: See IfcHvacDomain schema) typically classified according to the control action they seek to perform and generally responsible for making decisions about the elements under control.

Since this class and its subtypes typically relate to many different distribution flow elements (IfcDistributionFlowElement), the objectified relationship IfcRelFlowControlElements has been provided to relate control and flow elements as required.

Attribute definitions:

| ControlElementId | : | The ControlElement Point Identification assigned to this control element by the Building Automation System. |
| --- | --- | --- |
| AssignedToFlowElement | : | Reference to the relationship object, that related distribution flow elements. |

IfcController

Definition from IAI: This class defines properties of a controller which interacts with other devices in a control system such as a building automation control system.

An IfcController typically has a relationship with an IfcSensor and/or an IfcActuator. These relationships can be handled either through aggregation (e.g., a unitized controller/actuator assembly) using the IfcRelAssemblesElements objectified relationship or simply as an arbitrary grouping of related devices using the IfcRelGroups objectified relationship.

IfcCoolingTower

Definition from IAI: An IfcCoolingTower is a device which rejects heat to ambient air.

Attribute definitions:

| CoolingTowerType | : | Defines the typical types of cooling towers (e.g., OpenTower, ClosedTower, CrossFlow, etc.). |
| --- | --- | --- |
| AmbientDesignTemperature | : | Ambient design temperature used for selecting the cooling tower; for air the list consists of dry bulb temperature followed by wet bulb temperature. |

IfcDamper

Definition from IAI: This class defines elements of a damper, which typically is used in an HVAC air distribution system to control or modulate the flow of air.

An IfcActuator can be either aggregated into the definition of the IfcDamper using the IfcRelAssemblesElements relationship, or referenced using the IfcRelConnectsElements objectified relationship.

Attribute definitions:

| PredefinedType | : | Predefined generic types are specified in an Enumeration. A TypeDefinition is available for each generic type (as the required attributes differ). Use Type Definition corresponding to this generic type. Type Definitions Type driven PropertySets PreDefined Type Associated PropertySet FireDamper Pset_FireDamper SmokeDamper Pset_SmokeDamper FireSmokeDamper Pset_FireSmokeDamper BackdraftDamper Pset_BackdraftDamper ControlDamper Pset_ControlDamper Louver Pset_Louver UserDefined NotDefined |
| --- | --- | --- |
| FrameDepth | : | The length (or depth) of the damper frame. |
| SizingMethod | : | Enumeration that identifies whether the damper is sized nominally or with exact measurements. |
| CloseOffRating | : | Close off rating. |
| LeakageAirFlowRate | : | Leakage air flow rate: the volume of air that still passes through a fully closed damper. |
| PercentOpen | : | Defines the percentage open position for the damper blades. This value varies for dampers under automatic control, but typically remain fixed for dampers used for balancing purposes. |

IfcDiscreteElement

Definition from IAI: This class defines elements in a building services system that do not participate as either devices or distribution elements, such as insulation or attaching elements. This class will be more fully elaborated in future IFC releases.

HISTORY: New entity in IFC R2.0.

ISSUES: See issues and change log for changes made in IFC R2x.

Geometry Use Definitions

The geometric representation of IfcDiscreteElement is given by the IfcProductDefinitionShape, allowing multiple geometric representations. Included are:

B-Rep Representation

The faceted B-Rep capabilities (with or without voids) shall be supported for B-Rep representation.

Attribute definitions:

PredefinedType   :   Predefined generic types are specified in an Enumeration. A TypeDefinition is available for each generic type (as the required attributes differ). Use Type Definition corresponding to this generic type.

Type Definitions

Type driven PropertySets

PreDefined Type Associated PropertySet

Insulation Pset_Insulation

UserDefined

NotDefined

IfcDistributionFlowElement

SUPERTYPE OF (ONEOF(IfcFlowController, IfcFlowFitting, IfcFlowSegment, IfcFlowTerminal, IfcHeatTransferDevice, IfcFluidMovingDevice, IfcTreatmentDevice, IfcStorageDevice))

SUBTYPE OF (IfcDistributionElement);

Definition from IAI: This class defines elements of a distribution system that facilitate the distribution of energy or matter, such as air, water or power.

IfcFan

Definition from IAI: An IfcFan is a device which imparts mechanical work on a gas.

Attribute definitions:

| AirFlowType | : | Enumeration of possible Fan AirFlow types (e.g., Supply, Return, Exhaust, etc.). |
| --- | --- | --- |
| StaticPressure | : | The static pressure within the air stream that the fan must overcome to insure designed circulation of air. |
| FanPressureClass | : | Defines the Pressure Class of the fan used for identifying the thickness and types of materials required for the construction of the fan assembly. |
| FanWheelType | : | Defines the type of wheel typically utilized in fans. |
| WheelMaterial | : | The material used to construct the fan wheel. |
| WheelTipSpeed | : | The linear speed of the tip of the fan blade furthest from the shaft. |
| DischargeVelocity | : | The speed at which air discharges from the fan through the fan housing discharge opening. |
| HousingMaterial | : | The material used to construct the fan housing. |
| DischargePressureLoss | : | Fan discharge pressure losses associated with the discharge arrangement. |
| FanDischargeType | : | Defines the type of discharge arrangement from the fan housing discharge opening, which is used to determine the DischargePressureLoss |
| FanArrangement | : | Defines the type of fan arrangement for centrifugal fans. |
| FanRotation | : | Defines the types of fan rotation for centrifugal fans. |
| FanDriveArrangement | : | Defines the fan and motor drive arrangement as defined by AMCA. |
| DrivePowerLoss_ | : | Fan drive power losses associated with the type of connection between the motor and the fan wheel. |
| MotorDriveType | : | Defines the type of connection between the motor and the fan wheel. |
| MotorInAirstream_ | : | Boolean value to identify if the fan motor is in the conditioned airstream. TRUE = Yes, FALSE = No. |
| FanMountingType | : | Defines the method of mounting the fan in the building. |

IfcFlowController

Definition from IAI: This class defines elements of a distribution system that are used to regulate flow through a distribution system (e.g., damper, valve, switch, relay, etc.).

SUBTYPE OF (  IfcDistributionFlowElement);

IfcFlowFitting

Definition from IAI: A junction or transition in a flow distribution system (e.g., elbow, tee, etc.).

SUBTYPE OF (  IfcDistributionFlowElement);

IfcFlowSegment

Definition from IAI: A segment of a flow distribution system that is typically straight, contiguous and has two ports (e.g., a section of pipe or duct).

SUBTYPE OF (  IfcDistributionFlowElement);

Attribute definitions:

| PredefinedType | : | Predefined generic types are specified in an Enumeration. A TypeDefinition is available for each generic type (as the required attributes differ). Use Type Definition corresponding to this generic type. Type Definitions Type driven PropertySets PreDefined Type Associated PropertySet DuctSegment Pset_DuctSegment PipeSegment Pset_PipeSegment GutterSegment Pset_GutterSegment UserDefined NotDefined |
| --- | --- | --- |

IfcFluidFlowProperties

Attribute definitions:

| MaximumFlowRate | : | Maximum possible flowrate through all inlets. |
| --- | --- | --- |
| DesignFlowrate | : | Design or intended flowrate through all inlets. |
| MinimumFlowrate | : | Minimum flowrate through all the inlets. |
| PressureLoss | : | Pressure loss at the DesignFlowrate. |
| WorkingPressure | : | The working pressure, or pressure that is exerted on the inlets. |
| PressureRating | : | The design pressure rating, or maximum pressure that this device can be subjected to. |
| Fluid | : | The properties of the fluid. |
| DesignVelocity | : | Velocity of the fluid at the DesignFlowrate. |
| DesignTemperature | : | List of design temperature of the fluid; for air the list consists of dry bulb temperature followed by wet bulb temperature. |
| MaximumTemperature | : | Maximum temperature of the fluid; for air the list consists of dry bulb temperature followed by wet bulb temperature. |
| MinimumTemperature | : | Minimum temperature of the fluid; for air the list consists of dry bulb temperature followed by wet bulb temperature. |
| WorkingTemperature | : | Working or actual temperature of the fluid; for air the list consists of dry bulb temperature followed by wet bulb temperature. |
| WorkingQuality | : | Defines ratio of vapor to liquid. |

IfcFluidMovingDevice

SUPERTYPE OF (ONEOF(IfcCompressor, IfcFan, IfcPump))

Definition from IAI: IfcFluidMovingDevice is an apparatus used distribute, circulate or perform conveyance of fluids, including liquids and gases, and typically participates in a flow distribution system (e.g., pump, fan).

IfcFluidMovingDevice is a container entity that aggregates all components of the device it represents. The aggregation is handled via the IfcRelAssemblesElements relationship.

IfcHydronicHeater

SUBTYPE OF (IfcFlowTerminal);

Definition from IAI: An IfcHydronicHeater is a device which adds heat to a space utilizing a combination of radiation and natural convection. The heat source is typically steam or hot water. Examples of HydronicHeaters include radiators, convectors, baseboard and finned-tube heaters, etc. The physical dimensions and properties of the heating element can be defined by an aggregated coil element (IfcCoil).

Attribute definitions:

| HydronicHeaterType | : | Enumeration of possible HydronicHeater types (e.g., baseboard heater, convector, radiator, etc.). |
| --- | --- | --- |
| HeatOutput | : | Total nominal heat output as listed by the manufacturer. |
| Enclosure | : | Description of the the type of enclosure around the HydronicHeater. |
| BodyMass | : | Overall body mass of a HydronicHeater. |
| NumberOfPanels | : | Number of panels (panel radiators only). |
| NumberOfSections | : | Number of vertical sections, measured in the direction of flow. |

IfcHygroscopicMaterialProperties

Definition from IAI:A container class with material hygroscopic properties defined in IFC specification.

Attribute definitions:

| UpperVaporResistanceFactor | : | The vapor permeability relationship of air/material (typically value > 1), measured in high relative humidity (typically in 95/50 % RH). |
| --- | --- | --- |
| LowerVaporResistanceFactor | : | The vapor permeability relationship of air/material (typically value > 1), measured in low relative humidity (typically in 0/50 % RH). |
| IsothermalMoistureCapacity | : | Based on water vapor density, usually measured in [m3/ kg]. |
| VaporPermeability | : | Usually measured in [kg/s m Pa]. |
| MoistureDiffusivity | : | Usually measured in [m3/s]. |

IfcOpticalMaterialProperties

Definition from IAI:A container class with material optical properties defined in IFC specification.

Attribute definitions:

| VisibleTransmittance | : | Transmittance at normal incidence (visible). Defines the fraction of the visible spectrum of solar radiation that passes through per unit area, perpendicular to the surface. |
| --- | --- | --- |
| SolarTransmittance | : | Transmittance at normal incidence (solar). Defines the fraction of solar radiation that passes through per unit area, perpendicular to the surface. |
| ThermalIrTransmittance | : | Thermal IR transmittance at normal incidence. Defines the fraction of thermal energy that passes through per unit area, perpendicular to the surface. |
| ThermalIrEmissivityBack | : | Thermal IR emissivity: back side. Defines the fraction of thermal energy emitted per unit area to "blackbody" at the same temperature, through the "back" side of the material. |
| ThermalIrEmissivityFront | : | Thermal IR emissivity: front side. Defines the fraction of thermal energy emitted per unit area to "blackbody" at the same temperature, through the "front" side of the material. |
| VisibleReflectanceBack | : | Reflectance at normal incidence (visible): back side. Defines the fraction of the solar ray in the visible spectrum that is reflected and not transmitted when the ray passes from one medium into another, at the "back" side of the other material, perpendicular to the surface. Dependent on material and surface characteristics. |
| VisibleReflectanceFront | : | Reflectance at normal incidence (visible): front side. Defines the fraction of the solar ray in the visible spectrum that is reflected and not transmitted when the ray passes from one medium into another, at the "front" side of the other material, perpendicular to the surface. Dependent on material and surface characteristics. |
| SolarReflectanceFront | : | Reflectance at normal incidence (solar): front side. Defines the fraction of the solar ray that is reflected and not transmitted when the ray passes from one medium into another, at the "front" side of the other material, perpendicular to the surface. Dependent on material and surface characteristics. |
| SolarReflectanceBack | : | Reflectance at normal incidence (solar): back side. Defines the fraction of the solar ray that is reflected and not transmitted when the ray passes from one medium into another, at the "back" side of the other material, perpendicular to the surface. Dependent on material and surface characteristics. |

IfcPump

SUBTYPE OF (IfcFluidMovingDevice);

Definition from IAI: An IfcPump is a device which imparts mechanical work on a liquid.

Attribute definitions:

| PumpType | : | Defines the type of centrifugal pump typically used in building services. |
| --- | --- | --- |
| NetPositiveSuctionHead | : | Minimum liquid pressure at pump inlet to prevent cavitation. |
| ImpellerSealMaterial | : | The material used for the impeller shaft seals. |
| PumpBaseType | : | Defines the type of base used for centrifugal pumps. |
| MotorDriveType | : | Defines the type of connection between the motor and the pump impeller. |

IfcSanitaryTerminal

SUBTYPE OF (IfcFlowTerminal);

Definition from IAI: An IfcSanitaryTerminal is an IfcFlowTerminal specialized for use in sanitary plumbing applications (e.g., water closets, sinks, etc.).

Attribute definitions:

| PredefinedType | : | Predefined generic types are specified in an Enumeration. A TypeDefinition is available for each generic type (as the required attributes differ). Use Type Definition corresponding to this generic type. Type Definitions Type driven PropertySets PreDefined Type Associated PropertySet RoofDrain Pset_RoofDrain Scupper Pset_Scupper Faucet Pset_Faucet Sink Pset_Sink Toilet Pset_Toilet Urinal Pset_Urinal Shower Pset_Shower UserDefined NotDefined |
| --- | --- | --- |

IfcSensor

Definition from IAI: This class defines properties of a sensor which is used for detection in a control system such as a building automation control system.

Attribute definitions:

| PredefinedType | : | Predefined generic types are specified in an Enumeration. A TypeDefinition is available for each generic type (as the required attributes differ). Use Type Definition corresponding to this generic type. Type Definitions Type driven PropertySets PreDefined Type Associated PropertySet HvacSensor Pset_HvacSensor UserDefined NotDefined |
| --- | --- | --- |

IfcSpaceThermalLoad

Definition from IAI: The space thermal load (IfcSpaceThermalLoad) defines all thermal losses and gains occurring within a space or zone. Those losses or gains can either be requirements (desired values) or criteria (actual values). The source attribute defines the source of loss or gain, and the maximum value and applicable value ratio are interpreted according to the source (see definition of IfcUseCaseSourceEnum).

The IfcSpaceThermalLoad is a statically defined property set and should be attached to the instance(s) of IfcSpace through the IfcRelAssignsProperties relationship. If there are

several different thermal loads occuring within a space, multiple instances of IfcSpaceThermalLoad should be assigned.

Attribute definitions:

| ApplicableValueRatio | : | Percentage of use requirement or criteria applicable to the space, interpretation depends on the source type. |
| --- | --- | --- |
| ThermalLoadSource | : | Source or type of the use or load characteristic. Depending on the source, the maximum value has to be interpreted. |
| RequirementOrCriteria | : | Indicated whether the source values describe a desired value as requirement (REQUIREMENT) or an actual value as criteria (CRITERIA) for the space. |
| ConstantLoad | : | Indication, whether the use requirement or load is constant during the hours of a day (TRUE) or not (FALSE). If not, a Pset_24HRSchedule has to be referenced by ExtendedProperties. |
| LossOrGain | : | Indicated whether the source causes a loss (LOSS) or gain (GAIN) for the space. |
| SourceDescription | : | Further specification for the source, which might be specific for a region or project. E.g. whether the heat gain from Person is caused by specific activities. |

IfcTank

Definition from IAI: An IfcTank is a device used to hold gasses and liquids; e.g., expansion tank.

Attribute definitions:

| Volume | : | Nominal or design volume of the tank. |
| --- | --- | --- |
| ReliefValveSetting | : | Pressure at which the relief valve activates. |
| ChargePressure | : | Normal operating pressure of the tank. |
| PressureRegulatorSetting | : | Pressure that is automatically maintained in the tank. |

IfcThermalMaterialProperties

Definition from IAI:A container class with material thermal properties defined in IFC specification.

Attribute definitions:

| SpecificHeatCapacity | : | Defines the specific heat of the material: heat energy absorbed per temperature unit. Usually measured in [J/kg K]. |
| --- | --- | --- |
| BoilingPoint | : | The boiling point of the material (fluid). Usually measured in Kelvin. |
| FreezingPoint | : | The freezing point of the material (fluid). Usually measured in Kelvin. |
| ThermalConductivity | : | The rate at which thermal energy is transmitted through the material.Usually in [W/m K]. |

IfcTreatmentDevice

SUBTYPE OF (IfcDistributionFlowElement);

Definition from IAI: IfcTreatmentDevice is a device typically used to remove unwanted matter from a fluid, either liquid or gas, and typically participates in a flow distribution system (e.g., air filter).

IfcTubeBundle

Definition from IAI: An IfcTubeBundle is a device consisting of tubes and bundles of tubes used for heat transfer and contained typically within other devices (e.g., IfcChiller, IfcCoil, etc.).

An IfcTubeBundle will typically aggregate instances of IfcFluidFlowProperties to capture the flowrate and pressure conditions of the fluids within the tubes and within the shell. For TubeBundles that use electricity rather than fluids, aggregate an instance of IfcElectricalBaseProperties instead.

Attribute definitions:

| TubeSize | : | Nominal diameter or width of the tubes in the TubeBundle. |
| --- | --- | --- |
| TubeMaterial | : | Material used for construction of the tubes. |
| TubeLength | : | Length of the tubes in the TubeBundle. |
| TubeSpacing | : | Spacing between tubes in the TubeBundle. |
| TubeFluidEnteringTemperature | : | List of design temperatures of the fluid entering the tubes; for air the list consists of dry bulb temperature followed by wet bulb temperature. |
| TubeFluidLeavingTemperature | : | List of design temperatures of the fluid leaving the tubes; for air the list consists of dry bulb temperature followed by wet bulb temperature. |
| FinMaterial | : | Material used to construct the fins on a tube in the TubeBundle. |
| ShellMaterial | : | Material used to construct the shell of the TubeBundle. |
| FinSpacing | : | Distance between fins on a tube in the TubeBundle. |
| TubeFoulingFactor | : | Fouling factor of the tubes in the TubeBundle. |
| NumberOfTubeCircuits | : | Number of parallel fluid tube circuits. |
| NumberOfTubeRows | : | Number of tube rows in the TubeBundle assembly. |
| ShellFluidLeavingTemperature | : | List of design temperatures of the fluid leaving the shell or TubeBundle assembly; for air the list consists of dry bulb temperature followed by wet bulb temperature. |
| ShellFluidEnteringTemperature | : | List of design temperatures of the fluid entering the shell or TubeBundle assembly; for air the list consists of dry bulb temperature followed by wet bulb temperature. |

IfcUnitHeater

SUBTYPE OF (IfcHeatTransferDevice);

Definition from IAI: An IfcUnitHeater is a device which adds heat to a space.

IfcValve

Definition from IAI: This class defines elements of a valve, which typically is used in an HVAC piping distribution system to control or modulate the flow of the fluid.

Attribute definitions:

| CloseOffRating | : | Close off rating. |
| --- | --- | --- |
| ValveFlowCoefficient | : | Flow coefficient (the quantity of fluid that passes through a fully open valve at unit pressure drop), typically expressed as the Kv or Cv value for the valve. |
| ValveType | : | Type of valve. |

Pset_AggregateLoadInformation

| PropertySet Name | Pset_AggregateLoadInformation |
| --- | --- |
| Typed | False |
| TypedClass |  |
| TypeName |  |
| Definition | Definition from IAI: The aggregated thermal loads experienced by one or many spaces or zones. This aggregate load information is typically addressed by a system or plant. HISTORY: New property set in IFC Release 1.0. ISSUES: No issues to date. |

Property Definitions:

| Name | Property Type | Data Type | Definition |
| --- | --- | --- | --- |
| TotalCoolingLoad | IfcPropertySingleValue | IfcPowerMeasure / PowerUnit | The peak total cooling load for the building. |
| TotalHeatingLoad | IfcPropertySingleValue | IfcPowerMeasure / PowerUnit | The peak total heating load for the building. |
| LightingDiversity | IfcPropertySingleValue | IfcPositiveRatioMeasure | Lighting diversity. |
| InfiltrationDiversitySummer | IfcPropertySingleValue | IfcPositiveRatioMeasure | Diversity factor for Summer infiltration. |
| InfiltrationDiversityWinter | IfcPropertySingleValue | IfcPositiveRatioMeasure | Diversity factor for Winter infiltration. |
| ApplianceDiversity | IfcPropertySingleValue | IfcPositiveRatioMeasure | Diversity of applicance load. |
| LoadSafetyFactor | IfcPropertySingleValue | IfcPositiveRatioMeasure | Load safety factor. |

Pset_AirHandler

| PropertySet Name | Pset_AirHandler |
| --- | --- |
| Typed | False |
| TypedClass |  |
| TypeName |  |
| Definition | Definition from IAI: Equipment which modifies the psychrometric properties of a controlled air stream. It typically consists of an arrangement of Fans, Coils and AirFilters. HISTORY: New property set in IFC Release 1.0. ISSUES: No issues to date. |

Property Definitions:

| Name | Property Type | Data Type | Definition |
| --- | --- | --- | --- |
| AirHandlerConstructionEnum | IfcPropertyEnumeratedValue | Pset_AirHandlerConstructionEnum ManufacturedItem ConstructedOnSite Other NotKnown Unset | Enumeration defining how the air handler might be fabricated. |
| AirHandlerFanCoilArrangementEnum | IfcPropertyEnumeratedValue | Pset_AirHandlerFanCoilArrangementEnum BlowThrough DrawThrough Other NotKnown Unset | Enumeration defining the arrangement of the supply air fan and the cooling coil. |
| DualDeck | IfcPropertySingleValue | IfcBoolean | Does the AirHandler have a dual deck? TRUE = Yes, FALSE = No. |

Pset_AirSideSystemInformation

| PropertySet Name | Pset_AirSideSystemInformation |
| --- | --- |
| Typed | False |
| TypedClass |  |
| TypeName |  |
| Definition | Definition from IAI: Attributes that apply to an air side HVAC system. HISTORY: New property set in IFC Release 1.0. ISSUES: No issues to date. |

Property Definitions:

| Name | Property Type | Data Type | Definition |
| --- | --- | --- | --- |
| Name | IfcPropertySingleValue | IfcString | The name of the air side system |
| Description | IfcPropertySingleValue | IfcString | The description of the air side system |
| AirSideSystemTypeEnum | IfcPropertyEnumeratedValue | Pset_AirSideSystemTypeEnum ConstantVolume ConstantVolumeSingleZone ConstantVolumeMultipleZoneReheat ConstantVolumeBypass VariableAirVolume VariableAirVolumeReheat VariableAirVolumeInduction VariableAirVolumeFanPowered VariableAirVolumeDualConduit VariableAirVolumeVariableDiffusers VariableAirVolumeVariableTemperature Other NotKnown Unset | This enumeration specifies the basic types of possible air side systems (e.g., Constant Volume, Variable Volume, etc.) |
| AirSideSystemDistributionTypeEnum | IfcPropertyEnumeratedValue | Pset_AirSideSystemDistributionTypeEnum SingleDuct DualDuct Multizone Other NotKnown Unset | This enumeration defines the basic types of air side systems (e.g., SingleDuct, DualDuct, Multizone, etc.) |
| TotalAirflow | IfcPropertySingleValue | IfcVolumetricFlowRateMeasure / VolumetricFlowrateUnit | The total design supply air flowrate required for the system for either heating or cooling conditions, whichever is greater. |
| EnergyGainTotal | IfcPropertySingleValue | IfcPowerMeasure / PowerUnit | The total amount of energy gains for the spaces served by the system during the peak cooling conditions, plus any system-level total energy gains. |
| AirflowSensible | IfcPropertySingleValue | IfcVolumetricFlowRateMeasure / VolumetricFlowrateUnit | The air flowrate required to satisfy the sensible peak loads. |
| EnergyGainSensible | IfcPropertySingleValue | IfcPowerMeasure / PowerUnit | The sum of total energy gains for the spaces served by the system during the peak cooling conditions, plus any system-level sensible energy gains. |
| CoolingCoilEnteringDryBulb | IfcPropertySingleValue | IfcThermodynamicTemperatureMeasure | The system cooling coil entering dry bulb temperature at the peak |
| CoolingCoilEnteringWetBulb | IfcPropertySingleValue | IfcThermodynamicTemperatureMeasure | The system cooling coil entering wet bulb temperature at the peak |
| CoolingCoilLeavingDryBulb | IfcPropertySingleValue | IfcThermodynamicTemperatureMeasure | The system cooling coil entering dry bulb temperature at the peak |
| CoolingCoilLeavingWetBulb | IfcPropertySingleValue | IfcThermodynamicTemperatureMeasure | The system cooling coil entering wet bulb temperature at the peak |
| EnergyLoss | IfcPropertySingleValue | IfcPowerMeasure / PowerUnit | The sum of energy losses for the spaces served by the system during the peak heating conditions. |
| LightingDiversity | IfcPropertySingleValue | IfcPositiveRatioMeasure | Lighting diversity. |
| InfiltrationDiversitySummer | IfcPropertySingleValue | IfcPositiveRatioMeasure | Diversity factor for Summer infiltration. |
| InfiltrationDiversityWinter | IfcPropertySingleValue | IfcPositiveRatioMeasure | Diversity factor for Winter infiltration. |
| ApplianceDiversity | IfcPropertySingleValue | IfcPositiveRatioMeasure | Diversity of applicance load. |
| LoadSafetyFactor | IfcPropertySingleValue | IfcPositiveRatioMeasure | Load safety factor. |
| HeatingTemperatureDelta | IfcPropertySingleValue | IfcThermodynamicTemperatureMeasure | Heating temperature difference for calculating space air flow rates |
| CoolingTemperatureDelta | IfcPropertySingleValue | IfcThermodynamicTemperatureMeasure | Cooling temperature difference for calculating space air flow rates |
| Ventilation | IfcPropertySingleValue | IfcVolumetricFlowRateMeasure / VolumetricFlowrateUnit | Required outside air ventilation. |
| FanPower | IfcPropertySingleValue | IfcPowerMeasure / PowerUnit | Fan motor loads contributing to the cooling load. |

Pset_BackdraftDamper

| PropertySet Name | Pset_BackdraftDamper |
| --- | --- |
| Typed | True |
| TypedClass | IfcDamper |
| TypeName | BackdraftDamper |
| Definition | Definition from IAI: This property set is used to define the characteristics of a backdraft damper. HISTORY: New property set in IFC Release 2.0. ISSUES: No issues to date. |

Property Definitions:

| Name | Property Type | Data Type | Definition |
| --- | --- | --- | --- |
| FrameType | IfcPropertySingleValue | IfcString | The type of frame used by the damper (e.g., Standard, Single Flange, Single Reversed Flange, Double Flange, etc.) |

Pset_ControlDamper

| PropertySet Name | Pset_ControlDamper |
| --- | --- |
| Typed | True |
| TypedClass | IfcDamper |
| TypeName | ControlDamper |
| Definition | Definition from IAI: This property set is used to define the characteristics of a control damper. HISTORY: New property set in IFC Release 2.0. ISSUES: No issues to date. |

Property Definitions:

| Name | Property Type | Data Type | Definition |
| --- | --- | --- | --- |
| DesignAirVelocity | IfcPropertySingleValue | IfcReal / LinearVelocityUnit | The design air velocity for the damper assembly |
| BladeActionEnum | IfcPropertyEnumeratedValue | Pset_DamperBladeActionEnum Parallel Opposed Other NotKnown Unset | Enumeration that identifies the blade closing action for the damper |
| BladeType | IfcPropertySingleValue | IfcString | The type of blade used in the damper (e.g., Triple Vee, Fabricated Airfoil, Extruded Airfoil, etc.) |
| BladeMaterial | IfcPropertyReferenceValue | IfcMaterial | The primary material used to construct the damper blade |
| BladeThickness | IfcPropertySingleValue | IfcLengthMeasure | The thickness of the damper blade |
| FrameType | IfcPropertySingleValue | IfcString | The type of frame used by the damper (e.g., Standard, Single Flange, Single Reversed Flange, Double Flange, etc.) |
| FrameMaterial | IfcPropertyReferenceValue | IfcMaterial | The primary material used to construct the damper frame |
| FrameThickness | IfcPropertySingleValue | IfcLengthMeasure | The thickness of the damper frame |

Pset_DuctDesignCriteria

| PropertySet Name | Pset_DuctDesignCriteria |
| --- | --- |
| Typed | False |
| TypedClass |  |
| TypeName |  |
| Definition | Definition from IAI: This property set is used to define the general characteristics of the duct design parameters. This property set is typically attached to an instance of an IfcSystem, however, it may also be attached to individual elements within a duct distribution system where individual design parameters overrule those of the system. HISTORY: New property set in IFC Release 2.0. ISSUES: No issues to date. |

Property Definitions:

| Name | Property Type | Data Type | Definition |
| --- | --- | --- | --- |
| DesignName | IfcPropertySingleValue | IfcString | A name for the design values |
| DuctSizingMethodEnum | IfcPropertyEnumeratedValue | Pset_DuctSizingMethodEnum ConstantFriction ConstantPressure StaticRegain Other NotKnown Unset | Enumeration that identifies the methodology to be used to size system components |
| PressureClass | IfcPropertySingleValue | IfcPressureMeasure / PressureUnit | Nominal pressure rating of the system components. (Data type = PressureMeasure) |
| LeakageClass | IfcPropertySingleValue | IfcPressureMeasure / PressureUnit | Nominal leakage rating for the system components. |
| FrictionLoss | IfcPropertySingleValue | IfcReal / UserDefined | The pressure loss due to friction per unit length. (Data type = PressureMeasure/LengthMeasure) |
| ScrapFactor | IfcPropertySingleValue | IfcReal | Sheet metal scrap factor |
| DuctSealant | IfcPropertySingleValue | IfcString | Type of sealant used on the duct and fittings |
| MaximumVelocity | IfcPropertySingleValue | IfcLinearVelocityMeasure / LinearVelocityUnit | The maximum design velocity of the air in the duct or fitting. |
| AspectRatio | IfcPropertySingleValue | IfcReal | The default aspect ratio |
| MinimumHeight | IfcPropertySingleValue | IfcLengthMeasure | The minimum duct height for rectangular, oval or round duct |
| MinimumWidth | IfcPropertySingleValue | IfcLengthMeasure | The minimum duct width for oval or rectangular duct |

Pset_DuctFitting

| PropertySet Name | Pset_DuctFitting |
| --- | --- |
| Typed | True |
| TypedClass | IfcFlowFitting |
| TypeName | DuctFitting |
| Definition | Definition from IAI: This property set is used to define the characteristics of a duct fitting. Related property sets include Pset_DuctDesignCriteria. HISTORY: New property set in IFC Release 2.0. ISSUES: No issues to date. |

Property Definitions:

| Name | Property Type | Data Type | Definition |
| --- | --- | --- | --- |
| FittingSubType | IfcPropertySingleValue | IfcString | Subtype of fitting (I.e., 5-gore, pleated, stamped, etc.) |

Pset_DuctSegment

| PropertySet Name | Pset_DuctSegment |
| --- | --- |
| Typed | True |
| TypedClass | IfcFlowSegment |
| TypeName | DuctSegment |
| Definition | Definition from IAI: This property set is used to define the characteristics of a duct segment. Related property sets include Pset_DuctDesignCriteria. HISTORY: New property set in IFC Release 2.0. ISSUES: No issues to date. |

Property Definitions:

| Name | Property Type | Data Type | Definition |
| --- | --- | --- | --- |
| FinishedLength | IfcPropertySingleValue | IfcLengthMeasure | The finished length of the duct segment |
| LongitudinalSeam | IfcPropertySingleValue | IfcString | The type of seam to be used along the longitudinal axis of the duct segment |
| Reinforcement | IfcPropertySingleValue | IfcString | The type of reinforcement used for the duct segment |
| ReinforcementSpacing | IfcPropertySingleValue | IfcLengthMeasure | The spacing between reinforcing elements |

Pset_DuctSystemDesignCriteria

| PropertySet Name | Pset_DuctSystemDesignCriteria |
| --- | --- |
| Typed | False |
| TypedClass |  |
| TypeName |  |
| Definition | Definition from IAI: This property set is used to define the general characteristics of the duct system and is typically attached to an instance of an IfcSystem. HISTORY: New property set in IFC Release 2.0. ISSUES: No issues to date. |

Property Definitions:

| Name | Property Type | Data Type | Definition |
| --- | --- | --- | --- |
| DuctSystemTypeEnum | IfcPropertyEnumeratedValue | Pset_DuctSystemTypeEnum VariableAirVolume ConstantVolume DoubleDuct Other NotKnown Unset | Enumeration that identifies the type of system |
| SystemDescription | IfcPropertySingleValue | IfcString | System description |
| SystemLocation | IfcPropertySingleValue | IfcString | Physical description of the part of the building the system serves |

Pset_ElectricActuator

| PropertySet Name | Pset_ElectricActuator |
| --- | --- |
| Typed | True |
| TypedClass | IfcActuator |
| TypeName | ElectricActuator |
| Definition | Definition from IAI: This property set is used to define the characteristics of an electric actuator. HISTORY: New property set in IFC Release 2.0. ISSUES: No issues to date. |

Property Definitions:

| Name | Property Type | Data Type | Definition |
| --- | --- | --- | --- |
| ManualOverride | IfcPropertySingleValue | IfcBoolean | Identifies whether hand-operated operation is provided as an override |
| InputPower | IfcPropertySingleValue | IfcPowerMeasure / PowerUnit | Maximum input power requirement |
| ElectricActuatorType | IfcPropertyEnumeratedValue | Pset_ElectricActuatorTypeEnum MotorDrive Magnetic Other NotKnown Unset | Enumeration that identifies electric actuator as defined by its operational principle. |

Pset_FireDamper

| PropertySet Name | Pset_FireDamper |
| --- | --- |
| Typed | True |
| TypedClass | IfcDamper |
| TypeName | FireDamper |
| Definition | Definition from IAI: This property set is used to define the characteristics of a fire damper. HISTORY: New property set in IFC Release 2.0. ISSUES: No issues to date. |

Property Definitions:

| Name | Property Type | Data Type | Definition |
| --- | --- | --- | --- |
| BladeTypeEnum | IfcPropertyEnumeratedValue | Pset_FireDamperBladeTypeEnum ParallelBlade FoldingCurtain Other NotKnown Unset | Enumeration that identifies the different types of blades in the fire damper |
| ActuationTypeEnum | IfcPropertyEnumeratedValue | Pset_FireDamperActuationTypeEnum Gravity Spring Other NotKnown Unset | Enumeration that identifies the different types of dampers |
| ClosureRatingEnum | IfcPropertyEnumeratedValue | Pset_FireDamperClosureRatingEnum Dynamic Static Other NotKnown Unset | Enumeration that identifies the closure rating for the damper |
| FireResistanceRating | IfcPropertySingleValue | IfcReal | Measure of the fire resistance rating in hours (e.g., 1.5 hours, 2 hours, etc.). |
| MountingPositionEnum | IfcPropertyEnumeratedValue | Pset_DamperMountingPositionEnum Horizontal Vertical Other NotKnown Unset | Enumeration that identifies how the damper is mounted in the building |
| FusibleLinkTemperature | IfcPropertySingleValue | IfcThermodynamicTemperatureMeasure | The temperature that the fusible link melts |
| SleeveLength | IfcPropertySingleValue | IfcLengthMeasure | The length of the damper sleeve |
| SleeveThickness | IfcPropertySingleValue | IfcLengthMeasure | The thickness of the damper sleeve |
| DamperLocationInSleeve | IfcPropertySingleValue | IfcString | The location within the sleeve where the damper is mounted (e.g., Center) |

Pset_FireSmokeDamper

| PropertySet Name | Pset_FireSmokeDamper |
| --- | --- |
| Typed | True |
| TypedClass | IfcDamper |
| TypeName | FireSmokeDamper |
| Definition | Definition from IAI: This property set is used to define the characteristics of a combination fire and smoke damper. HISTORY: New property set in IFC Release 2.0. ISSUES: No issues to date. |

Property Definitions:

| Name | Property Type | Data Type | Definition |
| --- | --- | --- | --- |
| FrameThickness | IfcPropertySingleValue | IfcLengthMeasure | The thickness of the damper frame |
| FireResistanceRating | IfcPropertySingleValue | IfcReal | Measure of the fire resistance rating in hours (e.g., 1.5 hours, 2 hours, etc.). |
| BladeType | IfcPropertySingleValue | IfcString | The type of blade |
| MountingPositionEnum | IfcPropertyEnumeratedValue | Pset_DamperMountingPositionEnum Horizontal Vertical Other NotKnown Unset | Enumeration that identifies how the damper is mounted in the building |
| FusibleLinkTemperature | IfcPropertySingleValue | IfcThermodynamicTemperatureMeasure | The temperature that the fusible link melts |
| ControlType | IfcPropertySingleValue | IfcString | The type of control used to operate the damper (e.g., Open/Closed Indicator, Resetable Temperature Sensor, Temperature Override, etc.) |
| SleeveLength | IfcPropertySingleValue | IfcLengthMeasure | The length of the damper sleeve |
| SleeveThickness | IfcPropertySingleValue | IfcLengthMeasure | The thickness of the damper sleeve |
| DamperLocationInSleeve | IfcPropertySingleValue | IfcString | The location within the sleeve where the damper is mounted (e.g., Center) |

Pset_GlazingType

| PropertySet Name | Pset_GlazingType |
| --- | --- |
| Typed | False |
| TypedClass |  |
| TypeName |  |
| Definition | Definition from IAI: Properties common to the definition of all glazing as referred to by other property sets. |

Property Definitions:

| Name | Property Type | Data Type | Definition |
| --- | --- | --- | --- |
| NumberOfGlasses | IfcPropertySingleValue | IfcCountMeasure | Number of glass layers within the frame. E.g. "2" for double glazing. |
| Thickness | IfcPropertySingleValue | IfcPositiveLengthMeasure | Thickness of the glass. |
| FillGas | IfcPropertySingleValue | IfcString | Name of the gas by which the gap between two glass layers is filled. |
| Color | IfcPropertySingleValue | IfcString | Color (tint) selection for this glazing. |
| IsTempered | IfcPropertySingleValue | IfcBoolean | Indication whether the glass is tempered (TRUE) or not (FALSE) |
| IsLaminated | IfcPropertySingleValue | IfcBoolean | Indication whether the glass is layered with other materials (TRUE) or not (FALSE). |
| IsCoated | IfcPropertySingleValue | IfcBoolean | Indication whether the glass is coated with a material (TRUE) or not (FALSE). |
| IsWired | IfcPropertySingleValue | IfcBoolean | Indication whether the glass includes a contained wire mesh to prevent break-in (TRUE) or not (FALSE) |
| ImpactResistance | IfcPropertySingleValue | IfcString | Description of the resistance to shatter. Either given by description or by a numeric value of a scale (1..10) accoridng to regional classifications. |
| Translucency | IfcPropertySingleValue | IfcPositiveRatioMeasure | Fraction of the visible light that passes the glazing at normal incidence. It is a value without unit. |
| Reflectivity | IfcPropertySingleValue | IfcPositiveRatioMeasure | Fraction of the visible light that is reflected by the glazing at normal incidence. It is a value without unit. |
| BeamRadiationTransmittance | IfcPropertySingleValue | IfcPositiveRatioMeasure | Direct solar radiation tarnsmittance that passes the glazing at normal incidence. It is a value without unit, often refered to as (Tsol). |
| SolarHeatGain | IfcPropertySingleValue | IfcPositiveRatioMeasure | Total solar heat transmittance that passes the glazing at normal incidence. It is a value without unit, often refered to as (SHGC): |
| ThermalTransmittanceSummerShaded | IfcPropertySingleValue | IfcThermalTransmittanceMeasure / ThermalTransmittanceUnit | Summer shaded thermal transmittance coefficient, often refered to as (U-value) |
| ThermalTransmittanceSummerUnshaded | IfcPropertySingleValue | IfcThermalTransmittanceMeasure / ThermalTransmittanceUnit | Summer unshaded thermal transmittance coefficient, often refered to as (U-value) |
| ThermalTransmittanceWinter | IfcPropertySingleValue | IfcThermalTransmittanceMeasure / ThermalTransmittanceUnit | Winter thermal transmittance coefficient, often refered to as (U-value) |

Pset_GutterSegment

| PropertySet Name | Pset_GutterSegment |
| --- | --- |
| Typed | True |
| TypedClass | IfcFlowSegment |
| TypeName | GutterSegment |
| Definition | Definition from IAI: HISTORY: New property set in IFC Release 2.0. ISSUES: No issues to date. |

Property Definitions:

| Name | Property Type | Data Type | Definition |
| --- | --- | --- | --- |
| Slope | IfcPropertySingleValue | IfcPlaneAngleMeasure | Angle of the gutter to allow for drainage |
| FlowRating | IfcPropertySingleValue | IfcVolumetricFlowRateMeasure / VolumetricFlowrateUnit | Actual flow capacity for the gutter. Value of 0.00 means this value has not been set. |

Pset_HandOperatedActuator

| PropertySet Name | Pset_HandOperatedActuator |
| --- | --- |
| Typed | True |
| TypedClass | IfcActuator |
| TypeName | HandOperatedActuator |
| Definition | Definition from IAI: This property set is used to define the characteristics of a hand-operated actuator. HISTORY: New property set in IFC Release 2.0. ISSUES: No issues to date. |

Property Definitions:

| Name | Property Type | Data Type | Definition |
| --- | --- | --- | --- |
| ManualOverride | IfcPropertySingleValue | IfcBoolean | Identifies whether hand-operated operation is provided as an override |

Pset_HardwareGroup

| PropertySet Name | Pset_HardwareGroup |
| --- | --- |
| Typed | False |
| TypedClass |  |
| TypeName |  |
| Definition | Definition from IAI: Properties common to the definition of all hardware groups as referred to by other property sets. |

Property Definitions:

| Name | Property Type | Data Type | Definition |
| --- | --- | --- | --- |
| Reference | IfcPropertySingleValue | IfcIdentifier | User defined reference for this standard collection of hardware elements within this project. |
| Description | IfcPropertySingleValue | IfcString | Specific description for this type of hardware within this project. |
| Manufacturer | IfcPropertyReferenceValue | IfcOrganization | The organization that manufactured or assembled the item. |
| ModelLabel | IfcPropertySingleValue | IfcString | The model number and/or unit designator assigned by the manufacturer of the manufactured item. |
| ModelDescription | IfcPropertySingleValue | IfcString | A physical description of the manufactured item as provided by the manufacturer of the munufactured item. |
| Finish | IfcPropertySingleValue | IfcString | Finish applied to hardware |

Pset_HvacSensor

| PropertySet Name | Pset_HvacSensor |
| --- | --- |
| Typed | True |
| TypedClass | IfcSensor |
| TypeName | HvacSensor |
| Definition | Definition from IAI: This property set is used to define the general characteristics of a sensor used in an HVAC control system. HISTORY: New property set in IFC Release 2.0. ISSUES: No issues to date. |

Property Definitions:

| Name | Property Type | Data Type | Definition |
| --- | --- | --- | --- |
| SensorTypeEnum | IfcPropertyEnumeratedValue | Pset_SensorTypeEnum Flow Pressure Temperature Gas Concentration Volts Amps Density Viscosity Energy Humidity Other NotKnown Unset | Enumeration that identifies the type of HVAC sensor |
| Accuracy | IfcPropertySingleValue | IfcReal | The accuracy of the sensor |
| TimeConstant | IfcPropertySingleValue | IfcTimeMeasure | The time constant of the sensor . |
| UpperRangeValue | IfcPropertySingleValue | IfcReal | The upper range value. |
| LowerRangeValue | IfcPropertySingleValue | IfcReal | The lower range value. |

Pset_HydraulicActuator

| PropertySet Name | Pset_HydraulicActuator |
| --- | --- |
| Typed | True |
| TypedClass | IfcActuator |
| TypeName | HydraulicActuator |
| Definition | Definition from IAI: This property set is used to define the characteristics of a hydraulic actuator. HISTORY: New property set in IFC Release 2.0. ISSUES: No issues to date. |

Property Definitions:

| Name | Property Type | Data Type | Definition |
| --- | --- | --- | --- |
| ManualOverride | IfcPropertySingleValue | IfcBoolean | Identifies whether hand-operated operation is provided as an override |
| InputPressure | IfcPropertySingleValue | IfcPressureMeasure / PressureUnit | Maximum design pressure for the actuator |
| InputFlowrate | IfcPropertySingleValue | IfcVolumetricFlowRateMeasure / VolumetricFlowrateUnit | Maximum hydraulic flowrate requirement |

Pset_Insulation

| PropertySet Name | Pset_Insulation |
| --- | --- |
| Typed | True |
| TypedClass | IfcDiscreteElement |
| TypeName | Insulation |
| Definition | Definition from IAI: Materials with low heat conductance. HISTORY: New property set in IFC Release 1.0. ISSUES: No issues to date. |

Property Definitions:

| Name | Property Type | Data Type | Definition |
| --- | --- | --- | --- |
| InsulationTypeEnum | IfcPropertyEnumeratedValue | Pset_InsulationTypeEnum InorganicFibrous InorganicCellular OrganicFibrous OrganicCellular Metallic MetallizedOrganicReflectiveMembranes Other NotKnown Unset | This enumeration defines different types of insulation (I.e., InorganicFibrous, InorganicCellular, OrganicFibrous, OrganicCellular, etc.) as defined by ASHRAE 1997 Fundamenatals Section 22.2 Basic Materials. |
| Thickness | IfcPropertySingleValue | IfcPositiveLengthMeasure | Insulation Thickness |
| JacketType | IfcPropertyReferenceValue | IfcMaterial | Jacket material type of the insulation |
| FlamabilityRating | IfcPropertySingleValue | IfcString | Insulation flammability rating |

Pset_LinearActuator

| PropertySet Name | Pset_LinearActuator |
| --- | --- |
| Typed | False |
| TypedClass |  |
| TypeName |  |
| Definition | Definition from IAI: This property set is used to define the characteristics of a linear actuator. HISTORY: New property set in IFC Release 2.0. ISSUES: No issues to date. |

Property Definitions:

| Name | Property Type | Data Type | Definition |
| --- | --- | --- | --- |
| FailDirectionEnum | IfcPropertyEnumeratedValue | Pset_LinearActuatorFailDirectionEnum FailIn FailOut Other NotKnown Unset | Enumeration that identifies the behavior of the actuator in case of power failure |
| Force | IfcPropertySingleValue | IfcForceMeasure / ForceUnit | Indicates the maximum close-off force for the actuator |
| Stroke | IfcPropertySingleValue | IfcLengthMeasure | Indicates the maximum distance the actuator must traverse |

Pset_LoadDesignCriteria

| PropertySet Name | Pset_LoadDesignCriteria |
| --- | --- |
| Typed | False |
| TypedClass |  |
| TypeName |  |
| Definition | Definition from IAI: Building thermal load design data such as occupancy, appliance, and lighting criteria that are used for calculating thermal loads in a space or building. HISTORY: New property set in IFC Release 1.0. ISSUES: No issues to date. |

Property Definitions:

| Name | Property Type | Data Type | Definition |
| --- | --- | --- | --- |
| OccupancyTypeEnum | IfcPropertyEnumeratedValue | Pset_OccupancyTypeEnum Theater Office Hotel Apartment RetailStore DrugStore Bank Restaurant Factory DanceHall BowlingAlley Gymnasium Other NotKnown Unset | This enumeration identifies types of occupancy or space usage (e.g., Theater, Office, Hotel, Apartment, etc.) as defined by Table 3, Chapter 28, of the 1997 ASHRAE Handbook of Fundamentals. |
| AreaPerPerson | IfcPropertySingleValue | IfcAreaMeasure | Design occupancy loading for this type of usage |
| PeopleSensibleLoad | IfcPropertySingleValue | IfcPowerMeasure / PowerUnit | Sensible thermal load contributed per person. |
| PeopleLatentLoad | IfcPropertySingleValue | IfcPowerMeasure / PowerUnit | Latent thermal load contributed per person. |
| PeopleSensibleLoadToRadiant | IfcPropertySingleValue | IfcPositiveRatioMeasure | Percent of sensible thermal load contributed by people to radiant heat. |
| OccupancyDiversity | IfcPropertySingleValue | IfcPositiveRatioMeasure | Diversity factor that may be applied to the number of people in the space. |
| OutsideAirPerPerson | IfcPropertySingleValue | IfcVolumetricFlowRateMeasure / VolumetricFlowrateUnit | Design quantity of outside air to be provided per person in the space. |
| ReceptacleLoadIntensity | IfcPropertySingleValue | IfcReal / UserDefined | Average power use intensity of appliances and other non-HVAC equipment.in the space per unit area.(PowerMeasure/IfcAreaMeasure) |
| AppliancePercentLoadToRadiant | IfcPropertySingleValue | IfcPositiveRatioMeasure | Percent of sensible load to radiant heat. |
| LightingLoadIntensity | IfcPropertySingleValue | IfcReal / UserDefined | Average lighting load intensity in the space per unit area (PowerMeasure/IfcAreaMeasure) |
| LightingPercentLoadToReturnAir | IfcPropertySingleValue | IfcPositiveRatioMeasure | Percent of lighting load to the return air plenum. |

Pset_Louver

| PropertySet Name | Pset_Louver |
| --- | --- |
| Typed | True |
| TypedClass | IfcDamper |
| TypeName | Louver |
| Definition | Definition from IAI: This property set is used to define the characteristics of a louver. HISTORY: New property set in IFC Release 2.0. ISSUES: No issues to date. |

Property Definitions:

| Name | Property Type | Data Type | Definition |
| --- | --- | --- | --- |
| FrameType | IfcPropertySingleValue | IfcString | The type of frame used by the louver (e.g., Standard, Drainable, etc.) |
| FrameThickness | IfcPropertySingleValue | IfcLengthMeasure | The thickness of the louver frame |
| BladeType | IfcPropertySingleValue | IfcString | The type of blade used in the louver (e.g., "J", "K", Cheveron, Sightproof, Drainable, etc.) |
| BladeThickness | IfcPropertySingleValue | IfcLengthMeasure | The thickness of the louver blade |
| ScreenType | IfcPropertySingleValue | IfcString | The type of screen used in the louver (e.g., Birdscreen, Insect Screen, etc.) |

Pset_ManufactureOccurrence

| PropertySet Name | Pset_ManufactureOccurrence |
| --- | --- |
| Typed | True |
| TypedClass |  |
| TypeName |  |
| Definition | Definition from IAI: Properties about the occurrence specific manufacturer information. Can be attached to all IfcElement. |

Property Definitions:

| Name | Property Type | Data Type | Definition |
| --- | --- | --- | --- |
| SerialNumber | IfcPropertySingleValue | IfcString | The serial number assigned to the individual manufactured item |
| AcquisitionDate | IfcPropertyReferenceValue | IfcCalendarDate | The date that the manufactured item was purchased |

Pset_OpeningShadingType

| PropertySet Name | Pset_OpeningShadingType |
| --- | --- |
| Typed | False |
| TypedClass |  |
| TypeName |  |
| Definition | Definition from IAI: Properties common to the definition of all shading types as referred to by other property sets |

Property Definitions:

| Name | Property Type | Data Type | Definition |
| --- | --- | --- | --- |
| ExternalShadingCoefficient | IfcPropertySingleValue | IfcPositiveRatioMeasure | radiation transmission coefficient of the outside shading device. It is a value without unit. The following translations apply: G: Durchlasfaktor Sonnenschutz ausen, JA: GAIBU SHAHEI-KEISU |
| InternalShadingCoefficient | IfcPropertySingleValue | IfcPositiveRatioMeasure | radiation transmission coefficient of the inside shading device, symbol "b-value". It is a value without unit. The following translations apply: G: Durchlasfaktor Sonnenschutz innen, JA: NAIBU SHAHEI-KEISU |
| InsetShadingCoefficient | IfcPropertySingleValue | IfcPositiveRatioMeasure | radiation transmission coefficient of the shading device inside the glazing, symbol "b-value". It is a value without unit. The following translations apply: G: Durchlasfaktor Sonnenschutz innerhalb der Verglasung, JA: KUMIKOMI SHAHEI-KEISU |
| DistanceToLateralShadingLeft | IfcPropertySingleValue | IfcPositiveLengthMeasure | Distance between the lateral shading device and the window or door opening as shown in the figure. |
| DistanceToLateralShadingRight | IfcPropertySingleValue | IfcPositiveLengthMeasure | Distance between the lateral shading device and the window or door opening as shown in the figure. |
| ProjectionOfLateralShading | IfcPropertySingleValue | IfcPositiveLengthMeasure | Projection of the lateral shading device from the facade (outer surface of the building element, in which the door or window is located) |
| DistanceToTopShading | IfcPropertySingleValue | IfcPositiveLengthMeasure | Distance between the shading device on top and the window or door opening as shown in the figure. |
| ProjectionOfTopShading | IfcPropertySingleValue | IfcPositiveLengthMeasure | Projection of the shading device on the top from the facade (outer surface of the building element, in which the door or window is located) |

Pset_OutsideDesignCriteria

| PropertySet Name | Pset_OutsideDesignCriteria |
| --- | --- |
| Typed | False |
| TypedClass |  |
| TypeName |  |
| Definition | Definition from IAI: Outside air conditions used as the basis for calculating thermal loads at peak conditions. HISTORY: New property set in IFC Release 1.0. ISSUES: No issues to date. |

Property Definitions:

| Name | Property Type | Data Type | Definition |
| --- | --- | --- | --- |
| HeatingDryBulb | IfcPropertySingleValue | IfcThermodynamicTemperatureMeasure | Outside dry bulb temperature for heating design |
| HeatingWetBulb | IfcPropertySingleValue | IfcThermodynamicTemperatureMeasure | Outside wet bulb temperature for heating design |
| CoolingDryBulb | IfcPropertySingleValue | IfcThermodynamicTemperatureMeasure | Outside dry bulb temperature for cooling design |
| CoolingWetBulb | IfcPropertySingleValue | IfcThermodynamicTemperatureMeasure | Outside wet bulb temperature for cooling design |

Pset_PipeFitting

| PropertySet Name | Pset_PipeFitting |
| --- | --- |
| Typed | True |
| TypedClass | IfcFlowFitting |
| TypeName | PipeFitting |
| Definition | Definition from IAI: This property set is used to define the characteristics of a pipe fitting. Related property sets include Pset_PipeDesignCriteria. HISTORY: New property set in IFC Release 2.0. ISSUES: No issues to date. |

Property Definitions:

| Name | Property Type | Data Type | Definition |
| --- | --- | --- | --- |
| FittingSubTypeEnum | IfcPropertyEnumeratedValue | Pset_PipeFittingSubtypeEnum 45DegreeElbow 90DegreeElbow Cap Cock Crossover DoubleBranchElbow Flange Lateral PipeJoint Plug Reducer ReducingElbow Sleeve StreetElbow Tee Union Other NotKnown Unset | This enumeration identifies the fitting subtype. |

Pset_PipeSegment

| PropertySet Name | Pset_PipeSegment |
| --- | --- |
| Typed | True |
| TypedClass | IfcFlowSegment |
| TypeName | PipeSegment |
| Definition | Definition from IAI: This property set is used to define the characteristics of a pipe segment. Related property sets include Pset_PipeDesignCriteria. HISTORY: New property set in IFC Release 2.0. ISSUES: No issues to date. |

Property Definitions:

| Name | Property Type | Data Type | Definition |
| --- | --- | --- | --- |
| FinishedLength | IfcPropertySingleValue | IfcLengthMeasure | The finished length of the pipe segment |

Pset_PipeSystemDesignCriteria

| PropertySet Name | Pset_PipeSystemDesignCriteria |
| --- | --- |
| Typed | False |
| TypedClass |  |
| TypeName |  |
| Definition | Definition from IAI: This property set is used to define the general characteristics of the duct system and is typically attached to an instance of an IfcSystem. HISTORY: New property set in IFC Release 2.0. ISSUES: No issues to date. |

Property Definitions:

| Name | Property Type | Data Type | Definition |
| --- | --- | --- | --- |
| PipeSystemTypeEnum | IfcPropertyEnumeratedValue | Pset_PipeSystemTypeEnum DomesticHotWater ChilledWater CondenserWater HeatingHotWater Steam Other NotKnown Unset | Enumeration that identifies the type of system |
| SystemDescription | IfcPropertySingleValue | IfcString | System description |
| SystemLocation | IfcPropertySingleValue | IfcString | Physical description of the part of the building the system serves |
| FluidSourcePressure | IfcPropertySingleValue | IfcPressureMeasure / PressureUnit | Pressure in main for domestic water, sprinklers, system pressure for hydronic systems, etc. |
| FluidLiftHeight | IfcPropertySingleValue | IfcPressureMeasure / PressureUnit | Lift that may be required on open systems with dense fluids. |

Pset_SiteWeatherData

| PropertySet Name | Pset_SiteWeatherData |
| --- | --- |
| Typed | True |
| TypedClass | IfcSite |
| TypeName |  |
| Definition | Definition from IAI: Provides access to weather data appropriate to the site and is used for calculating thermal loads. HISTORY: New property set in IFC Release 1.0. ISSUES: No issues to date. |

Property Definitions:

| Name | Property Type | Data Type | Definition |
| --- | --- | --- | --- |
| Description | IfcPropertySingleValue | IfcString | The site weather data station description or reference to the data source from which weather data was obtained for use in calculations. |
| Date | IfcPropertyReferenceValue | IfcCalendarDate | The date for which the weather data was gathered. |

Pset_SmokeDamper

| PropertySet Name | Pset_SmokeDamper |
| --- | --- |
| Typed | True |
| TypedClass | IfcDamper |
| TypeName | SmokeDamper |
| Definition | Definition from IAI: This property set is used to define the characteristics of a smoke damper. HISTORY: New property set in IFC Release 2.0. ISSUES: No issues to date. |

Property Definitions:

| Name | Property Type | Data Type | Definition |
| --- | --- | --- | --- |
| FrameThickness | IfcPropertySingleValue | IfcLengthMeasure | The thickness of the damper frame |
| BladeType | IfcPropertySingleValue | IfcString | The type of blade used in the damper (e.g., Triple Vee, Fabricated Airfoil, Extruded Airfoil, etc.) |
| MountingPositionEnum | IfcPropertyEnumeratedValue | Pset_DamperMountingPositionEnum Horizontal Vertical Other NotKnown Unset | Enumeration that identifies how the damper is mounted in the building |
| ControlType | IfcPropertySingleValue | IfcString | The type of control used to operate the damper (e.g., Open/Closed Indicator, Resetable Temperature Sensor, Temperature Override, etc.) |
| SleeveLength | IfcPropertySingleValue | IfcLengthMeasure | The length of the damper sleeve |
| SleeveThickness | IfcPropertySingleValue | IfcLengthMeasure | The thickness of the damper sleeve |
| DamperLocationInSleeve | IfcPropertySingleValue | IfcString | The location within the sleeve where the damper is mounted (e.g., Center) |

Pset_SoundPowerLevels

| PropertySet Name | Pset_SoundPowerLevels |
| --- | --- |
| Typed | False |
| TypedClass |  |
| TypeName |  |
| Definition | Definition from IAI: Sound power levels across eight octave bands specifying the amount of sound generation or sound attenuation. |

Property Definitions:

| Name | Property Type | Data Type | Definition |
| --- | --- | --- | --- |
| 63Hertz | IfcPropertySingleValue | IfcReal / PressureUnit | Sound Power Level measured in decibels at a reference power of 1 picowatt(10^(-12) watt) for the octave band frequency centered around 63 Hertz. |
| 125Hetrz | IfcPropertySingleValue | IfcReal / PressureUnit | Sound Power Level measured in decibels at a reference power of 1 picowatt(10^(-12) watt) for the octave band frequency centered around 125 Hertz. |
| 250Hetrz | IfcPropertySingleValue | IfcReal / PressureUnit | Sound Power Level measured in decibels at a reference power of 1 picowatt(10^(-12) watt) for the octave band frequency centered around 250 Hertz. |
| 500Hertz | IfcPropertySingleValue | IfcReal / PressureUnit | Sound Power Level measured in decibels at a reference power of 1 picowatt(10^(-12) watt) for the octave band frequency centered around 500 Hertz. |
| 1000Hetrz | IfcPropertySingleValue | IfcReal / PressureUnit | Sound Power Level measured in decibels at a reference power of 1 picowatt(10^(-12) watt) for the octave band frequency centered around 1000 Hertz. |
| 2000Hetrz | IfcPropertySingleValue | IfcReal / PressureUnit | Sound Power Level measured in decibels at a reference power of 1 picowatt(10^(-12) watt) for the octave band frequency centered around 2000 Hertz. |
| 4000Hertz | IfcPropertySingleValue | IfcReal / PressureUnit | Sound Power Level measured in decibels at a reference power of 1 picowatt(10^(-12) watt) for the octave band frequency centered around 4000 Hertz. |
| 8000Hertz | IfcPropertySingleValue | IfcReal / PressureUnit | Sound Power Level measured in decibels at a reference power of 1 picowatt(10^(-12) watt) for the octave band frequency centered around 8000 Hertz. |
| Name | IfcPropertySingleValue | IfcString | The name of this property |
| Description | IfcPropertySingleValue | IfcString | Description for this object |
| Attenuates | IfcPropertySingleValue | IfcBoolean | If TRUE, values represent sound attenuation. If FALSE, values represent sound generation. |

Pset_SoundPressureLevels

| PropertySet Name | Pset_SoundPressureLevels |
| --- | --- |
| Typed | False |
| TypedClass |  |
| TypeName |  |
| Definition | Definition from IAI: Sound pressure levels across eight octave bands specifying the amount of sound generation ot sound attenuation. HISTORY: New property set in IFC Release 2.0. ISSUES: No issues to date. |

Property Definitions:

| Name | Property Type | Data Type | Definition |
| --- | --- | --- | --- |
| 63Hertz | IfcPropertySingleValue | IfcReal / PressureUnit | Sound Pressure Level measured in decibels at a reference pressure of 20 microPascals for the octave band frequency centered around 63 Hertz. |
| 125Hetrz | IfcPropertySingleValue | IfcReal / PressureUnit | Sound Pressure Level measured in decibels at a reference pressure of 20 microPascals for the octave band frequency centered around 125 Hertz. |
| 250Hetrz | IfcPropertySingleValue | IfcReal / PressureUnit | Sound Pressure Level measured in decibels at a reference pressure of 20 microPascals for the octave band frequency centered around 250 Hertz. |
| 500Hertz | IfcPropertySingleValue | IfcReal / PressureUnit | Sound Pressure Level measured in decibels at a reference pressure of 20 microPascals for the octave band frequency centered around 500 Hertz. |
| 1000Hetrz | IfcPropertySingleValue | IfcReal / PressureUnit | Sound Pressure Level measured in decibels at a reference pressure of 20 microPascals for the octave band frequency centered around 1000 Hertz. |
| 2000Hetrz | IfcPropertySingleValue | IfcReal / PressureUnit | Sound Pressure Level measured in decibels at a reference pressure of 20 microPascals for the octave band frequency centered around 2000 Hertz. |
| 4000Hertz | IfcPropertySingleValue | IfcReal / PressureUnit | Sound Pressure Level measured in decibels at a reference pressure of 20 microPascals for the octave band frequency centered around 4000 Hertz. |
| 8000Hertz | IfcPropertySingleValue | IfcReal / PressureUnit | Sound Pressure Level measured in decibels at a reference pressure of 20 microPascals for the octave band frequency centered around 8000 Hertz. |
| Name | IfcPropertySingleValue | IfcString | The name of this property |
| Description | IfcPropertySingleValue | IfcString | Description for this object |
| Attenuates | IfcPropertySingleValue | IfcBoolean | If TRUE, values represent sound attenuation. If FALSE, values represent sound generation. |

Pset_SpaceHvacInformation

| PropertySet Name | Pset_SpaceHvacInformation |
| --- | --- |
| Typed | False |
| TypedClass |  |
| TypeName |  |
| Definition | Definition from IAI: Space or zone thermal properties and desgn constraints. HISTORY: New property set in IFC Release 1.0. ISSUES: No issues to date. |

Property Definitions:

| Name | Property Type | Data Type | Definition |
| --- | --- | --- | --- |
| CoolingDesignAirflow | IfcPropertySingleValue | IfcVolumetricFlowRateMeasure / VolumetricFlowrateUnit | The air flowrate required during the peak cooling conditions. |
| HeatingDesignAirflow | IfcPropertySingleValue | IfcVolumetricFlowRateMeasure / VolumetricFlowrateUnit | The air flowrate required during the peak heating conditions, but could also be determined by minimum ventilation requirement or minimum air change requirements. |
| TotalSensibleHeatGain | IfcPropertySingleValue | IfcPowerMeasure / PowerUnit | The total sensible heat or energy gained by the space during the peak cooling conditions. |
| TotalHeatGain | IfcPropertySingleValue | IfcPowerMeasure / PowerUnit | The total amount of heat or energy gained by the space at the time of the space's peak cooling conditions. |
| TotalHeatLoss | IfcPropertySingleValue | IfcPowerMeasure / PowerUnit | The total amount of heat or energy lost by the space at the time of the space's peak heating conditions. |
| HeatingDryBulb | IfcPropertySingleValue | IfcThermodynamicTemperatureMeasure | Inside dry bulb temperature for heating design |
| HeatingRelativeHumidity | IfcPropertySingleValue | IfcPositiveRatioMeasure | Inside relative humidity for heating design. |
| CoolingDryBulb | IfcPropertySingleValue | IfcThermodynamicTemperatureMeasure | Inside dry bulb temperature for cooling design |
| CoolingRelativeHumidity | IfcPropertySingleValue | IfcPositiveRatioMeasure | Inside relative humidity for cooling design. |
| VentilationAirFlowrate | IfcPropertySingleValue | IfcVolumetricFlowRateMeasure / VolumetricFlowrateUnit | Ventilation outside air requirement. |
| ExhaustAirFlowrate | IfcPropertySingleValue | IfcVolumetricFlowRateMeasure / VolumetricFlowrateUnit | Exhaust air flow rate for the space. |
| CeilingRAPlenum | IfcPropertySingleValue | IfcBoolean | Ceiling plenum used for return air or not. TRUE = Yes, FALSE = No. |
| BoundaryAreaHeatLoss | IfcPropertySingleValue | IfcHeatFluxDensityMeasure / HeatFluxDensityUnit | Heat loss per unit area for the boundary object. This is a design input value for use in the absence of calculated load data. |