UNITED STATES ENVIRONMENTAL PROTECTION AGENCY

REGION IX AIR DIVISION

Technical Support Document

for

EPA(s Notice of Proposed Rulemaking and Direct Final Rule

for the

California State Implementation Plan

San Joaquin Valley Unified Air Pollution Control District

Rule 4905, Natural Gas-Fired, Fan-Type Residential Central Furnaces

Prepared by: Francisco Dóñez

February 2007

| AGENCY NAME: | San Joaquin Valley Unified Air Pollution Control District (SJVUAPCD) |
| --- | --- |
| SUBMITTED RULE: | Rule 4905, Natural Gas-Fired, Fan-Type Residential Central Furnaces Adopted: October 20, 2005 Submitted: March 10, 2006 Complete: March 30, 2006 |
| PREVIOUS RULE SUBMITTALS: | This is the first submittal of Rule 4905. |
| SIP-APPROVED RULE: | This is a new rule. No previous versions of Rule 4905 have been approved into the State Implementation Plan (SIP). |

RULE SUMMARY

The purpose of SJVUAPCD Rule 4905 is to limit emissions of oxides of nitrogen (NOx) from natural gas-fired, fan-type residential central furnaces with a rated heat input capacity of less than 175,000 Btu per hour, or a cooling capacity of less than 65,000 Btu per hour for combination heating and cooling units.  The rule’s compliance date is January 1, 2007.

Rule provisions

- Rule 4905 imposes an emission limit of 0.093 pounds NOx per million Btu of heat output or 55 ppm NOx at 3.00% O2 stack gas by volume (dry) on units to be used in the District.

- Units installed in manufactured homes, units using fuels other than natural gas, and nonfan-type residential central furnaces are exempt from Rule 4905 requirements.

- The rule contains requirements for demonstrating a unit’s certified emissions levels.

- The rule requires that compliance testing records be maintained by the manufacturer for five years and made available to the APCO upon request.

RULE EVALUATION

Generally, SIP rules must be enforceable (see section 110(a) of the Clean Air Act), must require Reasonably Available Control Technology (RACT) for major sources in ozone nonattainment areas (see section 182(a)(2)(A)), and must not relax existing requirements (see sections 110(l) and 193).  The San Joaquin Valley is an “extreme” ozone nonattainment area; therefore Rule 4307 must fulfil RACT.  The San Joaquin Valley is also a “serious” PM-10 nonattainment area, and is thus required under sections 189(b)(1)(B) and 189(e) of the Act to implement Best Available Control Measures (BACM) (which includes Best Available Control Technology or BACT) for control of PM-10 precursor emissions, including NOx.

Documents used to evaluate the rule include the following:  EPA’s Issues Relating to VOC Regulation Cutpoints, Deficiencies, and Deviations (May 25, 1988, the "Bluebook"); EPA Region IX(s Guidance Document for Correcting Common VOC and Other Rule Deficiencies (August 21, 2001, the (Little Bluebook(); and the EPA’s State Implementation Plans; Nitrogen Oxides Supplement to the General Preamble for the Implementation of Title I of the Clean Air Act Amendment of 1990 (the “NOx Supplement to the General Preamble”) (57 FR 55620, November 25, 1992).

The provisions of Rule 4905 are consistent with the relevant requirements under section 110(a) and part D of the Clean Air Act as amended in 1990.  Specifically, we find that Rule 4905 implements RACT as required for moderate and above ozone nonattainment areas under CAA sections 182(b)(2) and 182(f), RACM/RACT as required for moderate and above PM-10 nonattainment areas under CAA sections 189(a)(1)(C) and 189(e), and BACM/BACT as required for serious PM-10 nonattainment areas under CAA sections 189(b)(1)(B) and 189(e) for NOx emissions from the source category of natural gas-fired, fan-type residential central furnaces.  The NOx emission limit in Rule 4905 matches the most stringent limit (0.093 lb/MMBtu) that has been adopted by air districts in this source category.

Emissions Reductions

The staff report for Submitted Rule 4905 indicates emissions reductions of 0.251 tons per day by 2020.

RECOMMENDED ACTION

EPA staff recommends full approval of submitted SJVUAPCD Rule 4905.

ATTACHMENTS

SJVUAPCD Rule 4905, Natural Gas-Fired, Fan-Type Residential Central Furnaces, adopted October 20, 2005.

U.S. EPA.  Issues Relating to VOC Regulation Cutpoints, Deficiencies, and Deviations. May 25, 1988 (the "Bluebook," cover only).

U.S. EPA Region IX.  Guidance Document for Correcting Common VOC & Other Rule Deficiencies. August 21, 2001 (the "Little Bluebook," cover only).

State Implementation Plans; Nitrogen Oxides Supplement to the General Preamble for the Implementation of Title I of the Clean Air Act Amendment of 1990 (the “NOx Supplement to the General Preamble”), U.S. EPA, 57 FR 55620, November 25, 1992.