### Tearing mode / NTM physics

Goal: Study neoclassical and classical tearing modes in the unique low aspect ratio, high beta, and large ion gyro-radius plasmas available in NSTX, in order to both extrapolate our understanding to future ST devices and provide data complementary to that from conventional aspect ratio tokamaks.  Investigate the impact of these modes on plasma beta, rotation, fast particle redistribution, and the potential of low aspect ratio operation as being theoretically favorable for NTM stability. Determine scenarios that allow operation without these deleterious instabilities.

Contributes to:

- ITPA MDC-3 – Joint experiments on neoclassical tearing modes

- ITPA MDC-4 – Neoclassical tearing modes – aspect ratio comparison

(i) physics – results and plans

The neoclassical tearing mode (NTM) is a magnetic island driven by a hole in the bootstrap current. These modes are a likely problem for any high-performance tokamak, leading to confinement degradation (soft  limit) in the case of the m/n=4/3 and 3/2 modes, and potential mode-locking and disruption for the 2/1 NTM []. These modes were studies in early NSTX [] research, and have been observed in MAST []. We plan a renewed focus on NTM physics in the coming research period. Important areas for proposed NTM research include i) investigation of the onset-( and marginal island widths as functions of kinetic parameters and plasma rotation ii) studies of the NTM triggers in q0>1 regimes, iii), modeling these modes in low-aspect ratio geometry including the effects of flow and flow shear, and iv) studies of the interaction of NTMs with fast particles, including particle redistribution during mode activity.

The degrading effects of an m/n=2/1 NTM on a high performance discharge are shown in Fig 2.1.1-1. The mode amplitude is shown in frame a), with the mode striking at t=0.56 and maintaining it’s saturated state until t=0.71, when it locks; the plasma then disrupts at t=0.75. Frames b) and c) show that bN continually drops during the period of the mode, as does the energy confinement time (both determined by the EFIT code). The mode has a profound effect on the rotation profile: an immediate collapse of the core rotation and transition to rigid-body rotation. Indeed, it is likely that both the short-circuiting of the magnetic surfaces [] and the reduction of rotation and rotation shear contribute to the severe confinement degradation. It is clear that in NSTX as well as conventional tokamaks, these modes must be avoided in order to maintain the desired high-b state.

Fig 2.1.1-1: Illustration of the effects of a 2/1 NTM on discharge confinement. From top to bottom are the mode amplitude, bN, tE, the rotation frequency at five radii, and the plasma current.

The Modified Rutherford equation (MRE) provides a convenient basic framework to consider for the NTM studies described below:

(1)

This equation describes the evolution of the full island width (w), including classical tearing stability ((’), neoclassical drive due to the bootstrap current missing inside the island (( (P/w), stabilizing terms due to toroidal geometry (DR/w ( ( /w, the “Glasser, Greene and Johnson” term), and threshold effects (the transport threshold manifested by wd [] and the polarization threshold manifested through wpol []) which are important for small islands. Given that ( can begin to approach (P in NSTX, the GGJ term is expected to be strongly stabilizing [], an effect to be examined as these studies move forward. Additional terms can be added to this equation, such as those associated with stabilizing electron cyclotron current drive (ECCD) [].

Equation 1 predicts that for saturated island sizes larger than wd and w0, the island width should be proportional to bP. This trend is indeed observed, as illustrated in Fig. 2.1.1-2, where the square root of the magnetic fluctuation amplitude at the wall (( to the island width), is plotted against the global bP for four discharges where NBI power ramp downs occurred. The linear relationship is clear. This observation, coupled to the close frequency match between the magnetic fluctuations and the q=2 rotation frequencies and the observation of flat spots at q=2 in the electron temperature profile, confirms that the observed mode is indeed a neoclassical island. Similar observations have been made for 3/2 NTM as well, and the physics discussed above and below is typically relevant to both modes.

Fig 2.1.1-2: The measured m/n=2/1 island width  is proportional to bP, as expected for a saturated NTM.

The small island terms in (1), wd and wpol, prevent NTM growth for arbitrarily small islands when classical tearing is stable ((’<0). Instead, a seed island must be formed whose width exceeds some threshold value. For the 3/2 NTM, this seed-island is typically provided by sawteeth in conventional aspect ratio tokamaks; ELMs have been suggested to play a similar role for the 2/1 NTM in DIII-D and JET. In NSTX, rapid changes in the beam timing have been observed to trigger the 3/2 NTM. The NSTX discharge illustrated in Fig. 2.1.1-3, however, shows a large 2/1 NTM growing with no observable trigger. The spectrogram from a single Mirnov coil in the top frame shows the mode growing at t=0.83, with no precursor; this smooth growth is clearly indicated in the mode amplitude plot in the frame below. Neither the Ha nor the edge and core USXR signals show a precursor. The NTM eventually locks at t=0.95, as evidenced by the rapid drop of the edge USXR signal and spike in Ha, followed by a disruption. It is possible that cases like these begin as classical tearing modes, which transition to neoclassically driven modes when the island width exceeds the critical island width []. This classical physics can be especially important for high-b plasmas, where a pole in (’ occurs at the ideal kink limit []. This discharge had bwhen the mode struck, near to if not exceeding the no-wall limit. Understanding this triggering will be an important part of NSTX research.

Fig 2.1.1-3: Example of an m/n=2/1 NTM with no clear trigger.

The marginal island width, i.e. the island width where dw/dt=0 for the smallest (P where NTMs are still metastable, is a key parameter for understanding the relevant small island physics  (wd and wpol) and extrapolating to larger and hotter plasmas. Experiments at conventional aspect ratio in DIII-D [], JET [] and ASDEX-U [] suggest that the marginal island width scales empirically with the poloidal gyroradius. Verifying this empirical scaling at low aspect ratio is particularly important, as it predicts that an ST reactor or CTF (or indeed, ITER) will be very susceptible to NTM destabilization, and that NTM control techniques must be implemented. (P ramp down experiments will be conducted to establish the marginal island widths for both the 3/2 and 2/1 NTMs, as a function of parameters such as rotation and poloidal gyroradius.  It is planned to make a first complete set of marginal island-width experiments in the FY09-FY11 time-frame. However, the extended field and current capabilities of the upgraded NSTX will expand the parameter regime in quantities like poloidal gyroradius, collisionality, qmin and q-shear, providing greater a wider range of applicability for the results.

Plasma rotation and rotation shear enter the eqn. 1 in a number of places, for instance through the polarization threshold term and through modifications to (’, as well as through mechanisms outside of the MRE, such as modifications to the coupling between the rational surface and the surface where triggering instabilities occur. Given that the momentum input to a future reactor is likely to be much reduced compared to present experiments, there has been recent interest in how rotation and rotation shear experimentally impact the onset and saturation of NTMs. Experiments in JET and DIII-D demonstrated the importance of rotation in increasing the NTM threshold []. For the 3/2 NTM, this effect may be associated with dynamic rotation shielding between the NTM resonant surface and the q=1 surface, where the seed perturbation originates. Experiments in DIII-D have also demonstrated a reduction in the onset b for 2/1 modes when the co-injection beam torque is reduced to and beyond zero [].

Experiments in NSTX have already begun to study the dependence of the 2/1 mode onset on rotation shear. We have observed a ~20% reduction in onset global N as the rotation at q=2 is reduced. However, given that the NTM evolution in eqn. (1) is determined by local parameters, we have undertaken more systematic studies in terms of local bootstrap drive and rotation shear. Fig. 2.1.1-4 shows the local drive bootstrap drive for the island at mode onset,  , as a function of the local rotation shear at q=2, . The discharges in the scan were chosen from a wide variety of experiments which utilized n=3 braking and NBI torque to control the rotation. All were high-k, high-d plasmas with IP=1MA and BT=0.45T. typical of high-performance regimes in NSTX.  There is a clear offset-linear dependence of the bootstrap-drive on rotation shear when the mode strikes, implying the importance of rotation shear in allowing higher-boperation. Importantly, this is the first ever correlation of the local NTM properties with rotation shear, expanding on the previous DIII-D work.

Figure 2.1.1-4  Local bootstrap drive and a function of rotation shear at q=2, for discharges high-k, high-d discharge. Both n=3 braking and variations on the NBI are used to vary the rotation shear.

There may, however, be NTM physics outside the direct purview of eqn (1). For instance, the tearing modes in TFTR [], AUG [], and possibly other major tokamaks, are commonly coupled to core kink-like modes.  As these internal kink-like modes resemble the fishbone instability, it is reasonable to view this as a mechanism through which NTMs are coupled to the fast ion distribution.  Evidence for such coupling, e.g., strong frequency chirping, has not been seen as yet in NSTX, though it has been observed in AUG [] and TFTR.  However, NSTX presently operates in a fast ion regime far from typical operating regimes of present large aspect ratio tokamaks.  The upgrade to the center stack will allow higher field operation, bringing NSTX fast ion parameters more in line with those of conventional tokamaks.  This will allow experiments to study the interactions of fast ions, including potential drive mechanism, with NTMs.

These experimental tasks will be executed in parallel with modeling and simulations of NTM dynamics at low aspect ratio. A three part modeling effort is planned in this regard, involving the linear dispersion relation describing the threshold for onset of the mode, the quasilinear island evolution equation for intuitive study of the effects of low aspect ratio, and the simulation of mode onset and evolution with initial value codes.  The presence of toroidal flow shear introduces a number of physics issues into these analyses, which are critical to understanding the experimental outcome. A series of experimental discharges that exemplify the physics of flow shear effects in the onset and evolution of resistive MHD instabilities will be compared to theoretical predictions.

The effect of a sheared flow field on the coupling between modes can be described by the solution to the dispersion relation  where  includes both tearing () and interchange parities,  is the solution vector inside of the resonant layer, and  is the normalized growth rate. With flow shear  becomes complex in the sense that the growth rate now has both real and imaginary parts in the inner layer  where  (ignoring poloidal precession from  effects) represents the toroidal angular frequency at the rational surface, and  represents the mode growth rate.  This directly affects the coupling between modes in toroidal geometry, as addressed at length in [] and recently published in Ref. [ as well as the local stability via the inner layer physics, as described in [], among several others.

In this research plan, we intend to compute the tearing and interchange solutions for multiple rational surfaces using the PEST-III code, and compute the inner layer solutions using the code described in Ref. [] to solve the dispersion relation.  The individual effects can then be examined and compared with a similar approach to Refs. [xix,xxi] using the NIMROD code.

A further step will be to implement solutions of the MRE (equation 1) in full low aspect ratio geometry. These studies were begun in the work by [], where PEST-III was used to calculate (’, and routines from NIMROD were used to calculate the bootstrap drive and DR. These steps will allow full calculations of the island growth and decay rates, as well as the saturated island eigenfunctions, for comparison with the experimental measurements described above. A primary goal of these efforts will be to assess the impact of the GGJ term in the context of experimental measurements.

A more advanced modeling step will be to utilize initial value codes such as M3D and NIMROD to simulate the non-linear evolution of NTMs. Compared to the approach in equation (1), these methods are far more advanced in their treatment of heat conduction around the island, the effects of rotation shear, and self consistent current profile and island width evolution.

A thorough theoretical and computational analysis of the effects that low aspect ratio will have on the resistive stability will be complimentary to the results from the experiment.  Also, a comparison with results from the high aspect ratio experiments will give us insight to further develop our theoretical description of the physics of these instabilities.

Our ability to meet these scientific goals will be augmented through improved diagnostic coverage during this research period. NSTX plasmas are overdense, preventing traditional measurements of island widths via electron cyclotron emission (ECE); measurements to date have relied on edge magnetics and USXR emission to constrain the island size and location. However, the BES system currently under construction will allow core fluctuation measurements with high frequency and spatial resolution. The CIF-MSE system also has the ability to measure spatially localized fast magnetic fluctuations at NTM relevant frequencies. This measurement, combined with USXR emission and edge magnetics, should allow detailed studies of the island eigenfunction, including the coupling to internal kink-like modes if present.

(ii) NTM Control

The results in Fig. 2.1.1-1 illustrate that 2/1 NTMs must be avoided in order to maintain optimal performance in NSTX. Experiments in DIII-D, JT-60, and AUG have demonstrated the ability to suppress both the 2/1 and 3/2 NTM with ECCD replacing the missing bootstrap current. This method is not available in the overdense NSTX plasma. Hence, passive control techniques will be employed in the planned research period.

To date, the most successful means of mitigating the 2/1 NTM has been through the use of combined lithium conditioning and dynamic error field correction. This is illustrated in Fig. 2.1.1-5, where the mode activity is compared between discharges with and without lithium evaporation; the rotation frequency in the core and at q=2 are also shown, based on CHERS data and equilibrium reconstruction. Both discharges show a period of MHD activity during and immediately after the current ramp, as the q-profile evolves. The control shot 129013 then develops the large 2/1 mode, the plasma rotation is dramatically reduced, and the shot ultimately disrupts at t=1 sec. after the mode locks. The discharge with DEFC and lithium evaporation shows no sign of the later rotating instability, and ultimately succumbs to a fast-growing external mode, likely a resistive wall mode, at t=1.3 seconds.

Figure 2.1.1-5: Comparison of low-frequency mode activity in shots without (129013) and with (129072) with lithium evaporation. Also shown are the core (green) and q=2 (magenta) rotation frequencies. The two discharges, designed to determine the effect of lithium evaporation on plasma performance, have all other controlled parameters the same.

The stabilization noted in the above figure was achieved with both lithium evaporation and DEFC; in other more rare cases, simply one of these two ingredients is sufficient to suppress the mode for the duration of the discharge. A high priority for near-term studies is to understand how the current and rotation profiles with lithium and DEFC change the mode stability, including changes in mode triggering. The studies offer exciting prospects for NTM control, as the liquid lithium divertor and NCC should allow a significant extension of these high performance discharge regimes.

In the five-year period starting in FY2014, an additional 3 NBI sources will be added to the NSTX NBI system. As discussed in Chapter X, this upgrade should allow access to fully non-inductive equilibria with qmin > 2. This scenario would have the effect of eliminating the pernicious m/n = 2/1 and 3/2 resonances from the plasma. The effect of higher order NTMs, such as m/m=3/1 and 5/2, can then be studied. Additionally, the current profile control allowed with the more tangential beams may allow stabilization or mitigation of the NTM through modifications to (’, in a fashion similar to what was achieved in COMPASS-D [] with lower-hybrid current drive.

SUMMARY OF RESEARCH PLANS AND TIMELINE

FY09-FY11	Complete characterization of NTM onset, including triggering physics and the role of rotation, rotation shear, and small island effects.

FY09-FY11	Utilize bP ramp down experiments to characterize the dependencies of the small island physics on kinetic parameters at low aspect ratio

FY09-FY11	Utilize PEST-III for accurate calculations of (’ in NSTX geometry. Develop solutions to (1) utilizing low-aspect ratio solutions for all terms. Asses merits of low-A for NTM stability

FY10-FY12	Implement nonlinear initial value simulations of NTMs with NIMROD and M3D. Compare measured island seeding and evolution to simulations.

FY12-FY13	Utilize upgraded NSTX to look for interactions of NTM with fast particles

FY12-FY13      Utilize previously developed knowledge base and new tools to develop routine high- discharges with no deleterious island activity.

# Endnotes

[] T.C. Hender et al., Progress on the ITER Physics Basis (Chapter 3), Nucl. Fusion 47, S128 (2007).

[] D.A. Gates, et al., APS 2000 – NTM observation in NSTX reference.

[] R. Buttery, et al., Phys. Rev. Lett 88, 125005 (2002).

[] Z. Chang and J.D. Callen, Nuclear Fusion 30, 219 (1990).

[] R. Fitzpatrick, Phys. Plasmas 2, 825 (1995)

[] F. L. Waelbroeck, J.W. Conner, and J.R. Wilson, Phys. Rev. Lett. 87, 215003 (2001)

[] S. Kruger, C.C. Hegna, and J.D. Callen, Phys. Plasmas 5, 455 (1998).

[] R.J. La Haye, et al, Nuclear Fusion 46, 451 (2006)

[] H. Reimerdes, Phys. Rev. Lett 88, 105005 (2002)

[] D. Brennan, et al, Phys. Plasmas 10, 1643 (2003)

[] R.J. La Haye, Phys. Plasmas 13, 055501 (2006).

[] R.J. Buttery et al., 20th IAEA Fusion Energy Conference, (Vilamoura, Portugal  2004), paper IAEA-CN-116/EX/7-1, Conference & Symposium Papers CD ROM, IAEA-CSP-25/CD, ISBN 92-0-100405-2, ISSN 1562-4153, IAEA Vienna (2005).

[] M. Maraschek, et al, Plasma Phys. Control Fusion 45, 1369 (2003)

[] R. J. Buttery, et al, Rotation and Shape dependence of Neoclassical Tearing Mode thresholds on JET, 28th EPS Conference on Contr. Fusion and Plasma Phys. 2001.

[] R. Buttery, et al, Phys. Plasmas 15, 056115 (2008)

[] E. Fredrickson, Phys. Plasmas  9, 548 (2002)

[] A. Gude, S. Gunter, S. Sesnic, and the ASDEX upgrade Team, Nuclear Fusion 39, 127 (1999)

[] S. Sesnic, et al, Phys. Plasmas 7, 935 (2000)

[] S.E. Kruger, PhD Thesis, The University of Wisconsin - Madison (1999).

[] Chandra, Nucl. Fusion 45, 524 (2005).

[] X.L. Chen and P.J. Morrison, Phys. Fluids B 4, 845 (1992).

[] D.P. Brennan, A.D. Turnbull, M.S.Chu, R.J. La Haye, L.L. Lao, T.H. Osborne and S.A. Galkin, General Atomics Report A25648, Phys. Plasmas 14, 056108 (2007).

[] A.L. Rosenberg, et al, Phys. Plasmas 9, 4567 (2002)

[] C.D. Warrick, et al, Phys. Rev. Lett 85, 574 (2000)