Appendix A1.—Site statistics for inorganic constituent concentrations in samples collected and analyzed by the U.S. Geological Survey.

[SR, secondary road; NWIS, National Water Information System; wat., water; filt., filtered; unf., unfiltered; mg/L, milligram per liter; --, value is below the detection level and(or) cannot be calculated; *, value is estimated by using a log-probability regression to predict the values of data below the detection limit; ug/L, microgram per liter]

Table of Contents

Eno River at Hillsborough (initial site)	3

Eno River at Hillsborough (replaced initial site)	5

Eno River near Durham	8

Eno River near Weaver	10

Little River at SR 1461 near Orange Factory	13

Little River Reservoir at dam near Bahama	16

Little River below dam near Fairntosh	19

Flat River at Bahama	21

Lake Michie at dam near Bahama	24

Flat River at dam near Bahama	27

Knap of Reeds Creek near Butner	30

Ellerbe Creek near Gorman	32

Falls Lake at I-85 near Redwood	35

Little Lick Creek above SR 1814 near Oak Grove	38

Falls Lake at N.C. 50 near Sandy Plain	41

Falls Lake at N.C. 98 near Bayleaf	44

Falls Lake above dam at Falls	47

Neuse River near Falls	50

Neuse River at Smithfield	51

Swift Creek near Apex	54

Lake Benson at dam near Garner	57

Cane Creek near Orange Grove	60

Cane Creek Reservoir at dam near White Cross	63

Haw River near Bynum	66

B.E. Jordan Lake, Haw River arm above B.E. Jordan dam	69

New Hope Creek near Blands	72

Northeast Creek at SR 1100 near Genlee	75

Morgan Creek near White Cross	78

University Lake at the dam near Chapel Hill	81

Morgan Creek near Farrington	84

Jordan Lake at buoy 12 at Farrington	86

Jordan Lake at buoy 9 near Farrington	89

White Oak Creek at Green Level	91

B.E. Jordan Lake above U.S. 64 at Wilsonville	93

Jordan Lake at buoy 7 below U.S. 64 near Griffins Crossroads	96

B.E. Jordan Lake at Bells Landing near Griffins Crossroads	98

Haw River below B. Everett Jordan dam near Moncure	101

Deep River at Carbonton	102

Cape Fear River at N.C. 42 near Brickhaven	104

| NWIS Param-eter code | Constituent name | Sample size | Maximum | Minimum | Mean | Percentile |
| --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  | 95th | 75th | 50th | 25th | 5th |
| 0208491605 Eno River at Hillsborough—initial site (October 1988–September 1989) |
| 00080 | Color, wat., filt., platinum cobalt units | 12 | 170.000 | 30.000 | 83.167 | 170.000 | 110.000 | 80.000 | 51.250 | 30.000 |
| 00400 | pH, wat., unf., field, standard units | 12 | 7.100 | 5.700 | 6.175 | 7.100 | 6.625 | 5.950 | 5.800 | 5.700 |
| 00403 | pH, wat., unf., laboratory, standard units | 12 | 8.100 | 6.900 | 7.442 | 8.100 | 7.775 | 7.300 | 7.200 | 6.900 |
| 90095 | Specific conductance, wat., unf., laboratory, microsiemens per centimeter at 25 degrees Celsius | 12 | 87.000 | 65.000 | 77.500 | 87.000 | 83.000 | 81.500 | 68.250 | 65.000 |
| 00095 | Specific conductance, wat., unf., microsiemens per centimeter at 25 degrees Celsius | 12 | 138.000 | 63.000 | 79.000 | 138.000 | 80.000 | 78.000 | 65.750 | 63.000 |
| 00900 | Hardness, wat., unf., mg/L as calcium carbonate | 12 | 28.000 | 20.000 | 25.083 | 28.000 | 27.000 | 26.000 | 22.250 | 20.000 |
| 00915 | Calcium, wat., filt., mg/L | 12 | 6.700 | 4.600 | 5.850 | 6.700 | 6.375 | 5.950 | 5.175 | 4.600 |
| 00925 | Magnesium, wat., filt., mg/L | 12 | 3.000 | 2.100 | 2.558 | 3.000 | 2.775 | 2.600 | 2.300 | 2.100 |
| 00935 | Potassium, wat., filt., mg/L | 12 | 2.400 | 1.300 | 1.725 | 2.400 | 2.050 | 1.600 | 1.400 | 1.300 |
| 00931 | Sodium adsorption ratio, wat., number | 12 | 0.500 | 0.300 | 0.392 | 0.500 | 0.400 | 0.400 | 0.325 | 0.300 |
| 00930 | Sodium, wat., filt., mg/L | 12 | 5.800 | 3.300 | 4.492 | 5.800 | 4.975 | 4.450 | 4.025 | 3.300 |
| 00932 | Sodium, wat., percent in equivalents of major cations | 12 | 31.000 | 22.000 | 26.250 | 31.000 | 28.000 | 26.000 | 24.250 | 22.000 |
| 90410 | Acid neutralizing capacity, wat., unf., fixed endpoint (pH 4.5) titration, laboratory, mg/L as calcium carbonate | 12 | 31.000 | 17.000 | 23.500 | 31.000 | 25.000 | 24.000 | 20.250 | 17.000 |
| 00940 | Chloride, wat., filt., mg/L | 12 | 6.000 | 4.000 | 4.917 | 6.000 | 5.500 | 4.800 | 4.225 | 4.000 |
| 00950 | Fluoride, wat., filt., mg/L | 12 | 0.200 | 0.100 | 0.117 | 0.200 | 0.100 | 0.100 | 0.100 | 0.100 |
| 00955 | Silica, wat., filt., mg/L | 12 | 16.000 | 9.800 | 12.567 | 16.000 | 14.000 | 12.500 | 11.000 | 9.800 |
| 00945 | Sulfate, wat., filt., mg/L | 12 | 12.000 | 3.000 | 6.933 | 12.000 | 10.750 | 5.450 | 4.000 | 3.000 |
| 99890 | Sulfate, wat., filt., uncorrected, mg/L | 2 | -- | -- | -- | -- | -- | -- | -- | -- |
| 70300 | Residue on evaporation, dried at 180 degrees Celsius, wat., filt., mg/L | 12 | 67.000 | 42.000 | 56.000 | 67.000 | 63.250 | 55.500 | 51.250 | 42.000 |
| 00608 | Ammonia, wat., filt., mg/L as nitrogen | 12 | 0.120 | -- | 0.049* | *0.120 | *0.057 | *0.045 | *0.030 | *0.014 |
| 00623 | Ammonia plus organic nitrogen, wat., filt., mg/L as nitrogen | 10 | 0.800 | 0.400 | 0.530 | 0.800 | 0.625 | 0.500 | 0.400 | 0.400 |
| 00625 | Ammonia plus organic nitrogen, wat., unf., mg/L as nitrogen | 12 | 1.100 | 0.400 | 0.625 | 1.100 | 0.675 | 0.600 | 0.500 | 0.400 |
| 00610 | Ammonia, wat., unf., mg/L as nitrogen | 12 | 0.130 | -- | 0.052* | *0.130 | *0.078 | *0.040 | *0.020 | *0.009 |
| 00620 | Nitrate, wat., unf., mg/L as nitrogen | 5 | 0.870 | 0.190 | -- | -- | -- | -- | -- | -- |

| NWIS Param-eter code | Constituent name | Sample size | Maximum | Minimum | Mean | Percentile |
| --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  | 95th | 75th | 50th | 25th | 5th |
| 00631 | Nitrite plus nitrate, wat., filt., mg/L as nitrogen | 12 | 0.910 | -- | 0.296* | *0.910 | *0.270 | *0.240 | *0.183 | *0.066 |
| 00630 | Nitrite plus nitrate, wat., unf., mg/L as nitrogen | 12 | 0.900 | -- | 0.305* | *0.900 | *0.300 | *0.200 | *0.200 | *0.065 |
| 00615 | Nitrite, wat., unf., mg/L as nitrogen | 12 | 0.030 | -- | 0.008* | *0.030 | *0.010 | *0.005 | *0.002 | *0.001 |
| 00605 | Organic nitrogen, wat., unf., mg/L | 11 | 1.100 | 0.320 | 0.576 | 1.100 | 0.580 | 0.560 | 0.480 | 0.320 |
| 00666 | Phosphorus, wat., filt., mg/L | 12 | 0.040 | 0.010 | 0.028 | 0.040 | 0.037 | 0.030 | 0.020 | 0.010 |
| 00671 | Orthophosphate, wat., filt., mg/L as phosphorus | 12 | 0.040 | -- | 0.019* | *0.040 | *0.030 | *0.020 | *0.010 | *0.005 |
| 70507 | Orthophosphate, wat., unf., mg/L as phosphorus | 12 | 0.070 | -- | 0.023* | *0.070 | *0.030 | *0.020 | *0.010 | *0.004 |
| 00665 | Phosphorus, wat., unf., mg/L | 12 | 0.080 | 0.030 | 0.049 | 0.080 | 0.060 | 0.050 | 0.030 | 0.030 |
| 00680 | Organic carbon, wat., unf., mg/L | 12 | 8.100 | 5.000 | 6.383 | 8.100 | 7.350 | 6.300 | 5.225 | 5.000 |
| 01105 | Aluminum, wat., unf., recoverable, ug/L | 4 | 4200.000 | 160.000 | -- | -- | -- | -- | -- | -- |
| 01002 | Arsenic, wat., unf., ug/L | 4 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01027 | Cadmium, wat., unf., ug/L | 4 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01034 | Chromium, wat., unf., recoverable, ug/L | 4 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01037 | Cobalt, wat., unf., recoverable, ug/L | 4 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01045 | Iron, wat., unf., recoverable, ug/L | 4 | 7400.000 | 1000.000 | -- | -- | -- | -- | -- | -- |
| 01055 | Manganese, wat., unf., recoverable, ug/L | 4 | 1200.000 | 110.000 | -- | -- | -- | -- | -- | -- |
| 71900 | Mercury, wat., unf., recoverable, ug/L | 4 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01147 | Selenium, wat., unf., ug/L | 4 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01077 | Silver, wat., unf., recoverable, ug/L | 3 | -- | -- | -- | -- | -- | -- | -- | -- |
| 02085000 Eno River at Hillsborough—replaced initial site (October 1989–August 2001) |
| 00061 | Discharge, instantaneous, cubic feet per second | 110 | 9120.000 | 0.560 | 138.971 | 291.500 | 53.250 | 26.000 | 5.975 | 1.900 |
| 00080 | Color, wat., filt., platinum cobalt units | 108 | 350.000 | 7.000 | 62.880 | 180.000 | 65.000 | 52.500 | 35.250 | 23.350 |
| 00300 | Dissolved oxygen, wat., unf., mg/L | 110 | 16.000 | 3.800 | 8.668 | 12.745 | 10.800 | 8.475 | 6.575 | 5.100 |
| 00301 | Dissolved oxygen, wat., unf., percent of saturation | 108 | 139.000 | 44.000 | 84.231 | 109.000 | 95.750 | 86.000 | 71.250 | 59.000 |
| 00400 | pH, wat., unf., field, standard units | 110 | 7.710 | 4.650 | 6.870 | 7.357 | 7.100 | 6.900 | 6.707 | 6.300 |
| 00403 | pH, wat., unf., laboratory, standard units | 109 | 8.200 | 4.100 | 7.291 | 7.900 | 7.500 | 7.300 | 7.100 | 6.750 |
| 90095 | Specific conductance, wat., unf., laboratory, microsiemens per centimeter at 25 degrees Celsius | 109 | 310.000 | 40.000 | 94.587 | 126.000 | 107.000 | 89.000 | 81.000 | 66.500 |
| 00095 | Specific conductance, wat., unf., microsiemens per centimeter at 25 degrees Celsius | 109 | 304.000 | 33.000 | 91.191 | 120.000 | 104.000 | 86.000 | 77.150 | 64.500 |
| 00900 | Hardness, wat., unf., mg/L as calcium carbonate | 109 | 44.000 | 12.000 | 28.780 | 38.500 | 32.500 | 28.000 | 25.000 | 20.000 |
| 00915 | Calcium, wat., filt., mg/L | 109 | 11.000 | 2.900 | 6.906 | 9.550 | 7.850 | 6.800 | 5.850 | 4.650 |
| 00925 | Magnesium, wat., filt., mg/L | 109 | 4.000 | 1.100 | 2.798 | 3.600 | 3.150 | 2.800 | 2.500 | 2.000 |
| 00935 | Potassium, wat., filt., mg/L | 109 | 3.500 | 1.000 | 1.647 | 2.400 | 1.900 | 1.600 | 1.200 | 1.050 |
| 00931 | Sodium adsorption ratio, wat., number | 109 | 1.000 | 0.200 | 0.437 | 0.600 | 0.500 | 0.400 | 0.400 | 0.300 |
| 00930 | Sodium, wat., filt., mg/L | 109 | 16.000 | 1.400 | 5.402 | 8.650 | 6.050 | 5.100 | 4.600 | 3.650 |
| 00932 | Sodium, wat., percent in equivalents of major cations | 109 | 51.000 | 17.000 | 27.404 | 34.500 | 28.000 | 27.000 | 25.000 | 23.500 |
| 99430 | Carbonate, wat., unf., incremental titration, field, mg/L as calcium carbonate | 50 | 51.000 | 13.000 | 26.920 | 46.700 | 31.250 | 27.000 | 21.750 | 14.000 |
| 90410 | Acid neutralizing capacity, wat., unf., fixed endpoint (pH 4.5) titration, laboratory, mg/L as calcium carbonate | 107 | 46.000 | 9.200 | 28.217 | 39.200 | 34.000 | 28.000 | 24.000 | 17.400 |
| 29801 | Alkalinity, wat., filt., fixed endpoint (pH 4.5) titration, laboratory, mg/L as calcium carbonate | 1 | 34.000 | -- | -- | -- | -- | -- | -- | -- |
| 39086 | Alkalinity, wat., filt., incremental titration, field, mg/L as calcium carbonate | 4 | 62.000 | 10.000 | -- | -- | -- | -- | -- | -- |
| 00410 | Acid neutralizing capacity, wat., unf., fixed endpoint (pH 4.5) titration, field, mg/L as calcium carbonate | 55 | 50.000 | 15.000 | 27.618 | 46.000 | 31.000 | 27.000 | 22.000 | 16.000 |
| 00419 | Acid neutralizing capacity, wat., unf., incremental titration, field, mg/L as calcium carbonate | 17 | 52.000 | 15.000 | 28.647 | 52.000 | 33.000 | 27.000 | 25.000 | 15.000 |
| 99440 | Bicarbonate, wat., unf., incremental titration, field, mg/L | 67 | 63.000 | 16.000 | 33.340 | 58.200 | 39.000 | 33.000 | 27.000 | 17.400 |
| 00453 | Bicarbonate, wat., filt., incremental titration, field, mg/L | 2 | 76.000 | 12.200 | -- | -- | -- | -- | -- | -- |
| 99445 | Carbonate, wat., unf., incremental titration, field, mg/L | 12 | 0.000 | -- | -- | -- | -- | -- | -- | -- |
| 00940 | Chloride, wat., filt., mg/L | 105 | 15.000 | 1.600 | 5.592 | 11.700 | 5.800 | 5.200 | 4.750 | 3.630 |
| 00950 | Fluoride, wat., filt., mg/L | 105 | 0.300 | -- | 0.095* | *0.200 | *0.100 | *0.081 | *0.056 | *0.033 |
| 00955 | Silica, wat., filt., mg/L | 105 | 16.000 | 4.800 | 12.037 | 15.000 | 13.000 | 12.000 | 11.000 | 7.660 |
| 00945 | Sulfate, wat., filt., mg/L | 105 | 170.000 | 2.400 | 7.102 | 8.340 | 6.400 | 5.400 | 4.550 | 3.130 |
| 99890 | Sulfate, wat., filt., uncorrected, mg/L | 5 | -- | -- | -- | -- | -- | -- | -- | -- |
| 70300 | Residue on evaporation, dried at 180 degrees Celsius, wat., filt., mg/L | 103 | 212.000 | 14.000 | 68.612 | 90.000 | 75.000 | 66.000 | 60.000 | 46.200 |
| 00608 | Ammonia, wat., filt., mg/L as nitrogen | 108 | 0.170 | -- | 0.042* | *0.114 | *0.060 | *0.040 | *0.015 | *0.003 |
| 00623 | Ammonia plus organic nitrogen, wat., filt., mg/L as nitrogen | 75 | 0.700 | -- | 0.321* | *0.620 | *0.400 | *0.300 | *0.200 | *0.136 |
| 00625 | Ammonia plus organic nitrogen, wat., unf., mg/L as nitrogen | 108 | 2.900 | 0.200 | 0.404 | 0.700 | 0.500 | 0.300 | 0.300 | 0.200 |
| 00610 | Ammonia, wat., unf., mg/L as nitrogen | 31 | 0.130 | -- | 0.058* | *0.125 | *0.088 | *0.050 | *0.032 | *0.010 |
| 00620 | Nitrate, wat., unf., mg/L as nitrogen | 14 | 0.540 | 0.130 | 0.305 | 0.540 | 0.423 | 0.260 | 0.190 | 0.130 |
| 00631 | Nitrite plus nitrate, wat., filt., mg/L as nitrogen | 108 | 0.600 | 0.050 | 0.285 | 0.461 | 0.347 | 0.290 | 0.210 | 0.100 |
| 00630 | Nitrite plus nitrate, wat., unf., mg/L as nitrogen | 30 | 0.580 | 0.098 | 0.307 | 0.536 | 0.400 | 0.300 | 0.222 | 0.121 |
| 00613 | Nitrite, wat., filt., mg/L as nitrogen | 96 | 0.030 | -- | 0.006* | *0.020 | *0.006 | *0.003 | *0.002 | *0.001 |
| 00615 | Nitrite, wat., unf., mg/L as nitrogen | 31 | 0.040 | -- | 0.010* | *0.040 | *0.010 | *0.006 | *0.003 | *0.001 |
| 00605 | Organic nitrogen, wat., unf., mg/L | 96 | 2.800 | 0.130 | 0.376 | 0.732 | 0.440 | 0.315 | 0.240 | 0.170 |
| 00666 | Phosphorus, wat., filt., mg/L | 76 | 1.200 | -- | 0.034* | *0.054 | *0.020 | *0.012 | *0.010 | *0.003 |
| 00671 | Orthophosphate, wat., filt., mg/L as phosphorus | 108 | 0.060 | -- | 0.009* | *0.031 | *0.010 | *0.005 | *0.002 | *0.001 |
| 70507 | Orthophosphate, wat., unf., mg/L as phosphorus | 31 | 0.200 | -- | 0.026* | *0.137 | *0.030 | *0.015 | *0.006 | *0.002 |
| 00665 | Phosphorus, wat., unf., mg/L | 107 | 0.210 | -- | 0.043* | *0.127 | *0.043 | *0.030 | *0.024 | *0.010 |
| 00681 | Organic carbon, wat., filt., mg/L | 1 | 4.000 | -- | -- | -- | -- | -- | -- | -- |
| 00689 | Organic carbon, suspended sediment, total, mg/L | 1 | 0.200 | -- | -- | -- | -- | -- | -- | -- |
| 00680 | Organic carbon, wat., unf., mg/L | 108 | 15.000 | 2.700 | 5.722 | 11.000 | 6.600 | 4.900 | 4.200 | 3.200 |
| 31625 | Fecal coliform, M-FC MF (0.7 micron) method, wat., colonies per 100 milliliters | 1 | 270.000 | -- | -- | -- | -- | -- | -- | -- |
| 01105 | Aluminum, wat., unf., recoverable, ug/L | 39 | 2100.000 | 50.000 | 418.451 | 1500.000 | 540.000 | 230.000 | 110.000 | 50.600 |
| 01002 | Arsenic, wat., unf., ug/L | 40 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01027 | Cadmium, wat., unf., ug/L | 40 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01034 | Chromium, wat., unf., recoverable, ug/L | 40 | 8.000 | -- | 1.119* | *3.950 | *1.000 | *0.733 | *0.375 | *0.145 |
| 01037 | Cobalt, wat., unf., recoverable, ug/L | 40 | 3.000 | -- | 0.839* | *3.000 | *1.000 | *0.578 | *0.326 | *0.133 |
| 01042 | Copper, wat., unf., recoverable, ug/L | 40 | 9.000 | -- | 2.725* | *7.000 | *4.000 | *2.000 | *1.000 | *0.574 |
| 01046 | Iron, wat., filt., ug/L | 1 | 270.000 | -- | -- | -- | -- | -- | -- | -- |
| 01045 | Iron, wat., unf., recoverable, ug/L | 40 | 3600.000 | 80.000 | 1233.425 | 3190.000 | 1400.000 | 930.000 | 792.500 | 394.000 |
| 01051 | Lead, wat., unf., recoverable, ug/L | 40 | 5.000 | -- | 1.604* | *5.000 | *2.000 | *1.000 | *0.592 | *0.237 |
| 01056 | Manganese, wat., filt., ug/L | 1 | 190.000 | -- | -- | -- | -- | -- | -- | -- |
| 01055 | Manganese, wat., unf., recoverable, ug/L | 40 | 590.000 | 50.000 | 180.682 | 465.900 | 232.000 | 150.000 | 104.000 | 60.500 |
| 71900 | Mercury, wat., unf., recoverable, ug/L | 39 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01062 | Molybdenum, wat., unf., recoverable, ug/L | 40 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01067 | Nickel, wat., unf., recoverable, ug/L | 40 | 7.000 | -- | 1.031* | *2.950 | *1.000 | *0.634 | *0.350 | *0.143 |
| 01147 | Selenium, wat., unf., ug/L | 40 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01077 | Silver, wat., unf., recoverable, ug/L | 40 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01092 | Zinc, wat., unf., recoverable, ug/L | 40 | 50.000 | -- | 5.606* | *20.000 | *6.160 | *2.660 | *1.233 | *0.372 |
| 80154 | Suspended sediment concentration, mg/L | 105 | 660.000 | 1.000 | 27.348 | 88.610 | 20.000 | 10.000 | 6.000 | 3.300 |
| 02085070 Eno River near Durham (October 1988–April 1995) |
| 00061 | Discharge, instantaneous, cubic feet per second | 18 | 411.000 | 4.100 | 101.900 | 411.000 | 145.000 | 30.500 | 12.750 | 4.100 |
| 00080 | Color, wat., filt., platinum cobalt units | 2 | 150.000 | 23.000 | -- | -- | -- | -- | -- | -- |
| 00300 | Dissolved oxygen, wat., unf., mg/L | 19 | 12.800 | 6.200 | 9.442 | 12.800 | 10.400 | 9.600 | 8.000 | 6.200 |
| 00301 | Dissolved oxygen, wat., unf., percent of saturation | 2 | 101.000 | 90.000 | -- | -- | -- | -- | -- | -- |
| 00400 | pH, wat., unf., field, standard units | 19 | 7.500 | 6.100 | 7.125 | 7.500 | 7.420 | 7.200 | 7.000 | 6.100 |
| 00403 | pH, wat., unf., laboratory, standard units | 2 | 7.900 | 7.200 | -- | -- | -- | -- | -- | -- |
| 90095 | Specific conductance, wat., unf., laboratory, microsiemens per centimeter at 25 degrees Celsius | 2 | 277.000 | 80.000 | -- | -- | -- | -- | -- | -- |
| 00095 | Specific conductance, wat., unf., microsiemens per centimeter at 25 degrees Celsius | 19 | 540.000 | 58.000 | 167.947 | 540.000 | 173.000 | 128.000 | 85.000 | 58.000 |
| 00900 | Hardness, wat., unf., mg/L as calcium carbonate | 2 | 33.000 | 22.000 | -- | -- | -- | -- | -- | -- |
| 00915 | Calcium, wat., filt., mg/L | 2 | 7.800 | 5.300 | -- | -- | -- | -- | -- | -- |
| 00925 | Magnesium, wat., filt., mg/L | 2 | 3.200 | 2.200 | -- | -- | -- | -- | -- | -- |
| 00935 | Potassium, wat., filt., mg/L | 2 | 3.000 | 2.000 | -- | -- | -- | -- | -- | -- |
| 00931 | Sodium adsorption ratio, wat., number | 2 | 3.000 | 0.500 | -- | -- | -- | -- | -- | -- |
| 00930 | Sodium, wat., filt., mg/L | 2 | 38.000 | 5.300 | -- | -- | -- | -- | -- | -- |
| 00932 | Sodium, wat., percent in equivalents of major cations | 2 | 69.000 | 32.000 | -- | -- | -- | -- | -- | -- |
| 00431 | Acid neutralizing capacity, wat., unf., mg/L as calcium carbonate | 7 | 41.000 | 23.000 | 31.000 | 41.000 | 35.000 | 29.000 | 28.000 | 23.000 |
| 99430 | Carbonate, wat., unf., incremental titration, field, mg/L as calcium carbonate | 1 | 25.000 | -- | -- | -- | -- | -- | -- | -- |
| 90410 | Acid neutralizing capacity, wat., unf., fixed endpoint (pH 4.5) titration, laboratory, mg/L as calcium carbonate | 2 | 43.000 | 18.000 | -- | -- | -- | -- | -- | -- |
| 00410 | Acid neutralizing capacity, wat., unf., fixed endpoint (pH 4.5) titration, field, mg/L as calcium carbonate | 1 | 25.000 | -- | -- | -- | -- | -- | -- | -- |
| 99440 | Bicarbonate, wat., unf., incremental titration, field, mg/L | 1 | 31.000 | -- | -- | -- | -- | -- | -- | -- |
| 99445 | Carbonate, wat., unf., incremental titration, field, mg/L | 1 | 0.000 | -- | -- | -- | -- | -- | -- | -- |
| 00940 | Chloride, wat., filt., mg/L | 2 | 7.800 | 5.700 | -- | -- | -- | -- | -- | -- |
| 00950 | Fluoride, wat., filt., mg/L | 2 | -- | -- | -- | -- | -- | -- | -- | -- |
| 00955 | Silica, wat., filt., mg/L | 2 | 14.000 | 8.900 | -- | -- | -- | -- | -- | -- |
| 00945 | Sulfate, wat., filt., mg/L | 2 | 60.000 | 8.300 | -- | -- | -- | -- | -- | -- |
| 00530 | Residue, total nonfilterable, mg/L | 1 | 7.000 | -- | -- | -- | -- | -- | -- | -- |
| 70300 | Residue on evaporation, dried at 180 degrees Celsius, wat., filt., mg/L | 2 | 160.000 | 61.000 | -- | -- | -- | -- | -- | -- |
| 00500 | Residue on evaporation, dried at 105 degrees Celsius, wat., unf., mg/L | 1 | 150.000 | -- | -- | -- | -- | -- | -- | -- |
| 00625 | Ammonia plus organic nitrogen, wat., unf., mg/L as nitrogen | 1 | 0.500 | -- | -- | -- | -- | -- | -- | -- |
| 00665 | Phosphorus, wat., unf., mg/L | 1 | 0.100 | -- | -- | -- | -- | -- | -- | -- |
| 00680 | Organic carbon, wat., unf., mg/L | 1 | 12.000 | -- | -- | -- | -- | -- | -- | -- |
| 01105 | Aluminum, wat., unf., recoverable, ug/L | 1 | 940.000 | -- | -- | -- | -- | -- | -- | -- |
| 01002 | Arsenic, wat., unf., ug/L | 1 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01027 | Cadmium, wat., unf., ug/L | 1 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01034 | Chromium, wat., unf., recoverable, ug/L | 1 | 18.000 | -- | -- | -- | -- | -- | -- | -- |
| 01037 | Cobalt, wat., unf., recoverable, ug/L | 1 | 1.000 | -- | -- | -- | -- | -- | -- | -- |
| 01042 | Copper, wat., unf., recoverable, ug/L | 1 | 3.000 | -- | -- | -- | -- | -- | -- | -- |
| 01045 | Iron, wat., unf., recoverable, ug/L | 1 | 1800.000 | -- | -- | -- | -- | -- | -- | -- |
| 01051 | Lead, wat., unf., recoverable, ug/L | 1 | 2.000 | -- | -- | -- | -- | -- | -- | -- |
| 01055 | Manganese, wat., unf., recoverable, ug/L | 1 | 110.000 | -- | -- | -- | -- | -- | -- | -- |
| 71900 | Mercury, wat., unf., recoverable, ug/L | 1 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01062 | Molybdenum, wat., unf., recoverable, ug/L | 1 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01067 | Nickel, wat., unf., recoverable, ug/L | 1 | 2.000 | -- | -- | -- | -- | -- | -- | -- |
| 01147 | Selenium, wat., unf., ug/L | 1 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01077 | Silver, wat., unf., recoverable, ug/L | 1 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01092 | Zinc, wat., unf., recoverable, ug/L | 1 | -- | -- | -- | -- | -- | -- | -- | -- |
| 80154 | Suspended sediment concentration, mg/L | 2 | 59.000 | 6.000 | -- | -- | -- | -- | -- | -- |
| 02085079 Eno River near Weaver (October 1988–August 1999) |
| 00060 | Discharge, cubic feet per second | 1 | 275.000 | -- | -- | -- | -- | -- | -- | -- |
| 00061 | Discharge, instantaneous, cubic feet per second | 110 | 4200.000 | 2.900 | 148.595 | 449.800 | 114.000 | 60.500 | 22.000 | 4.755 |
| 00080 | Color, wat., filt., platinum cobalt units | 109 | 250.000 | 12.000 | 62.468 | 165.000 | 80.000 | 50.000 | 34.000 | 15.500 |
| 00300 | Dissolved oxygen, wat., unf., mg/L | 106 | 15.800 | 5.300 | 9.133 | 13.165 | 11.125 | 8.950 | 6.900 | 5.600 |
| 00301 | Dissolved oxygen, wat., unf., percent of saturation | 103 | 143.000 | 55.000 | 89.117 | 104.000 | 97.000 | 92.000 | 80.000 | 67.200 |
| 00400 | pH, wat., unf., field, standard units | 111 | 7.600 | 5.900 | 7.091 | 7.504 | 7.300 | 7.140 | 6.940 | 6.460 |
| 00403 | pH, wat., unf., laboratory, standard units | 109 | 8.000 | 6.800 | 7.371 | 7.800 | 7.500 | 7.400 | 7.200 | 6.900 |
| 90095 | Specific conductance, wat., unf., laboratory, microsiemens per centimeter at 25 degrees Celsius | 109 | 701.000 | 64.000 | 213.927 | 497.000 | 247.500 | 168.000 | 119.000 | 92.500 |
| 00095 | Specific conductance, wat., unf., microsiemens per centimeter at 25 degrees Celsius | 108 | 700.000 | 60.000 | 209.204 | 497.050 | 257.500 | 161.000 | 111.250 | 86.900 |
| 00900 | Hardness, wat., unf., mg/L as calcium carbonate | 109 | 86.000 | 18.000 | 36.229 | 65.000 | 40.000 | 34.000 | 28.000 | 24.000 |
| 00915 | Calcium, wat., filt., mg/L | 109 | 26.000 | 4.400 | 9.175 | 19.000 | 10.000 | 8.200 | 6.700 | 5.700 |
| 00925 | Magnesium, wat., filt., mg/L | 109 | 5.100 | 1.700 | 3.225 | 4.850 | 3.700 | 3.100 | 2.650 | 2.300 |
| 00935 | Potassium, wat., filt., mg/L | 109 | 9.600 | 0.100 | 3.028 | 6.500 | 3.800 | 2.600 | 1.750 | 1.500 |
| 00931 | Sodium adsorption ratio, wat., number | 109 | 8.000 | 0.400 | 1.783 | 4.500 | 2.000 | 1.000 | 0.800 | 0.550 |
| 00930 | Sodium, wat., filt., mg/L | 109 | 120.000 | 4.000 | 25.997 | 77.500 | 30.000 | 18.000 | 10.000 | 6.250 |
| 00932 | Sodium, wat., percent in equivalents of major cations | 108 | 83.000 | 29.000 | 52.000 | 72.550 | 58.000 | 52.500 | 42.250 | 34.450 |
| 99430 | Carbonate, wat., unf., incremental titration, field, mg/L as calcium carbonate | 51 | 58.000 | 17.000 | 33.137 | 51.200 | 43.000 | 30.000 | 23.000 | 19.800 |
| 90410 | Acid neutralizing capacity, wat., unf., fixed endpoint (pH 4.5) titration, laboratory, mg/L as calcium carbonate | 109 | 61.000 | 12.000 | 33.514 | 53.000 | 40.500 | 32.000 | 24.500 | 20.500 |
| 39086 | Alkalinity, wat., filt., incremental titration, field, mg/L as calcium carbonate | 1 | 53.000 | -- | -- | -- | -- | -- | -- | -- |
| 00410 | Acid neutralizing capacity, wat., unf., fixed endpoint (pH 4.5) titration, field, mg/L as calcium carbonate | 54 | 61.000 | 17.000 | 34.019 | 58.500 | 43.250 | 29.500 | 24.000 | 20.000 |

| NWIS Param-eter code | Constituent name | Sample size | Maximum | Minimum | Mean | Percentile |
| --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  | 95th | 75th | 50th | 25th | 5th |
| 00419 | Acid neutralizing capacity, wat., unf., incremental titration, field, mg/L as calcium carbonate | 5 | 61.000 | 21.000 | -- | -- | -- | -- | -- | -- |
| 99440 | Bicarbonate, wat., unf., incremental titration, field, mg/L | 56 | 74.000 | 21.000 | 40.839 | 65.900 | 53.500 | 36.000 | 27.250 | 24.550 |
| 99445 | Carbonate, wat., unf., incremental titration, field, mg/L | 12 | 0.000 | -- | -- | -- | -- | -- | -- | -- |
| 00452 | Carbonate, wat., filt., incremental titration, field, mg/L | 1 | 0.000 | -- | -- | -- | -- | -- | -- | -- |
| 00940 | Chloride, wat., filt., mg/L | 105 | 54.000 | 4.000 | 13.477 | 42.200 | 14.000 | 9.500 | 7.700 | 5.490 |
| 00950 | Fluoride, wat., filt., mg/L | 105 | 0.500 | -- | 0.145* | *0.400 | *0.200 | *0.100 | *0.074 | *0.039 |
| 00955 | Silica, wat., filt., mg/L | 105 | 14.000 | 1.000 | 9.645 | 13.000 | 12.000 | 10.000 | 7.900 | 2.830 |
| 00945 | Sulfate, wat., filt., mg/L | 105 | 240.000 | 5.300 | 38.817 | 127.000 | 42.000 | 25.000 | 14.500 | 8.350 |
| 99890 | Sulfate, wat., filt., uncorrected, mg/L | 7 | -- | -- | -- | -- | -- | -- | -- | -- |
| 70300 | Residue on evaporation, dried at 180 degrees Celsius, wat., filt., mg/L | 104 | 484.000 | 40.000 | 131.808 | 285.500 | 167.250 | 101.000 | 78.500 | 54.500 |
| 00608 | Ammonia, wat., filt., mg/L as nitrogen | 106 | 0.220 | -- | 0.050* | *0.127 | *0.070 | *0.040 | *0.020 | *0.006 |
| 00623 | Ammonia plus organic nitrogen, wat., filt., mg/L as nitrogen | 84 | 1.400 | 0.200 | 0.444 | 0.875 | 0.500 | 0.400 | 0.300 | 0.200 |
| 00625 | Ammonia plus organic nitrogen, wat., unf., mg/L as nitrogen | 110 | 1.900 | 0.200 | 0.491 | 0.890 | 0.600 | 0.400 | 0.375 | 0.255 |
| 00610 | Ammonia, wat., unf., mg/L as nitrogen | 48 | 0.120 | 0.000 | 0.051 | 0.115 | 0.070 | 0.050 | 0.030 | 0.005 |
| 00620 | Nitrate, wat., unf., mg/L as nitrogen | 41 | 9.080 | 0.270 | 1.371 | 3.069 | 1.780 | 0.970 | 0.585 | 0.381 |
| 00631 | Nitrite plus nitrate, wat., filt., mg/L as nitrogen | 106 | 9.200 | 0.005 | 1.015 | 3.000 | 1.100 | 0.605 | 0.377 | 0.120 |
| 00630 | Nitrite plus nitrate, wat., unf., mg/L as nitrogen | 48 | 9.100 | 0.230 | 1.256 | 3.055 | 1.700 | 0.830 | 0.500 | 0.300 |
| 00613 | Nitrite, wat., filt., mg/L as nitrogen | 82 | 0.120 | -- | 0.017* | *0.060 | *0.020 | *0.007 | *0.002 | *0.001 |
| 00615 | Nitrite, wat., unf., mg/L as nitrogen | 48 | 0.110 | -- | 0.023* | *0.090 | *0.030 | *0.020 | *0.010 | *0.005 |
| 00605 | Organic nitrogen, wat., unf., mg/L | 93 | 1.900 | 0.160 | 0.461 | 0.923 | 0.525 | 0.390 | 0.330 | 0.230 |
| 00666 | Phosphorus, wat., filt., mg/L | 89 | 1.000 | -- | 0.056* | *0.136 | *0.060 | *0.030 | *0.020 | *0.007 |
| 00671 | Orthophosphate, wat., filt., mg/L as phosphorus | 106 | 0.880 | -- | 0.040* | *0.110 | *0.040 | *0.020 | *0.010 | *0.003 |
| 70507 | Orthophosphate, wat., unf., mg/L as phosphorus | 48 | 0.950 | 0.000 | 0.072 | 0.153 | 0.070 | 0.050 | 0.030 | 0.005 |
| 00665 | Phosphorus, wat., unf., mg/L | 109 | 1.100 | 0.000 | 0.080 | 0.165 | 0.090 | 0.060 | 0.040 | 0.010 |
| 00680 | Organic carbon, wat., unf., mg/L | 109 | 22.000 | 3.300 | 6.351 | 11.500 | 6.800 | 5.800 | 4.800 | 3.800 |
| 01105 | Aluminum, wat., unf., recoverable, ug/L | 43 | 4000.000 | 70.000 | 597.093 | 2680.000 | 630.000 | 340.000 | 170.000 | 82.000 |
| 01002 | Arsenic, wat., unf., ug/L | 43 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01027 | Cadmium, wat., unf., ug/L | 43 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01034 | Chromium, wat., unf., recoverable, ug/L | 43 | 6.000 | -- | 1.162* | *5.600 | *1.000 | *0.542 | *0.221 | *0.060 |
| 01037 | Cobalt, wat., unf., recoverable, ug/L | 43 | 7.000 | -- | 0.820* | *3.000 | *1.000 | *0.379 | *0.156 | *0.043 |
| 01042 | Copper, wat., unf., recoverable, ug/L | 43 | 15.000 | 1.000 | 3.767 | 11.400 | 4.000 | 3.000 | 2.000 | 1.200 |
| 01045 | Iron, wat., unf., recoverable, ug/L | 43 | 6300.000 | 160.000 | 1149.977 | 3960.000 | 1200.000 | 790.000 | 590.000 | 234.000 |
| 01051 | Lead, wat., unf., recoverable, ug/L | 43 | 12.000 | -- | 2.061* | *9.400 | *3.000 | *1.000 | *0.458 | *0.134 |
| 01055 | Manganese, wat., unf., recoverable, ug/L | 43 | 860.000 | 40.000 | 120.505 | 448.000 | 120.000 | 80.000 | 60.000 | 50.000 |
| 71900 | Mercury, wat., unf., recoverable, ug/L | 43 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01062 | Molybdenum, wat., unf., recoverable, ug/L | 43 | 6.000 | -- | 0.875* | *5.800 | *1.000 | *0.337 | *0.125 | *0.030 |
| 01067 | Nickel, wat., unf., recoverable, ug/L | 43 | 6.000 | -- | 1.848* | *5.800 | *2.000 | *1.000 | *0.745 | *0.333 |
| 01147 | Selenium, wat., unf., ug/L | 43 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01077 | Silver, wat., unf., recoverable, ug/L | 42 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01092 | Zinc, wat., unf., recoverable, ug/L | 43 | 40.000 | -- | 12.991* | *30.000 | *20.000 | *10.000 | *6.128 | *2.979 |
| 80154 | Suspended sediment concentration, mg/L | 104 | 652.000 | 1.000 | 35.058 | 141.750 | 27.500 | 15.500 | 7.250 | 2.250 |
| 0208521324 Little River at SR 1461 near Orange Factory (October 1988–March 2001) |
| 00061 | Discharge, instantaneous, cubic feet per second | 43 | 4900.000 | 0.080 | 350.994 | 2364.000 | 258.000 | 26.000 | 7.600 | 0.748 |
| 00080 | Color, wat., filt., platinum cobalt units | 18 | 180.000 | 13.000 | 87.833 | 180.000 | 162.500 | 80.000 | 30.250 | 13.000 |
| 00300 | Dissolved oxygen, wat., unf., mg/L | 40 | 16.400 | 5.800 | 9.892 | 13.295 | 10.800 | 9.900 | 8.900 | 6.025 |
| 00301 | Dissolved oxygen, wat., unf., percent of saturation | 23 | 129.000 | 77.000 | 100.739 | 128.000 | 106.000 | 100.000 | 93.000 | 77.400 |
| 00400 | pH, wat., unf., field, standard units | 43 | 8.100 | 6.100 | 6.973 | 7.958 | 7.230 | 6.900 | 6.700 | 6.312 |
| 00403 | pH, wat., unf., laboratory, standard units | 21 | 8.200 | 6.500 | 7.352 | 8.190 | 7.650 | 7.300 | 6.950 | 6.510 |
| 90095 | Specific conductance, wat., unf., laboratory, microsiemens per centimeter at 25 degrees Celsius | 21 | 114.000 | 41.000 | 76.619 | 113.900 | 93.500 | 74.000 | 61.000 | 41.800 |
| 00095 | Specific conductance, wat., unf., microsiemens per centimeter at 25 degrees Celsius | 43 | 115.000 | 44.600 | 74.360 | 104.000 | 89.000 | 75.000 | 60.000 | 45.340 |
| 00900 | Hardness, wat., unf., mg/L as calcium carbonate | 27 | 39.000 | 11.000 | 24.185 | 39.000 | 31.000 | 22.000 | 19.000 | 12.200 |
| 00915 | Calcium, wat., filt., mg/L | 27 | 9.400 | 2.600 | 5.733 | 9.320 | 7.300 | 5.000 | 4.100 | 2.840 |
| 00925 | Magnesium, wat., filt., mg/L | 27 | 3.800 | 1.100 | 2.381 | 3.800 | 2.900 | 2.300 | 1.900 | 1.180 |
| 00935 | Potassium, wat., filt., mg/L | 27 | 4.500 | 1.000 | 1.959 | 4.220 | 2.300 | 1.600 | 1.200 | 1.000 |
| 00931 | Sodium adsorption ratio, wat., number | 27 | 0.500 | 0.200 | 0.344 | 0.460 | 0.400 | 0.400 | 0.300 | 0.200 |
| 00930 | Sodium, wat., filt., mg/L | 27 | 6.500 | 1.500 | 4.115 | 6.260 | 5.400 | 4.300 | 2.900 | 1.660 |
| 00932 | Sodium, wat., percent in equivalents of major cations | 27 | 32.000 | 18.000 | 24.926 | 31.600 | 29.000 | 25.000 | 20.000 | 18.000 |
| 99430 | Carbonate, wat., unf., incremental titration, field, mg/L as calcium carbonate | 2 | 12.000 | 12.000 | -- | -- | -- | -- | -- | -- |
| 90410 | Acid neutralizing capacity, wat., unf., fixed endpoint (pH 4.5) titration, laboratory, mg/L as calcium carbonate | 21 | 47.000 | 6.400 | 24.257 | 47.000 | 33.500 | 23.000 | 16.000 | 6.660 |
| 00410 | Acid neutralizing capacity, wat., unf., fixed endpoint (pH 4.5) titration, field, mg/L as calcium carbonate | 3 | 15.000 | 10.000 | -- | -- | -- | -- | -- | -- |
| 00419 | Acid neutralizing capacity, wat., unf., incremental titration, field, mg/L as calcium carbonate | 2 | 15.000 | 5.000 | -- | -- | -- | -- | -- | -- |
| 99440 | Bicarbonate, wat., unf., incremental titration, field, mg/L | 4 | 18.000 | 6.300 | -- | -- | -- | -- | -- | -- |

| NWIS Param-eter code | Constituent name | Sample size | Maximum | Minimum | Mean | Percentile |
| --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  | 95th | 75th | 50th | 25th | 5th |
| 99445 | Carbonate, wat., unf., incremental titration, field, mg/L | 2 | 0.000 | -- | -- | -- | -- | -- | -- | -- |
| 00940 | Chloride, wat., filt., mg/L | 25 | 6.300 | 2.400 | 4.504 | 6.270 | 5.300 | 4.500 | 3.850 | 2.430 |
| 00950 | Fluoride, wat., filt., mg/L | 25 | 0.300 | -- | 0.079* | *0.270 | *0.100 | *0.056 | *0.035 | *0.016 |
| 00955 | Silica, wat., filt., mg/L | 17 | 17.000 | 5.000 | 10.271 | 17.000 | 14.000 | 9.500 | 7.400 | 5.000 |
| 00945 | Sulfate, wat., filt., mg/L | 25 | 11.000 | 1.400 | 4.268 | 9.800 | 5.500 | 4.000 | 2.500 | 1.490 |
| 99890 | Sulfate, wat., filt., uncorrected, mg/L | 4 | -- | -- | -- | -- | -- | -- | -- | -- |
| 70300 | Residue on evaporation, dried at 180 degrees Celsius, wat., filt., mg/L | 20 | 74.000 | 37.000 | 56.700 | 73.600 | 62.500 | 59.000 | 49.250 | 37.350 |
| 00608 | Ammonia, wat., filt., mg/L as nitrogen | 8 | 0.128 | 0.005 | 0.033 | 0.128 | 0.036 | 0.020 | 0.012 | 0.005 |
| 00623 | Ammonia plus organic nitrogen, wat., filt., mg/L as nitrogen | 1 | 0.300 | -- | -- | -- | -- | -- | -- | -- |
| 00625 | Ammonia plus organic nitrogen, wat., unf., mg/L as nitrogen | 27 | 1.300 | 0.200 | 0.600 | 1.300 | 0.800 | 0.500 | 0.300 | 0.200 |
| 00610 | Ammonia, wat., unf., mg/L as nitrogen | 19 | 0.160 | -- | 0.040* | *0.160 | *0.050 | *0.030 | *0.020 | *0.005 |
| 00620 | Nitrate, wat., unf., mg/L as nitrogen | 1 | 0.210 | -- | -- | -- | -- | -- | -- | -- |
| 00631 | Nitrite plus nitrate, wat., filt., mg/L as nitrogen | 8 | 0.440 | 0.059 | 0.237 | 0.440 | 0.380 | 0.200 | 0.130 | 0.059 |
| 00630 | Nitrite plus nitrate, wat., unf., mg/L as nitrogen | 19 | 0.700 | -- | 0.337* | *0.700 | *0.400 | *0.300 | *0.220 | *0.100 |
| 00613 | Nitrite, wat., filt., mg/L as nitrogen | 5 | -- | -- | -- | -- | -- | -- | -- | -- |
| 00615 | Nitrite, wat., unf., mg/L as nitrogen | 4 | -- | -- | -- | -- | -- | -- | -- | -- |
| 00605 | Organic nitrogen, wat., unf., mg/L | 24 | 1.300 | 0.180 | 0.582 | 1.275 | 0.767 | 0.550 | 0.305 | 0.180 |
| 00666 | Phosphorus, wat., filt., mg/L | 1 | 0.040 | -- | -- | -- | -- | -- | -- | -- |
| 00671 | Orthophosphate, wat., filt., mg/L as phosphorus | 5 | 0.039 | 0.008 | -- | -- | -- | -- | -- | -- |
| 70507 | Orthophosphate, wat., unf., mg/L as phosphorus | 19 | 0.110 | -- | 0.034* | *0.110 | *0.040 | *0.030 | *0.010 | *0.004 |
| 00665 | Phosphorus, wat., unf., mg/L | 27 | 0.250 | 0.010 | 0.080 | 0.242 | 0.090 | 0.040 | 0.030 | 0.014 |
| 00680 | Organic carbon, wat., unf., mg/L | 24 | 38.000 | 3.000 | 10.692 | 33.750 | 14.750 | 8.750 | 4.675 | 3.175 |
| 01105 | Aluminum, wat., unf., recoverable, ug/L | 17 | 4000.000 | 50.000 | 1087.765 | 4000.000 | 1485.000 | 612.000 | 125.000 | 50.000 |
| 01002 | Arsenic, wat., unf., ug/L | 23 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01027 | Cadmium, wat., unf., ug/L | 26 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01034 | Chromium, wat., unf., recoverable, ug/L | 26 | 130.000 | -- | 6.062* | *85.900 | *2.499 | *0.401 | *0.095 | *0.012 |
| 01037 | Cobalt, wat., unf., recoverable, ug/L | 17 | 2.000 | -- | 1.059* | *2.000 | *1.000 | *1.000 | *0.714 | *0.486 |
| 01042 | Copper, wat., unf., recoverable, ug/L | 26 | 39.000 | -- | 5.330* | *38.650 | *4.250 | *2.109 | *1.000 | *0.343 |
| 01045 | Iron, wat., unf., recoverable, ug/L | 26 | 6700.000 | 360.000 | 1878.462 | 6700.000 | 2320.000 | 1350.000 | 785.000 | 360.000 |
| 01051 | Lead, wat., unf., recoverable, ug/L | 26 | 14.000 | -- | 2.096* | *10.500 | *3.000 | *1.623 | *0.693 | *0.292 |
| 01055 | Manganese, wat., unf., recoverable, ug/L | 26 | 1100.000 | 20.000 | 178.923 | 928.500 | 273.250 | 70.000 | 37.500 | 20.000 |
| 71900 | Mercury, wat., unf., recoverable, ug/L | 26 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01062 | Molybdenum, wat., unf., recoverable, ug/L | 17 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01067 | Nickel, wat., unf., recoverable, ug/L | 24 | 3.000 | -- | 1.285* | *2.750 | *2.000 | *1.000 | *0.798 | *0.465 |
| 01147 | Selenium, wat., unf., ug/L | 17 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01077 | Silver, wat., unf., recoverable, ug/L | 24 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01092 | Zinc, wat., unf., recoverable, ug/L | 26 | 30.000 | -- | 10.751* | *28.670 | *16.033 | *8.642 | *5.222 | *2.508 |
| 80154 | Suspended sediment concentration, mg/L | 25 | 476.000 | 2.000 | 87.360 | 422.600 | 159.500 | 28.000 | 5.000 | 2.000 |
| 0208524845 Little River Reservoir at dam near Bahama (October 1988–August 2001) |
| 00080 | Color, wat., filt., platinum cobalt units | 57 | 120.000 | 10.000 | 39.088 | 101.000 | 50.000 | 30.000 | 22.500 | 12.900 |
| 00078 | Transparency, wat., unf., Secchi disc, meters | 38 | 1.900 | 0.550 | 0.929 | 1.282 | 1.013 | 0.900 | 0.750 | 0.550 |
| 00300 | Dissolved oxygen, wat., unf., mg/L | 73 | 12.000 | 0.090 | 5.384 | 9.119 | 7.640 | 5.320 | 3.740 | 0.188 |
| 00301 | Dissolved oxygen, wat., unf., percent of saturation | 73 | 116.000 | 0.000 | 60.959 | 109.900 | 87.500 | 64.000 | 43.500 | 2.000 |
| 00400 | pH, wat., unf., field, standard units | 75 | 8.440 | 6.100 | 6.781 | 7.626 | 7.000 | 6.780 | 6.500 | 6.120 |
| 00403 | pH, wat., unf., laboratory, standard units | 58 | 8.200 | 6.500 | 7.267 | 7.910 | 7.500 | 7.200 | 7.000 | 6.790 |
| 90095 | Specific conductance, wat., unf., laboratory, microsiemens per centimeter at 25 degrees Celsius | 58 | 91.000 | 56.000 | 72.483 | 89.000 | 77.000 | 74.000 | 66.750 | 56.950 |
| 00095 | Specific conductance, wat., unf., microsiemens per centimeter at 25 degrees Celsius | 75 | 242.000 | 48.000 | 80.607 | 194.600 | 80.000 | 72.000 | 66.000 | 54.800 |
| 00900 | Hardness, wat., unf., mg/L as calcium carbonate | 58 | 31.000 | 17.000 | 22.966 | 28.150 | 25.000 | 23.000 | 21.000 | 18.000 |
| 00915 | Calcium, wat., filt., mg/L | 58 | 8.200 | 4.100 | 5.572 | 7.030 | 6.100 | 5.500 | 5.000 | 4.200 |
| 00925 | Magnesium, wat., filt., mg/L | 58 | 3.000 | 1.700 | 2.198 | 2.600 | 2.400 | 2.200 | 2.000 | 1.700 |
| 00935 | Potassium, wat., filt., mg/L | 58 | 2.600 | 1.200 | 1.831 | 2.600 | 2.000 | 1.800 | 1.600 | 1.300 |
| 00931 | Sodium adsorption ratio, wat., number | 58 | 0.400 | 0.200 | 0.355 | 0.400 | 0.400 | 0.400 | 0.300 | 0.300 |
| 00930 | Sodium, wat., filt., mg/L | 58 | 4.900 | 2.400 | 3.852 | 4.800 | 4.400 | 4.000 | 3.400 | 2.885 |
| 00932 | Sodium, wat., percent in equivalents of major cations | 58 | 30.000 | 20.000 | 24.879 | 28.000 | 27.000 | 25.000 | 23.000 | 20.950 |
| 99430 | Carbonate, wat., unf., incremental titration, field, mg/L as calcium carbonate | 25 | 29.000 | 9.000 | 20.680 | 28.700 | 24.000 | 20.000 | 17.000 | 10.200 |
| 90410 | Acid neutralizing capacity, wat., unf., fixed endpoint (pH 4.5) titration, laboratory, mg/L as calcium carbonate | 58 | 34.000 | 12.000 | 22.517 | 31.050 | 26.000 | 22.000 | 19.000 | 15.850 |
| 00410 | Acid neutralizing capacity, wat., unf., fixed endpoint (pH 4.5) titration, field, mg/L as calcium carbonate | 26 | 28.000 | 11.000 | 21.385 | 28.000 | 25.250 | 22.000 | 17.000 | 11.700 |
| 00419 | Acid neutralizing capacity, wat., unf., incremental titration, field, mg/L as calcium carbonate | 11 | 25.000 | 13.000 | 20.727 | 25.000 | 25.000 | 21.000 | 19.000 | 13.000 |
| 99440 | Bicarbonate, wat., unf., incremental titration, field, mg/L | 36 | 35.000 | 11.000 | 25.181 | 34.150 | 29.750 | 26.000 | 21.500 | 14.400 |

| NWIS Param-eter code | Constituent name | Sample size | Maximum | Minimum | Mean | Percentile |
| --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  | 95th | 75th | 50th | 25th | 5th |
| 99445 | Carbonate, wat., unf., incremental titration, field, mg/L | 9 | 0.000 | -- | -- | -- | -- | -- | -- | -- |
| 00940 | Chloride, wat., filt., mg/L | 57 | 5.900 | 2.900 | 4.460 | 5.510 | 5.000 | 4.600 | 3.950 | 3.300 |
| 00950 | Fluoride, wat., filt., mg/L | 57 | 1.900 | -- | 0.103* | *0.210 | *0.100 | *0.056 | *0.030 | *0.012 |
| 00955 | Silica, wat., filt., mg/L | 56 | 11.000 | 3.800 | 7.695 | 10.000 | 8.700 | 7.950 | 6.800 | 4.710 |
| 00945 | Sulfate, wat., filt., mg/L | 57 | 11.000 | 2.300 | 4.151 | 6.310 | 4.650 | 4.000 | 3.150 | 2.400 |
| 99890 | Sulfate, wat., filt., uncorrected, mg/L | 3 | -- | -- | -- | -- | -- | -- | -- | -- |
| 70300 | Residue on evaporation, dried at 180 degrees Celsius, wat., filt., mg/L | 56 | 88.000 | 10.000 | 51.232 | 67.500 | 58.000 | 52.000 | 45.000 | 31.250 |
| 00608 | Ammonia, wat., filt., mg/L as nitrogen | 64 | 0.754 | -- | 0.114* | *0.362 | *0.150 | *0.076 | *0.030 | *0.006 |
| 00623 | Ammonia plus organic nitrogen, wat., filt., mg/L as nitrogen | 36 | 0.800 | 0.200 | 0.442 | 0.800 | 0.575 | 0.400 | 0.300 | 0.200 |
| 00625 | Ammonia plus organic nitrogen, wat., unf., mg/L as nitrogen | 65 | 7.800 | 0.200 | 0.688 | 1.070 | 0.700 | 0.500 | 0.500 | 0.300 |
| 00610 | Ammonia, wat., unf., mg/L as nitrogen | 17 | 0.360 | 0.010 | 0.126 | 0.360 | 0.170 | 0.120 | 0.035 | 0.010 |
| 00620 | Nitrate, wat., unf., mg/L as nitrogen | 6 | 0.290 | 0.060 | 0.202 | 0.290 | 0.290 | 0.205 | 0.135 | 0.060 |
| 00631 | Nitrite plus nitrate, wat., filt., mg/L as nitrogen | 65 | 0.400 | -- | 0.108* | *0.327 | *0.160 | *0.086 | *0.020 | *0.005 |
| 00630 | Nitrite plus nitrate, wat., unf., mg/L as nitrogen | 17 | 0.340 | -- | 0.137* | *0.340 | *0.220 | *0.100 | *0.052 | *0.029 |
| 00613 | Nitrite, wat., filt., mg/L as nitrogen | 55 | 0.040 | -- | 0.007* | *0.040 | *0.008 | *0.004 | *0.002 | *0.001 |
| 00615 | Nitrite, wat., unf., mg/L as nitrogen | 17 | 0.040 | -- | 0.012* | *0.040 | *0.010 | *0.005 | *0.002 | *0.001 |
| 00605 | Organic nitrogen, wat., unf., mg/L | 60 | 0.750 | 0.190 | 0.458 | 0.736 | 0.560 | 0.455 | 0.370 | 0.240 |
| 00666 | Phosphorus, wat., filt., mg/L | 37 | 0.050 | -- | 0.010* | *0.041 | *0.015 | *0.006 | *0.003 | *0.001 |
| 00671 | Orthophosphate, wat., filt., mg/L as phosphorus | 65 | 0.190 | -- | 0.007* | *0.020 | *0.005 | *0.002 | *0.001 | *0.000 |
| 70507 | Orthophosphate, wat., unf., mg/L as phosphorus | 17 | 0.030 | -- | 0.016* | *0.030 | *0.020 | *0.016 | *0.013 | *0.010 |
| 00665 | Phosphorus, wat., unf., mg/L | 65 | 0.280 | -- | 0.033* | *0.070 | *0.040 | *0.030 | *0.020 | *0.008 |
| 00680 | Organic carbon, wat., unf., mg/L | 58 | 12.000 | 4.700 | 7.355 | 11.000 | 8.225 | 7.100 | 5.950 | 4.995 |
| 70953 | Chlorophyll a, phytoplankton, chromatographic-fluorometric method, ug/L | 58 | 19.500 | 0.100 | 6.060 | 16.555 | 9.300 | 4.250 | 2.500 | 0.485 |
| 70954 | Chlorophyll b, phytoplankton, chromatographic-fluorometric method, ug/L | 58 | 1.300 | -- | 0.374* | *1.015 | *0.500 | *0.300 | *0.169 | *0.091 |
| 01105 | Aluminum, wat., unf., recoverable, ug/L | 45 | 1500.000 | 20.000 | 147.640 | 875.001 | 130.500 | 60.000 | 45.000 | 26.360 |
| 01002 | Arsenic, wat., unf., ug/L | 45 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01027 | Cadmium, wat., unf., ug/L | 45 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01034 | Chromium, wat., unf., recoverable, ug/L | 45 | 9.000 | -- | 0.945* | *4.400 | *0.997 | *0.483 | *0.211 | *0.064 |
| 01037 | Cobalt, wat., unf., recoverable, ug/L | 45 | 1.000 | -- | 1.000* | *1.000 | *1.000 | *1.000 | *1.000 | *1.000 |
| 01042 | Copper, wat., unf., recoverable, ug/L | 44 | 28.000 | -- | 2.214* | *5.000 | *2.000 | *1.000 | *1.000 | *0.341 |
| 01045 | Iron, wat., unf., recoverable, ug/L | 64 | 51000.000 | 72.600 | 1774.634 | 11895.000 | 582.250 | 310.000 | 190.000 | 122.500 |
| 01051 | Lead, wat., unf., recoverable, ug/L | 44 | 7.000 | -- | 0.867* | *3.750 | *1.000 | *0.397 | *0.171 | *0.048 |
| 01055 | Manganese, wat., unf., recoverable, ug/L | 64 | 31500.000 | 19.300 | 1456.783 | 8385.000 | 538.500 | 300.000 | 118.750 | 26.550 |
| 71900 | Mercury, wat., unf., recoverable, ug/L | 45 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01062 | Molybdenum, wat., unf., recoverable, ug/L | 45 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01067 | Nickel, wat., unf., recoverable, ug/L | 43 | 4.000 | -- | 0.972* | *2.000 | *1.000 | *0.816 | *0.540 | *0.307 |
| 01147 | Selenium, wat., unf., ug/L | 45 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01077 | Silver, wat., unf., recoverable, ug/L | 43 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01092 | Zinc, wat., unf., recoverable, ug/L | 45 | 20.000 | -- | 6.358* | *20.000 | *8.609 | *5.142 | *3.215 | *1.656 |
| 0208524850 Little River below dam near Fairntosh (October 1988–June 1991) |
| 00080 | Color, wat., filt., platinum cobalt units | 36 | 160.000 | 13.000 | 47.528 | 117.500 | 63.750 | 37.500 | 22.750 | 13.000 |
| 00300 | Dissolved oxygen, wat., unf., mg/L | 35 | 14.600 | 5.600 | 9.774 | 13.400 | 11.200 | 9.800 | 8.300 | 6.720 |
| 00301 | Dissolved oxygen, wat., unf., percent of saturation | 34 | 122.000 | 68.000 | 101.765 | 119.000 | 108.250 | 102.000 | 95.500 | 83.750 |
| 00400 | pH, wat., unf., field, standard units | 35 | 7.750 | 6.400 | 7.097 | 7.702 | 7.300 | 7.100 | 6.900 | 6.400 |
| 00403 | pH, wat., unf., laboratory, standard units | 36 | 8.000 | 6.900 | 7.558 | 7.915 | 7.700 | 7.550 | 7.400 | 7.240 |
| 90095 | Specific conductance, wat., unf., laboratory, microsiemens per centimeter at 25 degrees Celsius | 36 | 144.000 | 58.000 | 89.806 | 127.850 | 102.750 | 88.500 | 70.250 | 59.700 |
| 00095 | Specific conductance, wat., unf., microsiemens per centimeter at 25 degrees Celsius | 35 | 135.000 | 54.000 | 86.514 | 131.000 | 100.000 | 87.000 | 68.000 | 57.200 |
| 00900 | Hardness, wat., unf., mg/L as calcium carbonate | 36 | 58.000 | 18.000 | 31.389 | 52.050 | 38.500 | 31.500 | 20.250 | 18.000 |
| 00915 | Calcium, wat., filt., mg/L | 36 | 17.000 | 4.300 | 8.528 | 15.300 | 10.750 | 8.650 | 4.900 | 4.385 |
| 00925 | Magnesium, wat., filt., mg/L | 36 | 3.700 | 1.700 | 2.428 | 3.530 | 2.875 | 2.300 | 1.925 | 1.785 |
| 00935 | Potassium, wat., filt., mg/L | 36 | 2.700 | 1.200 | 1.956 | 2.530 | 2.275 | 1.900 | 1.700 | 1.285 |
| 00931 | Sodium adsorption ratio, wat., number | 36 | 0.400 | 0.300 | 0.336 | 0.400 | 0.400 | 0.300 | 0.300 | 0.300 |
| 00930 | Sodium, wat., filt., mg/L | 36 | 6.400 | 3.000 | 4.244 | 5.635 | 4.850 | 4.150 | 3.700 | 3.000 |
| 00932 | Sodium, wat., percent in equivalents of major cations | 36 | 28.000 | 17.000 | 22.306 | 28.000 | 26.000 | 22.000 | 19.000 | 17.850 |
| 90410 | Acid neutralizing capacity, wat., unf., fixed endpoint (pH 4.5) titration, laboratory, mg/L as calcium carbonate | 36 | 58.000 | 13.000 | 30.167 | 52.900 | 36.500 | 29.500 | 20.000 | 15.550 |
| 00940 | Chloride, wat., filt., mg/L | 36 | 6.200 | 3.700 | 4.856 | 6.200 | 5.400 | 4.800 | 4.325 | 3.700 |
| 00950 | Fluoride, wat., filt., mg/L | 36 | 0.300 | -- | 0.105* | *0.215 | *0.100 | *0.100 | *0.063 | *0.037 |
| 00955 | Silica, wat., filt., mg/L | 36 | 12.000 | 2.600 | 8.750 | 12.000 | 10.000 | 8.750 | 8.000 | 3.280 |
| 00945 | Sulfate, wat., filt., mg/L | 35 | 13.000 | 3.000 | 5.717 | 12.200 | 6.700 | 5.200 | 4.000 | 3.160 |
| 99890 | Sulfate, wat., filt., uncorrected, mg/L | 7 | -- | -- | -- | -- | -- | -- | -- | -- |
| 70300 | Residue on evaporation, dried at 180 degrees Celsius, wat., filt., mg/L | 35 | 93.000 | 31.000 | 62.800 | 90.600 | 73.000 | 61.000 | 52.000 | 41.400 |
| 00608 | Ammonia, wat., filt., mg/L as nitrogen | 36 | 0.310 | -- | 0.058* | *0.166 | *0.070 | *0.050 | *0.030 | *0.010 |
| 00623 | Ammonia plus organic nitrogen, wat., filt., mg/L as nitrogen | 34 | 1.100 | 0.300 | 0.562 | 0.950 | 0.600 | 0.500 | 0.400 | 0.300 |
| 00625 | Ammonia plus organic nitrogen, wat., unf., mg/L as nitrogen | 36 | 2.500 | -- | 0.651* | *1.225 | *0.775 | *0.600 | *0.500 | *0.282 |
| 00610 | Ammonia, wat., unf., mg/L as nitrogen | 36 | 0.330 | 0.010 | 0.061 | 0.177 | 0.070 | 0.050 | 0.030 | 0.010 |
| 00620 | Nitrate, wat., unf., mg/L as nitrogen | 18 | 0.390 | 0.080 | 0.235 | 0.390 | 0.280 | 0.265 | 0.180 | 0.080 |
| 00631 | Nitrite plus nitrate, wat., filt., mg/L as nitrogen | 36 | 0.400 | -- | 0.214* | *0.400 | *0.300 | *0.200 | *0.119 | *0.075 |
| 00630 | Nitrite plus nitrate, wat., unf., mg/L as nitrogen | 36 | 0.400 | -- | 0.201* | *0.400 | *0.300 | *0.200 | *0.100 | *0.068 |
| 00613 | Nitrite, wat., filt., mg/L as nitrogen | 11 | -- | -- | -- | -- | -- | -- | -- | -- |
| 00615 | Nitrite, wat., unf., mg/L as nitrogen | 36 | 0.030 | -- | 0.013* | *0.030 | *0.020 | *0.010 | *0.007 | *0.004 |
| 00605 | Organic nitrogen, wat., unf., mg/L | 34 | 2.400 | 0.220 | 0.609 | 1.298 | 0.702 | 0.545 | 0.458 | 0.303 |
| 00666 | Phosphorus, wat., filt., mg/L | 36 | 0.060 | -- | 0.020* | *0.052 | *0.030 | *0.020 | *0.009 | *0.004 |
| 00671 | Orthophosphate, wat., filt., mg/L as phosphorus | 36 | 0.070 | -- | 0.012* | *0.036 | *0.020 | *0.008 | *0.004 | *0.002 |
| 70507 | Orthophosphate, wat., unf., mg/L as phosphorus | 36 | 0.100 | -- | 0.015* | *0.058 | *0.020 | *0.010 | *0.004 | *0.001 |
| 00665 | Phosphorus, wat., unf., mg/L | 36 | 0.130 | 0.010 | 0.043 | 0.113 | 0.050 | 0.040 | 0.020 | 0.010 |
| 00680 | Organic carbon, wat., unf., mg/L | 36 | 9.300 | 5.200 | 6.894 | 9.045 | 7.575 | 6.800 | 6.125 | 5.285 |
| 01105 | Aluminum, wat., unf., recoverable, ug/L | 14 | 940.000 | 20.000 | 197.857 | 940.000 | 147.500 | 120.000 | 57.500 | 20.000 |
| 01002 | Arsenic, wat., unf., ug/L | 14 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01027 | Cadmium, wat., unf., ug/L | 14 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01034 | Chromium, wat., unf., recoverable, ug/L | 14 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01037 | Cobalt, wat., unf., recoverable, ug/L | 14 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01042 | Copper, wat., unf., recoverable, ug/L | 14 | 7.000 | 1.000 | 2.571 | 7.000 | 3.000 | 2.000 | 1.750 | 1.000 |
| 01045 | Iron, wat., unf., recoverable, ug/L | 14 | 1500.000 | 190.000 | 488.571 | 1500.000 | 587.500 | 375.000 | 240.000 | 190.000 |
| 01051 | Lead, wat., unf., recoverable, ug/L | 14 | 7.000 | -- | 1.356* | *7.000 | *1.036 | *1.000 | *0.440 | *0.193 |
| 01055 | Manganese, wat., unf., recoverable, ug/L | 14 | 560.000 | 60.000 | 275.000 | 560.000 | 337.500 | 250.000 | 172.500 | 60.000 |
| 71900 | Mercury, wat., unf., recoverable, ug/L | 14 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01062 | Molybdenum, wat., unf., recoverable, ug/L | 14 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01067 | Nickel, wat., unf., recoverable, ug/L | 14 | 5.000 | -- | 1.596* | *5.000 | *2.250 | *1.000 | *0.548 | *0.253 |
| 01147 | Selenium, wat., unf., ug/L | 14 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01077 | Silver, wat., unf., recoverable, ug/L | 13 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01092 | Zinc, wat., unf., recoverable, ug/L | 14 | -- | -- | -- | -- | -- | -- | -- | -- |
| 80154 | Suspended sediment concentration, mg/L | 25 | 31.000 | 1.000 | 9.880 | 28.300 | 14.000 | 8.000 | 4.500 | 1.300 |
| 02085500 Flat River at Bahama (October 1988–December 1995) |
| 00061 | Discharge, instantaneous, cubic feet per second | 46 | 4280 | 0.9 | 314.617 | 2304.001 | 180 | 65.5 | 23.5 | 1.565 |
| 00080 | Color, wat., filt., platinum cobalt units | 15 | 250 | 25 | 73.8 | 250 | 110 | 50 | 29 | 25 |
| 00300 | Dissolved oxygen, wat., unf., mg/L | 43 | 13.5 | 3.7 | 8.66 | 13.06 | 10.3 | 8.4 | 6.6 | 4.08 |
| 00301 | Dissolved oxygen, wat., unf., percent of saturation | 26 | 109 | 54 | 90 | 107.95 | 99 | 92 | 85.75 | 58.9 |
| 00400 | pH, wat., unf., field, standard units | 45 | 7.9 | 6 | 6.931 | 7.47 | 7.2 | 6.9 | 6.75 | 6.19 |
| 00403 | pH, wat., unf., laboratory, standard units | 18 | 8 | 6.8 | 7.3 | 8 | 7.425 | 7.3 | 7.1 | 6.8 |
| 90095 | Specific conductance, wat., unf., laboratory, microsiemens per centimeter at 25 degrees Celsius | 18 | 99 | 55 | 79.333 | 99 | 90.25 | 82 | 66.75 | 55 |
| 00095 | Specific conductance, wat., unf., microsiemens per centimeter at 25 degrees Celsius | 45 | 101 | 41 | 72.156 | 94 | 84.5 | 70 | 61.5 | 44 |
| 00900 | Hardness, wat., unf., mg/L as calcium carbonate | 24 | 29 | 16 | 22.875 | 28.75 | 27.75 | 23.5 | 18.25 | 16 |
| 00915 | Calcium, wat., filt., mg/L | 24 | 7.3 | 3.6 | 5.319 | 7.15 | 6.2 | 5.5 | 4.155 | 3.65 |
| 00925 | Magnesium, wat., filt., mg/L | 24 | 3.2 | 1.6 | 2.326 | 3.175 | 2.775 | 2.305 | 1.825 | 1.625 |
| 00935 | Potassium, wat., filt., mg/L | 24 | 5.8 | 1.07 | 2.214 | 5.418 | 3.075 | 1.75 | 1.4 | 1.078 |
| 00931 | Sodium adsorption ratio, wat., number | 24 | 0.6 | 0.3 | 0.463 | 0.575 | 0.5 | 0.5 | 0.4 | 0.3 |
| 00930 | Sodium, wat., filt., mg/L | 24 | 6.8 | 2.9 | 5.064 | 6.75 | 5.875 | 5.4 | 4.225 | 2.925 |
| 00932 | Sodium, wat., percent in equivalents of major cations | 24 | 35 | 23 | 30 | 34.75 | 32.75 | 30 | 27.25 | 23.5 |
| 99430 | Carbonate, wat., unf., incremental titration, field, mg/L as calcium carbonate | 6 | 32 | 12 | 19.333 | 32 | 24.5 | 19 | 12 | 12 |
| 90410 | Acid neutralizing capacity, wat., unf., fixed endpoint (pH 4.5) titration, laboratory, mg/L as calcium carbonate | 18 | 35 | 9 | 23.278 | 35 | 31.5 | 23.5 | 14 | 9 |
| 00410 | Acid neutralizing capacity, wat., unf., fixed endpoint (pH 4.5) titration, field, mg/L as calcium carbonate | 5 | 22 | 12 | -- | -- | -- | -- | -- | -- |
| 99440 | Bicarbonate, wat., unf., incremental titration, field, mg/L | 6 | 39 | 14 | 23.5 | 39 | 30 | 23.5 | 14 | 14 |
| 00940 | Chloride, wat., filt., mg/L | 23 | 10 | 0.5 | 5.457 | 9.52 | 6 | 5.6 | 4.5 | 1.04 |
| 00950 | Fluoride, wat., filt., mg/L | 24 | 0.3 | -- | 0.103* | *0.300 | *0.175 | *0.072 | *0.040 | *0.017 |
| 00955 | Silica, wat., filt., mg/L | 15 | 16 | 6.9 | 11.033 | 16 | 14 | 11 | 9 | 6.9 |
| 00945 | Sulfate, wat., filt., mg/L | 23 | 12.5 | 1 | 5.026 | 12 | 6.5 | 4 | 3 | 1.12 |
| 99890 | Sulfate, wat., filt., uncorrected, mg/L | 4 | -- | -- | -- | -- | -- | -- | -- | -- |
| 00530 | Residue, total nonfilterable, mg/L | 1 | 51 | -- | -- | -- | -- | -- | -- | -- |
| 70300 | Residue on evaporation, dried at 180 degrees Celsius, wat., filt., mg/L | 18 | 68 | 46 | 58.167 | 68 | 64.25 | 57.5 | 53.5 | 46 |
| 00608 | Ammonia, wat., filt., mg/L as nitrogen | 9 | 0.1 | -- | 0.041* | *0.100 | *0.065 | *0.030 | *0.016 | *0.009 |
| 00623 | Ammonia plus organic nitrogen, wat., filt., mg/L as nitrogen | 6 | 0.6 | -- | 0.338* | *0.600 | *0.450 | *0.350 | *0.182 | *0.127 |
| 00625 | Ammonia plus organic nitrogen, wat., unf., mg/L as nitrogen | 29 | 1.8 | -- | 0.557* | *1.450 | *0.700 | *0.500 | *0.300 | *0.125 |
| 00610 | Ammonia, wat., unf., mg/L as nitrogen | 20 | 0.14 | -- | 0.051* | *0.139 | *0.090 | *0.040 | *0.020 | *0.007 |
| 00620 | Nitrate, wat., unf., mg/L as nitrogen | 2 | 0.33 | 0.24 | -- | -- | -- | -- | -- | -- |
| 00631 | Nitrite plus nitrate, wat., filt., mg/L as nitrogen | 9 | 0.8 | -- | 0.3* | *0.800 | *0.375 | *0.310 | *0.096 | *0.049 |
| 00630 | Nitrite plus nitrate, wat., unf., mg/L as nitrogen | 20 | 0.6 | -- | 0.321* | *0.590 | *0.400 | *0.320 | *0.200 | *0.155 |
| 00613 | Nitrite, wat., filt., mg/L as nitrogen | 6 | -- | -- | -- | -- | -- | -- | -- | -- |
| 00615 | Nitrite, wat., unf., mg/L as nitrogen | 3 | 0.03 | 0.01 | -- | -- | -- | -- | -- | -- |
| 00605 | Organic nitrogen, wat., unf., mg/L | 23 | 1.8 | 0.17 | 0.572 | 1.66 | 0.86 | 0.5 | 0.27 | 0.172 |
| 00666 | Phosphorus, wat., filt., mg/L | 6 | 0.05 | -- | 0.027* | *0.050 | *0.043 | *0.020 | *0.017 | *0.010 |
| 00671 | Orthophosphate, wat., filt., mg/L as phosphorus | 6 | 0.04 | -- | 0.022* | *0.040 | *0.025 | *0.020 | *0.018 | *0.012 |
| 70507 | Orthophosphate, wat., unf., mg/L as phosphorus | 20 | 0.11 | -- | 0.036* | *0.109 | *0.047 | *0.025 | *0.020 | *0.007 |
| 00665 | Phosphorus, wat., unf., mg/L | 29 | 0.25 | 0.01 | 0.072 | 0.23 | 0.095 | 0.05 | 0.04 | 0.01 |
| 00680 | Organic carbon, wat., unf., mg/L | 21 | 27 | 3.3 | 9.157 | 26.4 | 12 | 6.1 | 5.1 | 3.41 |
| 01105 | Aluminum, wat., unf., recoverable, ug/L | 16 | 4700 | 140 | 1203.75 | 4700 | 1550 | 510 | 240 | 140 |
| 01002 | Arsenic, wat., unf., ug/L | 22 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01027 | Cadmium, wat., unf., ug/L | 25 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01034 | Chromium, wat., unf., recoverable, ug/L | 25 | 30 | -- | 3.175* | *27.000 | *3.000 | *0.611 | *0.150 | *0.024 |
| 01037 | Cobalt, wat., unf., recoverable, ug/L | 16 | 3 | -- | 1.084* | *3.000 | *1.750 | *1.000 | *0.496 | *0.256 |
| 01042 | Copper, wat., unf., recoverable, ug/L | 25 | 80 | -- | 7.502* | *68.000 | *4.288 | *2.954 | *2.000 | *0.493 |
| 01045 | Iron, wat., unf., recoverable, ug/L | 25 | 8300 | 480 | 2320.4 | 8240 | 2825 | 1200 | 925 | 492 |
| 01051 | Lead, wat., unf., recoverable, ug/L | 25 | 8 | -- | 1.968* | *7.500 | *2.298 | *1.085 | *0.860 | *0.302 |
| 01055 | Manganese, wat., unf., recoverable, ug/L | 25 | 860 | 20 | 187.2 | 776 | 245 | 100 | 50 | 20 |
| 71900 | Mercury, wat., unf., recoverable, ug/L | 25 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01062 | Molybdenum, wat., unf., recoverable, ug/L | 16 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01067 | Nickel, wat., unf., recoverable, ug/L | 23 | 3 | -- | 1.509 | *3.000 | *2.000 | *1.110 | *0.807 | *0.466 |
| 01147 | Selenium, wat., unf., ug/L | 16 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01077 | Silver, wat., unf., recoverable, ug/L | 23 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01092 | Zinc, wat., unf., recoverable, ug/L | 25 | 40 | -- | 9.831* | *40.000 | *11.541 | *5.909 | *2.685 | *0.892 |
| 80154 | Suspended sediment concentration, mg/L | 26 | 885 | 4 | 106.423 | 705.45 | 130.25 | 22 | 9.75 | 4.35 |
| 02086490 Lake Michie at dam near Bahama (October 1988–August 2001) |
| 00080 | Color, wat., filt., platinum cobalt units | 58 | 160.000 | 12.000 | 44.034 | 110.500 | 50.750 | 35.000 | 23.000 | 13.000 |
| 00078 | Transparency, wat., unf., Secchi disc, meters | 38 | 2.500 | 0.450 | 0.931 | 1.645 | 1.000 | 0.850 | 0.750 | 0.545 |
| 00300 | Dissolved oxygen, wat., unf., mg/L | 73 | 9.680 | 0.080 | 5.903 | 8.993 | 7.555 | 6.600 | 4.975 | 0.275 |
| 00301 | Dissolved oxygen, wat., unf., percent of saturation | 73 | 128.000 | 0.700 | 67.119 | 112.000 | 88.500 | 77.000 | 49.500 | 3.000 |
| 00400 | pH, wat., unf., field, standard units | 73 | 8.610 | 3.270 | 6.715 | 7.660 | 7.015 | 6.770 | 6.480 | 5.700 |
| 00403 | pH, wat., unf., laboratory, standard units | 58 | 8.100 | 6.700 | 7.288 | 8.100 | 7.425 | 7.250 | 7.000 | 6.795 |
| 90095 | Specific conductance, wat., unf., laboratory, microsiemens per centimeter at 25 degrees Celsius | 58 | 84.000 | 52.000 | 70.862 | 83.000 | 77.250 | 70.500 | 65.000 | 53.000 |
| 00095 | Specific conductance, wat., unf., microsiemens per centimeter at 25 degrees Celsius | 74 | 173.000 | 48.000 | 70.670 | 90.500 | 75.000 | 68.000 | 62.000 | 51.000 |
| 00900 | Hardness, wat., unf., mg/L as calcium carbonate | 58 | 26.000 | 15.000 | 20.845 | 25.050 | 23.000 | 21.000 | 19.000 | 15.950 |
| 00915 | Calcium, wat., filt., mg/L | 58 | 6.200 | 3.500 | 4.893 | 6.005 | 5.400 | 4.900 | 4.475 | 3.695 |
| 00925 | Magnesium, wat., filt., mg/L | 58 | 2.600 | 1.500 | 2.100 | 2.600 | 2.325 | 2.100 | 1.900 | 1.600 |
| 00935 | Potassium, wat., filt., mg/L | 58 | 2.900 | 1.300 | 1.910 | 2.605 | 2.300 | 1.850 | 1.600 | 1.400 |
| 00931 | Sodium adsorption ratio, wat., number | 58 | 0.500 | 0.300 | 0.407 | 0.500 | 0.400 | 0.400 | 0.400 | 0.300 |
| 00930 | Sodium, wat., filt., mg/L | 58 | 5.600 | 2.400 | 4.286 | 5.500 | 4.800 | 4.450 | 3.775 | 3.000 |
| 00932 | Sodium, wat., percent in equivalents of major cations | 58 | 32.000 | 22.000 | 28.448 | 31.050 | 30.000 | 29.000 | 27.000 | 24.000 |
| 99430 | Carbonate, wat., unf., incremental titration, field, mg/L as calcium carbonate | 26 | 30.000 | 9.000 | 20.615 | 29.650 | 24.000 | 22.500 | 16.000 | 9.350 |
| 90410 | Acid neutralizing capacity, wat., unf., fixed endpoint (pH 4.5) titration, laboratory, mg/L as calcium carbonate | 58 | 30.000 | 10.000 | 21.603 | 29.050 | 26.000 | 22.000 | 17.750 | 11.950 |
| 00410 | Acid neutralizing capacity, wat., unf., fixed endpoint (pH 4.5) titration, field, mg/L as calcium carbonate | 29 | 38.000 | 9.000 | 20.707 | 35.000 | 24.500 | 22.000 | 16.500 | 9.500 |
| 00419 | Acid neutralizing capacity, wat., unf., incremental titration, field, mg/L as calcium carbonate | 11 | 31.000 | 11.000 | 20.636 | 31.000 | 25.000 | 21.000 | 16.000 | 11.000 |
| 99440 | Bicarbonate, wat., unf., incremental titration, field, mg/L | 37 | 38.000 | 11.000 | 25.159 | 37.100 | 29.000 | 26.000 | 20.000 | 11.900 |

| NWIS Param-eter code | Constituent name | Sample size | Maximum | Minimum | Mean | Percentile |
| --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  | 95th | 75th | 50th | 25th | 5th |
| 99445 | Carbonate, wat., unf., incremental titration, field, mg/L | 11 | 2.000 | 0.000 | 0.182 | 2.000 | 0.000 | 0.000 | 0.000 | 0.000 |
| 00940 | Chloride, wat., filt., mg/L | 56 | 12.000 | 3.400 | 4.880 | 6.745 | 5.350 | 4.700 | 4.200 | 3.670 |
| 00950 | Fluoride, wat., filt., mg/L | 56 | 0.200 | -- | 0.097* | *0.200 | *0.100 | *0.089 | *0.068 | *0.045 |
| 00955 | Silica, wat., filt., mg/L | 56 | 12.000 | 6.700 | 9.289 | 11.150 | 10.000 | 9.600 | 8.500 | 6.785 |
| 00945 | Sulfate, wat., filt., mg/L | 56 | 13.000 | 0.300 | 4.048 | 6.220 | 4.300 | 3.850 | 3.125 | 2.600 |
| 99890 | Sulfate, wat., filt., uncorrected, mg/L | 3 | -- | -- | -- | -- | -- | -- | -- | -- |
| 70300 | Residue on evaporation, dried at 180 degrees Celsius, wat., filt., mg/L | 56 | 67.000 | 2.000 | 50.982 | 66.000 | 58.000 | 54.500 | 46.000 | 26.800 |
| 00608 | Ammonia, wat., filt., mg/L as nitrogen | 64 | 3.100 | -- | 0.121* | *0.317 | *0.106 | *0.050 | *0.017 | *0.005 |
| 00623 | Ammonia plus organic nitrogen, wat., filt., mg/L as nitrogen | 37 | 1.100 | -- | 0.440* | *0.740 | *0.500 | *0.400 | *0.350 | *0.197 |
| 00625 | Ammonia plus organic nitrogen, wat., unf., mg/L as nitrogen | 64 | 4.300 | 0.300 | 0.631 | 0.900 | 0.675 | 0.550 | 0.500 | 0.300 |
| 00610 | Ammonia, wat., unf., mg/L as nitrogen | 18 | 0.220 | 0.010 | 0.076 | 0.220 | 0.110 | 0.075 | 0.020 | 0.010 |
| 00620 | Nitrate, wat., unf., mg/L as nitrogen | 5 | 0.280 | 0.160 | -- | -- | -- | -- | -- | -- |
| 00631 | Nitrite plus nitrate, wat., filt., mg/L as nitrogen | 64 | 0.430 | -- | 0.069* | *0.315 | *0.108 | *0.014 | *0.005 | *0.001 |
| 00630 | Nitrite plus nitrate, wat., unf., mg/L as nitrogen | 18 | 0.300 | -- | 0.098* | *0.300 | *0.178 | *0.053 | *0.026 | *0.012 |
| 00613 | Nitrite, wat., filt., mg/L as nitrogen | 54 | 0.043 | -- | 0.005* | *0.024 | *0.005 | *0.002 | *0.001 | *0.000 |
| 00615 | Nitrite, wat., unf., mg/L as nitrogen | 18 | 0.030 | -- | 0.008* | *0.030 | *0.010 | *0.005 | *0.003 | *0.001 |
| 00605 | Organic nitrogen, wat., unf., mg/L | 60 | 1.200 | 0.280 | 0.511 | 0.889 | 0.587 | 0.470 | 0.410 | 0.312 |
| 00666 | Phosphorus, wat., filt., mg/L | 38 | 0.060 | -- | 0.016* | *0.050 | *0.020 | *0.010 | *0.006 | *0.003 |
| 00671 | Orthophosphate, wat., filt., mg/L as phosphorus | 63 | 0.030 | -- | 0.004* | *0.019 | *0.004 | *0.002 | *0.001 | *0.000 |
| 70507 | Orthophosphate, wat., unf., mg/L as phosphorus | 18 | 0.060 | -- | 0.015* | *0.060 | *0.022 | *0.008 | *0.002 | *0.001 |
| 00665 | Phosphorus, wat., unf., mg/L | 64 | 0.390 | -- | 0.042* | *0.120 | *0.040 | *0.030 | *0.020 | *0.010 |
| 00680 | Organic carbon, wat., unf., mg/L | 55 | 15.000 | 2.100 | 7.985 | 12.400 | 8.900 | 7.600 | 6.700 | 5.440 |
| 70953 | Chlorophyll a, phytoplankton, chromatographic-fluorometric method, ug/L | 58 | 27.400 | 0.500 | 7.426 | 23.000 | 10.300 | 5.650 | 3.375 | 0.795 |
| 70954 | Chlorophyll b, phytoplankton, chromatographic-fluorometric method, ug/L | 58 | 2.200 | -- | 0.305* | *1.205 | *0.300 | *0.187 | *0.096 | *0.040 |
| 01105 | Aluminum, wat., unf., recoverable, ug/L | 45 | 4000.000 | 10.000 | 248.387 | 929.300 | 200.000 | 80.000 | 60.000 | 23.000 |
| 01002 | Arsenic, wat., unf., ug/L | 45 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01027 | Cadmium, wat., unf., ug/L | 45 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01034 | Chromium, wat., unf., recoverable, ug/L | 45 | 210.000 | -- | 5.963* | *21.100 | *1.000 | *0.316 | *0.071 | *0.008 |
| 01037 | Cobalt, wat., unf., recoverable, ug/L | 45 | 2.000 | -- | 0.678* | *1.000 | *0.821 | *0.625 | *0.475 | *0.325 |
| 01042 | Copper, wat., unf., recoverable, ug/L | 44 | 6.000 | -- | 2.381* | *5.000 | *3.000 | *2.000 | *1.000 | *0.704 |
| 01045 | Iron, wat., unf., recoverable, ug/L | 64 | 34000.000 | 109.000 | 1779.125 | 7675.000 | 1000.000 | 590.000 | 257.500 | 119.250 |
| 01051 | Lead, wat., unf., recoverable, ug/L | 45 | 5.000 | -- | 1.012* | *3.700 | *1.000 | *0.651 | *0.352 | *0.136 |
| 01055 | Manganese, wat., unf., recoverable, ug/L | 64 | 3660.000 | 18.600 | 358.327 | 1585.000 | 400.750 | 121.000 | 45.650 | 23.875 |
| 71900 | Mercury, wat., unf., recoverable, ug/L | 44 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01062 | Molybdenum, wat., unf., recoverable, ug/L | 45 | 4.000 | -- | 0.428* | *2.000 | *0.442 | *0.186 | *0.084 | *0.022 |
| 01067 | Nickel, wat., unf., recoverable, ug/L | 45 | 39.000 | -- | 2.072* | *5.700 | *2.000 | *1.000 | *0.301 | *0.087 |
| 01147 | Selenium, wat., unf., ug/L | 45 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01077 | Silver, wat., unf., recoverable, ug/L | 44 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01092 | Zinc, wat., unf., recoverable, ug/L | 45 | 20.000 | -- | 4.998* | *15.740 | *6.428 | *3.827 | *2.266 | *1.064 |
| 02086500 Flat River at dam near Bahama (October 1988–March 1993) |
| 00061 | Discharge, instantaneous, cubic feet per second | 34 | 2420.000 | 0.010 | 202.246 | 1024.250 | 193.000 | 84.000 | 36.500 | 0.018 |
| 00080 | Color, wat., filt., platinum cobalt units | 35 | 170.000 | 20.000 | 78.057 | 154.000 | 110.000 | 65.000 | 55.000 | 25.600 |
| 00300 | Dissolved oxygen, wat., unf., mg/L | 34 | 13.300 | 2.400 | 8.047 | 12.550 | 10.050 | 8.350 | 6.375 | 2.700 |
| 00301 | Dissolved oxygen, wat., unf., percent of saturation | 33 | 106.000 | 26.000 | 79.333 | 105.300 | 98.000 | 86.000 | 64.000 | 28.100 |
| 00400 | pH, wat., unf., field, standard units | 35 | 7.970 | 5.700 | 6.891 | 7.434 | 7.200 | 7.000 | 6.600 | 6.020 |
| 00403 | pH, wat., unf., laboratory, standard units | 35 | 8.300 | 6.600 | 7.157 | 7.820 | 7.300 | 7.100 | 6.900 | 6.680 |
| 90095 | Specific conductance, wat., unf., laboratory, microsiemens per centimeter at 25 degrees Celsius | 35 | 104.000 | 45.000 | 69.657 | 99.200 | 79.000 | 66.000 | 59.000 | 52.200 |
| 00095 | Specific conductance, wat., unf., microsiemens per centimeter at 25 degrees Celsius | 35 | 105.000 | 40.000 | 67.514 | 101.000 | 76.000 | 65.000 | 57.000 | 42.400 |
| 00900 | Hardness, wat., unf., mg/L as calcium carbonate | 35 | 35.000 | 14.000 | 20.486 | 34.200 | 22.000 | 20.000 | 17.000 | 14.800 |
| 00915 | Calcium, wat., filt., mg/L | 35 | 9.400 | 3.400 | 4.869 | 8.920 | 5.200 | 4.700 | 4.000 | 3.400 |
| 00925 | Magnesium, wat., filt., mg/L | 35 | 3.100 | 1.300 | 2.020 | 2.940 | 2.300 | 1.900 | 1.700 | 1.460 |
| 00935 | Potassium, wat., filt., mg/L | 35 | 3.000 | 1.200 | 1.997 | 2.920 | 2.400 | 1.900 | 1.600 | 1.360 |
| 00931 | Sodium adsorption ratio, wat., number | 35 | 0.500 | 0.200 | 0.403 | 0.500 | 0.400 | 0.400 | 0.400 | 0.280 |
| 00930 | Sodium, wat., filt., mg/L | 35 | 6.300 | 2.100 | 4.220 | 5.660 | 4.800 | 4.100 | 3.600 | 2.900 |
| 00932 | Sodium, wat., percent in equivalents of major cations | 35 | 34.000 | 21.000 | 28.543 | 32.400 | 31.000 | 28.000 | 27.000 | 22.600 |
| 99430 | Carbonate, wat., unf., incremental titration, field, mg/L as calcium carbonate | 1 | 4.000 | -- | -- | -- | -- | -- | -- | -- |
| 90410 | Acid neutralizing capacity, wat., unf., fixed endpoint (pH 4.5) titration, laboratory, mg/L as calcium carbonate | 35 | 39.000 | 8.000 | 17.954 | 36.600 | 20.000 | 17.000 | 13.000 | 8.800 |
| 00410 | Acid neutralizing capacity, wat., unf., fixed endpoint (pH 4.5) titration, field, mg/L as calcium carbonate | 1 | 10.000 | -- | -- | -- | -- | -- | -- | -- |
| 99440 | Bicarbonate, wat., unf., incremental titration, field, mg/L | 1 | 5.000 | -- | -- | -- | -- | -- | -- | -- |
| 99445 | Carbonate, wat., unf., incremental titration, field, mg/L | 1 | 0.000 | -- | -- | -- | -- | -- | -- | -- |
| 00940 | Chloride, wat., filt., mg/L | 35 | 6.700 | 3.400 | 4.874 | 6.460 | 5.500 | 4.700 | 4.200 | 3.560 |
| 00950 | Fluoride, wat., filt., mg/L | 35 | 0.400 | -- | 0.112* | *0.320 | *0.100 | *0.100 | *0.061 | *0.034 |
| 00955 | Silica, wat., filt., mg/L | 35 | 12.000 | 4.800 | 9.329 | 12.000 | 11.000 | 9.800 | 8.300 | 5.360 |
| 00945 | Sulfate, wat., filt., mg/L | 33 | 9.200 | 2.900 | 5.706 | 9.200 | 6.950 | 5.400 | 4.450 | 2.970 |
| 99890 | Sulfate, wat., filt., uncorrected, mg/L | 6 | -- | -- | -- | -- | -- | -- | -- | -- |
| 70300 | Residue on evaporation, dried at 180 degrees Celsius, wat., filt., mg/L | 34 | 70.000 | 28.000 | 52.824 | 67.750 | 59.250 | 53.500 | 49.250 | 28.750 |
| 00608 | Ammonia, wat., filt., mg/L as nitrogen | 33 | 0.310 | 0.010 | 0.107 | 0.296 | 0.155 | 0.090 | 0.045 | 0.010 |
| 00623 | Ammonia plus organic nitrogen, wat., filt., mg/L as nitrogen | 30 | 1.000 | 0.300 | 0.603 | 1.000 | 0.700 | 0.600 | 0.500 | 0.300 |
| 00625 | Ammonia plus organic nitrogen, wat., unf., mg/L as nitrogen | 35 | 1.000 | 0.200 | 0.626 | 0.920 | 0.700 | 0.600 | 0.500 | 0.280 |
| 00610 | Ammonia, wat., unf., mg/L as nitrogen | 33 | 0.330 | -- | 0.117* | *0.295 | *0.165 | *0.100 | *0.060 | *0.019 |
| 00620 | Nitrate, wat., unf., mg/L as nitrogen | 24 | 0.490 | 0.040 | 0.242 | 0.488 | 0.377 | 0.205 | 0.162 | 0.050 |
| 00631 | Nitrite plus nitrate, wat., filt., mg/L as nitrogen | 35 | 0.460 | -- | 0.245* | *0.444 | *0.400 | *0.200 | *0.130 | *0.081 |
| 00630 | Nitrite plus nitrate, wat., unf., mg/L as nitrogen | 34 | 0.500 | -- | 0.232* | *0.425 | *0.400 | *0.200 | *0.100 | *0.068 |
| 00613 | Nitrite, wat., filt., mg/L as nitrogen | 10 | 0.010 | -- | 0.010* | *0.010 | *0.010 | *0.010 | *0.010 | *0.010 |
| 00615 | Nitrite, wat., unf., mg/L as nitrogen | 34 | 0.040 | -- | 0.015* | *0.040 | *0.020 | *0.010 | *0.009 | *0.004 |
| 00605 | Organic nitrogen, wat., unf., mg/L | 34 | 0.940 | 0.220 | 0.517 | 0.902 | 0.610 | 0.485 | 0.412 | 0.228 |
| 00666 | Phosphorus, wat., filt., mg/L | 35 | 0.270 | -- | 0.032* | *0.118 | *0.030 | *0.020 | *0.020 | *0.006 |
| 00671 | Orthophosphate, wat., filt., mg/L as phosphorus | 35 | 0.240 | -- | 0.022* | *0.112 | *0.030 | *0.010 | *0.004 | *0.001 |
| 70507 | Orthophosphate, wat., unf., mg/L as phosphorus | 34 | 0.100 | -- | 0.025* | *0.085 | *0.030 | *0.020 | *0.009 | *0.004 |
| 00665 | Phosphorus, wat., unf., mg/L | 35 | 0.180 | 0.020 | 0.054 | 0.148 | 0.060 | 0.050 | 0.030 | 0.020 |
| 00680 | Organic carbon, wat., unf., mg/L | 34 | 12.000 | 4.600 | 7.612 | 10.350 | 8.800 | 7.750 | 6.150 | 4.900 |
| 01105 | Aluminum, wat., unf., recoverable, ug/L | 14 | 3000.000 | 30.000 | 604.286 | 3000.000 | 732.500 | 485.000 | 135.000 | 30.000 |
| 01002 | Arsenic, wat., unf., ug/L | 14 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01027 | Cadmium, wat., unf., ug/L | 14 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01034 | Chromium, wat., unf., recoverable, ug/L | 14 | 3.000 | -- | 1.088* | *3.000 | *2.000 | *0.801 | *0.461 | *0.232 |
| 01037 | Cobalt, wat., unf., recoverable, ug/L | 14 | 2.000 | -- | 0.840* | *2.000 | *1.000 | *0.666 | *0.422 | *0.239 |
| 01042 | Copper, wat., unf., recoverable, ug/L | 14 | 5.000 | 2.000 | 3.357 | 5.000 | 4.000 | 3.000 | 2.750 | 2.000 |
| 01045 | Iron, wat., unf., recoverable, ug/L | 14 | 3400.000 | 390.000 | 1080.714 | 3400.000 | 1250.000 | 855.000 | 612.500 | 390.000 |
| 01051 | Lead, wat., unf., recoverable, ug/L | 14 | 7.000 | -- | 1.958* | *7.000 | *2.250 | *1.494 | *1.000 | *0.426 |
| 01055 | Manganese, wat., unf., recoverable, ug/L | 14 | 580.000 | 70.000 | 217.857 | 580.000 | 345.000 | 140.000 | 77.500 | 70.000 |
| 71900 | Mercury, wat., unf., recoverable, ug/L | 14 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01062 | Molybdenum, wat., unf., recoverable, ug/L | 14 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01067 | Nickel, wat., unf., recoverable, ug/L | 14 | 5.000 | -- | 2.039* | *5.000 | *2.000 | *2.000 | *1.000 | *0.547 |
| 01147 | Selenium, wat., unf., ug/L | 14 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01077 | Silver, wat., unf., recoverable, ug/L | 13 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01092 | Zinc, wat., unf., recoverable, ug/L | 14 | -- | -- | -- | -- | -- | -- | -- | -- |
| 80154 | Suspended sediment concentration, mg/L | 31 | 59.000 | 2.000 | 17.290 | 56.000 | 24.000 | 8.000 | 6.000 | 2.000 |
| 02086624 Knap of Reeds Creek near Butner (October 1988–April 1995) |
| 00061 | Discharge, instantaneous, cubic feet per second | 18 | 536.000 | 3.200 | 43.617 | 536.000 | 21.500 | 7.500 | 5.175 | 3.200 |
| 00080 | Color, wat., filt., platinum cobalt units | 1 | 110.000 | -- | -- | -- | -- | -- | -- | -- |
| 00300 | Dissolved oxygen, wat., unf., mg/L | 18 | 9.400 | 5.600 | 7.322 | 9.400 | 8.250 | 7.400 | 6.250 | 5.600 |
| 00301 | Dissolved oxygen, wat., unf., percent of saturation | 1 | 80.000 | -- | -- | -- | -- | -- | -- | -- |
| 00400 | pH, wat., unf., field, standard units | 18 | 7.200 | 6.400 | 6.873 | 7.200 | 7.000 | 6.900 | 6.745 | 6.400 |
| 00403 | pH, wat., unf., laboratory, standard units | 1 | 6.600 | -- | -- | -- | -- | -- | -- | -- |
| 90095 | Specific conductance, wat., unf., laboratory, microsiemens per centimeter at 25 degrees Celsius | 1 | 67.000 | -- | -- | -- | -- | -- | -- | -- |
| 00095 | Specific conductance, wat., unf., microsiemens per centimeter at 25 degrees Celsius | 17 | 633.000 | 29.000 | 229.118 | 633.000 | 345.000 | 161.000 | 91.500 | 29.000 |
| 00900 | Hardness, wat., unf., mg/L as calcium carbonate | 1 | 19.000 | -- | -- | -- | -- | -- | -- | -- |
| 00915 | Calcium, wat., filt., mg/L | 1 | 4.500 | -- | -- | -- | -- | -- | -- | -- |
| 00925 | Magnesium, wat., filt., mg/L | 1 | 1.900 | -- | -- | -- | -- | -- | -- | -- |
| 00935 | Potassium, wat., filt., mg/L | 1 | 2.400 | -- | -- | -- | -- | -- | -- | -- |
| 00931 | Sodium adsorption ratio, wat., number | 1 | 0.400 | -- | -- | -- | -- | -- | -- | -- |
| 00930 | Sodium, wat., filt., mg/L | 1 | 3.600 | -- | -- | -- | -- | -- | -- | -- |
| 00932 | Sodium, wat., percent in equivalents of major cations | 1 | 26.000 | -- | -- | -- | -- | -- | -- | -- |
| 99430 | Carbonate, wat., unf., incremental titration, field, mg/L as calcium carbonate | 1 | 14.000 | -- | -- | -- | -- | -- | -- | -- |
| 90410 | Acid neutralizing capacity, wat., unf., fixed endpoint (pH 4.5) titration, laboratory, mg/L as calcium carbonate | 1 | 17.000 | -- | -- | -- | -- | -- | -- | -- |
| 00410 | Acid neutralizing capacity, wat., unf., fixed endpoint (pH 4.5) titration, field, mg/L as calcium carbonate | 1 | 14.000 | -- | -- | -- | -- | -- | -- | -- |
| 99440 | Bicarbonate, wat., unf., incremental titration, field, mg/L | 1 | 17.000 | -- | -- | -- | -- | -- | -- | -- |
| 99445 | Carbonate, wat., unf., incremental titration, field, mg/L | 1 | 0.000 | -- | -- | -- | -- | -- | -- | -- |
| 00940 | Chloride, wat., filt., mg/L | 1 | 4.300 | -- | -- | -- | -- | -- | -- | -- |
| 00950 | Fluoride, wat., filt., mg/L | 1 | 0.100 | -- | -- | -- | -- | -- | -- | -- |
| 00955 | Silica, wat., filt., mg/L | 1 | 4.400 | -- | -- | -- | -- | -- | -- | -- |
| 00945 | Sulfate, wat., filt., mg/L | 1 | 7.300 | -- | -- | -- | -- | -- | -- | -- |
| 70300 | Residue on evaporation, dried at 180 degrees Celsius, wat., filt., mg/L | 1 | 42.000 | -- | -- | -- | -- | -- | -- | -- |
| 00608 | Ammonia, wat., filt., mg/L as nitrogen | 1 | 0.110 | -- | -- | -- | -- | -- | -- | -- |
| 00623 | Ammonia plus organic nitrogen, wat., filt., mg/L as nitrogen | 1 | 0.500 | -- | -- | -- | -- | -- | -- | -- |
| 00625 | Ammonia plus organic nitrogen, wat., unf., mg/L as nitrogen | 1 | 2.000 | -- | -- | -- | -- | -- | -- | -- |
| 00631 | Nitrite plus nitrate, wat., filt., mg/L as nitrogen | 1 | 0.290 | -- | -- | -- | -- | -- | -- | -- |
| 00613 | Nitrite, wat., filt., mg/L as nitrogen | 1 | -- | -- | -- | -- | -- | -- | -- | -- |
| 00605 | Organic nitrogen, wat., unf., mg/L | 1 | 1.900 | -- | -- | -- | -- | -- | -- | -- |
| 00666 | Phosphorus, wat., filt., mg/L | 1 | 0.020 | -- | -- | -- | -- | -- | -- | -- |
| 00671 | Orthophosphate, wat., filt., mg/L as phosphorus | 1 | 0.010 | -- | -- | -- | -- | -- | -- | -- |
| 00665 | Phosphorus, wat., unf., mg/L | 1 | 0.470 | -- | -- | -- | -- | -- | -- | -- |
| 00680 | Organic carbon, wat., unf., mg/L | 1 | 6.500 | -- | -- | -- | -- | -- | -- | -- |
| 01105 | Aluminum, wat., unf., recoverable, ug/L | 1 | 24000.000 | -- | -- | -- | -- | -- | -- | -- |
| 01002 | Arsenic, wat., unf., ug/L | 1 | 2.000 | -- | -- | -- | -- | -- | -- | -- |
| 01027 | Cadmium, wat., unf., ug/L | 1 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01034 | Chromium, wat., unf., recoverable, ug/L | 1 | 8.000 | -- | -- | -- | -- | -- | -- | -- |
| 01037 | Cobalt, wat., unf., recoverable, ug/L | 1 | 20.000 | -- | -- | -- | -- | -- | -- | -- |
| 01042 | Copper, wat., unf., recoverable, ug/L | 1 | 35.000 | -- | -- | -- | -- | -- | -- | -- |
| 01045 | Iron, wat., unf., recoverable, ug/L | 1 | 18000.000 | -- | -- | -- | -- | -- | -- | -- |
| 01051 | Lead, wat., unf., recoverable, ug/L | 1 | 18.000 | -- | -- | -- | -- | -- | -- | -- |
| 01055 | Manganese, wat., unf., recoverable, ug/L | 1 | 2100.000 | -- | -- | -- | -- | -- | -- | -- |
| 71900 | Mercury, wat., unf., recoverable, ug/L | 1 | 0.100 | -- | -- | -- | -- | -- | -- | -- |
| 01062 | Molybdenum, wat., unf., recoverable, ug/L | 1 | 4.000 | -- | -- | -- | -- | -- | -- | -- |
| 01067 | Nickel, wat., unf., recoverable, ug/L | 1 | 21.000 | -- | -- | -- | -- | -- | -- | -- |
| 01147 | Selenium, wat., unf., ug/L | 1 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01077 | Silver, wat., unf., recoverable, ug/L | 1 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01092 | Zinc, wat., unf., recoverable, ug/L | 1 | 100.000 | -- | -- | -- | -- | -- | -- | -- |
| 80154 | Suspended sediment concentration, mg/L | 1 | 851.000 | -- | -- | -- | -- | -- | -- | -- |
| 02086849 Ellerbe Creek near Gorman (October 1988–April 1995) |
| 00061 | Discharge, instantaneous, cubic feet per second | 14 | 672.000 | 4.300 | 94.393 | 672.000 | 56.250 | 19.500 | 11.400 | 4.300 |
| 00080 | Color, wat., filt., platinum cobalt units | 2 | 100.000 | 45.000 | -- | -- | -- | -- | -- | -- |
| 00300 | Dissolved oxygen, wat., unf., mg/L | 20 | 9.600 | 5.600 | 7.478 | 9.585 | 8.400 | 7.525 | 6.350 | 5.610 |
| 00301 | Dissolved oxygen, wat., unf., percent of saturation | 3 | 81.000 | 71.000 | -- | -- | -- | -- | -- | -- |
| 00400 | pH, wat., unf., field, standard units | 21 | 7.420 | 6.740 | 7.131 | 7.418 | 7.300 | 7.200 | 7.040 | 6.744 |
| 00403 | pH, wat., unf., laboratory, standard units | 2 | 7.400 | 7.300 | -- | -- | -- | -- | -- | -- |
| 90095 | Specific conductance, wat., unf., laboratory, microsiemens per centimeter at 25 degrees Celsius | 2 | 382.000 | 176.000 | -- | -- | -- | -- | -- | -- |
| 00095 | Specific conductance, wat., unf., microsiemens per centimeter at 25 degrees Celsius | 20 | 490.000 | 86.000 | 330.400 | 489.500 | 429.500 | 363.500 | 237.750 | 87.200 |
| 00900 | Hardness, wat., unf., mg/L as calcium carbonate | 2 | 74.000 | 42.000 | -- | -- | -- | -- | -- | -- |
| 00915 | Calcium, wat., filt., mg/L | 2 | 19.000 | 12.000 | -- | -- | -- | -- | -- | -- |
| 00925 | Magnesium, wat., filt., mg/L | 2 | 6.500 | 2.800 | -- | -- | -- | -- | -- | -- |
| 00935 | Potassium, wat., filt., mg/L | 2 | 6.600 | 3.200 | -- | -- | -- | -- | -- | -- |
| 00931 | Sodium adsorption ratio, wat., number | 2 | 2.000 | 1.000 | -- | -- | -- | -- | -- | -- |
| 00930 | Sodium, wat., filt., mg/L | 2 | 44.000 | 15.000 | -- | -- | -- | -- | -- | -- |
| 00932 | Sodium, wat., percent in equivalents of major cations | 2 | 54.000 | 42.000 | -- | -- | -- | -- | -- | -- |
| 99430 | Carbonate, wat., unf., incremental titration, field, mg/L as calcium carbonate | 1 | 27.000 | -- | -- | -- | -- | -- | -- | -- |
| 90410 | Acid neutralizing capacity, wat., unf., fixed endpoint (pH 4.5) titration, laboratory, mg/L as calcium carbonate | 2 | 68.000 | 32.000 | -- | -- | -- | -- | -- | -- |
| 00410 | Acid neutralizing capacity, wat., unf., fixed endpoint (pH 4.5) titration, field, mg/L as calcium carbonate | 1 | 26.000 | -- | -- | -- | -- | -- | -- | -- |
| 99440 | Bicarbonate, wat., unf., incremental titration, field, mg/L | 1 | 33.000 | -- | -- | -- | -- | -- | -- | -- |
| 99445 | Carbonate, wat., unf., incremental titration, field, mg/L | 1 | 0.000 | -- | -- | -- | -- | -- | -- | -- |
| 00940 | Chloride, wat., filt., mg/L | 2 | 31.000 | 13.000 | -- | -- | -- | -- | -- | -- |
| 00950 | Fluoride, wat., filt., mg/L | 2 | 0.700 | 0.300 | -- | -- | -- | -- | -- | -- |
| 00955 | Silica, wat., filt., mg/L | 2 | 9.200 | 7.100 | -- | -- | -- | -- | -- | -- |
| 00945 | Sulfate, wat., filt., mg/L | 2 | 30.000 | 18.000 | -- | -- | -- | -- | -- | -- |
| 70300 | Residue on evaporation, dried at 180 degrees Celsius, wat., filt., mg/L | 2 | 226.000 | 124.000 | -- | -- | -- | -- | -- | -- |
| 00608 | Ammonia, wat., filt., mg/L as nitrogen | 2 | 0.140 | 0.120 | -- | -- | -- | -- | -- | -- |
| 00623 | Ammonia plus organic nitrogen, wat., filt., mg/L as nitrogen | 2 | 1.000 | 0.700 | -- | -- | -- | -- | -- | -- |
| 00625 | Ammonia plus organic nitrogen, wat., unf., mg/L as nitrogen | 2 | 1.400 | 0.700 | -- | -- | -- | -- | -- | -- |
| 00610 | Ammonia, wat., unf., mg/L as nitrogen | 1 | 0.130 | -- | -- | -- | -- | -- | -- | -- |
| 00620 | Nitrate, wat., unf., mg/L as nitrogen | 1 | 9.240 | -- | -- | -- | -- | -- | -- | -- |
| 00631 | Nitrite plus nitrate, wat., filt., mg/L as nitrogen | 2 | 9.300 | 2.900 | -- | -- | -- | -- | -- | -- |
| 00630 | Nitrite plus nitrate, wat., unf., mg/L as nitrogen | 1 | 9.300 | -- | -- | -- | -- | -- | -- | -- |
| 00613 | Nitrite, wat., filt., mg/L as nitrogen | 2 | 0.060 | 0.030 | -- | -- | -- | -- | -- | -- |
| 00615 | Nitrite, wat., unf., mg/L as nitrogen | 1 | 0.060 | -- | -- | -- | -- | -- | -- | -- |
| 00605 | Organic nitrogen, wat., unf., mg/L | 2 | 1.300 | 0.560 | -- | -- | -- | -- | -- | -- |
| 00666 | Phosphorus, wat., filt., mg/L | 2 | 0.600 | 0.060 | -- | -- | -- | -- | -- | -- |
| 00671 | Orthophosphate, wat., filt., mg/L as phosphorus | 2 | 0.560 | 0.050 | -- | -- | -- | -- | -- | -- |
| 70507 | Orthophosphate, wat., unf., mg/L as phosphorus | 1 | 0.630 | -- | -- | -- | -- | -- | -- | -- |
| 00665 | Phosphorus, wat., unf., mg/L | 2 | 0.790 | 0.110 | -- | -- | -- | -- | -- | -- |
| 00680 | Organic carbon, wat., unf., mg/L | 2 | 11.000 | 11.000 | -- | -- | -- | -- | -- | -- |
| 01105 | Aluminum, wat., unf., recoverable, ug/L | 2 | 1500.000 | 440.000 | -- | -- | -- | -- | -- | -- |
| 01002 | Arsenic, wat., unf., ug/L | 2 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01027 | Cadmium, wat., unf., ug/L | 2 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01034 | Chromium, wat., unf., recoverable, ug/L | 2 | 3.000 | 1.000 | -- | -- | -- | -- | -- | -- |
| 01037 | Cobalt, wat., unf., recoverable, ug/L | 2 | 2.000 | 2.000 | -- | -- | -- | -- | -- | -- |
| 01042 | Copper, wat., unf., recoverable, ug/L | 2 | 9.000 | 4.000 | -- | -- | -- | -- | -- | -- |
| 01045 | Iron, wat., unf., recoverable, ug/L | 2 | 1800.000 | 820.000 | -- | -- | -- | -- | -- | -- |
| 01051 | Lead, wat., unf., recoverable, ug/L | 2 | 4.000 | 3.000 | -- | -- | -- | -- | -- | -- |
| 01055 | Manganese, wat., unf., recoverable, ug/L | 2 | 140.000 | 130.000 | -- | -- | -- | -- | -- | -- |
| 71900 | Mercury, wat., unf., recoverable, ug/L | 2 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01062 | Molybdenum, wat., unf., recoverable, ug/L | 2 | 7.000 | 1.000 | -- | -- | -- | -- | -- | -- |
| 01067 | Nickel, wat., unf., recoverable, ug/L | 2 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01147 | Selenium, wat., unf., ug/L | 2 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01077 | Silver, wat., unf., recoverable, ug/L | 2 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01092 | Zinc, wat., unf., recoverable, ug/L | 2 | 50.000 | 30.000 | -- | -- | -- | -- | -- | -- |
| 80154 | Suspended sediment concentration, mg/L | 3 | 351.000 | 21.000 | -- | -- | -- | -- | -- | -- |
| 02086920 Falls Lake at I-85 near Redwood (October 1988–July 1995) |
| 00080 | Color, wat., filt., platinum cobalt units | 17 | 140.000 | 25.000 | 68.706 | 140.000 | 78.000 | 64.000 | 51.500 | 25.000 |
| 00078 | Transparency, wat., unf., Secchi disc, meters | 13 | 0.750 | 0.100 | 0.488 | 0.750 | 0.700 | 0.500 | 0.300 | 0.100 |
| 00300 | Dissolved oxygen, wat., unf., mg/L | 24 | 12.600 | 1.400 | 7.517 | 12.500 | 9.325 | 7.100 | 6.325 | 2.250 |
| 00301 | Dissolved oxygen, wat., unf., percent of saturation | 16 | 116.000 | 18.000 | 77.500 | 116.000 | 90.250 | 83.000 | 68.500 | 18.000 |
| 00400 | pH, wat., unf., field, standard units | 26 | 9.210 | 6.400 | 7.187 | 9.101 | 7.200 | 7.000 | 6.800 | 6.400 |
| 00403 | pH, wat., unf., laboratory, standard units | 17 | 9.300 | 6.700 | 7.447 | 9.300 | 7.700 | 7.300 | 7.050 | 6.700 |
| 90095 | Specific conductance, wat., unf., laboratory, microsiemens per centimeter at 25 degrees Celsius | 17 | 410.000 | 105.000 | 205.353 | 410.000 | 241.500 | 193.000 | 137.000 | 105.000 |
| 00095 | Specific conductance, wat., unf., microsiemens per centimeter at 25 degrees Celsius | 26 | 404.000 | 71.000 | 176.077 | 396.650 | 245.000 | 144.500 | 108.000 | 71.350 |
| 00900 | Hardness, wat., unf., mg/L as calcium carbonate | 17 | 58.000 | 23.000 | 36.000 | 58.000 | 40.000 | 34.000 | 31.000 | 23.000 |
| 00915 | Calcium, wat., filt., mg/L | 17 | 16.000 | 5.600 | 9.218 | 16.000 | 10.350 | 8.400 | 7.650 | 5.600 |
| 00925 | Magnesium, wat., filt., mg/L | 17 | 5.600 | 2.100 | 3.135 | 5.600 | 3.400 | 3.000 | 2.550 | 2.100 |
| 00935 | Potassium, wat., filt., mg/L | 17 | 7.300 | 2.500 | 3.782 | 7.300 | 4.450 | 3.300 | 2.900 | 2.500 |
| 00931 | Sodium adsorption ratio, wat., number | 17 | 3.000 | 0.500 | 1.612 | 3.000 | 2.000 | 2.000 | 1.000 | 0.500 |
| 00930 | Sodium, wat., filt., mg/L | 17 | 53.000 | 7.000 | 23.706 | 53.000 | 29.000 | 23.000 | 14.000 | 7.000 |
| 00932 | Sodium, wat., percent in equivalents of major cations | 17 | 63.000 | 30.000 | 53.235 | 63.000 | 61.000 | 55.000 | 48.000 | 30.000 |
| 99430 | Carbonate, wat., unf., incremental titration, field, mg/L as calcium carbonate | 13 | 64.000 | 15.000 | 36.231 | 64.000 | 43.500 | 34.000 | 29.000 | 15.000 |
| 90410 | Acid neutralizing capacity, wat., unf., fixed endpoint (pH 4.5) titration, laboratory, mg/L as calcium carbonate | 17 | 60.000 | 19.000 | 37.765 | 60.000 | 47.000 | 33.000 | 30.500 | 19.000 |
| 00410 | Acid neutralizing capacity, wat., unf., fixed endpoint (pH 4.5) titration, field, mg/L as calcium carbonate | 13 | 61.000 | 18.000 | 36.923 | 61.000 | 43.000 | 37.000 | 30.000 | 18.000 |
| 99440 | Bicarbonate, wat., unf., incremental titration, field, mg/L | 13 | 78.000 | 18.000 | 43.385 | 78.000 | 51.500 | 40.000 | 35.500 | 18.000 |
| 99445 | Carbonate, wat., unf., incremental titration, field, mg/L | 9 | 4.000 | 0.000 | 0.556 | 4.000 | 0.500 | 0.000 | 0.000 | 0.000 |
| 00940 | Chloride, wat., filt., mg/L | 17 | 39.000 | 6.500 | 17.012 | 39.000 | 23.000 | 16.000 | 9.550 | 6.500 |
| 00950 | Fluoride, wat., filt., mg/L | 17 | 0.500 | 0.100 | 0.247 | 0.500 | 0.350 | 0.200 | 0.100 | 0.100 |
| 00955 | Silica, wat., filt., mg/L | 17 | 17.000 | 3.200 | 6.641 | 17.000 | 7.350 | 6.000 | 5.150 | 3.200 |
| 00945 | Sulfate, wat., filt., mg/L | 17 | 55.000 | 5.700 | 23.924 | 55.000 | 25.500 | 20.000 | 14.500 | 5.700 |
| 70300 | Residue on evaporation, dried at 180 degrees Celsius, wat., filt., mg/L | 17 | 224.000 | 76.000 | 122.824 | 224.000 | 150.000 | 119.000 | 86.000 | 76.000 |
| 00608 | Ammonia, wat., filt., mg/L as nitrogen | 17 | 0.360 | -- | 0.107* | *0.360 | *0.210 | *0.050 | *0.020 | *0.004 |
| 00623 | Ammonia plus organic nitrogen, wat., filt., mg/L as nitrogen | 17 | 1.200 | 0.300 | 0.676 | 1.200 | 0.800 | 0.600 | 0.500 | 0.300 |
| 00625 | Ammonia plus organic nitrogen, wat., unf., mg/L as nitrogen | 17 | 2.900 | 0.500 | 1.206 | 2.900 | 1.600 | 1.100 | 0.750 | 0.500 |
| 00610 | Ammonia, wat., unf., mg/L as nitrogen | 3 | 0.220 | 0.020 | -- | -- | -- | -- | -- | -- |
| 00620 | Nitrate, wat., unf., mg/L as nitrogen | 2 | 7.530 | 0.570 | -- | -- | -- | -- | -- | -- |
| 00631 | Nitrite plus nitrate, wat., filt., mg/L as nitrogen | 17 | 7.100 | -- | 1.275* | *7.100 | *0.845 | *0.570 | *0.061 | *0.009 |
| 00630 | Nitrite plus nitrate, wat., unf., mg/L as nitrogen | 3 | -- | -- | -- | -- | -- | -- | -- | -- |
| 00613 | Nitrite, wat., filt., mg/L as nitrogen | 17 | 0.100 | -- | 0.024* | *0.100 | *0.025 | *0.020 | *0.010 | *0.003 |
| 00615 | Nitrite, wat., unf., mg/L as nitrogen | 3 | 0.100 | 0.020 | -- | -- | -- | -- | -- | -- |
| 00605 | Organic nitrogen, wat., unf., mg/L | 16 | 1.800 | 0.400 | 0.988 | 1.800 | 1.375 | 0.920 | 0.582 | 0.400 |
| 00666 | Phosphorus, wat., filt., mg/L | 17 | 0.110 | -- | 0.030* | *0.110 | *0.030 | *0.020 | *0.015 | *0.006 |
| 00671 | Orthophosphate, wat., filt., mg/L as phosphorus | 17 | -- | -- | -- | -- | -- | -- | -- | -- |
| 70507 | Orthophosphate, wat., unf., mg/L as phosphorus | 3 | 0.100 | 0.020 | -- | -- | -- | -- | -- | -- |
| 00665 | Phosphorus, wat., unf., mg/L | 17 | 0.280 | 0.040 | 0.139 | 0.280 | 0.190 | 0.120 | 0.080 | 0.040 |
| 00680 | Organic carbon, wat., unf., mg/L | 17 | 23.000 | 7.400 | 12.912 | 23.000 | 15.000 | 12.000 | 10.500 | 7.400 |
| 70953 | Chlorophyll a, phytoplankton, chromatographic-fluorometric method, ug/L | 16 | 176.000 | 3.100 | 40.075 | 176.000 | 39.500 | 33.450 | 13.825 | 3.100 |
| 70954 | Chlorophyll b, phytoplankton, chromatographic-fluorometric method, ug/L | 16 | 10.900 | -- | 3.730* | *10.900 | *5.775 | *2.700 | *1.075 | *0.282 |
| 01105 | Aluminum, wat., unf., recoverable, ug/L | 17 | 1700.000 | 140.000 | 771.176 | 1700.000 | 1050.000 | 730.000 | 410.000 | 140.000 |
| 01002 | Arsenic, wat., unf., ug/L | 17 | 1.000 | -- | 1.000* | *1.000 | *1.000 | *1.000 | *1.000 | *1.000 |
| 01027 | Cadmium, wat., unf., ug/L | 17 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01034 | Chromium, wat., unf., recoverable, ug/L | 17 | 4.000 | -- | 1.025* | *4.000 | *1.500 | *0.654 | *0.340 | *0.137 |
| 01037 | Cobalt, wat., unf., recoverable, ug/L | 17 | 3.000 | -- | 1.616* | *3.000 | *2.000 | *2.000 | *1.000 | *0.718 |
| 01042 | Copper, wat., unf., recoverable, ug/L | 17 | 5.000 | 1.000 | 3.118 | 5.000 | 4.000 | 3.000 | 2.000 | 1.000 |
| 01045 | Iron, wat., unf., recoverable, ug/L | 17 | 2500.000 | 510.000 | 1505.882 | 2500.000 | 1800.000 | 1500.000 | 1150.000 | 510.000 |
| 01051 | Lead, wat., unf., recoverable, ug/L | 17 | 5.000 | -- | 3.062* | *5.000 | *4.000 | *3.000 | *2.000 | *1.000 |

| NWIS Param-eter code | Constituent name | Sample size | Maximum | Minimum | Mean | Percentile |
| --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  | 95th | 75th | 50th | 25th | 5th |
| 01055 | Manganese, wat., unf., recoverable, ug/L | 17 | 950.000 | 200.000 | 535.882 | 950.000 | 695.000 | 550.000 | 345.000 | 200.000 |
| 71900 | Mercury, wat., unf., recoverable, ug/L | 17 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01062 | Molybdenum, wat., unf., recoverable, ug/L | 17 | 4.000 | -- | 1.682* | *4.000 | *2.500 | *1.000 | *1.000 | *0.421 |
| 01067 | Nickel, wat., unf., recoverable, ug/L | 16 | 5.000 | -- | 2.291* | *5.000 | *3.000 | *2.000 | *1.250 | *0.658 |
| 01147 | Selenium, wat., unf., ug/L | 17 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01077 | Silver, wat., unf., recoverable, ug/L | 17 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01092 | Zinc, wat., unf., recoverable, ug/L | 17 | 30.000 | -- | 11.223* | *30.000 | *15.000 | *10.000 | *5.843 | *3.292 |
| 0208700780 Little Lick Creek above SR 1814 near Oak Grove (October 1988–April 1995) |
| 00061 | Discharge, instantaneous, cubic feet per second | 29 | 459.000 | 0.300 | 60.753 | 412.500 | 99.000 | 3.300 | 1.600 | 0.450 |
| 00080 | Color, wat., filt., platinum cobalt units | 10 | 300.000 | 65.000 | 207.500 | 300.000 | 255.000 | 225.000 | 172.500 | 65.000 |
| 00300 | Dissolved oxygen, wat., unf., mg/L | 25 | 10.900 | 3.900 | 7.128 | 10.480 | 8.850 | 6.700 | 5.850 | 4.140 |
| 00301 | Dissolved oxygen, wat., unf., percent of saturation | 8 | 88.000 | 66.000 | 76.875 | 88.000 | 84.750 | 78.000 | 67.500 | 66.000 |
| 00400 | pH, wat., unf., field, standard units | 29 | 7.410 | 6.700 | 7.042 | 7.375 | 7.200 | 7.030 | 6.885 | 6.700 |
| 00403 | pH, wat., unf., laboratory, standard units | 10 | 7.600 | 7.000 | 7.190 | 7.600 | 7.425 | 7.100 | 7.000 | 7.000 |
| 90095 | Specific conductance, wat., unf., laboratory, microsiemens per centimeter at 25 degrees Celsius | 10 | 262.000 | 94.000 | 150.100 | 262.000 | 181.250 | 130.500 | 111.000 | 94.000 |
| 00095 | Specific conductance, wat., unf., microsiemens per centimeter at 25 degrees Celsius | 28 | 506.000 | 70.000 | 242.143 | 498.350 | 348.750 | 247.500 | 121.000 | 74.500 |
| 00900 | Hardness, wat., unf., mg/L as calcium carbonate | 10 | 68.000 | 27.000 | 40.900 | 68.000 | 47.750 | 36.000 | 31.500 | 27.000 |
| 00915 | Calcium, wat., filt., mg/L | 10 | 18.000 | 5.900 | 10.390 | 18.000 | 12.500 | 9.100 | 7.975 | 5.900 |
| 00925 | Magnesium, wat., filt., mg/L | 10 | 5.500 | 2.400 | 3.610 | 5.500 | 4.125 | 3.400 | 2.800 | 2.400 |
| 00935 | Potassium, wat., filt., mg/L | 10 | 4.400 | 2.400 | 3.190 | 4.400 | 3.950 | 2.800 | 2.600 | 2.400 |
| 00931 | Sodium adsorption ratio, wat., number | 10 | 1.000 | 0.500 | 0.770 | 1.000 | 1.000 | 0.700 | 0.600 | 0.500 |
| 00930 | Sodium, wat., filt., mg/L | 10 | 25.000 | 6.000 | 12.410 | 25.000 | 15.500 | 9.850 | 8.075 | 6.000 |
| 00932 | Sodium, wat., percent in equivalents of major cations | 10 | 44.000 | 30.000 | 36.400 | 44.000 | 41.500 | 35.500 | 31.750 | 30.000 |
| 99430 | Carbonate, wat., unf., incremental titration, field, mg/L as calcium carbonate | 5 | 55.000 | 23.000 | -- | -- | -- | -- | -- | -- |
| 90410 | Acid neutralizing capacity, wat., unf., fixed endpoint (pH 4.5) titration, laboratory, mg/L as calcium carbonate | 10 | 58.000 | 20.000 | 34.100 | 58.000 | 44.000 | 28.000 | 26.000 | 20.000 |
| 00410 | Acid neutralizing capacity, wat., unf., fixed endpoint (pH 4.5) titration, field, mg/L as calcium carbonate | 5 | 55.000 | 23.000 | -- | -- | -- | -- | -- | -- |
| 99440 | Bicarbonate, wat., unf., incremental titration, field, mg/L | 5 | 67.000 | 28.000 | -- | -- | -- | -- | -- | -- |
| 99445 | Carbonate, wat., unf., incremental titration, field, mg/L | 4 | 0.000 | -- | -- | -- | -- | -- | -- | -- |
| 00940 | Chloride, wat., filt., mg/L | 10 | 20.000 | 5.900 | 10.970 | 20.000 | 13.250 | 9.600 | 7.600 | 5.900 |
| 00950 | Fluoride, wat., filt., mg/L | 10 | 0.300 | -- | 0.176* | *0.300 | *0.225 | *0.200 | *0.100 | *0.062 |
| 00955 | Silica, wat., filt., mg/L | 10 | 10.000 | 4.300 | 7.350 | 10.000 | 8.800 | 7.450 | 6.225 | 4.300 |
| 00945 | Sulfate, wat., filt., mg/L | 10 | 19.000 | 8.000 | 12.410 | 19.000 | 15.250 | 11.000 | 9.775 | 8.000 |
| 70300 | Residue on evaporation, dried at 180 degrees Celsius, wat., filt., mg/L | 10 | 180.000 | 85.000 | 108.800 | 180.000 | 119.000 | 94.500 | 87.750 | 85.000 |
| 00608 | Ammonia, wat., filt., mg/L as nitrogen | 5 | 0.240 | 0.090 | -- | -- | -- | -- | -- | -- |
| 00623 | Ammonia plus organic nitrogen, wat., filt., mg/L as nitrogen | 5 | 1.000 | 0.400 | -- | -- | -- | -- | -- | -- |
| 00625 | Ammonia plus organic nitrogen, wat., unf., mg/L as nitrogen | 8 | 1.900 | 0.800 | 1.062 | 1.900 | 1.150 | 0.950 | 0.825 | 0.800 |
| 00610 | Ammonia, wat., unf., mg/L as nitrogen | 3 | 0.150 | 0.100 | -- | -- | -- | -- | -- | -- |
| 00620 | Nitrate, wat., unf., mg/L as nitrogen | 3 | 0.470 | 0.250 | -- | -- | -- | -- | -- | -- |
| 00631 | Nitrite plus nitrate, wat., filt., mg/L as nitrogen | 5 | 4.500 | 0.280 | -- | -- | -- | -- | -- | -- |
| 00630 | Nitrite plus nitrate, wat., unf., mg/L as nitrogen | 3 | 0.550 | 0.270 | -- | -- | -- | -- | -- | -- |
| 00613 | Nitrite, wat., filt., mg/L as nitrogen | 5 | -- | -- | -- | -- | -- | -- | -- | -- |
| 00615 | Nitrite, wat., unf., mg/L as nitrogen | 3 | 0.080 | 0.000 | -- | -- | -- | -- | -- | -- |
| 00605 | Organic nitrogen, wat., unf., mg/L | 7 | 1.800 | 0.660 | 0.944 | 1.800 | 1.000 | 0.810 | 0.730 | 0.660 |
| 00666 | Phosphorus, wat., filt., mg/L | 5 | 0.100 | 0.020 | -- | -- | -- | -- | -- | -- |
| 00671 | Orthophosphate, wat., filt., mg/L as phosphorus | 5 | 0.100 | 0.010 | -- | -- | -- | -- | -- | -- |
| 70507 | Orthophosphate, wat., unf., mg/L as phosphorus | 3 | 0.170 | 0.000 | -- | -- | -- | -- | -- | -- |
| 00665 | Phosphorus, wat., unf., mg/L | 8 | 0.600 | 0.080 | 0.214 | 0.600 | 0.195 | 0.180 | 0.132 | 0.080 |
| 00680 | Organic carbon, wat., unf., mg/L | 10 | 28.000 | 11.000 | 16.600 | 28.000 | 18.000 | 16.000 | 13.750 | 11.000 |
| 01105 | Aluminum, wat., unf., recoverable, ug/L | 9 | 5800.000 | 1200.000 | 2844.444 | 5800.000 | 3750.000 | 2900.000 | 1450.000 | 1200.000 |
| 01002 | Arsenic, wat., unf., ug/L | 8 | 2.000 | -- | 1.088* | *2.000 | *1.000 | *1.000 | *1.000 | *0.706 |
| 01027 | Cadmium, wat., unf., ug/L | 9 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01034 | Chromium, wat., unf., recoverable, ug/L | 9 | 9.000 | -- | 4.471* | *9.000 | *6.000 | *5.000 | *1.923 | *1.393 |
| 01037 | Cobalt, wat., unf., recoverable, ug/L | 9 | 4.000 | 1.000 | 2.444 | 4.000 | 3.500 | 2.000 | 2.000 | 1.000 |
| 01042 | Copper, wat., unf., recoverable, ug/L | 9 | 8.000 | 4.000 | 5.667 | 8.000 | 7.000 | 6.000 | 4.000 | 4.000 |
| 01045 | Iron, wat., unf., recoverable, ug/L | 9 | 4200.000 | 2100.000 | 3011.111 | 4200.000 | 3650.000 | 2900.000 | 2400.000 | 2100.000 |
| 01051 | Lead, wat., unf., recoverable, ug/L | 9 | 14.000 | 3.000 | 7.222 | 14.000 | 9.500 | 6.000 | 4.500 | 3.000 |
| 01055 | Manganese, wat., unf., recoverable, ug/L | 9 | 730.000 | 160.000 | 382.222 | 730.000 | 565.000 | 320.000 | 205.000 | 160.000 |
| 71900 | Mercury, wat., unf., recoverable, ug/L | 9 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01062 | Molybdenum, wat., unf., recoverable, ug/L | 9 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01067 | Nickel, wat., unf., recoverable, ug/L | 9 | 6.000 | 3.000 | 4.444 | 6.000 | 5.000 | 5.000 | 3.500 | 3.000 |
| 01147 | Selenium, wat., unf., ug/L | 9 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01077 | Silver, wat., unf., recoverable, ug/L | 9 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01092 | Zinc, wat., unf., recoverable, ug/L | 9 | 40.000 | -- | 24.837* | *40.000 | *30.000 | *20.000 | *20.000 | *13.534 |
| 80154 | Suspended sediment concentration, mg/L | 9 | 413.000 | 91.000 | 177.111 | 413.000 | 259.500 | 121.000 | 100.000 | 91.000 |
| 0208703650 Falls Lake at N.C. 50 near Sandy Plain (October 1988–July 1995) |
| 00080 | Color, wat., filt., platinum cobalt units | 18 | 92.000 | 14.000 | 33.333 | 92.000 | 31.250 | 26.000 | 23.000 | 14.000 |
| 00078 | Transparency, wat., unf., Secchi disc, meters | 13 | 0.850 | 0.350 | 0.592 | 0.850 | 0.700 | 0.650 | 0.425 | 0.350 |
| 00300 | Dissolved oxygen, wat., unf., mg/L | 26 | 11.800 | 3.800 | 8.550 | 11.730 | 9.725 | 8.600 | 7.675 | 4.605 |
| 00301 | Dissolved oxygen, wat., unf., percent of saturation | 18 | 123.000 | 48.000 | 96.556 | 123.000 | 107.000 | 99.000 | 87.000 | 48.000 |
| 00400 | pH, wat., unf., field, standard units | 27 | 8.430 | 6.400 | 7.344 | 8.338 | 7.800 | 7.200 | 6.900 | 6.456 |
| 00403 | pH, wat., unf., laboratory, standard units | 18 | 8.500 | 6.800 | 7.450 | 8.500 | 7.625 | 7.350 | 7.100 | 6.800 |
| 90095 | Specific conductance, wat., unf., laboratory, microsiemens per centimeter at 25 degrees Celsius | 18 | 159.000 | 64.000 | 112.556 | 159.000 | 134.000 | 111.000 | 94.250 | 64.000 |
| 00095 | Specific conductance, wat., unf., microsiemens per centimeter at 25 degrees Celsius | 27 | 155.000 | 59.000 | 102.074 | 150.600 | 130.000 | 102.000 | 76.000 | 59.400 |
| 00900 | Hardness, wat., unf., mg/L as calcium carbonate | 18 | 31.000 | 18.000 | 26.722 | 31.000 | 29.000 | 28.500 | 25.250 | 18.000 |
| 00915 | Calcium, wat., filt., mg/L | 18 | 7.200 | 4.300 | 6.478 | 7.200 | 7.000 | 6.900 | 6.150 | 4.300 |
| 00925 | Magnesium, wat., filt., mg/L | 18 | 3.100 | 1.800 | 2.561 | 3.100 | 2.800 | 2.700 | 2.350 | 1.800 |
| 00935 | Potassium, wat., filt., mg/L | 18 | 2.800 | 1.500 | 2.256 | 2.800 | 2.500 | 2.300 | 2.025 | 1.500 |
| 00931 | Sodium adsorption ratio, wat., number | 18 | 2.000 | 0.400 | 0.828 | 2.000 | 1.000 | 0.750 | 0.575 | 0.400 |
| 00930 | Sodium, wat., filt., mg/L | 18 | 19.000 | 4.100 | 10.478 | 19.000 | 13.500 | 9.200 | 6.725 | 4.100 |
| 00932 | Sodium, wat., percent in equivalents of major cations | 18 | 56.000 | 31.000 | 41.722 | 56.000 | 49.500 | 38.000 | 34.750 | 31.000 |
| 99430 | Carbonate, wat., unf., incremental titration, field, mg/L as calcium carbonate | 13 | 57.000 | 14.000 | 31.769 | 57.000 | 43.000 | 29.000 | 19.500 | 14.000 |
| 90410 | Acid neutralizing capacity, wat., unf., fixed endpoint (pH 4.5) titration, laboratory, mg/L as calcium carbonate | 18 | 37.000 | 17.000 | 28.889 | 37.000 | 32.250 | 31.000 | 24.000 | 17.000 |
| 00410 | Acid neutralizing capacity, wat., unf., fixed endpoint (pH 4.5) titration, field, mg/L as calcium carbonate | 13 | 56.000 | 14.000 | 32.462 | 56.000 | 44.000 | 30.000 | 20.500 | 14.000 |
| 99440 | Bicarbonate, wat., unf., incremental titration, field, mg/L | 13 | 70.000 | 17.000 | 38.615 | 70.000 | 52.500 | 35.000 | 23.500 | 17.000 |
| 99445 | Carbonate, wat., unf., incremental titration, field, mg/L | 10 | 0.000 | -- | -- | -- | -- | -- | -- | -- |
| 00940 | Chloride, wat., filt., mg/L | 18 | 13.000 | 4.100 | 8.006 | 13.000 | 10.250 | 7.000 | 5.900 | 4.100 |
| 00950 | Fluoride, wat., filt., mg/L | 18 | 0.200 | -- | 0.147* | *0.200 | *0.200 | *0.151 | *0.099 | *0.071 |
| 00955 | Silica, wat., filt., mg/L | 18 | 7.100 | 2.600 | 4.811 | 7.100 | 5.525 | 5.100 | 3.900 | 2.600 |
| 00945 | Sulfate, wat., filt., mg/L | 18 | 20.000 | 6.400 | 11.083 | 20.000 | 12.250 | 9.950 | 9.200 | 6.400 |
| 70300 | Residue on evaporation, dried at 180 degrees Celsius, wat., filt., mg/L | 18 | 126.000 | 54.000 | 74.444 | 126.000 | 82.000 | 71.000 | 63.500 | 54.000 |
| 00608 | Ammonia, wat., filt., mg/L as nitrogen | 18 | 0.180 | -- | 0.044* | *0.180 | *0.082 | *0.020 | *0.017 | *0.004 |
| 00623 | Ammonia plus organic nitrogen, wat., filt., mg/L as nitrogen | 18 | 0.600 | 0.300 | 0.411 | 0.600 | 0.500 | 0.400 | 0.300 | 0.300 |
| 00625 | Ammonia plus organic nitrogen, wat., unf., mg/L as nitrogen | 18 | 0.900 | 0.400 | 0.617 | 0.900 | 0.700 | 0.600 | 0.500 | 0.400 |
| 00610 | Ammonia, wat., unf., mg/L as nitrogen | 4 | 0.120 | 0.010 | -- | -- | -- | -- | -- | -- |
| 00620 | Nitrate, wat., unf., mg/L as nitrogen | 1 | 0.050 | -- | -- | -- | -- | -- | -- | -- |
| 00631 | Nitrite plus nitrate, wat., filt., mg/L as nitrogen | 18 | 0.220 | -- | 0.042* | *0.220 | *0.057 | *0.018 | *0.007 | *0.002 |
| 00630 | Nitrite plus nitrate, wat., unf., mg/L as nitrogen | 4 | -- | -- | -- | -- | -- | -- | -- | -- |
| 00613 | Nitrite, wat., filt., mg/L as nitrogen | 18 | -- | -- | -- | -- | -- | -- | -- | -- |
| 00615 | Nitrite, wat., unf., mg/L as nitrogen | 4 | -- | -- | -- | -- | -- | -- | -- | -- |
| 00605 | Organic nitrogen, wat., unf., mg/L | 14 | 0.890 | 0.380 | 0.559 | 0.890 | 0.635 | 0.515 | 0.480 | 0.380 |
| 00666 | Phosphorus, wat., filt., mg/L | 18 | 0.030 | -- | 0.008* | *0.030 | *0.010 | *0.004 | *0.002 | *0.000 |
| 00671 | Orthophosphate, wat., filt., mg/L as phosphorus | 18 | -- | -- | -- | -- | -- | -- | -- | -- |
| 70507 | Orthophosphate, wat., unf., mg/L as phosphorus | 4 | -- | -- | -- | -- | -- | -- | -- | -- |
| 00665 | Phosphorus, wat., unf., mg/L | 18 | 0.100 | -- | 0.031* | *0.100 | *0.040 | *0.030 | *0.020 | *0.009 |
| 00680 | Organic carbon, wat., unf., mg/L | 18 | 12.000 | 4.300 | 8.922 | 12.000 | 9.550 | 8.750 | 8.450 | 4.300 |
| 70953 | Chlorophyll a, phytoplankton, chromatographic-fluorometric method, ug/L | 18 | 37.300 | 1.200 | 14.700 | 37.300 | 21.350 | 11.550 | 8.375 | 1.200 |
| 70954 | Chlorophyll b, phytoplankton, chromatographic-fluorometric method, ug/L | 18 | 2.200 | -- | 0.914* | *2.200 | *1.200 | *0.800 | *0.398 | *0.192 |
| 01105 | Aluminum, wat., unf., recoverable, ug/L | 18 | 470.000 | 40.000 | 140.556 | 470.000 | 187.500 | 100.000 | 60.000 | 40.000 |
| 01002 | Arsenic, wat., unf., ug/L | 18 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01027 | Cadmium, wat., unf., ug/L | 18 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01034 | Chromium, wat., unf., recoverable, ug/L | 18 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01037 | Cobalt, wat., unf., recoverable, ug/L | 18 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01042 | Copper, wat., unf., recoverable, ug/L | 18 | 8.000 | -- | 1.485* | *8.000 | *2.000 | *1.000 | *0.345 | *0.111 |
| 01045 | Iron, wat., unf., recoverable, ug/L | 18 | 1300.000 | 60.000 | 385.000 | 1300.000 | 487.500 | 320.000 | 177.500 | 60.000 |
| 01051 | Lead, wat., unf., recoverable, ug/L | 18 | -- | -- | -- | -- | -- | -- | -- | -- |

| NWIS Param-eter code | Constituent name | Sample size | Maximum | Minimum | Mean | Percentile |
| --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  | 95th | 75th | 50th | 25th | 5th |
| 01055 | Manganese, wat., unf., recoverable, ug/L | 18 | 640.000 | 50.000 | 203.333 | 640.000 | 255.000 | 180.000 | 97.500 | 50.000 |
| 71900 | Mercury, wat., unf., recoverable, ug/L | 18 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01062 | Molybdenum, wat., unf., recoverable, ug/L | 18 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01067 | Nickel, wat., unf., recoverable, ug/L | 18 | 5.000 | -- | 1.238* | *5.000 | *2.000 | *0.890 | *0.452 | *0.191 |
| 01147 | Selenium, wat., unf., ug/L | 18 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01077 | Silver, wat., unf., recoverable, ug/L | 18 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01092 | Zinc, wat., unf., recoverable, ug/L | 18 | -- | -- | -- | -- | -- | -- | -- | -- |
| 0208708905 Falls Lake at N.C. 98 near Bayleaf (October 1988–July 1995) |
| 00080 | Color, wat., filt., platinum cobalt units | 18 | 88.000 | 13.000 | 28.833 | 88.000 | 32.500 | 22.500 | 14.750 | 13.000 |
| 00078 | Transparency, wat., unf., Secchi disc, meters | 13 | 1.200 | 0.650 | 0.804 | 1.200 | 0.875 | 0.750 | 0.700 | 0.650 |
| 00300 | Dissolved oxygen, wat., unf., mg/L | 26 | 12.600 | 3.500 | 7.927 | 12.075 | 9.300 | 8.000 | 6.925 | 3.640 |
| 00301 | Dissolved oxygen, wat., unf., percent of saturation | 18 | 122.000 | 39.000 | 88.500 | 122.000 | 106.250 | 94.000 | 79.500 | 39.000 |
| 00400 | pH, wat., unf., field, standard units | 27 | 7.800 | 6.300 | 7.131 | 7.796 | 7.500 | 7.100 | 6.800 | 6.380 |
| 00403 | pH, wat., unf., laboratory, standard units | 18 | 8.500 | 6.700 | 7.333 | 8.500 | 7.800 | 7.200 | 7.000 | 6.700 |
| 90095 | Specific conductance, wat., unf., laboratory, microsiemens per centimeter at 25 degrees Celsius | 18 | 129.000 | 61.000 | 98.333 | 129.000 | 115.000 | 94.500 | 85.500 | 61.000 |
| 00095 | Specific conductance, wat., unf., microsiemens per centimeter at 25 degrees Celsius | 27 | 127.000 | 59.000 | 92.593 | 126.600 | 111.000 | 88.000 | 77.000 | 61.800 |
| 00900 | Hardness, wat., unf., mg/L as calcium carbonate | 18 | 31.000 | 17.000 | 25.167 | 31.000 | 29.000 | 25.500 | 22.000 | 17.000 |
| 00915 | Calcium, wat., filt., mg/L | 18 | 7.400 | 4.100 | 5.989 | 7.400 | 7.000 | 5.950 | 5.300 | 4.100 |
| 00925 | Magnesium, wat., filt., mg/L | 18 | 3.000 | 1.700 | 2.489 | 3.000 | 2.825 | 2.600 | 2.175 | 1.700 |
| 00935 | Potassium, wat., filt., mg/L | 18 | 2.700 | 1.500 | 2.128 | 2.700 | 2.500 | 2.200 | 1.775 | 1.500 |
| 00931 | Sodium adsorption ratio, wat., number | 18 | 1.000 | 0.400 | 0.672 | 1.000 | 0.800 | 0.650 | 0.575 | 0.400 |
| 00930 | Sodium, wat., filt., mg/L | 18 | 13.000 | 3.900 | 7.911 | 13.000 | 9.925 | 7.300 | 6.100 | 3.900 |
| 00932 | Sodium, wat., percent in equivalents of major cations | 18 | 47.000 | 31.000 | 37.278 | 47.000 | 39.250 | 36.500 | 34.000 | 31.000 |
| 99430 | Carbonate, wat., unf., incremental titration, field, mg/L as calcium carbonate | 13 | 41.000 | 13.000 | 25.154 | 41.000 | 34.500 | 21.000 | 18.000 | 13.000 |
| 90410 | Acid neutralizing capacity, wat., unf., fixed endpoint (pH 4.5) titration, laboratory, mg/L as calcium carbonate | 18 | 42.000 | 15.000 | 27.278 | 42.000 | 34.000 | 26.500 | 20.750 | 15.000 |
| 00410 | Acid neutralizing capacity, wat., unf., fixed endpoint (pH 4.5) titration, field, mg/L as calcium carbonate | 13 | 43.000 | 14.000 | 26.077 | 43.000 | 35.000 | 23.000 | 18.000 | 14.000 |
| 99440 | Bicarbonate, wat., unf., incremental titration, field, mg/L | 13 | 50.000 | 16.000 | 30.538 | 50.000 | 42.000 | 26.000 | 21.500 | 16.000 |
| 99445 | Carbonate, wat., unf., incremental titration, field, mg/L | 9 | 0.000 | -- | -- | -- | -- | -- | -- | -- |
| 00940 | Chloride, wat., filt., mg/L | 18 | 9.000 | 3.800 | 6.406 | 9.000 | 7.850 | 6.300 | 5.325 | 3.800 |
| 00950 | Fluoride, wat., filt., mg/L | 18 | 0.200 | -- | 0.120* | *0.200 | *0.200 | *0.100 | *0.093 | *0.052 |
| 00955 | Silica, wat., filt., mg/L | 18 | 6.700 | -- | 4.950* | *6.700 | *5.850 | *5.300 | *4.000 | *2.694 |
| 00945 | Sulfate, wat., filt., mg/L | 18 | 13.000 | 6.500 | 8.411 | 13.000 | 9.600 | 8.150 | 6.925 | 6.500 |
| 70300 | Residue on evaporation, dried at 180 degrees Celsius, wat., filt., mg/L | 18 | 95.000 | 36.000 | 63.500 | 95.000 | 69.000 | 66.000 | 56.000 | 36.000 |
| 00608 | Ammonia, wat., filt., mg/L as nitrogen | 17 | 0.510 | -- | 0.104* | *0.510 | *0.125 | *0.040 | *0.020 | *0.003 |
| 00623 | Ammonia plus organic nitrogen, wat., filt., mg/L as nitrogen | 18 | 1.000 | 0.200 | 0.494 | 1.000 | 0.725 | 0.400 | 0.300 | 0.200 |
| 00625 | Ammonia plus organic nitrogen, wat., unf., mg/L as nitrogen | 18 | 1.500 | 0.400 | 0.617 | 1.500 | 0.725 | 0.500 | 0.400 | 0.400 |
| 00610 | Ammonia, wat., unf., mg/L as nitrogen | 4 | -- | -- | -- | -- | -- | -- | -- | -- |
| 00620 | Nitrate, wat., unf., mg/L as nitrogen | 2 | 0.070 | 0.040 | -- | -- | -- | -- | -- | -- |
| 00631 | Nitrite plus nitrate, wat., filt., mg/L as nitrogen | 18 | -- | -- | -- | -- | -- | -- | -- | -- |
| 00630 | Nitrite plus nitrate, wat., unf., mg/L as nitrogen | 4 | -- | -- | -- | -- | -- | -- | -- | -- |
| 00613 | Nitrite, wat., filt., mg/L as nitrogen | 18 | -- | -- | -- | -- | -- | -- | -- | -- |
| 00615 | Nitrite, wat., unf., mg/L as nitrogen | 4 | -- | -- | -- | -- | -- | -- | -- | -- |
| 00605 | Organic nitrogen, wat., unf., mg/L | 15 | 1.400 | 0.350 | 0.519 | 1.400 | 0.570 | 0.450 | 0.380 | 0.350 |
| 00666 | Phosphorus, wat., filt., mg/L | 18 | 0.110 | -- | 0.014* | *0.110 | *0.020 | *0.004 | *0.001 | *0.000 |
| 00671 | Orthophosphate, wat., filt., mg/L as phosphorus | 18 | -- | -- | -- | -- | -- | -- | -- | -- |
| 70507 | Orthophosphate, wat., unf., mg/L as phosphorus | 4 | -- | -- | -- | -- | -- | -- | -- | -- |
| 00665 | Phosphorus, wat., unf., mg/L | 18 | 0.070 | -- | 0.026* | *0.070 | *0.030 | *0.020 | *0.010 | *0.005 |
| 00680 | Organic carbon, wat., unf., mg/L | 18 | 14.000 | 6.500 | 8.200 | 14.000 | 9.050 | 7.500 | 6.850 | 6.500 |
| 70953 | Chlorophyll a, phytoplankton, chromatographic-fluorometric method, ug/L | 18 | 24.100 | 0.800 | 8.561 | 24.100 | 12.650 | 6.800 | 4.000 | 0.800 |
| 70954 | Chlorophyll b, phytoplankton, chromatographic-fluorometric method, ug/L | 18 | 1.500 | -- | 0.600* | *1.500 | *0.925 | *0.381 | *0.274 | *0.126 |
| 01105 | Aluminum, wat., unf., recoverable, ug/L | 18 | 310.000 | 40.000 | 100.556 | 310.000 | 142.500 | 60.000 | 50.000 | 40.000 |
| 01002 | Arsenic, wat., unf., ug/L | 18 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01027 | Cadmium, wat., unf., ug/L | 18 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01034 | Chromium, wat., unf., recoverable, ug/L | 18 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01037 | Cobalt, wat., unf., recoverable, ug/L | 18 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01042 | Copper, wat., unf., recoverable, ug/L | 18 | 3.000 | -- | 1.310* | *3.000 | *2.000 | *1.000 | *0.723 | *0.411 |
| 01045 | Iron, wat., unf., recoverable, ug/L | 18 | 790.000 | 60.000 | 274.444 | 790.000 | 387.500 | 220.000 | 117.500 | 60.000 |
| 01051 | Lead, wat., unf., recoverable, ug/L | 18 | -- | -- | -- | -- | -- | -- | -- | -- |

| NWIS Param-eter code | Constituent name | Sample size | Maximum | Minimum | Mean | Percentile |
| --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  | 95th | 75th | 50th | 25th | 5th |
| 01055 | Manganese, wat., unf., recoverable, ug/L | 18 | 770.000 | 20.000 | 198.889 | 770.000 | 337.500 | 95.000 | 40.000 | 20.000 |
| 71900 | Mercury, wat., unf., recoverable, ug/L | 18 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01062 | Molybdenum, wat., unf., recoverable, ug/L | 18 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01067 | Nickel, wat., unf., recoverable, ug/L | 18 | 7.000 | -- | 1.199* | *7.000 | *1.000 | *1.000 | *0.415 | *0.182 |
| 01147 | Selenium, wat., unf., ug/L | 18 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01077 | Silver, wat., unf., recoverable, ug/L | 18 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01092 | Zinc, wat., unf., recoverable, ug/L | 18 | -- | -- | -- | -- | -- | -- | -- | -- |
| 0208718195 Falls Lake above dam at Falls (October 1988–July 1995) |
| 00080 | Color, wat., filt., platinum cobalt units | 18 | 95.000 | 13.000 | 27.500 | 95.000 | 25.250 | 22.000 | 18.000 | 13.000 |
| 00078 | Transparency, wat., unf., Secchi disc, meters | 13 | 1.350 | 0.600 | 0.877 | 1.350 | 0.975 | 0.850 | 0.750 | 0.600 |
| 00300 | Dissolved oxygen, wat., unf., mg/L | 26 | 12.500 | 3.800 | 7.554 | 11.940 | 8.800 | 7.650 | 6.600 | 3.835 |
| 00301 | Dissolved oxygen, wat., unf., percent of saturation | 18 | 123.000 | 40.000 | 83.333 | 123.000 | 102.250 | 92.000 | 66.250 | 40.000 |
| 00400 | pH, wat., unf., field, standard units | 27 | 8.000 | 6.300 | 7.129 | 7.960 | 7.540 | 7.000 | 6.800 | 6.380 |
| 00403 | pH, wat., unf., laboratory, standard units | 18 | 8.400 | 6.600 | 7.261 | 8.400 | 7.500 | 7.200 | 6.875 | 6.600 |
| 90095 | Specific conductance, wat., unf., laboratory, microsiemens per centimeter at 25 degrees Celsius | 18 | 117.000 | 64.000 | 92.778 | 117.000 | 106.250 | 93.000 | 77.750 | 64.000 |
| 00095 | Specific conductance, wat., unf., microsiemens per centimeter at 25 degrees Celsius | 27 | 118.000 | 60.000 | 87.333 | 116.000 | 103.000 | 87.000 | 73.000 | 62.000 |
| 00900 | Hardness, wat., unf., mg/L as calcium carbonate | 18 | 32.000 | 18.000 | 24.722 | 32.000 | 28.250 | 25.500 | 20.750 | 18.000 |
| 00915 | Calcium, wat., filt., mg/L | 18 | 7.900 | 4.300 | 5.833 | 7.900 | 6.825 | 5.650 | 4.800 | 4.300 |
| 00925 | Magnesium, wat., filt., mg/L | 18 | 3.000 | 1.800 | 2.450 | 3.000 | 2.800 | 2.500 | 2.150 | 1.800 |
| 00935 | Potassium, wat., filt., mg/L | 18 | 2.700 | 1.500 | 2.078 | 2.700 | 2.325 | 2.100 | 1.775 | 1.500 |
| 00931 | Sodium adsorption ratio, wat., number | 18 | 0.800 | 0.400 | 0.622 | 0.800 | 0.700 | 0.600 | 0.500 | 0.400 |
| 00930 | Sodium, wat., filt., mg/L | 18 | 10.000 | 4.200 | 7.022 | 10.000 | 8.125 | 6.700 | 5.400 | 4.200 |
| 00932 | Sodium, wat., percent in equivalents of major cations | 18 | 41.000 | 30.000 | 35.500 | 41.000 | 37.250 | 36.000 | 33.750 | 30.000 |
| 99430 | Carbonate, wat., unf., incremental titration, field, mg/L as calcium carbonate | 13 | 80.000 | 10.000 | 31.231 | 80.000 | 43.000 | 23.000 | 19.500 | 10.000 |
| 90410 | Acid neutralizing capacity, wat., unf., fixed endpoint (pH 4.5) titration, laboratory, mg/L as calcium carbonate | 18 | 37.000 | 15.000 | 25.778 | 37.000 | 32.250 | 24.000 | 19.750 | 15.000 |
| 00410 | Acid neutralizing capacity, wat., unf., fixed endpoint (pH 4.5) titration, field, mg/L as calcium carbonate | 13 | 81.000 | 12.000 | 32.000 | 81.000 | 43.500 | 23.000 | 20.000 | 12.000 |
| 99440 | Bicarbonate, wat., unf., incremental titration, field, mg/L | 13 | 98.000 | 12.000 | 38.000 | 98.000 | 52.500 | 28.000 | 23.000 | 12.000 |
| 99445 | Carbonate, wat., unf., incremental titration, field, mg/L | 10 | 0.000 | -- | -- | -- | -- | -- | -- | -- |
| 00940 | Chloride, wat., filt., mg/L | 18 | 7.000 | 4.000 | 5.939 | 7.000 | 6.700 | 6.350 | 5.275 | 4.000 |
| 00950 | Fluoride, wat., filt., mg/L | 18 | 0.200 | -- | 0.109* | *0.200 | *0.100 | *0.100 | *0.094 | *0.057 |
| 00955 | Silica, wat., filt., mg/L | 18 | 7.700 | -- | 5.062* | *7.700 | *6.025 | *5.150 | *4.025 | *2.809 |
| 00945 | Sulfate, wat., filt., mg/L | 18 | 11.000 | 5.300 | 7.761 | 11.000 | 9.025 | 7.700 | 6.525 | 5.300 |
| 70300 | Residue on evaporation, dried at 180 degrees Celsius, wat., filt., mg/L | 18 | 72.000 | 45.000 | 58.611 | 72.000 | 63.250 | 59.000 | 53.500 | 45.000 |
| 00608 | Ammonia, wat., filt., mg/L as nitrogen | 18 | 0.530 | -- | 0.128* | *0.530 | *0.252 | *0.040 | *0.020 | *0.003 |
| 00623 | Ammonia plus organic nitrogen, wat., filt., mg/L as nitrogen | 18 | 0.800 | 0.300 | 0.472 | 0.800 | 0.625 | 0.400 | 0.300 | 0.300 |
| 00625 | Ammonia plus organic nitrogen, wat., unf., mg/L as nitrogen | 18 | 1.000 | 0.300 | 0.550 | 1.000 | 0.600 | 0.550 | 0.400 | 0.300 |
| 00610 | Ammonia, wat., unf., mg/L as nitrogen | 4 | -- | -- | -- | -- | -- | -- | -- | -- |
| 00620 | Nitrate, wat., unf., mg/L as nitrogen | 1 | 0.040 | -- | -- | -- | -- | -- | -- | -- |
| 00631 | Nitrite plus nitrate, wat., filt., mg/L as nitrogen | 18 | 0.200 | -- | 0.063* | *0.200 | *0.094 | *0.042 | *0.022 | *0.009 |
| 00630 | Nitrite plus nitrate, wat., unf., mg/L as nitrogen | 4 | -- | -- | -- | -- | -- | -- | -- | -- |
| 00613 | Nitrite, wat., filt., mg/L as nitrogen | 18 | -- | -- | -- | -- | -- | -- | -- | -- |
| 00615 | Nitrite, wat., unf., mg/L as nitrogen | 4 | -- | -- | -- | -- | -- | -- | -- | -- |
| 00605 | Organic nitrogen, wat., unf., mg/L | 17 | 0.580 | 0.230 | 0.430 | 0.580 | 0.500 | 0.450 | 0.375 | 0.230 |
| 00666 | Phosphorus, wat., filt., mg/L | 18 | 0.050 | -- | 0.012* | *0.050 | *0.015 | *0.006 | *0.002 | *0.001 |
| 00671 | Orthophosphate, wat., filt., mg/L as phosphorus | 18 | -- | -- | -- | -- | -- | -- | -- | -- |
| 70507 | Orthophosphate, wat., unf., mg/L as phosphorus | 4 | -- | -- | -- | -- | -- | -- | -- | -- |
| 00665 | Phosphorus, wat., unf., mg/L | 18 | 0.040 | -- | 0.020* | *0.040 | *0.040 | *0.010 | *0.007 | *0.003 |
| 00680 | Organic carbon, wat., unf., mg/L | 17 | 9.300 | 5.900 | 7.429 | 9.300 | 8.150 | 7.300 | 6.700 | 5.900 |
| 70953 | Chlorophyll a, phytoplankton, chromatographic-fluorometric method, ug/L | 18 | 65.800 | 1.900 | 11.133 | 65.800 | 13.200 | 7.400 | 3.775 | 1.900 |
| 70954 | Chlorophyll b, phytoplankton, chromatographic-fluorometric method, ug/L | 18 | 4.200 | -- | 0.758* | *4.200 | *0.925 | *0.450 | *0.246 | *0.088 |
| 01105 | Aluminum, wat., unf., recoverable, ug/L | 18 | 250.000 | 30.000 | 85.000 | 250.000 | 95.000 | 60.000 | 40.000 | 30.000 |
| 01002 | Arsenic, wat., unf., ug/L | 18 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01027 | Cadmium, wat., unf., ug/L | 18 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01034 | Chromium, wat., unf., recoverable, ug/L | 18 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01037 | Cobalt, wat., unf., recoverable, ug/L | 18 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01042 | Copper, wat., unf., recoverable, ug/L | 18 | 3.000 | -- | 1.338* | *3.000 | *2.000 | *1.000 | *0.658 | *0.342 |
| 01045 | Iron, wat., unf., recoverable, ug/L | 18 | 870.000 | 40.000 | 243.889 | 870.000 | 350.000 | 125.000 | 80.000 | 40.000 |
| 01051 | Lead, wat., unf., recoverable, ug/L | 18 | -- | -- | -- | -- | -- | -- | -- | -- |

| NWIS Param-eter code | Constituent name | Sample size | Maximum | Minimum | Mean | Percentile |
| --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  | 95th | 75th | 50th | 25th | 5th |
| 01055 | Manganese, wat., unf., recoverable, ug/L | 18 | 1000.000 | -- | 304.723* | *1000.000 | *680.000 | *80.000 | *40.000 | *5.010 |
| 71900 | Mercury, wat., unf., recoverable, ug/L | 18 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01062 | Molybdenum, wat., unf., recoverable, ug/L | 18 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01067 | Nickel, wat., unf., recoverable, ug/L | 18 | 5.000 | -- | 0.986* | *5.000 | *1.000 | *0.501 | *0.219 | *0.068 |
| 01147 | Selenium, wat., unf., ug/L | 18 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01077 | Silver, wat., unf., recoverable, ug/L | 18 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01092 | Zinc, wat., unf., recoverable, ug/L | 18 | -- | -- | -- | -- | -- | -- | -- | -- |
| 02087183 Neuse River near Falls (October 1988–September 1996) |
| 00061 | Discharge, instantaneous, cubic feet per second | 16 | 3670.000 | 108.000 | 738.000 | 3670.000 | 444.250 | 184.500 | 167.750 | 108.000 |
| 00300 | Dissolved oxygen, wat., unf., mg/L | 16 | 12.200 | 7.200 | 8.794 | 12.200 | 9.650 | 8.700 | 7.650 | 7.200 |
| 00400 | pH, wat., unf., field, standard units | 16 | 7.800 | 6.300 | 6.940 | 7.800 | 7.175 | 7.030 | 6.600 | 6.300 |
| 00095 | Specific conductance, wat., unf., microsiemens per centimeter at 25 degrees Celsius | 15 | 104.000 | 50.000 | 81.100 | 104.000 | 95.000 | 82.500 | 74.000 | 50.000 |
| 00431 | Acid neutralizing capacity, wat., unf., mg/L as calcium carbonate | 1 | 22.000 | -- | -- | -- | -- | -- | -- | -- |
| 02087570 Neuse River at Smithfield (October 1988–June 1995) |
| 00061 | Discharge, instantaneous, cubic feet per second | 84 | 6170 | 203 | 1387.143 | 5500 | 1672.5 | 483 | 329.25 | 267.5 |
| 00080 | Color, wat., filt., platinum cobalt units | 84 | 280 | 7 | 51.333 | 120 | 55 | 43 | 25.25 | 16.5 |
| 00300 | Dissolved oxygen, wat., unf., mg/L | 81 | 12.6 | 5.4 | 8.717 | 12.38 | 10.45 | 8.4 | 6.9 | 6.2 |
| 00301 | Dissolved oxygen, wat., unf., percent of saturation | 81 | 144 | 64 | 87.642 | 102.9 | 91.5 | 87 | 82 | 74.1 |
| 00400 | pH, wat., unf., field, standard units | 84 | 7.6 | 5.8 | 7.057 | 7.5 | 7.3 | 7.1 | 6.9 | 6.425 |
| 00403 | pH, wat., unf., laboratory, standard units | 84 | 8.1 | 6.9 | 7.448 | 7.9 | 7.6 | 7.4 | 7.3 | 7 |
| 90095 | Specific conductance, wat., unf., laboratory, microsiemens per centimeter at 25 degrees Celsius | 84 | 340 | 70 | 176.845 | 273.25 | 223.75 | 178 | 119.25 | 84 |
| 00095 | Specific conductance, wat., unf., microsiemens per centimeter at 25 degrees Celsius | 84 | 331 | 68 | 174.56 | 268.5 | 217.75 | 180.5 | 117.25 | 87.25 |
| 00900 | Hardness, wat., unf., mg/L as calcium carbonate | 84 | 40 | 17 | 28.44 | 37 | 32.75 | 29 | 24 | 18.5 |
| 00915 | Calcium, wat., filt., mg/L | 84 | 9.9 | 4.3 | 7.051 | 9.2 | 8 | 7.1 | 6.125 | 4.625 |
| 00925 | Magnesium, wat., filt., mg/L | 84 | 3.7 | 1.5 | 2.62 | 3.475 | 3 | 2.7 | 2.2 | 1.725 |
| 00935 | Potassium, wat., filt., mg/L | 84 | 6.8 | 1.8 | 3.689 | 6.1 | 4.4 | 3.5 | 2.8 | 2.225 |
| 00931 | Sodium adsorption ratio, wat., number | 84 | 3 | 0.4 | 1.704 | 3 | 2 | 2 | 1 | 0.725 |
| 00930 | Sodium, wat., filt., mg/L | 84 | 48 | 4.3 | 21.171 | 37 | 28.75 | 21 | 12.25 | 7.125 |
| 00932 | Sodium, wat., percent in equivalents of major cations | 84 | 70 | 25 | 55.595 | 68 | 62.75 | 57 | 50 | 41 |
| 99430 | Carbonate, wat., unf., incremental titration, field, mg/L as calcium carbonate | 35 | 44 | 14 | 29.171 | 43.2 | 34 | 30 | 24 | 14.8 |
| 90410 | Acid neutralizing capacity, wat., unf., fixed endpoint (pH 4.5) titration, laboratory, mg/L as calcium carbonate | 84 | 48 | 12 | 29.071 | 41.75 | 34.75 | 29 | 23 | 16 |
| 00410 | Acid neutralizing capacity, wat., unf., fixed endpoint (pH 4.5) titration, field, mg/L as calcium carbonate | 36 | 46 | 15 | 30.111 | 43.45 | 35.5 | 30.5 | 26 | 15.85 |
| 99440 | Bicarbonate, wat., unf., incremental titration, field, mg/L | 35 | 54 | 17 | 35.514 | 52.4 | 41 | 37 | 29 | 17.8 |
| 99445 | Carbonate, wat., unf., incremental titration, field, mg/L | 12 | 0 | -- | -- | -- | -- | -- | -- | -- |
| 00940 | Chloride, wat., filt., mg/L | 84 | 26 | 4.5 | 13.13 | 23.75 | 17 | 13 | 8.85 | 5.55 |
| 00950 | Fluoride, wat., filt., mg/L | 82 | 1.3 | -- | 0.203* | *0.300 | *0.200 | *0.200 | *0.100 | *0.068 |
| 00955 | Silica, wat., filt., mg/L | 84 | 13 | 3.7 | 9.513 | 12.75 | 11 | 9.65 | 8.325 | 6.4 |
| 00945 | Sulfate, wat., filt., mg/L | 84 | 730 | 7.1 | 33.302 | 54.5 | 32 | 23 | 16 | 9.875 |
| 99890 | Sulfate, wat., filt., uncorrected, mg/L | 6 | -- | -- | -- | -- | -- | -- | -- | -- |
| 70300 | Residue on evaporation, dried at 180 degrees Celsius, wat., filt., mg/L | 84 | 203 | 48 | 112.714 | 166 | 139.75 | 113.5 | 84 | 63.25 |
| 00608 | Ammonia, wat., filt., mg/L as nitrogen | 78 | 0.34 | -- | 0.058* | *0.146 | *0.070 | *0.040 | *0.030 | *0.012 |
| 00623 | Ammonia plus organic nitrogen, wat., filt., mg/L as nitrogen | 74 | 2.1 | 0.2 | 0.486 | 0.925 | 0.6 | 0.4 | 0.3 | 0.2 |
| 00625 | Ammonia plus organic nitrogen, wat., unf., mg/L as nitrogen | 81 | 2.1 | 0.3 | 0.654 | 0.99 | 0.8 | 0.6 | 0.5 | 0.4 |
| 00610 | Ammonia, wat., unf., mg/L as nitrogen | 45 | 0.37 | 0.01 | 0.06 | 0.148 | 0.075 | 0.04 | 0.03 | 0.01 |
| 00620 | Nitrate, wat., unf., mg/L as nitrogen | 34 | 2.48 | 0.29 | 1.294 | 2.338 | 1.89 | 1.285 | 0.59 | 0.357 |
| 00631 | Nitrite plus nitrate, wat., filt., mg/L as nitrogen | 78 | 3.2 | 0.3 | 1.479 | 2.71 | 2.125 | 1.4 | 0.815 | 0.398 |
| 00630 | Nitrite plus nitrate, wat., unf., mg/L as nitrogen | 45 | 2.9 | 0.3 | 1.286 | 2.47 | 1.9 | 1.3 | 0.6 | 0.4 |
| 00613 | Nitrite, wat., filt., mg/L as nitrogen | 54 | 0.05 | -- | 0.012* | *0.040 | *0.012 | *0.010 | *0.005 | *0.002 |
| 00615 | Nitrite, wat., unf., mg/L as nitrogen | 45 | 0.04 | -- | 0.014* | *0.030 | *0.020 | *0.010 | *0.009 | *0.005 |
| 00605 | Organic nitrogen, wat., unf., mg/L | 77 | 2 | 0.25 | 0.603 | 0.893 | 0.675 | 0.57 | 0.46 | 0.36 |
| 00666 | Phosphorus, wat., filt., mg/L | 78 | 0.34 | 0.02 | 0.116 | 0.311 | 0.17 | 0.09 | 0.06 | 0.02 |
| 00671 | Orthophosphate, wat., filt., mg/L as phosphorus | 78 | 0.33 | 0.01 | 0.107 | 0.271 | 0.16 | 0.08 | 0.05 | 0.02 |
| 70507 | Orthophosphate, wat., unf., mg/L as phosphorus | 45 | 0.32 | 0.01 | 0.103 | 0.307 | 0.125 | 0.08 | 0.055 | 0.02 |
| 00665 | Phosphorus, wat., unf., mg/L | 80 | 0.49 | 0.03 | 0.177 | 0.359 | 0.228 | 0.15 | 0.112 | 0.08 |
| 00680 | Organic carbon, wat., unf., mg/L | 84 | 16 | 4.8 | 7.567 | 12.5 | 8.525 | 6.9 | 6.1 | 5.025 |
| 01105 | Aluminum, wat., unf., recoverable, ug/L | 37 | 6800 | 170 | 1132.973 | 5269.998 | 935 | 630 | 375 | 179 |
| 01002 | Arsenic, wat., unf., ug/L | 37 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01027 | Cadmium, wat., unf., ug/L | 37 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01034 | Chromium, wat., unf., recoverable, ug/L | 37 | 48 | -- | 3.232* | *12.000 | *3.000 | *2.000 | *0.621 | *0.201 |
| 01037 | Cobalt, wat., unf., recoverable, ug/L | 37 | 5 | -- | 1.03* | *3.200 | *1.000 | *0.663 | *0.352 | *0.140 |
| 01042 | Copper, wat., unf., recoverable, ug/L | 36 | 99 | 1 | 10.583 | 75.2 | 9.5 | 5 | 4 | 1 |
| 01045 | Iron, wat., unf., recoverable, ug/L | 37 | 7200 | 220 | 1671.892 | 6930 | 1750 | 1200 | 900 | 319 |
| 01051 | Lead, wat., unf., recoverable, ug/L | 36 | 42 | -- | 7.107* | *33.500 | *7.000 | *4.500 | *2.000 | *0.931 |
| 71900 | Mercury, wat., unf., recoverable, ug/L | 35 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01062 | Molybdenum, wat., unf., recoverable, ug/L | 37 | 3 | -- | 1.062* | *3.000 | *1.000 | *1.000 | *0.507 | *0.252 |
| 01067 | Nickel, wat., unf., recoverable, ug/L | 36 | 7 | 1 | 2.167 | 6.15 | 2 | 2 | 1 | 1 |
| 01147 | Selenium, wat., unf., ug/L | 37 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01077 | Silver, wat., unf., recoverable, ug/L | 36 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01092 | Zinc, wat., unf., recoverable, ug/L | 37 | 60 | -- | 16.863* | *51.000 | *20.000 | *10.000 | *6.565 | *2.877 |
| 80154 | Suspended sediment concentration, mg/L | 78 | 458 | 4 | 64.077 | 228.45 | 73.75 | 37.5 | 23 | 8.95 |

| NWIS Param-eter code | Constituent name | Sample size | Maximum | Minimum | Mean | Percentile |
| --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  | 95th | 75th | 50th | 25th | 5th |
| 02087580 Swift Creek near Apex (October 1988–June 1995) |
| 00061 | Discharge, instantaneous, cubic feet per second | 45 | 111 | 0.19 | 9.758 | 39.3 | 10.5 | 3.9 | 1.15 | 0.267 |
| 00080 | Color, wat., filt., platinum cobalt units | 74 | 280 | 4 | 74.662 | 135 | 100 | 65 | 54.5 | 13.75 |
| 00300 | Dissolved oxygen, wat., unf., mg/L | 74 | 13.8 | 3.9 | 8.541 | 13.125 | 11.025 | 9 | 5.8 | 4.275 |
| 00301 | Dissolved oxygen, wat., unf., percent of saturation | 74 | 151 | 44 | 83.338 | 110.5 | 94 | 84 | 67 | 51.75 |
| 00400 | pH, wat., unf., field, standard units | 75 | 7.6 | 6 | 7.007 | 7.52 | 7.2 | 7 | 6.9 | 6.3 |
| 00403 | pH, wat., unf., laboratory, standard units | 74 | 7.9 | 6.7 | 7.305 | 7.825 | 7.5 | 7.3 | 7.1 | 6.9 |
| 90095 | Specific conductance, wat., unf., laboratory, microsiemens per centimeter at 25 degrees Celsius | 74 | 132 | 69 | 95.041 | 122.25 | 106 | 91.5 | 84 | 74 |
| 00095 | Specific conductance, wat., unf., microsiemens per centimeter at 25 degrees Celsius | 75 | 130 | 68 | 93.067 | 126.4 | 102 | 89 | 83 | 73.6 |
| 00900 | Hardness, wat., unf., mg/L as calcium carbonate | 74 | 46 | 21 | 30.541 | 43.5 | 35 | 28.5 | 25.75 | 23 |
| 00915 | Calcium, wat., filt., mg/L | 74 | 12 | 5.7 | 8.086 | 11.25 | 9.325 | 7.65 | 6.8 | 6.175 |
| 00925 | Magnesium, wat., filt., mg/L | 74 | 3.9 | 1.6 | 2.515 | 3.725 | 2.925 | 2.3 | 2.1 | 1.775 |
| 00935 | Potassium, wat., filt., mg/L | 74 | 4.3 | 0.3 | 2.512 | 3.525 | 2.8 | 2.5 | 2.1 | 1.775 |
| 00931 | Sodium adsorption ratio, wat., number | 74 | 0.8 | 0.2 | 0.403 | 0.5 | 0.4 | 0.4 | 0.4 | 0.3 |
| 00930 | Sodium, wat., filt., mg/L | 74 | 9.3 | 3.1 | 5.028 | 7.125 | 5.625 | 4.9 | 4.375 | 3.275 |
| 00932 | Sodium, wat., percent in equivalents of major cations | 74 | 41 | 16 | 24.459 | 30.25 | 26.25 | 24 | 22 | 18.75 |
| 99430 | Carbonate, wat., unf., incremental titration, field, mg/L as calcium carbonate | 33 | 52 | 17 | 30.667 | 49.9 | 37 | 27 | 23 | 18.4 |
| 90410 | Acid neutralizing capacity, wat., unf., fixed endpoint (pH 4.5) titration, laboratory, mg/L as calcium carbonate | 74 | 48 | 13 | 30.446 | 48 | 37 | 28 | 23 | 19.75 |
| 00410 | Acid neutralizing capacity, wat., unf., fixed endpoint (pH 4.5) titration, field, mg/L as calcium carbonate | 33 | 54 | 17 | 31.212 | 52.6 | 37 | 29 | 23 | 18.4 |
| 99440 | Bicarbonate, wat., unf., incremental titration, field, mg/L | 33 | 63 | 21 | 37.394 | 60.9 | 45 | 33 | 28 | 22.4 |
| 99445 | Carbonate, wat., unf., incremental titration, field, mg/L | 12 | 0 | -- | -- | -- | -- | -- | -- | -- |
| 00940 | Chloride, wat., filt., mg/L | 74 | 7.6 | 0.3 | 5.442 | 7.325 | 6.1 | 5.45 | 4.975 | 3.575 |
| 00950 | Fluoride, wat., filt., mg/L | 74 | 0.3 | -- | 0.11* | *0.300 | *0.100 | *0.100 | *0.064 | *0.037 |
| 00955 | Silica, wat., filt., mg/L | 74 | 16 | 4.3 | 9.158 | 15 | 11 | 8.75 | 7.25 | 4.95 |
| 00945 | Sulfate, wat., filt., mg/L | 74 | 12 | 1.4 | 5.809 | 8.65 | 7 | 5.85 | 4.6 | 2.375 |
| 99890 | Sulfate, wat., filt., uncorrected, mg/L | 5 | -- | -- | -- | -- | -- | -- | -- | -- |
| 70300 | Residue on evaporation, dried at 180 degrees Celsius, wat., filt., mg/L | 74 | 94 | 29 | 63.919 | 88.5 | 72 | 62.5 | 56 | 42.25 |
| 00608 | Ammonia, wat., filt., mg/L as nitrogen | 74 | 0.12 | -- | 0.045* | *0.087 | *0.060 | *0.040 | *0.030 | *0.010 |
| 00623 | Ammonia plus organic nitrogen, wat., filt., mg/L as nitrogen | 73 | 0.6 | -- | 0.3* | *0.530 | *0.400 | *0.300 | *0.200 | *0.152 |
| 00625 | Ammonia plus organic nitrogen, wat., unf., mg/L as nitrogen | 74 | 1.1 | 0.2 | 0.446 | 0.8 | 0.525 | 0.4 | 0.3 | 0.2 |
| 00610 | Ammonia, wat., unf., mg/L as nitrogen | 37 | 0.1 | 0.01 | 0.042 | 0.082 | 0.06 | 0.04 | 0.03 | 0.01 |
| 00620 | Nitrate, wat., unf., mg/L as nitrogen | 14 | 0.27 | 0.05 | 0.142 | 0.27 | 0.19 | 0.145 | 0.07 | 0.05 |
| 00631 | Nitrite plus nitrate, wat., filt., mg/L as nitrogen | 74 | 0.3 | -- | 0.133* | *0.262 | *0.200 | *0.110 | *0.069 | *0.041 |
| 00630 | Nitrite plus nitrate, wat., unf., mg/L as nitrogen | 37 | 0.3 | -- | 0.117* | *0.246 | *0.195 | *0.090 | *0.064 | *0.035 |
| 00613 | Nitrite, wat., filt., mg/L as nitrogen | 60 | 0.03 | -- | 0.008* | *0.020 | *0.010 | *0.007 | *0.005 | *0.003 |
| 00615 | Nitrite, wat., unf., mg/L as nitrogen | 37 | 0.03 | -- | 0.014* | *0.030 | *0.020 | *0.010 | *0.007 | *0.004 |
| 00605 | Organic nitrogen, wat., unf., mg/L | 70 | 1 | 0.12 | 0.409 | 0.764 | 0.505 | 0.37 | 0.278 | 0.181 |
| 00666 | Phosphorus, wat., filt., mg/L | 74 | 0.04 | -- | 0.012* | *0.022 | *0.020 | *0.010 | *0.007 | *0.004 |
| 00671 | Orthophosphate, wat., filt., mg/L as phosphorus | 74 | 0.03 | -- | 0.008* | *0.020 | *0.010 | *0.007 | *0.004 | *0.002 |
| 70507 | Orthophosphate, wat., unf., mg/L as phosphorus | 37 | 0.04 | -- | 0.016* | *0.040 | *0.020 | *0.010 | *0.007 | *0.003 |
| 00665 | Phosphorus, wat., unf., mg/L | 74 | 0.16 | 0.01 | 0.041 | 0.07 | 0.05 | 0.04 | 0.03 | 0.01 |
| 00680 | Organic carbon, wat., unf., mg/L | 73 | 14 | 3.8 | 6.345 | 10.23 | 7.3 | 6 | 5.1 | 4.17 |
| 01105 | Aluminum, wat., unf., recoverable, ug/L | 26 | 2900 | 30 | 525.385 | 2690 | 532.5 | 220 | 107.5 | 30 |
| 01002 | Arsenic, wat., unf., ug/L | 25 | 2 | -- | 0.845* | *1.700 | *1.000 | *0.796 | *0.648 | *0.478 |
| 01027 | Cadmium, wat., unf., ug/L | 26 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01034 | Chromium, wat., unf., recoverable, ug/L | 26 | 5 | -- | 0.987* | *4.650 | *1.000 | *0.426 | *0.163 | *0.040 |
| 01037 | Cobalt, wat., unf., recoverable, ug/L | 26 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01042 | Copper, wat., unf., recoverable, ug/L | 25 | 6 | 1 | 2.36 | 5.7 | 3 | 2 | 1.5 | 1 |
| 01045 | Iron, wat., unf., recoverable, ug/L | 26 | 5200 | 710 | 1471.538 | 4534.999 | 1500 | 1150 | 1000 | 717 |
| 01051 | Lead, wat., unf., recoverable, ug/L | 24 | 4 | -- | 1.229* | *3.750 | *2.000 | *0.932 | *0.525 | *0.238 |
| 01055 | Manganese, wat., unf., recoverable, ug/L | 26 | 380 | 50 | 142.692 | 362.5 | 185 | 105 | 87.5 | 50 |
| 71900 | Mercury, wat., unf., recoverable, ug/L | 26 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01062 | Molybdenum, wat., unf., recoverable, ug/L | 26 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01067 | Nickel, wat., unf., recoverable, ug/L | 24 | 4 | -- | 0.975* | *3.500 | *1.000 | *0.677 | *0.377 | *0.159 |
| 01147 | Selenium, wat., unf., ug/L | 26 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01077 | Silver, wat., unf., recoverable, ug/L | 26 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01092 | Zinc, wat., unf., recoverable, ug/L | 26 | -- | -- | -- | -- | -- | -- | -- | -- |
| 80154 | Suspended sediment concentration, mg/L | 68 | 427 | 2 | 25.441 | 93.65 | 21.75 | 13 | 8 | 3 |

| NWIS Param-eter code | Constituent name | Sample size | Maximum | Minimum | Mean | Percentile |
| --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  | 95th | 75th | 50th | 25th | 5th |
| 02087701 Lake Benson at dam near Garner (October 1989–June 1995) |
| 00080 | Color, wat., filt., platinum cobalt units | 29 | 120.000 | 2.000 | 34.241 | 115.000 | 34.000 | 24.000 | 18.000 | 2.500 |
| 00078 | Transparency, wat., unf., Secchi disc, meters | 13 | 1.600 | 0.450 | 0.769 | 1.600 | 0.950 | 0.650 | 0.500 | 0.450 |
| 00300 | Dissolved oxygen, wat., unf., mg/L | 27 | 11.200 | 4.270 | 8.173 | 11.000 | 9.800 | 8.500 | 6.800 | 4.402 |
| 00301 | Dissolved oxygen, wat., unf., percent of saturation | 27 | 139.000 | 51.000 | 95.593 | 137.800 | 113.000 | 100.000 | 76.000 | 52.200 |
| 00400 | pH, wat., unf., field, standard units | 29 | 8.620 | 6.450 | 7.091 | 8.475 | 7.200 | 7.030 | 6.720 | 6.450 |
| 00403 | pH, wat., unf., laboratory, standard units | 29 | 8.900 | 6.700 | 7.459 | 8.550 | 7.800 | 7.400 | 7.150 | 6.800 |
| 90095 | Specific conductance, wat., unf., laboratory, microsiemens per centimeter at 25 degrees Celsius | 29 | 92.000 | 58.000 | 71.172 | 88.500 | 77.000 | 71.000 | 63.000 | 58.500 |
| 00095 | Specific conductance, wat., unf., microsiemens per centimeter at 25 degrees Celsius | 29 | 94.000 | 53.000 | 69.834 | 88.500 | 74.500 | 70.000 | 63.000 | 56.000 |
| 00900 | Hardness, wat., unf., mg/L as calcium carbonate | 29 | 31.000 | 16.000 | 21.172 | 29.500 | 23.000 | 20.000 | 19.000 | 16.500 |
| 00915 | Calcium, wat., filt., mg/L | 29 | 7.600 | 3.900 | 5.183 | 7.300 | 5.650 | 5.000 | 4.600 | 4.000 |
| 00925 | Magnesium, wat., filt., mg/L | 29 | 2.800 | 1.500 | 1.983 | 2.700 | 2.150 | 1.900 | 1.800 | 1.550 |
| 00935 | Potassium, wat., filt., mg/L | 29 | 11.000 | 0.700 | 2.290 | 7.100 | 2.500 | 2.100 | 1.250 | 0.750 |
| 00931 | Sodium adsorption ratio, wat., number | 29 | 0.500 | 0.300 | 0.414 | 0.500 | 0.400 | 0.400 | 0.400 | 0.350 |
| 00930 | Sodium, wat., filt., mg/L | 29 | 5.300 | 2.900 | 4.379 | 5.150 | 4.800 | 4.400 | 4.000 | 3.250 |
| 00932 | Sodium, wat., percent in equivalents of major cations | 29 | 33.000 | 23.000 | 28.517 | 32.500 | 30.000 | 29.000 | 27.000 | 23.500 |
| 99430 | Carbonate, wat., unf., incremental titration, field, mg/L as calcium carbonate | 13 | 34.000 | 13.000 | 22.385 | 34.000 | 26.500 | 23.000 | 19.000 | 13.000 |
| 90410 | Acid neutralizing capacity, wat., unf., fixed endpoint (pH 4.5) titration, laboratory, mg/L as calcium carbonate | 29 | 34.000 | 14.000 | 22.552 | 31.000 | 25.500 | 22.000 | 19.500 | 15.000 |
| 00410 | Acid neutralizing capacity, wat., unf., fixed endpoint (pH 4.5) titration, field, mg/L as calcium carbonate | 13 | 40.000 | 13.000 | 22.923 | 40.000 | 26.500 | 23.000 | 18.000 | 13.000 |
| 99440 | Bicarbonate, wat., unf., incremental titration, field, mg/L | 13 | 41.000 | 16.000 | 27.154 | 41.000 | 32.500 | 28.000 | 23.000 | 16.000 |
| 99445 | Carbonate, wat., unf., incremental titration, field, mg/L | 10 | 0.000 | -- | -- | -- | -- | -- | -- | -- |
| 00940 | Chloride, wat., filt., mg/L | 28 | 5.800 | 3.300 | 4.371 | 5.665 | 4.875 | 4.350 | 3.825 | 3.345 |
| 00950 | Fluoride, wat., filt., mg/L | 29 | 0.300 | -- | 0.102* | *0.250 | *0.100 | *0.100 | *0.058 | *0.034 |
| 00955 | Silica, wat., filt., mg/L | 29 | 11.000 | 0.800 | 6.090 | 11.000 | 8.350 | 6.600 | 3.750 | 1.000 |
| 00945 | Sulfate, wat., filt., mg/L | 29 | 6.500 | 2.900 | 4.210 | 6.250 | 4.850 | 4.000 | 3.550 | 2.900 |
| 99890 | Sulfate, wat., filt., uncorrected, mg/L | 1 | 7.500 | -- | -- | -- | -- | -- | -- | -- |
| 70300 | Residue on evaporation, dried at 180 degrees Celsius, wat., filt., mg/L | 29 | 76.000 | 32.000 | 48.724 | 74.500 | 53.000 | 48.000 | 42.500 | 33.000 |
| 00608 | Ammonia, wat., filt., mg/L as nitrogen | 29 | 0.200 | -- | 0.049* | *0.195 | *0.055 | *0.030 | *0.020 | *0.006 |
| 00623 | Ammonia plus organic nitrogen, wat., filt., mg/L as nitrogen | 29 | 0.700 | 0.200 | 0.400 | 0.650 | 0.500 | 0.400 | 0.300 | 0.200 |
| 00625 | Ammonia plus organic nitrogen, wat., unf., mg/L as nitrogen | 29 | 3.800 | 0.400 | 0.731 | 2.750 | 0.700 | 0.600 | 0.450 | 0.400 |
| 00610 | Ammonia, wat., unf., mg/L as nitrogen | 14 | 0.200 | -- | 0.046* | *0.200 | *0.058 | *0.030 | *0.010 | *0.003 |
| 00620 | Nitrate, wat., unf., mg/L as nitrogen | 3 | 0.150 | 0.040 | -- | -- | -- | -- | -- | -- |
| 00631 | Nitrite plus nitrate, wat., filt., mg/L as nitrogen | 29 | 0.200 | -- | 0.041* | *0.165 | *0.054 | *0.027 | *0.013 | *0.005 |
| 00630 | Nitrite plus nitrate, wat., unf., mg/L as nitrogen | 14 | -- | -- | -- | -- | -- | -- | -- | -- |
| 00613 | Nitrite, wat., filt., mg/L as nitrogen | 23 | -- | -- | -- | -- | -- | -- | -- | -- |
| 00615 | Nitrite, wat., unf., mg/L as nitrogen | 14 | -- | -- | -- | -- | -- | -- | -- | -- |
| 00605 | Organic nitrogen, wat., unf., mg/L | 27 | 3.800 | 0.330 | 0.704 | 2.920 | 0.640 | 0.550 | 0.390 | 0.342 |
| 00666 | Phosphorus, wat., filt., mg/L | 29 | 0.030 | -- | 0.009* | *0.025 | *0.010 | *0.007 | *0.004 | *0.002 |
| 00671 | Orthophosphate, wat., filt., mg/L as phosphorus | 29 | -- | -- | -- | -- | -- | -- | -- | -- |
| 70507 | Orthophosphate, wat., unf., mg/L as phosphorus | 14 | -- | -- | -- | -- | -- | -- | -- | -- |
| 00665 | Phosphorus, wat., unf., mg/L | 29 | 0.080 | 0.000 | 0.031 | 0.070 | 0.040 | 0.030 | 0.015 | 0.005 |
| 00680 | Organic carbon, wat., unf., mg/L | 29 | 18.000 | 5.600 | 8.269 | 17.500 | 8.700 | 7.400 | 6.550 | 5.600 |
| 70953 | Chlorophyll a, phytoplankton, chromatographic-fluorometric method, ug/L | 29 | 26.300 | 0.100 | 7.445 | 21.400 | 10.500 | 6.100 | 3.150 | 0.800 |
| 70954 | Chlorophyll b, phytoplankton, chromatographic-fluorometric method, ug/L | 29 | 1.700 | -- | 0.394* | *1.500 | *0.500 | *0.200 | *0.109 | *0.045 |
| 01105 | Aluminum, wat., unf., recoverable, ug/L | 29 | 1600.000 | 10.000 | 217.241 | 1400.000 | 210.000 | 100.000 | 70.000 | 25.000 |
| 01002 | Arsenic, wat., unf., ug/L | 29 | 1.000 | -- | 1.000* | *1.000 | *1.000 | *1.000 | *1.000 | *1.000 |
| 01027 | Cadmium, wat., unf., ug/L | 29 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01034 | Chromium, wat., unf., recoverable, ug/L | 29 | 3.000 | -- | 0.809* | *2.500 | *1.000 | *0.674 | *0.458 | *0.259 |
| 01037 | Cobalt, wat., unf., recoverable, ug/L | 29 | 2.000 | -- | 0.588* | *1.500 | *0.742 | *0.492 | *0.325 | *0.177 |
| 01042 | Copper, wat., unf., recoverable, ug/L | 28 | 6.000 | 1.000 | 2.357 | 5.550 | 3.000 | 2.000 | 1.250 | 1.000 |
| 01045 | Iron, wat., unf., recoverable, ug/L | 29 | 2100.000 | 150.000 | 675.862 | 1950.000 | 880.000 | 450.000 | 325.000 | 185.000 |
| 01051 | Lead, wat., unf., recoverable, ug/L | 28 | 3.000 | -- | 1.179* | *3.000 | *2.000 | *0.908 | *0.486 | *0.214 |
| 01055 | Manganese, wat., unf., recoverable, ug/L | 29 | 1400.000 | 30.000 | 243.448 | 1085.000 | 280.000 | 140.000 | 70.000 | 35.000 |
| 71900 | Mercury, wat., unf., recoverable, ug/L | 28 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01062 | Molybdenum, wat., unf., recoverable, ug/L | 29 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01067 | Nickel, wat., unf., recoverable, ug/L | 28 | 3.000 | -- | 1.115* | *2.550 | *2.000 | *0.937 | *0.581 | *0.305 |
| 01147 | Selenium, wat., unf., ug/L | 29 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01077 | Silver, wat., unf., recoverable, ug/L | 29 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01092 | Zinc, wat., unf., recoverable, ug/L | 29 | 20.000 | -- | 6.432* | *20.000 | *8.924 | *4.688 | *2.669 | *1.172 |

| NWIS Param-eter code | Constituent name | Sample size | Maximum | Minimum | Mean | Percentile |
| --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  | 95th | 75th | 50th | 25th | 5th |
| 02096846 Cane Creek near Orange Grove (October 1988–September 2001) |
| 00061 | Discharge, instantaneous, cubic feet per second | 130 | 625.000 | 0.010 | 22.523 | 150.900 | 6.250 | 2.200 | 0.493 | 0.050 |
| 00080 | Color, wat., filt., platinum cobalt units | 123 | 250.000 | 1.000 | 55.537 | 140.000 | 65.000 | 45.000 | 30.000 | 18.400 |
| 00300 | Dissolved oxygen, wat., unf., mg/L | 121 | 15.400 | 3.100 | 9.461 | 13.980 | 11.600 | 9.000 | 7.445 | 5.300 |
| 00301 | Dissolved oxygen, wat., unf., percent of saturation | 118 | 169.000 | 31.000 | 92.153 | 123.100 | 102.000 | 92.000 | 84.750 | 55.800 |
| 00400 | pH, wat., unf., field, standard units | 130 | 8.100 | 5.500 | 6.945 | 7.545 | 7.207 | 7.080 | 6.790 | 5.957 |
| 00403 | pH, wat., unf., laboratory, standard units | 123 | 9.100 | 6.500 | 7.357 | 7.980 | 7.500 | 7.300 | 7.100 | 6.700 |
| 90095 | Specific conductance, wat., unf., laboratory, microsiemens per centimeter at 25 degrees Celsius | 122 | 178.000 | 28.000 | 88.885 | 125.000 | 102.000 | 85.000 | 73.500 | 59.000 |
| 00095 | Specific conductance, wat., unf., microsiemens per centimeter at 25 degrees Celsius | 129 | 175.000 | 26.000 | 85.647 | 125.000 | 98.000 | 82.000 | 69.800 | 51.000 |
| 00900 | Hardness, wat., unf., mg/L as calcium carbonate | 123 | 58.000 | 8.000 | 28.244 | 43.800 | 34.000 | 27.000 | 22.000 | 17.000 |
| 00915 | Calcium, wat., filt., mg/L | 123 | 14.000 | 1.900 | 7.013 | 11.000 | 8.300 | 6.700 | 5.400 | 4.100 |
| 00925 | Magnesium, wat., filt., mg/L | 123 | 5.600 | 0.800 | 2.613 | 3.960 | 3.100 | 2.500 | 2.100 | 1.620 |
| 00935 | Potassium, wat., filt., mg/L | 123 | 13.000 | 0.400 | 2.233 | 6.340 | 2.600 | 1.600 | 1.000 | 0.700 |
| 00931 | Sodium adsorption ratio, wat., number | 123 | 0.500 | 0.200 | 0.395 | 0.500 | 0.400 | 0.400 | 0.400 | 0.300 |
| 00930 | Sodium, wat., filt., mg/L | 123 | 6.600 | 1.200 | 4.837 | 6.180 | 5.400 | 4.900 | 4.400 | 3.200 |
| 00932 | Sodium, wat., percent in equivalents of major cations | 123 | 34.000 | 14.000 | 26.057 | 32.800 | 29.000 | 26.000 | 23.000 | 19.000 |
| 99430 | Carbonate, wat., unf., incremental titration, field, mg/L as calcium carbonate | 56 | 66.000 | 5.000 | 28.804 | 52.150 | 35.000 | 27.500 | 20.000 | 10.850 |
| 90410 | Acid neutralizing capacity, wat., unf., fixed endpoint (pH 4.5) titration, laboratory, mg/L as calcium carbonate | 123 | 65.000 | 5.900 | 27.280 | 48.800 | 35.000 | 24.000 | 19.000 | 12.000 |
| 39086 | Alkalinity, wat., filt., incremental titration, field, mg/L as calcium carbonate | 2 | 53.000 | 26.000 | -- | -- | -- | -- | -- | -- |
| 00410 | Acid neutralizing capacity, wat., unf., fixed endpoint (pH 4.5) titration, field, mg/L as calcium carbonate | 57 | 67.000 | 10.000 | 28.877 | 52.100 | 35.000 | 27.000 | 20.000 | 11.900 |

| NWIS Param-eter code | Constituent name | Sample size | Maximum | Minimum | Mean | Percentile |
| --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  | 95th | 75th | 50th | 25th | 5th |
| 00419 | Acid neutralizing capacity, wat., unf., incremental titration, field, mg/L as calcium carbonate | 13 | 62.000 | 7.000 | 25.615 | 62.000 | 31.500 | 21.000 | 17.500 | 7.000 |
| 99440 | Bicarbonate, wat., unf., incremental titration, field, mg/L | 69 | 81.000 | 5.000 | 34.443 | 63.500 | 42.000 | 33.000 | 23.500 | 12.000 |
| 00453 | Bicarbonate, wat., filt., incremental titration, field, mg/L | 1 | 32.000 | -- | -- | -- | -- | -- | -- | -- |
| 00440 | Bicarbonate, wat., unf., fixed endpoint (pH 4.5) titration, field, mg/L | 1 | 64.000 | -- | -- | -- | -- | -- | -- | -- |
| 99445 | Carbonate, wat., unf., incremental titration, field, mg/L | 12 | 0.000 | -- | -- | -- | -- | -- | -- | -- |
| 00452 | Carbonate, wat., filt., incremental titration, field, mg/L | 1 | 0.000 | -- | -- | -- | -- | -- | -- | -- |
| 00940 | Chloride, wat., filt., mg/L | 118 | 11.000 | 3.100 | 6.169 | 8.700 | 6.800 | 5.950 | 5.300 | 3.995 |
| 00950 | Fluoride, wat., filt., mg/L | 118 | 0.300 | -- | 0.075* | *0.200 | *0.100 | *0.063 | *0.042 | *0.024 |
| 00955 | Silica, wat., filt., mg/L | 118 | 30.000 | 0.100 | 13.025 | 17.000 | 15.000 | 13.000 | 11.000 | 6.790 |
| 00945 | Sulfate, wat., filt., mg/L | 117 | 12.000 | 1.300 | 3.817 | 8.010 | 4.750 | 3.500 | 2.400 | 1.500 |
| 99890 | Sulfate, wat., filt., uncorrected, mg/L | 7 | -- | -- | -- | -- | -- | -- | -- | -- |
| 70300 | Residue on evaporation, dried at 180 degrees Celsius, wat., filt., mg/L | 117 | 146.000 | 25.000 | 66.248 | 92.900 | 74.000 | 65.000 | 56.500 | 43.800 |
| 00608 | Ammonia, wat., filt., mg/L as nitrogen | 122 | 0.360 | -- | 0.036* | *0.110 | *0.040 | *0.020 | *0.009 | *0.003 |
| 00623 | Ammonia plus organic nitrogen, wat., filt., mg/L as nitrogen | 84 | 1.300 | -- | 0.349* | *0.900 | *0.400 | *0.300 | *0.200 | *0.117 |
| 00625 | Ammonia plus organic nitrogen, wat., unf., mg/L as nitrogen | 122 | 2.300 | -- | 0.441* | *1.270 | *0.500 | *0.300 | *0.200 | *0.116 |
| 00610 | Ammonia, wat., unf., mg/L as nitrogen | 45 | 0.340 | -- | 0.050* | *0.272 | *0.045 | *0.030 | *0.020 | *0.004 |
| 00620 | Nitrate, wat., unf., mg/L as nitrogen | 24 | 1.240 | 0.070 | 0.667 | 1.217 | 0.957 | 0.690 | 0.375 | 0.082 |
| 00631 | Nitrite plus nitrate, wat., filt., mg/L as nitrogen | 122 | 1.400 | 0.005 | 0.585 | 1.100 | 0.795 | 0.600 | 0.338 | 0.050 |
| 00630 | Nitrite plus nitrate, wat., unf., mg/L as nitrogen | 45 | 1.300 | 0.076 | 0.638 | 1.170 | 0.900 | 0.600 | 0.365 | 0.105 |
| 00613 | Nitrite, wat., filt., mg/L as nitrogen | 97 | 0.100 | -- | 0.008* | *0.030 | *0.010 | *0.003 | *0.002 | *0.001 |
| 00615 | Nitrite, wat., unf., mg/L as nitrogen | 45 | 0.120 | -- | 0.013* | *0.058 | *0.010 | *0.008 | *0.003 | *0.001 |
| 00605 | Organic nitrogen, wat., unf., mg/L | 92 | 2.000 | 0.130 | 0.476 | 1.335 | 0.558 | 0.360 | 0.270 | 0.170 |
| 00666 | Phosphorus, wat., filt., mg/L | 90 | 0.370 | -- | 0.063* | *0.170 | *0.090 | *0.040 | *0.020 | *0.008 |
| 00671 | Orthophosphate, wat., filt., mg/L as phosphorus | 122 | 0.750 | -- | 0.051* | *0.150 | *0.053 | *0.030 | *0.010 | *0.004 |
| 70507 | Orthophosphate, wat., unf., mg/L as phosphorus | 45 | 0.450 | 0.000 | 0.064 | 0.261 | 0.075 | 0.040 | 0.020 | 0.000 |
| 00665 | Phosphorus, wat., unf., mg/L | 122 | 0.820 | -- | 0.092* | *0.320 | *0.100 | *0.050 | *0.030 | *0.020 |
| 00680 | Organic carbon, wat., unf., mg/L | 122 | 31.000 | 2.100 | 6.289 | 13.000 | 7.500 | 5.000 | 3.650 | 2.815 |
| 31501 | Total coliform, M-Endo MF method, immediate, wat., colonies per 100 milliliters | 4 | 2100.000 | 380.000 | -- | -- | -- | -- | -- | -- |
| 90901 | Escherichia coli, MI MF method, wat., colonies per 100 milliliters | 4 | -- | -- | -- | -- | -- | -- | -- | -- |
| 90902 | Escherichia coli, modified m-TEC MF method, wat., colonies per 100 milliliters | 4 | 1300.000 | 36.000 | -- | -- | -- | -- | -- | -- |
| 31633 | Escherichia coli, m-TEC MF method, wat., colonies per 100 milliliters | 4 | 750.000 | 32.000 | -- | -- | -- | -- | -- | -- |
| 90900 | Total coliform, MI MF method, wat., colonies per 100 milliliters | 4 | 1900.000 | 86.000 | -- | -- | -- | -- | -- | -- |
| 01105 | Aluminum, wat., unf., recoverable, ug/L | 46 | 4080.000 | 10.000 | 331.726 | 1567.501 | 260.000 | 127.000 | 67.500 | 18.960 |
| 01002 | Arsenic, wat., unf., ug/L | 46 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01027 | Cadmium, wat., unf., ug/L | 46 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01034 | Chromium, wat., unf., recoverable, ug/L | 46 | 65.000 | -- | 2.458* | *14.575 | *1.000 | *0.334 | *0.092 | *0.015 |
| 01037 | Cobalt, wat., unf., recoverable, ug/L | 46 | 4.000 | -- | 0.668* | *2.650 | *1.000 | *0.442 | *0.246 | *0.107 |
| 01042 | Copper, wat., unf., recoverable, ug/L | 45 | 14.000 | -- | 2.219* | *8.400 | *2.000 | *2.000 | *0.950 | *0.412 |
| 01045 | Iron, wat., unf., recoverable, ug/L | 46 | 6510.000 | 163.000 | 966.804 | 3215.002 | 952.500 | 745.000 | 517.500 | 273.500 |
| 01051 | Lead, wat., unf., recoverable, ug/L | 46 | 10.000 | -- | 1.081* | *4.650 | *1.000 | *0.598 | *0.306 | *0.109 |
| 01055 | Manganese, wat., unf., recoverable, ug/L | 46 | 681.000 | 10.000 | 100.220 | 567.000 | 102.500 | 40.000 | 23.150 | 10.000 |
| 71900 | Mercury, wat., unf., recoverable, ug/L | 46 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01062 | Molybdenum, wat., unf., recoverable, ug/L | 46 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01067 | Nickel, wat., unf., recoverable, ug/L | 46 | 33.000 | -- | 1.305* | *3.300 | *1.000 | *0.268 | *0.085 | *0.017 |
| 01092 | Zinc, wat., unf., recoverable, ug/L | 46 | -- | -- | -- | -- | -- | -- | -- | -- |
| 80154 | Suspended sediment concentration, mg/L | 122 | 1110.000 | 0.000 | 36.125 | 105.250 | 17.800 | 7.000 | 4.000 | 2.000 |
| 0209684980 Cane Creek Reservoir at dam near White Cross (April 1989–August 2001) |  |
| 00080 | Color, wat., filt., platinum cobalt units | 58 | 120.000 | 1.000 | 36.034 | 75.750 | 55.000 | 25.500 | 20.000 | 9.900 |
| 00078 | Transparency, wat., unf., Secchi disc, meters | 37 | 1.750 | 0.350 | 1.046 | 1.705 | 1.250 | 1.100 | 0.825 | 0.440 |
| 00300 | Dissolved oxygen, wat., unf., mg/L | 75 | 11.600 | 0.080 | 6.413 | 9.908 | 8.600 | 7.200 | 4.630 | 0.248 |
| 00301 | Dissolved oxygen, wat., unf., percent of saturation | 75 | 128.000 | 0.000 | 73.667 | 114.000 | 103.000 | 84.000 | 49.000 | 2.000 |
| 00400 | pH, wat., unf., field, standard units | 76 | 9.200 | 5.820 | 7.117 | 8.818 | 7.500 | 6.900 | 6.600 | 5.964 |
| 00403 | pH, wat., unf., laboratory, standard units | 59 | 9.200 | 6.500 | 7.431 | 8.400 | 7.600 | 7.400 | 7.200 | 6.600 |
| 00480 | Salinity, wat., unf., parts per thousand | 1 | 0.000 | -- | -- | -- | -- | -- | -- | -- |
| 90095 | Specific conductance, wat., unf., laboratory, microsiemens per centimeter at 25 degrees Celsius | 59 | 120.000 | 50.000 | 78.864 | 102.000 | 83.000 | 77.000 | 72.000 | 65.000 |
| 00095 | Specific conductance, wat., unf., microsiemens per centimeter at 25 degrees Celsius | 76 | 163.000 | 42.000 | 81.392 | 142.150 | 84.250 | 76.000 | 69.250 | 61.700 |
| 00900 | Hardness, wat., unf., mg/L as calcium carbonate | 59 | 40.000 | 15.000 | 24.407 | 29.000 | 26.000 | 24.000 | 22.000 | 19.000 |
| 00915 | Calcium, wat., filt., mg/L | 59 | 9.600 | 3.600 | 5.914 | 7.500 | 6.400 | 5.800 | 5.200 | 4.600 |
| 00925 | Magnesium, wat., filt., mg/L | 59 | 3.800 | 1.500 | 2.346 | 2.700 | 2.500 | 2.400 | 2.100 | 1.800 |
| 00935 | Potassium, wat., filt., mg/L | 59 | 3.600 | 1.400 | 2.302 | 3.200 | 2.700 | 2.200 | 1.900 | 1.700 |
| 00931 | Sodium adsorption ratio, wat., number | 59 | 0.400 | 0.200 | 0.331 | 0.400 | 0.400 | 0.300 | 0.300 | 0.300 |
| 00930 | Sodium, wat., filt., mg/L | 59 | 5.800 | 2.400 | 3.834 | 5.300 | 4.100 | 3.900 | 3.500 | 2.400 |
| 00932 | Sodium, wat., percent in equivalents of major cations | 59 | 28.000 | 18.000 | 23.356 | 27.000 | 25.000 | 23.000 | 22.000 | 18.000 |
| 99430 | Carbonate, wat., unf., incremental titration, field, mg/L as calcium carbonate | 25 | 38.000 | 11.000 | 21.560 | 36.200 | 24.500 | 20.000 | 18.500 | 11.600 |
| 90410 | Acid neutralizing capacity, wat., unf., fixed endpoint (pH 4.5) titration, laboratory, mg/L as calcium carbonate | 58 | 36.000 | 13.000 | 24.638 | 33.050 | 28.000 | 24.500 | 21.000 | 17.950 |
| 39086 | Alkalinity, wat., filt., incremental titration, field, mg/L as calcium carbonate | 1 | 26.000 | -- | -- | -- | -- | -- | -- | -- |
| 00410 | Acid neutralizing capacity, wat., unf., fixed endpoint (pH 4.5) titration, field, mg/L as calcium carbonate | 24 | 41.000 | 11.000 | 23.083 | 38.750 | 26.500 | 22.500 | 19.250 | 11.500 |

| NWIS Param-eter code | Constituent name | Sample size | Maximum | Minimum | Mean | Percentile |
| --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  | 95th | 75th | 50th | 25th | 5th |
| 00419 | Acid neutralizing capacity, wat., unf., incremental titration, field, mg/L as calcium carbonate | 9 | 31.000 | 17.000 | 22.111 | 31.000 | 22.500 | 22.000 | 20.500 | 17.000 |
| 99440 | Bicarbonate, wat., unf., incremental titration, field, mg/L | 33 | 46.000 | 13.000 | 26.445 | 41.100 | 28.500 | 26.000 | 23.000 | 15.100 |
| 00453 | Bicarbonate, wat., filt., incremental titration, field, mg/L | 1 | 32.000 | -- | -- | -- | -- | -- | -- | -- |
| 99445 | Carbonate, wat., unf., incremental titration, field, mg/L | 10 | 0.000 | -- | -- | -- | -- | -- | -- | -- |
| 00452 | Carbonate, wat., filt., incremental titration, field, mg/L | 1 | 0.000 | -- | -- | -- | -- | -- | -- | -- |
| 00940 | Chloride, wat., filt., mg/L | 58 | 6.900 | 3.700 | 5.009 | 6.005 | 5.500 | 5.050 | 4.600 | 3.895 |
| 00950 | Fluoride, wat., filt., mg/L | 58 | 0.200 | -- | 0.085* | *0.200 | *0.100 | *0.076 | *0.054 | *0.035 |
| 00955 | Silica, wat., filt., mg/L | 57 | 16.000 | 2.200 | 6.953 | 13.100 | 7.550 | 6.700 | 5.550 | 3.220 |
| 00945 | Sulfate, wat., filt., mg/L | 58 | 7.000 | 1.200 | 3.803 | 5.515 | 4.350 | 3.900 | 3.000 | 1.785 |
| 99890 | Sulfate, wat., filt., uncorrected, mg/L | 3 | -- | -- | -- | -- | -- | -- | -- | -- |
| 70300 | Residue on evaporation, dried at 180 degrees Celsius, wat., filt., mg/L | 57 | 88.000 | 29.000 | 55.491 | 75.500 | 60.000 | 54.000 | 50.000 | 38.000 |
| 00608 | Ammonia, wat., filt., mg/L as nitrogen | 67 | 2.270 | -- | 0.137* | *0.610 | *0.098 | *0.030 | *0.010 | *0.004 |
| 00623 | Ammonia plus organic nitrogen, wat., filt., mg/L as nitrogen | 39 | 1.700 | 0.200 | 0.490 | 1.100 | 0.600 | 0.400 | 0.300 | 0.200 |
| 00625 | Ammonia plus organic nitrogen, wat., unf., mg/L as nitrogen | 67 | 3.100 | 0.300 | 0.730 | 1.480 | 0.800 | 0.600 | 0.500 | 0.400 |
| 00610 | Ammonia, wat., unf., mg/L as nitrogen | 19 | 0.660 | -- | 0.181* | *0.660 | *0.540 | *0.060 | *0.010 | *0.002 |
| 00620 | Nitrate, wat., unf., mg/L as nitrogen | 2 | 0.410 | 0.280 | -- | -- | -- | -- | -- | -- |
| 00631 | Nitrite plus nitrate, wat., filt., mg/L as nitrogen | 67 | 1.700 | -- | 0.127* | *0.486 | *0.160 | *0.020 | *0.005 | *0.001 |
| 00630 | Nitrite plus nitrate, wat., unf., mg/L as nitrogen | 19 | 1.700 | -- | 0.177* | *1.700 | *0.200 | *0.024 | *0.006 | *0.001 |
| 00613 | Nitrite, wat., filt., mg/L as nitrogen | 58 | 0.020 | -- | 0.004* | *0.014 | *0.005 | *0.002 | *0.001 | *0.000 |
| 00615 | Nitrite, wat., unf., mg/L as nitrogen | 19 | -- | -- | -- | -- | -- | -- | -- | -- |
| 00605 | Organic nitrogen, wat., unf., mg/L | 63 | 1.600 | 0.310 | 0.569 | 0.924 | 0.640 | 0.500 | 0.420 | 0.362 |
| 00666 | Phosphorus, wat., filt., mg/L | 39 | 0.200 | -- | 0.016* | *0.060 | *0.020 | *0.006 | *0.002 | *0.000 |
| 00671 | Orthophosphate, wat., filt., mg/L as phosphorus | 67 | 0.200 | -- | 0.012* | *0.065 | *0.007 | *0.002 | *0.001 | *0.000 |
| 70507 | Orthophosphate, wat., unf., mg/L as phosphorus | 19 | 0.200 | -- | 0.017* | *0.200 | *0.010 | *0.002 | *0.000 | *0.000 |
| 00665 | Phosphorus, wat., unf., mg/L | 66 | 0.250 | -- | 0.039* | *0.108 | *0.040 | *0.030 | *0.020 | *0.009 |
| 00680 | Organic carbon, wat., unf., mg/L | 59 | 49.000 | 2.900 | 8.498 | 16.000 | 8.800 | 7.400 | 6.400 | 4.100 |
| 70953 | Chlorophyll a, phytoplankton, chromatographic-fluorometric method, ug/L | 59 | 87.800 | 0.100 | 10.849 | 37.300 | 11.000 | 7.800 | 3.500 | 0.800 |
| 70954 | Chlorophyll b, phytoplankton, chromatographic-fluorometric method, ug/L | 59 | 11.700 | -- | 0.540* | *1.800 | *0.500 | *0.100 | *0.037 | *0.007 |
| 01105 | Aluminum, wat., unf., recoverable, ug/L | 46 | 360.000 | 10.000 | 70.665 | 252.500 | 83.325 | 50.000 | 30.000 | 18.245 |
| 01002 | Arsenic, wat., unf., ug/L | 46 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01027 | Cadmium, wat., unf., ug/L | 46 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01034 | Chromium, wat., unf., recoverable, ug/L | 46 | 8.400 | -- | 0.910* | *3.930 | *1.000 | *0.567 | *0.296 | *0.117 |
| 01037 | Cobalt, wat., unf., recoverable, ug/L | 46 | 4.000 | -- | 0.681* | *3.650 | *0.774 | *0.321 | *0.132 | *0.039 |
| 01042 | Copper, wat., unf., recoverable, ug/L | 45 | 400.000 | -- | 10.704* | *8.800 | *2.000 | *2.000 | *0.769 | *0.249 |
| 01045 | Iron, wat., unf., recoverable, ug/L | 65 | 15400.000 | 68.400 | 1349.960 | 9574.001 | 740.000 | 430.000 | 229.000 | 118.800 |
| 01051 | Lead, wat., unf., recoverable, ug/L | 46 | 3.000 | -- | 0.837* | *2.000 | *1.000 | *0.655 | *0.417 | *0.204 |
| 01055 | Manganese, wat., unf., recoverable, ug/L | 65 | 5600.000 | 30.000 | 960.242 | 5195.000 | 1200.000 | 290.000 | 82.700 | 30.000 |
| 71900 | Mercury, wat., unf., recoverable, ug/L | 46 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01062 | Molybdenum, wat., unf., recoverable, ug/L | 46 | 3.000 | -- | 0.494* | *2.000 | *0.587 | *0.300 | *0.153 | *0.054 |
| 01067 | Nickel, wat., unf., recoverable, ug/L | 46 | 15.000 | -- | 1.634* | *9.200 | *2.000 | *0.819 | *0.373 | *0.126 |
| 01147 | Selenium, wat., unf., ug/L | 46 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01077 | Silver, wat., unf., recoverable, ug/L | 43 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01092 | Zinc, wat., unf., recoverable, ug/L | 46 | 70.000 | -- | 6.205* | *20.000 | *6.707 | *2.714 | *1.095 | *0.313 |
| 02096960 Haw River near Bynum (November 1998–February 1998) |
| 00060 | Discharge, cubic feet per second | 1 | 328.000 | -- | -- | -- | -- | -- | -- | -- |
| 00061 | Discharge, instantaneous, cubic feet per second | 40 | 25000.000 | 55.000 | 4979.400 | 23430.002 | 5550.000 | 2740.000 | 343.000 | 56.950 |
| 00080 | Color, wat., filt., platinum cobalt units | 10 | 350.000 | 80.000 | 208.000 | 350.000 | 242.500 | 220.000 | 147.500 | 80.000 |
| 00300 | Dissolved oxygen, wat., unf., mg/L | 35 | 14.200 | 3.000 | 9.474 | 14.200 | 11.200 | 9.100 | 7.800 | 5.240 |
| 00301 | Dissolved oxygen, wat., unf., percent of saturation | 16 | 120.000 | 68.000 | 99.250 | 120.000 | 103.000 | 101.000 | 97.500 | 68.000 |
| 00400 | pH, wat., unf., field, standard units | 41 | 8.600 | 6.100 | 7.198 | 7.989 | 7.500 | 7.200 | 6.950 | 6.200 |
| 00403 | pH, wat., unf., laboratory, standard units | 10 | 7.700 | 6.800 | 7.310 | 7.700 | 7.600 | 7.400 | 7.075 | 6.800 |
| 90095 | Specific conductance, wat., unf., laboratory, microsiemens per centimeter at 25 degrees Celsius | 10 | 369.000 | 66.000 | 120.100 | 369.000 | 126.750 | 87.500 | 76.250 | 66.000 |
| 00095 | Specific conductance, wat., unf., microsiemens per centimeter at 25 degrees Celsius | 41 | 524.000 | 64.000 | 170.488 | 508.800 | 218.500 | 115.000 | 85.000 | 67.100 |
| 00900 | Hardness, wat., unf., mg/L as calcium carbonate | 10 | 41.000 | 19.000 | 24.500 | 41.000 | 27.000 | 23.000 | 19.750 | 19.000 |
| 00915 | Calcium, wat., filt., mg/L | 10 | 9.800 | 4.500 | 5.880 | 9.800 | 6.400 | 5.550 | 4.775 | 4.500 |
| 00925 | Magnesium, wat., filt., mg/L | 10 | 3.900 | 1.800 | 2.420 | 3.900 | 2.625 | 2.250 | 2.000 | 1.800 |
| 00935 | Potassium, wat., filt., mg/L | 10 | 6.200 | 1.400 | 2.870 | 6.200 | 3.475 | 2.550 | 1.975 | 1.400 |
| 00931 | Sodium adsorption ratio, wat., number | 10 | 4.000 | 0.400 | 0.970 | 4.000 | 1.000 | 0.600 | 0.475 | 0.400 |
| 00930 | Sodium, wat., filt., mg/L | 10 | 54.000 | 3.600 | 12.000 | 54.000 | 12.750 | 6.550 | 4.700 | 3.600 |
| 00932 | Sodium, wat., percent in equivalents of major cations | 10 | 71.000 | 27.000 | 39.700 | 71.000 | 46.750 | 35.000 | 30.750 | 27.000 |
| 99430 | Carbonate, wat., unf., incremental titration, field, mg/L as calcium carbonate | 5 | 33.000 | 13.000 | -- | -- | -- | -- | -- | -- |
| 90410 | Acid neutralizing capacity, wat., unf., fixed endpoint (pH 4.5) titration, laboratory, mg/L as calcium carbonate | 10 | 55.000 | 15.000 | 22.900 | 55.000 | 22.750 | 20.000 | 16.750 | 15.000 |
| 00410 | Acid neutralizing capacity, wat., unf., fixed endpoint (pH 4.5) titration, field, mg/L as calcium carbonate | 4 | 33.000 | 20.000 | -- | -- | -- | -- | -- | -- |
| 99440 | Bicarbonate, wat., unf., incremental titration, field, mg/L | 5 | 40.000 | 16.000 | -- | -- | -- | -- | -- | -- |
| 00440 | Bicarbonate, wat., unf., fixed endpoint (pH 4.5) titration, field, mg/L | 1 | 0.000 | -- | -- | -- | -- | -- | -- | -- |

| NWIS Param-eter code | Constituent name | Sample size | Maximum | Minimum | Mean | Percentile |
| --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  | 95th | 75th | 50th | 25th | 5th |
| 99445 | Carbonate, wat., unf., incremental titration, field, mg/L | 2 | 0.000 | -- | -- | -- | -- | -- | -- | -- |
| 00940 | Chloride, wat., filt., mg/L | 10 | 41.000 | 3.600 | 10.290 | 41.000 | 10.600 | 6.350 | 4.125 | 3.600 |
| 00950 | Fluoride, wat., filt., mg/L | 10 | 0.400 | -- | 0.106* | *0.400 | *0.100 | *0.100 | *0.042 | *0.025 |
| 00955 | Silica, wat., filt., mg/L | 10 | 12.000 | 6.800 | 8.920 | 12.000 | 10.250 | 8.850 | 7.075 | 6.800 |
| 00945 | Sulfate, wat., filt., mg/L | 10 | 51.000 | 6.900 | 13.570 | 51.000 | 12.500 | 9.300 | 7.275 | 6.900 |
| 70300 | Residue on evaporation, dried at 180 degrees Celsius, wat., filt., mg/L | 10 | 222.000 | 52.000 | 89.700 | 222.000 | 99.000 | 77.500 | 55.750 | 52.000 |
| 00608 | Ammonia, wat., filt., mg/L as nitrogen | 5 | 0.210 | 0.010 | -- | -- | -- | -- | -- | -- |
| 00623 | Ammonia plus organic nitrogen, wat., filt., mg/L as nitrogen | 4 | -- | -- | -- | -- | -- | -- | -- | -- |
| 00625 | Ammonia plus organic nitrogen, wat., unf., mg/L as nitrogen | 9 | 1.700 | 0.600 | 0.933 | 1.700 | 1.050 | 0.900 | 0.700 | 0.600 |
| 00610 | Ammonia, wat., unf., mg/L as nitrogen | 4 | 0.130 | 0.050 | -- | -- | -- | -- | -- | -- |
| 00620 | Nitrate, wat., unf., mg/L as nitrogen | 3 | 1.980 | 0.410 | -- | -- | -- | -- | -- | -- |
| 00631 | Nitrite plus nitrate, wat., filt., mg/L as nitrogen | 5 | 0.560 | 0.280 | -- | -- | -- | -- | -- | -- |
| 00630 | Nitrite plus nitrate, wat., unf., mg/L as nitrogen | 4 | 2.000 | 0.270 | -- | -- | -- | -- | -- | -- |
| 00613 | Nitrite, wat., filt., mg/L as nitrogen | 5 | -- | -- | -- | -- | -- | -- | -- | -- |
| 00615 | Nitrite, wat., unf., mg/L as nitrogen | 4 | -- | -- | -- | -- | -- | -- | -- | -- |
| 00605 | Organic nitrogen, wat., unf., mg/L | 9 | 1.600 | 0.540 | 0.836 | 1.600 | 0.915 | 0.750 | 0.625 | 0.540 |
| 00666 | Phosphorus, wat., filt., mg/L | 4 | 0.110 | 0.030 | -- | -- | -- | -- | -- | -- |
| 00671 | Orthophosphate, wat., filt., mg/L as phosphorus | 5 | 0.120 | 0.040 | -- | -- | -- | -- | -- | -- |
| 70507 | Orthophosphate, wat., unf., mg/L as phosphorus | 4 | 0.280 | 0.020 | -- | -- | -- | -- | -- | -- |
| 00665 | Phosphorus, wat., unf., mg/L | 9 | 0.580 | 0.070 | 0.229 | 0.580 | 0.255 | 0.200 | 0.150 | 0.070 |
| 00680 | Organic carbon, wat., unf., mg/L | 10 | 22.000 | 9.200 | 13.350 | 22.000 | 14.500 | 13.000 | 10.575 | 9.200 |
| 01105 | Aluminum, wat., unf., recoverable, ug/L | 10 | 5900.000 | 1000.000 | 2580.000 | 5900.000 | 3325.000 | 2000.000 | 1650.000 | 1000.000 |
| 01002 | Arsenic, wat., unf., ug/L | 10 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01027 | Cadmium, wat., unf., ug/L | 10 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01034 | Chromium, wat., unf., recoverable, ug/L | 10 | 11.000 | 1.000 | 6.030 | 11.000 | 8.250 | 5.500 | 4.500 | 1.000 |
| 01037 | Cobalt, wat., unf., recoverable, ug/L | 10 | 10.000 | -- | 3.477* | *10.000 | *4.000 | *3.000 | *1.750 | *0.770 |
| 01042 | Copper, wat., unf., recoverable, ug/L | 10 | 32.000 | 5.000 | 16.200 | 32.000 | 24.500 | 13.500 | 8.500 | 5.000 |
| 01045 | Iron, wat., unf., recoverable, ug/L | 10 | 9200.000 | 1700.000 | 3820.000 | 9200.000 | 4400.000 | 3350.000 | 2450.000 | 1700.000 |
| 01051 | Lead, wat., unf., recoverable, ug/L | 10 | 59.000 | 5.000 | 23.700 | 59.000 | 39.000 | 13.500 | 10.000 | 5.000 |
| 01055 | Manganese, wat., unf., recoverable, ug/L | 10 | 730.000 | 110.000 | 354.000 | 730.000 | 485.000 | 335.000 | 192.500 | 110.000 |
| 71900 | Mercury, wat., unf., recoverable, ug/L | 10 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01062 | Molybdenum, wat., unf., recoverable, ug/L | 10 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01067 | Nickel, wat., unf., recoverable, ug/L | 10 | 7.000 | 2.000 | 4.400 | 7.000 | 6.000 | 4.000 | 3.000 | 2.000 |
| 01147 | Selenium, wat., unf., ug/L | 10 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01077 | Silver, wat., unf., recoverable, ug/L | 10 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01092 | Zinc, wat., unf., recoverable, ug/L | 10 | 60.000 | 20.000 | 35.000 | 60.000 | 42.500 | 30.000 | 27.500 | 20.000 |
| 80154 | Suspended sediment concentration, mg/L | 17 | 691.000 | 49.000 | 254.647 | 691.000 | 338.000 | 209.000 | 146.000 | 49.000 |
| 0209719700 B.E. Jordan Lake, Haw River arm above B.E. Jordan dam (December 1988–August 2001) |
| 00080 | Color, wat., filt., platinum cobalt units | 42 | 130.000 | 15.000 | 35.310 | 76.700 | 43.500 | 30.000 | 22.250 | 15.000 |
| 00078 | Transparency, wat., unf., Secchi disc, meters | 37 | 0.950 | 0.300 | 0.628 | 0.905 | 0.750 | 0.650 | 0.525 | 0.345 |
| 00300 | Dissolved oxygen, wat., unf., mg/L | 64 | 14.200 | 0.300 | 8.581 | 13.225 | 10.600 | 8.635 | 7.100 | 2.027 |
| 00301 | Dissolved oxygen, wat., unf., percent of saturation | 56 | 184.000 | 3.000 | 97.661 | 180.150 | 115.750 | 95.000 | 75.250 | 20.900 |
| 00400 | pH, wat., unf., field, standard units | 65 | 11.500 | 6.320 | 7.902 | 10.580 | 8.925 | 7.500 | 7.000 | 6.450 |
| 00403 | pH, wat., unf., laboratory, standard units | 42 | 10.100 | 6.900 | 7.981 | 9.485 | 8.550 | 7.600 | 7.300 | 7.200 |
| 90095 | Specific conductance, wat., unf., laboratory, microsiemens per centimeter at 25 degrees Celsius | 42 | 367.000 | 106.000 | 193.095 | 332.750 | 222.250 | 193.500 | 157.500 | 114.300 |
| 00095 | Specific conductance, wat., unf., microsiemens per centimeter at 25 degrees Celsius | 65 | 362.000 | 101.000 | 184.585 | 285.100 | 215.500 | 185.000 | 144.000 | 104.300 |
| 00900 | Hardness, wat., unf., mg/L as calcium carbonate | 42 | 42.000 | 25.000 | 31.167 | 38.550 | 33.250 | 31.000 | 29.000 | 25.000 |
| 00915 | Calcium, wat., filt., mg/L | 42 | 10.000 | 5.900 | 7.590 | 9.210 | 8.000 | 7.600 | 7.075 | 6.015 |
| 00925 | Magnesium, wat., filt., mg/L | 42 | 3.900 | 2.300 | 2.969 | 3.840 | 3.200 | 3.000 | 2.775 | 2.300 |
| 00935 | Potassium, wat., filt., mg/L | 42 | 6.700 | 2.200 | 3.788 | 5.710 | 4.225 | 3.700 | 3.100 | 2.400 |
| 00931 | Sodium adsorption ratio, wat., number | 42 | 4.000 | 0.800 | 1.745 | 3.850 | 2.000 | 2.000 | 1.000 | 0.900 |
| 00930 | Sodium, wat., filt., mg/L | 42 | 56.000 | 9.900 | 23.164 | 48.200 | 28.250 | 23.000 | 15.000 | 10.000 |
| 00932 | Sodium, wat., percent in equivalents of major cations | 42 | 72.000 | 42.000 | 56.190 | 70.400 | 62.000 | 58.500 | 51.000 | 42.150 |
| 99430 | Carbonate, wat., unf., incremental titration, field, mg/L as calcium carbonate | 22 | 54.000 | 24.000 | 35.500 | 53.700 | 38.750 | 34.500 | 29.750 | 24.000 |
| 90410 | Acid neutralizing capacity, wat., unf., fixed endpoint (pH 4.5) titration, laboratory, mg/L as calcium carbonate | 42 | 56.000 | 24.000 | 37.024 | 52.100 | 41.250 | 37.500 | 32.000 | 25.150 |
| 39086 | Alkalinity, wat., filt., incremental titration, field, mg/L as calcium carbonate | 1 | 36.000 | -- | -- | -- | -- | -- | -- | -- |
| 00410 | Acid neutralizing capacity, wat., unf., fixed endpoint (pH 4.5) titration, field, mg/L as calcium carbonate | 23 | 54.000 | 24.000 | 37.000 | 53.800 | 42.000 | 35.000 | 31.000 | 24.400 |
| 00419 | Acid neutralizing capacity, wat., unf., incremental titration, field, mg/L as calcium carbonate | 7 | 43.000 | 25.000 | 35.571 | 43.000 | 42.000 | 34.000 | 31.000 | 25.000 |
| 99440 | Bicarbonate, wat., unf., incremental titration, field, mg/L | 29 | 66.000 | 10.000 | 39.041 | 64.500 | 49.000 | 38.000 | 30.000 | 11.500 |
| 00453 | Bicarbonate, wat., filt., incremental titration, field, mg/L | 1 | 44.000 | -- | -- | -- | -- | -- | -- | -- |
| 99445 | Carbonate, wat., unf., incremental titration, field, mg/L | 12 | 16.000 | 0.000 | 4.500 | 16.000 | 9.750 | 1.500 | 0.000 | 0.000 |
| 00452 | Carbonate, wat., filt., incremental titration, field, mg/L | 1 | 0.000 | -- | -- | -- | -- | -- | -- | -- |
| 00940 | Chloride, wat., filt., mg/L | 41 | 35.000 | 6.800 | 16.961 | 31.500 | 21.000 | 16.000 | 12.500 | 8.450 |
| 00950 | Fluoride, wat., filt., mg/L | 41 | 0.400 | 0.100 | 0.217 | 0.390 | 0.300 | 0.200 | 0.200 | 0.100 |
| 00955 | Silica, wat., filt., mg/L | 40 | 12.000 | 4.100 | 7.153 | 10.950 | 8.075 | 6.850 | 5.925 | 4.105 |
| 00945 | Sulfate, wat., filt., mg/L | 41 | 53.000 | 10.000 | 23.024 | 48.000 | 28.500 | 23.000 | 16.000 | 11.000 |
| 70300 | Residue on evaporation, dried at 180 degrees Celsius, wat., filt., mg/L | 40 | 220.000 | 74.000 | 117.125 | 201.200 | 127.500 | 116.500 | 98.500 | 76.150 |
| 00608 | Ammonia, wat., filt., mg/L as nitrogen | 49 | 0.427 | -- | 0.045* | *0.156 | *0.050 | *0.030 | *0.008 | *0.003 |
| 00623 | Ammonia plus organic nitrogen, wat., filt., mg/L as nitrogen | 21 | 1.100 | 0.300 | 0.519 | 1.070 | 0.700 | 0.400 | 0.400 | 0.300 |
| 00625 | Ammonia plus organic nitrogen, wat., unf., mg/L as nitrogen | 49 | 2.000 | 0.200 | 0.814 | 1.400 | 0.900 | 0.700 | 0.600 | 0.450 |
| 00610 | Ammonia, wat., unf., mg/L as nitrogen | 3 | 0.050 | 0.020 | -- | -- | -- | -- | -- | -- |
| 00620 | Nitrate, wat., unf., mg/L as nitrogen | 2 | 0.330 | 0.190 | -- | -- | -- | -- | -- | -- |
| 00631 | Nitrite plus nitrate, wat., filt., mg/L as nitrogen | 49 | 1.500 | -- | 0.325* | *0.805 | *0.495 | *0.260 | *0.090 | *0.028 |
| 00630 | Nitrite plus nitrate, wat., unf., mg/L as nitrogen | 3 | -- | -- | -- | -- | -- | -- | -- | -- |
| 00613 | Nitrite, wat., filt., mg/L as nitrogen | 49 | 0.040 | -- | 0.013* | *0.032 | *0.020 | *0.010 | *0.007 | *0.001 |
| 00615 | Nitrite, wat., unf., mg/L as nitrogen | 3 | 0.030 | 0.020 | -- | -- | -- | -- | -- | -- |
| 00605 | Organic nitrogen, wat., unf., mg/L | 43 | 2.000 | 0.330 | 0.796 | 1.460 | 0.920 | 0.750 | 0.570 | 0.394 |
| 00666 | Phosphorus, wat., filt., mg/L | 22 | 0.240 | -- | 0.033* | *0.215 | *0.040 | *0.020 | *0.009 | *0.003 |
| 00671 | Orthophosphate, wat., filt., mg/L as phosphorus | 49 | 0.220 | -- | 0.022* | *0.087 | *0.022 | *0.010 | *0.005 | *0.001 |
| 70507 | Orthophosphate, wat., unf., mg/L as phosphorus | 3 | -- | -- | -- | -- | -- | -- | -- | -- |
| 00665 | Phosphorus, wat., unf., mg/L | 49 | 0.250 | 0.010 | 0.080 | 0.175 | 0.100 | 0.070 | 0.045 | 0.015 |
| 00680 | Organic carbon, wat., unf., mg/L | 39 | 14.000 | 6.500 | 8.651 | 14.000 | 9.600 | 8.200 | 7.300 | 6.600 |
| 32213 | Pheophytin a, fluorometric method, ug/L | 7 | -- | -- | -- | -- | -- | -- | -- | -- |
| 32209 | Chlorophyll a, fluorometric method, corrected, wat., ug/L | 7 | 54.000 | 6.000 | 25.429 | 54.000 | 54.000 | 21.000 | 7.000 | 6.000 |

| NWIS Param-eter code | Constituent name | Sample size | Maximum | Minimum | Mean | Percentile |
| --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  | 95th | 75th | 50th | 25th | 5th |
| 32217 | Chlorophyll a, fluorometric method, uncorrected, ug/L | 7 | 61.000 | 7.000 | 27.857 | 61.000 | 54.000 | 21.000 | 8.000 | 7.000 |
| 70953 | Chlorophyll a, phytoplankton, chromatographic-fluorometric method, ug/L | 42 | 61.400 | 1.100 | 16.171 | 43.905 | 22.925 | 12.100 | 7.075 | 1.450 |
| 70954 | Chlorophyll b, phytoplankton, chromatographic-fluorometric method, ug/L | 41 | 123.000 | -- | 3.855* | *3.030 | *1.200 | *0.800 | *0.300 | *0.077 |
| 01105 | Aluminum, wat., unf., recoverable, ug/L | 29 | 530.000 | 40.000 | 124.483 | 390.000 | 158.000 | 100.000 | 70.800 | 45.000 |
| 01002 | Arsenic, wat., unf., ug/L | 29 | 2.000 | -- | 0.701* | *1.500 | *0.898 | *0.634 | *0.491 | *0.305 |
| 01025 | Cadmium, wat., filt., ug/L | 1 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01027 | Cadmium, wat., unf., ug/L | 29 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01034 | Chromium, wat., unf., recoverable, ug/L | 29 | 7.000 | -- | 0.898* | *4.500 | *0.995 | *0.571 | *0.287 | *0.107 |
| 01037 | Cobalt, wat., unf., recoverable, ug/L | 29 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01040 | Copper, wat., filt., ug/L | 1 | 1.000 | -- | -- | -- | -- | -- | -- | -- |
| 01042 | Copper, wat., unf., recoverable, ug/L | 29 | 6.000 | 1.000 | 2.414 | 5.500 | 3.000 | 2.000 | 2.000 | 1.000 |
| 01045 | Iron, wat., unf., recoverable, ug/L | 46 | 2260.000 | 70.000 | 437.783 | 1536.501 | 505.000 | 314.500 | 190.000 | 93.500 |
| 01049 | Lead, wat., filt., ug/L | 1 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01051 | Lead, wat., unf., recoverable, ug/L | 29 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01056 | Manganese, wat., filt., ug/L | 1 | 34.000 | -- | -- | -- | -- | -- | -- | -- |
| 01055 | Manganese, wat., unf., recoverable, ug/L | 46 | 1990.000 | 10.000 | 173.517 | 1643.501 | 94.500 | 60.000 | 39.875 | 20.000 |
| 71900 | Mercury, wat., unf., recoverable, ug/L | 29 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01062 | Molybdenum, wat., unf., recoverable, ug/L | 29 | 4.000 | -- | 1.903* | *4.000 | *2.100 | *2.000 | *0.998 | *0.567 |
| 01147 | Selenium, wat., unf., ug/L | 29 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01077 | Silver, wat., unf., recoverable, ug/L | 29 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01090 | Zinc, wat., filt., ug/L | 1 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01092 | Zinc, wat., unf., recoverable, ug/L | 29 | 40.000 | -- | 8.127* | *35.000 | *9.700 | *4.963 | *2.669 | *1.035 |
| 02097314 New Hope Creek near Blands (December 1988–March 2001) |
| 00061 | Discharge, instantaneous, cubic feet per second | 25 | 1900.000 | 7.000 | 134.192 | 1419.701 | 66.000 | 34.000 | 14.000 | 7.660 |
| 00080 | Color, wat., filt., platinum cobalt units | 4 | 130.000 | 50.000 | -- | -- | -- | -- | -- | -- |
| 00076 | Turbidity, wat., unf., nephelometric turbidity units | 1 | 19.400 | -- | -- | -- | -- | -- | -- | -- |
| 00300 | Dissolved oxygen, wat., unf., mg/L | 25 | 9.900 | 4.400 | 7.268 | 9.660 | 8.400 | 7.530 | 6.000 | 4.430 |
| 00301 | Dissolved oxygen, wat., unf., percent of saturation | 8 | 87.000 | 67.000 | 77.500 | 87.000 | 81.750 | 79.500 | 72.000 | 67.000 |
| 00400 | pH, wat., unf., field, standard units | 24 | 8.980 | 6.120 | 7.025 | 8.560 | 7.193 | 7.035 | 6.815 | 6.202 |
| 00403 | pH, wat., unf., laboratory, standard units | 4 | 7.500 | 6.600 | -- | -- | -- | -- | -- | -- |
| 90095 | Specific conductance, wat., unf., laboratory, microsiemens per centimeter at 25 degrees Celsius | 4 | 257.000 | 57.000 | -- | -- | -- | -- | -- | -- |
| 00095 | Specific conductance, wat., unf., microsiemens per centimeter at 25 degrees Celsius | 26 | 430.000 | 57.000 | 226.962 | 413.900 | 318.500 | 218.500 | 137.000 | 71.000 |
| 00900 | Hardness, wat., unf., mg/L as calcium carbonate | 4 | 55.000 | 17.000 | -- | -- | -- | -- | -- | -- |
| 00915 | Calcium, wat., filt., mg/L | 4 | 15.000 | 4.700 | -- | -- | -- | -- | -- | -- |
| 00925 | Magnesium, wat., filt., mg/L | 4 | 4.400 | 1.400 | -- | -- | -- | -- | -- | -- |
| 00935 | Potassium, wat., filt., mg/L | 4 | 5.000 | 2.000 | -- | -- | -- | -- | -- | -- |
| 00931 | Sodium adsorption ratio, wat., number | 4 | 1.000 | 0.300 | -- | -- | -- | -- | -- | -- |
| 00930 | Sodium, wat., filt., mg/L | 4 | 25.000 | 2.700 | -- | -- | -- | -- | -- | -- |
| 00932 | Sodium, wat., percent in equivalents of major cations | 4 | 47.000 | 23.000 | -- | -- | -- | -- | -- | -- |
| 99430 | Carbonate, wat., unf., incremental titration, field, mg/L as calcium carbonate | 1 | 37.000 | -- | -- | -- | -- | -- | -- | -- |
| 90410 | Acid neutralizing capacity, wat., unf., fixed endpoint (pH 4.5) titration, laboratory, mg/L as calcium carbonate | 4 | 50.000 | 14.000 | -- | -- | -- | -- | -- | -- |
| 00419 | Acid neutralizing capacity, wat., unf., incremental titration, field, mg/L as calcium carbonate | 1 | 44.000 | -- | -- | -- | -- | -- | -- | -- |
| 99440 | Bicarbonate, wat., unf., incremental titration, field, mg/L | 2 | 53.600 | 45.000 | -- | -- | -- | -- | -- | -- |
| 00940 | Chloride, wat., filt., mg/L | 4 | 25.000 | 2.500 | -- | -- | -- | -- | -- | -- |
| 00950 | Fluoride, wat., filt., mg/L | 4 | -- | -- | -- | -- | -- | -- | -- | -- |
| 00955 | Silica, wat., filt., mg/L | 4 | 9.400 | 6.700 | -- | -- | -- | -- | -- | -- |
| 00945 | Sulfate, wat., filt., mg/L | 4 | 21.000 | 5.900 | -- | -- | -- | -- | -- | -- |
| 70300 | Residue on evaporation, dried at 180 degrees Celsius, wat., filt., mg/L | 4 | 162.000 | 92.000 | -- | -- | -- | -- | -- | -- |
| 00608 | Ammonia, wat., filt., mg/L as nitrogen | 3 | 0.151 | 0.009 | -- | -- | -- | -- | -- | -- |
| 00625 | Ammonia plus organic nitrogen, wat., unf., mg/L as nitrogen | 3 | 1.000 | 0.600 | -- | -- | -- | -- | -- | -- |
| 00631 | Nitrite plus nitrate, wat., filt., mg/L as nitrogen | 3 | 2.400 | 0.120 | -- | -- | -- | -- | -- | -- |
| 00613 | Nitrite, wat., filt., mg/L as nitrogen | 3 | 0.017 | 0.004 | -- | -- | -- | -- | -- | -- |
| 00605 | Organic nitrogen, wat., unf., mg/L | 3 | 0.890 | 0.600 | -- | -- | -- | -- | -- | -- |
| 00671 | Orthophosphate, wat., filt., mg/L as phosphorus | 3 | 0.110 | 0.051 | -- | -- | -- | -- | -- | -- |
| 00665 | Phosphorus, wat., unf., mg/L | 3 | 0.220 | 0.110 | -- | -- | -- | -- | -- | -- |
| 00680 | Organic carbon, wat., unf., mg/L | 4 | 14.000 | 7.200 | -- | -- | -- | -- | -- | -- |
| 31501 | Total coliform, M-Endo MF method, immediate, wat., colonies per 100 milliliters | 4 | 2400.000 | 150.000 | -- | -- | -- | -- | -- | -- |
| 90901 | Escherichia coli, MI MF method, wat., colonies per 100 milliliters | 4 | 580.000 | 18.000 | -- | -- | -- | -- | -- | -- |
| 90902 | Escherichia coli, modified m-TEC MF method, wat., colonies per 100 milliliters | 4 | 580.000 | 16.000 | -- | -- | -- | -- | -- | -- |
| 31633 | Escherichia coli, m-TEC MF method, wat., colonies per 100 milliliters | 5 | 680.000 | 19.000 | -- | -- | -- | -- | -- | -- |
| 90900 | Total coliform, MI MF method, wat., colonies per 100 milliliters | 4 | 2000.000 | 190.000 | -- | -- | -- | -- | -- | -- |
| 01105 | Aluminum, wat., unf., recoverable, ug/L | 4 | 2400.000 | 40.000 | -- | -- | -- | -- | -- | -- |
| 01002 | Arsenic, wat., unf., ug/L | 3 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01027 | Cadmium, wat., unf., ug/L | 4 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01034 | Chromium, wat., unf., recoverable, ug/L | 4 | 4.000 | 0.900 | -- | -- | -- | -- | -- | -- |
| 01037 | Cobalt, wat., unf., recoverable, ug/L | 4 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01042 | Copper, wat., unf., recoverable, ug/L | 4 | 11.000 | 2.000 | -- | -- | -- | -- | -- | -- |
| 01045 | Iron, wat., unf., recoverable, ug/L | 4 | 2800.000 | 682.000 | -- | -- | -- | -- | -- | -- |
| 01051 | Lead, wat., unf., recoverable, ug/L | 4 | 5.000 | 1.000 | -- | -- | -- | -- | -- | -- |
| 01055 | Manganese, wat., unf., recoverable, ug/L | 4 | 230.000 | 20.200 | -- | -- | -- | -- | -- | -- |
| 71900 | Mercury, wat., unf., recoverable, ug/L | 4 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01062 | Molybdenum, wat., unf., recoverable, ug/L | 4 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01067 | Nickel, wat., unf., recoverable, ug/L | 4 | 4.000 | 2.000 | -- | -- | -- | -- | -- | -- |
| 01147 | Selenium, wat., unf., ug/L | 4 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01077 | Silver, wat., unf., recoverable, ug/L | 4 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01092 | Zinc, wat., unf., recoverable, ug/L | 4 | 90.200 | 20.000 | -- | -- | -- | -- | -- | -- |
| 80154 | Suspended sediment concentration, mg/L | 4 | 202.000 | 20.000 | -- | -- | -- | -- | -- | -- |
| 0209741955 Northeast Creek at SR 1100 near Genlee (December 1988–March 2001) |
| 00060 | Discharge, cubic feet per second | 3 | 15.000 | 8.000 | -- | -- | -- | -- | -- | -- |
| 00061 | Discharge, instantaneous, cubic feet per second | 27 | 901.000 | 4.100 | 176.800 | 832.600 | 394.000 | 26.000 | 7.900 | 4.460 |
| 00080 | Color, wat., filt., platinum cobalt units | 13 | 400.000 | 40.000 | 175.385 | 400.000 | 240.000 | 150.000 | 100.000 | 40.000 |
| 00300 | Dissolved oxygen, wat., unf., mg/L | 29 | 11.400 | 4.700 | 7.012 | 11.100 | 8.115 | 6.400 | 5.600 | 4.815 |
| 00301 | Dissolved oxygen, wat., unf., percent of saturation | 11 | 594.000 | 51.000 | 119.000 | 594.000 | 90.000 | 70.000 | 62.000 | 51.000 |
| 00400 | pH, wat., unf., field, standard units | 33 | 7.500 | 6.210 | 6.859 | 7.297 | 7.000 | 6.900 | 6.700 | 6.273 |
| 00403 | pH, wat., unf., laboratory, standard units | 13 | 7.600 | 6.600 | 7.085 | 7.600 | 7.200 | 7.100 | 6.900 | 6.600 |
| 90095 | Specific conductance, wat., unf., laboratory, microsiemens per centimeter at 25 degrees Celsius | 13 | 578.000 | 52.000 | 192.231 | 578.000 | 219.500 | 140.000 | 91.000 | 52.000 |
| 00095 | Specific conductance, wat., unf., microsiemens per centimeter at 25 degrees Celsius | 32 | 714.000 | 50.000 | 290.466 | 646.400 | 435.000 | 234.000 | 133.500 | 53.900 |
| 00900 | Hardness, wat., unf., mg/L as calcium carbonate | 13 | 77.000 | 16.000 | 38.231 | 77.000 | 52.000 | 34.000 | 25.000 | 16.000 |
| 00915 | Calcium, wat., filt., mg/L | 13 | 21.000 | 4.100 | 10.008 | 21.000 | 14.000 | 8.900 | 6.500 | 4.100 |
| 00925 | Magnesium, wat., filt., mg/L | 13 | 5.900 | 1.400 | 3.200 | 5.900 | 4.150 | 2.900 | 2.200 | 1.400 |
| 00935 | Potassium, wat., filt., mg/L | 13 | 9.100 | 1.300 | 3.608 | 9.100 | 4.350 | 2.900 | 2.000 | 1.300 |
| 00931 | Sodium adsorption ratio, wat., number | 13 | 4.000 | 0.300 | 1.115 | 4.000 | 1.000 | 0.800 | 0.550 | 0.300 |
| 00930 | Sodium, wat., filt., mg/L | 13 | 70.000 | 3.200 | 19.292 | 70.000 | 22.000 | 11.000 | 6.600 | 3.200 |
| 00932 | Sodium, wat., percent in equivalents of major cations | 13 | 68.000 | 26.000 | 40.308 | 68.000 | 45.500 | 36.000 | 31.500 | 26.000 |
| 99430 | Carbonate, wat., unf., incremental titration, field, mg/L as calcium carbonate | 5 | 69.000 | 13.000 | -- | -- | -- | -- | -- | -- |
| 90410 | Acid neutralizing capacity, wat., unf., fixed endpoint (pH 4.5) titration, laboratory, mg/L as calcium carbonate | 13 | 46.000 | 13.000 | 29.462 | 46.000 | 39.000 | 31.000 | 21.000 | 13.000 |
| 00410 | Acid neutralizing capacity, wat., unf., fixed endpoint (pH 4.5) titration, field, mg/L as calcium carbonate | 5 | 69.000 | 14.000 | -- | -- | -- | -- | -- | -- |
| 00419 | Acid neutralizing capacity, wat., unf., incremental titration, field, mg/L as calcium carbonate | 2 | 40.000 | 21.000 | -- | -- | -- | -- | -- | -- |
| 99440 | Bicarbonate, wat., unf., incremental titration, field, mg/L | 7 | 84.000 | 16.000 | 42.171 | 84.000 | 56.000 | 45.000 | 20.000 | 16.000 |
| 99445 | Carbonate, wat., unf., incremental titration, field, mg/L | 5 | 0.000 | -- | -- | -- | -- | -- | -- | -- |
| 00940 | Chloride, wat., filt., mg/L | 13 | 86.000 | 2.900 | 22.185 | 86.000 | 26.500 | 12.000 | 7.300 | 2.900 |
| 00950 | Fluoride, wat., filt., mg/L | 13 | 0.900 | -- | 0.269* | *0.900 | *0.300 | *0.200 | *0.100 | *0.043 |
| 00955 | Silica, wat., filt., mg/L | 13 | 12.000 | 4.100 | 6.577 | 12.000 | 6.950 | 6.200 | 5.600 | 4.100 |
| 00945 | Sulfate, wat., filt., mg/L | 13 | 46.000 | 5.000 | 16.854 | 46.000 | 24.000 | 11.000 | 8.450 | 5.000 |
| 70300 | Residue on evaporation, dried at 180 degrees Celsius, wat., filt., mg/L | 13 | 344.000 | 40.000 | 129.462 | 344.000 | 143.000 | 101.000 | 77.500 | 40.000 |
| 00608 | Ammonia, wat., filt., mg/L as nitrogen | 8 | 0.284 | 0.019 | 0.132 | 0.284 | 0.250 | 0.090 | 0.047 | 0.019 |
| 00623 | Ammonia plus organic nitrogen, wat., filt., mg/L as nitrogen | 5 | 0.700 | 0.300 | -- | -- | -- | -- | -- | -- |
| 00625 | Ammonia plus organic nitrogen, wat., unf., mg/L as nitrogen | 12 | 1.600 | 0.600 | 0.875 | 1.600 | 1.050 | 0.800 | 0.600 | 0.600 |
| 00610 | Ammonia, wat., unf., mg/L as nitrogen | 4 | 0.150 | 0.020 | -- | -- | -- | -- | -- | -- |
| 00620 | Nitrate, wat., unf., mg/L as nitrogen | 4 | 1.280 | 0.540 | -- | -- | -- | -- | -- | -- |
| 00631 | Nitrite plus nitrate, wat., filt., mg/L as nitrogen | 8 | 9.500 | 0.071 | 1.631 | 9.500 | 1.185 | 0.520 | 0.135 | 0.071 |
| 00630 | Nitrite plus nitrate, wat., unf., mg/L as nitrogen | 4 | 1.300 | 0.590 | -- | -- | -- | -- | -- | -- |
| 00613 | Nitrite, wat., filt., mg/L as nitrogen | 8 | 0.065 | -- | 0.020* | *0.065 | *0.033 | *0.010 | *0.008 | *0.005 |
| 00615 | Nitrite, wat., unf., mg/L as nitrogen | 4 | 0.050 | 0.020 | -- | -- | -- | -- | -- | -- |
| 00605 | Organic nitrogen, wat., unf., mg/L | 11 | 1.300 | 0.500 | 0.754 | 1.300 | 0.860 | 0.680 | 0.530 | 0.500 |
| 00666 | Phosphorus, wat., filt., mg/L | 5 | 0.170 | 0.030 | -- | -- | -- | -- | -- | -- |
| 00671 | Orthophosphate, wat., filt., mg/L as phosphorus | 8 | 1.500 | 0.030 | 0.247 | 1.500 | 0.132 | 0.062 | 0.032 | 0.030 |
| 70507 | Orthophosphate, wat., unf., mg/L as phosphorus | 4 | 0.180 | 0.040 | -- | -- | -- | -- | -- | -- |
| 00665 | Phosphorus, wat., unf., mg/L | 12 | 1.800 | 0.110 | 0.316 | 1.800 | 0.228 | 0.180 | 0.125 | 0.110 |
| 00680 | Organic carbon, wat., unf., mg/L | 13 | 25.000 | 8.900 | 13.069 | 25.000 | 14.500 | 13.000 | 10.500 | 8.900 |
| 01105 | Aluminum, wat., unf., recoverable, ug/L | 13 | 2500.000 | 301.000 | 1664.692 | 2500.000 | 2150.000 | 1700.000 | 1310.000 | 301.000 |
| 01002 | Arsenic, wat., unf., ug/L | 12 | 1.000 | -- | 1.000* | *1.000 | *1.000 | *1.000 | *1.000 | *1.000 |
| 01027 | Cadmium, wat., unf., ug/L | 13 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01034 | Chromium, wat., unf., recoverable, ug/L | 13 | 11.000 | -- | 3.997* | *11.000 | *6.000 | *3.300 | *1.900 | *0.659 |
| 01037 | Cobalt, wat., unf., recoverable, ug/L | 13 | 2.000 | -- | 1.429* | *2.000 | *2.000 | *1.134 | *0.948 | *0.710 |
| 01042 | Copper, wat., unf., recoverable, ug/L | 13 | 13.000 | 4.000 | 10.000 | 13.000 | 11.500 | 11.000 | 8.500 | 4.000 |
| 01045 | Iron, wat., unf., recoverable, ug/L | 13 | 2900.000 | 526.000 | 1929.538 | 2900.000 | 2600.000 | 2300.000 | 1174.000 | 526.000 |
| 01051 | Lead, wat., unf., recoverable, ug/L | 13 | 10.000 | 0.800 | 4.215 | 10.000 | 5.500 | 4.000 | 2.500 | 0.800 |
| 01055 | Manganese, wat., unf., recoverable, ug/L | 13 | 380.000 | 22.300 | 175.246 | 380.000 | 295.000 | 160.000 | 75.000 | 22.300 |
| 71900 | Mercury, wat., unf., recoverable, ug/L | 13 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01062 | Molybdenum, wat., unf., recoverable, ug/L | 13 | 21.000 | -- | 5.761* | *21.000 | *10.000 | *2.000 | *0.887 | *0.306 |
| 01067 | Nickel, wat., unf., recoverable, ug/L | 13 | 5.000 | 2.000 | 3.385 | 5.000 | 4.000 | 3.000 | 3.000 | 2.000 |
| 01147 | Selenium, wat., unf., ug/L | 13 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01077 | Silver, wat., unf., recoverable, ug/L | 13 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01092 | Zinc, wat., unf., recoverable, ug/L | 13 | 144.000 | -- | 44.412* | *144.000 | *40.000 | *30.000 | *26.678 | *20.000 |
| 80154 | Suspended sediment concentration, mg/L | 13 | 202.000 | 12.000 | 83.308 | 202.000 | 118.000 | 67.000 | 38.500 | 12.000 |
| 02097464 Morgan Creek near White Cross (October 1988–August 2001) |
| 00061 | Discharge, instantaneous, cubic feet per second | 129 | 309.000 | 0.050 | 13.617 | 68.500 | 6.950 | 3.100 | 1.100 | 0.155 |
| 00080 | Color, wat., filt., platinum cobalt units | 129 | 280.000 | 10.000 | 52.209 | 130.000 | 58.000 | 45.000 | 30.000 | 21.000 |
| 00300 | Dissolved oxygen, wat., unf., mg/L | 126 | 15.200 | 4.380 | 9.590 | 14.190 | 11.625 | 9.800 | 7.775 | 5.300 |
| 00301 | Dissolved oxygen, wat., unf., percent of saturation | 125 | 171.000 | 49.000 | 92.872 | 124.200 | 104.000 | 93.000 | 85.500 | 57.000 |
| 00400 | pH, wat., unf., field, standard units | 129 | 8.500 | 5.600 | 7.080 | 7.620 | 7.300 | 7.150 | 6.890 | 6.285 |
| 00403 | pH, wat., unf., laboratory, standard units | 129 | 9.100 | 6.700 | 7.454 | 8.100 | 7.600 | 7.400 | 7.200 | 7.000 |
| 90095 | Specific conductance, wat., unf., laboratory, microsiemens per centimeter at 25 degrees Celsius | 129 | 222.000 | 37.000 | 107.550 | 154.000 | 124.500 | 105.000 | 87.000 | 69.000 |
| 00095 | Specific conductance, wat., unf., microsiemens per centimeter at 25 degrees Celsius | 128 | 222.000 | 36.000 | 104.773 | 152.000 | 119.750 | 103.000 | 83.250 | 71.450 |
| 00900 | Hardness, wat., unf., mg/L as calcium carbonate | 129 | 61.000 | 10.000 | 34.403 | 49.500 | 41.000 | 34.000 | 27.500 | 21.500 |
| 00915 | Calcium, wat., filt., mg/L | 129 | 15.000 | 2.400 | 8.586 | 13.000 | 10.000 | 8.500 | 6.700 | 5.250 |
| 00925 | Magnesium, wat., filt., mg/L | 129 | 5.700 | 1.000 | 3.143 | 4.700 | 3.800 | 3.000 | 2.500 | 2.050 |
| 00935 | Potassium, wat., filt., mg/L | 129 | 18.000 | 0.100 | 3.553 | 8.950 | 4.350 | 2.700 | 1.600 | 1.200 |
| 00931 | Sodium adsorption ratio, wat., number | 129 | 0.500 | 0.200 | 0.385 | 0.400 | 0.400 | 0.400 | 0.400 | 0.300 |
| 00930 | Sodium, wat., filt., mg/L | 129 | 7.700 | 1.400 | 5.027 | 6.350 | 5.600 | 5.000 | 4.600 | 3.550 |
| 00932 | Sodium, wat., percent in equivalents of major cations | 128 | 28.000 | 15.000 | 22.562 | 28.000 | 25.000 | 23.000 | 20.000 | 18.000 |
| 99430 | Carbonate, wat., unf., incremental titration, field, mg/L as calcium carbonate | 52 | 69.000 | 6.000 | 33.865 | 60.800 | 42.750 | 31.500 | 24.250 | 12.200 |
| 90410 | Acid neutralizing capacity, wat., unf., fixed endpoint (pH 4.5) titration, laboratory, mg/L as calcium carbonate | 129 | 66.000 | 6.900 | 33.983 | 55.000 | 41.500 | 32.000 | 25.000 | 17.000 |
| 39036 | Alkalinity, wat., filt., fixed endpoint (pH 4.5) titration, field, mg/L as calcium carbonate | 1 | 31.000 | -- | -- | -- | -- | -- | -- | -- |
| 39086 | Alkalinity, wat., filt., incremental titration, field, mg/L as calcium carbonate | 3 | 34.000 | 17.000 | -- | -- | -- | -- | -- | -- |
| 00410 | Acid neutralizing capacity, wat., unf., fixed endpoint (pH 4.5) titration, field, mg/L as calcium carbonate | 60 | 410.000 | 6.000 | 41.167 | 67.500 | 45.000 | 33.000 | 26.000 | 15.000 |
| 00419 | Acid neutralizing capacity, wat., unf., incremental titration, field, mg/L as calcium carbonate | 16 | 68.000 | 12.000 | 33.438 | 68.000 | 44.750 | 30.500 | 23.500 | 12.000 |
| 99440 | Bicarbonate, wat., unf., incremental titration, field, mg/L | 67 | 84.000 | 7.000 | 41.157 | 77.000 | 53.000 | 38.000 | 29.000 | 14.920 |
| 00453 | Bicarbonate, wat., filt., incremental titration, field, mg/L | 3 | 41.000 | 20.000 | -- | -- | -- | -- | -- | -- |
| 99445 | Carbonate, wat., unf., incremental titration, field, mg/L | 12 | 0.000 | -- | -- | -- | -- | -- | -- | -- |
| 00452 | Carbonate, wat., filt., incremental titration, field, mg/L | 2 | 0.000 | -- | -- | -- | -- | -- | -- | -- |
| 00940 | Chloride, wat., filt., mg/L | 123 | 17.000 | 2.800 | 6.537 | 9.100 | 7.300 | 6.200 | 5.400 | 4.520 |
| 00950 | Fluoride, wat., filt., mg/L | 123 | 0.400 | -- | 0.088* | *0.200 | *0.100 | *0.073 | *0.048 | *0.027 |
| 00955 | Silica, wat., filt., mg/L | 122 | 21.000 | 1.200 | 13.332 | 19.000 | 16.000 | 14.000 | 11.000 | 7.215 |
| 00945 | Sulfate, wat., filt., mg/L | 122 | 12.000 | 0.100 | 4.651 | 8.740 | 5.500 | 4.100 | 3.275 | 2.600 |
| 99890 | Sulfate, wat., filt., uncorrected, mg/L | 7 | -- | -- | -- | -- | -- | -- | -- | -- |
| 70300 | Residue on evaporation, dried at 180 degrees Celsius, wat., filt., mg/L | 123 | 158.000 | 1.000 | 74.463 | 111.400 | 86.000 | 72.000 | 60.000 | 46.000 |
| 00608 | Ammonia, wat., filt., mg/L as nitrogen | 128 | 1.500 | -- | 0.073* | *0.267 | *0.057 | *0.030 | *0.010 | *0.003 |
| 00623 | Ammonia plus organic nitrogen, wat., filt., mg/L as nitrogen | 87 | 2.600 | -- | 0.479* | *1.600 | *0.500 | *0.300 | *0.200 | *0.099 |
| 00625 | Ammonia plus organic nitrogen, wat., unf., mg/L as nitrogen | 129 | 3.300 | -- | 0.575* | *2.100 | *0.600 | *0.400 | *0.300 | *0.129 |
| 00610 | Ammonia, wat., unf., mg/L as nitrogen | 49 | 1.600 | -- | 0.140* | *1.236 | *0.082 | *0.030 | *0.020 | *0.002 |
| 00620 | Nitrate, wat., unf., mg/L as nitrogen | 32 | 1.680 | 0.320 | 0.831 | 1.680 | 1.100 | 0.775 | 0.592 | 0.333 |
| 00631 | Nitrite plus nitrate, wat., filt., mg/L as nitrogen | 128 | 1.700 | 0.005 | 0.688 | 1.400 | 0.900 | 0.675 | 0.435 | 0.058 |
| 00630 | Nitrite plus nitrate, wat., unf., mg/L as nitrogen | 49 | 1.700 | 0.170 | 0.830 | 1.600 | 1.100 | 0.800 | 0.510 | 0.265 |
| 00613 | Nitrite, wat., filt., mg/L as nitrogen | 104 | 0.050 | -- | 0.010* | *0.039 | *0.015 | *0.006 | *0.003 | *0.001 |
| 00615 | Nitrite, wat., unf., mg/L as nitrogen | 49 | 0.100 | -- | 0.020* | *0.070 | *0.030 | *0.010 | *0.005 | *0.002 |
| 00605 | Organic nitrogen, wat., unf., mg/L | 112 | 2.000 | 0.110 | 0.517 | 1.540 | 0.585 | 0.380 | 0.290 | 0.186 |
| 00666 | Phosphorus, wat., filt., mg/L | 92 | 0.970 | 0.020 | 0.204 | 0.440 | 0.300 | 0.155 | 0.093 | 0.040 |
| 00671 | Orthophosphate, wat., filt., mg/L as phosphorus | 128 | 0.900 | 0.001 | 0.153 | 0.410 | 0.230 | 0.105 | 0.051 | 0.017 |
| 70507 | Orthophosphate, wat., unf., mg/L as phosphorus | 49 | 0.900 | 0.030 | 0.226 | 0.495 | 0.350 | 0.150 | 0.100 | 0.055 |
| 00665 | Phosphorus, wat., unf., mg/L | 129 | 2.800 | 0.040 | 0.234 | 0.575 | 0.290 | 0.150 | 0.090 | 0.045 |
| 00680 | Organic carbon, wat., unf., mg/L | 128 | 58.000 | 2.100 | 6.669 | 14.550 | 6.600 | 4.800 | 4.000 | 3.045 |
| 01105 | Aluminum, wat., unf., recoverable, ug/L | 48 | 4400.000 | 20.000 | 388.906 | 2387.499 | 238.250 | 120.000 | 70.000 | 29.305 |
| 01002 | Arsenic, wat., unf., ug/L | 48 | 2.000 | -- | 0.741* | *2.000 | *1.000 | *0.629 | *0.441 | *0.244 |
| 01027 | Cadmium, wat., unf., ug/L | 48 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01034 | Chromium, wat., unf., recoverable, ug/L | 48 | 11.000 | -- | 1.032* | *4.440 | *1.150 | *0.391 | *0.143 | *0.033 |
| 01037 | Cobalt, wat., unf., recoverable, ug/L | 48 | 5.000 | -- | 0.772* | *3.550 | *1.000 | *0.494 | *0.281 | *0.120 |
| 01042 | Copper, wat., unf., recoverable, ug/L | 48 | 10.000 | -- | 2.142* | *7.650 | *3.000 | *2.000 | *0.826 | *0.383 |
| 01045 | Iron, wat., unf., recoverable, ug/L | 48 | 6700.000 | 220.000 | 1113.958 | 5035.498 | 1095.000 | 740.000 | 590.250 | 268.350 |
| 01051 | Lead, wat., unf., recoverable, ug/L | 47 | 20.000 | -- | 1.609* | *9.600 | *2.000 | *0.533 | *0.202 | *0.045 |
| 01055 | Manganese, wat., unf., recoverable, ug/L | 48 | 750.000 | 17.200 | 132.829 | 667.600 | 142.000 | 55.000 | 34.850 | 20.000 |
| 71900 | Mercury, wat., unf., recoverable, ug/L | 47 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01062 | Molybdenum, wat., unf., recoverable, ug/L | 48 | 3.000 | -- | 0.429* | *1.550 | *0.499 | *0.251 | *0.125 | *0.047 |
| 01067 | Nickel, wat., unf., recoverable, ug/L | 48 | 5.000 | -- | 1.056* | *4.550 | *1.000 | *0.591 | *0.279 | *0.098 |
| 01147 | Selenium, wat., unf., ug/L | 48 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01077 | Silver, wat., unf., recoverable, ug/L | 47 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01092 | Zinc, wat., unf., recoverable, ug/L | 48 | 269.000 | -- | 9.905* | *43.845 | *3.929 | *0.851 | *0.184 | *0.019 |
| 80154 | Suspended sediment concentration, mg/L | 113 | 603.000 | 0.000 | 25.640 | 72.390 | 14.000 | 7.000 | 4.000 | 2.000 |
| 0209749990 University Lake at the dam near Chapel Hill (November 1988–August 2001) |
| 00080 | Color, wat., filt., platinum cobalt units | 57 | 120.000 | 8.000 | 32.912 | 75.000 | 36.000 | 25.000 | 22.000 | 13.800 |
| 00078 | Transparency, wat., unf., Secchi disc, meters | 36 | 1.450 | 0.250 | 0.693 | 1.025 | 0.887 | 0.675 | 0.512 | 0.335 |
| 00300 | Dissolved oxygen, wat., unf., mg/L | 61 | 11.700 | 0.140 | 6.628 | 10.400 | 9.460 | 7.770 | 4.800 | 0.279 |
| 00301 | Dissolved oxygen, wat., unf., percent of saturation | 60 | 133.000 | 2.000 | 76.783 | 129.750 | 105.000 | 87.000 | 56.250 | 3.000 |
| 00400 | pH, wat., unf., field, standard units | 73 | 8.600 | 5.970 | 7.157 | 8.543 | 7.290 | 7.060 | 6.825 | 6.082 |
| 00403 | pH, wat., unf., laboratory, standard units | 58 | 8.600 | 6.300 | 7.366 | 8.010 | 7.600 | 7.400 | 7.100 | 6.900 |
| 90095 | Specific conductance, wat., unf., laboratory, microsiemens per centimeter at 25 degrees Celsius | 58 | 161.000 | 70.000 | 90.103 | 118.600 | 92.500 | 88.000 | 82.000 | 74.000 |
| 00095 | Specific conductance, wat., unf., microsiemens per centimeter at 25 degrees Celsius | 73 | 467.000 | 66.000 | 104.189 | 247.500 | 93.600 | 88.000 | 80.500 | 70.400 |
| 00900 | Hardness, wat., unf., mg/L as calcium carbonate | 58 | 42.000 | 22.000 | 27.690 | 34.000 | 30.000 | 28.000 | 25.000 | 22.000 |
| 00915 | Calcium, wat., filt., mg/L | 58 | 12.000 | 5.400 | 7.031 | 8.710 | 7.525 | 7.050 | 6.200 | 5.595 |
| 00925 | Magnesium, wat., filt., mg/L | 58 | 2.900 | 2.000 | 2.469 | 2.900 | 2.700 | 2.500 | 2.200 | 2.000 |
| 00935 | Potassium, wat., filt., mg/L | 58 | 3.500 | 1.300 | 2.284 | 3.300 | 2.800 | 2.200 | 1.800 | 1.400 |
| 00931 | Sodium adsorption ratio, wat., number | 58 | 0.500 | 0.300 | 0.419 | 0.500 | 0.500 | 0.400 | 0.400 | 0.300 |
| 00930 | Sodium, wat., filt., mg/L | 58 | 6.400 | 3.200 | 5.052 | 6.205 | 5.625 | 5.000 | 4.500 | 3.585 |
| 00932 | Sodium, wat., percent in equivalents of major cations | 58 | 31.000 | 18.000 | 26.500 | 30.000 | 29.000 | 27.000 | 24.000 | 20.950 |
| 99430 | Carbonate, wat., unf., incremental titration, field, mg/L as calcium carbonate | 24 | 47.000 | 19.000 | 28.000 | 45.000 | 35.000 | 26.000 | 22.000 | 19.000 |
| 90410 | Acid neutralizing capacity, wat., unf., fixed endpoint (pH 4.5) titration, laboratory, mg/L as calcium carbonate | 58 | 49.000 | 20.000 | 30.034 | 39.050 | 33.250 | 29.500 | 26.000 | 22.950 |
| 00418 | Alkalinity, wat., filt., fixed endpoint (pH 4.5) titration, field, mg/L as calcium carbonate | 1 | 30.000 | -- | -- | -- | -- | -- | -- | -- |
| 39086 | Alkalinity, wat., filt., incremental titration, field, mg/L as calcium carbonate | 1 | 30.000 | -- | -- | -- | -- | -- | -- | -- |
| 00410 | Acid neutralizing capacity, wat., unf., fixed endpoint (pH 4.5) titration, field, mg/L as calcium carbonate | 25 | 47.000 | 19.000 | 29.320 | 44.600 | 35.000 | 29.000 | 23.000 | 19.000 |
| 00419 | Acid neutralizing capacity, wat., unf., incremental titration, field, mg/L as calcium carbonate | 10 | 35.000 | 23.000 | 29.600 | 35.000 | 33.500 | 29.500 | 26.750 | 23.000 |
| 99440 | Bicarbonate, wat., unf., incremental titration, field, mg/L | 34 | 57.000 | 23.000 | 33.703 | 50.250 | 38.250 | 32.500 | 27.000 | 23.000 |
| 00453 | Bicarbonate, wat., filt., incremental titration, field, mg/L | 1 | 37.000 | -- | -- | -- | -- | -- | -- | -- |
| 99445 | Carbonate, wat., unf., incremental titration, field, mg/L | 9 | 7.000 | 0.000 | 0.778 | 7.000 | 0.000 | 0.000 | 0.000 | 0.000 |
| 00452 | Carbonate, wat., filt., incremental titration, field, mg/L | 1 | 0.000 | -- | -- | -- | -- | -- | -- | -- |
| 00940 | Chloride, wat., filt., mg/L | 57 | 6.800 | 3.800 | 5.104 | 6.210 | 5.400 | 5.100 | 4.600 | 4.080 |
| 00950 | Fluoride, wat., filt., mg/L | 57 | 0.300 | -- | 0.083* | *0.200 | *0.100 | *0.073 | *0.052 | *0.032 |
| 00955 | Silica, wat., filt., mg/L | 56 | 20.000 | 4.200 | 12.864 | 17.150 | 15.000 | 13.000 | 11.000 | 5.765 |
| 00945 | Sulfate, wat., filt., mg/L | 57 | 11.000 | 0.200 | 4.591 | 7.100 | 5.350 | 4.600 | 3.600 | 2.380 |
| 99890 | Sulfate, wat., filt., uncorrected, mg/L | 3 | -- | -- | -- | -- | -- | -- | -- | -- |
| 70300 | Residue on evaporation, dried at 180 degrees Celsius, wat., filt., mg/L | 55 | 124.000 | 34.000 | 66.309 | 97.600 | 72.000 | 65.000 | 58.000 | 42.800 |
| 00608 | Ammonia, wat., filt., mg/L as nitrogen | 66 | 6.800 | -- | 0.206* | *1.108 | *0.061 | *0.030 | *0.007 | *0.001 |
| 00623 | Ammonia plus organic nitrogen, wat., filt., mg/L as nitrogen | 38 | 2.700 | -- | 0.468* | *1.085 | *0.500 | *0.300 | *0.300 | *0.130 |
| 00625 | Ammonia plus organic nitrogen, wat., unf., mg/L as nitrogen | 66 | 9.100 | 0.200 | 0.918 | 2.795 | 0.900 | 0.600 | 0.500 | 0.335 |
| 00610 | Ammonia, wat., unf., mg/L as nitrogen | 18 | 2.300 | 0.010 | 0.298 | 2.300 | 0.110 | 0.045 | 0.030 | 0.010 |
| 00620 | Nitrate, wat., unf., mg/L as nitrogen | 3 | 0.590 | 0.100 | -- | -- | -- | -- | -- | -- |
| 00631 | Nitrite plus nitrate, wat., filt., mg/L as nitrogen | 66 | 0.470 | -- | 0.033* | *0.186 | *0.015 | *0.005 | *0.001 | *0.000 |
| 00630 | Nitrite plus nitrate, wat., unf., mg/L as nitrogen | 18 | 0.600 | -- | 0.092* | *0.600 | *0.100 | *0.042 | *0.017 | *0.007 |
| 00613 | Nitrite, wat., filt., mg/L as nitrogen | 56 | 0.020 | -- | 0.002* | *0.010 | *0.003 | *0.001 | *0.000 | *0.000 |
| 00615 | Nitrite, wat., unf., mg/L as nitrogen | 18 | 0.020 | -- | 0.008* | *0.020 | *0.010 | *0.006 | *0.004 | *0.002 |
| 00605 | Organic nitrogen, wat., unf., mg/L | 53 | 2.700 | 0.270 | 0.685 | 1.290 | 0.775 | 0.590 | 0.495 | 0.367 |
| 00666 | Phosphorus, wat., filt., mg/L | 38 | 0.080 | -- | 0.013* | *0.053 | *0.020 | *0.007 | *0.003 | *0.001 |
| 00671 | Orthophosphate, wat., filt., mg/L as phosphorus | 66 | 0.150 | -- | 0.009* | *0.060 | *0.006 | *0.002 | *0.001 | *0.000 |
| 70507 | Orthophosphate, wat., unf., mg/L as phosphorus | 18 | 0.050 | -- | 0.015* | *0.050 | *0.020 | *0.010 | *0.005 | *0.002 |
| 00665 | Phosphorus, wat., unf., mg/L | 63 | 0.470 | -- | 0.055* | *0.116 | *0.060 | *0.040 | *0.030 | *0.015 |
| 00680 | Organic carbon, wat., unf., mg/L | 58 | 15.000 | 4.800 | 7.874 | 11.000 | 8.950 | 7.450 | 6.575 | 5.200 |

| NWIS Param-eter code | Constituent name | Sample size | Maximum | Minimum | Mean | Percentile |
| --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  | 95th | 75th | 50th | 25th | 5th |
| 70953 | Chlorophyll a, phytoplankton, chromatographic-fluorometric method, ug/L | 52 | 165.000 | 1.200 | 18.437 | 42.635 | 24.050 | 11.050 | 6.700 | 1.920 |
| 70954 | Chlorophyll b, phytoplankton, chromatographic-fluorometric method, ug/L | 52 | 47.600 | -- | 1.662* | *2.950 | *1.275 | *0.500 | *0.150 | *0.045 |
| 01105 | Aluminum, wat., unf., recoverable, ug/L | 45 | 240.000 | 10.000 | 51.971 | 156.700 | 66.000 | 40.000 | 27.600 | 10.000 |
| 01002 | Arsenic, wat., unf., ug/L | 45 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01027 | Cadmium, wat., unf., ug/L | 45 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01034 | Chromium, wat., unf., recoverable, ug/L | 45 | 4.000 | -- | 0.602* | *2.700 | *0.696 | *0.295 | *0.125 | *0.036 |
| 01037 | Cobalt, wat., unf., recoverable, ug/L | 45 | 2.000 | -- | 0.519* | *1.000 | *0.658 | *0.439 | *0.292 | *0.167 |
| 01042 | Copper, wat., unf., recoverable, ug/L | 32 | 95.000 | -- | 4.614* | *48.850 | *1.750 | *0.900 | *0.244 | *0.046 |
| 01045 | Iron, wat., unf., recoverable, ug/L | 63 | 49000.000 | 100.000 | 2058.873 | 12679.995 | 580.000 | 375.000 | 280.000 | 165.600 |
| 01051 | Lead, wat., unf., recoverable, ug/L | 33 | 3.000 | -- | 0.598* | *2.300 | *0.732 | *0.340 | *0.158 | *0.052 |
| 01055 | Manganese, wat., unf., recoverable, ug/L | 63 | 23000.000 | 50.000 | 1237.887 | 7354.000 | 520.000 | 160.000 | 94.100 | 60.000 |
| 71900 | Mercury, wat., unf., recoverable, ug/L | 45 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01062 | Molybdenum, wat., unf., recoverable, ug/L | 33 | 32.000 | -- | 1.251* | *12.400 | *0.188 | *0.026 | *0.004 | *0.000 |
| 01067 | Nickel, wat., unf., recoverable, ug/L | 32 | 2.000 | -- | 0.507* | *2.000 | *0.643 | *0.362 | *0.200 | *0.089 |
| 01147 | Selenium, wat., unf., ug/L | 45 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01077 | Silver, wat., unf., recoverable, ug/L | 44 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01092 | Zinc, wat., unf., recoverable, ug/L | 33 | 20.000 | -- | 4.707* | *20.000 | *6.093 | *3.087 | *1.562 | *0.617 |
| 020927521 Morgan Creek near Farrington (December 1988–April 1995) |
| 00061 | Discharge, instantaneous, cubic feet per second | 16 | 296.000 | 13.000 | 39.250 | 296.000 | 31.750 | 20.000 | 15.250 | 13.000 |
| 00080 | Color, wat., filt., platinum cobalt units | 1 | 120.000 | -- | -- | -- | -- | -- | -- | -- |
| 00300 | Dissolved oxygen, wat., unf., mg/L | 16 | 10.900 | 5.500 | 7.091 | 10.900 | 7.850 | 6.400 | 6.125 | 5.500 |
| 00301 | Dissolved oxygen, wat., unf., percent of saturation | 1 | 88.000 | -- | -- | -- | -- | -- | -- | -- |
| 00400 | pH, wat., unf., field, standard units | 16 | 7.540 | 6.300 | 7.091 | 7.540 | 7.267 | 7.115 | 7.025 | 6.300 |
| 00403 | pH, wat., unf., laboratory, standard units | 1 | 7.300 | -- | -- | -- | -- | -- | -- | -- |
| 90095 | Specific conductance, wat., unf., laboratory, microsiemens per centimeter at 25 degrees Celsius | 1 | 95.000 | -- | -- | -- | -- | -- | -- | -- |
| 00095 | Specific conductance, wat., unf., microsiemens per centimeter at 25 degrees Celsius | 16 | 411.000 | 75.000 | 246.938 | 411.000 | 354.000 | 244.500 | 151.250 | 75.000 |
| 00900 | Hardness, wat., unf., mg/L as calcium carbonate | 1 | 21.000 | -- | -- | -- | -- | -- | -- | -- |
| 00915 | Calcium, wat., filt., mg/L | 1 | 5.400 | -- | -- | -- | -- | -- | -- | -- |
| 00925 | Magnesium, wat., filt., mg/L | 1 | 1.800 | -- | -- | -- | -- | -- | -- | -- |
| 00935 | Potassium, wat., filt., mg/L | 1 | 2.100 | -- | -- | -- | -- | -- | -- | -- |
| 00931 | Sodium adsorption ratio, wat., number | 1 | 0.800 | -- | -- | -- | -- | -- | -- | -- |
| 00930 | Sodium, wat., filt., mg/L | 1 | 8.400 | -- | -- | -- | -- | -- | -- | -- |
| 00932 | Sodium, wat., percent in equivalents of major cations | 1 | 44.000 | -- | -- | -- | -- | -- | -- | -- |
| 99430 | Carbonate, wat., unf., incremental titration, field, mg/L as calcium carbonate | 1 | 14.000 | -- | -- | -- | -- | -- | -- | -- |
| 90410 | Acid neutralizing capacity, wat., unf., fixed endpoint (pH 4.5) titration, laboratory, mg/L as calcium carbonate | 1 | 15.000 | -- | -- | -- | -- | -- | -- | -- |
| 00410 | Acid neutralizing capacity, wat., unf., fixed endpoint (pH 4.5) titration, field, mg/L as calcium carbonate | 1 | 14.000 | -- | -- | -- | -- | -- | -- | -- |
| 99440 | Bicarbonate, wat., unf., incremental titration, field, mg/L | 1 | 17.000 | -- | -- | -- | -- | -- | -- | -- |
| 00940 | Chloride, wat., filt., mg/L | 1 | 7.300 | -- | -- | -- | -- | -- | -- | -- |
| 00950 | Fluoride, wat., filt., mg/L | 1 | -- | -- | -- | -- | -- | -- | -- | -- |
| 00955 | Silica, wat., filt., mg/L | 1 | 9.500 | -- | -- | -- | -- | -- | -- | -- |
| 00945 | Sulfate, wat., filt., mg/L | 1 | 13.000 | -- | -- | -- | -- | -- | -- | -- |
| 70300 | Residue on evaporation, dried at 180 degrees Celsius, wat., filt., mg/L | 1 | 76.000 | -- | -- | -- | -- | -- | -- | -- |
| 00608 | Ammonia, wat., filt., mg/L as nitrogen | 1 | 0.090 | -- | -- | -- | -- | -- | -- | -- |
| 00623 | Ammonia plus organic nitrogen, wat., filt., mg/L as nitrogen | 1 | 0.400 | -- | -- | -- | -- | -- | -- | -- |
| 00625 | Ammonia plus organic nitrogen, wat., unf., mg/L as nitrogen | 1 | 0.600 | -- | -- | -- | -- | -- | -- | -- |
| 00631 | Nitrite plus nitrate, wat., filt., mg/L as nitrogen | 1 | 0.530 | -- | -- | -- | -- | -- | -- | -- |
| 00613 | Nitrite, wat., filt., mg/L as nitrogen | 1 | 0.040 | -- | -- | -- | -- | -- | -- | -- |
| 00605 | Organic nitrogen, wat., unf., mg/L | 1 | 0.510 | -- | -- | -- | -- | -- | -- | -- |
| 00666 | Phosphorus, wat., filt., mg/L | 1 | 0.050 | -- | -- | -- | -- | -- | -- | -- |
| 00671 | Orthophosphate, wat., filt., mg/L as phosphorus | 1 | 0.040 | -- | -- | -- | -- | -- | -- | -- |
| 00665 | Phosphorus, wat., unf., mg/L | 1 | 0.140 | -- | -- | -- | -- | -- | -- | -- |
| 00680 | Organic carbon, wat., unf., mg/L | 1 | 10.000 | -- | -- | -- | -- | -- | -- | -- |
| 01105 | Aluminum, wat., unf., recoverable, ug/L | 1 | 940.000 | -- | -- | -- | -- | -- | -- | -- |
| 01002 | Arsenic, wat., unf., ug/L | 1 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01027 | Cadmium, wat., unf., ug/L | 1 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01034 | Chromium, wat., unf., recoverable, ug/L | 1 | 2.000 | -- | -- | -- | -- | -- | -- | -- |
| 01037 | Cobalt, wat., unf., recoverable, ug/L | 1 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01042 | Copper, wat., unf., recoverable, ug/L | 1 | 4.000 | -- | -- | -- | -- | -- | -- | -- |
| 01045 | Iron, wat., unf., recoverable, ug/L | 1 | 1400.000 | -- | -- | -- | -- | -- | -- | -- |
| 01051 | Lead, wat., unf., recoverable, ug/L | 1 | 3.000 | -- | -- | -- | -- | -- | -- | -- |
| 01055 | Manganese, wat., unf., recoverable, ug/L | 1 | 210.000 | -- | -- | -- | -- | -- | -- | -- |
| 71900 | Mercury, wat., unf., recoverable, ug/L | 1 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01062 | Molybdenum, wat., unf., recoverable, ug/L | 1 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01067 | Nickel, wat., unf., recoverable, ug/L | 1 | 1.000 | -- | -- | -- | -- | -- | -- | -- |
| 01147 | Selenium, wat., unf., ug/L | 1 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01077 | Silver, wat., unf., recoverable, ug/L | 1 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01092 | Zinc, wat., unf., recoverable, ug/L | 1 | -- | -- | -- | -- | -- | -- | -- | -- |
| 80154 | Suspended sediment concentration, mg/L | 1 | 102.000 | -- | -- | -- | -- | -- | -- | -- |
| 0209768310 Jordan Lake at buoy 12 at Farrington (August 1992–August 2001) |
| 00080 | Color, wat., filt., platinum cobalt units | 38 | 100.000 | 1.000 | 41.368 | 90.500 | 53.500 | 39.000 | 22.750 | 7.650 |
| 00078 | Transparency, wat., unf., Secchi disc, meters | 37 | 0.800 | 0.200 | 0.426 | 0.710 | 0.450 | 0.400 | 0.350 | 0.245 |
| 00300 | Dissolved oxygen, wat., unf., mg/L | 52 | 13.500 | 0.400 | 7.653 | 12.475 | 9.623 | 7.905 | 6.555 | 1.886 |
| 00301 | Dissolved oxygen, wat., unf., percent of saturation | 52 | 143.000 | 4.000 | 88.404 | 138.700 | 107.500 | 91.500 | 76.750 | 20.650 |
| 00400 | pH, wat., unf., field, standard units | 52 | 9.100 | 6.440 | 7.515 | 9.000 | 8.100 | 7.300 | 6.855 | 6.507 |
| 00403 | pH, wat., unf., laboratory, standard units | 37 | 8.900 | 6.700 | 7.695 | 8.900 | 8.100 | 7.600 | 7.250 | 6.700 |
| 90095 | Specific conductance, wat., unf., laboratory, microsiemens per centimeter at 25 degrees Celsius | 37 | 204.000 | 79.000 | 145.676 | 190.500 | 163.500 | 149.000 | 128.000 | 79.000 |
| 00095 | Specific conductance, wat., unf., microsiemens per centimeter at 25 degrees Celsius | 52 | 202.000 | 74.000 | 147.558 | 182.400 | 164.750 | 154.000 | 132.250 | 91.000 |
| 00900 | Hardness, wat., unf., mg/L as calcium carbonate | 37 | 37.000 | 20.000 | 30.405 | 36.100 | 33.000 | 31.000 | 28.500 | 20.000 |
| 00915 | Calcium, wat., filt., mg/L | 37 | 9.600 | 5.200 | 7.862 | 9.420 | 8.500 | 8.000 | 7.300 | 5.290 |
| 00925 | Magnesium, wat., filt., mg/L | 37 | 3.100 | 1.700 | 2.619 | 3.100 | 2.800 | 2.700 | 2.450 | 1.790 |
| 00935 | Potassium, wat., filt., mg/L | 37 | 4.000 | 1.700 | 3.008 | 4.000 | 3.300 | 3.100 | 2.600 | 2.150 |
| 00931 | Sodium adsorption ratio, wat., number | 37 | 2.000 | 0.500 | 0.968 | 1.100 | 1.000 | 1.000 | 0.900 | 0.590 |
| 00930 | Sodium, wat., filt., mg/L | 37 | 23.000 | 5.100 | 14.097 | 20.300 | 17.000 | 14.000 | 12.000 | 5.820 |
| 00932 | Sodium, wat., percent in equivalents of major cations | 37 | 55.000 | 32.000 | 46.216 | 52.300 | 51.000 | 47.000 | 43.000 | 35.600 |
| 99430 | Carbonate, wat., unf., incremental titration, field, mg/L as calcium carbonate | 22 | 77.000 | 16.000 | 31.773 | 71.600 | 33.000 | 32.000 | 26.750 | 16.450 |
| 90410 | Acid neutralizing capacity, wat., unf., fixed endpoint (pH 4.5) titration, laboratory, mg/L as calcium carbonate | 37 | 43.000 | 19.000 | 31.757 | 41.200 | 36.000 | 33.000 | 27.500 | 19.000 |
| 00410 | Acid neutralizing capacity, wat., unf., fixed endpoint (pH 4.5) titration, field, mg/L as calcium carbonate | 24 | 77.000 | 16.000 | 31.958 | 68.000 | 33.750 | 32.000 | 27.000 | 16.000 |
| 00419 | Acid neutralizing capacity, wat., unf., incremental titration, field, mg/L as calcium carbonate | 7 | 48.000 | 16.000 | 33.000 | 48.000 | 45.000 | 33.000 | 23.000 | 16.000 |
| 99440 | Bicarbonate, wat., unf., incremental titration, field, mg/L | 29 | 92.000 | 16.000 | 36.428 | 73.000 | 40.000 | 34.000 | 28.500 | 17.500 |

| NWIS Param-eter code | Constituent name | Sample size | Maximum | Minimum | Mean | Percentile |
| --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  | 95th | 75th | 50th | 25th | 5th |
| 99445 | Carbonate, wat., unf., incremental titration, field, mg/L | 14 | 9.000 | 0.000 | 2.500 | 9.000 | 5.000 | 1.000 | 0.000 | 0.000 |
| 00452 | Carbonate, wat., filt., incremental titration, field, mg/L | 1 | 0.000 | -- | -- | -- | -- | -- | -- | -- |
| 00940 | Chloride, wat., filt., mg/L | 36 | 22.000 | 4.500 | 13.514 | 20.300 | 16.750 | 13.000 | 11.000 | 5.435 |
| 00950 | Fluoride, wat., filt., mg/L | 36 | 0.300 | 0.100 | 0.219 | 0.300 | 0.300 | 0.200 | 0.200 | 0.100 |
| 00955 | Silica, wat., filt., mg/L | 35 | 7.500 | 0.900 | 4.200 | 7.100 | 5.500 | 4.000 | 3.000 | 1.140 |
| 00945 | Sulfate, wat., filt., mg/L | 36 | 22.000 | 6.900 | 13.128 | 20.300 | 15.750 | 13.000 | 11.000 | 7.325 |
| 70300 | Residue on evaporation, dried at 180 degrees Celsius, wat., filt., mg/L | 35 | 121.000 | 60.000 | 91.000 | 117.000 | 100.000 | 92.000 | 81.000 | 62.400 |
| 00608 | Ammonia, wat., filt., mg/L as nitrogen | 45 | 0.336 | -- | 0.050* | *0.238 | *0.061 | *0.020 | *0.007 | *0.002 |
| 00623 | Ammonia plus organic nitrogen, wat., filt., mg/L as nitrogen | 18 | 1.000 | -- | 0.483* | *1.000 | *0.525 | *0.400 | *0.375 | *0.203 |
| 00625 | Ammonia plus organic nitrogen, wat., unf., mg/L as nitrogen | 45 | 3.400 | 0.300 | 0.907 | 1.270 | 1.000 | 0.900 | 0.750 | 0.400 |
| 00631 | Nitrite plus nitrate, wat., filt., mg/L as nitrogen | 45 | 0.350 | -- | 0.052* | *0.215 | *0.092 | *0.012 | *0.005 | *0.001 |
| 00613 | Nitrite, wat., filt., mg/L as nitrogen | 45 | 0.031 | -- | 0.006* | *0.030 | *0.008 | *0.004 | *0.001 | *0.000 |
| 00605 | Organic nitrogen, wat., unf., mg/L | 40 | 3.400 | 0.260 | 0.840 | 1.295 | 0.935 | 0.780 | 0.642 | 0.312 |
| 00666 | Phosphorus, wat., filt., mg/L | 18 | 0.040 | -- | 0.009* | *0.040 | *0.010 | *0.005 | *0.002 | *0.001 |
| 00671 | Orthophosphate, wat., filt., mg/L as phosphorus | 45 | 0.022 | -- | 0.004* | *0.017 | *0.004 | *0.003 | *0.002 | *0.001 |
| 00665 | Phosphorus, wat., unf., mg/L | 45 | 0.300 | 0.010 | 0.066 | 0.107 | 0.080 | 0.060 | 0.040 | 0.013 |
| 00680 | Organic carbon, wat., unf., mg/L | 37 | 80.000 | 8.000 | 12.249 | 20.600 | 11.000 | 11.000 | 9.450 | 8.000 |
| 70953 | Chlorophyll a, phytoplankton, chromatographic-fluorometric method, ug/L | 37 | 63.700 | 0.900 | 23.370 | 60.640 | 29.700 | 21.900 | 10.300 | 1.170 |
| 70954 | Chlorophyll b, phytoplankton, chromatographic-fluorometric method, ug/L | 37 | 4.300 | -- | 1.658* | *4.120 | *2.100 | *1.400 | *1.000 | *0.246 |
| 01105 | Aluminum, wat., unf., recoverable, ug/L | 24 | 555.000 | 51.000 | 199.667 | 518.750 | 219.750 | 175.000 | 110.000 | 53.250 |
| 01002 | Arsenic, wat., unf., ug/L | 24 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01027 | Cadmium, wat., unf., ug/L | 24 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01034 | Chromium, wat., unf., recoverable, ug/L | 24 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01037 | Cobalt, wat., unf., recoverable, ug/L | 24 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01042 | Copper, wat., unf., recoverable, ug/L | 24 | 2.000 | -- | 1.439* | *2.000 | *2.000 | *1.101 | *1.000 | *0.717 |
| 01045 | Iron, wat., unf., recoverable, ug/L | 38 | 1090.000 | 130.000 | 443.368 | 1023.500 | 562.500 | 390.000 | 275.500 | 139.500 |
| 01051 | Lead, wat., unf., recoverable, ug/L | 24 | 1.000 | -- | 0.922* | *1.000 | *0.954 | *0.917 | *0.887 | *0.838 |

| NWIS Param-eter code | Constituent name | Sample size | Maximum | Minimum | Mean | Percentile |
| --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  | 95th | 75th | 50th | 25th | 5th |
| 01055 | Manganese, wat., unf., recoverable, ug/L | 38 | 807.000 | 60.000 | 207.895 | 674.000 | 235.000 | 180.000 | 122.250 | 88.500 |
| 71900 | Mercury, wat., unf., recoverable, ug/L | 24 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01062 | Molybdenum, wat., unf., recoverable, ug/L | 24 | 3.000 | -- | 1.530* | *2.950 | *2.000 | *1.350 | *0.969 | *0.565 |
| 01067 | Nickel, wat., unf., recoverable, ug/L | 24 | 3.000 | -- | 1.109* | *3.000 | *1.750 | *0.992 | *0.514 | *0.268 |
| 01147 | Selenium, wat., unf., ug/L | 24 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01077 | Silver, wat., unf., recoverable, ug/L | 24 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01092 | Zinc, wat., unf., recoverable, ug/L | 24 | -- | -- | -- | -- | -- | -- | -- | -- |
| 0209771550 Jordan Lake at buoy 9 near Farrington (December 1988–June 1992) |
| 00080 | Color, wat., filt., platinum cobalt units | 5 | 42.000 | 14.000 | -- | -- | -- | -- | -- | -- |
| 00300 | Dissolved oxygen, wat., unf., mg/L | 13 | 12.500 | 7.400 | 9.991 | 12.500 | 11.600 | 10.100 | 8.140 | 7.400 |
| 00301 | Dissolved oxygen, wat., unf., percent of saturation | 5 | 130.000 | 86.000 | -- | -- | -- | -- | -- | -- |
| 00400 | pH, wat., unf., field, standard units | 14 | 8.900 | 6.520 | 7.666 | 8.900 | 8.520 | 7.365 | 6.890 | 6.520 |
| 00403 | pH, wat., unf., laboratory, standard units | 5 | 8.300 | 7.100 | -- | -- | -- | -- | -- | -- |
| 90095 | Specific conductance, wat., unf., laboratory, microsiemens per centimeter at 25 degrees Celsius | 5 | 153.000 | 134.000 | -- | -- | -- | -- | -- | -- |
| 00095 | Specific conductance, wat., unf., microsiemens per centimeter at 25 degrees Celsius | 14 | 180.000 | 96.000 | 130.143 | 180.000 | 146.500 | 131.500 | 108.250 | 96.000 |
| 00900 | Hardness, wat., unf., mg/L as calcium carbonate | 5 | 31.000 | 28.000 | -- | -- | -- | -- | -- | -- |
| 00915 | Calcium, wat., filt., mg/L | 5 | 7.700 | 7.000 | -- | -- | -- | -- | -- | -- |
| 00925 | Magnesium, wat., filt., mg/L | 5 | 2.900 | 2.600 | -- | -- | -- | -- | -- | -- |
| 00935 | Potassium, wat., filt., mg/L | 5 | 3.100 | 2.900 | -- | -- | -- | -- | -- | -- |
| 00931 | Sodium adsorption ratio, wat., number | 5 | 1.000 | 1.000 | -- | -- | -- | -- | -- | -- |
| 00930 | Sodium, wat., filt., mg/L | 5 | 18.000 | 14.000 | -- | -- | -- | -- | -- | -- |
| 00932 | Sodium, wat., percent in equivalents of major cations | 5 | 54.000 | 48.000 | -- | -- | -- | -- | -- | -- |
| 90410 | Acid neutralizing capacity, wat., unf., fixed endpoint (pH 4.5) titration, laboratory, mg/L as calcium carbonate | 5 | 36.000 | 31.000 | -- | -- | -- | -- | -- | -- |
| 00940 | Chloride, wat., filt., mg/L | 5 | 14.000 | 11.000 | -- | -- | -- | -- | -- | -- |
| 00950 | Fluoride, wat., filt., mg/L | 5 | -- | -- | -- | -- | -- | -- | -- | -- |
| 00955 | Silica, wat., filt., mg/L | 5 | 4.800 | 2.300 | -- | -- | -- | -- | -- | -- |
| 00945 | Sulfate, wat., filt., mg/L | 5 | 17.000 | 14.000 | -- | -- | -- | -- | -- | -- |
| 70300 | Residue on evaporation, dried at 180 degrees Celsius, wat., filt., mg/L | 5 | 90.000 | 72.000 | -- | -- | -- | -- | -- | -- |
| 00608 | Ammonia, wat., filt., mg/L as nitrogen | 5 | -- | -- | -- | -- | -- | -- | -- | -- |
| 00623 | Ammonia plus organic nitrogen, wat., filt., mg/L as nitrogen | 5 | 0.500 | 0.300 | -- | -- | -- | -- | -- | -- |
| 00625 | Ammonia plus organic nitrogen, wat., unf., mg/L as nitrogen | 5 | 0.900 | 0.500 | -- | -- | -- | -- | -- | -- |
| 00610 | Ammonia, wat., unf., mg/L as nitrogen | 4 | 0.150 | 0.020 | -- | -- | -- | -- | -- | -- |
| 00620 | Nitrate, wat., unf., mg/L as nitrogen | 2 | 0.270 | 0.070 | -- | -- | -- | -- | -- | -- |

| NWIS Param-eter code | Constituent name | Sample size | Maximum | Minimum | Mean | Percentile |
| --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  | 95th | 75th | 50th | 25th | 5th |
| 00631 | Nitrite plus nitrate, wat., filt., mg/L as nitrogen | 5 | -- | -- | -- | -- | -- | -- | -- | -- |
| 00630 | Nitrite plus nitrate, wat., unf., mg/L as nitrogen | 4 | -- | -- | -- | -- | -- | -- | -- | -- |
| 00613 | Nitrite, wat., filt., mg/L as nitrogen | 5 | -- | -- | -- | -- | -- | -- | -- | -- |
| 00615 | Nitrite, wat., unf., mg/L as nitrogen | 4 | -- | -- | -- | -- | -- | -- | -- | -- |
| 00605 | Organic nitrogen, wat., unf., mg/L | 5 | 0.880 | 0.470 | -- | -- | -- | -- | -- | -- |
| 00666 | Phosphorus, wat., filt., mg/L | 5 | -- | -- | -- | -- | -- | -- | -- | -- |
| 00671 | Orthophosphate, wat., filt., mg/L as phosphorus | 5 | -- | -- | -- | -- | -- | -- | -- | -- |
| 70507 | Orthophosphate, wat., unf., mg/L as phosphorus | 4 | -- | -- | -- | -- | -- | -- | -- | -- |
| 00665 | Phosphorus, wat., unf., mg/L | 5 | 0.100 | 0.020 | -- | -- | -- | -- | -- | -- |
| 00680 | Organic carbon, wat., unf., mg/L | 5 | 11.000 | 8.000 | -- | -- | -- | -- | -- | -- |
| 70953 | Chlorophyll a, phytoplankton, chromatographic-fluorometric method, ug/L | 5 | 9.500 | 1.000 | -- | -- | -- | -- | -- | -- |
| 70954 | Chlorophyll b, phytoplankton, chromatographic-fluorometric method, ug/L | 5 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01105 | Aluminum, wat., unf., recoverable, ug/L | 5 | 310.000 | 40.000 | -- | -- | -- | -- | -- | -- |
| 01002 | Arsenic, wat., unf., ug/L | 5 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01027 | Cadmium, wat., unf., ug/L | 5 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01034 | Chromium, wat., unf., recoverable, ug/L | 5 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01037 | Cobalt, wat., unf., recoverable, ug/L | 5 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01042 | Copper, wat., unf., recoverable, ug/L | 5 | 7.000 | 1.000 | -- | -- | -- | -- | -- | -- |
| 01045 | Iron, wat., unf., recoverable, ug/L | 5 | 650.000 | 60.000 | -- | -- | -- | -- | -- | -- |
| 01051 | Lead, wat., unf., recoverable, ug/L | 5 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01055 | Manganese, wat., unf., recoverable, ug/L | 5 | 470.000 | 20.000 | -- | -- | -- | -- | -- | -- |
| 71900 | Mercury, wat., unf., recoverable, ug/L | 5 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01062 | Molybdenum, wat., unf., recoverable, ug/L | 5 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01067 | Nickel, wat., unf., recoverable, ug/L | 5 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01147 | Selenium, wat., unf., ug/L | 5 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01077 | Silver, wat., unf., recoverable, ug/L | 5 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01092 | Zinc, wat., unf., recoverable, ug/L | 5 | -- | -- | -- | -- | -- | -- | -- | -- |
| 0209782520 White Oak Creek at Green Level (September 1999–August 2002) |
| 00061 | Discharge, instantaneous, cubic feet per second | 17 | 317.000 | 0.720 | 42.591 | 317.000 | 14.500 | 6.200 | 1.600 | 0.720 |
| 00080 | Color, wat., filt., platinum cobalt units | 14 | 200.000 | 40.000 | 99.286 | 200.000 | 142.500 | 90.000 | 58.750 | 40.000 |
| 00300 | Dissolved oxygen, wat., unf., mg/L | 17 | 12.000 | 5.500 | 8.129 | 12.000 | 9.785 | 8.140 | 6.665 | 5.500 |
| 00301 | Dissolved oxygen, wat., unf., percent of saturation | 16 | 93.000 | 55.000 | 79.812 | 93.000 | 87.750 | 79.500 | 76.000 | 55.000 |
| 00400 | pH, wat., unf., field, standard units | 17 | 6.900 | 5.600 | 6.448 | 6.900 | 6.630 | 6.520 | 6.300 | 5.600 |
| 00403 | pH, wat., unf., laboratory, standard units | 16 | 7.500 | 6.400 | 7.094 | 7.500 | 7.200 | 7.100 | 7.025 | 6.400 |
| 90095 | Specific conductance, wat., unf., laboratory, microsiemens per centimeter at 25 degrees Celsius | 16 | 110.000 | 53.000 | 89.062 | 110.000 | 98.250 | 93.000 | 82.000 | 53.000 |
| 00095 | Specific conductance, wat., unf., microsiemens per centimeter at 25 degrees Celsius | 17 | 108.000 | 45.000 | 78.841 | 108.000 | 91.250 | 82.000 | 69.900 | 45.000 |
| 00900 | Hardness, wat., unf., mg/L as calcium carbonate | 16 | 32.000 | 12.000 | 22.938 | 32.000 | 26.750 | 23.000 | 19.250 | 12.000 |
| 00915 | Calcium, wat., filt., mg/L | 16 | 7.900 | 2.700 | 5.556 | 7.900 | 6.650 | 5.350 | 4.475 | 2.700 |
| 00925 | Magnesium, wat., filt., mg/L | 16 | 3.100 | 1.100 | 2.187 | 3.100 | 2.500 | 2.200 | 1.900 | 1.100 |
| 00935 | Potassium, wat., filt., mg/L | 16 | 3.700 | 2.000 | 2.688 | 3.700 | 3.050 | 2.550 | 2.400 | 2.000 |
| 00931 | Sodium adsorption ratio, wat., number | 16 | 0.700 | 0.400 | 0.544 | 0.700 | 0.600 | 0.500 | 0.500 | 0.400 |
| 00930 | Sodium, wat., filt., mg/L | 16 | 8.100 | 3.100 | 6.019 | 8.100 | 6.575 | 6.200 | 5.775 | 3.100 |
| 00932 | Sodium, wat., percent in equivalents of major cations | 16 | 41.000 | 27.000 | 33.500 | 41.000 | 38.000 | 32.500 | 30.250 | 27.000 |
| 90410 | Acid neutralizing capacity, wat., unf., fixed endpoint (pH 4.5) titration, laboratory, mg/L as calcium carbonate | 16 | 36.000 | 7.200 | 21.094 | 36.000 | 28.500 | 19.500 | 14.000 | 7.200 |
| 00410 | Acid neutralizing capacity, wat., unf., fixed endpoint (pH 4.5) titration, field, mg/L as calcium carbonate | 4 | 21.000 | 13.000 | -- | -- | -- | -- | -- | -- |
| 00419 | Acid neutralizing capacity, wat., unf., incremental titration, field, mg/L as calcium carbonate | 14 | 32.000 | 5.000 | 20.429 | 32.000 | 28.250 | 20.500 | 12.750 | 5.000 |
| 99440 | Bicarbonate, wat., unf., incremental titration, field, mg/L | 13 | 40.000 | 5.800 | 24.292 | 40.000 | 34.600 | 24.000 | 15.500 | 5.800 |
| 00940 | Chloride, wat., filt., mg/L | 16 | 10.000 | 3.800 | 6.981 | 10.000 | 8.525 | 6.950 | 6.250 | 3.800 |
| 00950 | Fluoride, wat., filt., mg/L | 16 | 0.200 | -- | 0.092* | *0.200 | *0.100 | *0.088 | *0.056 | *0.038 |
| 00955 | Silica, wat., filt., mg/L | 16 | 9.400 | 4.100 | 7.025 | 9.400 | 8.400 | 6.800 | 5.675 | 4.100 |
| 00945 | Sulfate, wat., filt., mg/L | 16 | 20.000 | 2.600 | 6.888 | 20.000 | 8.575 | 6.250 | 3.700 | 2.600 |
| 70300 | Residue on evaporation, dried at 180 degrees Celsius, wat., filt., mg/L | 16 | 83.000 | 57.000 | 70.438 | 83.000 | 79.750 | 71.000 | 62.000 | 57.000 |
| 00608 | Ammonia, wat., filt., mg/L as nitrogen | 16 | 0.045 | 0.002 | 0.016 | 0.045 | 0.025 | 0.013 | 0.004 | 0.002 |
| 00625 | Ammonia plus organic nitrogen, wat., unf., mg/L as nitrogen | 16 | 0.800 | 0.400 | 0.556 | 0.800 | 0.675 | 0.600 | 0.400 | 0.400 |
| 00631 | Nitrite plus nitrate, wat., filt., mg/L as nitrogen | 16 | 0.130 | -- | 0.038* | *0.130 | *0.053 | *0.025 | *0.015 | *0.005 |
| 00613 | Nitrite, wat., filt., mg/L as nitrogen | 16 | 0.004 | -- | 0.002* | *0.004 | *0.002 | *0.001 | *0.001 | *0.000 |
| 00605 | Organic nitrogen, wat., unf., mg/L | 16 | 0.840 | 0.340 | 0.536 | 0.840 | 0.637 | 0.530 | 0.433 | 0.340 |
| 00671 | Orthophosphate, wat., filt., mg/L as phosphorus | 16 | 0.130 | -- | 0.014* | *0.130 | *0.013 | *0.005 | *0.001 | *0.000 |
| 00665 | Phosphorus, wat., unf., mg/L | 15 | 0.110 | -- | 0.048* | *0.110 | *0.060 | *0.040 | *0.030 | *0.025 |
| 00680 | Organic carbon, wat., unf., mg/L | 16 | 17.000 | 8.500 | 11.519 | 17.000 | 13.000 | 11.000 | 10.000 | 8.500 |
| 01105 | Aluminum, wat., unf., recoverable, ug/L | 8 | 1020.000 | 50.700 | 435.087 | 1020.000 | 893.500 | 252.000 | 142.500 | 50.700 |
| 01002 | Arsenic, wat., unf., ug/L | 8 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01027 | Cadmium, wat., unf., ug/L | 8 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01034 | Chromium, wat., unf., recoverable, ug/L | 8 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01037 | Cobalt, wat., unf., recoverable, ug/L | 8 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01042 | Copper, wat., unf., recoverable, ug/L | 8 | 4.000 | -- | 1.883* | *4.000 | *2.750 | *1.531 | *1.000 | *1.000 |
| 01045 | Iron, wat., unf., recoverable, ug/L | 8 | 3190.000 | 902.000 | 1615.000 | 3190.000 | 2522.500 | 1185.000 | 1001.000 | 902.000 |
| 01051 | Lead, wat., unf., recoverable, ug/L | 8 | 3.000 | -- | 1.424* | *3.000 | *2.000 | *1.032 | *0.823 | *0.636 |
| 01055 | Manganese, wat., unf., recoverable, ug/L | 8 | 297.000 | 55.900 | 158.538 | 297.000 | 275.000 | 110.000 | 80.550 | 55.900 |
| 71900 | Mercury, wat., unf., recoverable, ug/L | 7 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01062 | Molybdenum, wat., unf., recoverable, ug/L | 8 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01067 | Nickel, wat., unf., recoverable, ug/L | 8 | 2.000 | -- | 1.247* | *2.000 | *1.792 | *1.000 | *0.932 | *0.900 |
| 01147 | Selenium, wat., unf., ug/L | 8 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01077 | Silver, wat., unf., recoverable, ug/L | 8 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01092 | Zinc, wat., unf., recoverable, ug/L | 8 | -- | -- | -- | -- | -- | -- | -- | -- |
| 80154 | Suspended sediment concentration, mg/L | 16 | 73.800 | 3.000 | 19.731 | 73.800 | 20.650 | 13.000 | 6.000 | 3.000 |
| 0209799150 B.E. Jordan Lake above U.S. 64 at Wilsonville (July 1991–August 2001) |
| 00080 | Color, wat., filt., platinum cobalt units | 44 | 90.000 | 5.000 | 29.455 | 62.500 | 36.500 | 27.500 | 18.250 | 9.250 |
| 00078 | Transparency, wat., unf., Secchi disc, meters | 37 | 1.200 | 0.450 | 0.650 | 1.020 | 0.750 | 0.600 | 0.550 | 0.450 |
| 00300 | Dissolved oxygen, wat., unf., mg/L | 58 | 12.000 | 0.400 | 7.280 | 10.285 | 8.802 | 7.990 | 6.475 | 0.477 |
| 00301 | Dissolved oxygen, wat., unf., percent of saturation | 58 | 138.000 | 5.000 | 82.966 | 124.500 | 104.000 | 88.500 | 72.750 | 5.000 |
| 00400 | pH, wat., unf., field, standard units | 59 | 9.050 | 6.300 | 7.436 | 8.800 | 7.800 | 7.170 | 6.940 | 6.470 |
| 00403 | pH, wat., unf., laboratory, standard units | 44 | 9.000 | 6.500 | 7.577 | 8.575 | 8.100 | 7.600 | 7.100 | 6.625 |
| 90095 | Specific conductance, wat., unf., laboratory, microsiemens per centimeter at 25 degrees Celsius | 44 | 166.000 | 85.000 | 134.591 | 165.000 | 147.750 | 137.000 | 124.500 | 87.250 |
| 00095 | Specific conductance, wat., unf., microsiemens per centimeter at 25 degrees Celsius | 59 | 194.000 | 80.000 | 135.780 | 166.000 | 147.000 | 136.000 | 128.000 | 94.000 |
| 00900 | Hardness, wat., unf., mg/L as calcium carbonate | 44 | 33.000 | 20.000 | 28.023 | 31.000 | 30.000 | 29.000 | 27.000 | 20.500 |
| 00915 | Calcium, wat., filt., mg/L | 44 | 8.200 | 5.100 | 7.023 | 7.900 | 7.500 | 7.200 | 6.700 | 5.200 |
| 00925 | Magnesium, wat., filt., mg/L | 44 | 3.000 | 1.800 | 2.550 | 2.900 | 2.700 | 2.600 | 2.400 | 1.825 |
| 00935 | Potassium, wat., filt., mg/L | 44 | 3.400 | 1.900 | 2.823 | 3.300 | 3.100 | 2.900 | 2.600 | 1.925 |
| 00931 | Sodium adsorption ratio, wat., number | 44 | 1.000 | 0.700 | 0.943 | 1.000 | 1.000 | 1.000 | 0.900 | 0.700 |
| 00930 | Sodium, wat., filt., mg/L | 44 | 18.000 | 6.900 | 13.109 | 18.000 | 15.000 | 13.000 | 11.000 | 6.975 |
| 00932 | Sodium, wat., percent in equivalents of major cations | 44 | 53.000 | 39.000 | 46.750 | 53.000 | 49.000 | 47.000 | 43.250 | 39.250 |
| 99430 | Carbonate, wat., unf., incremental titration, field, mg/L as calcium carbonate | 24 | 36.000 | 7.000 | 27.375 | 35.750 | 32.000 | 28.000 | 24.250 | 9.250 |
| 90410 | Acid neutralizing capacity, wat., unf., fixed endpoint (pH 4.5) titration, laboratory, mg/L as calcium carbonate | 44 | 38.000 | 11.000 | 29.909 | 36.000 | 34.750 | 31.500 | 26.000 | 18.500 |
| 00410 | Acid neutralizing capacity, wat., unf., fixed endpoint (pH 4.5) titration, field, mg/L as calcium carbonate | 25 | 36.000 | 10.000 | 28.100 | 35.850 | 32.500 | 29.000 | 25.000 | 11.800 |
| 00419 | Acid neutralizing capacity, wat., unf., incremental titration, field, mg/L as calcium carbonate | 8 | 33.000 | 24.800 | 29.225 | 33.000 | 31.750 | 29.500 | 26.500 | 24.800 |
| 99440 | Bicarbonate, wat., unf., incremental titration, field, mg/L | 32 | 42.000 | 9.000 | 33.175 | 41.350 | 38.000 | 34.000 | 30.475 | 16.150 |

| NWIS Param-eter code | Constituent name | Sample size | Maximum | Minimum | Mean | Percentile |
| --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  | 95th | 75th | 50th | 25th | 5th |
| 99445 | Carbonate, wat., unf., incremental titration, field, mg/L | 14 | 4.000 | 0.000 | 0.929 | 4.000 | 1.250 | 0.500 | 0.000 | 0.000 |
| 00452 | Carbonate, wat., filt., incremental titration, field, mg/L | 1 | 0.000 | -- | -- | -- | -- | -- | -- | -- |
| 00940 | Chloride, wat., filt., mg/L | 43 | 20.000 | 6.400 | 11.937 | 16.600 | 14.000 | 12.000 | 11.000 | 6.560 |
| 00950 | Fluoride, wat., filt., mg/L | 43 | 0.300 | 0.100 | 0.184 | 0.280 | 0.200 | 0.200 | 0.200 | 0.100 |
| 00955 | Silica, wat., filt., mg/L | 42 | 6.500 | 0.800 | 4.021 | 6.440 | 5.025 | 4.150 | 3.125 | 1.915 |
| 00945 | Sulfate, wat., filt., mg/L | 43 | 18.000 | 0.300 | 12.442 | 16.800 | 15.000 | 12.000 | 11.000 | 8.040 |
| 70300 | Residue on evaporation, dried at 180 degrees Celsius, wat., filt., mg/L | 42 | 114.000 | 62.000 | 82.548 | 106.250 | 90.500 | 80.500 | 74.000 | 64.300 |
| 00608 | Ammonia, wat., filt., mg/L as nitrogen | 53 | 1.400 | -- | 0.073* | *0.270 | *0.070 | *0.020 | *0.005 | *0.002 |
| 00623 | Ammonia plus organic nitrogen, wat., filt., mg/L as nitrogen | 26 | 0.900 | 0.200 | 0.438 | 0.830 | 0.500 | 0.400 | 0.375 | 0.235 |
| 00625 | Ammonia plus organic nitrogen, wat., unf., mg/L as nitrogen | 53 | 2.200 | 0.400 | 0.717 | 1.000 | 0.800 | 0.700 | 0.600 | 0.470 |
| 00610 | Ammonia, wat., unf., mg/L as nitrogen | 6 | -- | -- | -- | -- | -- | -- | -- | -- |
| 00620 | Nitrate, wat., unf., mg/L as nitrogen | 1 | 0.110 | -- | -- | -- | -- | -- | -- | -- |
| 00631 | Nitrite plus nitrate, wat., filt., mg/L as nitrogen | 53 | 0.270 | -- | 0.060* | *0.220 | *0.120 | *0.012 | *0.004 | *0.001 |
| 00630 | Nitrite plus nitrate, wat., unf., mg/L as nitrogen | 6 | -- | -- | -- | -- | -- | -- | -- | -- |
| 00613 | Nitrite, wat., filt., mg/L as nitrogen | 53 | 0.027 | -- | 0.006* | *0.020 | *0.008 | *0.004 | *0.002 | *0.001 |
| 00615 | Nitrite, wat., unf., mg/L as nitrogen | 6 | -- | -- | -- | -- | -- | -- | -- | -- |
| 00605 | Organic nitrogen, wat., unf., mg/L | 44 | 1.000 | 0.320 | 0.640 | 0.970 | 0.740 | 0.610 | 0.522 | 0.392 |
| 00666 | Phosphorus, wat., filt., mg/L | 26 | 0.030 | -- | 0.009* | *0.030 | *0.010 | *0.006 | *0.003 | *0.001 |
| 00671 | Orthophosphate, wat., filt., mg/L as phosphorus | 53 | 0.088 | -- | 0.004* | *0.010 | *0.004 | *0.002 | *0.001 | *0.000 |
| 70507 | Orthophosphate, wat., unf., mg/L as phosphorus | 6 | -- | -- | -- | -- | -- | -- | -- | -- |
| 00665 | Phosphorus, wat., unf., mg/L | 53 | 0.190 | -- | 0.039* | *0.063 | *0.041 | *0.040 | *0.030 | *0.014 |
| 00680 | Organic carbon, wat., unf., mg/L | 43 | 17.000 | 2.300 | 8.958 | 13.600 | 9.600 | 8.800 | 8.100 | 6.820 |
| 70953 | Chlorophyll a, phytoplankton, chromatographic-fluorometric method, ug/L | 43 | 40.500 | 1.200 | 13.307 | 37.700 | 18.600 | 10.500 | 4.700 | 1.620 |
| 70954 | Chlorophyll b, phytoplankton, chromatographic-fluorometric method, ug/L | 43 | 3.900 | -- | 0.801* | *2.060 | *1.100 | *0.700 | *0.293 | *0.105 |
| 01105 | Aluminum, wat., unf., recoverable, ug/L | 31 | 294.000 | 20.000 | 83.255 | 243.600 | 100.000 | 60.000 | 50.000 | 26.000 |
| 01002 | Arsenic, wat., unf., ug/L | 31 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01027 | Cadmium, wat., unf., ug/L | 31 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01034 | Chromium, wat., unf., recoverable, ug/L | 31 | 4.000 | -- | 0.677* | *3.580 | *0.733 | *0.271 | *0.100 | *0.024 |
| 01037 | Cobalt, wat., unf., recoverable, ug/L | 31 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01042 | Copper, wat., unf., recoverable, ug/L | 31 | 3.000 | -- | 1.232* | *3.000 | *2.000 | *1.000 | *0.698 | *0.370 |
| 01045 | Iron, wat., unf., recoverable, ug/L | 48 | 3910.000 | 40.000 | 335.879 | 1883.749 | 267.500 | 165.000 | 110.000 | 53.015 |
| 01051 | Lead, wat., unf., recoverable, ug/L | 30 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01055 | Manganese, wat., unf., recoverable, ug/L | 48 | 3670.000 | 10.000 | 293.363 | 2311.348 | 177.250 | 110.000 | 80.000 | 34.500 |
| 71900 | Mercury, wat., unf., recoverable, ug/L | 31 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01062 | Molybdenum, wat., unf., recoverable, ug/L | 31 | 3.000 | -- | 1.444* | *3.000 | *2.000 | *1.000 | *0.884 | *0.524 |
| 01067 | Nickel, wat., unf., recoverable, ug/L | 31 | 8.000 | -- | 1.081* | *5.000 | *1.000 | *0.617 | *0.304 | *0.104 |
| 01147 | Selenium, wat., unf., ug/L | 31 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01077 | Silver, wat., unf., recoverable, ug/L | 31 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01092 | Zinc, wat., unf., recoverable, ug/L | 31 | -- | -- | -- | -- | -- | -- | -- | -- |
| 0209801050 Jordan Lake at buoy 7 below U.S. 64 near Griffins Crossroads (December 1988–June 1992) |
| 00080 | Color, wat., filt., platinum cobalt units | 5 | 30.000 | 13.000 | -- | -- | -- | -- | -- | -- |
| 00300 | Dissolved oxygen, wat., unf., mg/L | 13 | 12.700 | 8.600 | 9.985 | 12.700 | 11.050 | 9.800 | 8.755 | 8.600 |
| 00301 | Dissolved oxygen, wat., unf., percent of saturation | 5 | 122.000 | 81.000 | -- | -- | -- | -- | -- | -- |
| 00400 | pH, wat., unf., field, standard units | 13 | 9.400 | 6.600 | 7.927 | 9.400 | 8.925 | 7.600 | 6.950 | 6.600 |
| 00403 | pH, wat., unf., laboratory, standard units | 5 | 8.700 | 7.200 | -- | -- | -- | -- | -- | -- |
| 90095 | Specific conductance, wat., unf., laboratory, microsiemens per centimeter at 25 degrees Celsius | 5 | 157.000 | 143.000 | -- | -- | -- | -- | -- | -- |
| 00095 | Specific conductance, wat., unf., microsiemens per centimeter at 25 degrees Celsius | 13 | 179.000 | 98.000 | 131.769 | 179.000 | 150.500 | 130.000 | 109.000 | 98.000 |
| 00900 | Hardness, wat., unf., mg/L as calcium carbonate | 5 | 30.000 | 28.000 | -- | -- | -- | -- | -- | -- |
| 00915 | Calcium, wat., filt., mg/L | 5 | 7.500 | 6.900 | -- | -- | -- | -- | -- | -- |
| 00925 | Magnesium, wat., filt., mg/L | 5 | 3.100 | 2.600 | -- | -- | -- | -- | -- | -- |
| 00935 | Potassium, wat., filt., mg/L | 5 | 3.200 | 3.000 | -- | -- | -- | -- | -- | -- |
| 00931 | Sodium adsorption ratio, wat., number | 5 | 1.000 | 1.000 | -- | -- | -- | -- | -- | -- |
| 00930 | Sodium, wat., filt., mg/L | 5 | 18.000 | 16.000 | -- | -- | -- | -- | -- | -- |
| 00932 | Sodium, wat., percent in equivalents of major cations | 5 | 54.000 | 50.000 | -- | -- | -- | -- | -- | -- |
| 90410 | Acid neutralizing capacity, wat., unf., fixed endpoint (pH 4.5) titration, laboratory, mg/L as calcium carbonate | 5 | 36.000 | 30.000 | -- | -- | -- | -- | -- | -- |
| 00940 | Chloride, wat., filt., mg/L | 5 | 14.000 | 12.000 | -- | -- | -- | -- | -- | -- |
| 00950 | Fluoride, wat., filt., mg/L | 5 | 0.300 | 0.200 | -- | -- | -- | -- | -- | -- |
| 00955 | Silica, wat., filt., mg/L | 5 | 4.900 | 2.300 | -- | -- | -- | -- | -- | -- |
| 00945 | Sulfate, wat., filt., mg/L | 5 | 18.000 | 15.000 | -- | -- | -- | -- | -- | -- |
| 70300 | Residue on evaporation, dried at 180 degrees Celsius, wat., filt., mg/L | 5 | 96.000 | 77.000 | -- | -- | -- | -- | -- | -- |
| 00608 | Ammonia, wat., filt., mg/L as nitrogen | 5 | -- | -- | -- | -- | -- | -- | -- | -- |
| 00623 | Ammonia plus organic nitrogen, wat., filt., mg/L as nitrogen | 5 | 0.500 | 0.300 | -- | -- | -- | -- | -- | -- |
| 00625 | Ammonia plus organic nitrogen, wat., unf., mg/L as nitrogen | 5 | 0.800 | 0.500 | -- | -- | -- | -- | -- | -- |
| 00610 | Ammonia, wat., unf., mg/L as nitrogen | 4 | -- | -- | -- | -- | -- | -- | -- | -- |
| 00620 | Nitrate, wat., unf., mg/L as nitrogen | 2 | 0.280 | 0.140 | -- | -- | -- | -- | -- | -- |

| NWIS Param-eter code | Constituent name | Sample size | Maximum | Minimum | Mean | Percentile |
| --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  | 95th | 75th | 50th | 25th | 5th |
| 00631 | Nitrite plus nitrate, wat., filt., mg/L as nitrogen | 5 | -- | -- | -- | -- | -- | -- | -- | -- |
| 00630 | Nitrite plus nitrate, wat., unf., mg/L as nitrogen | 4 | -- | -- | -- | -- | -- | -- | -- | -- |
| 00613 | Nitrite, wat., filt., mg/L as nitrogen | 5 | -- | -- | -- | -- | -- | -- | -- | -- |
| 00615 | Nitrite, wat., unf., mg/L as nitrogen | 4 | 0.020 | 0.000 | -- | -- | -- | -- | -- | -- |
| 00605 | Organic nitrogen, wat., unf., mg/L | 4 | 0.770 | 0.470 | -- | -- | -- | -- | -- | -- |
| 00666 | Phosphorus, wat., filt., mg/L | 5 | -- | -- | -- | -- | -- | -- | -- | -- |
| 00671 | Orthophosphate, wat., filt., mg/L as phosphorus | 5 | -- | -- | -- | -- | -- | -- | -- | -- |
| 70507 | Orthophosphate, wat., unf., mg/L as phosphorus | 4 | -- | -- | -- | -- | -- | -- | -- | -- |
| 00665 | Phosphorus, wat., unf., mg/L | 5 | 0.100 | 0.020 | -- | -- | -- | -- | -- | -- |
| 00680 | Organic carbon, wat., unf., mg/L | 5 | 26.000 | 8.000 | -- | -- | -- | -- | -- | -- |
| 70953 | Chlorophyll a, phytoplankton, chromatographic-fluorometric method, ug/L | 4 | 7.800 | 1.100 | -- | -- | -- | -- | -- | -- |
| 70954 | Chlorophyll b, phytoplankton, chromatographic-fluorometric method, ug/L | 4 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01105 | Aluminum, wat., unf., recoverable, ug/L | 5 | 300.000 | 40.000 | -- | -- | -- | -- | -- | -- |
| 01002 | Arsenic, wat., unf., ug/L | 5 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01027 | Cadmium, wat., unf., ug/L | 5 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01034 | Chromium, wat., unf., recoverable, ug/L | 5 | 2.000 | 1.000 | -- | -- | -- | -- | -- | -- |
| 01037 | Cobalt, wat., unf., recoverable, ug/L | 5 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01042 | Copper, wat., unf., recoverable, ug/L | 5 | 8.000 | 1.000 | -- | -- | -- | -- | -- | -- |
| 01045 | Iron, wat., unf., recoverable, ug/L | 5 | 570.000 | 60.000 | -- | -- | -- | -- | -- | -- |
| 01051 | Lead, wat., unf., recoverable, ug/L | 5 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01055 | Manganese, wat., unf., recoverable, ug/L | 5 | 390.000 | 20.000 | -- | -- | -- | -- | -- | -- |
| 71900 | Mercury, wat., unf., recoverable, ug/L | 5 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01062 | Molybdenum, wat., unf., recoverable, ug/L | 5 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01067 | Nickel, wat., unf., recoverable, ug/L | 5 | 2.000 | 1.000 | -- | -- | -- | -- | -- | -- |
| 01147 | Selenium, wat., unf., ug/L | 5 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01077 | Silver, wat., unf., recoverable, ug/L | 5 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01092 | Zinc, wat., unf., recoverable, ug/L | 5 | -- | -- | -- | -- | -- | -- | -- | -- |
| 0209801100 B.E. Jordan Lake at Bells Landing near Griffins Crossroads (July 1991–August 2001) |
| 00080 | Color, wat., filt., platinum cobalt units | 28 | 110.000 | 5.000 | 27.714 | 85.250 | 30.000 | 20.500 | 15.250 | 6.350 |
| 00078 | Transparency, wat., unf., Secchi disc, meters | 19 | 1.100 | 0.450 | 0.663 | 1.100 | 0.750 | 0.650 | 0.550 | 0.450 |
| 00300 | Dissolved oxygen, wat., unf., mg/L | 41 | 11.200 | 0.380 | 7.385 | 10.570 | 9.200 | 8.200 | 6.300 | 0.641 |
| 00301 | Dissolved oxygen, wat., unf., percent of saturation | 41 | 129.000 | 5.000 | 87.366 | 126.600 | 111.500 | 95.000 | 73.000 | 7.600 |
| 00400 | pH, wat., unf., field, standard units | 42 | 9.090 | 6.200 | 7.612 | 9.009 | 8.500 | 7.315 | 6.760 | 6.395 |
| 00403 | pH, wat., unf., laboratory, standard units | 28 | 9.000 | 6.800 | 7.782 | 8.955 | 8.450 | 7.600 | 7.300 | 6.890 |
| 90095 | Specific conductance, wat., unf., laboratory, microsiemens per centimeter at 25 degrees Celsius | 28 | 272.000 | 86.000 | 145.714 | 230.150 | 154.750 | 149.500 | 128.500 | 90.500 |
| 00095 | Specific conductance, wat., unf., microsiemens per centimeter at 25 degrees Celsius | 42 | 177.000 | 83.000 | 143.500 | 174.650 | 156.000 | 146.500 | 133.750 | 97.050 |
| 00900 | Hardness, wat., unf., mg/L as calcium carbonate | 28 | 32.000 | 20.000 | 27.893 | 31.550 | 30.000 | 28.000 | 27.000 | 20.900 |
| 00915 | Calcium, wat., filt., mg/L | 28 | 7.900 | 5.000 | 6.843 | 7.810 | 7.300 | 6.900 | 6.700 | 5.090 |
| 00925 | Magnesium, wat., filt., mg/L | 28 | 3.100 | 1.900 | 2.607 | 3.010 | 2.800 | 2.600 | 2.500 | 1.990 |
| 00935 | Potassium, wat., filt., mg/L | 28 | 3.600 | 1.900 | 2.943 | 3.555 | 3.275 | 3.000 | 2.625 | 1.945 |
| 00931 | Sodium adsorption ratio, wat., number | 28 | 2.000 | 0.700 | 1.004 | 1.550 | 1.000 | 1.000 | 1.000 | 0.745 |
| 00930 | Sodium, wat., filt., mg/L | 28 | 20.000 | 7.000 | 14.514 | 19.550 | 17.000 | 15.000 | 12.250 | 7.765 |
| 00932 | Sodium, wat., percent in equivalents of major cations | 28 | 57.000 | 39.000 | 49.250 | 55.650 | 52.750 | 49.000 | 47.250 | 40.800 |
| 99430 | Carbonate, wat., unf., incremental titration, field, mg/L as calcium carbonate | 13 | 39.000 | 16.000 | 27.154 | 39.000 | 33.000 | 26.000 | 22.500 | 16.000 |
| 90410 | Acid neutralizing capacity, wat., unf., fixed endpoint (pH 4.5) titration, laboratory, mg/L as calcium carbonate | 28 | 47.000 | 19.000 | 31.857 | 42.950 | 35.000 | 32.000 | 28.000 | 20.800 |
| 00410 | Acid neutralizing capacity, wat., unf., fixed endpoint (pH 4.5) titration, field, mg/L as calcium carbonate | 14 | 39.000 | 16.000 | 28.271 | 39.000 | 33.850 | 28.000 | 24.750 | 16.000 |
| 00419 | Acid neutralizing capacity, wat., unf., incremental titration, field, mg/L as calcium carbonate | 5 | 31.000 | 24.000 | -- | -- | -- | -- | -- | -- |
| 99440 | Bicarbonate, wat., unf., incremental titration, field, mg/L | 18 | 48.000 | 20.000 | 32.939 | 48.000 | 39.000 | 33.500 | 27.000 | 20.000 |

| NWIS Param-eter code | Constituent name | Sample size | Maximum | Minimum | Mean | Percentile |
| --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  | 95th | 75th | 50th | 25th | 5th |
| 99445 | Carbonate, wat., unf., incremental titration, field, mg/L | 10 | 9.000 | 0.000 | 1.200 | 9.000 | 1.250 | 0.000 | 0.000 | 0.000 |
| 00940 | Chloride, wat., filt., mg/L | 28 | 16.000 | 6.400 | 12.246 | 16.000 | 14.000 | 13.000 | 11.000 | 6.715 |
| 00950 | Fluoride, wat., filt., mg/L | 28 | 0.300 | -- | 0.194* | *0.300 | *0.200 | *0.200 | *0.200 | *0.100 |
| 00955 | Silica, wat., filt., mg/L | 28 | 6.300 | 1.900 | 4.114 | 6.075 | 5.250 | 4.450 | 2.700 | 2.035 |
| 00945 | Sulfate, wat., filt., mg/L | 28 | 18.000 | 9.300 | 14.171 | 18.000 | 16.750 | 14.500 | 12.000 | 9.390 |
| 70300 | Residue on evaporation, dried at 180 degrees Celsius, wat., filt., mg/L | 27 | 110.000 | 63.000 | 85.741 | 106.000 | 93.000 | 88.000 | 78.000 | 65.000 |
| 00608 | Ammonia, wat., filt., mg/L as nitrogen | 36 | 0.289 | -- | 0.046* | *0.189 | *0.040 | *0.020 | *0.006 | *0.002 |
| 00623 | Ammonia plus organic nitrogen, wat., filt., mg/L as nitrogen | 19 | 1.200 | 0.300 | 0.474 | 1.200 | 0.500 | 0.400 | 0.300 | 0.300 |
| 00625 | Ammonia plus organic nitrogen, wat., unf., mg/L as nitrogen | 36 | 1.300 | 0.400 | 0.722 | 1.215 | 0.800 | 0.700 | 0.600 | 0.485 |
| 00610 | Ammonia, wat., unf., mg/L as nitrogen | 5 | -- | -- | -- | -- | -- | -- | -- | -- |
| 00620 | Nitrate, wat., unf., mg/L as nitrogen | 1 | 0.150 | -- | -- | -- | -- | -- | -- | -- |
| 00631 | Nitrite plus nitrate, wat., filt., mg/L as nitrogen | 36 | 0.260 | -- | 0.072* | *0.243 | *0.110 | *0.021 | *0.006 | *0.002 |
| 00630 | Nitrite plus nitrate, wat., unf., mg/L as nitrogen | 5 | -- | -- | -- | -- | -- | -- | -- | -- |
| 00613 | Nitrite, wat., filt., mg/L as nitrogen | 36 | 0.020 | -- | 0.007* | *0.020 | *0.008 | *0.007 | *0.004 | *0.002 |
| 00615 | Nitrite, wat., unf., mg/L as nitrogen | 5 | -- | -- | -- | -- | -- | -- | -- | -- |
| 00605 | Organic nitrogen, wat., unf., mg/L | 30 | 1.200 | 0.380 | 0.659 | 1.046 | 0.740 | 0.660 | 0.575 | 0.424 |
| 00666 | Phosphorus, wat., filt., mg/L | 19 | 0.030 | -- | 0.007* | *0.030 | *0.010 | *0.004 | *0.002 | *0.001 |
| 00671 | Orthophosphate, wat., filt., mg/L as phosphorus | 36 | 0.010 | -- | 0.003* | *0.010 | *0.003 | *0.002 | *0.001 | *0.000 |
| 70507 | Orthophosphate, wat., unf., mg/L as phosphorus | 5 | -- | -- | -- | -- | -- | -- | -- | -- |
| 00665 | Phosphorus, wat., unf., mg/L | 36 | 0.130 | -- | 0.036* | *0.090 | *0.044 | *0.030 | *0.026 | *0.011 |
| 00680 | Organic carbon, wat., unf., mg/L | 26 | 10.000 | 6.700 | 8.488 | 9.930 | 9.225 | 8.550 | 7.700 | 6.910 |
| 70953 | Chlorophyll a, phytoplankton, chromatographic-fluorometric method, ug/L | 28 | 35.100 | 2.400 | 12.175 | 32.265 | 16.325 | 9.250 | 6.025 | 2.895 |
| 70954 | Chlorophyll b, phytoplankton, chromatographic-fluorometric method, ug/L | 28 | 1.800 | -- | 0.610* | *1.575 | *0.950 | *0.450 | *0.283 | *0.129 |
| 01105 | Aluminum, wat., unf., recoverable, ug/L | 23 | 257.000 | 30.000 | 92.191 | 255.600 | 130.000 | 60.000 | 40.000 | 30.000 |
| 01002 | Arsenic, wat., unf., ug/L | 23 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01025 | Cadmium, wat., filt., ug/L | 1 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01027 | Cadmium, wat., unf., ug/L | 23 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01034 | Chromium, wat., unf., recoverable, ug/L | 23 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01037 | Cobalt, wat., unf., recoverable, ug/L | 23 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01040 | Copper, wat., filt., ug/L | 1 | 2.000 | -- | -- | -- | -- | -- | -- | -- |
| 01042 | Copper, wat., unf., recoverable, ug/L | 23 | 6.000 | -- | 1.552* | *5.400 | *2.000 | *1.000 | *0.666 | *0.305 |
| 01045 | Iron, wat., unf., recoverable, ug/L | 40 | 2740.000 | 47.400 | 290.895 | 1719.151 | 247.500 | 140.000 | 80.000 | 49.905 |
| 01049 | Lead, wat., filt., ug/L | 1 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01051 | Lead, wat., unf., recoverable, ug/L | 22 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01056 | Manganese, wat., filt., ug/L | 1 | 66.000 | -- | -- | -- | -- | -- | -- | -- |
| 01055 | Manganese, wat., unf., recoverable, ug/L | 39 | 2930.000 | 20.000 | 208.526 | 664.000 | 161.000 | 90.000 | 57.400 | 20.000 |
| 71900 | Mercury, wat., unf., recoverable, ug/L | 23 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01062 | Molybdenum, wat., unf., recoverable, ug/L | 23 | 3.000 | -- | 1.211* | *2.800 | *2.000 | *1.000 | *0.704 | *0.404 |
| 01067 | Nickel, wat., unf., recoverable, ug/L | 23 | 3.000 | -- | 1.156* | *2.800 | *2.000 | *1.000 | *0.665 | *0.382 |
| 01145 | Selenium, wat., filt., ug/L | 1 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01147 | Selenium, wat., unf., ug/L | 23 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01077 | Silver, wat., unf., recoverable, ug/L | 23 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01090 | Zinc, wat., filt., ug/L | 1 | 21.000 | -- | -- | -- | -- | -- | -- | -- |
| 01092 | Zinc, wat., unf., recoverable, ug/L | 23 | -- | -- | -- | -- | -- | -- | -- | -- |
| 02098198 Haw River below B. Everett Jordan dam near Moncure (December 1988–April 1995) |
| 00060 | Discharge, cubic feet per second | 2 | 390.000 | 384.000 | -- | -- | -- | -- | -- | -- |
| 00061 | Discharge, instantaneous, cubic feet per second | 16 | 14700.000 | 235.000 | 2403.562 | 14700.000 | 3855.000 | 542.000 | 426.000 | 235.000 |
| 00300 | Dissolved oxygen, wat., unf., mg/L | 16 | 13.000 | 6.500 | 8.881 | 13.000 | 10.150 | 9.250 | 6.725 | 6.500 |
| 00400 | pH, wat., unf., field, standard units | 17 | 7.400 | 6.300 | 7.064 | 7.400 | 7.255 | 7.100 | 6.900 | 6.300 |
| 00095 | Specific conductance, wat., unf., microsiemens per centimeter at 25 degrees Celsius | 16 | 216.000 | 63.000 | 131.312 | 216.000 | 158.750 | 129.000 | 94.500 | 63.000 |
| 00927 | Magnesium, wat., unf., recoverable, mg/L | 1 | 2.700 | -- | -- | -- | -- | -- | -- | -- |
| 31616 | Fecal coliform, M-FC MF (0.45 micron) method, wat., colonies per 100 milliliters | 1 | -- | -- | -- | -- | -- | -- | -- | -- |
| 0210140200 Deep River at Carbonton (January 1993–August 1996) |
| 00080 | Color, wat., filt., platinum cobalt units | 1 | 200.000 | -- | -- | -- | -- | -- | -- | -- |
| 00300 | Dissolved oxygen, wat., unf., mg/L | 6 | 9.900 | 5.200 | 6.750 | 9.900 | 8.775 | 5.900 | 5.200 | 5.200 |
| 00301 | Dissolved oxygen, wat., unf., percent of saturation | 2 | 88.000 | 77.000 | -- | -- | -- | -- | -- | -- |
| 00400 | pH, wat., unf., field, standard units | 6 | 7.100 | 6.900 | 7.017 | 7.100 | 7.100 | 7.000 | 6.975 | 6.900 |
| 00403 | pH, wat., unf., laboratory, standard units | 1 | 6.700 | -- | -- | -- | -- | -- | -- | -- |
| 90095 | Specific conductance, wat., unf., laboratory, microsiemens per centimeter at 25 degrees Celsius | 1 | 86.000 | -- | -- | -- | -- | -- | -- | -- |
| 00095 | Specific conductance, wat., unf., microsiemens per centimeter at 25 degrees Celsius | 6 | 242.000 | 80.000 | 138.333 | 242.000 | 180.500 | 132.500 | 82.250 | 80.000 |
| 00900 | Hardness, wat., unf., mg/L as calcium carbonate | 1 | 23.000 | -- | -- | -- | -- | -- | -- | -- |
| 00915 | Calcium, wat., filt., mg/L | 1 | 5.400 | -- | -- | -- | -- | -- | -- | -- |
| 00925 | Magnesium, wat., filt., mg/L | 1 | 2.200 | -- | -- | -- | -- | -- | -- | -- |
| 00935 | Potassium, wat., filt., mg/L | 1 | 2.900 | -- | -- | -- | -- | -- | -- | -- |
| 00931 | Sodium adsorption ratio, wat., number | 1 | 0.500 | -- | -- | -- | -- | -- | -- | -- |
| 00930 | Sodium, wat., filt., mg/L | 1 | 5.800 | -- | -- | -- | -- | -- | -- | -- |
| 00932 | Sodium, wat., percent in equivalents of major cations | 1 | 32.000 | -- | -- | -- | -- | -- | -- | -- |
| 99430 | Carbonate, wat., unf., incremental titration, field, mg/L as calcium carbonate | 1 | 20.000 | -- | -- | -- | -- | -- | -- | -- |
| 90410 | Acid neutralizing capacity, wat., unf., fixed endpoint (pH 4.5) titration, laboratory, mg/L as calcium carbonate | 1 | 17.000 | -- | -- | -- | -- | -- | -- | -- |
| 00410 | Acid neutralizing capacity, wat., unf., fixed endpoint (pH 4.5) titration, field, mg/L as calcium carbonate | 1 | 22.000 | -- | -- | -- | -- | -- | -- | -- |
| 99440 | Bicarbonate, wat., unf., incremental titration, field, mg/L | 1 | 24.000 | -- | -- | -- | -- | -- | -- | -- |
| 99445 | Carbonate, wat., unf., incremental titration, field, mg/L | 1 | 0.000 | -- | -- | -- | -- | -- | -- | -- |
| 00940 | Chloride, wat., filt., mg/L | 1 | 7.600 | -- | -- | -- | -- | -- | -- | -- |
| 00950 | Fluoride, wat., filt., mg/L | 1 | -- | -- | -- | -- | -- | -- | -- | -- |
| 00955 | Silica, wat., filt., mg/L | 1 | 9.500 | -- | -- | -- | -- | -- | -- | -- |
| 00945 | Sulfate, wat., filt., mg/L | 1 | 7.300 | -- | -- | -- | -- | -- | -- | -- |
| 70300 | Residue on evaporation, dried at 180 degrees Celsius, wat., filt., mg/L | 1 | 66.000 | -- | -- | -- | -- | -- | -- | -- |
| 00608 | Ammonia, wat., filt., mg/L as nitrogen | 1 | 0.100 | -- | -- | -- | -- | -- | -- | -- |
| 00623 | Ammonia plus organic nitrogen, wat., filt., mg/L as nitrogen | 1 | 0.500 | -- | -- | -- | -- | -- | -- | -- |
| 00625 | Ammonia plus organic nitrogen, wat., unf., mg/L as nitrogen | 1 | 0.800 | -- | -- | -- | -- | -- | -- | -- |
| 00631 | Nitrite plus nitrate, wat., filt., mg/L as nitrogen | 1 | 0.800 | -- | -- | -- | -- | -- | -- | -- |
| 00613 | Nitrite, wat., filt., mg/L as nitrogen | 1 | 0.030 | -- | -- | -- | -- | -- | -- | -- |
| 00605 | Organic nitrogen, wat., unf., mg/L | 1 | 0.700 | -- | -- | -- | -- | -- | -- | -- |
| 00666 | Phosphorus, wat., filt., mg/L | 1 | 0.110 | -- | -- | -- | -- | -- | -- | -- |
| 00671 | Orthophosphate, wat., filt., mg/L as phosphorus | 1 | 0.100 | -- | -- | -- | -- | -- | -- | -- |
| 00665 | Phosphorus, wat., unf., mg/L | 1 | 0.250 | -- | -- | -- | -- | -- | -- | -- |
| 00680 | Organic carbon, wat., unf., mg/L | 1 | 12.000 | -- | -- | -- | -- | -- | -- | -- |
| 01105 | Aluminum, wat., unf., recoverable, ug/L | 1 | 1400.000 | -- | -- | -- | -- | -- | -- | -- |
| 01002 | Arsenic, wat., unf., ug/L | 1 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01027 | Cadmium, wat., unf., ug/L | 1 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01034 | Chromium, wat., unf., recoverable, ug/L | 1 | 4.000 | -- | -- | -- | -- | -- | -- | -- |
| 01037 | Cobalt, wat., unf., recoverable, ug/L | 1 | 1.000 | -- | -- | -- | -- | -- | -- | -- |
| 01042 | Copper, wat., unf., recoverable, ug/L | 1 | 5.000 | -- | -- | -- | -- | -- | -- | -- |
| 01045 | Iron, wat., unf., recoverable, ug/L | 1 | 1700.000 | -- | -- | -- | -- | -- | -- | -- |
| 01051 | Lead, wat., unf., recoverable, ug/L | 1 | 3.000 | -- | -- | -- | -- | -- | -- | -- |
| 01055 | Manganese, wat., unf., recoverable, ug/L | 1 | 70.000 | -- | -- | -- | -- | -- | -- | -- |
| 71900 | Mercury, wat., unf., recoverable, ug/L | 1 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01062 | Molybdenum, wat., unf., recoverable, ug/L | 1 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01067 | Nickel, wat., unf., recoverable, ug/L | 1 | 2.000 | -- | -- | -- | -- | -- | -- | -- |
| 01147 | Selenium, wat., unf., ug/L | 1 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01077 | Silver, wat., unf., recoverable, ug/L | 1 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01092 | Zinc, wat., unf., recoverable, ug/L | 1 | 20.000 | -- | -- | -- | -- | -- | -- | -- |
| 80154 | Suspended sediment concentration, mg/L | 2 | 68.000 | 48.000 | -- | -- | -- | -- | -- | -- |
| 0210215985 Cape Fear River at N.C. 42 near Brickhaven (October 1988–August 2001) |
| 00060 | Discharge, cubic feet per second | 121 | 22700.000 | 439.000 | 3318.248 | 15690.002 | 3635.000 | 1410.000 | 750.000 | 551.800 |
| 00080 | Color, wat., filt., platinum cobalt units | 120 | 250.000 | 12.000 | 69.550 | 199.000 | 91.500 | 55.000 | 35.250 | 15.250 |
| 00300 | Dissolved oxygen, wat., unf., mg/L | 119 | 15.000 | 2.200 | 9.084 | 12.900 | 11.400 | 9.100 | 7.200 | 4.200 |
| 00301 | Dissolved oxygen, wat., unf., percent of saturation | 117 | 173.000 | 27.000 | 91.068 | 123.200 | 101.000 | 93.000 | 80.000 | 51.000 |
| 00400 | pH, wat., unf., field, standard units | 121 | 8.430 | 6.200 | 7.114 | 7.754 | 7.310 | 7.100 | 6.855 | 6.600 |
| 00403 | pH, wat., unf., laboratory, standard units | 121 | 8.000 | 6.400 | 7.322 | 7.800 | 7.500 | 7.300 | 7.100 | 6.900 |
| 90095 | Specific conductance, wat., unf., laboratory, microsiemens per centimeter at 25 degrees Celsius | 121 | 298.000 | 46.000 | 152.612 | 261.700 | 176.500 | 146.000 | 116.500 | 77.000 |
| 00095 | Specific conductance, wat., unf., microsiemens per centimeter at 25 degrees Celsius | 120 | 298.000 | 42.000 | 150.667 | 258.800 | 176.750 | 145.000 | 116.000 | 72.250 |
| 00900 | Hardness, wat., unf., mg/L as calcium carbonate | 121 | 40.000 | 12.000 | 28.645 | 36.000 | 32.000 | 29.000 | 26.000 | 20.000 |
| 00915 | Calcium, wat., filt., mg/L | 121 | 10.000 | 2.500 | 6.948 | 9.000 | 7.700 | 6.900 | 6.300 | 4.910 |
| 00925 | Magnesium, wat., filt., mg/L | 121 | 3.600 | 1.300 | 2.735 | 3.390 | 3.100 | 2.800 | 2.500 | 1.900 |
| 00935 | Potassium, wat., filt., mg/L | 121 | 5.800 | 1.400 | 3.341 | 5.300 | 3.950 | 3.300 | 2.500 | 1.810 |
| 00931 | Sodium adsorption ratio, wat., number | 121 | 3.000 | 0.300 | 1.258 | 3.000 | 2.000 | 1.000 | 0.900 | 0.500 |
| 00930 | Sodium, wat., filt., mg/L | 121 | 40.000 | 2.700 | 16.426 | 34.900 | 20.500 | 14.000 | 10.500 | 5.700 |
| 00932 | Sodium, wat., percent in equivalents of major cations | 121 | 66.000 | 26.000 | 49.281 | 64.000 | 56.000 | 49.000 | 43.000 | 33.100 |
| 99430 | Carbonate, wat., unf., incremental titration, field, mg/L as calcium carbonate | 52 | 61.000 | 5.000 | 29.173 | 52.200 | 35.750 | 27.000 | 21.250 | 13.300 |
| 90410 | Acid neutralizing capacity, wat., unf., fixed endpoint (pH 4.5) titration, laboratory, mg/L as calcium carbonate | 121 | 50.000 | 11.000 | 29.463 | 43.900 | 36.000 | 29.000 | 24.000 | 16.000 |
| 39086 | Alkalinity, wat., filt., incremental titration, field, mg/L as calcium carbonate | 1 | 22.000 | -- | -- | -- | -- | -- | -- | -- |
| 00410 | Acid neutralizing capacity, wat., unf., fixed endpoint (pH 4.5) titration, field, mg/L as calcium carbonate | 59 | 62.000 | 7.000 | 29.559 | 48.000 | 36.000 | 28.000 | 22.000 | 14.000 |
| 00419 | Acid neutralizing capacity, wat., unf., incremental titration, field, mg/L as calcium carbonate | 15 | 41.000 | 13.000 | 29.733 | 41.000 | 37.000 | 31.000 | 24.000 | 13.000 |

| NWIS Param-eter code | Constituent name | Sample size | Maximum | Minimum | Mean | Percentile |
| --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  | 95th | 75th | 50th | 25th | 5th |
| 99440 | Bicarbonate, wat., unf., incremental titration, field, mg/L | 67 | 74.000 | 6.000 | 36.007 | 56.800 | 44.000 | 34.000 | 28.000 | 16.400 |
| 00453 | Bicarbonate, wat., filt., incremental titration, field, mg/L | 1 | 27.000 | -- | -- | -- | -- | -- | -- | -- |
| 99445 | Carbonate, wat., unf., incremental titration, field, mg/L | 12 | 0.000 | -- | -- | -- | -- | -- | -- | -- |
| 00940 | Chloride, wat., filt., mg/L | 116 | 32.000 | 4.800 | 13.851 | 29.150 | 17.000 | 12.000 | 9.325 | 5.685 |
| 00950 | Fluoride, wat., filt., mg/L | 115 | 0.600 | -- | 0.167* | *0.300 | *0.200 | *0.200 | *0.100 | *0.061 |
| 00955 | Silica, wat., filt., mg/L | 116 | 13.000 | 0.300 | 7.685 | 11.000 | 9.675 | 8.150 | 5.900 | 3.370 |
| 00945 | Sulfate, wat., filt., mg/L | 116 | 37.000 | 4.000 | 16.040 | 31.150 | 20.000 | 14.500 | 11.000 | 8.055 |
| 99890 | Sulfate, wat., filt., uncorrected, mg/L | 7 | -- | -- | -- | -- | -- | -- | -- | -- |
| 70300 | Residue on evaporation, dried at 180 degrees Celsius, wat., filt., mg/L | 115 | 268.000 | 32.000 | 99.461 | 150.400 | 112.000 | 94.000 | 80.000 | 59.800 |
| 00608 | Ammonia, wat., filt., mg/L as nitrogen | 115 | 0.410 | 0.002 | 0.085 | 0.215 | 0.120 | 0.070 | 0.040 | 0.013 |
| 00623 | Ammonia plus organic nitrogen, wat., filt., mg/L as nitrogen | 83 | 1.700 | 0.200 | 0.581 | 1.080 | 0.600 | 0.500 | 0.400 | 0.300 |
| 00625 | Ammonia plus organic nitrogen, wat., unf., mg/L as nitrogen | 119 | 1.700 | 0.100 | 0.728 | 1.100 | 0.900 | 0.700 | 0.600 | 0.500 |
| 00610 | Ammonia, wat., unf., mg/L as nitrogen | 44 | 0.410 | 0.020 | 0.104 | 0.257 | 0.130 | 0.090 | 0.060 | 0.022 |
| 00620 | Nitrate, wat., unf., mg/L as nitrogen | 41 | 1.390 | 0.280 | 0.588 | 1.169 | 0.685 | 0.570 | 0.450 | 0.292 |
| 00631 | Nitrite plus nitrate, wat., filt., mg/L as nitrogen | 116 | 1.200 | 0.007 | 0.544 | 0.908 | 0.697 | 0.535 | 0.442 | 0.053 |
| 00630 | Nitrite plus nitrate, wat., unf., mg/L as nitrogen | 44 | 1.400 | 0.100 | 0.592 | 1.150 | 0.700 | 0.575 | 0.500 | 0.150 |
| 00613 | Nitrite, wat., filt., mg/L as nitrogen | 91 | 0.160 | -- | 0.020* | *0.101 | *0.020 | *0.010 | *0.007 | *0.003 |
| 00615 | Nitrite, wat., unf., mg/L as nitrogen | 44 | 0.170 | 0.000 | 0.028 | 0.120 | 0.030 | 0.020 | 0.010 | 0.000 |
| 00605 | Organic nitrogen, wat., unf., mg/L | 118 | 1.600 | 0.340 | 0.646 | 1.000 | 0.745 | 0.610 | 0.507 | 0.410 |
| 00666 | Phosphorus, wat., filt., mg/L | 86 | 0.150 | 0.010 | 0.062 | 0.130 | 0.080 | 0.060 | 0.040 | 0.020 |
| 00671 | Orthophosphate, wat., filt., mg/L as phosphorus | 115 | 0.270 | -- | 0.053* | *0.130 | *0.070 | *0.040 | *0.030 | *0.008 |
| 70507 | Orthophosphate, wat., unf., mg/L as phosphorus | 44 | 0.160 | 0.020 | 0.071 | 0.142 | 0.100 | 0.070 | 0.050 | 0.020 |
| 00665 | Phosphorus, wat., unf., mg/L | 119 | 0.380 | 0.020 | 0.115 | 0.270 | 0.130 | 0.100 | 0.070 | 0.050 |
| 00680 | Organic carbon, wat., unf., mg/L | 120 | 22.000 | 0.800 | 8.700 | 14.000 | 9.475 | 8.000 | 7.300 | 5.905 |
| 01105 | Aluminum, wat., unf., recoverable, ug/L | 50 | 3400.000 | 60.000 | 645.420 | 2415.000 | 930.000 | 420.000 | 173.750 | 85.500 |
| 01002 | Arsenic, wat., unf., ug/L | 50 | 2.000 | -- | 0.720* | *1.450 | *1.000 | *0.651 | *0.496 | *0.317 |
| 01027 | Cadmium, wat., unf., ug/L | 50 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01034 | Chromium, wat., unf., recoverable, ug/L | 50 | 30.000 | -- | 1.914* | *6.700 | *2.000 | *0.813 | *0.369 | *0.109 |
| 01037 | Cobalt, wat., unf., recoverable, ug/L | 50 | 3.000 | -- | 0.913* | *2.000 | *1.000 | *0.800 | *0.552 | *0.337 |
| 01042 | Copper, wat., unf., recoverable, ug/L | 49 | 16.000 | 1.000 | 4.531 | 11.500 | 5.000 | 4.000 | 3.000 | 2.000 |
| 01045 | Iron, wat., unf., recoverable, ug/L | 50 | 4700.000 | 10.000 | 1100.540 | 3465.001 | 1525.000 | 840.000 | 485.000 | 215.950 |
| 01051 | Lead, wat., unf., recoverable, ug/L | 49 | 12.000 | -- | 1.968* | *8.500 | *2.000 | *1.000 | *0.652 | *0.275 |
| 01055 | Manganese, wat., unf., recoverable, ug/L | 50 | 680.000 | 60.000 | 180.074 | 670.000 | 190.000 | 130.000 | 100.000 | 60.000 |
| 71900 | Mercury, wat., unf., recoverable, ug/L | 49 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01062 | Molybdenum, wat., unf., recoverable, ug/L | 50 | 4.800 | -- | 1.480* | *4.000 | *2.000 | *1.000 | *0.696 | *0.332 |
| 01067 | Nickel, wat., unf., recoverable, ug/L | 49 | 8.000 | -- | 2.414* | *6.000 | *3.000 | *2.000 | *1.589 | *0.783 |
| 01147 | Selenium, wat., unf., ug/L | 50 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01077 | Silver, wat., unf., recoverable, ug/L | 48 | -- | -- | -- | -- | -- | -- | -- | -- |
| 01092 | Zinc, wat., unf., recoverable, ug/L | 50 | 210.000 | -- | 13.623* | *30.000 | *19.550 | *6.975 | *3.465 | *1.263 |
| 80154 | Suspended sediment concentration, mg/L | 106 | 290.000 | 1.000 | 29.395 | 99.650 | 30.250 | 16.000 | 10.000 | 5.000 |