Glen Carleton – Hydrologist, GS-12

Saltwater-intrusion modeling

Cape May County, N.J. ~300 mi2 area, Coastal Plain, 5 aquifers

Constructed, calibrated, interpreted shallow-system (3 aquifer) model and integrated results with results from new simulations using pre-existing deep-system (2 aquifer) model

Used SEAWAT, simulated saltwater intrusion in confined & unconfined aquifers, forecasted future intrusion rates

Evaluated GW/SW interactions, possible effects on water table and ecosystem of future pumping scenarios

Contaminated-site and fractured-rock modeling

Pohatcong valley, N.J.  ~30 mi2 area, fractured dolomite aquifer overlain by unconsolidated aquifer

Constructed, calibrated, interpreted model showing contaminant transport from a known site to unknown down-  gradient receptors, calibrated in part with age-dating results

Parameter estimation assisted calibration effort, particle tracking to show pathlines, receptors of  contamination

Simulation of solute transport (MODFLOW-GWT) to show simulated plume corresponded well with observed

Site-scale simulation of 3 tracer tests in a fractured sedimentary-rock aquifer

Constructed, calibrated transient model to multi-day, 15-well aquifer test, further calibrated using particle tracking to simulate tracer tests

Showed MODFLOW could successfully simulate relatively small-scale transient events in a fractured-rock setting

Other Coastal Plain models

Upper Maurice River Basin, N.J. ~100 mi2 area, Coastal Plain, unconfined aquifer

Assisted with model construction, including framework, stream base-flow, water-use

Camden, NJ area, ~400 mi2 area, Coastal Plain, 5 aquifers

Assisted with framework, water-use

Additional experience

Construction of GW model for combination with DAFLOW to simulate GW/SW interactions, Ramapo River, NJ

Aquifer-test analysis, stream base-flow estimation

Modeling and Coastal-Plain Study Publications

Lacombe, Carleton, Pope, and Rice, in review, Feasibility of existing and alternative potable and ecological water supply, Cape May County, NJ, 2006-2050:  USGS SIR 2007-xxxx

Carleton and Gordon, 2006, Hydrogeology of, and simulation of ground-water flow in, the Pohatcong Valley, Warren County, NJ: USGS SIR 2006-5269, 74 p.      http://pubs.usgs.gov/sir/2006/5269/

Carleton, Gordon, and Wieben, 2005, Aquifer properties, stream base flow, water use, and water levels in the Pohatcong Valley, Warren County, NJ: USGS SIR 2004-5127, 72 p.   http://pubs.er.usgs.gov/usgspubs/sir/sir20045127

Cauller, S.J. and Carleton, G.B., 2005, Hydrogeology and simulated effects of ground-water withdrawals, Kirkwood-Cohansey Aquifer System, Upper Maurice River Basin area, New Jersey:  U.S. Geological Survey Scientific Investigations Report 05-5258, 48 p.

Lacombe, P.J. and Carleton, G.B., 2002, Hydrogeologic framework, availability of water supplies, and saltwater intrusion, Cape May County, New Jersey:  U.S. Geological Survey Water-Resources Investigations Report 01-4246, 151 p.

Carleton and others, 1999, Design and analysis of tracer tests to determine effective porosity and dispersivity in fractured sedimentary rocks, Newark Basin, New Jersey: U.S. Geological Survey Water-Resources Investigations Report 98-4126A, 80 p.

Cauller, S.J., Carleton, G.B., and Storck, M.J., 1999, Hydrogeology of, water withdrawal from, and water levels and chloride concentrations in the major coastal plain aquifers of Gloucester and Salem Counties, New Jersey: U.S. Geological Survey Water-Resources Investigations Report 98-4136.

Navoy, A.S. and Carleton, G.B., 1995, Ground-water flow and future conditions in the Potomac-Raritan-Magothy aquifer system, Camden area, New Jersey: New Jersey Geological Survey Report GSR 38, 184 p.