Table 10

Brookhaven Medical Research Reactor Groundwater Investigation

Chronology of Spills or Discharges of Radioactive Liquids

to the SU-2 Sump and Haul-Away Tank

Releases to SU-2 Sump

| Date | Occurrence |
| --- | --- |
| 6/7/65 | Small leak of primary coolant to SU-2. Volume not given. |
| 9/14/65 | Drained about 135 gallons of primary coolant to SU-2. |
| 5/2/66 | Drained 6 gallons of primary coolant (H-3, 3 mCi) to SU-2. |
| 9/8/66 | Drained 6 gallons of primary coolant to SU-2. |
| 4/3/67 | Drained 50 gallons of primary coolant to SU-2. |
| 4/12/67 | Drained 17 gallons of primary coolant to SU-2. |
| 4/13/97 | Small spill of primary coolant to SU-2. Volume not given. |
| 8/26/67 | Spilled 60 gallons of primary coolant to SU-2. |
| 2/3/69 | Drained 350 gallons of primary coolant to SU-2. |
| 7/28/69 | Drained 6 gallons of primary coolant to SU-2. |
| 5/11/70 | Drained 70 gallons of primary coolant to SU-2. |
| 7/29/70 | Drained 6 gallons of primary coolant to SU-2. |
| 8/4/72 | Drained 6 gallons of primary coolant to SU-2. |
| 6/6/74 | Drained 6 gallons of primary coolant to SU-2. |
| 10/29/74 | Drained 6 gallons of primary coolant to SU-2. |
| 1/28/87 | Drained 70 gallons of primary coolant to SU-2. |

Spills Associated with Haul-Away Tank

| Date | Occurrence |
| --- | --- |
| 9/26/62 | Replaced haul-away tank hose (hoses leaked). |
| 9/14/71 | Haul-away tank overflowed. The water runoff read about 300 cpm. The tank and surrounding area were flushed with water. The runoff then contained no discernable activity. |
| 12/8/77 | Weepage from haul-away tank to asphalt. |

Note: Information provided by H. Hauptman (BNL-RD).  Based upon review of available S&EP and RD record logs.