03E01/07/08

S106-03E.doc

Use on all projects.

Section 106. - ACCEPTANCE OF WORK

106.01  Conformity with Contract Requirements.  Delete the text and substitute the following:

Follow the requirements of FAR Clause 52.246-12 Inspection of Construction.

References to standard test methods of AASHTO, ASTM, GSA, and other recognized standard authorities refer to the methods in effect on the date of solicitation for bids.

Perform all work to the lines, grades, cross-sections, dimensions, and processes or material requirements shown on the plans or specified in the contract.

Incorporate manufactured materials into the work according to the manufacturer’s recommendations or to these specifications, whichever is more strict.

Plan dimensions and contract specification values are the values to be strived for and complied with as the design values from which any deviations are allowed.  Perform work and provide material that is uniform in character and reasonably close to the prescribed value or within the specified tolerance range.  The purpose of a tolerance range is to accommodate occasional minor variations from the median zone that are unavoidable for practical reasons.

When standard manufactured items are specified (such as fence, wire, plates, rolled shapes, pipe conduits, etc., that are identified by gauge, unit mass, section dimensions, etc.), the identification will be considered to be nominal masses or dimensions.  Unless specific contract tolerances are noted, established manufacturing tolerances will be accepted.

The Government may inspect, sample, or test all work at any time before final acceptance of the project.  When the Government tests work, copies of test reports are furnished to the Contractor upon request.  Government tests may or may not be performed at the work site.  If Contractor testing and inspection is verified by the Government, the Contractor’s results may be used by the Government to evaluate work for acceptance.  Do not rely on the availability of Government test results for process control.

Acceptable work conforming to the contract will be paid for at the contract unit bid price.  Four methods of determining conformity and accepting work are described in Subsections 106.02 to 106.05 inclusive.  The primary method of acceptance is specified in each Section of work.  However, work may be rejected at any time it is found by any of the methods not to comply with the contract.

Remove and replace work that does not conform to the contract, or to prevailing industry standards where no specific contract requirements are noted, at no cost to the Government.

(a) Disputing Government test results.  If the accuracy of Government test results is disputed, promptly inform the CO.  If the dispute is unresolved after reasonable steps are taken to resolve the dispute, further evaluation may be obtained by written request.  Include a narrative describing the dispute and a proposed resolution protocol that addresses the following:

(1) Sampling method

(2) Number of samples

(3) Sample transport

(4) Test procedures

(5) Testing laboratories

(6) Reporting

(7) Estimated time and costs

(8) Validation process

If the evaluation requires additional sampling or testing be performed, mutually agree with the Government on witnessing procedures and on sampling and testing by a third party laboratory.  Use a third party laboratory accredited by the AASHTO accreditation program.  Provide proof of the laboratory’s accreditation for the test procedures to be used.  Do not use the same laboratory that produced the disputed Government test results or that produced the test results used as a basis for the dispute.

The CO will review the proposed resolution protocol and may modify it before final approval and execution.

The Government will use the approved resolution protocol test results to determine the validity of the disputed testing.  If the Government test results are validated, the Contractor will be responsible for all costs associated with developing and performing the resolution protocol.  If the Government test results are not validated, the Government will be responsible for all costs associated with developing and performing the resolution protocol.  If the validity of the Government test results cannot be determined, the Contractor and Government will equally share all costs associated with developing and carrying out the resolution protocol.

(b) Alternatives to removing and replacing non-conforming work.  As an alternative to removal and replacement, the Contractor may submit a written request to:

(1) Have the work accepted at a reduced price; or

(2) Be given permission to perform corrective measures to bring the work into conformity.

The request must contain supporting rationale and documentation.  Include references or data justifying the proposal based on an evaluation of test results, effect on service life, value of material or work, quality, aesthetics, and other tangible engineering basis.  The CO will determine disposition of the nonconforming work.

Where sample/testing procedures make reference to AASHTO, ASTM, or other standards (designated as FLH T), the procedure as modified in the Materials Manual shall govern.  Where the specifications make reference to AASHTO Test T11, “Procedure B - Washing Using a Wetting Agent” shall be the procedure followed.

Where the specifications make reference to AASHTO Test T310, “Direct Transmission Method of In-Place Nuclear Density and Moisture Content” shall be the procedure followed.

Reference to the Materials Manual means the Federal Lands Highway “Field Materials Manual, U.S. Department of Transportation, Federal Highway Administration,” Publication No. FHWA-FL-91-002, dated March 1991, revised March 1994, and all amendments and supplements thereto.  Copies are available from the Materials Engineer, Federal Highway Administration, Central Federal Lands Highway Division, Materials Branch, P.O. Box 25246, Denver, Colorado 80225-0246, Telephone: (720) 963-3537.

106.03  Certification.  Add the following after the second paragraph:

See Table 106-3 for schedule for full or partial acceptance by material certification.  Submit certification and sample of material for testing as required.

Use on all projects with statistical pay items.

106.05  Statistical Evaluation of Work and Determination of Pay Factor (Value of Work).

(b) Acceptance.  Delete the last sentence of the second paragraph and substitute the following:

If a lot is concluded or terminated with fewer than three samples, the samples will be combined with those of an adjacent lot.  In the event there is no adjacent lot, the material will be accepted according to Subsection 106.04.

Table 106-2  Pay Factor.

The Pay Factor 1.03, category I row:  Delete the value 84 in the n=9 column and substitute the value 94.

The Pay Factor 0.75, category II row:  Delete the value 35 in the n=3 column and substitute the value 25.

Add Table 106-3 to all projects.

Table 106-3 Schedule For Full or Partial Acceptance by Materials Certification.  Add Table 106-3 following Table 106-2.

Table 106-3

Schedule For Full or Partial Acceptance by Materials Certification

| Section | Description | Material | Material Property Or Specification | Frequency |
| --- | --- | --- | --- | --- |
|  |  |  |  | Certification | Sample |
| 306 | Dust Palliative | Magnesium Chloride, Emulsified Asphalt, Lignin Sulfonate, Calcium Chloride | As specified | 1 per shipment | First shipment |
| 308 | Minor Crushed Aggregate | Crushed Aggregate | Source, Quality and Gradation | 1 per source | 1 per source |
| 404 and 417 | Minor Hot Asphalt Concrete, Minor Cold Asphalt Mix | Aggregate Asphalt Mix | Source quality, Gradation, Stability, and Grade | 1 per mix | 1 per source |
| 634 and 635 | Permanent Pavement Markings, Temporary Traffic Control | 634.02 as applicable, 635 as applicable | As specified | 1 per source | ----- |
| 701 | Hydraulic Cement | Portland Cement, Blended Hydraulic Cement and Masonry Cement | AASHTO M 85, M 240, and ASTM C 91 | 1 per shipment | 1 per 100 tons |
| 702.01 | Asphalt Material | Asphalt Cement | AASHTO M 20, M 226, MP 1 or as applicable | 1 per shipment | 1 per shipment |
| 702.02 | Asphalt Material | Cut-back Asphalt | AASHTO M 81 or M 82 as applicable | 1 per shipment | 1 per shipment |
| 702.03 | Asphalt Material | Emulsified Asphalt | AASHTO M 140 or M 208 as applicable | 1 per shipment | 1 per shipment |
| 702.05 | Asphalt Material | Asphalt Materials used for Damproofing and Waterproofing Concrete Surfaces | As specified for each type of asphalt material | 1 per shipment | ----- |
| 702.06 | Recycling Agent | As specified | As applicable | 1 per shipment | 1 per shipment |
| 702.08 | Antistrip | As specified | As applicable | 1 per shipment | ----- |
| 706 | Concrete and Plastic Pipe | As specified | As applicable | 1 per shipment | ----- |
| 707 | Metal Pipe | Metal Pipe as specified | As applicable | 1 per shipment | ----- |
| 708 | Paint | As specified | As applicable | 1 per batch\lot | 1 sample for quantities > (25 gallons) |
| 709 | Reinforcing Steel and Wire Rope | As specified | As applicable | 1 per shipment | For 709.01 & 709.03 submit 3, 1-yard bars of each size and grade of bar furnished. 709.02 submit 1 6-foot length for each size furnished |
| 710 | Fence and Guardrail | As specified | As applicable | 1 per shipment | ----- |
| 711 | Concrete Curing Material and Admixtures | As specified | As applicable | 1 per material source per material type | ----- |
| 712 | Joint Material (all) | As specified | As applicable | 1 per shipment | ----- |
| 713 | Roadside Improvement Materials (all) | As specified | As applicable | 1 per shipment | ----- |
| 714 | Geotextile and Geocomposite Drain | As specified | As applicable | 1 per shipment | 1 per project per type |
| 715 | Piling | As specified | As applicable | 1 per shipment | ----- |
| 716 | Material for Timber Structures | Timber and Hardware | As applicable | 1 per shipment | ----- |
| 717 | Structural Metal | As specified | As applicable | 1 per shipment | 717.01(e) minimum 6 per shipment for each size used. 717.10 1 per project |
| 718 | Traffic Signing and Marking (all) | As specified | As applicable | 1 per shipment | ----- |
| 720 | Structural Wall and Stabilized Materials (all) | As specified | As applicable | 1 per shipment per material type | ----- |
| 721 | Electrical and Illumination Material (all) | As specified | As applicable | 1 per shipment per material type | ----- |
| 722 | Anchor Material | As specified | As applicable | 1 per shipment per material type | ----- |
| 725 | Miscellaneous materials | As specified | As applicable | 1 per shipment per material type | ----- |