A0 Photo Injector RF

Two High Power 1.3 Ghz RF Systems in Operation

# 5 Mwatt System

5 Mwatt Klystron Thales TH2104-C

2 mSec pulse Max but typical operation is 600uSec

@120KV with ~30usec rf pulse

HV supply

Charging supply

PFN + Bouncer

HV Pulse transformer

Isolator

Directional Couplers

High Power Waveguide Switch

TWT Amplifier

Vector Modulator

Low Level controls

Hardware for interlocks and protection

Hardware for low level rf feedback & feedforward control

Utilties

LCW

AC Power

Equipment Racks

# 200Kwatt System

300Kwatt Valvo-Philips Klystron  YK-1240

2 Sec pulse Max but typical operation is 2mSec @ 60 Kvolts

HV supply

65 Kvolt charging supply + Capacitor Bank

Series tube modulator (Tetrode).

Isolator

Directional Couplers

TWT Amplifier

Vector Modulator

Low Level controls

Hardware for interlocks, safety system, and equipment protection

Hardware for low level rf,  feedback & feedforward control

Utilties

LCW

AC Power

Equipment Racks

Presently building a second 200Kwatt 1.3Ghz system for a new high gradient superconducing cavity at A0.

Have 4 YK-1240 Klystrons but only two solenoids and oil tanks.

Have 2 TH 2104-C Klystrons but only one solenoid and pulse transformer.

Getting 5 TH2095A Klystrons from UCLA, but no solenoids, etc.

Have original Boeing Modulator for TH 2104-C, but it is not operational.

## New 1.3 Ghz test stand

What rf power level is needed?

Location of test stand.  Cave, Cryo stuff

Space requirements

Utility requirements

Low level rf stuff

Oscillator

Vector Modulator

Controls

Data acquisition system with post processing capability.