# CRITICAL AREA PLANTING

## PRACTICE INTRODUCTION

USDA, Natural Resources Conservation Service―Practice Code 342

### CRITICAL AREA PLANTING

Critical area planting is planting vegetation on critically eroding areas that require extraordinary treatment.

### PRACTICE INFORMATION

This practice is used on highly erodible areas that cannot be stabilized by ordinary planting techniques and, if left untreated, may cause severe erosion or sediment damage. Examples of critical areas include the following:

- Dams, dikes, levees, and other construction sites with very steep slopes

- Mine spoil and surface-mined land with poor quality soil and possibly chemical problems

- Agriculture land with severe gullies requiring specialized planting techniques and management

Erosion control is the primary consideration for plant material selection. However, a broad choice of grass, trees, shrubs, and vines are usually available and adapted for most sites. Wildlife and beautification are additional considerations that influence planning decisions on a site needing this practice.

The following decisions must be made when planning this practice:

- Function or use of the site following establishment

- Species of plants to establish

- Methods and rates of planting

- Fertilizer, lime, and soil amendments necessary for establishment and growth of the plants

- Mulching requirements

- Planting site preparation

- Irrigation requirement

- Site management following establishment of the vegetation

### COMMON ASSOCIATED PRACTICES

Critical Area Planting is commonly used in a Conservation Management System on a variety of land uses with practices such as Dam (402), Dike (356), and erosion control practices.

For more information, refer to the practice standard in the NRCS Field Office Technical Guide and associated specifications and design criteria.

# Text boxes

(+) increase; (-) decrease

Pathway

C.  Cumulative effect

I.  Indirect effect

D.  Direct effect

#.  Created by practice

LEGEND

Note:  Effects are qualified with a plus (+) or minus (-). These symbols indicate only an increase (+) or a decrease (-) in the effect upon the resource, not whether the effect is beneficial or adverse.

Start

I.4 (+) Air quality of the airshed

D.4 (+) Air quality

(-) Particulate materials

(+) Visibility

(-) Green house gas

D.3 (+) Restore vegetation on gullies and blow out areas

D.2 (+) Protect banks and shorelines of ponds and reservoirs; critically eroding areas

D.1 (+) Restore riparian areas

C.2 (+) Health of humans, domestic, and wild animals

I.3 (-) Airborne particles

C.1 (+) Aquatic health for humans, domestic, and wild animals

I.2 (-) Sediment in surface waters

I.1 (-) Water/wind erosion

1. Establish vegetation on disturbed areas

Initial setting: Any area requiring treatment for erosion that can be controlled by vegetative plantings

Critical Area Planting

5/2002

Critical Area Planting (342)