Table showing current parallel usage of PREPBUFR data in GBL-GSI – 12/23/2008

- /nwprod/exec/prepobs_prepdata

- /nwprod/parm/prepobs_prepdata.[gfs][gdas].parm

- /nwpara/fix/prepobs_errtable.global

- /nwpara/fix/global_convinfo.txt

- /nwpara/fix/global_satinfo.txt

- /nwpara/exec/global_gsi

GREEN – this type is USED by GBL-GSI

BLUE – this type is MONITORED by GBL-GSI

RED – this type is neither monitored nor used by GBL-GSI

GRAY – this type is never available in GBL (GDAS/GFS) PREPBUFR file

* - aircraft TOB is always sensible; previous and current ops GBL-GSI has a generalized test so that ANY obs type whose temperature has a “VIRTMP” event is assumed to have a TOB that is virtual and ANY obs type without a “VIRTMP” event in its temperature is assumed to have a TOB that is sensible and must be converted to virtual.  Thus, any aircraft type (130, 131, 133, 134, 135) TOB is always now identified as sensible regardless of its QQM and will be converted to virtual by the GBL-GSI.

** - IN GBLEVENTS, surface QQM is set to 9 if ps obs error is missing (regardless if q obs error is missing or non-missing), thus it is monitored by GBL-GSI regardless of whether or not convinfo is set to use or monitor

*** - IN GBLEVENTS, surface TQM is first set to 9 if ps obs error is missing (regardless if t obs error is missing or non-missing), and it is then reset to 9 when virtual t is calculated because QQM is set to 9 (see ** above), thus it is monitored by GBL-GSI regardless of whether or not convinfo is set to use or monitor

**** - OIQCBUFR is multi-variate and will use all obs with QM < 4 in its decision-making process.  Thus, any obs which are set to be monitored by the convinfo file but are not given a QM > 3 in the PREPBUFR file will incorrectly end up influencing OIQCBUFR.  For this reason, the obs error must remain missing for all obs set to be monitored by the convinfo file so that their QM is 9.  This will be the case until GBLEVENTS is modified to read in the convinfo file and flag all monitored and not-used obs (or until OIQCBUFR is removed from the GBL processing).

$ - SSM/I rain rate is assimilated (used) by GBL-GSI directly from the SPSSMI dump file (based on the settings in the global_pcpinfo.txt file.

% - Switched off (to not process) in PREPDATA parm cards (this supersedes any switches to otherwise flag with QM 15)

Italics – change vs. current operations

| Description | PREPBUFR report type and obs type | If YES, flagged with q.m. 15 by PREPDATA parm card switches | If YES, flagged with q.m. 9 due to obs error missing in PREPBUFR obs error file-**** | GSI convinfo | GSI satinfo (MONITOR or USE based on channel, not split up by channel here) |
| --- | --- | --- | --- | --- | --- |
| Synthetic t.c. storm center | 111 q | n/a | YES |  |  |
|  | 111 ps | n/a | YES |  |  |
| RAOB | 120 t | no | no | USE |  |
|  | 120 q | no | no | USE |  |
|  | 120 ps | no | no | USE |  |
|  | 120 sst | no | n/a | MONITOR |  |
| CLASS | 122 t | no-% | YES |  |  |
|  | 122 q | no-% | YES |  |  |
|  | 122 ps | no-% | YES |  |  |
| RASS (NPN and MAP) | 126 t | no | YES | MONITOR |  |
| AIREP/ PIREP | 130 t | no | no | USE |  |
|  | 130 q | YES | YES-* | MONITOR |  |
| AMDAR | 131 t | no | no | USE |  |
|  | 131 q | YES | YES-* | MONITOR |  |
| RECCO | 132 t | no | no | USE |  |
|  | 132 q | no | no | USE |  |
| DROP | 132 t above sfc | no | no | USE |  |
|  | 132 t at sfc | YES | no | USE |  |
|  | 132 NOAA (Gulf Stream/ P-3) q above sfc | no | no | USE |  |
|  | 132 USAF q above sfc | no | no | USE |  |
|  | 132 non-NOAA/ non-USAF q above sfc | YES | no | USE |  |
|  | 132 q at sfc | YES | no | USE |  |
|  | 132 ps | YES | no | MONITOR |  |
| MDCRS-ACARS | 133 t | no | no | USE |  |
|  | 133 q | no | YES-* | MONITOR |  |

| TAMDAR (Mesaba, PenAir, Chautauqua) | 134 t | no | YES | MONITOR |  |
| --- | --- | --- | --- | --- | --- |
|  | 134 q | no | YES-* | MONITOR |  |
| Canadian AMDAR | 135 t | no | YES | MONITOR |  |
|  | 135 q | YES | YES-* | MONITOR |  |
| SSM/I Rain rate | 150-$ | no | YES |  |  |
| SSM/I PW | 152 pw | no | YES | MONITOR |  |
| GPS-IPW | 153 pw | no | YES | MONITOR |  |
| GOES 1x1 PW, land, clear | 156 pw | no (G-11)-% no (G-12)-% | YES | MONITOR |  |
| GOES 1x1 PW, land, cloudy | 157 pw | no (G-11) -% no (G-12)-% | YES | MONITOR |  |
| GOES 1x1 PW, ocean, clear | 158 pw | no (G-11)-% no (G-12)-% | YES | MONITOR |  |
| GOES 1x1 PW, ocean, cloudy | 159 pw | no (G-11)-% no (G-12)-% | YES | MONITOR |  |
| GOES 1x1 radiances, land, clear | 164 bt | no-% | n/a | n/a | MONITOR all (tossed by GSI code) |
| GOES 1x1 radiances, land, cloudy | 165 bt | no-% | n/a | n/a | MONITOR all (tossed by GSI code) |
| GOES 1x1 radiances, ocean, clear | 174 bt | no-% | n/a | n/a | MONITOR all |
| GOES 1x1 radiances, ocean, cloudy | 175 bt | no-% | n/a | n/a | MONITOR all |
| Sfc marine w/ reported Pstn | 180 t | no | no | USE |  |
|  | 180 q | no | no | USE |  |
|  | 180 ps | no | no | USE |  |
|  | 180 sst | no | n/a | MONITOR |  |
| SYNOP or METAR w/ reported Pstn | 181 t | no | YES | MONITOR |  |
|  | 181 q | no | YES | MONITOR |  |
|  | 181 ps | no | no | USE |  |
|  | 181 sst | no | n/a | MONITOR |  |
| Splash-level DROP | 182 t | no | no | USE |  |
|  | 182 q | no | no | USE |  |
|  | 182 ps | no | no | USE |  |
| SYNOP, METAR or sfc marine w/ missing Pstn; METAR also w/ missing altimeter | 183 t | no | YES*** | MONITOR |  |
|  | 183 q | no | YES** | MONITOR |  |
|  | 183 ps | no | YES | MONITOR |  |
|  | 183 sst | no | n/a | MONITOR |  |
| METAR w/ missing Pstn, reported altimeter | 187 t | no | YES | MONITOR |  |
|  | 187 q | no | YES | MONITOR |  |
|  | 187 ps | no | no | USE |  |
|  | 187 sst | no | n/a | MONITOR |  |
| Sfc mesonet | 188 t | no-% | YES |  |  |
|  | 188 q | no-% | YES |  |  |
|  | 188 ps | no-% | YES |  |  |
| Austrlian PAOB | 191 ps | no-% | YES |  |  |
| Synthetic t.c. wind | 210 uv | no | no | USE |  |
| RAOB | 220 uv | no | no | USE |  |
| PIBAL | 221 uv | no | no | USE |  |
| CLASS | 222 uv | no-% | YES |  |  |
| NOAA profiler | 223 uv | no | no | USE |  |
| VAD wind | 224 uv | no | no | USE |  |
| MAP profiler | 227 uv | no-% | YES |  |  |
| JMA profiler | 228 uv | no | YES | MONITOR |  |
| Profiler decoded from PIBAL | 229 uv | no | no | USE |  |
| AIREP/ PIREP | 230 uv | no | no | USE |  |
| AMDAR | 231 uv | no | no | USE |  |
| RECCO/ DROP | 232 uv | no | no | USE |  |
| MDCRS-ACARS | 233 uv | no | no | USE |  |
| TAMDAR (Mesaba, PenAir, Chautauqua) | 234 uv | no | YES | MONITOR |  |
| Canadian AMDAR | 235 uv | no | YES | MONITOR |  |
| India IR satwind | 241 uv | no | YES | MONITOR |  |
| India visible satwind | 241 uv | no | YES | MONITOR |  |
| JMA IR/ visible satwind below 850 mb | 242 uv | no | no | USE |  |
| EUMETSAT IR satwind below 850 mb | 243 MET-7 uv | no | no | USE |  |
|  | 243 MET-9 uv | no | no | MONITOR |  |
| EUMETSAT visible satwind below 850 mb | 243 MET-7 uv | no | no | USE |  |
|  | 243 MET-9 uv | no | no | MONITOR |  |
| GOES IR satwind | 245 uv | no | no | USE |  |
| GOES imager WV, cloud-top satwind | 246 uv | no | no | USE |  |
| GOES imager WV, deep-layer satwind | 247 uv | no-% | YES | MONITOR |  |
| GOES sounder WV, cloud-top satwind | 248 uv | no-% | YES | MONITOR |  |
| GOES sounder WV, deep-layer satwind | 249 uv | no-% | YES | MONITOR |  |
| JMA imager WV satwind | 250 uv | no | YES | MONITOR |  |
| GOES visible satwind | 251 uv | no | YES | MONITOR |  |
| JMA IR/ visible satwind above 850 mb | 252 uv | no | no | USE |  |
| EUMETSAT IR satwind above 850 mb | 253 MET-7 uv | no | no | USE |  |
|  | 253 MET-9 uv | no | no | MONITOR |  |
| EUMETSAT visible satwind above 850 mb | 253 MET-7 uv | no | no | USE |  |
|  | 253 MET-9 uv | no | no | MONITOR |  |
| EUMETSAT imager WV satwind | 254 MET-7 uv | no | YES | MONITOR |  |
|  | 254 MET-9 uv | no | YES | MONITOR |  |
| GOES picture triplet satwind | 255 uv | no-% | no |  |  |
| India imager WV satwind | 256 uv | no | YES | MONITOR |  |
| MODIS IR satwind | 257 uv | no | no | USE |  |
| MODIS imager WV, cloud-top satwind at and below 600 mb | 258 uv | no | YES | USE |  |
| MODIS imager WV, cloud-top satwind above 600 mb | 258 uv | no | no | USE |  |
| MODIS imager WV, deep-layer satwind at and below 600 mb | 259 uv | no | YES | USE |  |
| MODIS imager WV, deep-layer satwind above 600 mb | 259 uv | no | no | USE |  |
| Sfc marine w/ reported Pstn | 280 uv | no | no | USE |  |
| SYNOP or METAR w/ reported Pstn | 281 uv | no | YES | MONITOR |  |
| ATLAS buoy (missing Pstn) | 282 uv | no | no | USE |  |
| SSM/I wind speed | 283 spd | no | no | USE |  |
| SYNOP, METAR or sfc marine w/ missing Pstn; METAR also w/ missing altimeter | 284 uv | no | YES | MONITOR |  |
| QuikScat scatterometer | 285 uv | no | no | USE |  |
| ERS scatterometer | 286 uv | no-% | YES | MONITOR |  |
| METAR w/ missing Pstn, reported altimeter | 287 uv | no | YES | MONITOR |  |
| Sfc mesonet | 288 uv | no-% | YES |  |  |
| WindSat scatterometer | 289 uv | no | no | USE |  |
| ASCAT scatterometer | 290 uv | no | YES | MONITOR |  |