U. S. Department                                                            Publication No. FHWA-NHI-04-160

of Transportation                                                             April 2004

Federal Highway

#### Administration

NHI Course No. XXXXXX

Fundamentals of Road Weather Management

Appendix B: Participant Workbook

##### Table of Contents

I. Introduction	2

II. Executive Summary	2

III. Course Goal and Outcomes	3

Course Goal	3

Course Outcomes	3

IV. Course Agenda	4

V. Course Material	5

Exercise – Handout 5-1	17

Acronym List	18

Glossary	19

# I. Introduction

The Fundamentals of Road Weather Management is a one-day course aimed at helping those involved in highway maintenance and operations develop techniques and strategies for tackling road weather problems. This course provides a basic knowledge of meteorology and addresses the technological resources available to support highway personnel in making effective road weather decisions.

# II. Executive Summary

Over the past 20 years, improvements have been made in the areas of road sensors, anti-icing and information dissemination via tools such as Road Weather Information Systems (RWIS).  However, concerns still remain regarding uniform standards and data sharing.

The Fundamentals of Road Weather Management is a one-day course aimed at transportation professionals involved in highway maintenance, highway safety, emergency management, and traffic management. The course provides   techniques and strategies for tackling road weather problems, specifically designed for those individuals directly involved in the implementation of road weather solutions and allocation of resources.  The course focuses heavily on resources and solutions, and how those solutions can reduce the impact of adverse weather on road users and highway personnel.

The following key points are covered in this course:

- Impact of weather on highway operations.

  - Discussion on the effects of weather on the traveling public and the impact of road weather on highway operation.

- Fundamentals of meteorology, including how it pertains to Road Weather Information Systems.

  - Includes discussion on the definitions of basic meteorology terms and the importance of climatology, tailored forecast and weather observations to roadway management.

- Technical and institutional resources available for implementing Road Weather Information Systems.

  - Key technological resources are identified for making road weather decisions, including challenges faced in implementing road weather technology.

- Range of effective and open solutions to the various types of weather conditions for various management practices.

  - Includes discussion on the importance of proactive planning and possible solutions to road weather challenges.

  - Various solutions to road weather problems are analyzed and applied to local environment.

In summary, the purpose of this course is not to make participants experts, but to provide them with the basic tools and resources needed for effective road weather decisions, and direction on where to go for more information.

# III. Course Goal and Outcomes

## Course Goal

The purpose of this course is to introduce the resources and basic information needed to effectively manage road weather issues. While some of this information may not be new to participants, this course will focus on using the presented KSA's (knowledge, skills and abilities) to effectively solve road weather issues. The goals of this course are to:

- Identify and discuss road weather problems.

- Discuss the resources available to support effective road weather decision-making.

- Enable participants to apply their knowledge, skills, and abilities to road weather management.

## Course Outcomes

At the end of this course, participants will be able to:

1. Examine the impact of weather on highway operations.

2. Discuss the fundamentals of meteorology, including how it pertains to Road Weather Information Systems (RWIS).

3. Identify the technical and institutional resources for implementing Road Weather Information Systems (RWIS).

4. Examine the range of effective and open solutions to the various types of weather conditions for various management practices.

# IV. Course Agenda

Length

Time                       	Lesson Title                     	(minutes)

8:30-9:00   	Welcome                                              	30

9:00-10:00   	Lesson 1: The Road Weather Problem                       	60

10:00-10:10 	Break	10

10:10- 11:10 	Lesson 2: Meteorology for Non-meteorologists Part I   	60

11:10-11:20 	Break	10

11:20- 12:00  	Lesson 3: Meteorology for Non-meteorologists Part II 	40

12:00-1:00  	Lunch             	60

1:00-2:00   	Lesson 4: Technology: Resources & Implementation 	60

2:00-2:10   	Break  	10

2:10 - 3:00   	Lesson 5: Solutions to RWP - Case Studies Part I        	50

3:00-3:10   	Break                                                 	10

3:10-4:00   	Lesson 6: Solutions to RWP - Case Studies Part II 		50

4:00-4:30   	Wrap-up                                           	30

# V. Course Material

| Lesson 4: Technology: Resources and Implementation |
| --- |
|  | __________________________ __________________________ __________________________ __________________________ __________________________ __________________________ __________________________ __________________________ __________________________ __________________________ __________________________ |
|  | __________________________ __________________________ __________________________ __________________________ __________________________ __________________________ __________________________ __________________________ __________________________ __________________________ __________________________ |
|  | __________________________ __________________________ __________________________ __________________________ __________________________ __________________________ __________________________ __________________________ __________________________ __________________________ __________________________ |
| Why use technology: Make your operations more efficient and effective To provide a higher level of service Keep roads safer and keep traffic moving |
|  | __________________________ __________________________ __________________________ __________________________ __________________________ __________________________ __________________________ __________________________ __________________________ __________________________ __________________________ |
|  | __________________________ __________________________ __________________________ __________________________ __________________________ __________________________ __________________________ __________________________ __________________________ __________________________ __________________________ |
|  | __________________________ __________________________ __________________________ __________________________ __________________________ __________________________ __________________________ __________________________ __________________________ __________________________ __________________________ |
|  | __________________________ __________________________ __________________________ __________________________ __________________________ __________________________ __________________________ __________________________ __________________________ __________________________ __________________________ |
| For more information on Environmental Sensor Stations please refer to Chapter 4: “Technology Resources” in the Fundamentals of Road Weather Management reference manual. |
|  | __________________________ __________________________ __________________________ __________________________ __________________________ __________________________ __________________________ __________________________ __________________________ __________________________ __________________________ |
| RPU: Remote Processing Unit CPU: Control Processing Unit For more information on RWIS please refer to Chapter 4: “Technology Resources” in the Fundamentals of Road Weather Management reference manual. |
|  | __________________________ __________________________ __________________________ __________________________ __________________________ __________________________ __________________________ __________________________ __________________________ __________________________ __________________________ |
| Weather forecasts are either provided by the ESS vendor or if a VAMS has been contracted, by the VAMS using sensor data from an ESS. |
|  | __________________________ __________________________ __________________________ __________________________ __________________________ __________________________ __________________________ __________________________ __________________________ __________________________ __________________________ |
|  | __________________________ __________________________ __________________________ __________________________ __________________________ __________________________ __________________________ __________________________ __________________________ __________________________ __________________________ |
| For more information on the benefits of using RWIS please refer to Chapter 4: “Technology Resources” in the Fundamentals of Road Weather Management reference manual. |
|  | __________________________ __________________________ __________________________ __________________________ __________________________ __________________________ __________________________ __________________________ __________________________ __________________________ __________________________ |
| For more information on data sharing issues please refer to Chapter 4: “Technology Resources” in the Fundamentals of Road Weather Management reference manual. |
|  | __________________________ __________________________ __________________________ __________________________ __________________________ __________________________ __________________________ __________________________ __________________________ __________________________ __________________________ |
|  | __________________________ __________________________ __________________________ __________________________ __________________________ __________________________ __________________________ __________________________ __________________________ __________________________ __________________________ |

DECISION SUPPORT SYSTEM

|  | __________________________ __________________________ __________________________ __________________________ __________________________ __________________________ __________________________ __________________________ __________________________ __________________________ __________________________ |
| --- | --- |
|  | __________________________ __________________________ __________________________ __________________________ __________________________ __________________________ __________________________ __________________________ __________________________ __________________________ __________________________ |

# Exercise – Handout 5-1

Instructions:  Match the technological resource or device on the right – with its RWIS component on the left.  Write in the number of the resource or device in the space next to its related component.

Component of RWIS		Resource/Device

ESS				_____		1.  RPU

_____		2.  Value added Meteorological Services

(VAMS)

Processing Systems		_____		3.  Kiosks

_____		4.  Pavement icing

Forecasts and Models		_____		5.  Road sensors

_____		6.  Variable message boards

Dissemination			_____		7.  Sensor stations

_____		8.  CPU

# Acronym List

CPU						Central Processing Unit

CVU						Commercial Vehicle Operators

DSS						Decision Support System

ESS						Environmental Sensor Stations

Hazmat					Hazardous Materials

MDSS						Maintenance Decision Support System

NOAA						National Oceanic and Atmospheric

Administration

NTCIP					National Transportation Communications

for ITS Protocol

NWS						National Weather Service

PMA						Primary Market Area

RPU						Remote Processing Unit

RWIS						Road Weather Information Systems

TMC						Traffic Management Center

VAMS						Value-Added Meteorological Services

# Glossary

| Decision Support System (DSS) | A system that integrates weather, road condition, and resource information to facilitate road weather information decision making. |
| --- | --- |
| Environmental Sensor Station (ESS) | A suite of atmospheric and roadway sensors, plus a remote processing unit (RPU). |
| ENTERPRISE | A pool-fund organization, consisting of seven U.S. state Departments of Transportation, Canada, and the Netherlands, that has developed a set of standard test procedures for implementing road weather technology. |
| Humidity | The amount of moisture (e.g., water vapor) in the atmosphere. |
| Maintenance Decision Support System (MDSS) | An FHWA initiative to develop a decision support system (DSS) for winter road maintenance. |
| Mesonet | A collection of weather observing stations typically combining data from multiple agencies and applications. |
| National Transportation Communications for ITS Protocol (NTCIP) | The generic name of standards that define how roadside services talk to a central road weather information system. |
| Road Weather Information Systems (RWIS) | The main technological resource available for managing road weather issues. Refers to a coordinated system of data collection, analysis, dissemination, and display of road weather information. |
| Value added Meteorological Services (VAMS) | A for-hire company which develops specific weather planning programs for businesses and industries. |