Mid-Coast LRT Extension

San Diego, California

(November 2004)

The San Diego Association of Governments (SANDAG) is proposing to construct and operate a 3.4-mile extension of the Blue Line on its existing light rail transit (LRT) system from the Old Town Transit Center (OTTC) to Balboa Avenue in the Claremont/Mission Bay area of northwest San Diego.  The Mid-Coast LRT Extension project would be built primarily within an existing rail right-of-way currently accommodating commuter and intercity rail.  Three new stations are proposed, each with small park-and-ride and bus transfer facilities.  The project scope includes the purchase of seven new LRT vehicles.  The project would operate at 7.5-minute peak period frequencies.

The Mid-Coast LRT alignment parallels Interstate 5 (I-5), the only continuous major north-south spine between the northwest San Diego area and downtown.  Topographic constraints in the corridor (canyons and mesas to the west, Mission Bay to the east) have limited options for transportation improvements, resulting in increased pressure on I-5 to serve both long- and short-distance trips.  This, in turn, has resulted in congested conditions during and beyond peak travel hours, with more congestion projected for the future.  In addition, I-5 is largely disconnected from the OTTC, which serves as the regional transit access point for both the Blue and Orange LRT lines, as well as commuter rail and local bus.  Consequently, bus and vehicular access from the north must travel on circuitous local streets to reach the OTTC.  By extending the Blue Line north to Balboa Avenue, the Mid-Coast LRT Extension project is intended to improve access to the regional rail system, while providing a fixed guideway transportation alternative within the congested I-5 travel shed.

| Summary Description |
| --- |
| Proposed Project: | Light Rail Transit |
|  | 3.4 Miles 3 Stations |
| Total Capital Cost ($YOE): | $131.6 Million |
| Section 5309 New Starts Share ($YOE): | $65.8 Million (50.0%) |
| Annual Forecast Year Operating Cost: | $3.9 Million |
| Ridership Forecast (2025): | 10,500 Average Weekday Boardings |
|  | 4,500 Daily New Riders |
| Opening Year Ridership Forecast (2008): | 9,900 Average Weekday Boardings |
| FY 2006 Finance Rating: | Medium |
| FY 2006 Project Justification Rating: | Medium-High |
| FY 2006 Overall Project Rating: | Recommended |

SANDAG anticipates requesting final design approval for the Mid-Coast LRT Extension in early 2005.  While the information submitted for the project is considered reliable, SANDAG is in the process of updating its mode choice model, capital cost estimate, and implementation schedule for the project, and each of these efforts must be completed and reviewed by FTA before consideration of the final design request.  In addition, the project’s financial plan must be updated to more accurately reflect operating expenses associated with the growth in systemwide service required to meet projected population and employment increases; ensure that fare policy and ridership growth assumptions are consistent with those in the travel forecasts; and isolate and report the operating costs of the project from the system as a whole.

Project Development History and Current Status

SANDAG completed an alternatives analysis on the Mid-Coast corridor in 1995, resulting in the selection of a 10.7-mile Mid-Coast LRT Extension project as the locally preferred alternative.  FTA approved SANDAG’s request to enter preliminary engineering (PE) for the 3.4-mile initial minimum operable segment between the OTTC and Balboa Avenue in September 1996.  A Record of Decision on the project was issued in August 2001.  SANDAG has done little work on the Mid-Coast LRT project since then, as it has its focused attention primarily on the construction of the Orange Line extension in Mission Valley.  However, it is expected to request FTA approval to advance the project into final design in early 2005.

Significant Changes Since Last Evaluation (November 2003)

There have been no significant changes to the project since its last evaluation.  SANDAG’s estimate of the project’s annualized cost has been corrected (previous costs were calculated in year-of-expenditure dollars, rather than current year dollars), and travel forecasts have been adjusted to reflect a 2025 horizon year.  In November 2004, San Diego County voters approved a reauthorization of SANDAG’s TransNet sales tax, which secured local funding for the project.

Project Justification Rating: Medium-High

The Medium-High project justification rating is based upon a Medium-High rating for cost effectiveness and a Medium rating for transit-supportive land use.

Cost Effectiveness Rating: Medium-High

The Medium-High rating is based upon the excellent level of travel-time benefits (2,800 weekday hours) generated by the project relative to its annualized costs.  SANDAG’s estimate of travel-time benefits may change upon completion of improvements to its travel forecasting procedures.  In addition, project costs are expected to increase following the completion of a comprehensive cost update.  These expected changes to the project’s estimated costs and benefits are not expected to threaten the sufficiency of its cost effectiveness rating.

| Cost Effectiveness |
| --- |
| Cost per Hour of Transportation System User Benefit Incremental Cost per Incremental Trip | New Start vs. Baseline $12.85* $7.61 |

* Indicates that measure is a component of Cost Effectiveness rating.

Current travel forecasts for the Mid-Coast project demonstrate travel time benefits to three primary markets.  The first is downtown-bound commuters who would board the extended Blue Line.  These riders generate approximately 40 percent of travel-time benefits because rail travel times are competitive with direct express bus on I-5, and LRT provides circulation downtown beyond the express bus termini.  The second market includes transit riders from the north and west taking advantage of improved access to the OTTC for trips throughout the regional rail and bus system.  Approximately 35 percent of benefits are attributable to this market.  Finally, over 15 percent of benefits accrue to trips destined for the three stations proposed within the Mid-Coast corridor.

The Mid-Coast LRT Extension’s current cost is based on a six year-old estimate, which has been adjusted annually to reflect inflation.  FTA believes that this cost is likely low, based on construction costs recently incurred on the Mission Valley East LRT extension currently.  In addition, the project implementation schedule needs to be updated.

Transit-Supportive Land Use Rating: Medium

The Medium rating is based upon Medium ratings for transit supportive policies and the performance of policies, and a Medium-Low rating for existing land use.

Existing Land Use: Medium-Low

- Total population in the station areas is estimated at 8,900.  Total station area employment is estimated at 18,000 employees.  Existing population and employment densities are approximately 3,400 persons and 6,800 employees per square mile, respectively.

- The project provides direct access to downtown San Diego, which contains over 77,000 jobs.

- The three proposed station areas (Tecolote, Claremont, and Balboa) are bounded by I-5 and recreational facilities at Mission Bay on the west.  The area east of the corridor is dominated by single-family homes with some commercial, multi-family and small-scale industrial development.

- Sidewalks follow most streets in a grid pattern in a primarily residential area on the east side of the proposed alignment.  Pedestrians must cross arterial bridges to reach Mission Bay and other developments west of the freeway.  Needed improvements to existing pedestrian facilities are planned as part of the project.

Transit-Supportive Plans and Policies: Medium

- Regional growth management plans, including the County of San Diego General Plan and the city of San Diego's City of Villages Strategic Framework have been revised to include more specific references to land preservation and promotion of more intense development in existing urban areas. The recent reorganization of functions into SANDAG unites planning entities for regional growth management with transit planning.

- Several city and county documents call for increasing transit accessibility for both pedestrians and bicyclists, improvements in street design, and increased density of development.  These documents include the Mission Bay Master Plan and the Pacific Beach Community Plan.  Parking maximum ratios have been introduced citywide with no specific timetable to reduce the ratios in the Mid-Coast Corridor.  SANDAG’s Transit/Land Use Policy encourages high-density development and coordination of land use and transportation planning.

- Special "zones" have specifically supported increased density development including  Townhouse, Small Lot Single Dwelling, and Shared Parking zones.  Zoning in the areas around the three proposed stations has not been revised specifically to support transit-oriented development

- SANDAG’s predecessor agency, MTDB, implemented a successful joint development program with major development projects including transit-supportive housing, commercial, and public uses.  The Claremont Project Advisory Committee was formed to provide input on issues during the preliminary engineering phase of the Mid-Coast project.  SANDAG has conducted preliminary workshops with the community around the proposed Claremont station to develop a possible concept plan.

Performance and Impacts of Policies: Medium

- The Bayview Plaza development near the Claremont station features locally-oriented shops and a supermarket with links to the new light rail station.

- Progress on transit-supportive development is region-wide, although specific application to the Mid-Coast corridor is limited.   Corridor topographic conditions and the heavily developed nature of the station areas to the east of the corridor, as well as the location of I-5 and Mission Bay to the west, limit the potential for significant new development.

Other Project Justification Criteria

| Mobility Improvements Rating: Medium |
| --- |
| Within ½-mile radius of boarding areas: Existing Employment Projected Employment (2025) Low Income Households (% of total HH) Average Per Station: Employment Low Income Households Transportation System User Benefit Per Project Passenger Mile (Minutes) | 18,000 20,500 200 (7%) 6,000* 67* New Start vs. Baseline 5.98* |
| Environmental Benefits Rating: High |
| Criteria Pollutant (Reduction in tons) Carbon Monoxide (CO) Nitrogen Oxide (NOx) Volatile Organic Compounds (VOC) Particulate Matter (PM10) Carbon Dioxide (CO2) Criteria Pollutant Status Carbon Monoxide 1-Hour Ozone (O3) 8-Hour Ozone Nitrogen Oxide Particulate Matter Annual Energy Savings (million British Thermal Units) | New Start vs. Baseline 66 9 6 1 3,717 EPA Designation Serious Non-Attainment Area* Extreme Non-Attainment Area* Severe Non-Attainment Area* Maintenance Area* Serious Non-Attainment Area* 46,225 |
| Operating Efficiencies Rating: Medium |
| System Operating Cost per Passenger Mile (current year dollars) | Baseline $0.296* | New Start $0.297* |

* Indicates that measure is a component of rating for each criterion.

N/A indicates information was not available for this entry.

# Local Financial Commitment Rating: Medium

The Medium rating for local financial commitment is based on Medium ratings for the New Starts share of project costs and for both the capital and operating finance plans.

Section 5309 New Starts Share of Total Project Costs: 50%

Rating: Medium

SANDAG is requesting a 50 percent New Starts share of total project costs, which results in a Medium rating for this measure.

| Locally Proposed Financial Plan |
| --- |
| Source of Funds | Total Funds ($million) | Percent of Total |
| Federal: Section 5309 New Starts STIP Funds* | $65.8 $9.3 | 50.0% 7.1% |
| State: Traffic Congestion Relief Funds | $10.0 | 7.6% |
| Local: TransNet Sales Tax | $46.6 | 35.4% |
| Total: | $131.6 | 100.0% |

NOTE:  The financial plan reflected in this table has been developed by the project sponsor and does not reflect a commitment by DOT or FTA.  The sum of the figures may differ from the total as listed due to rounding.

*STIP funds are state-administered Federal flexible funds augmented by state gas tax and other revenues.  These funds are passed from the state to local transportation agencies as STIP funds, but all Federal requirements apply.

# Capital Finance Plan Rating: Medium

The capital finance plan is rated Medium, based upon the average of the ratings assigned to each of the subfactors listed below.  The commitment of capital funds subfactor is rated High; capital condition and plan completeness are rated Medium; the capital cost estimate and planning assumptions subfactor is rated Medium-Low; and capital funding capacity is rated Low.

#### Agency Capital Condition: Medium

- SANDAG’S bus fleet has an average age of 6.9 years, which is in line with the industry average.

- SANDAG does not have bond ratings.

#### Completeness of Capital Plan: Medium

- The plan is generally complete, but several pieces, including the fleet management plan and the sensitivity analysis, are outdated.

#### Commitment of Capital Funds: High

- All non-New Starts funding is committed or budgeted.  Funding sources include local sales tax revenues, State Transportation Improvement Program (STIP) funds and State Traffic Congestion Relief funds.

#### Capital Funding Capacity: Low

- SANDAG does not have the financial capacity to cover any project cost increases or funding shortfalls, and a deficit is projected in the existing capital program.

#### Capital Cost Estimate and Planning Assumptions: Medium-Low

### The capital plan includes somewhat optimistic assumptions regarding Federal and State funding.

- An updated capital cost estimate will be available for next year’s assessment rather than this year’s, because the transfer of responsibilities from MDTB to SANDAG has caused some delay.

#### Operating Finance Plan Rating: Medium

The operating finance plan is rated Medium, based upon the average of the ratings of the five subfactors listed below.  Commitment of operating funds received a High rating.  The operating financial capacity and operating cost estimates and planning assumptions subfactors received Medium-Low ratings.  All other subfactors received Medium ratings.

#### Agency Operating Condition: Medium

- SANDAG is in fair operating condition. Minor service cutbacks have been made in recent years.

- SANDAG’s current ratio of assets to liabilities as reported in its most recent audited financial statement is 1.3.

#### Completeness of Operating Plan: Medium

- Comprehensive information was provided for systemwide operation; however, project-specific information was lacking and no sensitivity analysis was provided.

#### Commitment of Operating Funds: High

- All operating funding is committed, including fare revenues, local sales tax revenues, and State transit assistance.

#### Operating Funding Capacity: Medium-Low

- The project’s financial plan shows projected cash balances of zero, with reserve accounts and/or access to credit less than four percent of annual operating expenses.

#### Operating Cost Estimates and Planning Assumptions: Medium-Low

- The plan contains optimistic assumptions regarding future operating expense growth and ridership when compared with historical experience.

Map