REHAB WORK IN PROGRESS

INSPECTION CHECKLIST

Note: All construction materials and methods can be evaluated using detailed technical specifications and tests.  Inspectors are encouraged to pursue this information.  The following list includes the major inspection issues to consider.  It may not address all of the issues in the work write-up for a particular job.

Remember to take all relevant documents, plans, write-up, previous change orders, payment request and other documents to job site.

Job Number or Name: _____________________	Contractor: ____________________

Date: _______________________________	___	Time: ________________________

Address: ________________________________________________________________

Reason for Inspection: _____________________________________________________

People at the job site:

____________________________ 	_______________________		 __________

Name					Company				On Contract?

____________________________ 	_______________________		 __________

Name					Company				On Contract?

____________________________ 	_______________________		 __________

Name					Company				On Contract?

____________________________ 	_______________________		 __________

Name					Company				On Contract?

____________________________ 	_______________________		 __________

Name					Company				On Contract?

Attach a list if more space is required.

Condition of Work Site (E for excellent, G for good, F for fair, P for poor):

Comments

___ 	Cleanliness				______________________________

___ 	Safety					______________________________

___ 	Presence of debris			______________________________

___ 	Presence of unused materials		______________________________

## Items to Consider:

- Do workers appear to know what they are doing?

- For small projects, interview owner to determine satisfaction and what they know about how the job is going.

| Work Component | Status | Is Work Being Completed According to Plan? |
| --- | --- | --- |

## FOOTING CHECKLIST

___	Is footing dug and formed to adequate size?

___ 	Footing depth will be below the frost line (36 inches in most areas)

___ 	Soil under footing is undisturbed

___ 	Forms level +/- ¼ in. per 10 ft.

___	Is sufficient reinforcing bar installed and securely joined?

___ 	Drain tubing installed properly and covered with gravel

___ 	A slump test was performed

___ 	Concrete is finished flat and level +/- ¼ in. in 10 ft., not more than ½ in. overall, and left rough

___ 	Proper steps taken to keep concrete from freezing in cold weather or drying too fast in hot weather or high winds

___ 	Soil is unfrozen, without snow or ice

## FOUNDATION INSPECTION CHECKLIST

___ 	Is foundation plumb and level?

___ 	Walls square +/- ¼ in. in 20 ft.  Not more than ½ in. out of square in any dimension.

___ 	Walls straight +/- ¼ in. in 20 ft.  Not more than ½ in. overall in any wall.

___ 	Foundation bolts or hold down anchor straps are placed 6 ft. o.c.  Bolts or straps are placed within 12 in. of each corner in both directions.

___ 	J-bolts or anchors centered in sill plate.

___ 	Is foundation properly sealed with waterproof sealant (good complete coverage, no missed spots)?

___ 	Parging is 3/8 in. thick and covered at the bottom of the wall where it meets the footing.

___ 	Cores on block walls poured with concrete grout (not mortar) according to the prints or drawings.

___ 	Are mortar joints completely sealed and resistant to chipping or flaking?

___ 	Is concrete poured and worked properly to assure curing with no air pockets?

___ 	Has adequate drainage been provided around foundation?

## FRAMING QUALITY CHECKLIST

___ 	All lumber meets or exceeds CABO code requirements and spec requirements.

___ 	Are components plumb, level and square?

___ 	Is framing installed to provide proper support at all points, especially at corners and around doors and windows?

___ 	Are proper sized used for the spans involved, and are adequate piers and beams installed where necessary to support load?

___ 	Is framing installed to provide adequate nailers for drywall, electrical and plumbing components, especially in corners and around fixtures?

___ 	Is the lumber dry, reasonably straight, and properly secured?

### FLOORS

___ 	Sill sealer insulation installed between foundation sill plates and concrete.

___ 	Minimum bearing of floor joists is 1 ½ in.

___ 	Rim joist toe-nailed to mud sill plate every 16 in. with 16d nails.

___ 	Floor joist crowned up.

___ 	Each joist is nailed to the rim joist with at least 3 16d nails.

___ 	Floor joists which are doubled are nailed together with 12d nails at 16 in. o.c.

___ 	Double floor joists installed around stairwell openings, at bearing walls and at other locations as required by the plans and specifications.

___ 	Notches, holes or cuts, if necessary, are made in the center of joists’ width, not on the top or bottom edges.

___ 	Notches, holes or cuts, if necessary, are made in the first third of the jost span, not on the center 1/3 of the span.

___ 	Construction adhesive used under all floor sheathing.

___ 	Plywood or OSB subfloor nailed 6 in. o.c. on edges, 12 in. o.c. at intermediate supports.

___ 	1/16 in. to 1/8 in. spacing around plywood or OSB sheets for expansion or T&G sheets used.

### WALLS

___ 	Wall plumb +/- ¼ in. in 8 ft.

___ 	Bearing wall studs are not notched more than 25% of the width of the studs, non bearing wall studs are not notched more than 40% of the width of the studs.

___ 	Holes drilled in studs do not exceed more than 40%  and are at least 5/8 in. from the edge of the stud.

___ 	Backing installed for cabinets, grab bars, etc.

### INTERIOR PARTITIONS

___ 	Plumb +/- ¼ in. in 8 ft.

___ 	Bottom plates are nailed to the floor 16 in. o.c.

___ 	All drywall backing is installed.

### ROOF FRAMING

___ 	Truss anchors installed on both ends of every truss.

___ 	Attic vents installed properly.

___ 	A minimum bearing surface of 3 in. is required of all rafters.

___ 	Lateral bracing installed per truss specs.

___ 	Roof sheathing nailed 8 in. o.c. on edges and 12 in. o.c. at supports.

___ 	Joist hangers installed on girder trusses.

### BACKING

___ 	Backing for cabinets installed.

___ 	Backing for grab bars, towel bars, etc.

___ 	Cabinet soffits are correct size and straight, plumb and level.  (Check carefully with a tape, square and level.)

___ 	Fire blocking installed at cabinet stops.

___ 	Fire blocking installed wherever required by local code.

### WINDOWS AND DOORS INSPECTION CHECKLIST

___ 	Door openings plumb +/- ¼ in.

___ 	Door properly shimmed, especially at each hinge and at the strike plate.

___ 	Windows installed level, plumb and square +/- 1/8 in.

___ 	Windows properly shimmed and nailed at 16 in. o.c. or per manufacturer’s specs.

___ 	Check to assure window is not in upside down or backwards.

___ 	Installed plumb and level and work properly, sealing well with no binding or rubbing?

___ 	Warranties provided?

## INSULATION QUALITY CHECKLIST

___ 	Gaps around window foam-insulated or caulked on the side and top.  Stuffed with batt insulation on the sills.

___ 	Rim joists, vertical joints at outside corners and bottom plates on exterior or garage walls sealed and caulked.

___ 	All pipes and outlet boxes penetrating outside walls sealed or insulated.

___ 	Cracks or holes in exterior sheathing sealed with foam prior to batts being installed.

___ 	All holes penetrating double top plate are sealed.

___ 	Exterior sheathing holes repaired and taped properly.

___ 	Wall insulation batts not compressed.

___ 	Tightly cut to fit irregular spaces.

___ 	No insulation within 1 ½ in. of B-vents.  Unfaced insulation only near B-vents.

___ 	Cut out for electrical boxes, no compression insulation cutout placed behind the electrical box.

___ 	Vapor barrier, 2 mil. Polyethylene, installed properly, no holes, splices overlap, proper thickness, etc.

___ 	Insulation collar installed around attic access.

___ 	Statement of R-Value stapled to side of attic access opening.

___ 	Access hatch insulated to the same R-Value as the rest of the ceiling.

## PLUMBING ROUGH QUALITY CHECKLIST

___ 	Are roughed-in pipes sealed during other work to prevent entry of foreign material?

___ 	Are joints secure and straight?

___ 	Make sure that all water and drainage lines are properly supported.

___ 	Make sure vent lines at roof are properly flashed with a roof jack.

___ 	Make sure tub is properly installed and nail flange is nailed with 8d nails 16 in. o.c.

___ 	Studs in an exterior or bearing wall should not be notched more than 25% of their width.  2x4=1 in., 2x6=1¼.  Studs on interior or nonbearing walls should not be notched more than 40% of their width.  2x4=1 5/8, 2x6=2 in.

___ 	Studs may be drilled a maximum of 40% of their width provided the hole is no closer than 5/8 in. from edge of the stud and the stud is not notched.

___ 	Holes in floor joists should not be more than 1/3 of the depth of the joist in diameter and should not be located within 2 in. of the top or bottom of the joist.

___ 	Notches in the joists should not exceed 1/6 of the depth of the joist and should not be located within the middle of the third span.

___ 	Steel protection plates are used whenever plumbing pipes are closer than 1 ½ in. from the edge of the plate or stud.

___ 	Tubs and showers on exterior walls are insulated behind them prior to being set.

___ 	Inspection card is filled out and signed.

___ 	Have lines been pressure tested?

___ 	Shut-offs installed at right places?

___ 	Warranties provided for fixtures?

___ 	All equipment works properly with no signs of leaking or loose mounts?

## ELECTRICAL

___ 	Are circuits marked?
___ 	Adequate number of circuits and GFI circuits?

___ 	Wire run properly protected from nails?
___ 	Equipment functions properly with no sign of excess load?
___ 	Warranties provided?

## HEATING AND COOLING

___ 	Ducts secure, well sealed and insulated?
___ 	Balanced delivery of treated air with adequate return?

___ 	Combustion air provided from outside?

___ 	Exhaust stack vents properly?

___ 	All piping installed with no sign of crimping or damage?

___	 Equipment works properly with no leakage of gas or exhaust?

___ 	Warranty provided?