SVX II Silicon Strip Detector Upgrade Project

Readout Electronics

Configuration ROM, and

Control and Status Registers and

Geographical Addressing Definitions

for

SVX II Silicon Strip Detector Upgrade Project

Readout Electronics VMEbus Module Designs

Version 1.0--PRELIMINARY--

February 7, 1996February 6, 1996

K. Woodbury, J. Anderson

Document # ESE-SVX-9602060118

1. GENERAL INFORMATION

1.1 System Introduction

1.2 Configuration ROM and Control and Status Register Requirements

2. THEORY OF OPERATION

2.1 Bus Monarch

2.2 Addressing of SVX Modules

2.3 Address Modifies Used by SVX modules

2.4 CR/CSR Base Address - Geographical Addressing Mechanisms

2.4.1 160 Pin P1/J1

3. CR AND CSR TABLES

3.1 Configuration ROM

4. Front Panel LED - VMEbus SELECT

4.1 LED Color Guidelines

GENERAL INFORMATION

The information for these register definitions has been gathered from the VME64 (rev 1.11, 2/4/95) specification and VME64 extensions ballot (Draft 1.0, 12/7/95) specification.  After review of the VME64 and VME64 Extensions it has been deemed inappropriate to include those CR/CSR definitions in to the SVX system.  A greatly reduced set of CR/CSR information is presented here which is independent of but not in conflict with the VME64/VME 64 Extensions technique.

System Introduction

The VMEbus modules being designed for this project are responsible for the control and readout of the SVX-III Integrated Circuit chips as part of the SVX Silicon Strip Detector Upgrade Project.

Configuration ROM and Control and Status Register Requirements

To improve both system and software maintenance the following primary features are to be implemented on the SVX VMEbus modules:

Geographical Address Assignment

Board Identification

THEORY OF OPERATION

Bus Monarch

During system configuration there is assumed to be one Bus Master that is assigned the task, often referred to as the Resource Manager Task, of dynamically allocating board location/baselogical address This Bus Master can be referred to as the Bus Monarch.  The SVX addressing scheme detailed below obviates the requirement for a Bus Monarch and is processor-independent.

Addressing of SVX Modules

To allow for base logical address assignment, and the other features provided by CR and CSR registers, there must be some mechanism to “force” the CR and CSR registers to a known location at boot-up. In the SVX system  there is no dynamic allocation of addresses.  Module addresses are defined such that each module is allocated a space of 128 MBytes, with the starting address of every module determined solely by its Geographic Address.  The base address of the module may not be modified by the Bus Monarch or any other processor.

Upon power up each module takes the Geographic Address as found on the GA pins and shifts it left 27 bits to determine the module Base Address (see Figure 1 on the next page).  All SVX modules are to be addressed in A32 mode.

Address Modifies Used by SVX modules

SVX Modules shall respond to the following Address Modifier Codes ONLY:

0x08     A32 non-privileged D64 transfer

0x09     A32 non-privileged D32/D16/D08 transfer

0x0A    A32 non-privileged program access

0x0B    A32 non privileged block transfer

CR/CSR BaseLogical Address - Geographical Addressing Mechanisms

The CR/CSR Logical Address can be set using two different mechanisms.

Geographical Address pins GA0..GA4,GAP on the 160-pin J1 as defined in the VME64 Extensions. specification, or

oOptional jumpers on the board which override the GA pins for non-VME64 Extensions subracks or for diagnostics.(for diagnostics).

SVX  modules shall ignore the parity on the J1 connector.  A map of how all SVX modules fit in to VME address space is shown in Figure 1 on the next page.

Figure 1

SVX Address Map

160 Pin P1/J1

As defined in the VME64 Extensions, wWhen a 160 Pin J1 connector is used, the following Geographical Address Pins have been pre-defined:

Table 1

J1 Geographic Address Pins

|  | Pin Number (row d) | Pin Assignment |
| --- | --- | --- |
|  | J1 - 9 | GAP* |
|  | J1 - 10 | GA0* |
|  | J1 - 11 | GA1* |
|  | J1 - 13 | GA2* |
|  | J1 - 15 | GA3* |
|  | J1 - 17 | GA4* |

Table 2 below  shows how these pin assignments are translated to the Slot Address:

Table 2

GA pin voltages for various slot addresses

|  | Slot Address | GAP* pin (even parity) | GA4* pin | GA3* pin | GA2* pin | GA1* pin | GA0* pin |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  | 1 | Open | Open | Open | Open | Open | GND |
|  | 2 | Open | Open | Open | Open | GND | Open |
|  | 3 | GND | Open | Open | Open | GND | GND |
|  | 4 | Open | Open | Open | GND | Open | Open |
|  | 5 | GND | Open | Open | GND | Open | GND |
|  | 6 | GND | Open | Open | GND | GND | Open |
|  | 7 | Open | Open | Open | GND | GND | GND |
|  | 8 | Open | Open | GND | Open | Open | Open |
|  | 9 | GND | Open | GND | Open | Open | GND |
|  | 10 | GND | Open | GND | Open | GND | Open |
|  | 11 | Open | Open | GND | Open | GND | GND |
|  | 12 | GND | Open | GND | GND | Open | Open |
|  | 13 | Open | Open | GND | GND | Open | GND |
|  | 14 | Open | Open | GND | GND | GND | Open |
|  | 15 | GND | Open | GND | GND | GND | GND |
|  | 16 | Open | GND | Open | Open | Open | Open |
|  | 17 | GND | GND | Open | Open | Open | GND |
|  | 18 | GND | GND | Open | Open | GND | Open |
|  | 19 | Open | GND | Open | Open | GND | GND |
|  | 20 | GND | GND | Open | GND | Open | Open |
|  | 21 | Open | GND | Open | GND | Open | GND |

Please note that the maximum current through the geographical address pin will be limited to 2 mA.

All open positions will be pulled up to VCC on the SVX modules.

CR AND CSR TABLES

Table 3 below defines the single Configuration ROM location which is common to SVX Modules.  SVX Modules have no common CSRs, although individual modules may define them as needed within their allowed address space.

Configuration ROM

Table 3

SVX Configuration ROM

|  | Address Offset | Definition |
| --- | --- | --- |
|  | 0x00 |

Module Type code:

00:   illegal

01:   SRC

02:   FIB

03:  VRB

04:  FIB Fanout

05:  SVX Test Module

06 - FE: Reserved for future use.

FF:  illegal

|  | 0x01, 0x02, 0x03 | User defined bytes. The authors suggest these be used to encode module revision data such as ECO number, netlist revision, firmware version, serial number, etc. |
| --- | --- | --- |

Front Panel LED - VMEbus SELECT

One front panel amber LED is required, labeled SELECT, which indicates when the module recognizes its address on the bus.

The LED should stay on for a minimum of 100 milliseconds, so that the human eye can recognize that the LED did turn on.

The LED should be mounted at the top of the front panel, as close as possible to the top extraction handle, as shown in Figure 2.

Figure 2

Select LED Mounting

LED Color Guidelines

Red should only be used for error indicators.

Green should only be used for static status indicators.

Amber should only be used for transient status indicators (e.g. operation in progress, module addressed, etc.)

Blue may be used for any other indicator purpose.

# Comments

.