P9-20, P9-30, P9-40 and P9-50

- Originally designed for Sector 2

- Insertion Device Integral Shutter

- Pink Beam Photon Shutter

- Pink Beam Safety Shutter

- Pink Beam Fixed Mask

- Pink Beam Collimator

Beam Line locations:

- 10 Shutters total

2ID-A:	P9-30	Pink beam, D-E beam line, 0.3 degrees from the axis of the ID beam

P9-40	Pink beam, C beam line, 2.5 degrees from the axis of D-E branch

P9-20	Pink beam, B beam line, 5.0 degrees from the axis of D-E branch

Horizontally deflecting mirrors

D-E beam line - 	Maximum energy of 40 keV

C beam line -		Intermediate energy range of 0.5 to 3 keV

B beam line -		Intermediate energy range of 0.5 to 4 keV

2ID-E			P9-50, Pink/Mono beam

4ID-A			P9-40,	Pink beam, C branch

8ID-A			P9-30,	Pink beam

8ID-D-MH-1		P9-50,	Pink beam

9ID-A			P9-50,	Mono beam

34ID-B		P9-30, 	Pink beam

34ID-D		P9-30	White beam	A.R. The mask in 34-ID-B has a restriction to operate only to gaps of 15 mm due to thermal effects. The ID gap has currently an administrative limit of 15 mm gap and a hardware limit set for 14.8 mm.

- 20, 30, 40 and 50 is only a designation - denotes physical difference – see drawings

Flange size

Port location

Vacuum Chamber – All - flange to flange length – 622 mm

P9-20 – in line w/beam – 4 ½” flange & 6” flange, Pump out port – 8” flange (side)

P9-40 - in line w/beam – 4 ½” flange & 6” flange, Pump out port – 8” flange(bottom)

P9-20 & P9-40 Design difference – (pump out port position)

P9-30 – in line w/beam – 6” flanges, Pump out port – 8” flange (side)

P9-50 – in line w/beam – 8” flanges, Pump out port – 8” flange (bottom)

Pump out port - 8” – decreased conductance

General Differences:

P9-20, 30 and 40

Internal Fixed Mask	(bellows for expansion P9-30)

Internal Collimator

P9-50

External Fixed Mask	(bolted to the vacuum chamber)

External Collimator

All are water cooled -

Shutters - Top connections									Fixed Mask - Side connections

P9-20 and P9-40 – Maximum Heat Load: 60 watts Pink Beam:

Absorber Material: OFHC copper

Optical Aperture Area: 100 mm (Horiz.) x 34 mm (Vert.)

Absorber length: 54 mm

Safety Shutter

Mask (Stop) material: tungsten

Heavy Metal Size: 70 mm (Horiz.) x 35 mm (Vert.)

Length: 21 mm

P9-30 – Maximum Heat Load: 600 watts Pink Beam:

Absorber Material: GLID-COP/OHFC copper

Optical Aperture Area: 127 mm (Horiz.) x 34 mm (Vert.)

Absorber length: 54 mm

Safety Shutter

Mask (Stop) material: tungsten

Heavy Metal Size: 90 mm (Horiz.) x 35 mm (Vert.)

Length: 35 mm

P9-50 - Maximum Heat Load: 600 watts Pink Beam:

Absorber Material: OFHC copper

Optical Aperture Area: 50 mm (Horiz.) x 72 mm (Vert.)

Absorber length: 72 mm

Safety Shutter

Mask (stop) material: tungsten

Heavy Metal Size: 50 mm (Horiz.) x 72 mm (Vert.)

Length: 25 mm

P9-20 and P9-40:

Fixed Mask - material (tungsten/304 sst)

Optical Aperture Area: 30 mm (Horiz.) x 20 mm (Vert.)

Follows through into the collimator – material (tungsten)

Collimator length – 50 mm

P9-30:

Fixed Mask – material (Glid-Cop)

Optical Aperture Area: 12 mm (Horiz.) x 10 mm (Vert.)

Collimator – material (tungsten)

Optical Aperture Area: 15 mm (Horiz.) x 13 mm (Vert.)

Collimator length – 100 mm

P9-50:

Fixed Mask – material (OFHC copper)

Optical Aperture Area: 16 mm (Horiz.) x 52 mm (Vert.)

Collimator – material (tungsten)

Optical Aperture Area: 20 mm (Horiz. x 56 mm (Vert.)

Design Characteristic – P9-50:

Large Vertical Aperture – 52 mm

Designed for downstream of the Monochromator

Allow Pink beam or Mono beam

Vertical offset of 22 mm to allow transport of Mono beam, (2ID-E station)

Acknowledgements

Thanks to the following people for contributing reference information

AOD Staff

Mohan Ramanathan

P. K. Job

ASD Staff

Sushil Sharma

XFD Staff

Barry Lai

Deming Shu