Exposition Corridor LRT

Los Angeles, California

(November 2004)

The Los Angeles County Metropolitan Transportation Authority (LACMTA) is proposing to construct a 9.6-mile light rail transit (LRT) line extending from the 7th and Metrocenter Blue Line light rail /

Red Line heavy rail station in the Los Angeles central business district (CBD) west to Culver City.  The proposed project would use the existing “Exposition” railroad right-of-way, which was used for passenger rail service until the 1950’s, to provide high-capacity transit service to a number of activity centers within the corridor.  These include the University of Southern California, Exposition Park, Crenshaw, and Culver City.  The project includes the construction of eight new stations, three park-and-ride lots with 1,300 spaces, and the purchase of 16 light rail vehicles.  The project would operate with five-minute headways and provide for intermodal connections with LACMTA Metro Rapid Bus service at the Vermont, Western, Crenshaw, and La Cienega stations.

The Exposition Corridor parallels the Santa Monica Freeway (I-10) which currently maintains traffic volumes exceeding 300,000 vehicles per day.  I-10 is often cited as the most congested highway in Los Angeles.  Likewise, local arterials operate at capacity, and travel speeds average below 20 miles per hour.  Existing local bus transit service is severely delayed by these congested road conditions; nevertheless, bus routes in the corridor are heavily utilized.  The communities in the corridor have a population density of over 20,000 persons per square mile.  Moreover, approximately 50 percent of the households within ½ mile of proposed stations have incomes of less than $25,000 per year, and 30 percent do not have access to an automobile.  Because of the existing land use and limited room for roadway expansion, LACMTA’s proposal to improve transportation capacity is to extend rail service into the corridor from the Blue Line, which is one of the most heavily utilized light rail lines in the U.S.  The Exposition Corridor LRT project will thereby provide improved access to employment opportunities beyond the corridor and CBD, including other areas served by LACMTA’s regional rail system.

| Summary Description |
| --- |
| Proposed Project: | Light Rail Transit |
|  | 9.6 Miles 8 Stations |
| Total Capital Cost ($YOE): | $552.1 Million (includes $34.2 million in finance charges) |
| Section 5309 New Starts Share ($YOE): | $276.0 Million (50.0%) |
| Annual Forecast Year Operating Cost: | $50.7 Million |
| Ridership Forecast (2025): | Not Available |
| Opening Year Ridership Forecast: | Not Available |
| FY 2006 Finance Rating: | Medium-High |
| FY 2006 Project Justification Rating: | Not Rated |
| FY 2006 Overall Project Rating: | Not Rated |

FTA acknowledges the progress made by LACMTA in the development of an acceptable financial plan for the Exposition Corridor LRT project.  However, the project is Not Rated at this time because LACMTA’s current estimate of ridership and travel-time benefits is not considered reliable.  FTA will work with LACMTA to address these travel forecasting concerns, and will re-rate the project when they have been satisfactorily addressed.

Project Development History and Current Status

After abandoning plans to construct and operate an extension of its heavy rail system underneath Wilshire Avenue, LACMTA undertook an alternatives analysis to analyze and evaluate feasible alternatives in the Mid-City/Exposition corridor.  In March 2000, LACMTA initiated a Draft Environmental Impact Statement (EIS) to analyze transportation alternatives in the re-defined Exposition corridor.  FTA approved the project’s entry into preliminary engineering in February 2002.  LACMTA has initiated the Final EIS and plans to complete the NEPA process in Spring 2005.

Significant Changes Since Last Evaluation (November 2003)

The project cost has increased from $505 million to $552 million because LACMTA added financing costs (consistent with FTA policy), escalated the capital costs due to inflation, and incorporated some grade separation improvements into the project scope.  LACMTA also improved its systemwide financial plan to reflect more realistic revenue forecasts and adopted a new operating cost model, resulting in revised systemwide operations and maintenance costs.

###### Project Justification Rating: Not Rated

The project is Not Rated for project justification based on the absence of reliable information on the cost effectiveness of the project, despite a Medium-High rating for transit-supportive land use.

Cost Effectiveness Rating: Not Rated

As noted, LACMTA has not submitted to FTA reliable estimates of the travel-time benefits of the Exposition Corridor LRT project.  Therefore, FTA cannot rate its cost effectiveness.  FTA is continuing to work with LACMTA to develop an acceptable and reliable travel forecast for the project.

Transit-Supportive Land Use Rating: Medium-High

The Medium-High land use rating reflects the Medium-High ratings assigned to existing land use and transit supportive plans and policies and the Medium rating for the performance of land use policies.

Existing Land Use: Medium-High

- The proposed project is located within an abandoned urban rail corridor that has been developed into predominantly industrial land uses.   There are transit-supportive population and employment densities throughout the corridor, within a block of the rail alignment in most areas.

- Over 84,000 residents and nearly 76,000 jobs are currently located within ½ mile of the proposed station sites.  The corridor contains a high number of trip generators, especially in the eastern end, which encompasses downtown Los Angeles, the Los Angeles Convention Center, Staples Center Arena, the University of Southern California and Exposition Park (including the Memorial Coliseum, Sports Arena, California Science Center, and the California Afro-American Museum).  High trip generators in the western end of the corridor include downtown Culver City and the West Angeles Cathedral.

- Pedestrian accessibility is transit-supportive and sidewalk facilities are provided along a dense grid street network.  However, parking is generally plentiful around station areas and comprises a significant portion of proposed station area land uses.

Transit-Supportive Plans and Policies: Medium-High

- LACMTA and the city of Los Angeles have jointly adopted a land use and transportation policy that provides strong incentives and prototypes for development around station areas.

- A station area planning process is underway and more station-specific land use plans and policies are being developed.  There are opportunities in the corridor for the expansion of high trip generators, especially the museums around Exposition Park and an entertainment district around Staples Center, which may promote additional redevelopment.

- Redevelopment zones around the Crenshaw and Vermont stations provide an opportunity to promote economic development around proposed station sites.  Additionally, current industrial land around rail stations may provide further opportunity for new transit-oriented development as station sites are planned and designed.

Performance and Impacts of Policies: Medium

- LACMTA has recently begun to pursue transit-supportive land use under its joint development program.  The developments have occurred primarily near Red Line subway stations, as the opportunities along other rail corridors have been limited.

- Transit-oriented development projects along LACMTA light rail lines have been successful in cities that have provided significant planning support to the projects, such as mixed-use developments at two Pasadena Gold Line stations.

Other Project Justification Criteria

| Mobility Improvements Rating: Not Rated |
| --- |
| Within ½-mile radius of boarding areas: Existing Employment Projected Employment (2020) Low Income Households (% of total HH) Average Per Station: Employment Low Income Households Transportation System User Benefit Per Project Passenger Mile (Minutes) | 75,800 78,300 7,900 (27%) 9,475* 988* New Start vs. Baseline N/A* |
| Environmental Benefits Rating: Not Rated |
| Criteria Pollutant (Reduction in tons) Carbon Monoxide (CO) Nitrogen Oxide (NOx) Volatile Organic Compounds (VOC) Particulate Matter (PM10) Carbon Dioxide (CO2) Criteria Pollutant Status Carbon Monoxide 1-Hour Ozone (O3) 8-Hour Ozone Nitrogen Oxide Particulate Matter Annual Energy Savings (million British Thermal Units) | New Start vs. Baseline N/A N/A N/A N/A N/A EPA Designation Serious Non-Attainment Area* Extreme Non-Attainment Area* Severe Non-Attainment Area* Maintenance Area* Serious Non-Attainment* N/A |
| Operating Efficiencies Rating: Not Rated |
| System Operating Cost per Passenger Mile (current year dollars) | Baseline N/A* | New Start N/A* |

* Indicates that measure is a component of rating for each criterion.

N/A indicates information was not available for this entry.

# Local Financial Commitment Rating: Medium-High

The Medium-High rating for local financial commitment is based on Medium-High ratings for the New Starts share of project costs and for both the capital and operating finance plans.

Section 5309 New Starts Share of Total Project Costs: 50%

Rating: Medium

LACMTA is requesting a 50 percent New Starts share of total project costs, which results in a Medium rating for this measure.

| Locally Proposed Financial Plan |
| --- |
| Source of Funds | Total Funds ($million) | Percent of Total |
| Federal: Section 5309 New Starts STIP Funds* | $276.0 $111.7 | 50.0% 20.2% |
| State: Traffic Congestion Relief Program | $11.0 | 2.0% |
| Local: LACMTA Sales Tax Revenues LACMTA Lease Revenue | $148.9 $4.5 | 27.0% 0.8% |
| Total: | $552.1 | 100.0% |

NOTE:  The financial plan reflected in this table has been developed by the project sponsor and does not reflect a commitment by DOT or FTA.  The sum of the figures may differ from the total as listed due to rounding.

*STIP funds are state-administered Federal flexible funds augmented by state gas tax and other revenues.  These funds are passed from the state to local transportation agencies as STIP funds, but all Federal requirements apply.

# Capital Finance Plan Rating: Medium-High

The capital finance plan is rated Medium-High, based upon the average of the ratings assigned to each of the subfactors listed below. The commitment of funds received a High rating; capital condition and completeness were rated Medium-High; and the remaining two subfactors were rated Medium.

#### Agency Capital Condition: Medium-High

- The average age of LACMTA’s bus fleet is 4.2 years, which is significantly younger than the industry average.

- The agency’s good bond ratings, which were issued in 2003, are: Moody’s Aa3; Standard & Poor’s AA-; and Fitch A+.

#### Completeness of Capital Plan: Medium-High

- The submittal was complete.  It contained all required elements including a 20-year cash flow statement, identification of key assumptions, fleet management plans and other supporting documentation, and more than five years of historical data.  The plan included a limited sensitivity analysis that examined the effect of changes in passenger fares.

#### Commitment of Capital Funds: High

- Approximately 89 percent of non-New Starts funding is committed.  The committed funds include Traffic Congestion Relief Program funds, State Transportation Improvement Program (STIP) funds, and Proposition A and C tax revenues which are totally under the control of LACMTA.

#### Capital Funding Capacity: Medium

- The project’s financial plan shows projected cash balances, reserve accounts, and/or access to credit that would allow LACMTA to cover cost increases or funding shortfalls equal to approximately 25 percent of project costs.

#### Capital Cost Estimate and Planning Assumptions: Medium

### Key assumptions regarding sales tax revenue growth, inflation rates, and receipt of Federal funds are consistent with historical trends.

#### Operating Finance Plan Rating: Medium-High

The operating finance plan is rated Medium-High, based upon the average of the ratings assigned to each of the five subfactors listed below.  The operating condition and commitment of funds subfactors received High ratings, while the remainder of the subfactors received Medium ratings.

#### Agency Operating Condition: High

- LACMTA is in excellent financial condition.  There have been no cash flow shortages in the operating plan in the last five years.  From FY 1997 to FY 2003, LACMTA steadily increased its service, adding 23 percent more revenue hours.

- LACMTA’s current ratio of assets to liabilities as reported in its most recent audited financial statement is 3.6.

#### Completeness of Operating Plan: Medium

- The operating plan is reasonably detailed for the LACMTA system as a whole, but lacks some detail regarding the project’s specific operating costs and fare revenue estimates.

#### Commitment of Operating Funds: High

- Over 75 percent of operating funding is committed.  Operating funds include passenger revenues, Proposition A and C sales tax revenues, State Transportation Development Act funds, and FTA Section 5307 Formula funds (used for preventative maintenance).

#### Operating Funding Capacity: Medium

- The project’s financial plan shows projected cash balances, reserve accounts, and/or access to credit exceeding 12 percent of annual operating expenses.

#### Operating Cost Estimates and Planning Assumptions: Medium

- Forecasts of key components of the operating plan (operating costs, passenger revenues, sales tax and other revenues) are reasonable in comparison to historical trends.

Map