#### PASSPORT Label Acquisition System

#### Mailer Reference Manual

PASSPORT Label Acquisition System	Section 010

Software Licensing	010-1

Acquiring the Software	010-1

Hardware Requirements	010-1

Documentation	010-3

Typographic Conventions Used in This Manual	010-5

Application Support	010-5

PASSPORT System Overview	Section 020

Purpose	020-1

Overview	020-1

PASSPORT Versions	020-2

Quick Setup	Section 030

Installing the Software	030-1

Running the Program	030-1

Originating Site	030-2

PASSPORT Site	030-4

Ordering Configuration - Registering with Topeka	030-5

Software Upgrades	030-7

Barcoded Tray and Sack Labels	Section 040

Label Products	040-1

Label Data	040-3

The Label Ordering Process	Section 050

Introduction to Label Ordering	050-1

Bulk Label Ordering	050-1

DMM Label List Ordering	050-5

Collated Set Orders	050-8

Label Order Preparation	050-11

Transmitting a Label Order to the Label Printing Center	050-12

Retransmit Orders	050-12

View/Delete Prepared Batch	050-12

Reports Menu	050-13

The Label Printing Process	Section 060

Importing and Exporting Label Data	Section 080

Reference Tables	Section 090

Product Code Table	090-1

Mail Type (Content Identification Number) Table	090-1

Appendix A - Label Printer Setup and Specifications

Intermec 3000A	A-1

Intermec 3400	A-1

Microcom 410 ECA	A-1

Monarch 9425	A-2

Monarch 9445	A-4

Sato M-8400	A-6

Whittier Mailing Products	A-7

Appendix B – PASSPORT System Hardware Reference

Personal Computer	B-1

Modem	B-1

Console Printer	B-2

Label Printer	B-2

Appendix C – Cabling Requirements

Troubleshooting	Section 130

Installation Problems	130-1

Communications Problems	130-1

Other common Problems	130-1

System Support	130-2

Glossary of Terms	Section 140

Index	Section Error! Bookmark not defined.

## Software Licensing

The PASSPORT System was developed at the request of the Office of Processing Policies and Programs, Processing and Distribution, U.S. Postal Service Headquarters.  It was written by the Raleigh Integrated Business Systems Solution Center (RA IBSSC) located in Raleigh, North Carolina.  The Label Printing Center (LPC) located in Topeka, Kansas also participated in the development of this application and was instrumental in reducing turnaround time for label orders.

PASSPORT provides a comprehensive and flexible method of obtaining barcoded tray and sack labels used by the USPS and its customers.  Labels may either be ordered through an automated ordering process from the LPC and/or printed locally.  The application software and internal data files are kept updated through an automated upgrade process.

Copyright (C) 1993-2005

U.S. Postal Service Raleigh IBSSC,

4200 Wake Forest Road, Raleigh, NC 27668 - 9000

No part of this software and corresponding documentation may be reproduced or transmitted in any form or by any means, electronic or mechanical, including photocopying, recording, or by any information storage and retrieval system, without permission in writing from the U.S. Postal Service.

COPYRIGHT. The Quick BASIC Run-time Library is owned by Microsoft or its suppliers and is protected by United States copyright laws and international treaty provisions. It is included with this system under its licensing conditions.

## Acquiring the Software

### Download Software and Documentation Via the Internet

External Mailer customers may download the Mailer version of the PASSPORT software from a publicly accessible Web site:

http://ribbs.usps.gov/files/PASSPORT/

Arrangements can be made for those mailers customers unable to download software.

## Hardware Requirements

The hardware requirements for PASSPORT are:

386/20mhz or higher, 4mb memory

40mb hard-disk space (exclusively for PASSPORT)

2400 baud rate modem (9600+ recommended) and modem compatible phone line

MS- DOS version 3.3 or higher

Console Printer - Okidata 320 or 390 or compatible for report printing.

PASSPORT reports are printed to a parallel port printer as ASCII text files with space-delimited formatting. Most dot matrix or laser printers will provide these reports.

Label Printer - (Required for on-site label printing)

### CPU and Operating System

The minimum system hardware is an 80386 or compatible PC. At least 4MB of RAM is required. A 3-1/2 inch High-Density floppy drive is used to install software. The PASSPORT software requires a VGA or better video display and adapter. A parallel port is required for output to a console report printer. Serial ports are required for both the modem and for any serial interface label printer.

### Modem

A 2400-baud modem will work with PASSPORT, but upgrades to the software may require up to 2 hours to download. A 9600-baud modem is recommended for faster data transfers.

Plug and Play modems may be used with PASSPORT, but the program must be run under Windows to allow access to the Windows hardware drivers.

The user must determine the communication settings for the modem. PASSPORT has no way to detect the communication (COM) port or interrupt request number (IRQ). In addition, the user may have to provide a customized initialization string to set the modem to emulate a Hayes modem.

### Label Printer

The following printers may be used to produce barcoded tray and sack labels:

Monarch 9425

Monarch 9445

Intermec 3000 ALI

Intermec 3400

SATO Model M-8400

Microcom Model 410 ECA

Whittier Mailing Products (Eltron, Orion, etc.)

Mailers may also use:

Hewlett Packard LaserJet III or compatible

NOTE: The laser printer must have enough memory to support full-page graphics. The printer must also allow the use of 70# card stock.

### Console Printer

Reports and reference tables may be printed using the console printer. The console printer is to be connected to the parallel port (LPT1). The following are specifically supported:

Okidata 320

Okidata 390

The reports are sent to the printer as ASCII text files and will therefore print on most types of dot matrix and laser printers.

### Hardware Vendors

Contact information for hardware vendors is available in Appendix B of this guide

## Documentation

### Readme Files

The first diskette in the new installation package includes a file named README.CAA. This file contains important notes about the current software release and any special installation instructions.

After each software upgrade, upgrade specific information can be found in READnnnn.CAA where nnnn is the version number of the upgrade. For example, after downloading V01.24-BE, the file READ0124.CAA will be added to your system.

All ReadMe files are located in the C:\CAA.V01 directory.

### User Manuals

PASSPORT distributes most User Documentation with the installation diskettes. In addition, updates are distributed along with system upgrade downloads.

Run the program USERMAN.EXE. This will extract the following 3 files to the C:\CAA.V01 Directory:

QUICKREF.DOC –Microsoft Word( Document

QUICKREF.TXT - ASCII text Document

QUICKREF.HP3 - Hewlett Packard LaserJet III print file

These three files are the same PASSPORT Quick Reference Guide in different formats. This document is a simplified operating manual with specific instructions on getting started using the PASSPORT system.

In addition, after each software upgrade, updated user documentation is provided in a file USRMnnnn.EXE where nnnn is the version number of the upgrade. Executing this file, located in the C:\CAA.V01 directory, will extract the following four files:

QUICKREF.DOC –Latest complete version in Microsoft Word( format

QUICKREF.TXT - Latest complete version in ASCII text

QUICKREF.HP3 - Latest complete version as an HP LaserJet III print file

USRMnnnn.DOC – Detailed Release Notice in Microsoft Word format

### Hotnews

Each time a connection is made to a PASSPORT BBS to either order labels or upgrade software, a Hotnews file is retrieved. This Hotnews file will be displayed the next time PASSPORT is run, or may be opened directly using the Upgrade Software/Tables menu. New information is provided here to keep PASSPORT users up-to-date on the latest PASSPORT labeling news.

## Typographic Conventions Used in This Manual

The following are typographic conventions used in this guide:

PASSPORT Menu choices are shown with the sequence of menus to follow to access that choice. A | is used to denote a submenu. Menu items are shown in the text: Menu Level 1 | Menu Level 2…

PASSPORT Screen names are shown in this text: Screen Name

PASSPORT data field names are shown in this text: DataField

Typed commands are usually followed by the <Enter> key. Command text that a user is to enter is shown in this text: TYPED COMMAND <Enter>

Keyboard commands are shown in this text: F1-Help

References to other sections of the user guide are shown in this text: See also…

## Application Support

The PASSPORT System is a PC-based application not requiring daily connectivity to the Raleigh Integrated Business Systems Solution Center (RA IBSSC) in Raleigh, North Carolina.  Although the system is user-installed, the RA IBSSC will provide assistance, as needed, in the coordination and installation of the PASSPORT hardware.  Users are responsible for procuring hardware maintenance.  All software distribution and version updates will be distributed by the RA IBSSC via dial-up connection.  The application will indicate when it is necessary to execute the Get Update option which must be done periodically to ensure that all updates are received.

The Raleigh Integrated Business Systems Solution Center (RA IBSSC) maintains a Customer Support Hotline which provides assistance for application related problems.

1-800-USPSHELP (1-800-877-7435)

All of the INFORMATION SYSTEMS SUPPORT (ISS) locations will be available through this new number and can be reached by pressing the following option number at any time after reaching the recording.

Press 5 for Raleigh (PASSPORT SUPPORT)

Anyone who is calling from a rotary phone may still use 1-800-USPSHELP (1-800-877-7435) and SPEAK the option number associated with the support group they need, and the system will route their call.

NOTE:  Please see the Troubleshooting Chapter in this manual for resolutions to common questions and problems before calling Customer Support.

### Postal Business Centers and/or BMEU Representatives

Questions relating specifically to labeling rather than software operation should be directed to your local USPS Business Mail Specialist.

## Purpose

Tray and sack labels are a vital link in the efficient movement of the mail. Barcoded labels provide the interface to the automated mail handling systems in the Postal Service today, those currently in use and under development.  Since changes are constantly being made to improve transportation efficiency, labels must be modified to reflect these changes.

The intent of the PASSPORT System is to automate and improve the accuracy of ordering preprinted tray and sack labels from the LPC.  The use of this system and associated handling/processing changes at the LPC also drastically reduces the turnaround time required for receipt of the requested labels. This improved ordering process allows users to maintain a minimal label inventory and reduces waste when label requirements change. Both bulk and collated label sets are handled via this system. Built-in Domestic Mail Manual Labeling Lists, Five-digit ZIP Code, and Contents ID tables assist in ensuring accuracy of labels ordered. These tables and all components of the application software are nationally maintained through an automated software update process. (Future plans are to include the Distribution Requirements System labeling lists in the built-in tables.)

PASSPORT can also locally print barcoded tray and sack labels that meet Postal standards in a cost-effective manner which may be used in conjunction with the automated ordering process.  This type of printing will allow label changes to be implemented on an immediate basis until the revised preprinted labels are received from the LPC.  Thus, the need for handwritten labels (and the associated problems of using them) are eliminated.

PASSPORT allows label printing, ordering, or both. Each local PASSPORT site may determine what functions best supply its labeling needs.

## Overview

The PASSPORT system was designed to serve the label acquisition needs of a variety of users. It provides a means for both ordering and printing labels.

A simple menu-based interface, standard keyboard commands and a context sensitive help system provide easy access to PASSPORT’s features

The system must be configured before use. At least one originating site must be specified with location and contact information. One originating site must be specified as the PASSPORT Site. Hardware must be specified using the Ordering Configuration Setup.

PASSPORT allows ordering of barcoded labels from the Topeka Label Printing Center by transmitting an electronic version of the Postal Form PS-1578B. Originating Site information is transmitted to Topeka on an electronic version of the Postal form PS-8131. Transmission may be immediate, or scheduled for a time when the system is unattended.

The PASSPORT System allows local printing using a single PC and one of the supported label printers.

As needed, program and data upgrades will be made available on the Raleigh IBSSC Bulletin Board System (BBS). PASSPORT will keep the system current by forcing the user to check for updates on a regular basis and  notify the user when an upgrade should be downloaded. PASSPORT connects to the BBS and downloads upgrades when the user selects that menu option.

## PASSPORT Versions

PASSPORT is available in two distinct versions. The Postal Version is for use by Postal facilities and will support originating sites designated as Postal or Mailer. The Mailer version is for use by Mailer facilities and only supports originating sites designated as Mailer.

The Postal version has support for Access Level Security and requires an account Name and Password to begin running the software. The mailer version allows access to all program functions without password protection. If you see a Login Screen upon starting PASSPORT, immediately contact the ISS Support Number to request the proper PASSPORT version.

### The Label Ordering System

Figure 1 - The Label Ordering System

This local print option requires no label printer. It consists of a single PC, connected via modem to the Topeka Label Printing Center. This option is available to users of both the Mailer and Postal versions of the PASSPORT software

### The Label Ordering/Printing System

Figure 2 - The Label Ordering/PrintingSystem

This System setup offers the flexibility for users who wish to print or order labels directly from the LPC. This system requires a single PC and one of the supported label printers.

## Navigating in PASSPORT

### The Menu System

PASSPORT offers a set of easy-to-use menus that provide access to all the features of the program. Once the Licensing information screens and Logon screen are displayed, the menu structure begins as follows:

MAIN MENU

  - LABEL ORDERING MENU

    - ORDER ENTRY MENU (PS FORM 1578-B)

      - BULK LABELS

      - DMM SET LABELS

      - COLLATED SET LABELS

      - EXIT

    - ADDRESS DATABASE CHANGE (FORM 8131)

    - TRANSMIT MENU

      - PREPARE ORDERS

      - SCHEDULE TRANSMISSION

      - RETRANSMIT ORDERS

      - VIEW/DELETE PREPARED BATCHES

      - EXIT

    - REPORTS MENU

      - ORDER STATUS

      - ORIGINATING SITES

      - BATCH TRANSACTION

      - COLLATED SET LIST

      - EXIT

    - EXIT

MAIN MENU

…

  - LABEL PRINTING MENU

    - PRINT LABELS

    - DOWNLOAD LABEL FORMATS

    - EXIT

  - UPDATE SOFTWARE/TABLES MENU

    - GET UPDATE

    - SEND MESSAGE TO PASSPORT CENTRAL

    - BROWSE OLD HOTNEWS ITEMS

    - SYNCHRONIZE OTHER PASSPORT COMPUTERS

    - EXIT

  - SETUP MENU

    - ORIGINATING SITES

    - PASSPORT SITE

    - ORDERING CONFIGURATION

    - CUSTOMIZING TABLES MENU

      - MAIL TYPE (CIN) TABLE

      - PRODUCT CODE TABLE

      - EXIT

    - EXIT

  - EXIT

NOTE: Some menu choices may be unavailable, depending on whether the software is Mailer Version or Postal.

### Standard Keyboard Commands

In addition to the menu system, there are a number of standard keyboard commands. These are keystrokes or keystroke combinations that perform certain actions. Available keyboard commands are displayed along the bottom of each screen. Each screen in PASSPORT will allow access to a limited number of the following common commands:

Standard Keyboard Commands

| Keyboard Command | Functional Description |
| --- | --- |
| Backspace | Moves the cursor left one character, deleting that character |
| Backtab (Shift + Tab) | Enters the contents of the current field and moves the cursor to the previous data entry field |
| Down Arrow | Highlights the next menu entry, scrolls to the next entry in a popup list or report screen, or moves to the next data entry field |
| End | Highlights the last menu entry, scrolls to the last entry in a popup list or report screen |
| Enter | Selects the current menu item or data record. Stores the contents of the current data field |
| ESC (Escape Key) | Selects the EXIT option from the current menu, or exits the current screen without saving changes. |
| F1 – Help | Displays context-sensitive help to assist the user with the current task. |
| F2 – Clr | Clear the contentes of the current data entry field |
| F3 – Add | Append a new data record. |
| F4 – Chg | Change the contents of the current data record or currently selected file |
| F5 – Del/Rcl | The currently selected data record or file is deleted. Records marked for deletion are marked with a small dot on the screen to the left of the record. |
| F6 – Print | Print a report of the current data |
| F7 - Print Labels | Print labels |
| F10 – Process | Exits current screen and saves changes made. |
| Home | Highlights the first entry in a menu, scrolls to the first entry in a popup list or report screen |
| Page Down | Scrolls down several entries in a popup list or report screen |
| Page Up | Scrolls up several entries in a popup list or report screen |
| Tab | Stores the contents of the current data entry field and advances cursor to next field |
| Up Arrow | Highlights the previous menu entry, scrolls to the previous entry in a popup list or report screen, or moves to the previous data entry field |

## Installing the Software

PASSPORT is provided on a set of three 3-1/2 inch high density floppy diskettes. To begin installing the software, insert the diskette labeled “Disk 1” in the floppy drive. Make the floppy drive the current drive by typing the drive letter followed by a colon and pressing enter. Next, the installation program is run by typing Install and pressing <Enter>. The following example assumes that the floppy drive is the A: drive:

A: <Enter>

INSTALL <Enter>

The program will prompt for subsequent diskettes. When all the data has been transferred to the PC, the program expands its compressed files, makes modifications to the AUTOEXEC.BAT and CONFIG.SYS files as needed and displays the readme file. Review this file for any important notes about installing or using PASSPORT.

NOTE: If this is not a first time installation: PASSPORT will check to see if there are user data files on the target drive. PASSPORT will install all files except the user data files in this case. If you want to perform a complete new installation, delete the directory: C:\CAA.V01 and its subdirectories.

## Running the Program

PASSPORT creates a batch file in the root directory named C:\PASSPORT.BAT. To run the program, change the current directory to the root directory (CD \ <Enter>) then type PASSPORT and press the enter key.

The program runs several preliminary setup routines when run for the first time. Messages will be displayed to show the progress of these first time processes. When these have concluded, the MAIN MENU will be displayed. Option 1 is the current selection and will be highlighted. To move the current selection bar, use the arrow keys ( ( and (). To select a menu option, press enter. You may also enter the menu item number to make a menu choice.

NOTE: The bottom of the screen displays the available keyboard commands. F1-Help will display a help message for the current screen

The Main Menu: Modem communication may be scheduled to run at a time when the machine is unattended. The main menu must be on the display for this scheduled transmission to take place.

Most functions of the program are disabled until PASSPORT has been properly configured. The next several sections review the configuration for a simple setup.

## Originating Site

### Entering Originating Site Information

Once the software is installed, specify the originating site information. The first site entered should be the user's own location. Any number of subsequent originating sites may be entered.

When the MAIN MENU | SETUP MENU | ORIGINATING SITES option is selected, a list of previously specified originating sites will be displayed. Use the F3-Add key to create a new originating site. Enter data using the originating site data entry screen.

Figure 030-3 - Originating Site Data Entry Screen

Data Entry Fields for Originating Site Data Entry Screen

| Field Name | Values/Validation | Description |
| --- | --- | --- |
| Origin ZIP + 4 | Specify a unique 9 digit ZIP code for the originating site. | If more than one originating site exists for a given ZIP+4, specify any unique ZIP+4 to identify the site, then enter the mailing ZIP+4 in the address detail lines |
| Site Name | The site name may be any text at least 5 characters long. | Specify the originating site name |
| Requestor Code (REQ. CODE) | The Mailer version of PASSPORT only allows the creation of Mailer Origin Sites. This field is display only. | The requestor code will determine the product codes and CIN's available for ordering and printing. Enter the correct requestor code for each site. |
| Finance Number | This field is not used in the Mailer version. | The finance number is only available for Postal facilities |
| Address Detail Lines (ADDR1-ADDR6) | Specify the mailing address for the originating site. The address must contain at least 3 lines and the last line must be in the form: CITY ST ZZZZZ-ZZZZ | The state must be one of the postal standard 2 character abbreviations and the ZIP code must be the facility's correct ZIP+4. |
| Contact | The contact name must be any text at least 5 characters long | Specify the name of the person to contact regarding questions about label orders. |
| Bottom Label Line | Must contain valid text at least 5 characters long | Enter oringinating site location information in this field. Each label produced for the site will include this text. The DMM specifies that this should contain facility name and location. Abbreviations may be required, and a ZIP+4 is recommended, |

Originating Site ZIP + 4: While it is preferred that the origin ZIP+4 match the mailing ZIP+4, this is not required. Specifically, a Postal site may wish to create multiple origin sites for itself, each with a different ZIP+4 appearing on the label, but maintain one mailing address ZIP+4.

## PASSPORT Site

### Specifying the Primary PASSPORT Site

Once at least one originating site is setup, a primary originating or PASSPORT Site is specified. Use MAIN MENU | SETUP MENU | PASSPORT SITE option to specify one of the previously entered originating sites as the passport site. To select one of the originating sites, specify a site in the Office Number field. A popup of available sites is available by entering a '?' in the field.

Figure 030-4 - PASSPORT Site Data Entry Screen

## Ordering Configuration - Registering with Topeka

Use the MAIN MENU | SETUP MENU | ORDERING CONFIGURATION menu choice to access the ordering configuration screen.

The ordering configuration specifies the hardware to be used for report printing and communication to the PASSPORT BBS’s. Once the data entry fields are completed, the user must register with the Topeka LPC by pressing the Alt-F10 keyboard command.

Problems with communication are usually caused by an error in the Modem Port or Modem IRQ specification. See the Troubleshooting section for solutions to common problems.

Figure 5 -Ordering Configuration Data Entry Screen

Data Entry Fields for Ordering Configuration

| Field Name | Values/Validation | Description |
| --- | --- | --- |
| Printer Type | Supported Label Printer | Specifies the the label printer for locally printed labels. |
| Printer Port | This field is display only. | This field is fixed to the COM1: port except for the HP LaserJet where the printer port is specified in HP3.INI. |
| Modem Port | I/O Port name. Choose one of the available serial (COM) ports | The user must determine the value for this entry based on the modem’s hardware configuration. |
| Modem IRQ | Interrupt Request Number must be specified. | Autoselects the default IRQ for the specified Modem Port. May be changed as needed based on modem’s hardware configuration. |
| Modem Type | Select from popup list or leave the entry blank | A list of supported modems is provided. Use PASSPORT Default for a modem not listed. |
| Modem Initialization String | If an initialization string is required by your modem, it must be entered here | Automatically entered for supported modems. User may edit or create new string as needed. Check modem hardware manual. |
| Label Order Phone Number | Enter the number to dial to reach the Topeka Label Printing Center | If a 9 must be dialed to access an outside line, enter a 9 and a comma at the start of the phone number |
| Software Order Phone Number | Enter the number to dial to reach the Raleigh IBSSC BBBS | If a 9 must be dialed to access an outside line, enter a 9 and a comma at the start of the phone number |
| System ID | A value must be entered here | If a site has multiple PASSPORT computers, different System ID’s should be used on each. Otherwise, enter an A here. |

## Software Upgrades

It is critical that PASSPORT produces labels that meet current Postal Regulations for content and format. For this reason, PASSPORT ensures that the user is running the latest release of the software. Upgrades are freely available via modem. Use the MAIN MENU | UPDATE SOFTWARE/TABLES MENU | GET UPDATE to access the Raleigh Bulletin Board System and download an upgrade.

The amount of time required for downloading an upgrade is determined by the size of the upgrade and the speed of the user's modem. The communication may be scheduled for sometime when the PASSPORT machine is unattended if necessary. If you have scheduled an upgrade but would like to cancel the communication, use the F2-Cancel keyboard command. Otherwise, PASSPORT will continue to try to get the upgrade each time you start the system.

Each time the system connects to a BBS for label ordering, sending a message to PASSPORT Central, or getting an update, the software checks for a new release. If no communication is made for more than a month, PASSPORT reminds the user to check for an update. PASSPORT will disable label ordering and printing functions if the upgrade is not downloaded and applied when required.

## Label Products

All labels ordered must have a specific product code assigned. The available product codes are listed below.

| Product Code | Product Description | Available for Mailer Sites | Available for Postal Sites |
| --- | --- | --- | --- |
| A1 | Bulk Strip Foreign Blue | Yes | Yes |
| A2 | Bulk Strip Foreign Orange | Yes | Yes |
| A9 | Bulk Strip White | Yes | Yes |
| AN | Bulk Strip Pink | Yes | Yes |
| AP | Mini-Bulk Strip Pink | Yes | No |
| AW | Mini-Bulk Strip White | Yes | No |
| B1 | Bulk Large Foreign Blue | Yes | Yes |
| B2 | Bulk Large Foreign Orange | Yes | Yes |
| B9 | Bulk Large White | Yes | Yes |
| BN | Bulk Large Pink | Yes | Yes |
| BP | Mini-Bulk Large Pink | Yes | No |
| BW | Mini-Bulk Large White | Yes | No |
| E9 | Collated Strip White | Yes | Yes |
| EN | Collated Strip Pink | Yes | Yes |
| F9 | Collated Large White | Yes | Yes |
| FN | Collated Large Pink | Yes | Yes |

Table 1 - Product Code Table

Different product codes are used for collated set orders versus bulk orders

Pink labels are used only for periodical and news mail types.

Blue labels are to be used for trays or sacks of international printed matter.

Orange labels are used for PER/NEWS to Canada.

### Tray Labels

Products in the table designated ‘Large’ are used to label mail trays. The Domestic Mail Manual provides complete details on the size and form of tray labels.

Figure 6 - Tray Label

### Sack Labels

Labels designated as ‘Strip’ are used to label mail sacks. The labels are smaller and contain fewer text fields. In addition, the barcode consists of only 8 digits.

Figure 7 - Sack Label

### Pink, Blue, and Orange Label Products

Often these other products are printed on an infrequent basis by the LPC. Some are printed quarterly or annually. Please contact the LPC regarding when such an order would be fulfilled.

## Label Data

Figure 8 - Label Fields

### Bottom Label Line - Originating Site

Line 3 on tray and sack labels contains the office of mailing or mailer information line. This line must show the entry post office or the mailer’s name and location. PASSPORT provides a data entry field designated Bottom Label Line for each originating site. Since the field is limited to 26 characters, abbreviations may be needed to provide the information required. The ZIP plus 4 should be used to uniquely identify the originating location.

### Destination

All labels printed or ordered for Postal originating sites and all automation rate labels for Mailer sites must include complete destination information. For some of the sortation levels, popups are provided with valid destinations listed. In the case of destination-based lists, a two column popup is available. The left column lists facility destinations, the right column lists ZIP code ranges to be processed by each facility.

The destination ZIP code is printed in the upper right corner of the label. The destination text line is referred to as the 'Top Label Line,' because it is the first text field required on the label according to the DMM.

The first 5 digits of the barcode are the destination ZIP.

### Content Identification Number

The Content Identification Number (CIN) is a 3 digit code and a text field printed on the label to indicate several pieces of information about the mail in the labeled container:

Mail Processing Code, specifies the Barcode Status of the mailpieces

Sortation Level, DMM list for mailers

Type or shape of Mail

Class of Mail

PASSPORT helps the user specify the correct Content ID to use by providing popup lists that act as a decision tree. Each popup list only provides values that are valid for the previously specified parameters. Once the MP Code/Sort/Class and Type are specified, a list of valid CIN’s is available in a popup list. As an alternative to the decision tree, the user may specify the CIN directly, but will then be prompted to select a valid combination of MP Code/Sort/Class and Type for that CIN.

The text description for the CIN is referred to as the 'Second Label Line,' because it is printed on the second DMM required text line.

The text field for certain CIN’s may be completely or partially overwritten for certain CIN’s.

The 3 digit CIN is used for digits 6-8 of the barcode field.

### Barcode

Tray labels have a 10 digit Interleaved 2 of 5 barcode. Sack labels only use the first 8 digits. The first 5 digits of the barcode are the destination ZIP. The next 3 digits are the Content Identification Number. The ninth digit specifies a delivery day requirement, which will always be zero for Mailer labels. The last digit is the Mail Processing Code.

| Delivery Day (Ninth Digit) |  | MP Code (Tenth Digit) |  |
| --- | --- | --- | --- |
| 0 | No Delivery Day |  | 1 | Automation |  |
|  |  |  | 7 | Mixed or Unknown |  |

Figure 9 - Barcode Ninth and Tenth Digit Values

### Human Readable Barcode Data

This field displays the 8 or 10 numeric characters that makes up the barcode.

Note: PASSPORT does not print a HR barcode value on Sack Labels.

### Zebra Stripe

If the mailpieces in the container have destination point barcodes printed on each, then the zebra stripe will be printed on the label. The user does not specify whether this will appear on the label. The CIN dictates whether a zebra stripe will be printed.

## Introduction to Label Ordering

Label ordering is a three step process:

Define label order header and detail data

Prepare label order into batch for transmission

Transmit batch to Topeka Label Printing Center

Use the MAIN MENU | LABEL ORDERING MENU to access these functions.

Label orders are either temporary or collated set orders. A temporary order results in one order of labels shipped to the originating site each time an order is placed. Bulk orders are temporary orders. DMM Set orders are a special type of bulk order with destination information provided by PASSPORT based on the standard label lists provided in Section L of the DMM. Collated sets result in continuing, regular shipments from the LPC.

## Bulk Label Ordering

Use the MAIN MENU | LABEL ORDERING MENU | ORDER ENTRY MENU (PS FORM 1578-B) | BULK LABELS to create or edit bulk label orders.

You may add a new order by pressing F3-Add, modify an order by pressing F4-Chg, delete or recall an order by pressing F5-Del/Rcl, view a previous page (if any) of orders by pressing PgUp, view the next page (if any) of orders by pressing PgDn, or quit by pressing ESC-Quit.  The F1-Help key is available for help.

If no orders currently exist, selecting either F3-Add or F4-Chg will advance you to a screen where an order can be added.

Pressing F4-Chg while on a selected order will allow you to edit that order by advancing you to the Bulk Label Edit screen.  This option will only function with non-deleted orders.

You may delete an order by selecting the order and pressing F5-Del/Rcl.  When prompted to confirm deletion, press F10-Process.  A deleted record is one that has a small solid white dot to its left.

You may recall a previously deleted order by selecting the order and pressing F5-Del/Rcl.  When prompted to confirm the recall, press F10-Process.

You can recall a previously Transmitted Order by pressing Alt-F3, the History option.  This will advance you to the Add Bulk Orders screen described later in this section.

You can copy an existing order by moving the highlight bar to the order you wish to copy and pressing F8.  This will advance you to the Add Bulk Labels screen described later in this section.

Figure 10 - Bulk Order Header Data Entry Screen

This screen is used to add and process a new, copied, or retrieved from history bulk label order header and may be accessed by selecting F3-Add from the Bulk Order Header Selection Screen

If you are copying an existing order, at this point you can change the Bottom Label Line, or press F4-Chg to change the Originating Site for whom you wish to place the order.  You may change to another Originating Site only if it has the same Requester Code as the original order.  Press F10-Process to process the data.

If you are retrieving from history, enter the origin ZIP of the Originating Site whose order you wish to retrieve.  A popup will appear listing past orders which have been previously transmitted for that site.  Select the order you wish to copy.  After selecting the order, you can change the Bottom Label Line, or press F4-Chg to change the Originating Site for whom you wish to place the order.  You may change to another Originating Site only if it has the same Requester Code as the original order.  Press F10-Process to process the data.  As history details are retrieved, their destination ZIP Codes and MP Code, Sort, Class and Type are tested against current DMM requirements.  If any labels are invalid, a popup will be displayed allowing the user to select current values.

All fields on this screen are required.  Once the data is entered, you may press F10 to process and advance Bulk Order Detail Data Entry Screen.

Data Entry Fields for Bulk Order Header Data Entry Screen

| Field Name | Values/Validation | Description |
| --- | --- | --- |
| Origin ZIP | Field must contain a valid defined originating site. A popup of defined originating sites is available | Specifies the originating site ZIP +4 to be used on the printed labels. Define originating sites under Originating Site Setup |
| Bottom Label Line | Use the default value or enter a different value to be printed on each label in this order | This is the text for the bottom label line which will be printed on the labels. |
| Requester Code | Field will always contain “M”. This is entered by PASSPORT for the selected originating site. | This field is display only |
| Product Code | Field must contain a valid product code. A popup list is available | This is the product code for the label order. If retrieving an order from history, you may be forced to change the product code if it is no longer valid. |

Figure 11 - Bulk Order Detail Data Entry Screen

This screen will be displayed after pressing F4-Change from the Bulk Order Header Selection Screen, or pressing F10-Process after adding a header. Bulk order detail lines are edited here. Each detail line represents one label definition. An order may have any number of order detail lines.

You may press ESC-Quit to abandon the order and return to the Bulk Order Header Selection Screen.  Pressing F1-Help will activate the Help screen.

The top part of the screen displays the header information for the order which is being modified.

To clear the current field, press F2-Clr.  To insert a record above the currently highlighted record, press Alt-F3-Ins.  Pressing F5-Del will delete the current record.  Once deleted, this record cannot be recalled.

Pressing F3-Add will append a record to the bottom.  This new record will be completed with the same data as the currently highlighted record.

Each time a detail line is added, or when Alt-F9-Defaults is pressed, a window will appear displaying the currently selected mail processing code, sortation level, mail class and type. The current CIN and description is also given in this decision tree window. Use the popup lists for each field to select valid values. Press F10-Process to save the current settings. Press Ctrl/F10 to save the current settings, and disable or enable the automatic popup of this window each time a record is added. Pressing Alt-F9-Defaults will still present the decision tree window.

Data Entry Fields for Bulk Order Detail Data Entry Screen

| Field Name | Values/Validation | Description |
| --- | --- | --- |
| Qty | Must contain a valid quantity. Minimum, maximum and quantity increments are dictated by product code | Specifies the number of labels to be ordered using the current label definition. Most allow 300 minimum in increments of 300. Mini-Bulk products allow 25 minimum in increments of 25, up to a maximum of 575 |
| Destination ZIP | Field must contain a valid 3 or 5 digit non-zero destination ZIP for any order from a Postal originating site, or for automation rate CIN’s for mailers. Popup lists are available for some Sortation Levels. | Specifies the destination ZIP code for the mailpieces in the labeled container. The ZIP code is used for the first 5 digits of the barcode on the label. |
| Destination | Field must contain a valid destination description. For destinations included in a Popup list, this entry is made by PASSPORT | This is the text for the destination ZIP. It may also be used for PO Box information for firm direct mail. |
| CIN | Field must contain a valid Content Identification code. A popup list is available | Press the Alt-F9 keyboard command to access the MP Code/Sort/Class ant Type Decision Tree window |
| CIN Description | Field must contain the text description for the current CIN. | Some CIN’s allow editing of all or part of this field. To see which characters may be overwritten, access the Decision Tree Window. Characters displayed on a green background may be modified by the user |
| Status? | Display only field that indicates whether the label detail line is complete (will produce a barcoded label) | Only detail lines marked OK will be transmitted to Topeka for Automation rate CINs. If the NoBC value is displayed, check that there is a valid destination and CIN. |

## DMM Label List Ordering

A second type of temporary order is the DMM label list order. This order is similar to the bulk order, having a single header record and some number of detail lines for each order. The difference is that the destination information is supplied by PASSPORT based on current DMM label list standards. Detail lines may be deleted so that a subset of the specified DMM list can be ordered.

NOTE: The Topeka LPC has an option to order “DMM Sets.” PASSPORT, however, does NOT make use of this feature. Instead, PASSPORT creates and sends Topeka BULK ORDERS that mirror the DMM Label Lists. If you call the LPC concerning a Label List order, do not mention that this is a DMM Set order or confusion could arise. Simply inquire about your BULK order.

The Label List Order Selection Screen offers functions for adding new orders (F3-Add), modifying an existing order (F4-Chg), and deleting/recalling orders ((F5-Del/Rcl). The PgUp, Up Arrow, PgDn, and Down Arrow keyboard commands may be used to scroll through the list of pending orders. F8-Copy allows an order to be copied and modified separately. Use the Esc key to exit this screen.

Data Entry Fields for DMM List Order Header Data Entry Screen

| Field Name | Values/Validation | Description |
| --- | --- | --- |
| Origin ZIP | Field must contain a valid defined originating site. A popup of defined originating sites is available | Specifies the originating site ZIP +4 to be used on the printed labels. Define originating sites under Originating Site Setup |
| Bottom Label Line | Use the default value or enter a different value to be printed on each label in this order | This is the text for the bottom label line which will be printed on the labels. |
| Requester Code | Field will always contain “M”. This is entered by PASSPORT for the selected originating site. | This field is display only |
| Product Code | Field must contain a valid product code. A popup list is available | This is the product code for the label order. This field is view only if you are copying an order or retrieving an order from history. |

Once an order is added or selected for change, the DMM List Order Detail Screen, the following data fields are displayed:

Data Entry Fields for DMM List Order Detail Data Entry Screen

| Field Name | Values/Validation | Description |
| --- | --- | --- |
| Qty | Must contain a valid quantity. Minimum, maximum and quantity increments are dictated by product code | Specifies the number of labels to be ordered using the current label definition. Most allow 300 minimum in increments of 300. Mini-Bulk products allow 25 minimum in increments of 25, up to a maximum of 575 |
| Destination ZIP | A detail line for each destination ZIP in a selected label list is generated. This field may not be edited | The label list used to generate these values is specified when the user enters the Sortation level (Sort) on the CIN Decision Tree window. |
| Destination | Field is completed by PASSPORT, based on the selected DMM Label List. The field may not be edited | The label list used to generate these values is specified when the user enters the Sortation level (Sort) on the CIN Decision Tree window. |
| CIN | Field must contain a valid Content Identification code. A popup list is available | The MP Code/Sort/Class and Type Decision Tree window is presented when an order is added. |
| CIN Description | Field contain the text description for the current CIN. It may not be edited | The standard CIN text description is provided by PASSPORT |
| Status | Display only field that indicates whether the label detail line is complete (will produce a barcoded label) | Only detail lines marked OK will be transmitted to Topeka. |

## Collated Set Orders

A collated set order, unlike bulk and DMM label list orders, is a permanent order. The order details result in 14 sets (multiplied by the set quantity requested) of labels produced every two weeks until it is deleted. Because existing orders are maintained on file with the Topeka Label Printing Center, the label ordering functions in PASSPORT allow you to enter changes to sets on file. Each change, or order transaction, has a header record and detail lines.

When the MAIN MENU | LABEL ORDERING MENU | ORDER ENTRY MENU (PS FORM 1578-B) | COLLATED SET LABELS is selected, the Collated Set Header Selection Screen is displayed.  From this screen, the user may press F3-Add to create a new collated set order transaction. Alt-F4 allows changes to the transaction header, F4-Chg is used to change the details of a pending order transaction. F5-Del/Rcl is used to delete or recall a pending order transaction. The PgUp, Up Arrow, PgDn, and Down Arrow keyboard commands may be used to scroll through the list of pending order transactions.

When a new order change is added (F3-Add) or the header record is chosen for change (Alt-F4), the Collated Set Order Header Data Entry Screen is displayed. The fields in this screen are listed below:

Data Entry Fields for Collated Set Order Header Data Entry Screen

| Field Name | Values/Validation | Description |
| --- | --- | --- |
| Origin ZIP | Field must contain a valid defined originating site. A popup of defined originating sites is available | Specifies the originating site ZIP +4 to be used on the printed labels. Define originating sites under Originating Site Setup |
| Bottom Label Line | Use the default value or enter a different value to be printed on each label in this order | This is the text for the bottom label line which will be printed on the labels. |
| Requester Code | Field will always contain an “M”. This is entered by PASSPORT for the selected originating site. | This field is display only. |
| Product Code | Field must contain a valid collated set product code. A popup list is available. | The product code entered here on the transaction header must match the product code entered when the collated set was initially transmitted to the LPC. |
| Set Number | The set number is a 3 digit identifier for the collated set. | The set number, originating site and product code are considered together to uniquely specify the set to which the changes in this transaction will be applied |
| Activity Code | Valid entries are: ‘U’ for update, ‘D’ for delete and ‘N’ (Mailer sites only) to create a new set. Postal sites should use Scheme maintenance to create new collated sets. | The type of change to be made to the specified collated set. If a set is being deleted, |
| Set Quantity | Number of sets required daily. Valid entries are from 0 to 99 | To temporarily suspend shipment of a particular collated set, enter a 0 in this field |
| Revision Date | This field is view only on this screen. It can be modified or simply confirmed in a sub-screen upon pressing F10 to process. | The date of the last revision to the current collated set. If the collated set was not issued using PASSPORT originally, a window will be displayed and the user must enter the Last Revision Date for the set. That is found on the stack header label on the last order received from Topeka. The user also has to enter the highest address number, or number of labels in the order. |
| Stack Header Label Lines | 3 lines of text that will appear on the header label of the current set | This text is used to on the stack header label and does not affect the labels to be used for mail container labeling |

Once the data for the Collated Set Order Header Data Entry Screen is entered, the Collated Set Order Detail Data Entry Screen is displayed, unless the activity code for the current transaction is ‘D’ for delete. First the CIN Decision Tree Window is displayed. Enter values in the MP code, sort, class and type fields, then specify the CIN to use on the first detail line.

Data Entry Fields for Collated Set Order Detail Data Entry Screen

| Field Name | Values/Validation | Description |
| --- | --- | --- |
| Operation Code (OP CD) | Valid entries are: Add Copy Delete Move Update | Specifies the operation to be performed to change the current address line from what is stored on file in Topeka to what the revised line should be |
| Address Number (ADR NO) | Specify a valid address line number that is currently on file with the LPC | This field is unavailable if the operation code is ‘Add’ |
| New Address Number (NEW ADR) | Specify a valid address line number. | The address number will be changed to the new address number. |
| Quantity (QY) | Enter a valid detail quantity | Specifies the number of labels with the current detail to be printed after the transaction is applied to the order on file |
| ZIP | Enter the Destination ZIP code here. The ZIP must be valid for the current CIN | This field is only required if a change is to be made to the ZIP on file for the current detail address number |
| Destination | Enter valid destination description for the current address line | This field is only required if a change to be made to the destination on file for the current detail address number |
| CIN | Valid Content Identification Number | Use the CIN Decision Tree Window to specify the CIN. Press Alt-F9-Defaults to change the current MP code, sort, class and type then change the CIN as needed. |
| Description | Field must contain the text description for the current CIN. | Some CIN’s allow editing of all or part of this field. To see which characters may be overwritten, access the Decision Tree Window. Characters displayed on a green background may be modified by the user |

## Label Order Preparation

The second step in the label ordering process is to prepare the orders into batches for transmission to the Topeka LPC. Choose MAIN MENU | LABEL ORDERING MENU | TRANSMIT MENU | PREPARE ORDERS to prepare orders.

If print schemes maintained in Topeka have been defined or modified (using Scheme Maintenance under the Label Printing Menu) there will be a listing presented here. The user must specify which of these print scheme orders are to be prepared into the current batch.

Before preparing the batch, an information screen is displayed, describing the process. You may press ESC-Quit to cancel the process, or F10-Process to prepare the batch transmission file

Once batch preparation is complete, the report screen is displayed. Verify that the number of orders, number of labels and the number of 8131 (changes to originating site data) are accurate. Record the batch number for future reference.

Figure 12 - Prepare Batch Process Report Screen

## Transmitting a Label Order to the Topeka Label Printing Center

The last step in the order process is to transmit the prepared batch to the Topeka LPC. Use the  MAIN MENU | LABEL ORDERING MENU | TRANSMIT MENU | SCHEDULE TRANSMISSION function to schedule transmission. Enter the date and time to begin transmission, or press the Alt-F10 keyboard command to begin transmission immediately.

Orders are processed by the LPC at the close of the day on the day when the order is received. The user should receive the label order within 2-3 weeks after transmission. Problems with the order will result in the labels not being printed.

## Retransmit Orders

The Retransmit Orders screen is used to restore previously transmitted batches to a state suitable for transmitting again.

This feature is intended to re-transmit orders that were once successfully transmitted, but, for some reason, never processed by Topeka.  For this reason, all internal dates, batch numbers, and transaction codes are left intact when they are re-transmitted.

DO NOT USE THIS FEATURE IF ALL YOU WANT IS ANOTHER COPY OF SOME PREVIOUS ORDER - USE “COPY FROM HISTORY” INSTEAD

## View/Delete Prepared Batch

Once a batch has been prepared, it is assigned a batch number. The batch number begins with an “M” for mailers. The batch may be reviewed or deleted using MAIN MENU | LABEL ORDERING MENU | TRANSMIT MENU | VIEW/DELETE PREPARED BATCHES. For more detailed information on a batch, use the MAIN MENU | LABEL ORDERING MENU | REPORTS MENU function.

When a batch is deleted, the orders revert to pending, or unprepared status. To delete the order data, the order entry functions must be used after batch deletion.

## Reports Menu

PASSPORT offers report features to allow review of label orders, prepared batches and originating sites. Use MAIN MENU | LABEL ORDERING MENU | REPORTS MENU to access a variety of report functions.

### Order Status

Order status is displayed with the option MAIN MENU | LABEL ORDERING MENU | REPORTS MENU | ORDER STATUS.

### Originating Sites

Originating sites is displayed with the option MAIN MENU | LABEL ORDERING MENU | REPORTS MENU | ORIGINATING SITES.

### Batch Transactions

Batch transaction data is displayed with the option MAIN MENU | LABEL ORDERING MENU | REPORTS MENU | BATCH TRANSACTION.

### Collated Set List

Batch transaction data is displayed with the option MAIN MENU | LABEL ORDERING MENU | REPORTS MENU | COLLATED SET LIST. This only lists collated sets entered using the Label Ordering Menu.

## Mailer Version Label Printing

The mailer version of the PASSPORT Software has an on-demand label printing function. Choose MAIN MENU | LABEL PRINTING MENU | PRINT LABELS to use this option. One of the supported label printers must be attached to the PASSPORT system. When first used, or when formats change, the download printer formats option must be executed.

### Download Printer Formats

Most of the label printers supported by PASSPORT require that a printer format be downloaded prior to printing any labels. The printer will retain this format information even after the power is turned off. If a new printer is added, or if the printer formats  are lost, the formats will have to be downloaded. If the label format changes due to a software upgrade, PASSPORT will notify the user that formats must be downloaded to the printer.

To download printer formats, choose MAIN MENU | LABEL PRINTING MENU | DOWNLOAD PRINTER FORMATS

### Printing Labels

Figure 13 - Label Printing Screen for the Mailer Version

The label printing screen for mailers has 2 parts. The top identifies the originating site and the Content ID, The bottom specifies the destination and label count information.

F1-Help displays the online help screen. F2-ClrFld clears the current data field. Press F7 when the label has been defined. The label will be printed to the label printer specified in the MAIN MENU | SETUP MENU | ORDERING CONFIGURATION option.

Alt-F7 imports and prints a space delimited format (SDF) data file. The data file should contain one record for each label definition.

F9 moves the cursor from the destination information at the bottom of the screen to the CIN information at the top. Press F10 to move from the CIN fields to the destination fields.

### This Section is left intentionally blank.

## SDF Data Import

While on the Mailer Version Print Screen, the user can hit Alt-F7. This will bring up a dialog window to select an import file. This file should have an extension of DAT or TXT and have the following format:

ASCII, fixed field length, CR or CR/LF ends each record

Field	Field	Field

Loc	Size	Description		Comments

01-03	03	Bin# (optional)		If provided, prints above ZIP in top right

04-24	21	Destination

25-29	05	ZIP			3 or 5 digits left justified

30-50	21	Description

51-53	03	CIN #			Desc and CIN should match

54	01	Mail Piece BC Status	B-Barcoded, U-Upgradable, N-Nonbarcoded.

(optional on sacks)	  B and U are for automation rate mail

55-56	02	Quantity			i.e. number of copies of label

57	01	Label Format		T-Tray (Large), S-Sack (Strip)

58-83	26	Origin Line		Who Prepared Tray/Sack, should contain ZIP+4

as minimum

84-99	16	Scheme Name (optional)	ID name for the label set/file

## Product Code Table

Select MAIN MENU | SETUP MENU | CUSTOMIZING TABLES MENU | PRODUCT CODE TABLE to list Label Product Codes.

This table lists available label Product Codes (see Section 040). The list may be printed using the F6-Print keyboard command.

## Mail Type (Content Identification Number) Table

The Mail Type (CIN) Table provides a listing of the CIN values to use when specifying labels in PASSPORT.

Select MAIN MENU | SETUP MENU | CUSTOMIZING TABLES MENU | MAIL TYPE (CIN) TABLE to list CIN Codes. F6-Print will send a report listing to the printer.

Figure 14 - Mail Type (CIN) Table

The first column tells whether the CIN is available for Postal site ('P'), mailer sites ('M'), or both ('   '). The next column is the 3 digit CIN. The next field is the text description for the CIN. The remaining 2 fields determine whether the CIN requires a zebra stripe and delivery day to be printed on the label.

When printing this list, there are 4 options. The first option, CIN List, provides a printed list of the table as it is displayed. The only other available option provides a detailed lists of CIN's for Mailer use. This reports specifies the required Product Code, MP Code, Class and type required.

Each supported label printer may need special hardware and software configuration. Refer to this appendix for instructions on configuring the printer to use with PASSPORT.

## Intermec 3000A

The Intermec 3000A label printer is configured by setting DIP switches on the printer. There are two groups of switches located on the rear of the printer near the AC power cord connector and the RS-232 interface connector. The top group has 8 switches and just below that is a group of 4. These switches should be set as follows:

Note -Switch number 1 is located at the top of the DIP switches. The switches are labeled on the printer for easy identification.

| Switch Number | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Setting | Off | Off | Off | Off | Off | Off | Off | Off | Off | Off | On | Off |

Table 2 - Intermec 3000A DIP Switch Settings

## Intermec 3400

The Intermec 3400A label printer is configured by setting DIP switches on the printer. There are two groups of switches located on the rear of the printer near the AC power cord connector and the RS-232 interface connector. The top group has 8 switches and is labeled ‘TOP’. Below that is another group of 8 switches labeled ‘Bottom’. Set the switches according to the following tables:

Note -Switch number 1 is located at the top of the DIP switches. The switches are labeled on the printer for easy identification.

| Switch Number | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Setting | On | Off | Off | Off | Off | Off | Off | Off |

Table 3 - Intermec 3400A TOP DIP Switch Settings

| Switch Number | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Setting | Off | Off | Off | Off | Off | On | Off | Off* |

Table 4 - Intermec 3400A BOTTOM DIP Switch Settings

NOTE: If thermal stock is to be used, BOTTOM DIP Switch 8 must be set ‘Off.’ If non-thermal label stock will be used, set the BOTTOM DIP Switch 8 to ‘On,’ and install a thermal transfer ribbon.

## Microcom 410 ECA

This printer has no manual setup features. All configuration changes must be sent via serial communications. PASSPORT has provided an automated means to configure the Microcom 410 printer for an Entry-Level setup. If these printers are to be used in a Standard-System, the user must first connect the printer to the COM1: port of another computer (PASSPORT does not need to be loaded, only the four files listed below) using an Entry-Level Serial cable described in Appendix C.

Use the following procedure to setup the Microcom 410 ECA printer for use with PASSPORT:

At the DOS Prompt, change to the EXE directory by typing CD\CAA.V01\EXE <enter>

Run the batch file included with PASSPORT by typing MC410SET <enter>. Follow the instructions on-the screen for resetting the printer to Default Mode.

Once the setup program completes, the printer will print a test pattern label. Turn off the printer after this is printed.

The printer is now ready for use with PASSPORT

If the printer is to be setup using a computer without PASSPORT installed on it, follow these steps:

Copy the following files from a PASSPORT computer to a floppy disk:

C:\CAA.VØ1\EXE\CAA6Ø5B.EXE

C:\CAA.VØ1\EXE\BRT71EFR.EXE

C:\CAA.VØ1\EXE\MC41ØSET.BAT

C:\CAA.VØ1\EXE\MC41ØSET.DAT

Insert the floppy in the drive and make that drive the current drive by typing: A: <enter>, or B: <enter>

Type MC410SET <enter> and follow the on-screen instruction for resetting the printer to Default Mode.

Once the setup program completes, the printer will print a test pattern label. Turn off the printer when this is printed.

The printer is now ready for use with PASSPORT

## Monarch 9425

The Monarch 9425 is configured using the keypad attached to the printer to change settings using the menu system. Access the configuration menus by pressing the F2 key on the printer keypad. The password default is ONLINE.

To scroll to the next or previous menu item, use the ( or ( key. So select a menu item or change the value of the menu item, press the Enter key. Once a menu item has been selected, you may scroll through the available values using the ( or ( keys.

Select Operating Mode

Data Entry		PASSPORT does not use entries in this menu

Format Entry	PASSPORT does not use entries in this menu

Batch Control	PASSPORT does not use entries in this menu

Online			Select this item to exit configuration and return to Online Mode Ready

Printer Options

Use Batch Separators (Y/N)	N

Adjust Cut Position

Cut Adjustment (I/D)	I

Adjust Cut Position	0

Adjust Print Position

Print Adjustment (I/D)	I

Adjust Print Position	0 (This value may need to be changed to position label printing on the label)

Define Cost Code	PASSPORT does not use entries in this menu

Entered Char	blank

Printed Char	blank

Define Supply Type	B or D depending on supply type being used. Black Mark stock has a black indicator mark on each label. Die cut stock has indentations on the edges or apertures through the middle of the stock. Use the Align function if printing is not aligned properly on the labels

Define Monetary Symbol	PASSPORT does not use entries in this menu

Select Monetary Symbol	dollar

Use Cent Sign in Price Fields	PASSPORT does not use entries in this menu

Use Cent Sign where applic.	N

Define Numbering System	PASSPORT does not use entries in this menu

Select Numbering System	English

Define Print Mode	<Command Not Available>

Use Batch Names	PASSPORT does not use entries in this menu

Use Batch Names	N

Printer Configuration	PASSPORT does not use entries in this menu

Define Check Digit Schemes

CD Scheme Number (1-12)	1

CD Calculation Method	A

CD Modulus (2-11)	10

Number of Data Digits	10

Weights for each position	7137137131

Change Password(s)	Use this option only if there is a problem with unauthorized access to these configuration menus. Once set, keep you password safe. If you forget your password, you must contact the printer manufacturer

Enter Old Password	<old password>

Enter New Password	<new password>

Display Password

Password(s)	Displays password for subordinate printer modes

Set Time	Note that PASSPORT prints the system time from the computer, not the printer.

Enter New Time	<hh:mm:ss>

Set Date	Note that PASSPORT prints the system date from the computer, not the printer

Enter New Date	<mm/dd/yy>

Set Date Format	PASSPORT does not use entries in this menu

Select a Date Format

Host Port Configuration	IMPORTANT - The entries in this menu determine how PASSPORT will communicate with the printer. They must be set as specified here, or Syntax and Framing or other error messages will appear on the printer.

Select Baud Rate	9600

Select Parity	E

Enter Word Length (7-8)	7

Enter Stop Bits (1-2)	1

Enter Start (XON) Char	128

Enter Stop (XOFF) Char	128

Clear Batch Memory at power-up

Clear batches at power-up	E

9420/9440 Compatible Mode

9420/9440 Compatible Mode	D

9420/9440 Imaging Mode

9420/9440 Imaging Mode	D

Enhance Paper Handling Mode

Enh. Paper Handling Mode	E

Auto Online Mode

Auto Online Mode	E

Version

## Monarch 9445

The Monarch 9445 is configured using the keypad attached to the printer to change settings using the menu system. Access the configuration menus by pressing the F2 key on the printer keypad. The password default is ONLINE.

To scroll to the next or previous menu item, use the ( or ( key. So select a menu item or change the value of the menu item, press the Enter key. Once a menu item has been selected, you may scroll through the available values using the ( or ( keys.

Select Operating Mode

Data Entry		PASSPORT does not use entries in this menu

Format Entry	PASSPORT does not use entries in this menu

Batch Control	PASSPORT does not use entries in this menu

Online			Select this item to exit configuration and return to Online Mode Ready

Printer Options

Use Batch Separators (Y/N)	N

Adjust Cut Position

Cut Adjustment (I/D)	I

Adjust Cut Position	0

Adjust Print Position

Print Adjustment (I/D)	I

Adjust Print Position	0 (This value may need to be changed to position label printing on the label)

Define Cost Code	PASSPORT does not use entries in this menu

Entered Char	blank

Printed Char	blank

Define Supply Type	B or D depending on supply type being used. Black Mark stock has a black indicator mark on each label. Die cut stock has indentations on the edges or apertures through the middle of the stock. Use the Align function if printing is not aligned properly on the labels

Define Monetary Symbol	PASSPORT does not use entries in this menu

Select Monetary Symbol	dollar

Use Cent Sign in Price Fields	PASSPORT does not use entries in this menu

Use Cent Sign where applic.	N

Define Numbering System	PASSPORT does not use entries in this menu

Select Numbering System	English

Define Print Mode	<Command Not Available>

Use Batch Names	PASSPORT does not use entries in this menu

Use Batch Names	N

Printer Configuration	PASSPORT does not use entries in this menu

Define Check Digit Schemes

CD Scheme Number (1-12)	1

CD Calculation Method	A

CD Modulus (2-11)	10

Number of Data Digits	10

Weights for each position	7137137131

Change Password(s)	Use this option only if there is a problem with unauthorized access to these configuration menus. Once set, keep you password safe. If you forget your password, you must contact the printer manufacturer

Enter Old Password	<old password>

Enter New Password	<new password>

Display Password

Password(s)	Displays password for subordinate printer modes

Set Time	Note that PASSPORT prints the system time from the computer, not the printer.

Enter New Time	<hh:mm:ss>

Set Date	Note that PASSPORT prints the system date from the computer, not the printer

Enter New Date	<mm/dd/yy>

Set Date Format	PASSPORT does not use entries in this menu

Select a Date Format

Host Port Configuration	IMPORTANT - The entries in this menu determine how PASSPORT will communicate with the printer. They must be set as specified here, or Syntax and Framing or other error messages will appear on the printer.

Select Baud Rate	9600

Select Parity	E

Enter Word Length (7-8)	7

Enter Stop Bits (1-2)	1

Enter Start (XON) Char	128

Enter Stop (XOFF) Char	128

Clear Batch Memory at power-up

Clear batches at power-up	E

9420/9440 Compatible Mode

9420/9440 Compatible Mode	D

9420/9440 Imaging Mode

9420/9440 Imaging Mode	D

Enhance Paper Handling Mode

Enh. Paper Handling Mode	E

Auto Online Mode

Auto Online Mode	E

Version

## Sato M-8400

Select Mode			Mode 1

Mode 1 Options	Setup Interface

Select Interface	RS-232C

Select Baud Rate	9600

Stop bit length	1 bit

Parity	Even

Data Bit Length	7 bits

Protocol	PCI RS On/Off

Multidrop Printer Number	01

Select Mode			Mode S

Mode S Options	Setup Sensor

Sensor Setup	(This value will depend upon your Label Stock.) See the printer manual for details.

Mode S Options	Set VH Offset

VertOffset	0020 dots (Adjust to the current label stock)

HortOffset	0080 dots (Adjust to the current label stock)

## Whittier Mailing Products (WMP-LT, WMP-LT4, WMP-LT5, a Orion BTP-400)

These printer have no manual setup features. All configuration changes must be sent via serial communications. PASSPORT has provided an automated means to configure the WMP printers for an Entry-Level setup. If these printers are to be used in a Standard-System, the user must first connect the printer to the COM1: port of another computer (PASSPORT does not need to be loaded, only the five files listed below) using an Entry-Level Serial cable described in Appendix C.

Use the following procedure to setup a WMP printer for use with PASSPORT:

At the DOS Prompt, change to the EXE directory by typing CD\CAA.V01\EXE <enter>

Run the batch file included with PASSPORT by typing WMP-SET <Enter>. Follow the instructions on-the screen for resetting the printer to Default Mode.

Once the setup program completes, the printer will print a status label. Turn off the printer when after this is printed.

The printer is now ready for use with PASSPORT

If the printer is to be setup using a computer without PASSPORT installed on it, follow these steps:

Copy the following files from a PASSPORT computer to a floppy disk:

C:\CAA.VØ1\EXE\CAA6Ø5B.EXE

C:\CAA.VØ1\EXE\BRT71EFR.EXE

C:\CAA.VØ1\EXE\WMP-SET.BAT

C:\CAA.VØ1\EXE\WMP-SET1.DAT

C:\CAA.VØ1\EXE\WMP-SET2.DAT

Insert the floppy in the drive and make that drive the current drive by typing: A: <Enter>, or B: <Enter>

Type WMP-SET <Enter> and follow the on-screen instruction for resetting the printer to Default Mode.

Once the setup program completes, the printer will print a test pattern label. Turn off the printer when this is printed.

The printer is now ready for use with PASSPORT

## Personal Computer

### Entry Level System

A single computer is required for the Entry Level System. The system must be at least meet the following specifications:

80486/33MHz or higher processor

4 MB RAM

one 3-1/2 inch high density floppy drive

40 MB available hard drive space

one parallel, two serial I/O ports

Video display monitor and adapter card

DOS version 3.3 or higher

Modem

### Standard System

The Standard System requires two PC’s, each of which must meet the minimum specifications detailed for the Entry Level System.

### Power Requirements

Each PC will require a 110 VAC source. Each video display monitor will require a 110 VAC source.

## Modem

PASSPORT supports a variety of modems. Specify the modem type and connection settings to PASSPORT using the MAIN MENU | SETUP MENU | ORDERING CONFIGURATION screen. The user must determine the communications port (COM port) and interrupt request number (IRQ) for the modem hardware. Consult the modem hardware guide for information on these settings. Users of windows may find this information available using the Control Panel/System or Control Panel/Modem icons.

Note: PASSPORT cannot be used without a modem. It is the user's responsibility to provide the COM port and IRQ information for configuration. The PASSPORT Technical Support Team cannot determine these settings for your system.

While the highest speed available in PASSPORT is 9600 baud, most modems rated at higher speeds will operate at 9600.

The modem initialization string is also hardware-dependant. Suggested strings for several popular modems are included with PASSPORT. If your modem is not listed, try PASSPORT Default or Other.

If there is a problem with the initialization string, review your modem hardware guide for the correct initialization string to set your modem to emulate a Hayes 9600 baud modem.

The modem will require an outside telephone line.

## Console Printer

The console printer is used for printing reports. It cannot be used to print labels.

The console printers listed in MAIN MENU | SETUP MENU | ORDERING CONFIGURATION include only the Okidata 320 or 390. To use other compatible printers, connect any ASCII text printer to the LPT1: port and select the Okidata 320. PASSPORT prints reports with pre-defined line lengths. Some reports require more than 80 characters on a line. To properly print these reports, the printer must be set, using front panel controls, to condensed character pitch.

### Power Requirements

Each console printer will require a 110VAC source.

### Specifications

The Okidata 320 is a 9-pin dot matrix printer that prints at a rate of 50, 64, or 100 characters per second, depending on print mode. The printer dimensions are 15.7”w x 13.6”d x 4.6”h, weighing 16 lbs. It uses a standard Microline 100 ribbon, with a 3,000,000 character nominal life, measured in Utility Mode. Power requirements are 120VAC

The Okidata 390 is a 24-pin dot matrix printer that prints at a rate of 90 or 270 characters per second, depending on print mode. The printer dimensions are 15.7”w x 13.0”d x 4.6”h, weighing 18 lbs. It uses a standard Microline 390 ribbon, with a 2,000,000 character nominal life, measured in Utility Mode. Power requirements are 120VAC

The Okidata 320 is a 9-pinb dot matrix printer that prints at a rate of 50, 64, or 100 characters per second, depending on print mode. The printer dimensions are 15.7”w x 13.6”d x 4.6”h, weighing 16 lbs. It uses a standard Microline ribbon, with a 3,000,000 character nominal life, measured in Utility Mode. Power requirements are 120VAC

### Manufacturer Information

Okidata printers are available through:

Okidata Company

Mt. Laurel, NJ 08054

(609) 235-2600

## Label Printer

Each of the supported label printers must be configured to work with PASSPORT. See Appendix A for details on label printer configuration

The printers must be connected using cables as specified in Appendix C.

### Power Requirements

Each label printer will require a 110 VAC source.

### Manufacturer Information

Intermec Printers:

Intermec® Corporation

6001 36th Avenue West

P.O. Box 4280

Everett, WA  98203-9280

(800) 755-5505  Sales/Service

(800) 227-9947  Media Supplies

Monarch Printers

Monarch Marking Systems, Inc.

A Pitney Bowes Company

(800) 543-6650  Sales

(800) 231-7700  Service

Sato Printers

SATO America, Inc.

545 Weddell Drive

Sunnydale, CA  94089

(408) 745-1300

(201) 529-1930 - Eastern Region

(313) 295-4243 - Central Region

(770) 969-2333 - Southern Region

(602) 491-0141 - Western Region

Microcom Printers

Microcom Corporation

8333 Green Meadows Drive North

Westerville, Ohio 43081 USA

Phone: (614) 548-6262 or (800) MICROCOM

FAX: (614) 548-6556

Email: msales@microcomcorp.com

WMP Printers:

Whittier Mailing Products

12366 Penn Street

Whittier, CA 90602-1103

Phone: (562) 464-3000

FAX: (562-464-3007

http://www.wmptagger.com

## Printer Cabling

### Printer Cable for Use with Monarch Printers

Use the following cable for the Monarch 9425 or Monarch 9445 thermal label printer with an Entry Level system.

| PC COM1: DB25-F |  | Monarch Printer DB25-M |
| --- | --- | --- |
| Pin # |  | Pin # |
| 2 | ------------- | 3 |
| 3 | ------------- | 2 |
| 5 | ------------- | 20 |
| 7 | ------------- | 7 |

Figure 15 –Monarch 9425/9445 Cabling

If the COM1: port on the PC is has a 9 pin connector, use the following to build a cable to use with the Monarch 9425/9445 printer.

| PC COM1: DB9-F |  | Monarch Printer DB25-M |
| --- | --- | --- |
| Pin # |  | Pin # |
| 2 | ------------ | 2 |
| 3 | ------------ | 3 |
| 5 | ------------ | 7 |
| 8 | ------------ | 20 |

Figure 16 –9 Pin to 25 Pin Cable for  the Monarch 9425/9445 Printer

### Printer Cable for Use with Intermec 3000 Printers

Use the following cable for the Intermec 3000A.

| PC COM1: DB25-F |  | Intermec 3000A DB25-M |
| --- | --- | --- |
| Pin # |  | Pin # |
| 2 | ------------ | 3 |
| 3 | ------------ | 2 |
| 5 | ------------ | 11 |
| 7 | ------------ | 7 |

Figure 17 –Intermec 3000A Cabling

If the COM1: port on the PC is has a 9 pin connector, use the following to build a cable to the Intermec 3000A.

| PC COM1: DB9-F |  | Intermec 3000A DB25-M |
| --- | --- | --- |
| Pin # |  | Pin # |
| 2 | ------------ | 2 |
| 3 | ------------ | 3 |
| 5 | ------------ | 7 |
| 8 | ------------ | 11 |

Figure 18 –9 Pin to 25 Pin Cable for use with the Intermec 3000A Printer

### Printer Cable for Use with Intermec 3400 Printers

Use the following cable for the Intermec 3400.

| PC COM1: DB25-F |  | Intermec 3400 DB25-M |
| --- | --- | --- |
| Pin # |  | Pin # |
| 2 | ------------ | 3 |
| 3 | ------------ | 2 |
| 5 | ------------ | 11 |
| 7 | ------------ | 7 |

Figure 19 –Intermec 3400 Cabling

If the COM1: port on the PC is has a 9 pin connector, use the following to build a cable to the Intermec 3400.

| PC COM1: DB9-F |  | Intermec 3400 DB25-M |
| --- | --- | --- |
| Pin # |  | Pin # |
| 2 | ------------ | 2 |
| 3 | ------------ | 3 |
| 5 | ------------ | 7 |
| 8 | ------------ | 11 |

Figure 20 –9 Pin to 25 Pin Cable for use with the Intermec 3400 Printer

### Printer Cable for Use with Sato M-8400 Printer

Use the following cable for the Sato M-8400 thermal label printer.

| PC COM1: DB25-F |  | Sato M-8400 DB25-M |
| --- | --- | --- |
| Pin # |  | Pin # |
| 2 | ------------ | 3 |
| 3 | ------------ | 2 |
| 5 | ------------ | 20 |
| 7 | ------------ | 7 |

Figure 21 –Sato M-8400 Cabling

If the COM1: port on the PC is has a 9 pin connector, use the following to build a cable to use with the Sato M-8400 printer.

| PC COM1: DB9-F |  | Sato M-8400 Printer DB25-M |
| --- | --- | --- |
| Pin # |  | Pin # |
| 2 | ------------ | 2 |
| 3 | ------------ | 3 |
| 5 | ------------ | 7 |
| 8 | ------------ | 20 |

Figure 22 –9 Pin to 25 Pin Cable for  the Sato M-8400 Printer

### Printer Cable for Use with Microcom 410 ECA Printer

Use the following cable for the Microcom 410 ECA thermal label printer.

| PC COM1: DB25-F |  | Microcom 410 ECA DB9-M |
| --- | --- | --- |
| Pin # |  | Pin # |
| 2 | ------------ | 3 |
| 3 | ------------ | 2 |
| 5 | ------------ | 8 |
| 7 | ------------ | 5 |

Figure 23 –System Microcom 410 ECA Cabling

If the COM1: port on the PC is has a 9 pin connector, use the following to build a cable to use with the Microcom 410 ECA printer.

| PC COM1: DB9-F |  | Microcom 410 ECA DB9-M |
| --- | --- | --- |
| Pin # |  | Pin # |
| 2 | ------------ | 2 |
| 3 | ------------ | 3 |
| 5 | ------------ | 5 |
| 8 | ------------ | 8 |

Figure 24 –9 Pin Cable for the Microcom 410 ECA Printer

(The cable represented in the preceding Figure can be purchased commercially off-the-shelf. It is available as a 9 pin video cable)

### Printer Cable for Use with WMP LT, LT4, LT5 and Orion BTP-400 Printers

Use the following cable for the WMP thermal label printers.

| PC COM1: DB25-F |  | WMP LT, LT4, LT5 DB9-M |
| --- | --- | --- |
| Pin # |  | Pin # |
| 2 | ------------ | 3 |
| 3 | ------------ | 2 |
| 5 | ------------ | 8 |
| 7 | ------------ | 5 |

Figure 25 –WMP Cabling

If the COM1: port on the PC is has a 9 pin connector, use the following to build a cable to use with the WMP LT, LT4, or LT5 printers.

| PC COM1: DB9-F |  | WMP LT, LT4, LT5 DB9-M |
| --- | --- | --- |
| Pin # |  | Pin # |
| 2 | ------------ | 2 |
| 3 | ------------ | 3 |
| 5 | ------------ | 5 |
| 8 | ------------ | 8 |

Figure 26 –9 Pin Cable for the WMP Printers

(The cable represented in the preceding Figure can be purchased commercially off-the-shelf. It is available as a 9 pin video cable)

## Installation Problems

If the install was unsuccessful, or you are having problems with the software, check the following possible problem/solutions and follow the suggested method of solving the problem before calling the help line.

If you get an error message that indicates you have a file missing it could be due to the file command.com missing from your path.  Make sure that either the root directory ( C:\ ) is in your path or that C:\DOS is in your path and has the file command.com in it.

If you are installing a new version of the software after having an old version on your system and getting a file missing error, you can try deleting all files in the sortdata subdirectory (except caa409d, caa410d, caa418d and all associated files extensions because these files contain data specific to your site) and rerunning the install.

## Communications Problems

Make sure the modem is configured correctly and set up with the correct com port. If The port specified is not a valid port on the PC, the message “Result 01- Unable to Access Port” will be displayed. If the port exists, but there is no modem attached to it, the user will see the message: “Your modem has indicated a problem with the modem initialization string.” If the user continues, the message Unable to disconnect” will appear.

Make sure the phone line is active and connected correctly to the modem (do not use the jack labeled PHONE, use the jack labeled LINE). If there is a problem with the phone line, the message “No Dialtone” will be displayed.

If the modem emits audible dialtone and the user hears the modem dial, but the BBS does not answer, make sure phone numbers reflect the correct outside access code.  PASSPORT assumes ‘8’.

If the BBS answers, the user will hear the sounds of the computer linking to the BBS. If communications fail at this point, there is probably a problem with the modem initialization string. The user should try specifying other modem types under the Ordering Configuration setup in PASSPORT.

If communications fail during transmission, try a slower baud rate

## Other common Problems

If you are getting an “ACCESS DENIED” message, it may be due to SHARE  being loaded without parameters in your AUTOEXEC.BAT or CONFIG.SYS. This will limit the number of databases that may be opened.   If you must have SHARE loaded, add the /F:5120 and /L:500 parameters to the SHARE line which will permit you to open more databases in work areas.

ex.	SHARE /F:5120 /L:500

Non USA Addresses are not allowed for Origin Sites. Labels with Foreign Destinations may, however, be ordered.

If PASSPORT is not allowing the required CIN Code, first review the CIN listings under SETUP MENU/CUSTOMIZING TABLES MENU/MAIL TYPE (CIN) LISTINGS option. PASSPORT will enforce these rules as implemented in the reclassification and not permit invalid labels to be printed or ordered. Contact your Area Label Coordinator (see the listing later in this guide) if questions remain about which Content Identifier to use.

If the labels printed with PASSPORT are not being read by your processing equipment, (ie. Scan Where You Band and others), first verify that the barcode is readable using a code verifier. If the code doesn’t scan at all, verify that the code print quality, label reflectance and other physical factors are within tolerance. If the label scans with the verifier, make sure the code read yields the same number as is printed under the barcode. If the label is readable and the code data matches the human readable data, make sure the processing equipment is using the latest CIN list.

If the program issues a black box error and terminates, call technical support. This problem will probably only affect the operation that was being performed at the time. Restart PASSPORT from the C: prompt and other operations should still be available.

## System Support

PASSPORT system support is provided by Information System Support (ISS) in Raleigh  and also by the Raleigh Integrated Business Systems Solution Center (RAIBSSC) which developed the PASSPORT software and will provide system operational support.

The user should first familiarize himself with the system and learn as much as possible  to be able to understand how to implement possible solutions and to be aware of  system functions and capabilities. Please review the documentation, step through the system, and contact label personnel for questions involving postal procedure and policy. In particular, questions regarding appropriate CIN codes should be directed to your local Business Mail Representative.

When a call to the hotline is first placed, the ISS personnel will attempt to resolve the problem.  However, their expertise in the system is limited and they cannot handle any complex technical questions.  If your problem is due to something that has nothing to do with the PASSPORT system itself or is of a technical nature, they cannot solve your problem.  In this case it would be wise to have an IS person at your site take a look at the problem before calling the hotline.

If the problem is a PASSPORT problem and is one of a technical nature, then ISS will pass the problem on to the RAIBSSC.

BBS (Bulletin Board System) - The Raleigh Integrated Business Systems Solution Center maintains a BBS to allow users to connect via modem to download software upgrades. The Topeka Label Printing Center maintains a BBS to allow users to connect via modem to submit orders for label printing.

Bulk Order - All labels for a bulk order are for the same originating site and will be printed using the same product. A bulk order consists of one  line for each label definition specified. The minimum quantity for each line is 300 for most products, except for mini-bulk products which allow as few as 25.

CIN (Content Identification Number) - The Content Identification Number specifies the characteristics of mailpieces in the container being labeled.

Hotnews - Current news is provided to users when an upgrade is downloaded and applied. These hotnews files are also available under the Upgrade Software/Tables menu

ODLS - On-Demand Label System. This software was the predecessor to the PASSPORT Label Acquisition System. It is no longer supported by the USPS.

Originating Site - The originating site is the source of the mailpieces in the container to be labeled. Each originating site must have a unique Zip plus 4 specified in the Originating Site Setup.

PASSPORT Site - One of the originating sites specified under the Originating Site Setup must be selected as the PASSPORT Site.

Synchronization Disk - Also referred to as Synch disks, these may be created on a PASSPORT system when it downloads an upgrade. These are used to upgrade other machines at the site which do not have modem access to the BBS.

Barcode Values	040-5

Bottom Label Line	040-3

Cable Diagrams	C-4

CIN (Content Identification Number)

Defined	040-4

Collated Set Orders	050-8

Communications Problems	130-1

Hotnews	010-8

Importing Data

SDF files	060-14

Keyboard Commands	020-5

Menu Structure	020-3

Modem, requirement	010-6

Ordering Configuration	030-5

Passport Site	030-4

Specifying the Primary Passport Site	030-4

Prepare Orders	050-11

Printers, Setup	A-1

Printers, supported console printers	010-7

Printers, supported label printers	010-6

Product Code Table	060-2

Quick Reference Guide	010-8

Readme file	010-7

Registering with Topeka	030-5

RIBBS	010-1

Sack Labels	040-2

Transmitting an Order	050-12

Tray Labels	040-2

Versions of Passport

Mailer	020-2

Postal	020-2

Wiring Diagrams	C-1

# Text boxes

CAA424S2           UNITED STATES POSTAL SERVICE PASSPORT SYSTEM      01/05/1998

V01.23-BE                      ORIGINATING SITES                      12:48:14

PASSPORT SITE NAME:    RALEIGH ISSC PASSPORT TEAM(   1)    FINANCE NO.:111111

ORIGIN      SITE                                  REQ.  FINANCE  LAST

ZIP+4       NAME / ADDRESS                        CODE    NO.    UPDATED

27668-0002    RALEIGH ISSC PASSPORT TEAM             M            08/15/1996

ADDR 1  ATTN PASSPORT COORDINATOR

ADDR 2  RALEIGH ISSC

ADDR 3  U S POSTAL SERVICE                         SITE

ADDR 4  4200 WAKE FOREST RD                        NUMBER

ADDR 5  RALEIGH NC 27668-9200                          1

ADDR 6

CONTACT           : PASSPORT COORDINATOR

PHONE NO          : (919)786-2000

BOTTOM LABEL LINE : RALEIGH NC ISSC 27668-9200

F1-Help                              F10-Process                        ESC-Quit

CAA425S1           UNITED STATES POSTAL SERVICE PASSPORT SYSTEM      01/05/1998

V01.23-BE                        PASSPORT SITE                        12:55:55

OFFICE NO :    1

SITE NAME : RALEIGH ISSC PASSPORT TEAM                FINANCE NO.:

CURRENT STATUS (FOR INFO ONLY)

LAST OFFICE NUMBER USED     6

TRANSMIT START DATE    /  /              UPDATE START DATE    /  /

TRANSMIT START TIME                      UPDATE START TIME

F1-Help                              F10-Process                        ESC-Quit

CAA427S1           UNITED STATES POSTAL SERVICE PASSPORT SYSTEM      01/05/1998

V01.23-BE                    ORDERING CONFIGURATION                   14:08:47

Printer Type: HP LaserJet III or Compatible

Printer Port: See HP3.INI

Modem Port: COM3

Modem IRQ#: 04

Baud Rate: 9600

Modem Type: -PASSPORT DEFAULT

Modem Initialization String:

ATZE0Q0V1X4 S11=55 S0=0 S7=60

Label Order Phone Number: 9,1-913-861-2756

Software Order Phone Number: 9,1-919-501-9173

System ID: A

Alt/F10 - Register with Topeka LPC

F1-Help                              F10-Process                        ESC-Quit

CAA420S2           UNITED STATES POSTAL SERVICE PASSPORT SYSTEM      01/06/1998

V01.23-BE                    BULK LABELS (RECLASS)                    16:11:37

ORIGIN                                  REQUESTER  PRODUCT

ZIP         BOTTOM LABEL LINE           CODE       CODE

27668-0002  RALEIGH NC ISSC 27668-9200  M          B9

F1-Help                              F10-Process                        ESC-Quit

CAA420S3           UNITED STATES POSTAL SERVICE PASSPORT SYSTEM      01/06/1998

V01.23-BE                         BULK LABELS                         16:23:47

ORIGIN                                  REQUESTER  PRODUCT

ZIP         BOTTOM LABEL LINE           CODE       CODE

27668 0001  RALEIGH NC ISSC 27668-9200  M          B9

QTY   ZIP   DESTINATION            CIN  DESCRIPTION             Status ?

300 27668 RALEIGH NC             242  FCM LTRS 5D BC          NoBC

300 22310 ALEXANDRIA VA          242  FCM LTRS 5D BC          NoBC

300 02115 BOSTON MA              242  FCM LTRS 5D BC          NoBC

300                              242  FCM LTRS 5D BC          NoBC

Alt/F3-Insert F2-Clr Field                                       Alt/F9-Defaults

F1-Help       F3-Add        F5-Del  F10-Process  PGUP-Prev  PGDN-Next   ESC-Quit

CAA461S1           UNITED STATES POSTAL SERVICE PASSPORT SYSTEM      01/07/1998

V01.23-BE                        PREPARE ORDERS                       10:24:05

Batch Preparation Completed

Batch Name: M0000109

# of Orders:       1

# of Labels:       1

# of 8131's:       6

For future reference, it would be a good idea to make a copy of

this screen and attach it to the 1578 and 8131 forms.

Press any key to continue...

CAA602S1           UNITED STATES POSTAL SERVICE PASSPORT SYSTEM      01/07/1998

V01.23-BE                         PRINT LABELS                        10:35:55

+---------------------------------------------+

¦                                             ¦

¦ Origin Site : 0002  MAILER RALEIGH NC 276   ¦

¦ Label Format: 01    B9/BN Tray Label Format ¦

¦ MP Code     : B     BARCODED MAIL PIECES    ¦

¦ Sort        : L801  AADC DESTINATIONS       ¦

¦ Class       : 3     STANDARD (A)            ¦

¦ Type        : 1     LETTER                  ¦

¦ Content ID  : 545   STD LTRS AADC BC        ¦

¦                                             ¦

¦ ------------------------------------------- ¦

¦                                             ¦

¦ Zip Code    : 275   AADC RALEIGH NC         ¦

¦ Quantity    :   2                           ¦

¦                                             ¦

+---------------------------------------------+

F2-Clr Field                 F7-Print Labels                     F9-Default Info

F1-Help                      Alt/F7-Print Import File                   ESC-Quit

CAA430S1           UNITED STATES POSTAL SERVICE PASSPORT SYSTEM      01/07/1998

V01.23-BE                    MAIL TYPE (CIN) TABLE                    13:23:06

MAIL  CONTENTS                        REQ

PST/MLR TYPE  IDENTIFICATION           ZEBRA  DEL

USE   (CIN) DESCRIPTION              CODE   DAY

P     141  EXPRESS MAIL               N     N

P     142  EXPRESS COLLECTOR          N     N

M     143  EXPRESS DROP SHIP          N     N

P     144  SAME DAY EXPRESS MAIL      N     N

P     145  PRIORITY                   N     N

P     147  PRIORITY LTRS              N     N

M     148  PRIORITY LTRS 5D           N     N

M     149  PRIORITY LTRS 3D           N     N

M     150  PRIORITY LTRS SCF          N     N

M     151  PRIORITY LTRS ADC          N     N

M     152  PRIORITY LTRS WKG          N     N

P     153  PRIORITY FLTS              N     N

F1-Help          F6-Prt CINs         F4-Modify    PgUp-Prev  PgDn-Next  ESC-Quit