# D-29096

# Earth Observing System (EOS)

# Tropospheric Emission Spectrometer (TES)

# Mission Planning Requirements

# Version 1.0

# Author:	Reinhard Beer

June 16, 2004

# Jet Propulsion Laboratory

California Institute of Technology

Pasadena, CA

D-29096

# Earth Observing System (EOS)

# Tropospheric Emission Spectrometer (TES)

# Mission Planning Requirements

# Version 1.0

Original signed by				Original signed by

------------------------------------			----------------------------------

Dr. Reinhard Beer				Padma Varanasi

Principal Investigator				Mission Operations Team Leader

June 16, 2004

# Jet Propulsion Laboratory

California Institute of Technology

Pasadena, CA

Paper copies of this document may not be current and should not be relied upon for official purposes. The current version is in the TES library at http://tes-lib.jpl.nasa.gov/

# Table of Contents

1	INTRODUCTION	1

1.1	Identification	1

1.2	Purpose	1

1.3	Applicable Documents	1

2	SUMMARY REQUIREMENTS	2

3	INTRODUCTION	3

3.1	Assumptions	3

4	BASIS	3

5	GLOBAL SURVEY SCHEDULE	39

6	REPORTING	39

7	REFERENCES	41

8	ACRONYMS	42

APPENDIX	43

# 1	INTRODUCTION

## 1.1	Identification

This is the Tropospheric Emission Spectrometer (TES) Mission Planning Requirements document, version 1.0

## 1.2	Purpose

The primary purpose of this document is to provide requirements for the planning of TES Special Observations (i.e., all non-Global Survey operations). However, the Global Surveys is also included for completeness

## Applicable Documents

JPL D-28402, Mission Plan, version 1.0

JPL D-11294, Scientific Objectives & Approach, Goals & Requirements, version 6.0

JPL D-19450, Ground System Requirements

JPL D-17848, Flight Operations Requirements & Plan

TES A&S DFM 562, ‘Transect Mode Revisited’

# 2	SUMMARY REQUIREMENTS

The Science Team (ST) shall provide the Mission Operations Team (MOT) with:

MPR_1: A 16-day rotating schedule for performing Global Surveys;

MPR_2: A list of potential fixed targets for Special Observations;

MPR_3: A latitude, longitude, altitude and UTC start time for staring-mode Special Observations at least TBD (72) hours in advance, except in emergencies when this time can be reduced to TBD (36) hours in advance;

MPR_4: A set of latitudes, longitudes and altitudes with a UTC start time for transect-mode Special Observations at least TBD (72) hours in advance, except in emergencies when this time can be reduced to TBD (36) hours in advance.

The MOT shall:

MPR_5: Initiate the 233-orbit Global Survey cycle of 8 sets of “2 orbits of pre-calibration, 16 orbits of atmospheric measurements, 2 orbits of post calibration” one-quarter of an orbit into WRS path 1.

MPR_6: Provide the ST with a rolling 3-day ephemeris prediction every day.

MPR_7: Accept inputs for Special Observations from the ST and prepare/upload all necessary macros and macro parameter table entries in time for execution at the requested location(s) and time.

MPR_8: Provide the ST a daily list of all macros actually executed.

# 3	INTRODUCTION

An outline of the TES Mission Plan was documented in D-28402. Conspicuously missing from that document were days and times for the phasing of Global Surveys with Special Observations (without which it is impossible to generate useful requirements). This document attempts to remedy this deficiency but it must be recognized that the planned Ascending Node crossing time of 13:45 Local Mean Solar Time has a pre-launch uncertainty of +/- 15 minutes so this document will need to be updated after launch. However, all the necessary tools are in place.

## 3.1	Assumptions

- All ascending nodes occur at 13:45 Local Mean Solar Time

- All orbits follow the Worldwide Reference System (WRS) prescription for paths and descending nodes (Appendix).

While it is believed that every effort is made by the GSFC Flight Dynamics branch to ensure that a) & b) are true, I have noted that, in reality, nodal crossing times can be off by 1 – 2 minutes and nodal longitudes off by about 0.2 degrees. Caveat emptor. Nevertheless, this document will suffice to initiate the long-term planning process.

- All TES orbits begin at the Southern Apex (-81.79o latitude).

- UTC = GMT = Local Mean Solar Time at the prime meridian (more-or-less true).

# 4	BASIS

The first task, based on the tabulated WRS Descending Nodes (DN; see Appendix) is to determine the longitude and UTC of the Southern Apex (SA) and the next Ascending Node (AN). The longitudes follow from elementary spherical trigonometry. The times are determined from the knowledge that the time difference between any AN longitude a and the prime meridian is simply a/15 hours (with the appropriate sign) and that the SA occurs ¼ of a period earlier, the DN ½ of a period later. The results are also shown in the Appendix.

The second task is to set up a “standard orbit” whose SA is at 0o longitude and runs from one SA to the next. The time step chosen was 1 second, which is more than adequate resolution given the caveats above.  All orbits are then simply the standard orbit started from the SA longitudes listed in the Appendix. Again, all real orbits are not self-similar but the differences are inconsequential for the present purpose. Initialization of actual observations will require a good-quality predicted ephemeris because the timing requirements are +/- 5 seconds [Requirement MPR_6].

In the third step, each of the 233 orbits is tested against the location of the targets listed in the Mission Plan (about 25) using an IDL program called “target.pro”. All orbits that pass within 45o nadir angle and allow at least 52 seconds (= 10 short scans) of observation time are logged together with the location of the spacecraft at closest approach, the minimum nadir angle, the allowed observation time, the UTC of the encounter and the Local Mean Solar Time at the target and the spacecraft.  It should also be noted that the associated WRS path numbers (1-based indexing) have 0.25 added to them as a reminder that TES orbits (0-based indexing) begin ¼ of an orbit after the Descending Node (where WRS paths begin). Fortunately, for every target tested so far, there are at least 16 orbits from which to choose.

The same code is used to specify transect origins, where the spacecraft location at closest approach is used by another program (“transect.pro”) to lay out the transect planning parameters (see the Mission Plan and A&S DFM 562).

At the fourth step, a program called “overlap_sort.pro”, written by Helen Worden, takes these tables and sorts them by orbit. There is sufficient “clumping” of target opportunities to permit a clear choice of which sets of 9 or 10 “off days” should be assigned to Special Observations. That is, Global Surveys (although their 20-orbit blocks are reserved) do not drive the phasing. One consequence of this choice was to make it cosmetically-convenient to rotate the orbit file 2 positions right so that the first Global Survey begins at TES orbit 2 (= WRS path 1.25; see the Appendix) [Requirement MPR_5]. The outcome of this exercise is shown in Table I. It must be emphasized that the Special Observations listed are those that can be made on that orbit. The decision as to which ones will be made rests with Science Planning Team.

The Special Observation opportunities for known targets are expanded upon in Tables II – XXV. The orbits marked in red fall into times reserved for Global Surveys, so are not normally available. Nevertheless, despite this fairly strong filtering, every target has at least 4 opportunities within each 16 day cycle. Of these targets, the first eight are ARM or NDSC validation sites (Tables II – IX) and Table X is for a so-far unique site (Ascension Island between Africa and South America which can be used either as a secondary validation site (ozonesondes have been launched from there in the past) or to monitor the convergence of the southern springtime biomass burning plumes from both continents. Tables XI – XIII are for transects that we will use early in the mission for “show & tell”, Table XIV is for a short (10 scan) transect for PCS validation, Table XV is for radiance validations and Tables XVI – XXV are for the 10 volcanoes identified for monitoring. True “targets of opportunity” such as wildfires are only semi-predictable in time (and not at all in location) and industrial accidents are, of course, completely unpredictable. Our ability to study such events will depend on close cooperation between the Science Team and the Mission Operations Teams (both at JPL and GSFC) [Requirements MPR_1, _2, _3, _4 & _7].

Table I: Selection List For TES Targets

(list wrapped around to preserve logical groupings)

Color Code: RED = stare site; GREEN = transect site; BLACK = either;

BLUE = volcano

orbit = 2 target sites:  ---------------------------------------------------------

orbit = 3 target sites:

orbit = 4 target sites:

orbit = 5 target sites:  		G

orbit = 6 target sites:  		L

orbit = 7 target sites:  		O

orbit = 8 target sites:  		B

orbit = 9 target sites:  		A

orbit = 10 target sites:		L

orbit = 11 target sites:

orbit = 12 target sites:  	S

orbit = 13 target sites:  	U

orbit = 14 target sites:  	R

orbit = 15 target sites:  	V

orbit = 16 target sites:  	E

orbit = 17 target sites: 	Y

orbit = 18 target sites:

orbit = 19 target sites:  	0

orbit = 20 target sites:

orbit = 21 target sites:  -------------------------------------------------------

orbit = 22 target sites:  Barrow White Is.

orbit = 23 target sites:  Barrow Nauru

orbit = 24 target sites:  Darwin

orbit = 25 target sites:  Masaya

orbit = 26 target sites:  Colima

orbit = 27 target sites:  Barrow Reunion

orbit = 28 target sites:  Hilo Barrow Middle_East Pu’u O’o

orbit = 29 target sites:  Etna White Is.

orbit = 30 target sites:  Lauder Ascension Erebus

orbit = 31 target sites:  --------------------------------------------------------

orbit = 32 target sites:

orbit = 33 target sites:

orbit = 34 target sites:  	G

orbit = 35 target sites:  	L

orbit = 36 target sites:  	O

orbit = 37 target sites:  	B

orbit = 38 target sites:  	A

orbit = 39 target sites:  	L

orbit = 40 target sites:

orbit = 41 target sites:  	S

orbit = 42 target sites:  	U

orbit = 43 target sites:  	R

orbit = 44 target sites:  	V

orbit = 45 target sites:  	E

orbit = 46 target sites: 	Y

orbit = 47 target sites:

orbit = 48 target sites:  	1

orbit = 49 target sites:

orbit = 50 target sites: -----------------------------------------------------

orbit = 51 target sites:  Barrow White Is.

orbit = 52 target sites:  Barrow Nauru

orbit = 53 target sites: 0

orbit = 54 target sites: 0

orbit = 55 target sites:  Colima

orbit = 56 target sites:  Barrow

orbit = 57 target sites:  Barrow Middle_East Hilo Pu’u O’o

orbit = 58 target sites:  Etna

orbit = 59 target sites:  Lauder Ascension Erebus

orbit = 60 target sites:  ------------------------------------------------------

orbit = 61 target sites:

orbit = 62 target sites:

orbit = 63 target sites:  	G

orbit = 64 target sites:  	L

orbit = 65 target sites:  	O

orbit = 66 target sites:  	B

orbit = 67 target sites:  	A

orbit = 68 target sites:  	L

orbit = 69 target sites:

orbit = 70 target sites:  	S

orbit = 71 target sites:  	U

orbit = 72 target sites:  	R

orbit = 73 target sites:  	V

orbit = 74 target sites:  	E

orbit = 75 target sites: 	Y

orbit = 76 target sites:

orbit = 77 target sites:  	2

orbit = 78 target sites:

orbit = 79 target sites: -----------------------------------------------------------

orbit = 80 target sites:  Barrow

orbit = 81 target sites:  Barrow Nauru Lauder

orbit = 82 target sites:  Manus

orbit = 83 target sites:  Lascar

orbit = 84 target sites:  NA_Southeast SGP Colima

orbit = 85 target sites:  Tahoe_NS Tahoe Barrow

orbit = 86 target sites:  Middle_East Hilo Barrow Pu’u O’o

orbit = 87 target sites:  Etna

orbit = 88 target sites:  Lauder Nauru Erebus

orbit = 89 target sites: ----------------------------------------------------------------

orbit = 90 target sites:

orbit = 91 target sites:

orbit = 92 target sites:  	G

orbit = 93 target sites:  	L

orbit = 94 target sites:  	O

orbit = 95 target sites:  	B

orbit = 96 target sites: 	A

orbit = 97 target sites:  	L

orbit = 98 target sites:

orbit = 99 target sites:  	S

orbit = 100 target sites:  	U

orbit = 101 target sites:  	R

orbit = 102 target sites: 	V

orbit = 103 target sites:  	E

orbit = 104 target sites:  	Y

orbit = 105 target sites:

orbit = 106 target sites:  	3

orbit = 107 target sites:

orbit = 108 target sites: ---------------------------------------------------------------

orbit = 109 target sites:  Barrow

orbit = 110 target sites:  Barrow Nauru Lauder Erebus

orbit = 111 target sites:  Manus

orbit = 112 target sites:  Lascar Sakurajima

orbit = 113 target sites:  NA_Southeast SGP Colima Fuego

orbit = 114 target sites:  Tahoe_NS Tahoe Barrow

orbit = 115 target sites:  Middle_East Barrow

orbit = 116 target sites:  E_Med

orbit = 117 target sites:  Lauder Nauru Erebus

orbit = 118 target sites: -----------------------------------------------------------------

orbit = 119 target sites:

orbit = 120 target sites:

orbit = 121 target sites:  	G

orbit = 122 target sites:  	L

orbit = 123 target sites:  	O

orbit = 124 target sites:  	B

orbit = 125 target sites:  	A

orbit = 126 target sites:  	L

orbit = 127 target sites:

orbit = 128 target sites: 	S

orbit = 129 target sites:  	U

orbit = 130 target sites:  	R

orbit = 131 target sites: 	V

orbit = 132 target sites:  	E

orbit = 133 target sites:  	Y

orbit = 134 target sites:

orbit = 135 target sites: 	4

orbit = 136 target sites:

orbit = 137 target sites:  -----------------------------------------------------------------

orbit = 138 target sites:  Barrow Hilo Pu’u O’o

orbit = 139 target sites:  Ascension Barrow Nauru Lauder Erebus White Is.

orbit = 140 target sites:  Manus

orbit = 141 target sites:  Lascar Sakurajima

orbit = 142 target sites:  NA_Southeast SGP Fuego Pacaya

orbit = 143 target sites:  Tahoe_NS Tahoe Barrow

orbit = 144 target sites:  Barrow Middle_East

orbit = 145 target sites:  E_Med

orbit = 146 target sites:  Lauder Nauru White Is.

orbit = 147 target sites:  -------------------------------------------------------------

orbit = 148 target sites:

orbit = 149 target sites:

orbit = 150 target sites:  	G

orbit = 151 target sites:  	L

orbit = 152 target sites: 	O

orbit = 153 target sites:  	B

orbit = 154 target sites:  	A

orbit = 155 target sites:  	L

orbit = 156 target sites:

orbit = 157 target sites: 	S

orbit = 158 target sites:  	U

orbit = 159 target sites:  	R

orbit = 160 target sites: 	V

orbit = 161 target sites:  	E

orbit = 162 target sites:  	Y

orbit = 163 target sites:

orbit = 164 target sites:	5

orbit = 165 target sites:

orbit = 166 target sites:  -----------------------------------------------------------------

orbit = 167 target sites:  Barrow Hilo Pu’u O’o

orbit = 168 target sites:  Ascension Barrow Lauder Erebus White Is.

orbit = 169 target sites:  Manus

orbit = 170 target sites:  Darwin Lascar Sakurajima

orbit = 171 target sites:  NA_Southeast SGP Fuego Masaya Pacaya

orbit = 172 target sites:  Tahoe_NS Tahoe Barrow

orbit = 173 target sites:  Barrow Reunion

orbit = 174 target sites:  E_Med

orbit = 175 target sites:  Lauder Nauru Etna White Is.

orbit = 176 target sites:  Manus Erebus

orbit = 177 target sites: ------------------------------------------------------------------

orbit = 178 target sites:

orbit = 179 target sites:

orbit = 180 target sites:  	G

orbit = 181 target sites: 	L

orbit = 182 target sites:  	O

orbit = 183 target sites:  	B

orbit = 184 target sites: 	A

orbit = 185 target sites: 	L

orbit = 186 target sites:

orbit = 187 target sites:  	S

orbit = 188 target sites:  	U

orbit = 189 target sites: 	R

orbit = 190 target sites:  	V

orbit = 191 target sites:  	E

orbit = 192 target sites: 	Y

orbit = 193 target sites:

orbit = 194 target sites:  	6

orbit = 195 target sites:

orbit = 196 target sites:  --------------------------------------------------------

orbit = 197 target sites:  Ascension Barrow Lauder White Is.

orbit = 198 target sites: 0

orbit = 199 target sites:  Darwin Sakurajima

orbit = 200 target sites:  NA_Southeast SGP Fuego Masaya Pacaya

orbit = 201 target sites:  Tahoe_NS Tahoe Barrow

orbit = 202 target sites:  Barrow Reunion

orbit = 203 target sites:  E_Med

orbit = 204 target sites:  Etna White Is.

orbit = 205 target sites:  Manus Ascension Erebus

orbit = 206 target sites:  ------------------------------------------------------------

orbit = 207 target sites:

orbit = 208 target sites:

orbit = 209 target sites:  	G

orbit = 210 target sites: 	L

orbit = 211 target sites:  	O

orbit = 212 target sites:  	B

orbit = 213 target sites:  	A

orbit = 214 target sites: 	L

orbit = 215 target sites:

orbit = 216 target sites:  	S

orbit = 217 target sites:  	U

orbit = 218 target sites: 	R

orbit = 219 target sites:  	V

orbit = 220 target sites: 	E

orbit = 221 target sites: 	Y

orbit = 222 target sites:

orbit = 223 target sites:  	7

orbit = 224 target sites:

orbit = 225 target sites:  -------------------------------------------------------------

orbit = 226 target sites:  Ascension Barrow Lauder White Is.

orbit = 227 target sites:  Barrow

orbit = 228 target sites:  Darwin Sakurajima

orbit = 229 target sites:  NA_Southeast Fuego Masaya Pacaya

orbit = 230 target sites:  Tahoe_NS Tahoe Colima

orbit = 231 target sites:  Barrow Reunion

orbit = 232 target sites:  Hilo E_Med Pu’u O’o

orbit = 0 target sites:      Etna White Is.

orbit = 1 target sites:      Manus Ascension Erebus

| Table II. ARM Validation Site: Barrow, Alaska (off-shore); Lat 71.400; Lon 203.200 Orbits in RED are not normally available. |
| --- |
| WRS Path | TES Orbit | Descending Node (deg) | Ascending Node (deg) | S/C Lat (deg) | S/C Lon (deg) | Miss Distance (km) | Min. Nadir Angle (deg) | Obs. Time (secs) | UTC Day | UTC of Closest Approach | LMST @ Target | LMST @ S/C |
| 81.25 | 7 | 171.79479 | 4.15531 | 70.12905 | 215.02055 | 453.8 | 31.5 | 176 | 0 | 13:58 | 03:31 | 04:18 |
| 97.25 | 8 | 147.07379 | 339.43429 | 73.04869 | 194.79873 | 337.9 | 24.7 | 200 | 0 | 15:36 | 05:09 | 04:35 |
| 161.25 | 12 | 48.18970 | 240.55020 | 74.07125 | 215.33257 | 496.1 | 33.7 | 168 | 0 | 22:04 | 11:37 | 12:25 |
| 177.25 | 13 | 23.46870 | 215.82920 | 70.59722 | 196.52536 | 257.0 | 19.4 | 209 | 0 | 23:42 | 13:14 | 12:48 |
| 88.25 | 22 | 160.97939 | 353.33989 | 71.06036 | 205.46955 | 89.4 | 7.0 | 222 | 1 | 14:41 | 04:14 | 04:23 |
| 104.25 | 23 | 136.25839 | 328.61889 | 75.01755 | 188.19640 | 623.5 | 39.5 | 124 | 1 | 16:19 | 05:52 | 04:51 |
| 168.25 | 27 | 37.37420 | 229.73470 | 72.22420 | 207.99240 | 189.5 | 14.6 | 216 | 1 | 22:46 | 12:19 | 12:38 |
| 184.25 | 28 | 12.65320 | 205.01370 | 69.88226 | 186.64153 | 629.8 | 39.8 | 120 | 1 | 00:25 | 13:57 | 12:51 |
| 79.25 | 36 | 174.88499 | 7.24551 | 69.90856 | 217.83058 | 561.2 | 36.8 | 147 | 2 | 13:46 | 03:19 | 04:17 |
| 95.25 | 37 | 150.16389 | 342.52439 | 72.51723 | 196.94122 | 248.1 | 18.8 | 211 | 2 | 15:24 | 04:57 | 04:32 |
| 159.25 | 41 | 51.27980 | 243.64030 | 74.63740 | 217.15750 | 575.3 | 37.4 | 144 | 2 | 21:52 | 11:24 | 12:20 |
| 175.25 | 42 | 26.55880 | 218.91930 | 70.87071 | 199.23833 | 153.8 | 12.0 | 218 | 2 | 23:29 | 13:02 | 12:46 |
| 86.25 | 51 | 164.06949 | 356.42999 | 70.73278 | 208.09923 | 191.3 | 14.7 | 216 | 3 | 14:29 | 04:02 | 04:21 |
| 102.25 | 52 | 139.34849 | 331.70899 | 74.40552 | 189.84025 | 546.9 | 36.1 | 153 | 3 | 16:07 | 05:39 | 04:46 |
| 166.25 | 56 | 40.46440 | 232.82490 | 72.70505 | 210.26087 | 281.3 | 21.1 | 208 | 3 | 22:34 | 12:07 | 12:35 |
| 182.25 | 57 | 15.74330 | 208.10380 | 70.04773 | 189.52265 | 521.8 | 35.0 | 159 | 3 | 00:12 | 13:45 | 12:50 |
| 77.25 | 65 | 177.97509 | 10.33561 | 69.79812 | 220.78293 | 669.5 | 41.4 | 99 | 4 | 13:33 | 03:06 | 04:17 |
| 93.25 | 66 | 153.25409 | 345.61459 | 72.03496 | 199.22730 | 155.2 | 12.1 | 219 | 4 | 15:12 | 04:44 | 04:29 |
| 157.25 | 70 | 54.37000 | 246.73050 | 75.29580 | 218.62660 | 650.4 | 40.6 | 111 | 4 | 21:39 | 11:12 | 12:14 |
| 173.25 | 71 | 29.64890 | 222.00940 | 71.25213 | 201.78172 | 53.0 | 4.2 | 223 | 4 | 23:17 | 12:50 | 12:44 |
| 84.25 | 80 | 167.15969 | 359.52019 | 70.45885 | 210.81773 | 295.1 | 22.0 | 205 | 5 | 14:17 | 03:49 | 04:20 |
| 100.25 | 81 | 142.43859 | 334.79909 | 73.83624 | 191.70250 | 466.1 | 32.1 | 176 | 5 | 15:54 | 05:27 | 04:41 |
| 164.25 | 85 | 43.55450 | 235.91500 | 73.23478 | 212.38217 | 369.9 | 26.7 | 195 | 5 | 22:22 | 11:55 | 12:32 |
| 180.25 | 86 | 18.83350 | 211.19400 | 70.21291 | 192.40033 | 414.8 | 29.3 | 185 | 5 | 24:00 | 13:33 | 12:50 |
| 91.25 | 95 | 156.34419 | 348.70469 | 71.60338 | 201.63860 | 59.4 | 4.7 | 223 | 6 | 14:59 | 04:32 | 04:26 |
| 155.25 | 99 | 57.46010 | 249.82060 | 75.89195 | 220.08596 | 721.1 | 43.2 | 60 | 6 | 21:27 | 11:00 | 12:08 |
| 171.25 | 100 | 32.73910 | 225.09960 | 71.63170 | 204.30222 | 46.5 | 3.7 | 223 | 6 | 23:05 | 12:38 | 12:42 |
| 82.25 | 109 | 170.24979 | 2.61031 | 70.23912 | 213.61801 | 400.5 | 28.5 | 188 | 7 | 14:04 | 03:37 | 04:19 |
| 98.25 | 110 | 145.52879 | 337.88929 | 73.25989 | 193.64979 | 381.6 | 27.4 | 193 | 7 | 15:42 | 05:15 | 04:37 |
| 162.25 | 114 | 46.64460 | 239.00510 | 73.75928 | 214.43982 | 455.0 | 31.5 | 178 | 7 | 22:10 | 11:43 | 12:28 |
| 178.25 | 115 | 21.92360 | 214.28410 | 70.43271 | 195.20139 | 309.2 | 22.9 | 202 | 7 | 23:48 | 13:20 | 12:48 |
| 89.25 | 124 | 159.43429 | 351.79479 | 71.22366 | 204.16077 | 39.4 | 3.1 | 223 | 8 | 14:47 | 04:20 | 04:24 |
| 105.25 | 125 | 134.71329 | 327.07379 | 75.31969 | 187.41984 | 660.2 | 41.0 | 105 | 8 | 16:25 | 05:58 | 04:54 |
| 169.25 | 129 | 35.82920 | 228.18970 | 72.00934 | 206.79831 | 142.4 | 11.1 | 220 | 8 | 22:53 | 12:25 | 12:40 |
| 185.25 | 130 | 11.10820 | 203.46870 | 69.82705 | 185.16541 | 684.1 | 41.9 | 90 | 8 | 00:31 | 14:04 | 12:51 |
| 80.25 | 138 | 173.33989 | 5.70041 | 70.01887 | 216.42478 | 507.3 | 34.3 | 163 | 9 | 13:52 | 03:25 | 04:18 |
| 96.25 | 139 | 148.61889 | 340.97939 | 72.78357 | 195.86262 | 293.4 | 21.9 | 206 | 9 | 15:30 | 05:03 | 04:33 |
| 160.25 | 143 | 49.73480 | 242.09530 | 74.38102 | 216.19906 | 536.2 | 35.6 | 157 | 9 | 21:58 | 11:30 | 12:22 |
| 176.25 | 144 | 25.01370 | 217.37420 | 70.70672 | 197.92081 | 205.1 | 15.7 | 214 | 9 | 23:35 | 13:08 | 12:47 |
| 87.25 | 153 | 162.52449 | 354.88499 | 70.89673 | 206.78244 | 140.1 | 10.9 | 219 | 10 | 14:35 | 04:08 | 04:22 |
| 103.25 | 154 | 137.80339 | 330.16389 | 74.71278 | 189.00366 | 585.7 | 37.9 | 140 | 10 | 16:13 | 05:45 | 04:49 |
| 167.25 | 158 | 38.91930 | 231.27980 | 72.49180 | 209.08663 | 235.8 | 17.9 | 213 | 10 | 22:40 | 12:13 | 12:37 |
| 183.25 | 159 | 14.19830 | 206.55880 | 69.93745 | 188.11736 | 575.7 | 37.5 | 142 | 10 | 00:18 | 13:51 | 12:51 |
| 78.25 | 167 | 176.42999 | 8.79051 | 69.85336 | 219.30652 | 615.2 | 39.2 | 127 | 11 | 13:40 | 03:12 | 04:17 |
| 94.25 | 168 | 151.70899 | 344.06949 | 72.30333 | 198.12345 | 202.0 | 15.5 | 216 | 11 | 15:18 | 04:51 | 04:30 |
| 158.25 | 172 | 52.82490 | 245.18540 | 74.94280 | 217.97219 | 613.4 | 39.1 | 128 | 11 | 21:46 | 11:18 | 12:17 |
| 174.25 | 173 | 28.10390 | 220.46440 | 71.03439 | 200.55186 | 103.0 | 8.1 | 221 | 11 | 23:23 | 12:56 | 12:45 |
| 85.25 | 182 | 165.61459 | 357.97509 | 70.56853 | 209.42003 | 243.0 | 18.4 | 211 | 12 | 14:23 | 03:55 | 04:20 |
| 101.25 | 183 | 140.89359 | 333.25409 | 74.09592 | 190.70460 | 507.0 | 34.2 | 165 | 12 | 16:00 | 05:33 | 04:43 |
| 165.25 | 187 | 42.00940 | 234.36990 | 72.97054 | 211.32910 | 326.0 | 24.0 | 202 | 12 | 22:28 | 12:01 | 12:33 |
| 181.25 | 188 | 17.28840 | 209.64890 | 70.10282 | 190.99731 | 468.2 | 32.3 | 174 | 12 | 00:06 | 13:39 | 12:50 |
| 76.25 | 196 | 179.52019 | 11.88071 | 69.79812 | 222.32803 | 723.9 | 43.4 | 56 | 13 | 13:27 | 03:00 | 04:17 |
| 92.25 | 197 | 154.79909 | 347.15959 | 71.81950 | 200.42882 | 107.6 | 8.4 | 221 | 13 | 15:06 | 04:38 | 04:27 |
| 156.25 | 201 | 55.91500 | 248.27550 | 75.59536 | 219.37325 | 686.3 | 42.0 | 89 | 13 | 21:33 | 11:06 | 12:11 |
| 172.25 | 202 | 31.19400 | 223.55450 | 71.41503 | 203.08555 | 4.4 | 0.3 | 223 | 13 | 23:11 | 12:44 | 12:43 |
| 83.25 | 211 | 168.70469 | 1.06521 | 70.29410 | 212.14475 | 347.7 | 25.4 | 197 | 14 | 14:10 | 03:43 | 04:19 |
| 99.25 | 212 | 143.98369 | 336.34419 | 73.52269 | 192.61417 | 424.3 | 29.9 | 185 | 14 | 15:48 | 05:21 | 04:39 |
| 163.25 | 216 | 45.09960 | 237.46010 | 73.49771 | 213.41934 | 412.9 | 29.2 | 188 | 14 | 22:16 | 11:49 | 12:30 |
| 179.25 | 217 | 20.37850 | 212.73900 | 70.32288 | 193.80163 | 361.8 | 26.2 | 195 | 14 | 23:54 | 13:27 | 12:49 |
| 90.25 | 226 | 157.88929 | 350.24979 | 71.44087 | 202.93742 | 10.3 | 0.8 | 224 | 15 | 14:53 | 04:26 | 04:25 |
| 106.25 | 227 | 133.16819 | 325.52869 | 75.66862 | 186.81251 | 695.8 | 42.3 | 82 | 15 | 16:31 | 06:04 | 04:58 |
| 170.25 | 231 | 34.28410 | 226.64460 | 71.79379 | 205.59570 | 94.6 | 7.4 | 222 | 15 | 22:59 | 12:31 | 12:41 |

| Table III. ARM Validation Site: Darwin, Australia (off-shore); Lat -12.320; Lon 130.780 Orbits in RED are not normally available. |
| --- |
| WRS Path | TES Orbit | Descending Node (deg) | Ascending Node (deg) | S/C Lat (deg) | S/C Lon (deg) | Miss Distance (km) | Min. Nadir Angle (deg) | Obs. Time (secs) | UTC Day | UTC of Closest Approach | LMST @ Target | LMST @ S/C |
| 1.25 | 2 | 295.39998 | 127.76051 | -12.51798 | 128.63728 | 233.9 | 18.2 | 212 | 0 | 05:10 | 13:54 | 13:45 |
| 120.25 | 24 | 111.53729 | 303.89780 | -12.73232 | 135.17909 | 480.2 | 33.5 | 171 | 1 | 18:22 | 03:06 | 03:23 |
| 232.25 | 31 | 298.49008 | 130.85061 | -12.21786 | 131.70281 | 101.0 | 8.1 | 221 | 2 | 04:58 | 13:41 | 13:45 |
| 127.25 | 39 | 100.72189 | 293.08240 | -11.89196 | 124.43244 | 692.4 | 42.9 | 86 | 2 | 19:05 | 03:49 | 03:23 |
| 230.25 | 60 | 301.58028 | 133.94081 | -12.03778 | 134.77831 | 436.1 | 31.2 | 182 | 4 | 04:46 | 13:29 | 13:45 |
| 125.25 | 68 | 103.81199 | 296.17250 | -12.07204 | 127.50788 | 357.0 | 26.5 | 196 | 4 | 18:53 | 03:36 | 03:23 |
| 123.25 | 97 | 106.90209 | 299.26260 | -12.31214 | 130.57837 | 21.9 | 1.8 | 223 | 6 | 18:41 | 03:24 | 03:23 |
| 2.25 | 104 | 293.85488 | 126.21541 | -12.63803 | 127.10204 | 401.3 | 29.2 | 188 | 7 | 05:17 | 14:00 | 13:45 |
| 121.25 | 126 | 109.99229 | 302.35280 | -12.61227 | 133.64396 | 312.9 | 23.7 | 203 | 8 | 18:29 | 03:12 | 03:23 |
| 233.25 | 133 | 296.94508 | 129.30561 | -12.33791 | 130.16762 | 66.6 | 5.4 | 223 | 9 | 05:04 | 13:47 | 13:45 |
| 119.25 | 155 | 113.08239 | 305.44290 | -12.85236 | 136.71430 | 647.3 | 41.2 | 112 | 10 | 18:16 | 02:59 | 03:23 |
| 231.25 | 162 | 300.03518 | 132.39571 | -12.15783 | 133.24300 | 268.5 | 20.7 | 208 | 11 | 04:52 | 13:35 | 13:45 |
| 126.25 | 170 | 102.26699 | 294.62750 | -12.01201 | 125.96777 | 524.7 | 35.8 | 159 | 11 | 18:59 | 03:42 | 03:23 |
| 229.25 | 191 | 303.12528 | 135.48581 | -11.91772 | 136.31353 | 603.8 | 39.4 | 132 | 13 | 04:40 | 13:23 | 13:45 |
| 124.25 | 199 | 105.35709 | 297.71760 | -12.19209 | 129.04318 | 189.4 | 15.0 | 216 | 13 | 18:47 | 03:30 | 03:23 |
| 3.25 | 206 | 292.30988 | 124.67041 | -12.75808 | 125.56691 | 568.5 | 37.8 | 145 | 14 | 05:23 | 14:06 | 13:45 |
| 122.25 | 228 | 108.44719 | 300.80770 | -12.43219 | 132.11364 | 145.5 | 11.6 | 218 | 15 | 18:35 | 03:18 | 03:23 |

| Table IV. ARM Validation Site: Manus Island (off-shore); Lat -2.180; Lon 147.45 Orbits in RED are not normally available. |
| --- |
| WRS Path | TES Orbit | Descending Node (deg) | Ascending Node (deg) | S/C Lat (deg) | S/C Lon (deg) | Miss Distance (km) | Min. Nadir Angle (deg) | Obs. Time (secs) | UTC Day | UTC of Closest Approach | LMST @ Target | LMST @ S/C |
| 218.25 | 1 | 320.12098 | 152.48151 | -1.770205 | 152.52389 | 566.3 | 37.8 | 147 | 0 | 03:35 | 13:24 | 13:45 |
| 113.25 | 9 | 122.35279 | 314.7133 | -2.104758 | 146.82148 | 70.4 | 5.7 | 222 | 0 | 17:36 | 03:26 | 03:23 |
| 225.25 | 16 | 309.30558 | 141.66611 | -2.610965 | 141.77164 | 633.4 | 40.7 | 120 | 1 | 04:18 | 14:07 | 13:45 |
| 111.25 | 38 | 125.44289 | 317.8034 | -2.344975 | 149.89353 | 272.4 | 21 | 208 | 2 | 17:24 | 03:14 | 03:23 |
| 223.25 | 45 | 312.39568 | 144.75621 | -2.370749 | 144.84369 | 290.7 | 22.2 | 206 | 3 | 04:05 | 13:55 | 13:45 |
| 109.25 | 67 | 128.53299 | 320.89349 | -2.585191 | 152.96557 | 615.1 | 39.9 | 128 | 4 | 17:12 | 03:01 | 03:23 |
| 221.25 | 74 | 315.48578 | 147.84631 | -2.130532 | 147.91574 | 52.1 | 4.2 | 222 | 5 | 03:53 | 13:43 | 13:45 |
| 116.25 | 82 | 117.71759 | 310.0781 | -1.804486 | 142.20882 | 584.6 | 38.6 | 141 | 5 | 17:55 | 03:44 | 03:23 |
| 219.25 | 103 | 318.57598 | 150.93651 | -1.890315 | 150.9879 | 394.9 | 28.8 | 189 | 7 | 03:41 | 13:31 | 13:45 |
| 114.25 | 111 | 120.80769 | 313.1682 | -1.984649 | 145.28539 | 241.8 | 18.8 | 212 | 7 | 17:42 | 03:32 | 03:23 |
| 112.25 | 140 | 123.89789 | 316.2584 | -2.224867 | 148.35755 | 101.1 | 8.2 | 222 | 9 | 17:30 | 03:20 | 03:23 |
| 224.25 | 147 | 310.85058 | 143.21111 | -2.490858 | 143.30761 | 462 | 32.6 | 176 | 10 | 04:11 | 14:01 | 13:45 |
| 110.25 | 169 | 126.98799 | 319.34849 | -2.465083 | 151.4296 | 443.8 | 31.6 | 180 | 11 | 17:18 | 03:08 | 03:23 |
| 222.25 | 176 | 313.94078 | 146.30131 | -2.250641 | 146.37976 | 119.3 | 9.6 | 220 | 12 | 03:59 | 13:49 | 13:45 |
| 220.25 | 205 | 317.03088 | 149.39141 | -2.010424 | 149.45182 | 223.5 | 17.5 | 213 | 14 | 03:47 | 13:37 | 13:45 |
| 115.25 | 213 | 119.26269 | 311.6232 | -1.924595 | 143.7449 | 413.2 | 29.9 | 187 | 14 | 17:48 | 03:38 | 03:23 |

| Table V. ARM Validation Site: Nauru Island (off-shore); Lat -0.500; Lon 166.820 Orbits in RED are not normally available. |
| --- |
| WRS Path | TES Orbit | Descending Node (deg) | Ascending Node (deg) | S/C Lat (deg) | S/C Lon (deg) | Miss Distance (km) | Min. Nadir Angle (deg) | Obs. Time (secs) | UTC Day | UTC of Closest Approach | LMST @ Target | LMST @ S/C |
| 97.25 | 8 | 147.07379 | 339.43429 | -0.84361 | 171.63706 | 537.6 | 36.4 | 156 | 0 | 15:57 | 03:04 | 03:24 |
| 209.25 | 15 | 334.02658 | 166.38710 | -0.50905 | 166.33495 | 54.0 | 4.4 | 223 | 1 | 02:39 | 13:47 | 13:45 |
| 104.25 | 23 | 136.25839 | 328.61889 | -0.06289 | 160.88015 | 663.0 | 41.8 | 105 | 1 | 16:40 | 03:47 | 03:24 |
| 207.25 | 44 | 337.11668 | 169.47720 | -0.32889 | 169.41155 | 289.1 | 22.1 | 206 | 3 | 02:27 | 13:34 | 13:45 |
| 102.25 | 52 | 139.34849 | 331.70899 | -0.30311 | 163.95225 | 320.0 | 24.2 | 203 | 3 | 16:28 | 03:35 | 03:24 |
| 205.25 | 73 | 340.20688 | 172.56740 | -0.08867 | 172.48376 | 632.1 | 40.6 | 120 | 5 | 02:15 | 13:22 | 13:45 |
| 100.25 | 81 | 142.43859 | 334.79909 | -0.48328 | 167.02886 | 23.3 | 1.9 | 224 | 5 | 16:15 | 03:23 | 03:24 |
| 212.25 | 88 | 329.39138 | 161.75190 | -0.86938 | 161.72675 | 568.4 | 37.9 | 146 | 6 | 02:58 | 14:05 | 13:45 |
| 98.25 | 110 | 145.52879 | 337.88929 | -0.72350 | 170.10106 | 366.1 | 27.1 | 196 | 7 | 16:03 | 03:10 | 03:24 |
| 210.25 | 117 | 332.48148 | 164.84200 | -0.62916 | 164.79885 | 225.4 | 17.6 | 213 | 8 | 02:45 | 13:53 | 13:45 |
| 96.25 | 139 | 148.61889 | 340.97939 | -0.96372 | 173.17316 | 709.1 | 43.6 | 74 | 9 | 15:51 | 02:58 | 03:24 |
| 208.25 | 146 | 335.57168 | 167.93220 | -0.38894 | 167.87105 | 117.7 | 9.5 | 221 | 10 | 02:33 | 13:40 | 13:45 |
| 103.25 | 154 | 137.80339 | 330.16389 | -0.18300 | 162.41615 | 491.5 | 34.2 | 169 | 10 | 16:34 | 03:41 | 03:24 |
| 206.25 | 175 | 338.66178 | 171.02230 | -0.20878 | 170.94766 | 460.6 | 32.5 | 176 | 12 | 02:21 | 13:28 | 13:45 |
| 101.25 | 183 | 140.89359 | 333.25409 | -0.36317 | 165.49286 | 148.5 | 11.9 | 220 | 12 | 16:22 | 03:29 | 03:24 |
| 99.25 | 212 | 143.98369 | 336.34419 | -0.60339 | 168.56496 | 194.6 | 15.4 | 216 | 14 | 16:09 | 03:17 | 03:24 |
| 211.25 | 219 | 330.93648 | 163.29700 | -0.74927 | 163.26285 | 396.9 | 28.9 | 189 | 15 | 02:52 | 13:59 | 13:45 |

| Table VI. ARM Validation Site: Southern Great Plains; Lat 36.617; Lon 262.500 Orbits in RED are not normally available. |
| --- |
| WRS Path | TES Orbit | Descending Node (deg) | Ascending Node (deg) | S/C Lat (deg) | S/C Lon (deg) | Miss Distance (km) | Min. Nadir Angle (deg) | Obs. Time (secs) | UTC Day | UTC of Closest Approach | LMST @ Target | LMST @ S/C |
| 145.25 | 11 | 72.91070 | 265.27120 | 36.54315 | 261.58222 | 82.4 | 6.6 | 222 | 0 | 20:14 | 13:44 | 13:40 |
| 40.25 | 19 | 235.14249 | 67.50301 | 36.51188 | 263.36709 | 78.3 | 6.3 | 222 | 1 | 09:54 | 03:24 | 03:28 |
| 143.25 | 40 | 76.00090 | 268.36140 | 36.84168 | 264.62587 | 191.1 | 15.0 | 216 | 2 | 20:02 | 13:32 | 13:40 |
| 38.25 | 48 | 238.23259 | 70.59311 | 36.27302 | 266.42037 | 352.7 | 26.0 | 197 | 3 | 09:42 | 03:12 | 03:28 |
| 45.25 | 63 | 227.41719 | 59.77771 | 37.46707 | 255.79244 | 602.6 | 39.1 | 133 | 4 | 10:25 | 03:55 | 03:28 |
| 141.25 | 69 | 79.09100 | 271.45150 | 37.25957 | 267.64991 | 463.1 | 32.4 | 176 | 4 | 19:50 | 13:20 | 13:40 |
| 36.25 | 77 | 241.32268 | 73.68321 | 36.09386 | 269.48307 | 627.9 | 40.1 | 121 | 5 | 09:30 | 03:00 | 03:28 |
| 148.25 | 84 | 68.27550 | 260.63600 | 36.24457 | 256.99305 | 494.3 | 34.0 | 167 | 5 | 20:33 | 14:03 | 13:40 |
| 43.25 | 92 | 230.50729 | 62.86781 | 37.04923 | 258.81596 | 331.3 | 24.7 | 200 | 6 | 10:13 | 03:43 | 03:28 |
| 146.25 | 113 | 71.36570 | 263.72620 | 36.42372 | 260.05569 | 219.5 | 17.0 | 213 | 7 | 20:20 | 13:50 | 13:40 |
| 41.25 | 121 | 233.59739 | 65.95791 | 36.69101 | 261.84983 | 58.6 | 4.7 | 222 | 8 | 10:00 | 03:30 | 03:28 |
| 144.25 | 142 | 74.45580 | 266.81630 | 36.72227 | 263.09945 | 54.7 | 4.4 | 223 | 9 | 20:08 | 13:38 | 13:40 |
| 39.25 | 150 | 236.68759 | 69.04811 | 36.39246 | 264.89374 | 215.4 | 16.7 | 214 | 10 | 09:48 | 03:18 | 03:28 |
| 142.25 | 171 | 77.54590 | 269.90640 | 37.08048 | 266.13325 | 327.3 | 24.4 | 201 | 11 | 19:56 | 13:26 | 13:40 |
| 37.25 | 179 | 239.77768 | 72.13821 | 36.21331 | 267.95632 | 490.2 | 33.8 | 168 | 12 | 09:36 | 03:06 | 03:28 |
| 149.25 | 186 | 66.73050 | 259.09100 | 36.12514 | 255.46631 | 631.9 | 40.3 | 120 | 12 | 20:39 | 14:09 | 13:41 |
| 44.25 | 194 | 228.96219 | 61.32271 | 37.22831 | 257.29927 | 467.2 | 32.6 | 175 | 13 | 10:19 | 03:49 | 03:28 |
| 140.25 | 200 | 80.63609 | 272.99660 | 37.49833 | 269.15679 | 598.6 | 38.9 | 135 | 13 | 19:43 | 13:13 | 13:40 |
| 147.25 | 215 | 69.82060 | 262.18110 | 36.30429 | 258.52898 | 356.8 | 26.3 | 196 | 14 | 20:26 | 13:56 | 13:40 |
| 42.25 | 223 | 232.05239 | 64.41291 | 36.87013 | 260.33285 | 195.1 | 15.3 | 216 | 15 | 10:07 | 03:37 | 03:28 |

| Table VII. NDSC Validation Site: Hilo, Hawai'I (off-shore); Lat 19.800; Lon 205.000 Orbits in RED are not normally available. |
| --- |
| WRS Path | TES Orbit | Descending Node (deg) | Ascending Node (deg) | S/C Lat (deg) | S/C Lon (deg) | Miss Distance (km) | Min. Nadir Angle (deg) | Obs. Time (secs) | UTC Day | UTC of Closest Approach | LMST @ Target | LMST @ S/C |
| 81.25 | 7 | 171.79479 | 4.15531 | 20.46926 | 198.09193 | 725.5 | 44.0 | 57 | 0 | 14:12 | 03:52 | 03:25 |
| 72.25 | 21 | 185.70039 | 18.06091 | 19.32977 | 211.89048 | 724.3 | 44.0 | 57 | 1 | 13:17 | 02:57 | 03:24 |
| 184.25 | 28 | 12.65320 | 205.01370 | 19.72104 | 203.32763 | 175.4 | 13.9 | 217 | 1 | 00:10 | 13:50 | 13:44 |
| 79.25 | 36 | 174.88499 | 7.24551 | 20.16942 | 201.15370 | 404.3 | 29.3 | 188 | 2 | 14:00 | 03:40 | 03:24 |
| 182.25 | 57 | 15.74330 | 208.10380 | 19.96093 | 206.39522 | 147.1 | 11.7 | 219 | 3 | 23:58 | 13:38 | 13:44 |
| 77.25 | 65 | 177.97509 | 10.33561 | 19.86956 | 204.21555 | 82.5 | 6.6 | 222 | 4 | 13:48 | 03:28 | 03:24 |
| 180.25 | 86 | 18.83350 | 211.19400 | 20.26079 | 209.45712 | 468.8 | 32.9 | 175 | 5 | 23:46 | 13:26 | 13:44 |
| 75.25 | 94 | 181.06519 | 13.42571 | 19.62966 | 207.28319 | 239.9 | 18.6 | 212 | 6 | 13:35 | 03:15 | 03:24 |
| 187.25 | 101 | 8.01800 | 200.37850 | 19.42116 | 198.72039 | 659.6 | 41.6 | 105 | 6 | 00:29 | 14:09 | 13:44 |
| 73.25 | 123 | 184.15539 | 16.51591 | 19.38975 | 210.35105 | 562.8 | 37.5 | 147 | 8 | 13:23 | 03:03 | 03:24 |
| 185.25 | 130 | 11.10820 | 203.46870 | 19.60109 | 201.79383 | 336.6 | 25.2 | 199 | 8 | 00:17 | 13:57 | 13:44 |
| 80.25 | 138 | 173.33989 | 5.70041 | 20.28936 | 199.61995 | 565.0 | 37.6 | 147 | 9 | 14:06 | 03:46 | 03:24 |
| 183.25 | 159 | 14.19830 | 206.55880 | 19.84099 | 204.86149 | 15.2 | 1.2 | 223 | 10 | 00:04 | 13:44 | 13:44 |
| 78.25 | 167 | 176.42999 | 8.79051 | 19.98950 | 202.68173 | 243.5 | 18.9 | 211 | 11 | 13:54 | 03:34 | 03:24 |
| 181.25 | 188 | 17.28840 | 209.64890 | 20.08088 | 207.92902 | 308.0 | 23.3 | 204 | 12 | 23:52 | 13:32 | 13:44 |
| 76.25 | 196 | 179.52019 | 11.88071 | 19.74961 | 205.74941 | 78.7 | 6.3 | 222 | 13 | 13:41 | 03:21 | 03:24 |
| 179.25 | 217 | 20.37850 | 212.73900 | 20.44070 | 210.98505 | 629.4 | 40.4 | 121 | 14 | 23:40 | 13:20 | 13:44 |
| 74.25 | 225 | 182.61029 | 14.97081 | 19.50971 | 208.81711 | 401.3 | 29.1 | 188 | 15 | 13:29 | 03:09 | 03:24 |
| 186.25 | 232 | 9.56310 | 201.92360 | 19.48113 | 200.25991 | 498.0 | 34.4 | 166 | 15 | 00:23 | 14:03 | 13:44 |

| Table VIII. NDSC Validation Site: Lauder, New Zealand; Lat -45.050; Lon 169.680 Orbits in RED are not normally available. |
| --- |
| WRS Path | TES Orbit | Descending Node (deg) | Ascending Node (deg) | S/C Lat (deg) | S/C Lon (deg) | Miss Distance (km) | Min. Nadir Angle (deg) | Obs. Time (secs) | UTC Day | UTC of Closest Approach | LMST @ Target | LMST @ S/C |
| 97.25 | 8 | 147.07379 | 339.43429 | -44.73773 | 166.59347 | 245.3 | 18.8 | 210 | 0 | 16:09 | 03:28 | 03:16 |
| 209.25 | 15 | 334.02658 | 166.38710 | -44.82268 | 171.42223 | 139.2 | 11.0 | 219 | 1 | 02:27 | 13:46 | 13:53 |
| 216.25 | 30 | 323.21118 | 155.57171 | -46.36707 | 160.95874 | 692.3 | 42.5 | 86 | 2 | 03:10 | 14:29 | 13:54 |
| 95.25 | 37 | 150.16389 | 342.52439 | -45.03489 | 169.61810 | 4.9 | 0.4 | 224 | 2 | 15:57 | 03:16 | 03:15 |
| 207.25 | 44 | 337.11668 | 169.47720 | -44.58492 | 174.46039 | 380.2 | 27.6 | 191 | 3 | 02:15 | 13:33 | 13:53 |
| 214.25 | 59 | 326.30128 | 158.66181 | -45.83268 | 163.92414 | 457.3 | 32.0 | 178 | 4 | 02:58 | 14:16 | 13:53 |
| 93.25 | 66 | 153.25409 | 345.61459 | -45.45080 | 172.61512 | 234.1 | 18.0 | 213 | 4 | 15:45 | 03:03 | 03:15 |
| 205.25 | 73 | 340.20688 | 172.56740 | -44.46602 | 177.52483 | 622.2 | 39.8 | 124 | 5 | 02:02 | 13:21 | 13:52 |
| 100.25 | 81 | 142.43859 | 334.79909 | -44.44051 | 162.02286 | 607.9 | 39.2 | 130 | 5 | 16:28 | 03:46 | 03:16 |
| 212.25 | 88 | 329.39138 | 161.75190 | -45.35748 | 166.90599 | 220.1 | 17.0 | 213 | 6 | 02:45 | 14:04 | 13:53 |
| 91.25 | 95 | 156.34419 | 348.70469 | -45.86658 | 175.61022 | 471.2 | 32.7 | 174 | 6 | 15:32 | 02:51 | 03:15 |
| 98.25 | 110 | 145.52879 | 337.88929 | -44.61885 | 165.07441 | 366.0 | 26.7 | 194 | 7 | 16:15 | 03:34 | 03:16 |
| 210.25 | 117 | 332.48148 | 164.84200 | -45.00097 | 169.91646 | 19.1 | 1.5 | 223 | 8 | 02:33 | 13:52 | 13:53 |
| 89.25 | 124 | 159.43429 | 351.79479 | -46.46032 | 178.56135 | 706.1 | 43.0 | 75 | 8 | 15:20 | 02:39 | 03:14 |
| 96.25 | 139 | 148.61889 | 340.97939 | -44.85660 | 168.11249 | 125.0 | 9.9 | 220 | 9 | 16:03 | 03:22 | 03:15 |
| 208.25 | 146 | 335.57168 | 167.93220 | -44.70380 | 172.94129 | 259.5 | 19.8 | 209 | 10 | 02:21 | 13:40 | 13:53 |
| 215.25 | 161 | 324.75618 | 157.11671 | -46.07022 | 162.43407 | 575.1 | 37.8 | 143 | 11 | 03:04 | 14:22 | 13:53 |
| 94.25 | 168 | 151.70899 | 344.06949 | -45.21315 | 171.12348 | 114.8 | 9.1 | 220 | 11 | 15:51 | 03:09 | 03:15 |
| 206.25 | 175 | 338.66178 | 171.02230 | -44.52547 | 175.99259 | 501.1 | 34.2 | 166 | 12 | 02:09 | 13:27 | 13:52 |
| 101.25 | 183 | 140.89359 | 333.25409 | -44.44051 | 160.47786 | 729.1 | 43.9 | 51 | 12 | 16:34 | 03:53 | 03:16 |
| 213.25 | 190 | 327.84638 | 160.20690 | -45.59510 | 165.41482 | 338.9 | 25.1 | 200 | 13 | 02:51 | 14:10 | 13:53 |
| 92.25 | 197 | 154.79909 | 347.15959 | -45.62901 | 174.11963 | 352.9 | 25.9 | 198 | 13 | 15:39 | 02:57 | 03:15 |
| 99.25 | 212 | 143.98369 | 336.34419 | -44.55941 | 163.54223 | 486.8 | 33.5 | 169 | 14 | 16:21 | 03:40 | 03:16 |
| 211.25 | 219 | 330.93648 | 163.29700 | -45.17924 | 168.41111 | 100.7 | 8.0 | 222 | 15 | 02:39 | 13:58 | 13:53 |
| 90.25 | 226 | 157.88929 | 350.24979 | -46.16348 | 177.08632 | 589.0 | 38.4 | 139 | 15 | 15:26 | 02:45 | 03:15 |

| Table IX. NDSC Validation Site: Reunion Island (off-shore); Lat -21.400; Lon 55.500 Orbits in RED are not normally available. |
| --- |
| WRS Path | TES Orbit | Descending Node (deg) | Ascending Node (deg) | S/C Lat (deg) | S/C Lon (deg) | Miss Distance (km) | Min. Nadir Angle (deg) | Obs. Time (secs) | UTC Day | UTC of Closest Approach | LMST @ Target | LMST @ S/C |
| 49.25 | 5 | 221.23689 | 53.59741 | -21.39729 | 55.26275 | 24.6 | 2.0 | 223 | 0 | 10:05 | 13:47 | 13:46 |
| 168.25 | 27 | 37.37420 | 229.73470 | -21.85121 | 60.20067 | 488.8 | 33.9 | 170 | 1 | 23:22 | 03:04 | 03:22 |
| 47.25 | 34 | 224.32699 | 56.68751 | -21.15744 | 58.32960 | 294.6 | 22.4 | 205 | 2 | 09:52 | 13:34 | 13:46 |
| 175.25 | 42 | 26.55880 | 218.91930 | -21.01179 | 49.46694 | 627.3 | 40.3 | 122 | 2 | 00:05 | 03:47 | 03:22 |
| 45.25 | 63 | 227.41719 | 59.77771 | -20.97756 | 61.40245 | 614.1 | 39.8 | 127 | 4 | 09:40 | 13:22 | 13:46 |
| 173.25 | 71 | 29.64890 | 222.00940 | -21.19167 | 52.53968 | 307.8 | 23.3 | 203 | 4 | 23:52 | 03:34 | 03:22 |
| 52.25 | 78 | 216.60169 | 48.96221 | -21.87694 | 50.67444 | 501.9 | 34.6 | 166 | 5 | 10:23 | 14:05 | 13:46 |
| 171.25 | 100 | 32.73910 | 225.09960 | -21.43151 | 55.60661 | 11.6 | 0.9 | 223 | 6 | 23:40 | 03:22 | 03:22 |
| 50.25 | 107 | 219.69179 | 52.05231 | -21.51720 | 53.72933 | 183.8 | 14.5 | 217 | 7 | 10:11 | 13:53 | 13:46 |
| 169.25 | 129 | 35.82920 | 228.18970 | -21.73130 | 58.66744 | 329.8 | 24.7 | 201 | 8 | 23:28 | 03:10 | 03:22 |
| 48.25 | 136 | 222.78199 | 55.14251 | -21.27737 | 56.79621 | 135.0 | 10.8 | 219 | 9 | 09:59 | 13:41 | 13:46 |
| 167.25 | 158 | 38.91930 | 231.27980 | -22.09102 | 61.72214 | 647.6 | 41.1 | 113 | 10 | 23:15 | 02:57 | 03:22 |
| 46.25 | 165 | 225.87209 | 58.23261 | -21.03752 | 59.86313 | 454.4 | 32.1 | 177 | 11 | 09:46 | 13:28 | 13:46 |
| 174.25 | 173 | 28.10390 | 220.46440 | -21.07175 | 51.00626 | 467.5 | 32.8 | 174 | 11 | 23:58 | 03:40 | 03:22 |
| 53.25 | 180 | 215.05669 | 47.41721 | -22.05680 | 49.14717 | 660.6 | 41.6 | 106 | 12 | 10:29 | 14:11 | 13:46 |
| 172.25 | 202 | 31.19400 | 223.55450 | -21.31159 | 54.07316 | 148.2 | 11.8 | 219 | 13 | 23:46 | 03:28 | 03:22 |
| 51.25 | 209 | 218.14679 | 50.50731 | -21.69707 | 52.20190 | 342.9 | 25.6 | 199 | 14 | 10:17 | 13:59 | 13:46 |
| 170.25 | 231 | 34.28410 | 226.64460 | -21.55143 | 57.13993 | 170.6 | 13.5 | 218 | 15 | 23:34 | 03:16 | 03:22 |

| Table X. Stare & Transect Target: Ascension Island; Lat -7.950; Lon 345.630 Orbits in RED are not normally available. |
| --- |
| WRS Path | TES Orbit | Descending Node (deg) | Ascending Node (deg) | S/C Lat (deg) | S/C Lon (deg) | Miss Distance (km) | Min. Nadir Angle (deg) | Obs. Time (secs) | UTC Day | UTC of Closest Approach | LMST @ Target | LMST @ S/C |
| 218.25 | 1 | 320.12098 | 152.48151 | -7.86955 | 344.15079 | 163.3 | 13.0 | 217 | 0 | 04:27 | 03:29 | 03:23 |
| 97.25 | 8 | 147.07379 | 339.43429 | -8.43570 | 339.98476 | 624.3 | 40.3 | 124 | 0 | 15:05 | 14:07 | 13:45 |
| 216.25 | 30 | 323.21118 | 155.57171 | -8.10972 | 347.22231 | 176.4 | 14.0 | 217 | 2 | 04:14 | 03:17 | 03:23 |
| 95.25 | 37 | 150.16389 | 342.52439 | -8.13549 | 343.05145 | 284.9 | 21.8 | 207 | 2 | 14:53 | 13:55 | 13:45 |
| 214.25 | 59 | 326.30128 | 158.66181 | -8.34989 | 350.29369 | 515.8 | 35.4 | 162 | 4 | 04:02 | 03:05 | 03:23 |
| 93.25 | 66 | 153.25409 | 345.61459 | -7.89532 | 346.12297 | 54.7 | 4.4 | 222 | 4 | 14:40 | 13:43 | 13:45 |
| 221.25 | 74 | 315.48578 | 147.84631 | -7.50929 | 339.54352 | 673.1 | 42.2 | 98 | 5 | 04:45 | 03:48 | 03:23 |
| 91.25 | 95 | 156.34419 | 348.70469 | -7.65515 | 349.19444 | 394.5 | 28.8 | 189 | 6 | 14:28 | 13:31 | 13:45 |
| 219.25 | 103 | 318.57598 | 150.93651 | -7.74946 | 342.61511 | 333.2 | 25.0 | 200 | 7 | 04:33 | 03:35 | 03:23 |
| 217.25 | 132 | 321.66608 | 154.02661 | -7.98964 | 345.68655 | 7.6 | 0.6 | 223 | 9 | 04:21 | 03:23 | 03:23 |
| 96.25 | 139 | 148.61889 | 340.97939 | -8.25558 | 341.51581 | 454.7 | 32.2 | 177 | 9 | 14:59 | 14:01 | 13:45 |
| 215.25 | 161 | 324.75618 | 157.11671 | -8.22981 | 348.75796 | 346.1 | 25.8 | 198 | 11 | 04:08 | 03:11 | 03:23 |
| 94.25 | 168 | 151.70899 | 344.06949 | -8.01541 | 344.58721 | 115.2 | 9.3 | 220 | 11 | 14:47 | 13:49 | 13:45 |
| 213.25 | 190 | 327.84638 | 160.20690 | -8.46997 | 351.82942 | 685.4 | 42.7 | 90 | 13 | 03:56 | 02:59 | 03:23 |
| 92.25 | 197 | 154.79909 | 347.15959 | -7.77523 | 347.65865 | 224.5 | 17.6 | 213 | 13 | 14:34 | 13:37 | 13:45 |
| 220.25 | 205 | 317.03088 | 149.39141 | -7.62938 | 341.07932 | 503.1 | 34.7 | 166 | 14 | 04:39 | 03:42 | 03:23 |
| 90.25 | 226 | 157.88929 | 350.24979 | -7.59510 | 350.73488 | 564.4 | 37.7 | 146 | 15 | 14:22 | 13:24 | 13:45 |

| Table XI. Transect Target: Eastern Mediterranean; Lat 35.000; Lon 32.000 Orbits in RED are not normally available. |
| --- |
| WRS Path | TES Orbit | Descending Node (deg) | Ascending Node (deg) | S/C Lat (deg) | S/C Lon (deg) | Miss Distance (km) | Min. Nadir Angle (deg) | Obs. Time (secs) | UTC Day | UTC of Closest Approach | LMST @ Target | LMST @ S/C |
| 65.25 | 6 | 196.51589 | 28.87641 | 34.57190 | 25.48208 | 597.0 | 38.9 | 135 | 0 | 11:59 | 14:07 | 13:41 |
| 193.25 | 14 | 358.74758 | 191.10810 | 35.61604 | 26.83579 | 473.5 | 33.0 | 174 | 1 | 01:40 | 03:48 | 03:27 |
| 56.25 | 20 | 210.42149 | 42.78201 | 35.94596 | 39.18458 | 658.9 | 41.4 | 107 | 1 | 11:04 | 13:12 | 13:41 |
| 63.25 | 35 | 199.60599 | 31.96651 | 34.69141 | 28.55492 | 316.2 | 23.7 | 202 | 2 | 11:47 | 13:55 | 13:41 |
| 191.25 | 43 | 1.83780 | 194.19830 | 35.19787 | 29.86386 | 195.6 | 15.3 | 215 | 2 | 01:28 | 03:36 | 03:27 |
| 61.25 | 64 | 202.69609 | 35.05661 | 34.99017 | 31.60153 | 36.3 | 2.9 | 223 | 4 | 11:34 | 13:42 | 13:41 |
| 189.25 | 72 | 4.92790 | 197.28840 | 34.89914 | 32.91015 | 83.7 | 6.7 | 222 | 4 | 01:16 | 03:24 | 03:27 |
| 59.25 | 93 | 205.78629 | 38.14681 | 35.28890 | 34.64778 | 242.9 | 18.7 | 212 | 6 | 11:22 | 13:30 | 13:41 |
| 187.25 | 101 | 8.01800 | 200.37850 | 34.66013 | 35.96554 | 363.9 | 26.7 | 195 | 6 | 01:03 | 03:11 | 03:27 |
| 194.25 | 116 | 357.20258 | 189.56310 | 35.85496 | 25.32673 | 611.9 | 39.5 | 130 | 8 | 01:46 | 03:54 | 03:28 |
| 57.25 | 122 | 208.87639 | 41.23691 | 35.70705 | 37.67554 | 520.6 | 35.3 | 161 | 8 | 11:10 | 13:18 | 13:41 |
| 185.25 | 130 | 11.10820 | 203.46870 | 34.48085 | 39.02990 | 644.8 | 40.9 | 113 | 8 | 00:51 | 02:59 | 03:27 |
| 64.25 | 137 | 198.06089 | 30.42141 | 34.63166 | 27.01846 | 456.6 | 32.1 | 177 | 9 | 11:53 | 14:01 | 13:41 |
| 192.25 | 145 | 0.29270 | 192.65320 | 35.43683 | 28.35415 | 334.7 | 24.9 | 200 | 10 | 01:34 | 03:42 | 03:27 |
| 62.25 | 166 | 201.15109 | 33.51161 | 34.87067 | 30.07398 | 176.2 | 13.9 | 217 | 11 | 11:41 | 13:49 | 13:41 |
| 190.25 | 174 | 3.38280 | 195.74330 | 35.01864 | 31.38251 | 56.3 | 4.5 | 223 | 11 | 01:22 | 03:30 | 03:27 |
| 60.25 | 195 | 204.24119 | 36.60171 | 35.16941 | 33.12032 | 103.7 | 8.3 | 221 | 13 | 11:28 | 13:36 | 13:41 |
| 188.25 | 203 | 6.47300 | 198.83350 | 34.77963 | 34.43786 | 223.7 | 17.4 | 212 | 13 | 01:09 | 03:17 | 03:27 |
| 58.25 | 224 | 207.33129 | 39.69181 | 35.52785 | 36.15727 | 381.9 | 27.8 | 193 | 15 | 11:16 | 13:24 | 13:41 |
| 186.25 | 232 | 9.56310 | 201.92360 | 34.60037 | 37.50201 | 504.3 | 34.5 | 164 | 15 | 00:57 | 03:05 | 03:27 |

| Table XII. Transect Target: Middle East; Lat 25.000; Lon 45.000 Orbits in RED are not normally available. |
| --- |
| WRS Path | TES Orbit | Descending Node (deg) | Ascending Node (deg) | S/C Lat (deg) | S/C Lon (deg) | Miss Distance (km) | Min. Nadir Angle (deg) | Obs. Time (secs) | UTC Day | UTC of Closest Approach | LMST @ Target | LMST @ S/C |
| 49.25 | 5 | 221.23689 | 53.59741 | 25.715487 | 51.30821 | 639.1 | 40.7 | 117 | 0 | 10:18 | 13:18 | 13:43 |
| 177.25 | 13 | 23.4687 | 215.8292 | 24.605607 | 50.17963 | 524.9 | 35.7 | 159 | 0 | 00:04 | 03:04 | 03:25 |
| 56.25 | 20 | 210.42149 | 42.78201 | 24.696906 | 40.60192 | 445.3 | 31.6 | 179 | 1 | 11:01 | 14:01 | 13:43 |
| 184.25 | 28 | 12.6532 | 205.0137 | 25.564296 | 39.46648 | 560.1 | 37.3 | 149 | 1 | 00:47 | 03:47 | 03:25 |
| 54.25 | 49 | 213.51159 | 45.87211 | 24.936592 | 43.66661 | 134.7 | 10.7 | 219 | 3 | 10:48 | 13:48 | 13:43 |
| 182.25 | 57 | 15.7433 | 208.1038 | 25.20481 | 42.51789 | 251.1 | 19.4 | 211 | 3 | 00:35 | 03:35 | 03:25 |
| 52.25 | 78 | 216.60169 | 48.96221 | 25.176266 | 46.73115 | 175.5 | 13.9 | 217 | 5 | 10:36 | 13:36 | 13:43 |
| 180.25 | 86 | 18.8335 | 211.194 | 24.965137 | 45.5825 | 58.9 | 4.7 | 222 | 5 | 00:23 | 03:23 | 03:25 |
| 50.25 | 107 | 219.69179 | 52.05231 | 25.535754 | 49.78258 | 484.8 | 33.7 | 171 | 7 | 10:24 | 13:24 | 13:43 |
| 178.25 | 115 | 21.9236 | 214.2841 | 24.725453 | 48.64718 | 369.4 | 27.2 | 194 | 7 | 00:10 | 03:10 | 03:25 |
| 57.25 | 122 | 208.87639 | 41.23691 | 24.636983 | 39.06314 | 600.8 | 39.1 | 133 | 8 | 11:07 | 14:07 | 13:43 |
| 185.25 | 130 | 11.1082 | 203.4687 | 25.803937 | 37.94749 | 714.3 | 43.6 | 68 | 8 | 00:53 | 03:53 | 03:25 |
| 176.25 | 144 | 25.0137 | 217.3742 | 24.545682 | 51.71832 | 680.5 | 42.4 | 93 | 9 | 23:58 | 02:58 | 03:25 |
| 55.25 | 151 | 211.96649 | 44.32701 | 24.816751 | 42.13424 | 289.9 | 22.1 | 205 | 10 | 10:55 | 13:55 | 13:43 |
| 183.25 | 159 | 14.1983 | 206.5588 | 25.384556 | 40.99219 | 405.7 | 29.3 | 188 | 10 | 00:41 | 03:41 | 03:25 |
| 53.25 | 180 | 215.05669 | 47.41721 | 25.05643 | 45.19895 | 21 | 1.7 | 223 | 12 | 10:42 | 13:42 | 13:43 |
| 181.25 | 188 | 17.2884 | 209.6489 | 25.084975 | 44.05017 | 96.2 | 7.7 | 222 | 12 | 00:29 | 03:29 | 03:25 |
| 51.25 | 209 | 218.14679 | 50.50731 | 25.356013 | 48.25696 | 330.3 | 24.7 | 201 | 14 | 10:30 | 13:30 | 13:43 |
| 179.25 | 217 | 20.3785 | 212.739 | 24.845297 | 47.11477 | 214.1 | 16.7 | 214 | 14 | 00:17 | 03:17 | 03:25 |

| Table XIII. Transect Target: Southeastern US; Lat 35.000; Lon 265.000 Orbits in RED are not normally available. |
| --- |
| WRS Path | TES Orbit | Descending Node (deg) | Ascending Node (deg) | S/C Lat (deg) | S/C Lon (deg) | Miss Distance (km) | Min. Nadir Angle (deg) | Obs. Time (secs) | UTC Day | UTC of Closest Approach | LMST @ Target | LMST @ S/C |
| 145.25 | 11 | 72.9107 | 265.2712 | 34.751168 | 261.85094 | 288.6 | 21.9 | 206 | 0 | 20:14 | 13:54 | 13:41 |
| 40.25 | 19 | 235.14249 | 67.50301 | 35.197872 | 263.16854 | 168.1 | 13.2 | 218 | 1 | 09:55 | 03:35 | 03:27 |
| 143.25 | 40 | 76.0009 | 268.3614 | 34.990172 | 264.90632 | 8.6 | 0.7 | 224 | 2 | 20:01 | 13:41 | 13:41 |
| 38.25 | 48 | 238.23259 | 70.59311 | 34.899138 | 266.21484 | 111.3 | 8.9 | 220 | 3 | 09:42 | 03:22 | 03:27 |
| 141.25 | 69 | 79.091 | 271.4515 | 35.348636 | 267.94362 | 270.3 | 20.6 | 209 | 4 | 19:49 | 13:29 | 13:41 |
| 36.25 | 77 | 241.32268 | 73.68321 | 34.660126 | 269.27023 | 391.6 | 28.4 | 190 | 5 | 09:30 | 03:10 | 03:27 |
| 148.25 | 84 | 68.2755 | 260.636 | 34.512143 | 257.25027 | 709.9 | 43.3 | 71 | 5 | 20:32 | 14:12 | 13:41 |
| 43.25 | 92 | 230.50729 | 62.86781 | 35.795236 | 258.6224 | 584.7 | 38.3 | 140 | 6 | 10:13 | 03:53 | 03:28 |
| 139.25 | 98 | 82.18109 | 274.5416 | 35.766781 | 270.97124 | 547.9 | 36.6 | 153 | 6 | 19:37 | 13:17 | 13:41 |
| 34.25 | 106 | 244.41288 | 76.77341 | 34.480853 | 272.33459 | 672.5 | 41.9 | 98 | 7 | 09:18 | 02:58 | 03:27 |
| 146.25 | 113 | 71.3657 | 263.7262 | 34.631658 | 260.32324 | 428.9 | 30.5 | 182 | 7 | 20:20 | 14:00 | 13:41 |
| 41.25 | 121 | 233.59739 | 65.95791 | 35.377096 | 261.64996 | 307.3 | 23.1 | 204 | 8 | 10:01 | 03:41 | 03:27 |
| 144.25 | 142 | 74.4558 | 266.8163 | 34.870673 | 263.37867 | 148.5 | 11.8 | 219 | 9 | 20:07 | 13:47 | 13:41 |
| 39.25 | 150 | 236.68759 | 69.04811 | 35.018635 | 264.6873 | 28.6 | 2.3 | 223 | 10 | 09:49 | 03:29 | 03:27 |
| 142.25 | 171 | 77.5459 | 269.9064 | 35.16941 | 266.425 | 131 | 10.4 | 220 | 11 | 19:55 | 13:35 | 13:41 |
| 37.25 | 179 | 239.77768 | 72.13821 | 34.779634 | 267.74254 | 251.3 | 19.3 | 210 | 12 | 09:36 | 03:16 | 03:27 |
| 44.25 | 194 | 228.96219 | 61.32271 | 36.034141 | 257.11348 | 722.8 | 43.8 | 59 | 13 | 10:19 | 03:59 | 03:28 |
| 140.25 | 200 | 80.63609 | 272.9966 | 35.52785 | 269.46206 | 409.3 | 29.4 | 188 | 13 | 19:43 | 13:23 | 13:41 |
| 35.25 | 208 | 242.86778 | 75.22831 | 34.540612 | 270.79808 | 532 | 35.9 | 157 | 14 | 09:24 | 03:04 | 03:27 |
| 147.25 | 215 | 69.8206 | 262.1811 | 34.571901 | 258.78676 | 569.3 | 37.6 | 145 | 14 | 20:26 | 14:06 | 13:41 |
| 42.25 | 223 | 232.05239 | 64.41291 | 35.556307 | 260.13165 | 446.2 | 31.5 | 179 | 15 | 10:07 | 03:47 | 03:27 |
| 138.25 | 229 | 83.72619 | 276.0867 | 36.005689 | 272.4802 | 686.1 | 42.4 | 90 | 15 | 19:31 | 13:11 | 13:41 |

| Table XIV. Transect Target: Lake Tahoe North Shore; Lat 39.240; Lon 239.940 Orbits in RED are not normally available. |
| --- |
| WRS Path | TES Orbit | Descending Node (deg) | Ascending Node (deg) | S/C Lat (deg) | S/C Lon (deg) | Miss Distance (km) | Min. Nadir Angle (deg) | Obs. Time (secs) | UTC Day | UTC of Closest Approach | LMST @ Target | LMST @ S/C |
| 161.25 | 12 | 48.1897 | 240.5502 | 38.930317 | 236.47348 | 301.1 | 22.7 | 204 | 0 | 21:54 | 13:53 | 13:40 |
| 56.25 | 20 | 210.42149 | 42.78201 | 39.316571 | 239.10494 | 72.4 | 5.8 | 222 | 1 | 11:32 | 03:32 | 03:29 |
| 159.25 | 41 | 51.2798 | 243.6403 | 39.228525 | 239.51251 | 36.8 | 3 | 223 | 2 | 21:41 | 13:41 | 13:39 |
| 54.25 | 49 | 213.51159 | 45.87211 | 39.018376 | 242.14379 | 191.6 | 15 | 215 | 3 | 11:20 | 03:20 | 03:29 |
| 61.25 | 64 | 202.69609 | 35.05661 | 40.449295 | 231.57999 | 725.8 | 43.8 | 56 | 4 | 12:03 | 04:03 | 03:29 |
| 157.25 | 70 | 54.37 | 246.7305 | 39.586316 | 242.54063 | 226.6 | 17.5 | 213 | 4 | 21:29 | 13:29 | 13:39 |
| 52.25 | 78 | 216.60169 | 48.96221 | 38.779789 | 245.19334 | 456.6 | 32 | 177 | 5 | 11:08 | 03:08 | 03:29 |
| 164.25 | 85 | 43.5545 | 235.915 | 38.69172 | 231.87869 | 699.2 | 42.9 | 80 | 5 | 22:12 | 14:12 | 13:40 |
| 59.25 | 93 | 205.78629 | 38.14681 | 39.912825 | 234.57408 | 465.7 | 32.5 | 175 | 6 | 11:51 | 03:51 | 03:29 |
| 155.25 | 99 | 57.4601 | 249.8206 | 39.94404 | 245.56774 | 488.3 | 33.7 | 170 | 6 | 21:17 | 13:17 | 13:39 |
| 50.25 | 107 | 219.69179 | 52.05231 | 38.660485 | 248.2633 | 722.2 | 43.7 | 59 | 7 | 10:55 | 02:55 | 03:29 |
| 162.25 | 114 | 46.6446 | 239.0051 | 38.87067 | 234.93852 | 433.7 | 30.8 | 181 | 7 | 22:00 | 14:00 | 13:40 |
| 57.25 | 122 | 208.87639 | 41.23691 | 39.495466 | 237.59088 | 203.9 | 15.9 | 215 | 8 | 11:39 | 03:38 | 03:29 |
| 160.25 | 143 | 49.7348 | 242.0953 | 39.109247 | 237.98801 | 168.8 | 13.3 | 217 | 9 | 21:47 | 13:47 | 13:39 |
| 55.25 | 151 | 211.96649 | 44.32701 | 39.13766 | 240.61912 | 59.6 | 4.8 | 223 | 10 | 11:26 | 03:26 | 03:29 |
| 158.25 | 172 | 52.8249 | 245.1854 | 39.347796 | 241.03702 | 95.1 | 7.6 | 222 | 11 | 21:35 | 13:35 | 13:39 |
| 53.25 | 180 | 215.05669 | 47.41721 | 38.899086 | 243.66857 | 324 | 24.2 | 201 | 12 | 11:14 | 03:14 | 03:29 |
| 60.25 | 195 | 204.24119 | 36.60171 | 40.151275 | 233.07144 | 596 | 38.8 | 136 | 13 | 11:57 | 03:57 | 03:29 |
| 156.25 | 201 | 55.915 | 248.2755 | 39.765186 | 244.05425 | 357.7 | 26.3 | 197 | 13 | 21:23 | 13:23 | 13:39 |
| 51.25 | 209 | 218.14679 | 50.50731 | 38.720138 | 246.72836 | 589.4 | 38.5 | 137 | 14 | 11:02 | 03:01 | 03:29 |
| 163.25 | 216 | 45.0996 | 237.4601 | 38.751372 | 233.41372 | 566.4 | 37.4 | 146 | 14 | 22:06 | 14:06 | 13:40 |
| 58.25 | 224 | 207.33129 | 39.69181 | 39.733968 | 236.08751 | 335 | 24.9 | 200 | 15 | 11:45 | 03:44 | 03:29 |
| 154.25 | 230 | 59.0052 | 251.3657 | 40.242093 | 247.05964 | 618.5 | 39.7 | 127 | 15 | 21:11 | 13:10 | 13:39 |

| Table XV. Radiometric Target: Lake Tahoe, CA; Lat 39.100; Lon 239.970 Orbits in RED are not normally available. |
| --- |
| WRS Path | TES Orbit | Descending Node (deg) | Ascending Node (deg) | S/C Lat (deg) | S/C Lon (deg) | Miss Distance (km) | Min. Nadir Angle (deg) | Obs. Time (secs) | UTC Day | UTC of Closest Approach | LMST @ Target | LMST @ S/C |
| 161.25 | 12 | 48.18970 | 240.55020 | 38.81102 | 236.49373 | 302.2 | 22.7 | 204 | 0 | 21:54 | 13:53 | 13:40 |
| 56.25 | 20 | 210.42149 | 42.78201 | 39.19730 | 239.08437 | 77.1 | 6.2 | 222 | 1 | 11:32 | 03:32 | 03:29 |
| 159.25 | 41 | 51.27980 | 243.64030 | 39.10925 | 239.53301 | 37.7 | 3.0 | 223 | 2 | 21:41 | 13:41 | 13:39 |
| 54.25 | 49 | 213.51159 | 45.87211 | 38.89909 | 242.12347 | 187.4 | 14.7 | 216 | 3 | 11:20 | 03:20 | 03:29 |
| 157.25 | 70 | 54.37000 | 246.73050 | 39.40743 | 242.57178 | 226.6 | 17.5 | 213 | 4 | 21:29 | 13:29 | 13:39 |
| 52.25 | 78 | 216.60169 | 48.96221 | 38.66049 | 245.17320 | 452.9 | 31.8 | 177 | 5 | 11:08 | 03:08 | 03:29 |
| 164.25 | 85 | 43.55450 | 235.91500 | 38.57241 | 231.89876 | 701.2 | 42.9 | 78 | 5 | 22:12 | 14:12 | 13:40 |
| 59.25 | 93 | 205.78629 | 38.14681 | 39.79359 | 234.55301 | 471.3 | 32.8 | 174 | 6 | 11:51 | 03:51 | 03:29 |
| 155.25 | 99 | 57.46010 | 249.82060 | 39.82481 | 245.58884 | 488.8 | 33.7 | 170 | 6 | 21:17 | 13:17 | 13:39 |
| 50.25 | 107 | 219.69179 | 52.05231 | 38.54117 | 248.24326 | 719.0 | 43.6 | 62 | 7 | 10:56 | 02:55 | 03:28 |
| 162.25 | 114 | 46.64460 | 239.00510 | 38.69172 | 234.96879 | 435.0 | 30.8 | 182 | 7 | 22:00 | 14:00 | 13:40 |
| 57.25 | 122 | 208.87639 | 41.23691 | 39.37621 | 237.57016 | 208.9 | 16.2 | 214 | 8 | 11:39 | 03:38 | 03:29 |
| 160.25 | 143 | 49.73480 | 242.09530 | 38.93032 | 238.01858 | 169.6 | 13.3 | 217 | 9 | 21:47 | 13:47 | 13:40 |
| 55.25 | 151 | 211.96649 | 44.32701 | 39.01838 | 240.59869 | 55.0 | 4.4 | 223 | 10 | 11:26 | 03:26 | 03:29 |
| 158.25 | 172 | 52.82490 | 245.18540 | 39.22853 | 241.05761 | 94.8 | 7.6 | 222 | 11 | 21:35 | 13:35 | 13:39 |
| 53.25 | 180 | 215.05669 | 47.41721 | 38.77979 | 243.64834 | 320.0 | 23.9 | 202 | 12 | 11:14 | 03:14 | 03:29 |
| 60.25 | 195 | 204.24119 | 36.60171 | 40.03205 | 233.05016 | 601.8 | 39.0 | 134 | 13 | 11:57 | 03:57 | 03:29 |
| 156.25 | 201 | 55.91500 | 248.27550 | 39.64594 | 244.07519 | 357.9 | 26.3 | 197 | 13 | 21:23 | 13:23 | 13:39 |
| 51.25 | 209 | 218.14679 | 50.50731 | 38.60083 | 246.70827 | 585.9 | 38.3 | 138 | 14 | 11:02 | 03:02 | 03:29 |
| 163.25 | 216 | 45.09960 | 237.46010 | 38.63207 | 233.43384 | 568.0 | 37.5 | 145 | 14 | 22:06 | 14:06 | 13:40 |
| 58.25 | 224 | 207.33129 | 39.69181 | 39.55510 | 236.05617 | 340.3 | 25.2 | 199 | 15 | 11:45 | 03:45 | 03:29 |
| 154.25 | 230 | 59.00520 | 251.36570 | 40.06327 | 247.09164 | 619.3 | 39.7 | 126 | 15 | 21:11 | 13:11 | 13:39 |

| Table XVI. Volcano: Colima, Mexico; Lat 13.420; Lon 256.280 Orbits in RED are not normally available. |
| --- |
| WRS Path | TES Orbit | Descending Node (deg) | Ascending Node (deg) | S/C Lat (deg) | S/C Lon (deg) | Miss Distance (km) | Min. Nadir Angle (deg) | Obs. Time (secs) | UTC Day | UTC of Closest Approach | LMST @ Target | LMST @ S/C |
| 40.25 | 19 | 235.14249 | 67.50301 | 19.08986 | 261.31038 | 529.7 | 36.0 | 158 | 1 | 09:59 | 03:04 | 03:24 |
| 152.25 | 26 | 62.09530 | 254.45580 | 19.18124 | 252.81993 | 364.4 | 26.9 | 195 | 1 | 20:52 | 13:58 | 13:44 |
| 47.25 | 34 | 224.32699 | 56.68751 | 19.98950 | 250.57873 | 600.6 | 39.2 | 134 | 2 | 10:42 | 03:47 | 03:24 |
| 150.25 | 55 | 65.18540 | 257.54590 | 19.42116 | 255.88779 | 41.2 | 3.3 | 223 | 3 | 20:40 | 13:45 | 13:44 |
| 45.25 | 63 | 227.41719 | 59.77771 | 19.62966 | 253.63519 | 278.4 | 21.3 | 207 | 4 | 10:30 | 03:35 | 03:24 |
| 148.25 | 84 | 68.27550 | 260.63600 | 19.72104 | 258.94992 | 281.9 | 21.6 | 207 | 5 | 20:28 | 13:33 | 13:44 |
| 43.25 | 92 | 230.50729 | 62.86781 | 19.38975 | 256.70295 | 44.5 | 3.6 | 222 | 6 | 10:18 | 03:23 | 03:24 |
| 146.25 | 113 | 71.36570 | 263.72620 | 20.02090 | 262.01197 | 604.1 | 39.3 | 133 | 7 | 20:16 | 13:21 | 13:44 |
| 41.25 | 121 | 233.59739 | 65.95791 | 19.14984 | 259.77082 | 367.9 | 27.1 | 194 | 8 | 10:05 | 03:10 | 03:24 |
| 153.25 | 128 | 60.55020 | 252.91070 | 19.12126 | 251.28038 | 526.2 | 35.8 | 159 | 8 | 20:59 | 14:04 | 13:44 |
| 39.25 | 150 | 236.68759 | 69.04811 | 18.96989 | 262.84442 | 691.6 | 42.8 | 86 | 10 | 09:53 | 02:58 | 03:24 |
| 151.25 | 157 | 63.64030 | 256.00080 | 19.30120 | 254.35383 | 202.6 | 15.9 | 215 | 10 | 20:46 | 13:51 | 13:44 |
| 46.25 | 165 | 225.87209 | 58.23261 | 19.80958 | 252.10692 | 439.6 | 31.3 | 181 | 11 | 10:36 | 03:41 | 03:24 |
| 149.25 | 186 | 66.73050 | 259.09100 | 19.54111 | 257.42172 | 120.5 | 9.7 | 220 | 12 | 20:34 | 13:39 | 13:44 |
| 44.25 | 194 | 228.96219 | 61.32271 | 19.50971 | 255.16900 | 117.0 | 9.4 | 220 | 13 | 10:24 | 03:29 | 03:24 |
| 147.25 | 215 | 69.82060 | 262.18110 | 19.84099 | 260.48378 | 443.1 | 31.5 | 180 | 14 | 20:22 | 13:27 | 13:44 |
| 42.25 | 223 | 232.05239 | 64.41291 | 19.26980 | 258.23692 | 206.1 | 16.2 | 214 | 15 | 10:11 | 03:17 | 03:24 |
| 154.25 | 230 | 59.00520 | 251.36570 | 19.00130 | 249.74644 | 688.1 | 42.7 | 88 | 15 | 21:05 | 14:10 | 13:44 |

| Table XVII. Volcano: Erebus, Antarctica; Lat -77.525; Lon 167.120 Orbits in RED are not normally available. |
| --- |
| WRS Path | TES Orbit | Descending Node (deg) | Ascending Node (deg) | S/C Lat (deg) | S/C Lon (deg) | Miss Distance (km) | Min. Nadir Angle (deg) | Obs. Time (secs) | UTC Day | UTC of Closest Approach | LMST @ Target | LMST @ S/C |
| 218.25 | 1 | 320.12098 | 152.48151 | -75.74170 | 181.60847 | 419.5 | 29.6 | 184 | 0 | 03:14 | 14:22 | 15:20 |
| 1.25 | 2 | 295.39998 | 127.76051 | -77.99777 | 164.83197 | 75.1 | 5.9 | 222 | 0 | 04:52 | 16:00 | 15:51 |
| 17.25 | 3 | 270.67898 | 103.03951 | -80.38420 | 155.50106 | 400.6 | 28.5 | 166 | 0 | 06:30 | 17:38 | 16:52 |
| 33.25 | 4 | 245.95788 | 78.31841 | -81.68498 | 152.95961 | 538.4 | 35.7 | 93 | 0 | 09:46 | 20:55 | 19:58 |
| 49.25 | 5 | 221.23689 | 53.59741 | -81.18191 | 183.37873 | 521.3 | 34.9 | 105 | 0 | 11:24 | 22:32 | 23:37 |
| 65.25 | 6 | 196.51589 | 28.87641 | -79.65032 | 174.70010 | 288.2 | 21.5 | 206 | 0 | 13:02 | 00:10 | 00:41 |
| 81.25 | 7 | 171.79479 | 4.15531 | -76.92839 | 163.48197 | 111.1 | 8.7 | 220 | 0 | 14:40 | 01:48 | 01:34 |
| 97.25 | 8 | 147.07379 | 339.43429 | -75.27189 | 143.74863 | 653.6 | 40.7 | 108 | 0 | 16:18 | 03:27 | 01:53 |
| 225.25 | 16 | 309.30558 | 141.66611 | -76.56908 | 173.29784 | 186.6 | 14.4 | 216 | 1 | 03:57 | 15:05 | 15:30 |
| 8.25 | 17 | 284.58448 | 116.94501 | -79.24916 | 160.60692 | 240.1 | 18.2 | 212 | 1 | 05:34 | 16:43 | 16:17 |
| 24.25 | 18 | 259.86348 | 92.22401 | -81.00476 | 151.91197 | 494.7 | 33.6 | 121 | 1 | 07:12 | 18:21 | 17:20 |
| 40.25 | 19 | 235.14249 | 67.50301 | -81.76679 | 180.23878 | 535.6 | 35.6 | 92 | 1 | 10:29 | 21:37 | 22:30 |
| 56.25 | 20 | 210.42149 | 42.78201 | -80.61439 | 180.11883 | 436.5 | 30.5 | 149 | 1 | 12:07 | 23:15 | 00:07 |
| 72.25 | 21 | 185.70039 | 18.06091 | -78.41316 | 171.21912 | 136.7 | 10.7 | 220 | 1 | 13:45 | 00:53 | 01:10 |
| 88.25 | 22 | 160.97939 | 353.33989 | -76.01576 | 155.60079 | 336.3 | 24.6 | 199 | 1 | 15:23 | 02:31 | 01:45 |
| 216.25 | 30 | 323.21118 | 155.57171 | -75.59301 | 184.28697 | 489.5 | 33.3 | 168 | 2 | 03:01 | 14:10 | 15:18 |
| 232.25 | 31 | 298.49008 | 130.85061 | -77.64048 | 166.39789 | 21.5 | 1.7 | 223 | 2 | 04:39 | 15:48 | 15:45 |
| 15.25 | 32 | 273.76908 | 106.12961 | -80.15721 | 156.49575 | 369.5 | 26.6 | 179 | 2 | 06:17 | 17:26 | 16:43 |
| 31.25 | 33 | 249.04808 | 81.40861 | -81.56801 | 152.00202 | 538.5 | 35.7 | 96 | 2 | 09:34 | 20:43 | 19:42 |
| 47.25 | 34 | 224.32699 | 56.68751 | -81.38416 | 182.73484 | 529.1 | 35.3 | 101 | 2 | 11:12 | 22:20 | 23:23 |
| 63.25 | 35 | 199.60599 | 31.96651 | -79.90246 | 175.89339 | 324.7 | 23.9 | 193 | 2 | 12:50 | 23:58 | 00:33 |
| 79.25 | 36 | 174.88499 | 7.24551 | -77.25499 | 165.38564 | 51.6 | 4.1 | 223 | 2 | 14:28 | 01:36 | 01:29 |
| 95.25 | 37 | 150.16389 | 342.52439 | -75.37214 | 146.57714 | 581.2 | 37.7 | 140 | 2 | 16:06 | 03:14 | 01:52 |
| 223.25 | 45 | 312.39568 | 144.75621 | -76.32856 | 175.61958 | 250.9 | 19.0 | 210 | 3 | 03:44 | 14:53 | 15:27 |
| 6.25 | 46 | 287.67468 | 120.03521 | -78.89003 | 161.56459 | 196.8 | 15.1 | 216 | 3 | 05:22 | 16:31 | 16:08 |
| 22.25 | 47 | 262.95358 | 95.31411 | -80.85051 | 152.93550 | 470.0 | 32.3 | 134 | 3 | 07:00 | 18:09 | 17:12 |
| 38.25 | 48 | 238.23259 | 70.59311 | -81.78966 | 179.55033 | 531.4 | 35.4 | 91 | 3 | 10:17 | 21:25 | 22:15 |
| 54.25 | 49 | 213.51159 | 45.87211 | -80.78473 | 181.24285 | 464.1 | 32.0 | 136 | 3 | 11:55 | 23:03 | 24:00 |
| 70.25 | 50 | 188.79059 | 21.15111 | -78.79054 | 172.34918 | 184.0 | 14.2 | 217 | 3 | 13:32 | 00:41 | 01:02 |
| 86.25 | 51 | 164.06949 | 356.42999 | -76.25936 | 157.95692 | 269.6 | 20.2 | 208 | 3 | 15:10 | 02:19 | 01:42 |
| 214.25 | 59 | 326.30128 | 158.66181 | -75.39361 | 186.84134 | 560.8 | 36.8 | 147 | 4 | 02:49 | 13:57 | 15:16 |
| 230.25 | 60 | 301.58028 | 133.94081 | -77.32096 | 168.22612 | 35.0 | 2.8 | 224 | 4 | 04:27 | 15:36 | 15:40 |
| 13.25 | 61 | 276.85918 | 109.21971 | -79.95253 | 157.86739 | 335.0 | 24.5 | 191 | 4 | 06:05 | 17:13 | 16:36 |
| 29.25 | 62 | 252.13818 | 84.49871 | -81.42757 | 151.55955 | 532.0 | 35.4 | 100 | 4 | 09:22 | 20:30 | 19:28 |
| 45.25 | 63 | 227.41719 | 59.77771 | -81.54789 | 181.92858 | 533.5 | 35.5 | 98 | 4 | 11:00 | 22:08 | 23:07 |
| 61.25 | 64 | 202.69609 | 35.05661 | -80.10928 | 177.28192 | 359.6 | 26.0 | 181 | 4 | 12:37 | 23:46 | 00:27 |
| 77.25 | 65 | 177.97509 | 10.33561 | -77.57575 | 167.22694 | 6.2 | 0.5 | 223 | 4 | 14:15 | 01:24 | 01:24 |
| 93.25 | 66 | 153.25409 | 345.61459 | -75.57168 | 149.13320 | 509.7 | 34.3 | 163 | 4 | 15:53 | 03:02 | 01:50 |
| 221.25 | 74 | 315.48578 | 147.84631 | -76.08563 | 177.96824 | 317.1 | 23.4 | 202 | 5 | 03:32 | 14:40 | 15:24 |
| 4.25 | 75 | 290.76478 | 123.12531 | -78.51633 | 162.65902 | 150.4 | 11.7 | 219 | 5 | 05:10 | 16:18 | 16:01 |
| 20.25 | 76 | 266.04378 | 98.40431 | -80.65596 | 153.70490 | 445.1 | 31.0 | 147 | 5 | 06:48 | 17:56 | 17:03 |
| 36.25 | 77 | 241.32268 | 73.68321 | -81.77650 | 154.14064 | 535.2 | 35.5 | 91 | 5 | 10:05 | 21:13 | 20:21 |
| 52.25 | 78 | 216.60169 | 48.96221 | -80.96910 | 181.94854 | 487.2 | 33.2 | 123 | 5 | 11:42 | 22:51 | 23:50 |
| 68.25 | 79 | 191.88069 | 24.24121 | -79.15375 | 173.34449 | 228.1 | 17.4 | 213 | 5 | 13:20 | 00:29 | 00:54 |
| 84.25 | 80 | 167.15969 | 359.52019 | -76.50059 | 160.28658 | 204.7 | 15.7 | 214 | 5 | 14:58 | 02:07 | 01:39 |
| 212.25 | 88 | 329.39138 | 161.75190 | -75.29343 | 189.66908 | 632.9 | 39.9 | 118 | 6 | 02:37 | 13:45 | 15:15 |
| 228.25 | 89 | 304.67038 | 137.03091 | -76.99552 | 170.11728 | 94.0 | 7.4 | 221 | 6 | 04:15 | 15:23 | 15:35 |
| 11.25 | 90 | 279.94938 | 112.30991 | -79.73910 | 159.30949 | 298.7 | 22.2 | 204 | 6 | 05:53 | 17:01 | 16:30 |
| 27.25 | 91 | 255.22828 | 87.58881 | -81.23445 | 150.87406 | 525.1 | 35.1 | 104 | 6 | 09:10 | 20:18 | 19:13 |
| 43.25 | 92 | 230.50729 | 62.86781 | -81.66044 | 181.39570 | 537.4 | 35.7 | 94 | 6 | 10:47 | 21:56 | 22:53 |
| 59.25 | 93 | 205.78629 | 38.14681 | -80.30692 | 178.59921 | 392.6 | 28.0 | 168 | 6 | 12:25 | 23:34 | 00:20 |
| 75.25 | 94 | 181.06519 | 13.42571 | -77.93459 | 168.80885 | 60.4 | 4.8 | 223 | 6 | 14:03 | 01:12 | 01:18 |
| 91.25 | 95 | 156.34419 | 348.70469 | -75.72048 | 151.81284 | 439.3 | 30.7 | 180 | 6 | 15:41 | 02:50 | 01:48 |
| 219.25 | 103 | 318.57598 | 150.93651 | -75.84040 | 180.34277 | 385.0 | 27.6 | 191 | 7 | 03:20 | 14:28 | 15:21 |
| 2.25 | 104 | 293.85488 | 126.21541 | -78.17305 | 164.08343 | 101.0 | 7.9 | 222 | 7 | 04:58 | 16:06 | 15:54 |
| 18.25 | 105 | 269.13388 | 101.49441 | -80.47738 | 154.88415 | 415.9 | 29.4 | 159 | 7 | 06:36 | 17:44 | 16:55 |
| 34.25 | 106 | 244.41288 | 76.77341 | -81.72749 | 153.47636 | 537.0 | 35.6 | 93 | 7 | 09:52 | 21:01 | 20:06 |
| 50.25 | 107 | 219.69179 | 52.05231 | -81.11411 | 182.91896 | 510.5 | 34.4 | 111 | 7 | 11:30 | 22:39 | 23:42 |
| 66.25 | 108 | 194.97079 | 27.33131 | -79.53888 | 173.93942 | 269.0 | 20.2 | 209 | 7 | 13:08 | 00:17 | 00:44 |
| 82.25 | 109 | 170.24979 | 2.61031 | -76.78674 | 162.42730 | 141.7 | 11.0 | 219 | 7 | 14:46 | 01:54 | 01:36 |
| 98.25 | 110 | 145.52879 | 337.88929 | -75.22165 | 142.33307 | 690.1 | 42.1 | 86 | 7 | 16:24 | 03:33 | 01:54 |
| 210.25 | 117 | 332.48148 | 164.84200 | -75.19294 | 192.50041 | 705.9 | 42.7 | 73 | 8 | 02:24 | 13:33 | 15:14 |
| 226.25 | 118 | 307.76048 | 140.12101 | -76.71219 | 172.22715 | 155.1 | 12.0 | 218 | 8 | 04:03 | 15:11 | 15:32 |
| 9.25 | 119 | 283.03948 | 115.40001 | -79.44183 | 160.30870 | 260.4 | 19.6 | 210 | 8 | 05:41 | 16:49 | 16:22 |
| 25.25 | 120 | 258.31848 | 90.67901 | -81.07734 | 151.42645 | 506.4 | 34.2 | 115 | 8 | 07:19 | 18:27 | 17:24 |
| 41.25 | 121 | 233.59739 | 65.95791 | -81.73860 | 180.77880 | 538.2 | 35.7 | 93 | 8 | 10:35 | 21:44 | 22:38 |
| 57.25 | 122 | 208.87639 | 41.23691 | -80.52515 | 179.52958 | 421.9 | 29.7 | 155 | 8 | 12:13 | 23:21 | 00:11 |
| 73.25 | 123 | 184.15539 | 16.51591 | -78.24123 | 170.50423 | 111.9 | 8.8 | 222 | 8 | 13:51 | 00:59 | 01:13 |
| 89.25 | 124 | 159.43429 | 351.79479 | -75.91768 | 154.34208 | 370.2 | 26.7 | 193 | 8 | 15:29 | 02:37 | 01:46 |
| 217.25 | 132 | 321.66608 | 154.02661 | -75.64266 | 182.87815 | 454.4 | 31.5 | 177 | 9 | 03:07 | 14:16 | 15:19 |
| 233.25 | 133 | 296.94508 | 129.30561 | -77.82022 | 165.60373 | 48.6 | 3.8 | 224 | 9 | 04:46 | 15:54 | 15:48 |
| 16.25 | 134 | 272.22398 | 104.58451 | -80.28853 | 156.13600 | 384.7 | 27.5 | 172 | 9 | 06:23 | 17:32 | 16:48 |
| 32.25 | 135 | 247.50298 | 79.86351 | -81.63175 | 152.46663 | 538.9 | 35.7 | 95 | 9 | 09:40 | 20:49 | 19:50 |
| 48.25 | 136 | 222.78199 | 55.14251 | -81.28769 | 183.07857 | 525.7 | 35.1 | 103 | 9 | 11:18 | 22:26 | 23:30 |
| 64.25 | 137 | 198.06089 | 30.42141 | -79.75976 | 175.44368 | 306.9 | 22.7 | 200 | 9 | 12:56 | 00:04 | 00:38 |
| 80.25 | 138 | 173.33989 | 5.70041 | -77.06905 | 164.52595 | 81.0 | 6.4 | 222 | 9 | 14:34 | 01:42 | 01:32 |
| 96.25 | 139 | 148.61889 | 340.97939 | -75.32205 | 145.16339 | 617.3 | 39.2 | 126 | 9 | 16:12 | 03:20 | 01:53 |
| 224.25 | 147 | 310.85058 | 143.21111 | -76.42507 | 174.37853 | 218.5 | 16.7 | 213 | 10 | 03:50 | 14:59 | 15:28 |
| 7.25 | 148 | 286.12958 | 118.49011 | -79.05153 | 160.94991 | 218.9 | 16.7 | 215 | 10 | 05:28 | 16:37 | 16:12 |
| 23.25 | 149 | 261.40858 | 93.76911 | -80.92912 | 152.41497 | 482.6 | 33.0 | 127 | 10 | 07:06 | 18:15 | 17:16 |
| 39.25 | 150 | 236.68759 | 69.04811 | -81.78394 | 179.68721 | 532.1 | 35.4 | 92 | 10 | 10:23 | 21:31 | 22:22 |
| 55.25 | 151 | 211.96649 | 44.32701 | -80.70094 | 180.68983 | 450.6 | 31.3 | 142 | 10 | 12:01 | 23:09 | 00:03 |
| 71.25 | 152 | 187.24549 | 19.60601 | -78.62448 | 171.69139 | 160.8 | 12.5 | 219 | 10 | 13:39 | 00:47 | 01:05 |
| 87.25 | 153 | 162.52449 | 354.88499 | -76.11348 | 156.85542 | 302.7 | 22.4 | 204 | 10 | 15:17 | 02:25 | 01:44 |
| 215.25 | 161 | 324.75618 | 157.11671 | -75.49347 | 185.56225 | 525.0 | 35.1 | 158 | 11 | 02:55 | 14:04 | 15:17 |
| 231.25 | 162 | 300.03518 | 132.39571 | -77.45865 | 167.21393 | 7.7 | 0.6 | 223 | 11 | 04:33 | 15:42 | 15:42 |
| 14.25 | 163 | 275.31418 | 107.67471 | -80.05600 | 157.17274 | 352.4 | 25.6 | 185 | 11 | 06:11 | 17:20 | 16:40 |
| 30.25 | 164 | 250.59308 | 82.95361 | -81.49400 | 151.56997 | 537.2 | 35.6 | 98 | 11 | 09:28 | 20:36 | 19:34 |
| 46.25 | 165 | 225.87209 | 58.23261 | -81.47099 | 182.35047 | 531.7 | 35.4 | 99 | 11 | 11:06 | 22:14 | 23:15 |
| 62.25 | 166 | 201.15109 | 33.51161 | -80.00698 | 176.59654 | 342.4 | 25.0 | 187 | 11 | 12:44 | 23:52 | 00:30 |
| 78.25 | 167 | 176.42999 | 8.79051 | -77.39320 | 166.40328 | 22.6 | 1.8 | 224 | 11 | 14:21 | 01:30 | 01:27 |
| 94.25 | 168 | 151.70899 | 344.06949 | -75.47207 | 147.85702 | 545.3 | 36.0 | 152 | 11 | 16:00 | 03:08 | 01:51 |
| 222.25 | 176 | 313.94078 | 146.30131 | -76.18308 | 176.71666 | 283.8 | 21.2 | 206 | 12 | 03:38 | 14:47 | 15:25 |
| 5.25 | 177 | 289.21968 | 121.58021 | -78.68413 | 161.98451 | 174.1 | 13.5 | 217 | 12 | 05:16 | 16:25 | 16:04 |
| 21.25 | 178 | 264.49868 | 96.85921 | -80.76901 | 153.47397 | 456.8 | 31.6 | 140 | 12 | 06:54 | 18:02 | 17:08 |
| 37.25 | 179 | 239.77768 | 72.13821 | -81.78680 | 154.27541 | 534.9 | 35.5 | 92 | 12 | 10:11 | 21:19 | 20:28 |
| 53.25 | 180 | 215.05669 | 47.41721 | -80.86569 | 181.77792 | 477.2 | 32.7 | 130 | 12 | 11:48 | 22:57 | 23:56 |
| 69.25 | 181 | 190.33559 | 22.69611 | -78.99417 | 172.74755 | 206.5 | 15.8 | 215 | 12 | 13:26 | 00:35 | 00:57 |
| 85.25 | 182 | 165.61459 | 357.97509 | -76.40439 | 159.04896 | 236.9 | 18.0 | 211 | 12 | 15:04 | 02:13 | 01:40 |
| 213.25 | 190 | 327.84638 | 160.20690 | -75.34356 | 188.25481 | 596.7 | 38.4 | 134 | 13 | 02:43 | 13:51 | 15:16 |
| 229.25 | 191 | 303.12528 | 135.48581 | -77.13570 | 169.07853 | 64.3 | 5.1 | 223 | 13 | 04:21 | 15:30 | 15:37 |
| 12.25 | 192 | 278.40428 | 110.76481 | -79.84687 | 158.57974 | 317.0 | 23.4 | 197 | 13 | 05:59 | 17:07 | 16:33 |
| 28.25 | 193 | 253.68328 | 86.04381 | -81.33574 | 151.19575 | 529.0 | 35.3 | 102 | 13 | 09:16 | 20:24 | 19:21 |
| 44.25 | 194 | 228.96219 | 61.32271 | -81.60208 | 181.87546 | 537.4 | 35.7 | 95 | 13 | 10:53 | 22:02 | 23:01 |
| 60.25 | 195 | 204.24119 | 36.60171 | -80.20928 | 177.94955 | 376.3 | 27.0 | 175 | 13 | 12:31 | 23:40 | 00:23 |
| 76.25 | 196 | 179.52019 | 11.88071 | -77.75624 | 168.02907 | 33.5 | 2.6 | 223 | 13 | 14:09 | 01:18 | 01:21 |
| 92.25 | 197 | 154.79909 | 347.15959 | -75.62136 | 150.54233 | 474.3 | 32.5 | 172 | 13 | 15:47 | 02:56 | 01:49 |
| 220.25 | 205 | 317.03088 | 149.39141 | -75.93876 | 179.08091 | 350.9 | 25.5 | 197 | 14 | 03:26 | 14:34 | 15:22 |
| 3.25 | 206 | 292.30988 | 124.67041 | -78.34594 | 163.35894 | 126.1 | 9.8 | 220 | 14 | 05:04 | 16:12 | 15:57 |
| 19.25 | 207 | 267.58878 | 99.94931 | -80.56799 | 154.28539 | 430.8 | 30.2 | 153 | 14 | 06:42 | 17:50 | 16:59 |
| 35.25 | 208 | 242.86778 | 75.22831 | -81.75367 | 153.59432 | 538.2 | 35.7 | 92 | 14 | 09:58 | 21:07 | 20:13 |
| 51.25 | 209 | 218.14679 | 50.50731 | -81.04315 | 182.44241 | 499.1 | 33.8 | 117 | 14 | 11:36 | 22:45 | 23:46 |
| 67.25 | 210 | 193.42579 | 25.78631 | -79.34886 | 173.66467 | 249.0 | 18.8 | 211 | 14 | 13:14 | 00:23 | 00:49 |
| 83.25 | 211 | 168.70469 | 1.06521 | -76.64413 | 161.36201 | 172.9 | 13.4 | 217 | 14 | 14:52 | 02:00 | 01:37 |
| 99.25 | 212 | 143.98369 | 336.34419 | -75.22165 | 140.78797 | 726.7 | 43.4 | 53 | 14 | 16:30 | 03:39 | 01:54 |
| 211.25 | 219 | 330.93648 | 163.29700 | -75.24322 | 191.08435 | 669.3 | 41.3 | 99 | 15 | 02:30 | 13:39 | 15:15 |
| 227.25 | 220 | 306.21548 | 138.57601 | -76.85434 | 171.16694 | 124.3 | 9.7 | 220 | 15 | 04:09 | 15:17 | 15:33 |
| 10.25 | 221 | 281.49438 | 113.85491 | -79.59221 | 159.79405 | 280.0 | 20.9 | 208 | 15 | 05:47 | 16:55 | 16:26 |
| 26.25 | 222 | 256.77338 | 89.13391 | -81.14681 | 150.95789 | 517.5 | 34.7 | 109 | 15 | 07:25 | 18:33 | 17:28 |
| 42.25 | 223 | 232.05239 | 64.41291 | -81.70818 | 180.88994 | 536.6 | 35.6 | 94 | 15 | 10:41 | 21:50 | 22:45 |
| 58.25 | 224 | 207.33129 | 39.69181 | -80.40213 | 179.23071 | 408.4 | 28.9 | 162 | 15 | 12:19 | 23:28 | 00:16 |
| 74.25 | 225 | 182.61029 | 14.97081 | -78.06688 | 169.76500 | 86.4 | 6.8 | 222 | 15 | 13:57 | 01:05 | 01:16 |
| 90.25 | 226 | 157.88929 | 350.24979 | -75.81925 | 153.07948 | 404.6 | 28.7 | 187 | 15 | 15:35 | 02:43 | 01:47 |

| Table XVIII. Volcano: Etna, Sicily; Lat 37.730; Lon 15.000 Orbits in RED are not normally available. |
| --- |
| WRS Path | TES Orbit | Descending Node (deg) | Ascending Node (deg) | S/C Lat (deg) | S/C Lon (deg) | Miss Distance (km) | Min. Nadir Angle (deg) | Obs. Time (secs) | UTC Day | UTC of Closest Approach | LMST @ Target | LMST @ S/C |
| 202.25 | 0 | 344.84208 | 177.20260 | 37.88484 | 13.28501 | 151.6 | 12.0 | 219 | 0 | 02:35 | 03:35 | 03:28 |
| 72.25 | 21 | 185.70039 | 18.06091 | 37.67738 | 14.19221 | 71.3 | 5.7 | 222 | 1 | 12:43 | 13:43 | 13:40 |
| 200.25 | 29 | 347.93218 | 180.29270 | 37.58644 | 16.32667 | 117.9 | 9.4 | 220 | 2 | 02:23 | 03:23 | 03:28 |
| 70.25 | 50 | 188.79059 | 21.15111 | 37.97576 | 17.23380 | 198.0 | 15.5 | 216 | 3 | 12:31 | 13:31 | 13:40 |
| 198.25 | 58 | 351.02228 | 183.38280 | 37.34770 | 19.37842 | 388.3 | 28.2 | 191 | 4 | 02:11 | 03:11 | 03:28 |
| 205.25 | 73 | 340.20688 | 172.56740 | 38.54117 | 8.75837 | 553.1 | 36.9 | 152 | 5 | 02:53 | 03:53 | 03:28 |
| 68.25 | 79 | 191.88069 | 24.24121 | 38.39343 | 20.25489 | 465.8 | 32.5 | 176 | 5 | 12:19 | 13:19 | 13:40 |
| 196.25 | 87 | 354.11238 | 186.47290 | 37.22831 | 22.44948 | 659.5 | 41.4 | 106 | 6 | 01:58 | 02:58 | 03:28 |
| 75.25 | 94 | 181.06519 | 13.42571 | 37.31926 | 9.61460 | 477.0 | 33.1 | 172 | 6 | 13:02 | 14:02 | 13:40 |
| 203.25 | 102 | 343.29698 | 175.65750 | 38.06386 | 11.76924 | 285.8 | 21.7 | 207 | 7 | 02:41 | 03:41 | 03:28 |
| 73.25 | 123 | 184.15539 | 16.51591 | 37.49833 | 12.67610 | 206.3 | 16.1 | 214 | 8 | 12:49 | 13:49 | 13:40 |
| 201.25 | 131 | 346.38708 | 178.74760 | 37.70581 | 14.80088 | 17.7 | 1.4 | 223 | 9 | 02:29 | 03:29 | 03:28 |
| 71.25 | 152 | 187.24549 | 19.60601 | 37.79674 | 15.71793 | 63.5 | 5.1 | 222 | 10 | 12:37 | 13:37 | 13:40 |
| 199.25 | 160 | 349.47728 | 181.83780 | 37.46707 | 17.85255 | 253.0 | 19.4 | 210 | 11 | 02:17 | 03:17 | 03:28 |
| 206.25 | 175 | 338.66178 | 171.02230 | 38.77979 | 7.25345 | 686.1 | 42.4 | 90 | 12 | 03:00 | 04:00 | 03:29 |
| 69.25 | 181 | 190.33559 | 22.69611 | 38.21444 | 18.73950 | 332.1 | 24.7 | 201 | 12 | 12:25 | 13:25 | 13:40 |
| 197.25 | 189 | 352.56738 | 184.92790 | 37.22831 | 20.90448 | 523.8 | 35.5 | 159 | 13 | 02:04 | 03:04 | 03:28 |
| 76.25 | 196 | 179.52019 | 11.88071 | 37.25957 | 8.07913 | 612.6 | 39.5 | 128 | 13 | 13:08 | 14:08 | 13:40 |
| 204.25 | 204 | 341.75188 | 174.11240 | 38.30253 | 10.26357 | 419.7 | 30.0 | 186 | 14 | 02:47 | 03:47 | 03:28 |
| 67.25 | 210 | 193.42579 | 25.78631 | 38.63207 | 21.76005 | 599.1 | 38.9 | 134 | 14 | 12:13 | 13:13 | 13:40 |
| 74.25 | 225 | 182.61029 | 14.97081 | 37.43864 | 11.14059 | 341.5 | 25.3 | 199 | 15 | 12:56 | 13:56 | 13:40 |

| Table XIX. Volcano: Fuego, Guatemala; Lat 14.480; Lon 269.120 Orbits in RED are not normally available. |
| --- |
| WRS Path | TES Orbit | Descending Node (deg) | Ascending Node (deg) | S/C Lat (deg) | S/C Lon (deg) | Miss Distance (km) | Min. Nadir Angle (deg) | Obs. Time (secs) | UTC Day | UTC of Closest Approach | LMST @ Target | LMST @ S/C |
| 33.25 | 4 | 245.95788 | 78.31841 | 14.28998 | 271.70305 | 279.3 | 21.4 | 206 | 0 | 09:17 | 03:14 | 03:24 |
| 145.25 | 11 | 72.91070 | 265.27120 | 14.14136 | 264.07902 | 544.9 | 36.7 | 153 | 0 | 20:08 | 14:04 | 13:44 |
| 31.25 | 33 | 249.04808 | 81.40861 | 14.04992 | 274.77305 | 611.6 | 39.7 | 129 | 2 | 09:05 | 03:01 | 03:24 |
| 143.25 | 40 | 76.00090 | 268.36140 | 14.32140 | 267.15405 | 212.7 | 16.7 | 214 | 2 | 19:56 | 13:52 | 13:44 |
| 38.25 | 48 | 238.23259 | 70.59311 | 14.95012 | 264.03372 | 550.0 | 37.0 | 152 | 3 | 09:48 | 03:44 | 03:24 |
| 141.25 | 69 | 79.09100 | 271.45150 | 14.56146 | 270.22386 | 119.3 | 9.6 | 220 | 4 | 19:43 | 13:40 | 13:44 |
| 36.25 | 77 | 241.32268 | 73.68321 | 14.65006 | 267.09830 | 218.6 | 17.1 | 214 | 5 | 09:36 | 03:32 | 03:24 |
| 139.25 | 98 | 82.18109 | 274.54160 | 14.86152 | 273.28848 | 450.8 | 32.0 | 178 | 6 | 19:31 | 13:27 | 13:44 |
| 34.25 | 106 | 244.41288 | 76.77341 | 14.41001 | 270.16818 | 113.2 | 9.1 | 220 | 7 | 09:23 | 03:20 | 03:24 |
| 146.25 | 113 | 71.36570 | 263.72620 | 14.08134 | 262.53906 | 711.2 | 43.6 | 71 | 7 | 20:14 | 14:10 | 13:44 |
| 32.25 | 135 | 247.50298 | 79.86351 | 14.16995 | 273.23804 | 445.4 | 31.7 | 179 | 9 | 09:11 | 03:08 | 03:24 |
| 144.25 | 142 | 74.45580 | 266.81630 | 14.26139 | 265.61401 | 378.8 | 27.8 | 193 | 9 | 20:02 | 13:58 | 13:44 |
| 39.25 | 150 | 236.68759 | 69.04811 | 15.07014 | 262.49896 | 715.5 | 43.7 | 67 | 10 | 09:54 | 03:51 | 03:24 |
| 142.25 | 171 | 77.54590 | 269.90640 | 14.44143 | 268.68892 | 46.7 | 3.8 | 222 | 11 | 19:49 | 13:46 | 13:44 |
| 37.25 | 179 | 239.77768 | 72.13821 | 14.77008 | 265.56349 | 384.4 | 28.2 | 192 | 12 | 09:42 | 03:38 | 03:24 |
| 140.25 | 200 | 80.63609 | 272.99660 | 14.74149 | 271.75369 | 285.1 | 21.8 | 207 | 13 | 19:37 | 13:34 | 13:44 |
| 35.25 | 208 | 242.86778 | 75.22831 | 14.53003 | 268.63323 | 52.7 | 4.3 | 222 | 14 | 09:29 | 03:26 | 03:24 |
| 138.25 | 229 | 83.72619 | 276.08670 | 15.04155 | 274.81823 | 616.4 | 39.9 | 127 | 15 | 19:25 | 13:21 | 13:44 |

| Table XX. Volcano: Lascar, Chile; Lat -23.370; Lon 292.270 Orbits in RED are not normally available. |
| --- |
| WRS Path | TES Orbit | Descending Node (deg) | Ascending Node (deg) | S/C Lat (deg) | S/C Lon (deg) | Miss Distance (km) | Min. Nadir Angle (deg) | Obs. Time (secs) | UTC Day | UTC of Closest Approach | LMST @ Target | LMST @ S/C |
| 17.25 | 3 | 270.67898 | 103.03951 | -23.46975 | 293.34321 | 110.1 | 8.8 | 220 | 0 | 07:49 | 03:18 | 03:22 |
| 129.25 | 10 | 97.63179 | 289.99230 | -23.37560 | 291.85464 | 42.4 | 3.4 | 223 | 0 | 18:19 | 13:48 | 13:46 |
| 15.25 | 32 | 273.76908 | 106.12961 | -23.76943 | 296.40253 | 423.7 | 30.4 | 184 | 2 | 07:37 | 03:06 | 03:22 |
| 127.25 | 39 | 100.72189 | 293.08240 | -23.13584 | 294.92035 | 272.2 | 20.9 | 207 | 2 | 18:06 | 13:35 | 13:46 |
| 22.25 | 47 | 262.95358 | 95.31411 | -22.93029 | 285.67262 | 676.6 | 42.2 | 96 | 3 | 08:20 | 03:49 | 03:22 |
| 125.25 | 68 | 103.81199 | 296.17250 | -22.95602 | 297.99225 | 587.1 | 38.6 | 139 | 4 | 17:54 | 13:23 | 13:46 |
| 20.25 | 76 | 266.04378 | 98.40431 | -23.11012 | 288.74463 | 361.6 | 26.7 | 196 | 5 | 08:07 | 03:36 | 03:22 |
| 132.25 | 83 | 92.99659 | 285.35710 | -23.85509 | 287.26868 | 512.7 | 35.1 | 163 | 5 | 18:37 | 14:06 | 13:46 |
| 18.25 | 105 | 269.13388 | 101.49441 | -23.34988 | 291.81035 | 47.0 | 3.8 | 223 | 7 | 07:55 | 03:24 | 03:22 |
| 130.25 | 112 | 96.08669 | 288.44720 | -23.55541 | 290.32793 | 199.3 | 15.6 | 216 | 7 | 18:25 | 13:54 | 13:46 |
| 16.25 | 134 | 272.22398 | 104.58451 | -23.64956 | 294.86977 | 267.1 | 20.5 | 209 | 9 | 07:43 | 03:12 | 03:22 |
| 128.25 | 141 | 99.17679 | 291.53730 | -23.25572 | 293.38742 | 114.9 | 9.2 | 221 | 9 | 18:12 | 13:41 | 13:46 |
| 14.25 | 163 | 275.31418 | 107.67471 | -23.94923 | 297.92905 | 580.2 | 38.3 | 142 | 11 | 07:30 | 02:59 | 03:22 |
| 126.25 | 170 | 102.26699 | 294.62750 | -23.07590 | 296.45937 | 429.6 | 30.7 | 182 | 11 | 18:00 | 13:29 | 13:46 |
| 21.25 | 178 | 264.49868 | 96.85921 | -23.05018 | 287.20560 | 519.1 | 35.4 | 161 | 12 | 08:13 | 03:42 | 03:22 |
| 133.25 | 185 | 91.45149 | 283.81200 | -24.03488 | 285.74220 | 669.0 | 41.9 | 101 | 12 | 18:43 | 14:12 | 13:46 |
| 19.25 | 207 | 267.58878 | 99.94931 | -23.23000 | 290.27746 | 204.2 | 16.0 | 215 | 14 | 08:01 | 03:30 | 03:22 |
| 131.25 | 214 | 94.54159 | 286.90210 | -23.67529 | 288.79514 | 356.1 | 26.4 | 197 | 14 | 18:31 | 14:00 | 13:46 |

| Table XXI. Volcano: Masaya, Nicaragua; Lat 11.980; Lon 273.850 Orbits in RED are not normally available. |
| --- |
| WRS Path | TES Orbit | Descending Node (deg) | Ascending Node (deg) | S/C Lat (deg) | S/C Lon (deg) | Miss Distance (km) | Min. Nadir Angle (deg) | Obs. Time (secs) | UTC Day | UTC of Closest Approach | LMST @ Target | LMST @ S/C |
| 33.25 | 4 | 245.95788 | 78.31841 | 12.18926 | 271.52879 | 253.7 | 19.6 | 210 | 0 | 09:18 | 03:33 | 03:24 |
| 136.25 | 25 | 86.81629 | 279.17680 | 12.34074 | 278.13398 | 467.8 | 32.9 | 174 | 1 | 19:12 | 13:27 | 13:44 |
| 31.25 | 33 | 249.04808 | 81.40861 | 11.88913 | 274.59453 | 81.7 | 6.6 | 221 | 2 | 09:06 | 03:21 | 03:24 |
| 143.25 | 40 | 76.00090 | 268.36140 | 11.56039 | 267.38210 | 706.3 | 43.4 | 75 | 2 | 19:55 | 14:10 | 13:44 |
| 29.25 | 62 | 252.13818 | 84.49871 | 11.70904 | 277.67000 | 417.2 | 30.1 | 186 | 4 | 08:53 | 03:09 | 03:24 |
| 141.25 | 69 | 79.09100 | 271.45150 | 11.74047 | 270.45760 | 370.5 | 27.3 | 194 | 4 | 19:42 | 13:58 | 13:44 |
| 139.25 | 98 | 82.18109 | 274.54160 | 11.98058 | 273.52818 | 35.0 | 2.8 | 223 | 6 | 19:30 | 13:46 | 13:44 |
| 34.25 | 106 | 244.41288 | 76.77341 | 12.30931 | 269.99360 | 421.2 | 30.3 | 184 | 7 | 09:24 | 03:39 | 03:24 |
| 137.25 | 127 | 85.27119 | 277.63170 | 12.22069 | 276.59870 | 300.3 | 22.8 | 204 | 8 | 19:18 | 13:33 | 13:44 |
| 32.25 | 135 | 247.50298 | 79.86351 | 12.00918 | 273.05920 | 86.2 | 7.0 | 221 | 9 | 09:12 | 03:27 | 03:24 |
| 135.25 | 156 | 88.36139 | 280.72190 | 12.52081 | 279.66432 | 635.3 | 40.7 | 119 | 10 | 19:06 | 13:21 | 13:44 |
| 30.25 | 164 | 250.59308 | 82.95361 | 11.82910 | 276.13465 | 249.4 | 19.3 | 210 | 11 | 08:59 | 03:15 | 03:24 |
| 142.25 | 171 | 77.54590 | 269.90640 | 11.68044 | 268.91737 | 538.4 | 36.4 | 155 | 11 | 19:49 | 14:04 | 13:44 |
| 28.25 | 193 | 253.68328 | 86.04381 | 11.58898 | 279.20536 | 585.1 | 38.6 | 139 | 13 | 08:47 | 03:02 | 03:24 |
| 140.25 | 200 | 80.63609 | 272.99660 | 11.86053 | 271.99295 | 202.7 | 16.0 | 215 | 13 | 19:36 | 13:52 | 13:44 |
| 35.25 | 208 | 242.86778 | 75.22831 | 12.42936 | 268.45833 | 588.7 | 38.7 | 139 | 14 | 09:30 | 03:45 | 03:24 |
| 138.25 | 229 | 83.72619 | 276.08670 | 12.10064 | 275.06350 | 132.8 | 10.6 | 219 | 15 | 19:24 | 13:39 | 13:44 |

| Table XXII. Volcano: Pacaya, Guatemala; Lat 14.380; Lon 269.400 Orbits in RED are not normally available. |
| --- |
| WRS Path | TES Orbit | Descending Node (deg) | Ascending Node (deg) | S/C Lat (deg) | S/C Lon (deg) | Miss Distance (km) | Min. Nadir Angle (deg) | Obs. Time (secs) | UTC Day | UTC of Closest Approach | LMST @ Target | LMST @ S/C |
| 33.25 | 4 | 245.95788 | 78.31841 | 14.16995 | 271.69294 | 248.4 | 19.3 | 211 | 0 | 09:17 | 03:15 | 03:24 |
| 145.25 | 11 | 72.91070 | 265.27120 | 14.02132 | 264.08910 | 574.4 | 38.1 | 144 | 0 | 20:08 | 14:05 | 13:44 |
| 31.25 | 33 | 249.04808 | 81.40861 | 13.98990 | 274.76801 | 580.8 | 38.4 | 141 | 2 | 09:05 | 03:03 | 03:24 |
| 143.25 | 40 | 76.00090 | 268.36140 | 14.26139 | 267.15911 | 242.0 | 18.8 | 211 | 2 | 19:56 | 13:53 | 13:44 |
| 38.25 | 48 | 238.23259 | 70.59311 | 14.83009 | 264.02350 | 581.2 | 38.4 | 141 | 3 | 09:48 | 03:46 | 03:24 |
| 141.25 | 69 | 79.09100 | 271.45150 | 14.44143 | 270.23402 | 90.2 | 7.3 | 222 | 4 | 19:43 | 13:41 | 13:44 |
| 36.25 | 77 | 241.32268 | 73.68321 | 14.59005 | 267.09322 | 249.7 | 19.3 | 210 | 5 | 09:36 | 03:33 | 03:24 |
| 139.25 | 98 | 82.18109 | 274.54160 | 14.74149 | 273.29869 | 421.9 | 30.3 | 185 | 6 | 19:31 | 13:29 | 13:44 |
| 34.25 | 106 | 244.41288 | 76.77341 | 14.28998 | 270.15805 | 82.4 | 6.6 | 221 | 7 | 09:23 | 03:21 | 03:24 |
| 32.25 | 135 | 247.50298 | 79.86351 | 14.10993 | 273.23299 | 414.6 | 29.9 | 186 | 9 | 09:11 | 03:09 | 03:24 |
| 144.25 | 142 | 74.45580 | 266.81630 | 14.14136 | 265.62412 | 408.2 | 29.6 | 187 | 9 | 20:02 | 13:59 | 13:44 |
| 142.25 | 171 | 77.54590 | 269.90640 | 14.32140 | 268.69905 | 75.9 | 6.1 | 222 | 11 | 19:49 | 13:47 | 13:44 |
| 37.25 | 179 | 239.77768 | 72.13821 | 14.71007 | 265.55840 | 415.5 | 30.0 | 186 | 12 | 09:42 | 03:39 | 03:24 |
| 140.25 | 200 | 80.63609 | 272.99660 | 14.56146 | 271.76896 | 256.1 | 19.8 | 210 | 13 | 19:37 | 13:35 | 13:44 |
| 35.25 | 208 | 242.86778 | 75.22831 | 14.41001 | 268.62308 | 83.8 | 6.8 | 221 | 14 | 09:30 | 03:27 | 03:24 |
| 138.25 | 229 | 83.72619 | 276.08670 | 14.92153 | 274.82847 | 587.6 | 38.7 | 139 | 15 | 19:25 | 13:22 | 13:44 |

| Table XXIII. Volcano: Pu'u O'o (Kilauea), Hawai'i; Lat 13.392; Lon 204.892 Orbits in RED are not normally available. |
| --- |
| WRS Path | TES Orbit | Descending Node (deg) | Ascending Node (deg) | S/C Lat (deg) | S/C Lon (deg) | Miss Distance (km) | Min. Nadir Angle (deg) | Obs. Time (secs) | UTC Day | UTC of Closest Approach | LMST @ Target | LMST @ S/C |
| 72.25 | 21 | 185.70039 | 18.06091 | 12.96957 | 211.33538 | 699.8 | 43.2 | 80 | 1 | 13:19 | 02:58 | 03:24 |
| 184.25 | 28 | 12.65320 | 205.01370 | 13.36113 | 203.88675 | 108.9 | 8.8 | 221 | 1 | 00:09 | 13:48 | 13:44 |
| 79.25 | 36 | 174.88499 | 7.24551 | 13.74983 | 200.58481 | 467.7 | 32.9 | 175 | 2 | 14:02 | 03:41 | 03:24 |
| 182.25 | 57 | 15.74330 | 208.10380 | 13.60120 | 206.95686 | 224.7 | 17.6 | 213 | 3 | 23:56 | 13:36 | 13:44 |
| 77.25 | 65 | 177.97509 | 10.33561 | 13.44974 | 203.64988 | 134.6 | 10.8 | 219 | 4 | 13:49 | 03:29 | 03:24 |
| 180.25 | 86 | 18.83350 | 211.19400 | 13.84127 | 210.02700 | 557.7 | 37.3 | 150 | 5 | 23:44 | 13:24 | 13:44 |
| 75.25 | 94 | 181.06519 | 13.42571 | 13.20966 | 206.72005 | 199.0 | 15.7 | 215 | 6 | 13:37 | 03:17 | 03:24 |
| 187.25 | 101 | 8.01800 | 200.37850 | 13.00100 | 199.28139 | 609.5 | 39.6 | 130 | 6 | 00:27 | 14:07 | 13:44 |
| 73.25 | 123 | 184.15539 | 16.51591 | 13.02959 | 209.79534 | 532.8 | 36.2 | 157 | 8 | 13:25 | 03:04 | 03:24 |
| 185.25 | 130 | 11.10820 | 203.46870 | 13.24108 | 202.35171 | 275.6 | 21.2 | 207 | 8 | 00:15 | 13:54 | 13:44 |
| 80.25 | 138 | 173.33989 | 5.70041 | 13.92988 | 199.05478 | 634.1 | 40.6 | 120 | 9 | 14:08 | 03:47 | 03:24 |
| 183.25 | 159 | 14.19830 | 206.55880 | 13.42115 | 205.42686 | 58.0 | 4.7 | 222 | 10 | 00:02 | 13:42 | 13:44 |
| 78.25 | 167 | 176.42999 | 8.79051 | 13.62980 | 202.11979 | 301.2 | 22.9 | 204 | 11 | 13:56 | 03:35 | 03:24 |
| 181.25 | 188 | 17.28840 | 209.64890 | 13.72124 | 208.49194 | 391.2 | 28.6 | 191 | 12 | 23:50 | 13:30 | 13:44 |
| 76.25 | 196 | 179.52019 | 11.88071 | 13.32970 | 205.18501 | 32.5 | 2.6 | 223 | 13 | 13:43 | 03:23 | 03:24 |
| 179.25 | 217 | 20.37850 | 212.73900 | 14.02132 | 211.55691 | 724.0 | 44.0 | 58 | 14 | 23:38 | 13:18 | 13:44 |
| 74.25 | 225 | 182.61029 | 14.97081 | 13.14964 | 208.26017 | 365.9 | 27.0 | 194 | 15 | 13:31 | 03:10 | 03:24 |
| 186.25 | 232 | 9.56310 | 201.92360 | 13.12104 | 200.81656 | 442.5 | 31.5 | 180 | 15 | 00:21 | 14:01 | 13:44 |

| Table XXIV. Volcano: Sakurajima, Japan; Lat 31.580; Lon 130.670 Orbits in RED are not normally available. |
| --- |
| WRS Path | TES Orbit | Descending Node (deg) | Ascending Node (deg) | S/C Lat (deg) | S/C Lon (deg) | Miss Distance (km) | Min. Nadir Angle (deg) | Obs. Time (secs) | UTC Day | UTC of Closest Approach | LMST @ Target | LMST @ S/C |
| 1.25 | 2 | 295.39998 | 127.76051 | 31.22352 | 124.82155 | 556.5 | 37.1 | 149 | 0 | 05:23 | 14:05 | 13:42 |
| 129.25 | 10 | 97.63179 | 289.99230 | 32.20907 | 125.23987 | 517.4 | 35.2 | 162 | 0 | 19:06 | 03:48 | 03:26 |
| 232.25 | 31 | 298.49008 | 130.85061 | 31.34317 | 127.89626 | 264.4 | 20.3 | 208 | 2 | 05:10 | 13:53 | 13:42 |
| 127.25 | 39 | 100.72189 | 293.08240 | 31.79040 | 128.27480 | 227.9 | 17.7 | 213 | 2 | 18:53 | 03:36 | 03:26 |
| 230.25 | 60 | 301.58028 | 133.94081 | 31.64227 | 130.94771 | 27.2 | 2.2 | 223 | 4 | 04:58 | 13:41 | 13:42 |
| 125.25 | 68 | 103.81199 | 296.17250 | 31.49131 | 131.32595 | 63.0 | 5.1 | 223 | 4 | 18:41 | 03:24 | 03:26 |
| 228.25 | 89 | 304.67038 | 137.03091 | 31.94134 | 133.99867 | 317.3 | 23.8 | 202 | 6 | 04:46 | 13:28 | 13:42 |
| 123.25 | 97 | 106.90209 | 299.26260 | 31.25202 | 134.38518 | 354.5 | 26.2 | 197 | 6 | 18:29 | 03:11 | 03:26 |
| 2.25 | 104 | 293.85488 | 126.21541 | 31.10387 | 123.29179 | 702.7 | 43.1 | 78 | 7 | 05:29 | 14:11 | 13:42 |
| 130.25 | 112 | 96.08669 | 288.44720 | 32.38849 | 123.71865 | 661.7 | 41.6 | 105 | 7 | 19:12 | 03:54 | 03:27 |
| 226.25 | 118 | 307.76048 | 140.12101 | 32.36000 | 137.03332 | 606.5 | 39.3 | 132 | 8 | 04:34 | 13:16 | 13:42 |
| 121.25 | 126 | 109.99229 | 302.35280 | 31.13237 | 137.46003 | 646.7 | 41.0 | 112 | 8 | 18:16 | 02:59 | 03:26 |
| 233.25 | 133 | 296.94508 | 129.30561 | 31.28335 | 126.35897 | 410.4 | 29.5 | 187 | 9 | 05:16 | 13:59 | 13:42 |
| 128.25 | 141 | 99.17679 | 291.53730 | 32.02965 | 126.76113 | 372.8 | 27.3 | 194 | 9 | 18:59 | 03:42 | 03:26 |
| 231.25 | 162 | 300.03518 | 132.39571 | 31.46281 | 129.42591 | 118.7 | 9.5 | 220 | 11 | 05:04 | 13:47 | 13:42 |
| 126.25 | 170 | 102.26699 | 294.62750 | 31.67077 | 129.80427 | 82.6 | 6.6 | 222 | 11 | 18:47 | 03:30 | 03:26 |
| 229.25 | 191 | 303.12528 | 135.48581 | 31.76190 | 132.47710 | 172.2 | 13.6 | 218 | 13 | 04:52 | 13:35 | 13:42 |
| 124.25 | 199 | 105.35709 | 297.71760 | 31.37167 | 132.85559 | 208.6 | 16.3 | 214 | 13 | 18:35 | 03:18 | 03:26 |
| 227.25 | 220 | 306.21548 | 138.57601 | 32.12077 | 135.52010 | 462.1 | 32.4 | 176 | 15 | 04:40 | 13:22 | 13:42 |
| 122.25 | 228 | 108.44719 | 300.80770 | 31.19220 | 135.92259 | 500.5 | 34.4 | 166 | 15 | 18:23 | 03:05 | 03:26 |

| Table XXV. Volcano: White Island, New Zealand; Lat -37.520; Lon 177.180 Orbits in RED are not normally available. |
| --- |
| WRS Path | TES Orbit | Descending Node (deg) | Ascending Node (deg) | S/C Lat (deg) | S/C Lon (deg) | Miss Distance (km) | Min. Nadir Angle (deg) | Obs. Time (secs) | UTC Day | UTC of Closest Approach | LMST @ Target | LMST @ S/C |
| 202.25 | 0 | 344.84208 | 177.20260 | -37.19706 | 180.81367 | 323.1 | 24.1 | 201 | 0 | 01:46 | 13:35 | 13:49 |
| 209.25 | 15 | 334.02658 | 166.38710 | -38.45028 | 170.20233 | 620.0 | 39.8 | 126 | 1 | 02:29 | 14:17 | 13:50 |
| 88.25 | 22 | 160.97939 | 353.33989 | -38.06668 | 181.76390 | 407.2 | 29.3 | 188 | 1 | 15:12 | 03:00 | 03:19 |
| 200.25 | 29 | 347.93218 | 180.29270 | -37.01797 | 183.87540 | 594.9 | 38.7 | 135 | 2 | 01:34 | 13:22 | 13:49 |
| 95.25 | 37 | 150.16389 | 342.52439 | -37.05204 | 171.11199 | 539.2 | 36.2 | 154 | 2 | 15:55 | 03:43 | 03:19 |
| 207.25 | 44 | 337.11668 | 169.47720 | -37.97295 | 173.21349 | 352.3 | 26.0 | 197 | 3 | 02:17 | 14:05 | 13:49 |
| 86.25 | 51 | 164.06949 | 356.42999 | -38.54399 | 184.77477 | 674.5 | 42.0 | 98 | 3 | 14:59 | 02:48 | 03:19 |
| 93.25 | 66 | 153.25409 | 345.61459 | -37.23113 | 174.17378 | 267.5 | 20.4 | 208 | 4 | 15:42 | 03:31 | 03:19 |
| 205.25 | 73 | 340.20688 | 172.56740 | -37.61488 | 176.24543 | 83.0 | 6.6 | 222 | 5 | 02:04 | 13:53 | 13:49 |
| 91.25 | 95 | 156.34419 | 348.70469 | -37.52958 | 177.21610 | 3.4 | 0.3 | 224 | 6 | 15:30 | 03:19 | 03:19 |
| 203.25 | 102 | 343.29698 | 175.65750 | -37.31644 | 179.28759 | 187.5 | 14.7 | 216 | 7 | 01:52 | 13:41 | 13:49 |
| 89.25 | 124 | 159.43429 | 351.79479 | -37.88766 | 180.24814 | 272.9 | 20.8 | 208 | 8 | 15:18 | 03:07 | 03:19 |
| 201.25 | 131 | 346.38708 | 178.74760 | -37.13736 | 182.34919 | 458.9 | 32.2 | 176 | 9 | 01:40 | 13:28 | 13:49 |
| 96.25 | 139 | 148.61889 | 340.97939 | -36.99235 | 169.57642 | 675.2 | 42.0 | 96 | 9 | 16:01 | 03:50 | 03:19 |
| 208.25 | 146 | 335.57168 | 167.93220 | -38.21163 | 171.70778 | 486.3 | 33.6 | 170 | 10 | 02:23 | 14:11 | 13:49 |
| 87.25 | 153 | 162.52449 | 354.88499 | -38.36501 | 183.25965 | 541.2 | 36.3 | 155 | 10 | 15:06 | 02:54 | 03:19 |
| 94.25 | 168 | 151.70899 | 344.06949 | -37.17144 | 172.63817 | 403.3 | 29.1 | 187 | 11 | 15:49 | 03:37 | 03:19 |
| 206.25 | 175 | 338.66178 | 171.02230 | -37.79392 | 174.72936 | 217.8 | 16.9 | 214 | 12 | 02:10 | 13:59 | 13:49 |
| 92.25 | 197 | 154.79909 | 347.15959 | -37.41020 | 175.69018 | 132.0 | 10.5 | 219 | 13 | 15:36 | 03:25 | 03:19 |
| 204.25 | 204 | 341.75188 | 174.11240 | -37.43582 | 177.76160 | 52.2 | 4.2 | 223 | 14 | 01:58 | 13:47 | 13:49 |
| 90.25 | 226 | 157.88929 | 350.24979 | -37.70863 | 178.73227 | 138.3 | 11.0 | 219 | 15 | 15:24 | 03:13 | 03:19 |

# GLOBAL SURVEY SCHEDULE

The foregoing analysis also leads to the Global Survey schedule (Table XXVI). The times are correct to about +/- 2 minutes with the added caveat that any deviation of the nodal crossing time (ascending) from 13:45 LMST puts a permanent offset into the times.

The reader must also be aware of the fact that TES orbits begin at the Southern Apex, whereas AURA orbits are counted from the ascending node. That is, the first quarter of a TES orbit maps to AURA orbit N-1 and the remainder to AURA orbit N.

# REPORTING

Because the ICS translator mechanism has been identified as a limited-lifetime subsystem, it is essential that the ST keep a careful watch on the ICS accumulated “mileage” (accomplished using a tool called “odometer.pro”). Thus it is also essential that the MOT provide the ST (at least weekly) with a list of all macros actually executed [Requirement MPR_8].

| Table XXVI: TES GLOBAL SURVEYS & CALIBRATION TIMES |
| --- |
| Label | Start Day | Start Time (UTC) | End Day | End Time (UTC) | TES Orbit (Start) | TES Orbit (End) | WRS Path (Start) | WRS Path (End) |
| Pre-Cal 0 | 0 | 04:49 | 0 | 08:07 | 2 | 3 | 1.25 | 17.25 |
| GS 0 | 0 | 08:07 | 1 | 10:29 | 4 | 19 | 33.25 | 4.25 |
| Post-Cal 0 | 1 | 10:29 | 1 | 13:46 | 20 | 21 | 56.25 | 72.25 |
| Pre-Cal 1 | 2 | 04:37 | 2 | 07:25 | 31 | 32 | 232.25 | 15.25 |
| GS 1 | 2 | 07:25 | 3 | 10:17 | 33 | 48 | 31.25 | 38.25 |
| Post-Cal 1 | 3 | 10:17 | 3 | 13:34 | 49 | 50 | 54.25 | 70.25 |
| Pre-Cal 2 | 4 | 04:25 | 4 | 07:42 | 60 | 61 | 230.25 | 13.25 |
| GS 2 | 4 | 07:42 | 5 | 10:04 | 62 | 77 | 29.25 | 36.25 |
| Post-Cal 2 | 5 | 10:04 | 5 | 13:22 | 78 | 79 | 52.25 | 68.25 |
| Pre-Cal 3 | 6 | 04:12 | 6 | 07:30 | 89 | 90 | 228.25 | 11.25 |
| GS 3 | 6 | 07:30 | 7 | 09:52 | 91 | 106 | 27.25 | 34.25 |
| Post-Cal 3 | 7 | 09:52 | 7 | 13:10 | 107 | 108 | 50.25 | 66.25 |
| Pre-Cal 4 | 8 | 04:00 | 8 | 07:17 | 118 | 119 | 226.25 | 9.25 |
| GS 4 | 8 | 07:17 | 9 | 09:40 | 120 | 135 | 25.25 | 32.25 |
| Post-Cal 4 | 9 | 09:40 | 9 | 12:57 | 136 | 137 | 48.25 | 64.25 |
| Pre-Cal 5 | 10 | 03:47 | 10 | 07:05 | 147 | 148 | 224.25 | 7.25 |
| GS 5 | 10 | 07:05 | 11 | 09:27 | 149 | 164 | 23.25 | 30.25 |
| Post-Cal 5 | 11 | 09:27 | 11 | 12:45 | 165 | 166 | 46.25 | 62.25 |
| Pre-Cal 6 | 12 | 05:14 | 12 | 08:31 | 177 | 178 | 5.25 | 21.25 |
| GS 6 | 12 | 08:31 | 13 | 10:54 | 179 | 194 | 37.25 | 44.25 |
| Post-Cal 6 | 13 | 10:54 | 13 | 14:12 | 195 | 196 | 60.25 | 76.25 |
| Pre-Cal 7 | 14 | 05:02 | 14 | 08:19 | 206 | 207 | 3.25 | 19.25 |
| GS 7 | 14 | 08:19 | 15 | 10:41 | 208 | 223 | 35.25 | 42.25 |
| Post-Cal 7 | 15 | 10:41 | 15 | 13:59 | 224 | 225 | 58.25 | 74.25 |

# REFERENCES

1) Beer, R., T.A. Glavich and D.M. Rider, “Tropospheric Emission Spectrometer for the Earth Observing System AURA Satellite”,  Appl. Opt. 40, 2356 - 2367 (2001)

2) Realmuto, V.J. and H.M. Worden, "Impact of atmospheric water vapor on the thermal infrared remote sensing of volcanic sulfur dioxide emissions: A case study from the Pu'u 'O'o vent of Kilauea Volcano, Hawaii", , J. Geophys. Res.  105 ,  21,497 – 21,507, (2000)

3) Worden, H.M., R. Beer and C.P.Rinsland, "Airborne High Resolution Infrared Spectroscopy of Western Wildfires", J. Geophys. Res. 102, 1287-1299 (1997)

# 8	ACRONYMS

| AN |  | Ascending Node of the orbit (Equator crossing northbound) |
| --- | --- | --- |
| ARM |  | Atmospheric Radiation Measurements (DoE program) |
| AVDC |  | Aura Validation Data Center (at the Goddard Space Flight Center) |
| DAAC |  | Distributed Active Archive Center |
| DN |  | Descending Node of the orbit (Equator crossing southbound) |
| EOS |  | Earth Observing System (Aura is a component) |
| GMT |  | Greenwich Mean Time (officially obsolete) |
| GSFC |  | NASA Goddard Space Flight Center |
| HiRDLS |  | High Resolution Dynamics Limb Sounder (Aura instrument) |
| ICS |  | Interferometer Control System |
| JPL |  | Jet Propulsion Laboratory, California Institute of Technology |
| LaRC |  | NASA Langley Research Center |
| LMST |  | Local Mean Solar Time |
| MLS |  | Microwave Limb Sounder (Aura instrument) |
| MOT |  | Mission Operations Team |
| MPT |  | Macro Parameter Table |
| NASA |  | National Aeronautics and Space Administration |
| NDSC |  | Network for the Detection of Stratospheric Change (NASA program) |
| NESR |  | Noise Equivalent Source Radiance |
| OBRCS |  | On-board Radiometric Calibration Source (TES sub-system) |
| OBSCS |  | On-board Spatial Calibration Source (TES sub-system) |
| OMIS |  | Ozone Measuring Instrument System (Aura instrument) |
| PCS |  | Pointing Control System |
| SA |  | Southern Apex (most southerly latitude of the orbit) |
| SCF |  | Science Computing Facility |
| SIPS |  | Science Investigator-led Processing System |
| ST |  | Science Team |
| TES |  | Tropospheric Emission Spectrometer (Aura instrument) |
| UTC |  | Coordinated Universal Time |
| WRS |  | Worldwide Reference System (LandSat & EOS orbits) |

# APPENDIX

This appendix contains 3 further tables:

A1:	The WRS orbits sorted by path

A2:	The WRS orbits sorted in time order

A3:	Nodal parameters for the TES orbits sorted in time order

Table A1:					Table A2:

WRS longitudes sorted			WRS longitudes sorted

by path number				in time order

| Path | Order | Longitude of the Descending Node |  | Path | Order | Longitude of the Descending Node |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | 295.4000 |  | 1 | 1 | 295.4000 |
| 2 | 103 | 293.8549 |  | 17 | 2 | 270.6790 |
| 3 | 205 | 292.3099 |  | 33 | 3 | 245.9579 |
| 4 | 74 | 290.7648 |  | 49 | 4 | 221.2369 |
| 5 | 176 | 289.2197 |  | 65 | 5 | 196.5159 |
| 6 | 45 | 287.6747 |  | 81 | 6 | 171.7948 |
| 7 | 147 | 286.1296 |  | 97 | 7 | 147.0738 |
| 8 | 16 | 284.5845 |  | 113 | 8 | 122.3528 |
| 9 | 118 | 283.0395 |  | 129 | 9 | 97.6318 |
| 10 | 220 | 281.4944 |  | 145 | 10 | 72.9107 |
| 11 | 89 | 279.9494 |  | 161 | 11 | 48.1897 |
| 12 | 191 | 278.4043 |  | 177 | 12 | 23.4687 |
| 13 | 60 | 276.8592 |  | 193 | 13 | 358.7476 |
| 14 | 162 | 275.3142 |  | 209 | 14 | 334.0266 |
| 15 | 31 | 273.7691 |  | 225 | 15 | 309.3056 |
| 16 | 133 | 272.2240 |  | 8 | 16 | 284.5845 |
| 17 | 2 | 270.6790 |  | 24 | 17 | 259.8635 |
| 18 | 104 | 269.1339 |  | 40 | 18 | 235.1425 |
| 19 | 206 | 267.5888 |  | 56 | 19 | 210.4215 |
| 20 | 75 | 266.0438 |  | 72 | 20 | 185.7004 |
| 21 | 177 | 264.4987 |  | 88 | 21 | 160.9794 |
| 22 | 46 | 262.9536 |  | 104 | 22 | 136.2584 |
| 23 | 148 | 261.4086 |  | 120 | 23 | 111.5373 |
| 24 | 17 | 259.8635 |  | 136 | 24 | 86.8163 |
| 25 | 119 | 258.3185 |  | 152 | 25 | 62.0953 |
| 26 | 221 | 256.7734 |  | 168 | 26 | 37.3742 |
| 27 | 90 | 255.2283 |  | 184 | 27 | 12.6532 |
| 28 | 192 | 253.6833 |  | 200 | 28 | 347.9322 |
| 29 | 61 | 252.1382 |  | 216 | 29 | 323.2112 |
| 30 | 163 | 250.5931 |  | 232 | 30 | 298.4901 |
| 31 | 32 | 249.0481 |  | 15 | 31 | 273.7691 |
| 32 | 134 | 247.5030 |  | 31 | 32 | 249.0481 |
| 33 | 3 | 245.9579 |  | 47 | 33 | 224.3270 |
| 34 | 105 | 244.4129 |  | 63 | 34 | 199.6060 |
| 35 | 207 | 242.8678 |  | 79 | 35 | 174.8850 |
| 36 | 76 | 241.3227 |  | 95 | 36 | 150.1639 |
| 37 | 178 | 239.7777 |  | 111 | 37 | 125.4429 |
| 38 | 47 | 238.2326 |  | 127 | 38 | 100.7219 |
| 39 | 149 | 236.6876 |  | 143 | 39 | 76.0009 |
| 40 | 18 | 235.1425 |  | 159 | 40 | 51.2798 |
| 41 | 120 | 233.5974 |  | 175 | 41 | 26.5588 |
| 42 | 222 | 232.0524 |  | 191 | 42 | 1.8378 |
| 43 | 91 | 230.5073 |  | 207 | 43 | 337.1167 |
| 44 | 193 | 228.9622 |  | 223 | 44 | 312.3957 |
| 45 | 62 | 227.4172 |  | 6 | 45 | 287.6747 |
| 46 | 164 | 225.8721 |  | 22 | 46 | 262.9536 |
| 47 | 33 | 224.3270 |  | 38 | 47 | 238.2326 |
| 48 | 135 | 222.7820 |  | 54 | 48 | 213.5116 |
| 49 | 4 | 221.2369 |  | 70 | 49 | 188.7906 |
| 50 | 106 | 219.6918 |  | 86 | 50 | 164.0695 |
| 51 | 208 | 218.1468 |  | 102 | 51 | 139.3485 |
| 52 | 77 | 216.6017 |  | 118 | 52 | 114.6275 |
| 53 | 179 | 215.0567 |  | 134 | 53 | 89.9064 |
| 54 | 48 | 213.5116 |  | 150 | 54 | 65.1854 |
| 55 | 150 | 211.9665 |  | 166 | 55 | 40.4644 |
| 56 | 19 | 210.4215 |  | 182 | 56 | 15.7433 |
| 57 | 121 | 208.8764 |  | 198 | 57 | 351.0223 |
| 58 | 223 | 207.3313 |  | 214 | 58 | 326.3013 |
| 59 | 92 | 205.7863 |  | 230 | 59 | 301.5803 |
| 60 | 194 | 204.2412 |  | 13 | 60 | 276.8592 |
| 61 | 63 | 202.6961 |  | 29 | 61 | 252.1382 |
| 62 | 165 | 201.1511 |  | 45 | 62 | 227.4172 |
| 63 | 34 | 199.6060 |  | 61 | 63 | 202.6961 |
| 64 | 136 | 198.0609 |  | 77 | 64 | 177.9751 |
| 65 | 5 | 196.5159 |  | 93 | 65 | 153.2541 |
| 66 | 107 | 194.9708 |  | 109 | 66 | 128.5330 |
| 67 | 209 | 193.4258 |  | 125 | 67 | 103.8120 |
| 68 | 78 | 191.8807 |  | 141 | 68 | 79.0910 |
| 69 | 180 | 190.3356 |  | 157 | 69 | 54.3700 |
| 70 | 49 | 188.7906 |  | 173 | 70 | 29.6489 |
| 71 | 151 | 187.2455 |  | 189 | 71 | 4.9279 |
| 72 | 20 | 185.7004 |  | 205 | 72 | 340.2069 |
| 73 | 122 | 184.1554 |  | 221 | 73 | 315.4858 |
| 74 | 224 | 182.6103 |  | 4 | 74 | 290.7648 |
| 75 | 93 | 181.0652 |  | 20 | 75 | 266.0438 |
| 76 | 195 | 179.5202 |  | 36 | 76 | 241.3227 |
| 77 | 64 | 177.9751 |  | 52 | 77 | 216.6017 |
| 78 | 166 | 176.4300 |  | 68 | 78 | 191.8807 |
| 79 | 35 | 174.8850 |  | 84 | 79 | 167.1597 |
| 80 | 137 | 173.3399 |  | 100 | 80 | 142.4386 |
| 81 | 6 | 171.7948 |  | 116 | 81 | 117.7176 |
| 82 | 108 | 170.2498 |  | 132 | 82 | 92.9966 |
| 83 | 210 | 168.7047 |  | 148 | 83 | 68.2755 |
| 84 | 79 | 167.1597 |  | 164 | 84 | 43.5545 |
| 85 | 181 | 165.6146 |  | 180 | 85 | 18.8335 |
| 86 | 50 | 164.0695 |  | 196 | 86 | 354.1124 |
| 87 | 152 | 162.5245 |  | 212 | 87 | 329.3914 |
| 88 | 21 | 160.9794 |  | 228 | 88 | 304.6704 |
| 89 | 123 | 159.4343 |  | 11 | 89 | 279.9494 |
| 90 | 225 | 157.8893 |  | 27 | 90 | 255.2283 |
| 91 | 94 | 156.3442 |  | 43 | 91 | 230.5073 |
| 92 | 196 | 154.7991 |  | 59 | 92 | 205.7863 |
| 93 | 65 | 153.2541 |  | 75 | 93 | 181.0652 |
| 94 | 167 | 151.7090 |  | 91 | 94 | 156.3442 |
| 95 | 36 | 150.1639 |  | 107 | 95 | 131.6232 |
| 96 | 138 | 148.6189 |  | 123 | 96 | 106.9021 |
| 97 | 7 | 147.0738 |  | 139 | 97 | 82.1811 |
| 98 | 109 | 145.5288 |  | 155 | 98 | 57.4601 |
| 99 | 211 | 143.9837 |  | 171 | 99 | 32.7391 |
| 100 | 80 | 142.4386 |  | 187 | 100 | 8.0180 |
| 101 | 182 | 140.8936 |  | 203 | 101 | 343.2970 |
| 102 | 51 | 139.3485 |  | 219 | 102 | 318.5760 |
| 103 | 153 | 137.8034 |  | 2 | 103 | 293.8549 |
| 104 | 22 | 136.2584 |  | 18 | 104 | 269.1339 |
| 105 | 124 | 134.7133 |  | 34 | 105 | 244.4129 |
| 106 | 226 | 133.1682 |  | 50 | 106 | 219.6918 |
| 107 | 95 | 131.6232 |  | 66 | 107 | 194.9708 |
| 108 | 197 | 130.0781 |  | 82 | 108 | 170.2498 |
| 109 | 66 | 128.5330 |  | 98 | 109 | 145.5288 |
| 110 | 168 | 126.9880 |  | 114 | 110 | 120.8077 |
| 111 | 37 | 125.4429 |  | 130 | 111 | 96.0867 |
| 112 | 139 | 123.8979 |  | 146 | 112 | 71.3657 |
| 113 | 8 | 122.3528 |  | 162 | 113 | 46.6446 |
| 114 | 110 | 120.8077 |  | 178 | 114 | 21.9236 |
| 115 | 212 | 119.2627 |  | 194 | 115 | 357.2026 |
| 116 | 81 | 117.7176 |  | 210 | 116 | 332.4815 |
| 117 | 183 | 116.1725 |  | 226 | 117 | 307.7605 |
| 118 | 52 | 114.6275 |  | 9 | 118 | 283.0395 |
| 119 | 154 | 113.0824 |  | 25 | 119 | 258.3185 |
| 120 | 23 | 111.5373 |  | 41 | 120 | 233.5974 |
| 121 | 125 | 109.9923 |  | 57 | 121 | 208.8764 |
| 122 | 227 | 108.4472 |  | 73 | 122 | 184.1554 |
| 123 | 96 | 106.9021 |  | 89 | 123 | 159.4343 |
| 124 | 198 | 105.3571 |  | 105 | 124 | 134.7133 |
| 125 | 67 | 103.8120 |  | 121 | 125 | 109.9923 |
| 126 | 169 | 102.2670 |  | 137 | 126 | 85.2712 |
| 127 | 38 | 100.7219 |  | 153 | 127 | 60.5502 |
| 128 | 140 | 99.1768 |  | 169 | 128 | 35.8292 |
| 129 | 9 | 97.6318 |  | 185 | 129 | 11.1082 |
| 130 | 111 | 96.0867 |  | 201 | 130 | 346.3871 |
| 131 | 213 | 94.5416 |  | 217 | 131 | 321.6661 |
| 132 | 82 | 92.9966 |  | 233 | 132 | 296.9451 |
| 133 | 184 | 91.4515 |  | 16 | 133 | 272.2240 |
| 134 | 53 | 89.9064 |  | 32 | 134 | 247.5030 |
| 135 | 155 | 88.3614 |  | 48 | 135 | 222.7820 |
| 136 | 24 | 86.8163 |  | 64 | 136 | 198.0609 |
| 137 | 126 | 85.2712 |  | 80 | 137 | 173.3399 |
| 138 | 228 | 83.7262 |  | 96 | 138 | 148.6189 |
| 139 | 97 | 82.1811 |  | 112 | 139 | 123.8979 |
| 140 | 199 | 80.6361 |  | 128 | 140 | 99.1768 |
| 141 | 68 | 79.0910 |  | 144 | 141 | 74.4558 |
| 142 | 170 | 77.5459 |  | 160 | 142 | 49.7348 |
| 143 | 39 | 76.0009 |  | 176 | 143 | 25.0137 |
| 144 | 141 | 74.4558 |  | 192 | 144 | 0.2927 |
| 145 | 10 | 72.9107 |  | 208 | 145 | 335.5717 |
| 146 | 112 | 71.3657 |  | 224 | 146 | 310.8506 |
| 147 | 214 | 69.8206 |  | 7 | 147 | 286.1296 |
| 148 | 83 | 68.2755 |  | 23 | 148 | 261.4086 |
| 149 | 185 | 66.7305 |  | 39 | 149 | 236.6876 |
| 150 | 54 | 65.1854 |  | 55 | 150 | 211.9665 |
| 151 | 156 | 63.6403 |  | 71 | 151 | 187.2455 |
| 152 | 25 | 62.0953 |  | 87 | 152 | 162.5245 |
| 153 | 127 | 60.5502 |  | 103 | 153 | 137.8034 |
| 154 | 229 | 59.0052 |  | 119 | 154 | 113.0824 |
| 155 | 98 | 57.4601 |  | 135 | 155 | 88.3614 |
| 156 | 200 | 55.9150 |  | 151 | 156 | 63.6403 |
| 157 | 69 | 54.3700 |  | 167 | 157 | 38.9193 |
| 158 | 171 | 52.8249 |  | 183 | 158 | 14.1983 |
| 159 | 40 | 51.2798 |  | 199 | 159 | 349.4773 |
| 160 | 142 | 49.7348 |  | 215 | 160 | 324.7562 |
| 161 | 11 | 48.1897 |  | 231 | 161 | 300.0352 |
| 162 | 113 | 46.6446 |  | 14 | 162 | 275.3142 |
| 163 | 215 | 45.0996 |  | 30 | 163 | 250.5931 |
| 164 | 84 | 43.5545 |  | 46 | 164 | 225.8721 |
| 165 | 186 | 42.0094 |  | 62 | 165 | 201.1511 |
| 166 | 55 | 40.4644 |  | 78 | 166 | 176.4300 |
| 167 | 157 | 38.9193 |  | 94 | 167 | 151.7090 |
| 168 | 26 | 37.3742 |  | 110 | 168 | 126.9880 |
| 169 | 128 | 35.8292 |  | 126 | 169 | 102.2670 |
| 170 | 230 | 34.2841 |  | 142 | 170 | 77.5459 |
| 171 | 99 | 32.7391 |  | 158 | 171 | 52.8249 |
| 172 | 201 | 31.1940 |  | 174 | 172 | 28.1039 |
| 173 | 70 | 29.6489 |  | 190 | 173 | 3.3828 |
| 174 | 172 | 28.1039 |  | 206 | 174 | 338.6618 |
| 175 | 41 | 26.5588 |  | 222 | 175 | 313.9408 |
| 176 | 143 | 25.0137 |  | 5 | 176 | 289.2197 |
| 177 | 12 | 23.4687 |  | 21 | 177 | 264.4987 |
| 178 | 114 | 21.9236 |  | 37 | 178 | 239.7777 |
| 179 | 216 | 20.3785 |  | 53 | 179 | 215.0567 |
| 180 | 85 | 18.8335 |  | 69 | 180 | 190.3356 |
| 181 | 187 | 17.2884 |  | 85 | 181 | 165.6146 |
| 182 | 56 | 15.7433 |  | 101 | 182 | 140.8936 |
| 183 | 158 | 14.1983 |  | 117 | 183 | 116.1725 |
| 184 | 27 | 12.6532 |  | 133 | 184 | 91.4515 |
| 185 | 129 | 11.1082 |  | 149 | 185 | 66.7305 |
| 186 | 231 | 9.5631 |  | 165 | 186 | 42.0094 |
| 187 | 100 | 8.0180 |  | 181 | 187 | 17.2884 |
| 188 | 202 | 6.4730 |  | 197 | 188 | 352.5674 |
| 189 | 71 | 4.9279 |  | 213 | 189 | 327.8464 |
| 190 | 173 | 3.3828 |  | 229 | 190 | 303.1253 |
| 191 | 42 | 1.8378 |  | 12 | 191 | 278.4043 |
| 192 | 144 | 0.2927 |  | 28 | 192 | 253.6833 |
| 193 | 13 | 358.7476 |  | 44 | 193 | 228.9622 |
| 194 | 115 | 357.2026 |  | 60 | 194 | 204.2412 |
| 195 | 217 | 355.6575 |  | 76 | 195 | 179.5202 |
| 196 | 86 | 354.1124 |  | 92 | 196 | 154.7991 |
| 197 | 188 | 352.5674 |  | 108 | 197 | 130.0781 |
| 198 | 57 | 351.0223 |  | 124 | 198 | 105.3571 |
| 199 | 159 | 349.4773 |  | 140 | 199 | 80.6361 |
| 200 | 28 | 347.9322 |  | 156 | 200 | 55.9150 |
| 201 | 130 | 346.3871 |  | 172 | 201 | 31.1940 |
| 202 | 232 | 344.8421 |  | 188 | 202 | 6.4730 |
| 203 | 101 | 343.2970 |  | 204 | 203 | 341.7519 |
| 204 | 203 | 341.7519 |  | 220 | 204 | 317.0309 |
| 205 | 72 | 340.2069 |  | 3 | 205 | 292.3099 |
| 206 | 174 | 338.6618 |  | 19 | 206 | 267.5888 |
| 207 | 43 | 337.1167 |  | 35 | 207 | 242.8678 |
| 208 | 145 | 335.5717 |  | 51 | 208 | 218.1468 |
| 209 | 14 | 334.0266 |  | 67 | 209 | 193.4258 |
| 210 | 116 | 332.4815 |  | 83 | 210 | 168.7047 |
| 211 | 218 | 330.9365 |  | 99 | 211 | 143.9837 |
| 212 | 87 | 329.3914 |  | 115 | 212 | 119.2627 |
| 213 | 189 | 327.8464 |  | 131 | 213 | 94.5416 |
| 214 | 58 | 326.3013 |  | 147 | 214 | 69.8206 |
| 215 | 160 | 324.7562 |  | 163 | 215 | 45.0996 |
| 216 | 29 | 323.2112 |  | 179 | 216 | 20.3785 |
| 217 | 131 | 321.6661 |  | 195 | 217 | 355.6575 |
| 218 | 233 | 320.1210 |  | 211 | 218 | 330.9365 |
| 219 | 102 | 318.5760 |  | 227 | 219 | 306.2155 |
| 220 | 204 | 317.0309 |  | 10 | 220 | 281.4944 |
| 221 | 73 | 315.4858 |  | 26 | 221 | 256.7734 |
| 222 | 175 | 313.9408 |  | 42 | 222 | 232.0524 |
| 223 | 44 | 312.3957 |  | 58 | 223 | 207.3313 |
| 224 | 146 | 310.8506 |  | 74 | 224 | 182.6103 |
| 225 | 15 | 309.3056 |  | 90 | 225 | 157.8893 |
| 226 | 117 | 307.7605 |  | 106 | 226 | 133.1682 |
| 227 | 219 | 306.2155 |  | 122 | 227 | 108.4472 |
| 228 | 88 | 304.6704 |  | 138 | 228 | 83.7262 |
| 229 | 190 | 303.1253 |  | 154 | 229 | 59.0052 |
| 230 | 59 | 301.5803 |  | 170 | 230 | 34.2841 |
| 231 | 161 | 300.0352 |  | 186 | 231 | 9.5631 |
| 232 | 30 | 298.4901 |  | 202 | 232 | 344.8421 |
| 233 | 132 | 296.9451 |  | 218 | 233 | 320.1210 |

Table A3: Nodal Parameters for the TES orbits

| TES Orbit | WRS path | UTC Day | Longitude of Southern Apex | UTC of Southern Apex | Longitude of Ascending Node | UTC of Ascending Node | Longitude of Descending Node | UTC of Descending node |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | 202.25 | 0 | 261.02236 | 01:31:28 | 177.20262 | 01:56:11 | 344.84210 | 02:45:38 |
| 1 | 218.25 | 0 | 236.30126 | 03:10:21 | 152.48151 | 03:35:04 | 320.12100 | 04:24:31 |
| 2 | 1.25 | 0 | 211.58026 | 04:49:14 | 127.76051 | 05:13:57 | 295.40000 | 06:03:24 |
| 3 | 17.25 | 0 | 186.85926 | 06:28:07 | 103.03951 | 06:52:51 | 270.67900 | 07:42:17 |
| 4 | 33.25 | 0 | 162.13816 | 08:07:00 | 78.31841 | 08:31:44 | 245.95790 | 09:21:10 |
| 5 | 49.25 | 0 | 137.41716 | 09:45:53 | 53.59741 | 10:10:37 | 221.23690 | 11:00:03 |
| 6 | 65.25 | 0 | 112.69616 | 11:24:46 | 28.87641 | 11:49:30 | 196.51590 | 12:38:56 |
| 7 | 81.25 | 0 | 87.97506 | 13:03:39 | 4.15532 | 13:28:23 | 171.79480 | 14:17:49 |
| 8 | 97.25 | 0 | 63.25406 | 14:42:33 | 339.43431 | 15:07:16 | 147.07380 | 15:56:42 |
| 9 | 113.25 | 0 | 38.53306 | 16:21:26 | 314.71331 | 16:46:09 | 122.35280 | 17:35:35 |
| 10 | 129.25 | 0 | 13.81206 | 18:00:19 | 289.99231 | 18:25:02 | 97.63180 | 19:14:28 |
| 11 | 145.25 | 0 | 349.09096 | 19:39:12 | 265.27121 | 20:03:55 | 72.91070 | 20:53:21 |
| 12 | 161.25 | 0 | 324.36996 | 21:18:05 | 240.55021 | 21:42:48 | 48.18970 | 22:32:14 |
| 13 | 177.25 | 0 | 299.64896 | 22:56:58 | 215.82921 | 23:21:41 | 23.46870 | 00:11:08 |
| 14 | 193.25 | 1 | 274.92786 | 00:35:51 | 191.10811 | 01:00:34 | 358.74760 | 01:50:01 |
| 15 | 209.25 | 1 | 250.20686 | 02:14:44 | 166.38711 | 02:39:27 | 334.02660 | 03:28:54 |
| 16 | 225.25 | 1 | 225.48586 | 03:53:37 | 141.66612 | 04:18:20 | 309.30560 | 05:07:47 |
| 17 | 8.25 | 1 | 200.76476 | 05:32:30 | 116.94501 | 05:57:13 | 284.58450 | 06:46:40 |
| 18 | 24.25 | 1 | 176.04376 | 07:11:23 | 92.22401 | 07:36:06 | 259.86350 | 08:25:33 |
| 19 | 40.25 | 1 | 151.32276 | 08:50:16 | 67.50302 | 09:14:59 | 235.14250 | 10:04:26 |
| 20 | 56.25 | 1 | 126.60176 | 10:29:09 | 42.78202 | 10:53:52 | 210.42150 | 11:43:19 |
| 21 | 72.25 | 1 | 101.88066 | 12:08:02 | 18.06091 | 12:32:45 | 185.70040 | 13:22:12 |
| 22 | 88.25 | 1 | 77.15966 | 13:46:55 | 353.33992 | 14:11:38 | 160.97940 | 15:01:05 |
| 23 | 104.25 | 1 | 52.43866 | 15:25:48 | 328.61892 | 15:50:31 | 136.25840 | 16:39:58 |
| 24 | 120.25 | 1 | 27.71756 | 17:04:41 | 303.89781 | 17:29:25 | 111.53730 | 18:18:51 |
| 25 | 136.25 | 1 | 2.99656 | 18:43:34 | 279.17681 | 19:08:18 | 86.81630 | 19:57:44 |
| 26 | 152.25 | 1 | 338.27556 | 20:22:27 | 254.45582 | 20:47:11 | 62.09530 | 21:36:37 |
| 27 | 168.25 | 1 | 313.55446 | 22:01:20 | 229.73471 | 22:26:04 | 37.37420 | 23:15:30 |
| 28 | 184.25 | 1 | 288.83346 | 23:40:13 | 205.01371 | 00:04:57 | 12.65320 | 00:54:23 |
| 29 | 200.25 | 2 | 264.11246 | 01:19:06 | 180.29272 | 01:43:50 | 347.93220 | 02:33:16 |
| 30 | 216.25 | 2 | 239.39146 | 02:58:00 | 155.57172 | 03:22:43 | 323.21120 | 04:12:09 |
| 31 | 232.25 | 2 | 214.67036 | 04:36:53 | 130.85061 | 05:01:36 | 298.49010 | 05:51:02 |
| 32 | 15.25 | 2 | 189.94936 | 06:15:46 | 106.12961 | 06:40:29 | 273.76910 | 07:29:55 |
| 33 | 31.25 | 2 | 165.22836 | 07:54:39 | 81.40861 | 08:19:22 | 249.04810 | 09:08:48 |
| 34 | 47.25 | 2 | 140.50726 | 09:33:32 | 56.68751 | 09:58:15 | 224.32700 | 10:47:42 |
| 35 | 63.25 | 2 | 115.78626 | 11:12:25 | 31.96651 | 11:37:08 | 199.60600 | 12:26:35 |
| 36 | 79.25 | 2 | 91.06526 | 12:51:18 | 7.24551 | 13:16:01 | 174.88500 | 14:05:28 |
| 37 | 95.25 | 2 | 66.34416 | 14:30:11 | 342.52441 | 14:54:54 | 150.16390 | 15:44:21 |
| 38 | 111.25 | 2 | 41.62316 | 16:09:04 | 317.80341 | 16:33:47 | 125.44290 | 17:23:14 |
| 39 | 127.25 | 2 | 16.90216 | 17:47:57 | 293.08241 | 18:12:40 | 100.72190 | 19:02:07 |
| 40 | 143.25 | 2 | 352.18116 | 19:26:50 | 268.36141 | 19:51:33 | 76.00090 | 20:41:00 |
| 41 | 159.25 | 2 | 327.46006 | 21:05:43 | 243.64031 | 21:30:26 | 51.27980 | 22:19:53 |
| 42 | 175.25 | 2 | 302.73906 | 22:44:36 | 218.91931 | 23:09:19 | 26.55880 | 23:58:46 |
| 43 | 191.25 | 3 | 278.01806 | 00:23:29 | 194.19831 | 00:48:12 | 1.83780 | 01:37:39 |
| 44 | 207.25 | 3 | 253.29696 | 02:02:22 | 169.47721 | 02:27:05 | 337.11670 | 03:16:32 |
| 45 | 223.25 | 3 | 228.57596 | 03:41:15 | 144.75621 | 04:05:59 | 312.39570 | 04:55:25 |
| 46 | 6.25 | 3 | 203.85496 | 05:20:08 | 120.03521 | 05:44:52 | 287.67470 | 06:34:18 |
| 47 | 22.25 | 3 | 179.13386 | 06:59:01 | 95.31411 | 07:23:45 | 262.95360 | 08:13:11 |
| 48 | 38.25 | 3 | 154.41286 | 08:37:54 | 70.59311 | 09:02:38 | 238.23260 | 09:52:04 |
| 49 | 54.25 | 3 | 129.69186 | 10:16:47 | 45.87211 | 10:41:31 | 213.51160 | 11:30:57 |
| 50 | 70.25 | 3 | 104.97086 | 11:55:40 | 21.15112 | 12:20:24 | 188.79060 | 13:09:50 |
| 51 | 86.25 | 3 | 80.24976 | 13:34:34 | 356.43002 | 13:59:17 | 164.06950 | 14:48:43 |
| 52 | 102.25 | 3 | 55.52876 | 15:13:27 | 331.70902 | 15:38:10 | 139.34850 | 16:27:36 |
| 53 | 118.25 | 3 | 30.80776 | 16:52:20 | 306.98802 | 17:17:03 | 114.62750 | 18:06:29 |
| 54 | 134.25 | 3 | 6.08666 | 18:31:13 | 282.26691 | 18:55:56 | 89.90640 | 19:45:22 |
| 55 | 150.25 | 3 | 341.36566 | 20:10:06 | 257.54591 | 20:34:49 | 65.18540 | 21:24:16 |
| 56 | 166.25 | 3 | 316.64466 | 21:48:59 | 232.82491 | 22:13:42 | 40.46440 | 23:03:09 |
| 57 | 182.25 | 3 | 291.92356 | 23:27:52 | 208.10381 | 23:52:35 | 15.74330 | 00:42:02 |
| 58 | 198.25 | 4 | 267.20256 | 01:06:45 | 183.38281 | 01:31:28 | 351.02230 | 02:20:55 |
| 59 | 214.25 | 4 | 242.48156 | 02:45:38 | 158.66182 | 03:10:21 | 326.30130 | 03:59:48 |
| 60 | 230.25 | 4 | 217.76056 | 04:24:31 | 133.94082 | 04:49:14 | 301.58030 | 05:38:41 |
| 61 | 13.25 | 4 | 193.03946 | 06:03:24 | 109.21971 | 06:28:07 | 276.85920 | 07:17:34 |
| 62 | 29.25 | 4 | 168.31846 | 07:42:17 | 84.49872 | 08:07:00 | 252.13820 | 08:56:27 |
| 63 | 45.25 | 4 | 143.59746 | 09:21:10 | 59.77772 | 09:45:53 | 227.41720 | 10:35:20 |
| 64 | 61.25 | 4 | 118.87636 | 11:00:03 | 35.05661 | 11:24:46 | 202.69610 | 12:14:13 |
| 65 | 77.25 | 4 | 94.15536 | 12:38:56 | 10.33561 | 13:03:39 | 177.97510 | 13:53:06 |
| 66 | 93.25 | 4 | 69.43436 | 14:17:49 | 345.61461 | 14:42:32 | 153.25410 | 15:31:59 |
| 67 | 109.25 | 4 | 44.71326 | 15:56:42 | 320.89351 | 16:21:26 | 128.53300 | 17:10:52 |
| 68 | 125.25 | 4 | 19.99226 | 17:35:35 | 296.17251 | 18:00:19 | 103.81200 | 18:49:45 |
| 69 | 141.25 | 4 | 355.27126 | 19:14:28 | 271.45151 | 19:39:12 | 79.09100 | 20:28:38 |
| 70 | 157.25 | 4 | 330.55026 | 20:53:21 | 246.73051 | 21:18:05 | 54.37000 | 22:07:31 |
| 71 | 173.25 | 4 | 305.82916 | 22:32:14 | 222.00941 | 22:56:58 | 29.64890 | 23:46:24 |
| 72 | 189.25 | 5 | 281.10816 | 00:11:08 | 197.28841 | 00:35:51 | 4.92790 | 01:25:17 |
| 73 | 205.25 | 5 | 256.38716 | 01:50:01 | 172.56742 | 02:14:44 | 340.20690 | 03:04:10 |
| 74 | 221.25 | 5 | 231.66606 | 03:28:54 | 147.84631 | 03:53:37 | 315.48580 | 04:43:03 |
| 75 | 4.25 | 5 | 206.94506 | 05:07:47 | 123.12531 | 05:32:30 | 290.76480 | 06:21:56 |
| 76 | 20.25 | 5 | 182.22406 | 06:46:40 | 98.40431 | 07:11:23 | 266.04380 | 08:00:49 |
| 77 | 36.25 | 5 | 157.50296 | 08:25:33 | 73.68321 | 08:50:16 | 241.32270 | 09:39:43 |
| 78 | 52.25 | 5 | 132.78196 | 10:04:26 | 48.96221 | 10:29:09 | 216.60170 | 11:18:36 |
| 79 | 68.25 | 5 | 108.06096 | 11:43:19 | 24.24121 | 12:08:02 | 191.88070 | 12:57:29 |
| 80 | 84.25 | 5 | 83.33996 | 13:22:12 | 359.52022 | 13:46:55 | 167.15970 | 14:36:22 |
| 81 | 100.25 | 5 | 58.61886 | 15:01:05 | 334.79912 | 15:25:48 | 142.43860 | 16:15:15 |
| 82 | 116.25 | 5 | 33.89786 | 16:39:58 | 310.07812 | 17:04:41 | 117.71760 | 17:54:08 |
| 83 | 132.25 | 5 | 9.17686 | 18:18:51 | 285.35712 | 18:43:34 | 92.99660 | 19:33:01 |
| 84 | 148.25 | 5 | 344.45576 | 19:57:44 | 260.63601 | 20:22:27 | 68.27550 | 21:11:54 |
| 85 | 164.25 | 5 | 319.73476 | 21:36:37 | 235.91501 | 22:01:20 | 43.55450 | 22:50:47 |
| 86 | 180.25 | 5 | 295.01376 | 23:15:30 | 211.19401 | 23:40:13 | 18.83350 | 00:29:40 |
| 87 | 196.25 | 6 | 270.29266 | 00:54:23 | 186.47291 | 01:19:07 | 354.11240 | 02:08:33 |
| 88 | 212.25 | 6 | 245.57166 | 02:33:16 | 161.75191 | 02:58:00 | 329.39140 | 03:47:26 |
| 89 | 228.25 | 6 | 220.85066 | 04:12:09 | 137.03091 | 04:36:53 | 304.67040 | 05:26:19 |
| 90 | 11.25 | 6 | 196.12966 | 05:51:02 | 112.30992 | 06:15:46 | 279.94940 | 07:05:12 |
| 91 | 27.25 | 6 | 171.40856 | 07:29:55 | 87.58881 | 07:54:39 | 255.22830 | 08:44:05 |
| 92 | 43.25 | 6 | 146.68756 | 09:08:48 | 62.86781 | 09:33:32 | 230.50730 | 10:22:58 |
| 93 | 59.25 | 6 | 121.96656 | 10:47:42 | 38.14682 | 11:12:25 | 205.78630 | 12:01:51 |
| 94 | 75.25 | 6 | 97.24546 | 12:26:35 | 13.42571 | 12:51:18 | 181.06520 | 13:40:44 |
| 95 | 91.25 | 6 | 72.52446 | 14:05:28 | 348.70471 | 14:30:11 | 156.34420 | 15:19:37 |
| 96 | 107.25 | 6 | 47.80346 | 15:44:21 | 323.98371 | 16:09:04 | 131.62320 | 16:58:30 |
| 97 | 123.25 | 6 | 23.08236 | 17:23:14 | 299.26261 | 17:47:57 | 106.90210 | 18:37:23 |
| 98 | 139.25 | 6 | 358.36136 | 19:02:07 | 274.54161 | 19:26:50 | 82.18110 | 20:16:17 |
| 99 | 155.25 | 6 | 333.64036 | 20:41:00 | 249.82061 | 21:05:43 | 57.46010 | 21:55:10 |
| 100 | 171.25 | 6 | 308.91936 | 22:19:53 | 225.09962 | 22:44:36 | 32.73910 | 23:34:03 |
| 101 | 187.25 | 6 | 284.19826 | 23:58:46 | 200.37851 | 00:23:29 | 8.01800 | 01:12:56 |
| 102 | 203.25 | 7 | 259.47726 | 01:37:39 | 175.65752 | 02:02:22 | 343.29700 | 02:51:49 |
| 103 | 219.25 | 7 | 234.75626 | 03:16:32 | 150.93652 | 03:41:15 | 318.57600 | 04:30:42 |
| 104 | 2.25 | 7 | 210.03516 | 04:55:25 | 126.21541 | 05:20:08 | 293.85490 | 06:09:35 |
| 105 | 18.25 | 7 | 185.31416 | 06:34:18 | 101.49441 | 06:59:01 | 269.13390 | 07:48:28 |
| 106 | 34.25 | 7 | 160.59316 | 08:13:11 | 76.77341 | 08:37:54 | 244.41290 | 09:27:21 |
| 107 | 50.25 | 7 | 135.87206 | 09:52:04 | 52.05231 | 10:16:47 | 219.69180 | 11:06:14 |
| 108 | 66.25 | 7 | 111.15106 | 11:30:57 | 27.33131 | 11:55:40 | 194.97080 | 12:45:07 |
| 109 | 82.25 | 7 | 86.43006 | 13:09:50 | 2.61031 | 13:34:34 | 170.24980 | 14:24:00 |
| 110 | 98.25 | 7 | 61.70906 | 14:48:43 | 337.88932 | 15:13:27 | 145.52880 | 16:02:53 |
| 111 | 114.25 | 7 | 36.98796 | 16:27:36 | 313.16821 | 16:52:20 | 120.80770 | 17:41:46 |
| 112 | 130.25 | 7 | 12.26696 | 18:06:29 | 288.44721 | 18:31:13 | 96.08670 | 19:20:39 |
| 113 | 146.25 | 7 | 347.54596 | 19:45:22 | 263.72622 | 20:10:06 | 71.36570 | 20:59:32 |
| 114 | 162.25 | 7 | 322.82486 | 21:24:16 | 239.00511 | 21:48:59 | 46.64460 | 22:38:25 |
| 115 | 178.25 | 7 | 298.10386 | 23:03:09 | 214.28411 | 23:27:52 | 21.92360 | 00:17:18 |
| 116 | 194.25 | 8 | 273.38286 | 00:42:02 | 189.56312 | 01:06:45 | 357.20260 | 01:56:11 |
| 117 | 210.25 | 8 | 248.66176 | 02:20:55 | 164.84201 | 02:45:38 | 332.48150 | 03:35:04 |
| 118 | 226.25 | 8 | 223.94076 | 03:59:48 | 140.12101 | 04:24:31 | 307.76050 | 05:13:57 |
| 119 | 9.25 | 8 | 199.21976 | 05:38:41 | 115.40001 | 06:03:24 | 283.03950 | 06:52:51 |
| 120 | 25.25 | 8 | 174.49876 | 07:17:34 | 90.67901 | 07:42:17 | 258.31850 | 08:31:44 |
| 121 | 41.25 | 8 | 149.77766 | 08:56:27 | 65.95791 | 09:21:10 | 233.59740 | 10:10:37 |
| 122 | 57.25 | 8 | 125.05666 | 10:35:20 | 41.23691 | 11:00:03 | 208.87640 | 11:49:30 |
| 123 | 73.25 | 8 | 100.33566 | 12:14:13 | 16.51591 | 12:38:56 | 184.15540 | 13:28:23 |
| 124 | 89.25 | 8 | 75.61456 | 13:53:06 | 351.79481 | 14:17:49 | 159.43430 | 15:07:16 |
| 125 | 105.25 | 8 | 50.89356 | 15:31:59 | 327.07381 | 15:56:42 | 134.71330 | 16:46:09 |
| 126 | 121.25 | 8 | 26.17256 | 17:10:52 | 302.35281 | 17:35:35 | 109.99230 | 18:25:02 |
| 127 | 137.25 | 8 | 1.45146 | 18:49:45 | 277.63171 | 19:14:28 | 85.27120 | 20:03:55 |
| 128 | 153.25 | 8 | 336.73046 | 20:28:38 | 252.91071 | 20:53:21 | 60.55020 | 21:42:48 |
| 129 | 169.25 | 8 | 312.00946 | 22:07:31 | 228.18971 | 22:32:14 | 35.82920 | 23:21:41 |
| 130 | 185.25 | 8 | 287.28846 | 23:46:24 | 203.46872 | 00:11:08 | 11.10820 | 01:00:34 |
| 131 | 201.25 | 9 | 262.56736 | 01:25:17 | 178.74761 | 01:50:01 | 346.38710 | 02:39:27 |
| 132 | 217.25 | 9 | 237.84636 | 03:04:10 | 154.02661 | 03:28:54 | 321.66610 | 04:18:20 |
| 133 | 233.25 | 9 | 213.12536 | 04:43:03 | 129.30562 | 05:07:47 | 296.94510 | 05:57:13 |
| 134 | 16.25 | 9 | 188.40426 | 06:21:56 | 104.58451 | 06:46:40 | 272.22400 | 07:36:06 |
| 135 | 32.25 | 9 | 163.68326 | 08:00:49 | 79.86351 | 08:25:33 | 247.50300 | 09:14:59 |
| 136 | 48.25 | 9 | 138.96226 | 09:39:43 | 55.14252 | 10:04:26 | 222.78200 | 10:53:52 |
| 137 | 64.25 | 9 | 114.24116 | 11:18:36 | 30.42141 | 11:43:19 | 198.06090 | 12:32:45 |
| 138 | 80.25 | 9 | 89.52016 | 12:57:29 | 5.70041 | 13:22:12 | 173.33990 | 14:11:38 |
| 139 | 96.25 | 9 | 64.79916 | 14:36:22 | 340.97942 | 15:01:05 | 148.61890 | 15:50:31 |
| 140 | 112.25 | 9 | 40.07816 | 16:15:15 | 316.25842 | 16:39:58 | 123.89790 | 17:29:25 |
| 141 | 128.25 | 9 | 15.35706 | 17:54:08 | 291.53731 | 18:18:51 | 99.17680 | 19:08:18 |
| 142 | 144.25 | 9 | 350.63606 | 19:33:01 | 266.81631 | 19:57:44 | 74.45580 | 20:47:11 |
| 143 | 160.25 | 9 | 325.91506 | 21:11:54 | 242.09531 | 21:36:37 | 49.73480 | 22:26:04 |
| 144 | 176.25 | 9 | 301.19396 | 22:50:47 | 217.37421 | 23:15:30 | 25.01370 | 00:04:57 |
| 145 | 192.25 | 10 | 276.47296 | 00:29:40 | 192.65321 | 00:54:23 | 0.29270 | 01:43:50 |
| 146 | 208.25 | 10 | 251.75196 | 02:08:33 | 167.93222 | 02:33:16 | 335.57170 | 03:22:43 |
| 147 | 224.25 | 10 | 227.03086 | 03:47:26 | 143.21111 | 04:12:09 | 310.85060 | 05:01:36 |
| 148 | 7.25 | 10 | 202.30986 | 05:26:19 | 118.49011 | 05:51:02 | 286.12960 | 06:40:29 |
| 149 | 23.25 | 10 | 177.58886 | 07:05:12 | 93.76911 | 07:29:55 | 261.40860 | 08:19:22 |
| 150 | 39.25 | 10 | 152.86786 | 08:44:05 | 69.04811 | 09:08:48 | 236.68760 | 09:58:15 |
| 151 | 55.25 | 10 | 128.14676 | 10:22:58 | 44.32701 | 10:47:42 | 211.96650 | 11:37:08 |
| 152 | 71.25 | 10 | 103.42576 | 12:01:51 | 19.60601 | 12:26:35 | 187.24550 | 13:16:01 |
| 153 | 87.25 | 10 | 78.70476 | 13:40:44 | 354.88501 | 14:05:28 | 162.52450 | 14:54:54 |
| 154 | 103.25 | 10 | 53.98366 | 15:19:37 | 330.16391 | 15:44:21 | 137.80340 | 16:33:47 |
| 155 | 119.25 | 10 | 29.26266 | 16:58:30 | 305.44291 | 17:23:14 | 113.08240 | 18:12:40 |
| 156 | 135.25 | 10 | 4.54166 | 18:37:23 | 280.72191 | 19:02:07 | 88.36140 | 19:51:33 |
| 157 | 151.25 | 10 | 339.82056 | 20:16:17 | 256.00081 | 20:41:00 | 63.64030 | 21:30:26 |
| 158 | 167.25 | 10 | 315.09956 | 21:55:10 | 231.27981 | 22:19:53 | 38.91930 | 23:09:19 |
| 159 | 183.25 | 10 | 290.37856 | 23:34:03 | 206.55881 | 23:58:46 | 14.19830 | 00:48:12 |
| 160 | 199.25 | 11 | 265.65756 | 01:12:56 | 181.83782 | 01:37:39 | 349.47730 | 02:27:05 |
| 161 | 215.25 | 11 | 240.93646 | 02:51:49 | 157.11671 | 03:16:32 | 324.75620 | 04:05:59 |
| 162 | 231.25 | 11 | 216.21546 | 04:30:42 | 132.39571 | 04:55:25 | 300.03520 | 05:44:52 |
| 163 | 14.25 | 11 | 191.49446 | 06:09:35 | 107.67472 | 06:34:18 | 275.31420 | 07:23:45 |
| 164 | 30.25 | 11 | 166.77336 | 07:48:28 | 82.95361 | 08:13:11 | 250.59310 | 09:02:38 |
| 165 | 46.25 | 11 | 142.05236 | 09:27:21 | 58.23261 | 09:52:04 | 225.87210 | 10:41:31 |
| 166 | 62.25 | 11 | 117.33136 | 11:06:14 | 33.51162 | 11:30:57 | 201.15110 | 12:20:24 |
| 167 | 78.25 | 11 | 92.61026 | 12:45:07 | 8.79051 | 13:09:50 | 176.43000 | 13:59:17 |
| 168 | 94.25 | 11 | 67.88926 | 14:24:00 | 344.06952 | 14:48:43 | 151.70900 | 15:38:10 |
| 169 | 110.25 | 11 | 43.16826 | 16:02:53 | 319.34852 | 16:27:36 | 126.98800 | 17:17:03 |
| 170 | 126.25 | 11 | 18.44726 | 17:41:46 | 294.62752 | 18:06:29 | 102.26700 | 18:55:56 |
| 171 | 142.25 | 11 | 353.72616 | 19:20:39 | 269.90641 | 19:45:22 | 77.54590 | 20:34:49 |
| 172 | 158.25 | 11 | 329.00516 | 20:59:32 | 245.18541 | 21:24:16 | 52.82490 | 22:13:42 |
| 173 | 174.25 | 11 | 304.28416 | 22:38:25 | 220.46442 | 23:03:09 | 28.10390 | 23:52:35 |
| 174 | 190.25 | 12 | 279.56306 | 00:17:18 | 195.74331 | 00:42:02 | 3.38280 | 01:31:28 |
| 175 | 206.25 | 12 | 254.84206 | 01:56:11 | 171.02232 | 02:20:55 | 338.66180 | 03:10:21 |
| 176 | 222.25 | 12 | 230.12106 | 03:35:04 | 146.30132 | 03:59:48 | 313.94080 | 04:49:14 |
| 177 | 5.25 | 12 | 205.39996 | 05:13:57 | 121.58021 | 05:38:41 | 289.21970 | 06:28:07 |
| 178 | 21.25 | 12 | 180.67896 | 06:52:51 | 96.85921 | 07:17:34 | 264.49870 | 08:07:00 |
| 179 | 37.25 | 12 | 155.95796 | 08:31:44 | 72.13822 | 08:56:27 | 239.77770 | 09:45:53 |
| 180 | 53.25 | 12 | 131.23696 | 10:10:37 | 47.41721 | 10:35:20 | 215.05670 | 11:24:46 |
| 181 | 69.25 | 12 | 106.51586 | 11:49:30 | 22.69611 | 12:14:13 | 190.33560 | 13:03:39 |
| 182 | 85.25 | 12 | 81.79486 | 13:28:23 | 357.97511 | 13:53:06 | 165.61460 | 14:42:32 |
| 183 | 101.25 | 12 | 57.07386 | 15:07:16 | 333.25411 | 15:31:59 | 140.89360 | 16:21:26 |
| 184 | 117.25 | 12 | 32.35276 | 16:46:09 | 308.53301 | 17:10:52 | 116.17250 | 18:00:19 |
| 185 | 133.25 | 12 | 7.63176 | 18:25:02 | 283.81201 | 18:49:45 | 91.45150 | 19:39:12 |
| 186 | 149.25 | 12 | 342.91076 | 20:03:55 | 259.09101 | 20:28:38 | 66.73050 | 21:18:05 |
| 187 | 165.25 | 12 | 318.18966 | 21:42:48 | 234.36991 | 22:07:31 | 42.00940 | 22:56:58 |
| 188 | 181.25 | 12 | 293.46866 | 23:21:41 | 209.64891 | 23:46:24 | 17.28840 | 00:35:51 |
| 189 | 197.25 | 13 | 268.74766 | 01:00:34 | 184.92792 | 01:25:17 | 352.56740 | 02:14:44 |
| 190 | 213.25 | 13 | 244.02666 | 02:39:27 | 160.20692 | 03:04:10 | 327.84640 | 03:53:37 |
| 191 | 229.25 | 13 | 219.30556 | 04:18:20 | 135.48581 | 04:43:03 | 303.12530 | 05:32:30 |
| 192 | 12.25 | 13 | 194.58456 | 05:57:13 | 110.76481 | 06:21:56 | 278.40430 | 07:11:23 |
| 193 | 28.25 | 13 | 169.86356 | 07:36:06 | 86.04381 | 08:00:49 | 253.68330 | 08:50:16 |
| 194 | 44.25 | 13 | 145.14246 | 09:14:59 | 61.32271 | 09:39:43 | 228.96220 | 10:29:09 |
| 195 | 60.25 | 13 | 120.42146 | 10:53:52 | 36.60171 | 11:18:36 | 204.24120 | 12:08:02 |
| 196 | 76.25 | 13 | 95.70046 | 12:32:45 | 11.88071 | 12:57:29 | 179.52020 | 13:46:55 |
| 197 | 92.25 | 13 | 70.97936 | 14:11:38 | 347.15962 | 14:36:22 | 154.79910 | 15:25:48 |
| 198 | 108.25 | 13 | 46.25836 | 15:50:31 | 322.43862 | 16:15:15 | 130.07810 | 17:04:41 |
| 199 | 124.25 | 13 | 21.53736 | 17:29:25 | 297.71762 | 17:54:08 | 105.35710 | 18:43:34 |
| 200 | 140.25 | 13 | 356.81636 | 19:08:18 | 272.99662 | 19:33:01 | 80.63610 | 20:22:27 |
| 201 | 156.25 | 13 | 332.09526 | 20:47:11 | 248.27551 | 21:11:54 | 55.91500 | 22:01:20 |
| 202 | 172.25 | 13 | 307.37426 | 22:26:04 | 223.55451 | 22:50:47 | 31.19400 | 23:40:13 |
| 203 | 188.25 | 14 | 282.65326 | 00:04:57 | 198.83352 | 00:29:40 | 6.47300 | 01:19:06 |
| 204 | 204.25 | 14 | 257.93216 | 01:43:50 | 174.11241 | 02:08:33 | 341.75190 | 02:58:00 |
| 205 | 220.25 | 14 | 233.21116 | 03:22:43 | 149.39141 | 03:47:26 | 317.03090 | 04:36:53 |
| 206 | 3.25 | 14 | 208.49016 | 05:01:36 | 124.67042 | 05:26:19 | 292.30990 | 06:15:46 |
| 207 | 19.25 | 14 | 183.76906 | 06:40:29 | 99.94931 | 07:05:12 | 267.58880 | 07:54:39 |
| 208 | 35.25 | 14 | 159.04806 | 08:19:22 | 75.22831 | 08:44:05 | 242.86780 | 09:33:32 |
| 209 | 51.25 | 14 | 134.32706 | 09:58:15 | 50.50732 | 10:22:58 | 218.14680 | 11:12:25 |
| 210 | 67.25 | 14 | 109.60606 | 11:37:08 | 25.78632 | 12:01:51 | 193.42580 | 12:51:18 |
| 211 | 83.25 | 14 | 84.88496 | 13:16:01 | 1.06521 | 13:40:44 | 168.70470 | 14:30:11 |
| 212 | 99.25 | 14 | 60.16396 | 14:54:54 | 336.34421 | 15:19:37 | 143.98370 | 16:09:04 |
| 213 | 115.25 | 14 | 35.44296 | 16:33:47 | 311.62321 | 16:58:30 | 119.26270 | 17:47:57 |
| 214 | 131.25 | 14 | 10.72186 | 18:12:40 | 286.90211 | 18:37:23 | 94.54160 | 19:26:50 |
| 215 | 147.25 | 14 | 346.00086 | 19:51:33 | 262.18111 | 20:16:17 | 69.82060 | 21:05:43 |
| 216 | 163.25 | 14 | 321.27986 | 21:30:26 | 237.46012 | 21:55:10 | 45.09960 | 22:44:36 |
| 217 | 179.25 | 14 | 296.55876 | 23:09:19 | 212.73901 | 23:34:03 | 20.37850 | 00:23:29 |
| 218 | 195.25 | 15 | 271.83776 | 00:48:12 | 188.01802 | 01:12:56 | 355.65750 | 02:02:22 |
| 219 | 211.25 | 15 | 247.11676 | 02:27:05 | 163.29702 | 02:51:49 | 330.93650 | 03:41:15 |
| 220 | 227.25 | 15 | 222.39576 | 04:05:58 | 138.57602 | 04:30:42 | 306.21550 | 05:20:08 |
| 221 | 10.25 | 15 | 197.67466 | 05:44:52 | 113.85491 | 06:09:35 | 281.49440 | 06:59:01 |
| 222 | 26.25 | 15 | 172.95366 | 07:23:45 | 89.13391 | 07:48:28 | 256.77340 | 08:37:54 |
| 223 | 42.25 | 15 | 148.23266 | 09:02:38 | 64.41291 | 09:27:21 | 232.05240 | 10:16:47 |
| 224 | 58.25 | 15 | 123.51156 | 10:41:31 | 39.69181 | 11:06:14 | 207.33130 | 11:55:40 |
| 225 | 74.25 | 15 | 98.79056 | 12:20:24 | 14.97081 | 12:45:07 | 182.61030 | 13:34:34 |
| 226 | 90.25 | 15 | 74.06956 | 13:59:17 | 350.24982 | 14:24:00 | 157.88930 | 15:13:27 |
| 227 | 106.25 | 15 | 49.34846 | 15:38:10 | 325.52872 | 16:02:53 | 133.16820 | 16:52:20 |
| 228 | 122.25 | 15 | 24.62746 | 17:17:03 | 300.80771 | 17:41:46 | 108.44720 | 18:31:13 |
| 229 | 138.25 | 15 | 359.90646 | 18:55:56 | 276.08672 | 19:20:39 | 83.72620 | 20:10:06 |
| 230 | 154.25 | 15 | 335.18546 | 20:34:49 | 251.36571 | 20:59:32 | 59.00520 | 21:48:59 |
| 231 | 170.25 | 15 | 310.46436 | 22:13:42 | 226.64461 | 22:38:25 | 34.28410 | 23:27:52 |
| 232 | 186.25 | 15 | 285.74336 | 23:52:35 | 201.92361 | 00:17:18 | 9.56310 | 01:06:45 |

# Footnotes

The reader is reminded that Local Mean Solar Time is not a reliable indicator of illumination conditions. The clock on the wall may say “noon” but if you are near the North pole in winter it will be pitch dark outside! A calendar date is required to determine the actual Sun angles.