Mechanical Support Department		PHG Markup – need to insert

19.d.  Background

The Mechanical Support Department provides all mechanical maintenance and engineering support for the Accelerator complex other than cryogenic needs and conventional plant utilities.

Although the Department is also tasked with maintaining and upgrading complex-wide systems (primarily low conductivity water (LCW) and vacuum systems), a large majority of its work consists of providing mechanical engineering, drafting, and technician support for the Machine Departments and Accelerator Division Projects.

19. f.  Accomplishments in FY05

The Mechanical Support Department continued its ongoing role of maintaining and upgrading the systems and devices that make up the accelerator complex. These tasks include change-out of failed accelerator components, repair/construction of spare components, LCW and vacuum system repair and maintenance, and upgrades to improve machine performance. A few highlights are listed below:

- Tevatron vacuum pipe upgrades in E-0 and D-0 with addition of

non-evaporative getter materials.

- MiniBooNE Horn was change-out and began construction of spare horn.

- Continued critical device spare production (Lithium lenses) for the P-bar 		Target Hall.

- Cleaned the Tevatron LCW heat exchangers.

- Water Quality Analysis Skids were completed and brought online at the 		Central Utilities Building.

- AP-2 Beam stop was changed-out and re-design started.

The Department also participated in many of the Accelerator Division’s Projects and R&D efforts. Some highlights of these activities included:

- Completed installation and commissioning of Electron Cooling into the 		Recycler Ring including ancillary water and SF6 gas systems.

- Stacktail stochastic cooling upgrade in P-Bar Source.

- P-Bar Source acceptance improvements, including production of diffusion 		bonded High Gradient Lithium Lenses (8 mm and Prototype 2).

- Construction of superconducting RF cavities and cryomodules in support of 		the Linear Collider and Proton Driver efforts (and SM&TF).

- Installation, commissioning and operation of the NuMI beam line and 			Target Hall including production of spare horns and target.

19.g.1.  Accomplishments Expected in FY06

The Mechanical Support Department will continue to provide engineering and technical support to the operation of the accelerator complex and target halls. Maintenance and upgrades to systems under Mechanical Support Department’s control (primarily vacuum and low conductivity water systems) will include the following:

- Continue to repair and replace failed or obsolete vacuum equipment needed 		to maintain reliability of beam-tube vacuum for the accelerator complex.

- Replace obsolete Tevatron vacuum pumping stations including shielding 			controls from beam radiation.

- Purchase replacement filaments for two-sectors worth of titanium 				sublimation pumps (TSPs) for the Main Injector.

- Install and commission the new pump room at MI-8.

- Improve the Booster LCW system.

- Add de-oxygenation systems at CUB for the Tevatron and Main Injector 			LCW systems.

- Clean Main Injector LCW heat exchangers.

Mechanical Support Department will continue providing support to efforts by the Machine Departments and Projects such as described in the previous section.

19.g.2.  Future Accomplishments Expected in FY07 and Beyond

The Mechanical Support Department will continue to provide engineering and technical support to the operation of the accelerator complex and target halls similar to our FY06 efforts. The most notable of these are:

- Continue vacuum reliability upgrades for the accelerator complex.

- Continue operations support including spare device construction and 				change-out activities for MiniBooNE, NuMI, and AP-0 Target Halls.

- Continue support for Proton Improvement Plan

- Add an electro-deionization system to CUB.

- Provide significant engineering, drafting and technician support to Linear 			Collider and Proton Driver efforts.