UNITED STATES ENVIRONMENTAL PROTECTION AGENCY

WASHINGTON, D.C.  20460

OFFICE OF PREVENTION,

PESTICIDES AND TOXIC

SUBSTANCES

April 23, 2007

DP Barcode: D339258										PC Code: 036602

MEMORANDUM

SUBJECT:	Drinking water assessment for mandipropamid and its two degradates (SYN500003, SYN504851) use on brassica vegetables, bulb vegetables, cucurbits, fruiting vegetables, grapes, leafy vegetables, potatoes, tomatoes, tuberous and corm vegetables.

TO:		Dennis McNeilly, Chemist

Registration Action Branch 2

Health Effects Division (P7509)

FROM:	Ibrahim Abdel-Saheb, Ph.D., Environmental Scientist

Environmental Risk Branch II

Environmental Fate and Effects Division

THRU:	Dana Spatz, Senior Chemist

Environmental Risk Branch II

Environmental Fate and Effects Division

Tom Bailey, Ph.D., Branch Chief

Environmental Risk Branch II

Environmental Fate and Effects Division

INTRODUCTION

This memorandum transmits the Tier I Estimated Environmental Concentrations (EECs) resulting from 4 applications of 0.13 lb ai/acre of mandipropamid and its two degradates (SYN500003 and SYN504851). HED requested to include these two degradates in this water assessment due to their high amounts formed in laboratory studies (9.4 and 38% of the applied radioactivity under aerobic aquatic conditions), and toxicological concerns.

CONCLUSIONS

A screening assessment of estimated environmental concentrations (EECs) for mandipropamid and its major aquatic degradates (SYN500003 and SYN504851) in drinking water was conducted.  Screening models were used to determine estimated concentrations in ground water and surface water.  A national PCA of 0.87 (default) was used in order to better reflect the expected exposures from the proposed uses.

Based on surface (FIRST 1.1.0) and ground water (SCI-GROW 2.3) modeling , the surface and groundwater Expected Environmental Concentrations (EEC) of mandipropamid  and its major degradates (SYN500003 and SYN504851) are shown in table 1.

| Table 1. Estimated drinking water concentrations to be used for exposure to mandipropamid and its major degradates (SYN500003, SYN504851) in drinking water derived from surface water and ground water. |
| --- |
|  | Model EEC Value (μg/L) |
|  | Mandipropamid | SYN500003 | SYN504851 | Four applications @0.13 lbai/A with 7 days interval between applications | PCA % |
| Acute | 25.2 | 2.323 | 8.993 |  | 0.87 |
| Annual average (chronic) | 1.00 | 0.381 | 5.858 |  | 0.87 |
| Groundwater | 5.22E-02 | 5.85E-01 | 1.73E | Four applications @0.13 lbai/A with 7 days interval between applications | None |

BACKGROUND

Mandipropamid is a new pesticide (also known as Revus) is the active ingredient in the fungicide

RevusTM, which is proposed for control of a certain diseases in brassica vegetables, bulb vegetables,

cucurbits, fruiting vegetables, grapes, leafy vegetables, potatoes, tomatoes, tuberous and corm

vegetables.

Groundwater and surface water monitoring data are not available to the Environmental Fate and Effects Division (EFED) for mandipropamid or its degradates (new chemical). Screening models were used to determine drinking water EECs.

SURFACE WATER

| Table 2. Selected Surface Water Exposure Inputs for FIRST 1.1.0 for Mandipropamid. |
| --- |
| MODEL INPUT VARIABLE | INPUT VALUE | COMMENTS |
| Application rate (lb ai/A) | 0.13 | EPA Reg. 100-RELU |
| Number of application | 4 | EPA Reg. 100-RELU |
| Interval between appl. (d) | 7 | EPA Reg. 100-RELU |
| Koc(mL/g) | 405.1 | MRID# 46800040-41; Lowest non-sand; Input Parameters Guidance, 2002 |
| Aerobic Soil Metabolic Half-life (days) | 81.3 (parent) | MRID# 46800020,21,22,24,25,27-28; Input Parameters Guidance, 2002 |
| Wetted in? | No | EPA Reg. 100-RELU |
| Depth of Incorporation (cm) | 0 | EPA Reg. 100-RELU |
| Method of application | Aerial | EPA Reg. 100-RELU |
| Percent cropped area | 0.87 | PCA that gives the max. EECs used; FIRST users manual. |
| Solubility (mg/L) | 2.3 | MRID# 46800007, 46800008 |
| Aerobic Aquatic Metabolic Half-life (days) | 19.3 | MRID# 46800033-34; Input Parameters Guidance, 2002 |
| Hydrolysis (pH 7) half-life (days) | 0 | MRID# 46800007, 46800008 |
| Aqt. Photolysis Half-life (days) | 1.1 | MRID# 46800014; maximum value. |

| Table 3. Selected Surface Water Exposure Inputs for FIRST 1.1.0 for mandipropamid degradate, SYN 00003. |
| --- |
| MODEL INPUT VARIABLE | INPUT VALUE | Data Source/ Comments |
| Application rate (lb ai/A) | 0.007* | EPA Reg. 100-RELU |
| Number of application | 4 | EPA Reg. 100-RELU |
| Interval between appl. (d) | 7 | EPA Reg. 100-RELU |
| Koc(mL/g) | 2.89 | MRID# 46800037; Lowest non-sand; Input Parameters Guidance, 2002 |
| Aerobic Soil Metabolic Half-life (days) | 81.3 (parent) | No data available for degradate; MRID# 46800020,21,22,24,25,27-28; Input Parameters Guidance, 2002 |
| Wetted in? | No | EPA Reg. 100-RELU |
| Depth of Incorporation (cm) | 0 | EPA Reg. 100-RELU |
| Method of application | Ground | EPA Reg. 100-RELU |
| Percent cropped area | 0.87 | PCA that gives the max. EECs used; FIRST users manual. |
| Solubility (mg/L) | 170000 | Europena Federal Office for Food Safety; Monograph prepared in the context of inclusion of following active substance in Annex I of the Council Directive 91/414/EEC (Mandipropamid), 2006. |
| Aerobic Aquatic Metabolic Half-life (days) | 58.1 | MRID# 46800029; Input Parameters Guidance, 2002 |
| Hydrolysis (pH 7) half-life (days) | 0 | No data available for degradate;MRID# 46800007, 46800008 |
| Aqt. Photolysis Half-life (days) | 0 | No data available for degradate; Input Parameters Guidance, 2002 |

*: Application rate was calculated by multiplying the parent appl. rate X maximum percent of degradate formed (i.e. 	9.4% of applied radioactivity; MRID# 46800031) X (degradate M.Wt/parent M.Wt).

| Table4. Selected Surface Water Exposure Inputs for FIRST 1.1.0 for mandipropamid degradate, SYN 504851. |
| --- |
| MODEL INPUT VARIABLE | INPUT VALUE | Data Source/ Comments |
| Application rate (lb ai/A) | 0.027* | EPA Reg. 100-RELU |
| Number of application | 4 | EPA Reg. 100-RELU |
| Interval between appl. (d) | 7 | EPA Reg. 100-RELU |
| Koc(mL/g) | 3 | MRID# 46800044; Lowest non-sand; Input Parameters Guidance, 2002 |
| Aerobic Soil Metabolic Half-life (days) | 81.3 (parent) | No data available for degradate; MRID# 46800020,21,22,24,25,27-28; Input Parameters Guidance, 2002 |
| Wetted in? | No | EPA Reg. 100-RELU |
| Depth of Incorporation (cm) | 0 | EPA Reg. 100-RELU |
| Method of application | Ground | EPA Reg. 100-RELU |
| Percent cropped area | 0.87 | PCA that gives the max. EECs used; FIRST users manual. |
| Solubility (mg/L) | 500000 | Europena Federal Office for Food Safety; Monograph prepared in the context of inclusion of following active substance in Annex I of the Council Directive 91/414/EEC (Mandipropamid), 2006. |
| Aerobic Aquatic Metabolic Half-life (days) | 1323 (441 X 3) | MRID# 46800029; single half life multiplied by 3; Input Parameters Guidance, 2002 |
| Hydrolysis (pH 7) half-life (days) | 0 | No data available for degradate; MRID# 46800007, 46800008 |
| Aqt. Photolysis Half-life (days) | 0 | No data available for degradate; Input Parameters Guidance, 2002 |

**: Application rate was calculated by multiplying the parent appl. rate X maximum percent of degradate formed 	(i.e. 38% of applied radioactivity; MRID# 46800031) X (degradate M.Wt/parent M.Wt).

GROUND WATER

The SCI-GROW model is based on scaled ground water concentration from ground water monitoring studies, environmental fate properties (aerobic soil half-lives and organic carbon partitioning coefficients-Koc 's) and application rates. The model is based on permeable soils that are vulnerable to leaching and on shallow ground water (10-30 feet). SCI-GROW version 2.3 (executable file dated 08/05/2003) was used to estimate concentrations of mandipropamid and its major degradate (SYN500003, SYN504851) that could be found in drinking water derived from ground water, using the input values listed in the table 3.

| Table 5. Ground Water Exposure Inputs for SCI-GROW for parent mandipropamid and its two degradate (SYN 00003, SYN 504851). |
| --- |
| MODEL INPUT VARIABLE | INPUT VALUE | Data Source/ Comments |
|  | Parent | SYN 00003 | SYN 504851 |  |
| Application Rate (lbs. ai/A) | 0.13 | 0.007* | 0.027* | EPA Reg. 100-RELU |
| Maximum No. of Applications | 4 | 4 | 4 | EPA Reg. 100-RELU |
| Koc | 782 | 2.92 | 5 | Median non-sand. MRID 46800038-41 (parent); 46800037 (SYN 00003), 46800044 (SYN 504851); Input parameter guidance, 2002. |
| Aerobic Soil Metabolic Half-life(days) | 75.1 (median) | 81.3 (parent) | 81.3 (parent) | No data available for degradate; MRID# 46800033-34; MRID# 46800029; Input parameter guidance, 2002. |

*: Application rate was calculated by multiplying the parent appl. rates X maximum percent of degradate formed X (degradate M.Wt/parent M.Wt).

Results from the SCI-GROW screening model predict that the maximum chronic and acute concentration of parent mandipropamid and its major degradate (SYN500003, SYN504851) in shallow ground water is not expected to exceed 4.19E+01 µg/L for the current maximum seasonal use rate.

APPENDIX I

FIRST MODEL 1.1.0 INPUT & OUTPUT FILES

RUN No.   1 FOR Mandipropamid    ON   all           * INPUT VALUES *

--------------------------------------------------------------------------------------------------------

RATE (#/AC)   No.APPS &   SOIL  SOLUBIL  APPL TYPE  %CROPPED INCORP

ONE(MULT)    INTERVAL    Koc   (PPM )   (%DRIFT)     AREA    (IN)

--------------------------------------------------------------------------------------------------------

.130(   .477)         4       7           405.1    2.3          AERIAL(16.0)  87.0    .0

FIELD AND RESERVOIR HALFLIFE VALUES (DAYS)

-----------------------------------------------------------------------------------------------------------------

METABOLIC  DAYS UNTIL  HYDROLYSIS   PHOTOLYSIS   METABOLIC  COMBINED

(FIELD)  RAIN/RUNOFF  (RESERVOIR)  (RES.-EFF)   (RESER.)   (RESER.)

-------------------------------------------------------------------------------------------------------------------

81.30        2          N/A      1.10-  136.40    19.30     16.91

UNTREATED WATER CONC (MICROGRAMS/LITER (PPB)) Ver 1.1.0 DEC 12, 2005

----------------------------------------------------------------------------------

PEAK DAY  (ACUTE)      ANNUAL AVERAGE (CHRONIC)

CONCENTRATION             CONCENTRATION

----------------------------------------------------------------------------------

  - 1.006

RUN No.   2 FOR  SYN00003         ON   all           * INPUT VALUES *

--------------------------------------------------------------------

RATE (#/AC)   No.APPS &   SOIL  SOLUBIL  APPL TYPE  %CROPPED INCORP

ONE(MULT)    INTERVAL    Koc   (PPM )   (%DRIFT)     AREA    (IN)

--------------------------------------------------------------------

.007(   .026)   4   7       2.9*******   GROUND( 6.4)  87.0    .0

FIELD AND RESERVOIR HALFLIFE VALUES (DAYS)

--------------------------------------------------------------------

METABOLIC  DAYS UNTIL  HYDROLYSIS   PHOTOLYSIS   METABOLIC  COMBINED

(FIELD)  RAIN/RUNOFF  (RESERVOIR)  (RES.-EFF)   (RESER.)   (RESER.)

--------------------------------------------------------------------

81.30        2          N/A       .00-     .00    58.10     58.10

UNTREATED WATER CONC (MICROGRAMS/LITER (PPB)) Ver 1.1.0 DEC 12, 2005

--------------------------------------------------------------------

PEAK DAY  (ACUTE)      ANNUAL AVERAGE (CHRONIC)

CONCENTRATION             CONCENTRATION

--------------------------------------------------------------------

2.323                     		  .381

RUN No.   3 FOR SYN504851        ON   all           * INPUT VALUES *

--------------------------------------------------------------------

RATE (#/AC)   No.APPS &   SOIL  SOLUBIL  APPL TYPE  %CROPPED INCORP

ONE(MULT)    INTERVAL    Koc   (PPM )   (%DRIFT)     AREA    (IN)

--------------------------------------------------------------------

.027(   .099)   4   7       3.050000.0   GROUND( 6.4)  87.0    .0

FIELD AND RESERVOIR HALFLIFE VALUES (DAYS)

--------------------------------------------------------------------

METABOLIC  DAYS UNTIL  HYDROLYSIS   PHOTOLYSIS   METABOLIC  COMBINED

(FIELD)  RAIN/RUNOFF  (RESERVOIR)  (RES.-EFF)   (RESER.)   (RESER.)

--------------------------------------------------------------------

81.30        2          N/A       .00-     .00   ******   1323.00

UNTREATED WATER CONC (MICROGRAMS/LITER (PPB)) Ver 1.1.0 DEC 12, 2005

--------------------------------------------------------------------

PEAK DAY  (ACUTE)      ANNUAL AVERAGE (CHRONIC)

CONCENTRATION             CONCENTRATION

--------------------------------------------------------------------

8.993           		           5.858

SCI-GROW MODEL 2.3 INPUT & OUTPUT FILES

SCIGROW

VERSION 2.3

ENVIRONMENTAL FATE AND EFFECTS DIVISION

OFFICE OF PESTICIDE PROGRAMS

U.S. ENVIRONMENTAL PROTECTION AGENCY

SCREENING MODEL

FOR AQUATIC PESTICIDE EXPOSURE

SciGrow version 2.3

chemical:Manidpropamid

time is  4/19/2007  16:20: 6

------------------------------------------------------------------------

Application      Number of       Total Use    Koc      Soil Aerobic

rate (lb/acre)  applications   (lb/acre/yr)  (ml/g)   metabolism (days)

------------------------------------------------------------------------

0.130           4.0           0.520      7.82E+02       75.1

------------------------------------------------------------------------

groundwater screening cond (ppb) =   5.22E-02

************************************************************************

SCIGROW

VERSION 2.3

ENVIRONMENTAL FATE AND EFFECTS DIVISION

OFFICE OF PESTICIDE PROGRAMS

U.S. ENVIRONMENTAL PROTECTION AGENCY

SCREENING MODEL

FOR AQUATIC PESTICIDE EXPOSURE

SciGrow version 2.3

chemical:SYN00003

time is  4/23/2007  15:55:32

------------------------------------------------------------------------

Application      Number of       Total Use    Koc      Soil Aerobic

rate (lb/acre)  applications   (lb/acre/yr)  (ml/g)   metabolism (days)

------------------------------------------------------------------------

0.007           4.0           0.028      2.92E+00       81.3

------------------------------------------------------------------------

groundwater screening cond (ppb) =   5.85E-01

************************************************************************

SCIGROW

VERSION 2.3

ENVIRONMENTAL FATE AND EFFECTS DIVISION

OFFICE OF PESTICIDE PROGRAMS

U.S. ENVIRONMENTAL PROTECTION AGENCY

SCREENING MODEL

FOR AQUATIC PESTICIDE EXPOSURE

SciGrow version 2.3

chemical:SYN504851

time is  4/23/2007  15:56: 6

------------------------------------------------------------------------

Application      Number of       Total Use    Koc      Soil Aerobic

rate (lb/acre)  applications   (lb/acre/yr)  (ml/g)   metabolism (days)

------------------------------------------------------------------------

0.027           4.0           0.108      5.00E+00       81.3

------------------------------------------------------------------------

groundwater screening cond (ppb) =   1.73E+00

************************************************************************