PRELIMINARY INFORMATION
PACKAGE

FOR

NSTX TF FLAG JOINT

#### DESIGN REVIEW

E. Baker, A. Brooks, J. Chrzanowski,

P. Heitzenroeder, M. Kalish, R. Marsala, C. Neumeyer,

B. Paul, H. Schneider, I. Zatz

4/3/3

Table of Contents

INTRODUCTION	3

PERFORMANCE REQUIREMENTS	7

OPERATIONAL HISTORY	9

FACTORS LEADING TO FAILURE OF ORIGINAL TF ASSEMBLY	9

Design Factors	9

Quality Factors	10

Operational Factors	10

KEY DESIGN DRIVERS	10

SUMMARY OF FORCES	12

LOAD PATHS	12

DESCRIPTION OF SELECTED DESIGN	13

COMPARISON OF OLD AND NEW DESIGNS	18

Deficiencies of Original Design	Error! Bookmark not defined.

Corrective Features of New Design	Error! Bookmark not defined.

# INTRODUCTION

The TF Inner Leg Assembly failed on 2/14/03 at the Inner Leg-to-Flag joint. The NSTX Project is now mobilizing to fabricate a new TF Inner Leg Assembly. The need for a new flag joint design is the schedule driver at present. A spare set of extruded conductor was purchased some time ago. However, the Project cannot proceed with the machining of the new inner leg conductors until an approved design is ready. Therefore the design of the new Inner Leg-To-Flag joint is the pacing item.

The Project seeks a more robust design which will not suffer from the shortcomings of the original design. Toward this end, the re-design activity must:

- factor in lessons learned from failure

- ensure that all engineering aspects analyzed at appropriate level of detail

- perform testing as necessary for engineering input and design verification

- reduce dependence on precision manufacturing/assembly

- facilitate ease of  maintenance

The purpose of the design review is to approve the design of the new joint. Design  shortcomings needing attention need to be highlighted by chits. However, an important objective is to obtain approval to release inner leg conductors for machining.

Figures 1, 2, and 3 depict the main elements of the joint and serve to identify the nomenclature. The scope of this review is limited to the following elements:

- Inner Leg / Flag Interface

- Flag

- Flag Fasteners (threaded inserts, studs, washers, nuts, etc.)

- Hub Assembly/Torque Collar

Other improvements may be discussed but are out of scope.

Figure 1 – TF Coil System

Figure 2 – Elements Related to TF Inner Leg –to- Flag Joint

Figure 3 – Joint Fasteners

As shown in Figure 4, recovery activites have led to the development of a plan which consists of three main thrusts:

- Design (drawing) development

- Detailed Finite Element Analysis

- Testing

Figure 4 – Joint Development Plan

The testing is subdivided into “component” tests and “prototype” tests. The component tests are designed to provide information necessary for the engineering design. The prototype tests are designed to confirm the design. Ideally, all testing would be complete prior to design review. However, due to the schedule constraint this will not be possible.

Component testing consists of:

- Pull-out tests on threaded inserts (one time and 50,000 cycle)

- Friction coefficient and electrical resistance tests for silver plated copper

- Shear tests on simulated torque collar attachment

- Tensile tests on e-beam welded joints

Original NSTX R&D provides other essential information such as contact resistance vs. pressure.

Prototype testing consists of:

- Mechanical mock-up tested for 50,000 cycles

- Electrical mock-up tested at full current and I2T

Since some of the testing will follow after the design review, and since chit resolution will also follow, another checkpoint is identified in the plan which will ensure that all design issues have been closed out. The exact form has not been decided upon yet, but it could be, e.g., the PPPL Activity Certification Committee.

# PERFORMANCE REQUIREMENTS

The base GRD requirement is for Bt=3kG at R0=0.854m with 4.5 sec flat top, corresponding to 35580 Amp with the 36 turn coil. There is also a “high field” GRD requirement for 6kG at R0=0.854m with 0.6 sec flat top, corresponding to 71160 Amp with the 36 turn coil. Waveforms are shown in Figure 5.

Figure 5 – Current Waveforms

(Shot 108712 was an actual 6kG Test Shot)

Allowing for the possibility of a power supply fault at the end of flat top from full current, the I2T requirements imposed by the waveforms are of order 6.0 x 109 A2-sec. However the coil design anticipates a maximum of 6.5 x 109 A2-sec, corresponding to an 80oC rise in the main conductor.

The 6kG pulse is the design driver, not only because the forces are 4x higher than at 3kG, but also because of the short duration of the 6kG pulse, where minimal time is available for heat diffusion. This is the most severe condition in terms of peak local temperature rise at the joint. Figure 6 shows the result of a finite element analysis (of the original joint design) which shows how the temperature distribution tends to peak at the corner of the joint, where the current bunches up. Simulations have shown that this current bunching effect is due primarily to resistive effects, and that inductive effects are not significant.

Figure 6 – Temperature Distribution

The TF system is driven by a 1kV power supply, so the voltage is of order 30V/turn. However, the TF conductor faces structure which can be biased to 1kV during Coaxial Helicity Injection (CHI) operations, so the groundwall insulation needs to anticipate 2kV. Thus the hipot requirement is 2E+1=5kV.

# OPERATIONAL HISTORY

Approximately 7200 shots were executed with the original TF Inner Leg Assembly prior to failure. A spectrum is shown if Figure 7. The test shots, performed at 50% and 100% of the operating envelope in effect, are evident, along with the plasma shots which comprise the vast majority.

Figure 7 – TF Operational History

It is noted that the early shots were mainly at 3kG, and that most of the machine operations have been conducted at 4.5kG. The number of 6kG shots was quite limited. In this context it is noted that the forces present during the 3kG and 4.5kG shots are 25% and 50%, respectively, of those at 6kG.

# FAILURE OF ORIGINAL TF ASSEMBLY

On February 14, 2003, following our morning test shots, the first plasma attempt of the day resulted in a loud bang (heard on thecontrol room audio monitors) accompanied by a plume of smoke (visible on the control room video monitors). Waveforms of the prior 100% test shot and the failed shot are shown superimposed in Figure 8.

Figure 7 – TF Operational History

The target flat top level was 53.4kA which produces Bt=4.5kG. The fault occurred just prior to flat top as the current passed 50kA.Several protective devices tripped:

- TF power supply fault detector section overcurrent

- TF Analog Coil Protection (ACP) overcurrent

- TF Rochester Instrument System (RIS) overcurrent

- TF ground fault current relay

Initial inspection revealed that one of the TF “flags” had been displaced radially by about 1 inch as shown in Figure 8. Subsequent inspection revealed the extent of the damage as shown in Figure 9.

Figure 8 – Radially Displaced Flag

Figure 9 – Peak Damage Area

Analysis of the electrical signals led to the following postulated fault scenario:

- An open circuit fault (the flag joint opening up) led to turn-to-turn (inner and outer legs) and turn-to-ground faults (to the hub and umbrella assemblies) at or near the high-voltage terminals of the TF circuit.

- This fault condition led to a spike of fault current from the power supply which shunted the coil inner/outer leg assembly.

- Once the power supply tripped, the current spike decayed.

- This was followed by an L/R decay of the coil current as the coil released its stored energy. The L/R decay can be modeled by an arc with V=125V and R=500µΩ.

- The energy dissipated in the arc was of order 1.4MJ.

A combination of factors are thought to have led to the failure as follows.

## Design Factors

- hub stiffness not adequate to react moment

- imprecise shimming, poor communication of load from flag to hub

- bolt thread and shoulder engagement too small

- bolts necked down too far at threads, not enough on shaft

- dual shear/preload function of bolts

- split flag aggravating current density peaking

- lack of feature to facilitate joint resistance measurement without disassembly

## Quality Factors

- frequent manual reworking of contact surfaces

- non-planar flag surfaces

- shoulder bolt concentricity

## Operational Factors

- monitoring of joint integrity too infrequent, too imprecise

All of the above factors have been addressed in the new design.

# KEY DESIGN DRIVERS

Electrical contact resistance vs. pressure behavior is the key design driver. The contact pressure requirement drives the structural design, and the contact resistance determines heating and limits flat top time. The performance range is bracketed by two extremes, namely 1) an ordinary Cu-Cu joint, and 2) a high quality silver plated joint (as tested during NSTX R&D). Prior in-situ measurements hint at what is achievable, and future measurements will ultimately establish the operating envelope.

The design basis information is summarized in Figure 8.

Figure 8 – Contact Resistance Data

As shown in Figure 9 (from original design, assuming constant contact resistance across the joint) the contact resistance and temperature allowable will essentially dictate the realizable system performance in terms of flat top time.

##### Figure 9 –Effect of Contact Resistance on Temperature

The following design guidelines have been established:

- Structural systems shall maintain 1ksi minimum contact pressure across joint

- Performance range is assumed bracketed by two extremes...

• ordinary Cu-Cu joint: R=10000*P1.04

(4/in2@ 2ksi/in2@ 1ksi

• high quality silver plated joints: 1/in2@ P ≥ 1ksi

-   Peak local temperatures to be limited to 120oC

Future measurements will provide more data and ultimately establish the operating envelope. Improved procedures (surface prep, silver plating), quality control and maintenance can improve situation.

# SUMMARY OF FORCES

The in-plane EM forces on the flags and links (contribution out to half-way through flex link) at 6kG (71.2kA/turn) are given in the following table.

Summary of Forces and Moments at 6kG

|  | Fvertical (lbs) | dR from point of application to flag inboard edge (in) | Moment w.r.t. point X (in-lbs) |
| --- | --- | --- | --- |
| Inner Tier Flag | 7380 | 4.3 | 31719 |
| Inner Tier Link | 1855 | 13.8 | 25652 |
| Outer Tier Flag | 1845 | 4.3 | 7930 |
| Outer Tier Link | 464 | 13.8 | 6413 |
| Total from All Turns | 249324 |  |  |

Clearly the forces on the inner tier (associated with the 24 turn outer layer) are much higher than the outer tier.

# LOAD PATHS

A simplified diagram of the in-plane force application and the elements available to react the load is given in Figure 10.

Figure 10 – Load Paths

The three primary load paths are 1) the hub, 2) the bolted joint, and 3) the torque collar attachment. At the bolted joint, contact pressure results in friction which takes part of the shear load. In addition, shear keys or the bolts themselves can be used to take part of the load. At the torque collar, a maximum torsional load of 22480 lbf will add to any additional vertical load from the hub.

Sharing of the vertical forces and the moments amongst these three paths, and establishing their ability to react same while maintaining adequate contact pressure along the joint, is the essential design problem.

It is noted that thermal displacements result in additional forces. The two significant effects are as follows:

- Vertical length of inner leg from torque collar to top of flag increases due to inner leg temperature rise (T ≤80oC) during a pulse, whereas flag and hub remain relatively cool

- Radial length of flag increases modestly during a pulse (T ~ 5oC) but can ratchet by as much as T ≤25oC with rated I2T pulsing at 300 second rep rate.

# DESCRIPTION OF NEW DESIGN

The ideal design would have the following attributes:

- Perfect communication of load through insulation/shimming/potting to hub

- Infinitely stiff hub

- Full vertical load shear capability at the inner leg/flat interface

- Contact pressure everywhere along the joint ≥ minimum allowable over the full temperature range

These design goals guide in the selection and sizing of the various design features and dimensions.

Several views of the new design are given in Figures 11-15. The following are some highlights of the design features:

- Solid flags (no split) are insulated with two half-lapped layers of Kapton, then glass tape wrapped and potted (Hysol RE2039 & HD3561) in SS boxes which are bolted to the hub disks. Communication of in-plane and out-of-plane forces from flag to hub is very efficient.

- Boxes bolted to hub disks form very stiff “I-beam” type hub structure.

- Mold release agent is used so that potting is not bonded to the box, thereby  allowing for thermal displacement of the flag.

- Potting is accomplished “in place” with boxes flags already installed and tightened so as to ensure best possible contact surface fit. However, potted flag-boxes can be removed as necessary when sliding TF Inner Leg Assembly into OH Coil Tension Tube

- Flags are attached to inner legs using 3/8” dia. A286 SS studs screwed into threaded inserts. Washer plate is used under tee at end of flag. Belleville washer and nut then complete the attachment.

- Studs necked down over their length to enhance elasticity.

- Upper 24 outer layer, lower tier flags are e-beam welded, joint at end of flag. Number of high performance joints is reduced from 72 to 48.

- Shear shoe/key located on outer edge of flags (except e-beam welded flags).

- Voltage taps positioned on flag, routed across joint then twisted around water tube, allowing in-situ joint resistance measurements without breaking outer flag joints.

Figure 11 – Unfolded View of New Design

Figure 12 – Isometric View of New Design

Figure 13 – Section View of New Design

##### Figure 14 – Details of New Design, Top End of Machine

Figure 15 – Details of New Design,  Bottom End of Machine

# COMPARISON OF OLD AND NEW DESIGNS

Features of the old and new designs are compared in the following table.

|  | Old Design | New Design |
| --- | --- | --- |
| Hub Stiffness | Not adequate; lacking stiff linkages between disks because flags could slide w.r.t. disks | Very stiff. Boxes form webs with disks like I-beams. |
| Bolts/Studs | Shoulder engagement was too small (4 bolts x 0.1 depth = .4 @ 1/2" dia, Area = 0.18 in^2) | Shear pin (0.688" @ 1/2" dia, Area = 0.344 in^2) |
|  | Bolt 5/16” thread was necked down too far to 0.232" | Studs necked down to root dia of 3/8" bolt = 0.314" |
|  | 0.438” shank diameter was too large, bolt was not compliant for thermal cycling | Neck down to root dia of 3/8" bolt = 0.314" |
|  | No back-up to bolt compliance to accomodate creep | Belleville washer, initially flattened |
|  | Torsion in long bolts during tightening | Studs with nuts used in place of long bolts |
|  | Dual purpose bolts, combined tension and shear functions, tolerance issues, torque(tension) uncertainty | Loose fitting clearance holes for studs, separate shear keys |
|  | Four 5/16" bolts @ 2500#, marginal friction to carry shear (4*2500=10000lbf applied vs. 9230lbs, requires mu ~1.0) | Four 3/8" studs @ 5000#, doubling of preload (4*5000=20000lbf) |
|  | Thin washers under bolt heads at tee-ends | 1/4" thick washer plate under Belleville washers at tee-ends |
| Inserts | Keensert type, thread engagement = 0.113" | Taplok type, thread engagement > 0.5" |
| Shimming | Manually selected and inserted G10 shim stock | Hysol/glass tape potting in boxes, mold released to permit thermal growth |
| Out-of-Plane Load Path | Wedged G10 blocks with pusher bolts | Flags potted in boxes, boxes bolted to hub disks |