Active Final Approach Spacing Tool (AFAST)

# General Description

January 31, 2002

# NAS2-98005

# Technical Research in Advanced Air Transportation Technologies

Final

General Description

Active Final Approach Spacing Tool (aFAST)

CDRL Item 5e

# Prepared under

# RTO - 62

# AATT Operational Concept for ATM – Year 2002 Update

#### January 31, 2002

#### Prepared For:  NASA Ames Research Center

#### Moffett Field, CA 94035-1000

#### Prepared By:  Titan Systems Corporation – SRC Division

#### Billerica, MA 01821-4134

ACKNOWLEDGEMENT

The majority of the descriptions presented in this document have been taken directly from NASA documents shown in the bibliography. Minor modifications have been made to the text to provide readability.  The aFAST Flow chart has however been independently developed for this description.   This approach to the development of this document was taken in order to remain faithful to the efforts that are presently being undertaken by the NASA AATT Project Office, the aFAST Tool Developers and the associated NASA AATT contractors.

Table of Contents

- Description	1

- Operational Concept	4

- Functional Flow	9

# List of Figures

- aFAST System Overview	4

- PGUI for DFW Arrivals	6

- Speed Advisory Using Color	7

- Heading Advisory Using Color	8

- Combined Speed and Heading Advisory Using Color	9

- Trajectory Quick Look Using Color	10

- aFAST Functional Flow	11

- aFAST Software Architecture	13

# Appendicies

### Bibliography

## AATT ACTIVE FINAL APPROACH SPACING TOOL (aFAST)

## GENERAL DESCRIPTION

1.  DESCRIPTION

Purpose

- Help terminal area controllers optimize traffic flow to runways to minimize delay and increase throughput.

- Compute an efficient landing sequence, approach spacing and runway assignment for arrival aircraft.

Users

- Terminal area air traffic controllers

- Terminal area traffic management coordinators (TMCs)

Operational Results

- In operational testing at DFW,  passive FAST increased landing rates by 9-13%.

- The FAA estimates that passive FAST saves airlines US$10 million per year at DFW.

- aFAST is not operational  however benefits analysis indicates a potential savings of over $300 M/year for 10 major airports (see #35 Bibliography).

Overview

The Final Approach Spacing Tool (FAST) is a decision support tool for terminal area (TRACON) air traffic controllers. The TRACON typically encompasses the airspace within approximately 40 miles of a major airport. TRACON air traffic controllers manage arrival aircraft which enter their airspace from adjacent ATC facilities or internal airports. The controllers are responsible for assigning an appropriate runway and landing sequence to each aircraft and maintaining safe separation.

FAST assists air traffic controllers by providing its advisory information on the radar planview displays. Additionally, FAST assists traffic management coordinators by providing schedule information on auxiliary timeline displays.

Early in the development of FAST, its functionality was divided into two parts: Passive and Active. Passive advisories consist of runway assignments and landing sequences to increase the efficiency of runway usage. Active advisories consist of turn and speed commands to increase the precision of final approach spacing.

In general, arrival aircraft are vectored from en-route airspace into terminal airspace over metering fixes. Aircraft are assigned to a default runway, which is typically the closest runway to their respective metering fix. A controller occasionally reassigns aircraft to alternate runways to reduce delay on a particular runway or to balance delay and aircraft among multiple runways. Ideally, a controller would prefer to finalize an aircraft's runway assignment as early as possible (i.e. near the metering fix), but uncertainties in the traffic situation often require later reassignments.

The strength of an automation system such as FAST is its ability to assign runways based upon accurate estimations of delay savings and workload benefits early in the arrival process. The FAST runway allocation algorithm attempts to meet four primary objectives: making an early and accurate decision, reducing overall system delay, increasing overall system throughput and reducing controller workload.

During each scheduling cycle, FAST builds a trajectory for each aircraft from its current position to the runway threshold. The FAST sequencing algorithm uses these trajectories to systematically order aircraft on common trajectory paths and to merge aircraft on different trajectory paths. Fuzzy reasoning is used to model the controllers' cognitive processes related to determining an efficient landing sequence.

Using the relative sequences of aircraft on each trajectory path, FAST performs conflict prediction and resolution in order to achieve a conflict-free arrival plan. The criteria considered during conflict prediction are wake vortex minimum separation, custom runway specific separation and custom flight-specific separation. When a conflict is predicted, it is resolved by adding delay to the aircraft's trajectories in the form of vectoring and speed control.

Future Research

While the current concept for aFAST is focused on generating speed and heading advisories, consideration is also being given to adding altitude advisories.  There are numerous instances where altitude is a critical component of the arrival controllers overall plan.  However, adding altitude advisories to aFAST sequencing increases complexity, requiring very accurate altitude information.  Because very accurate altitude information would be a requirement, potential research may be dependent upon receiving direct altitude updates from the aircraft FMS via Datalink.

The integration of FMS and CTAS information exchanged via Datalink has been a topic of consideration for many years.  Aircraft equipage has been a stumbling block, but there are other complicating human factors issues surrounding the integration of FMS and the use of Datalink for aFAST advisories.

Dynamic spacing is a candidate for aFAST related research.  In the current operational environment, the minimum separation allowed behind aircraft is static, and set by the FAA.  Controllers comply with a structured matrix defined in the 7110.65 (e.g. 4 miles for a heavy jet following a heavy jet).  This matrix is based upon the “worst case scenario” for wake turbulence.  It has been postulated that in many instances, these wake turbulence minimums can be safely reduced.  In order to reduce separation, controllers would need a tool like aFAST to assist them in dynamically spacing the arrivals.  The feasibility of this concept is another area for aFAST research.

Another area where aFAST may provide potential benefits is in the environmental impact arena.  Nominal routes avoiding noise-sensitive areas can be incorporated into aFAST.  The possibility of dynamically altering routes based on conditions (e.g. time of day or weather conditions) is a potential area of research.

Finally, there are numerous integration issues to be explored between aFAST and surface automation. Active FAST can provide a surface automation tool with the specific gaps between arrivals allowing for better departure queue management.  Surface automation tools can provide aFAST with surface conditions allowing for a negotiation between the two systems.

A research plan has been established which will address preliminary human factors issues such as use of color, information format, and timing of advisories.  Human factors research will continue, as the algorithms are refined.  Algorithms must first be validated in closed-loop simulations.  This will ensure that the system will calculate optimized conflict free trajectories.  In addition, controller-in-the-loop simulations must be conducted to validate accuracy and stability of advisory information, usability, suitability, and controller acceptance of advisory presentation.  These simulations will be conducted initially at NASA-Ames, but will eventually transition to the FAA Technical Center.  Field-testing is also essential to the development of aFAST.  The current plan calls for conducting the field test activities at DFW TRACON.  It is anticipated that there will be color workstations available at TRACON arrival positions prior to the onset of field evaluations.

2.  OPERATIONAL CONCEPT

Active FAST is designed to deal with the complexities of inter-arrival spacing within the TRACON (particularly on the final approach path).  Active FAST generates “control instruction” level advisories whereby controllers issue specific speed and heading instructions based upon the advisories.  Advisories will be displayed to controllers via their standard terminal color displays.  Dedicated aFAST displays will be provided for TMCs in the ARTCC and TRACON.  These displays will be used for strategic planning.  Displays will also be available for ATCSs in the Tower.  The Tower displays will provide enhanced situational awareness.

As arrivals enter the TRACON, they are assigned a runway and sequence number.  Active FAST builds a plan for these arrivals based on aircraft performance characteristics, airspace constraints, and separation requirements.  A trajectory for each aircraft is created and adjusted based on real time radar updates.  These trajectory calculations include identification of when and where each aircraft should receive speed adjustments or headings.  These speeds and headings will eventually be able to be incorporated into future technologies such as Datalink.  However, in the near term operational environment, these advisories will be displayed in logical increments (e.g. speeds of 210 knots and 180 knots, headings in 10 degree increments) to the TRACON arrival controller so that they can be issued as control instructions.  Active FAST continues to monitor and update the plan based upon radar track updates.  The plan is modified when necessary, and ultimately leads to an optimized delivery of aircraft to the runway threshold.

The primary users of the aFAST advisories are the TRACON arrival controllers.  However, many other users can benefit from the information.  Other controllers within the TRACON can view the aFAST advisories to better understand the arrival controller’s plan (e.g. a departure controller may want to know whether or not an arrival may be instructed to slow down or turn).  TMCs in the TRACON can use the aFAST information to make dynamic runway changes for aircraft near the TRACON boundary.  The information displayed on the Planview Graphical User Interface (PGUI) can also help the TMCs in the TRACON and ARTCC better understand the traffic situation inside the TRACON.  Controllers in the ATCT can also benefit from the PGUI by observing where gaps will occur in the arrival stream (for runway crossings or departure slots).

Other potential users of the aFAST information are in the Ramp Tower and the Airline Operations Centers.  For example, the Ramp Tower can use the information to accurately determine when an aircraft will be on the ground, and thus need a gate.  The Airline Operations Center may also benefit from aFAST information, since it is more accurate than their current source of information.  It has been shown that CTAS information sharing with airline operations control centers leads to an improvement in airline operational planning.  The applications of Ramp Tower and Airline Operations Center usage are potential research areas.

Figure 1	aFAST System Overview

As shown in Figure 1, the aFAST system uses aircraft flight plans and position data from FAA computers, inputs from TRACON arrival controllers and traffic managers, and current weather information, to produce advisories to assist controllers in managing and controlling arrival traffic. The weather information is provided either by the Rapid Update Cycle (RUC), or by the Integrated Terminal Weather System (ITWS).  RUC provides a weather forecast every 3 hours (80 km grid).  ITWS provides a weather forecast every 5 minutes (2 km grid).

TRACON arrival controllers interact with aFAST, both receiving advisories and providing inputs, through standard FAA hardware. The aFAST advisories will be displayed to TRACON controllers on FAA TRACON display systems. Controller inputs will be made through message entry devices.  Traffic managers interact with aFAST through dedicated aFAST displays.  They provide inputs such as runway spacing requirements, airport configuration, and airport acceptance rates.  Traffic managers in both the ARTCC and TRACON may monitor aFAST timelines to gain a more accurate picture of the real-time operation in the TRACON.

In the current operational environment, there is only a minimal set of automation tools to assist air traffic controllers.   The most advanced automation for controllers includes the Display System Replacement (DSR) in the ARTCCs and Full Digital ARTS Displays (FDADs) in the TRACONs (though the majority of TRACONs have even earlier generation displays).  These displays are monochrome, and have very limited capabilities.  As a result, controllers are forced to rely primarily on their mental skills to solve the complex problems presented to them.  While controllers have always done an excellent job managing these complexities, some situations are beyond the scope of their informational awareness.  Aircraft performance characteristics and wind speed/direction are two areas where controllers often lack accurate information.  Active FAST’s ability to integrate such information into its trajectory predictions suggests that it may be a valuable resource to controllers in such situations.

The principal techniques that controllers use for sequencing and spacing aircraft in the TRACON are speed, heading, and altitude instructions.  If aircraft are on a straight route segment, speed is the primary degree of freedom.  On curved approaches and base turns heading is the primary degree of freedom.  On merging routes, altitude is the primary degree of freedom.

Although much of the CHI requirements definition for aFAST is still being investigated, it will build upon research that was conducted during the development of the pFAST.  As in pFAST, advisory information will be displayed in the full data blocks.  Additional symbology will be drawn on the display at the position where the turn or speed reduction should occur.  It is likely that color will be used either for the advisory, the advisory position indicator, or both.

Once the usability and acceptability of aFAST advisories have been assessed in simulation, the operational implications must be addressed in high fidelity simulation and limited operational testing.  Since the advisories may be displayed to controllers in both the feeder and final sectors, the procedures required for coordinating the handoff of an aircraft with an active advisory must be addressed.

Figure 2 is a graphical representation of aircraft inbound to DFW Airport.  The Full Data Blocks (FDBs) for these aircraft include the Aircraft Identification (e.g. AAL 467), runway assigned (e.g. 18R), aircraft type (e.g. MD80), sequence number to the runway (e.g. 4).  In some cases, aFAST advisories for heading and speed (EGF 824 has a heading advisory of 090 and a speed advisory of 190) are also displayed.  The letters associated with the FDBs (e.g. the H associated with AAL 467) indicate the controlling position within the TRACON.  The controller responsible for the final approach course to Runway 18R uses an “H” symbol.

The underlying white video map shows the airport layout for DFW, as well as numerous airports, navigation aids, and airspace boundaries.  The timelines to the left of the display show aircraft inbound to 3 different runways.  These timelines show when specific aircraft are estimated (left side of the timeline) and scheduled (right side of the timeline) at each selected runway.  The aircraft are color-coded indicating which gate the aircraft entered the TRACON.  The TMCs in the TRACON and Tower can use these timelines to determine runway loading and gaps in the arrival stream.

Figure 2 	PGUI for DFW Arrivals

Figure 3	Speed Advisory Using Color

Figure 3 illustrates an aFAST-generated speed advisory using color.  Active FAST has generated a speed advisory of 190 knots for ASE 243.  This is denoted by the orange “190” in the third visible line of the FDB of ASE 243.  The orange dot identifies the location where the advisory needs to be issued by the controller to the pilot.  This speed of 190 knots will assist the controller in spacing ASE 243 behind EGF 695.  This speed will synchronize the arrival stream.  However, as soon as AAL 1109 begins to further reduce to the final approach speed, EGF 695 and subsequently ASE 243 will also need additional speed reductions.

Figure4	Heading Advisory Using Color

Figure 4 illustrates an aFAST-generated heading advisory using color. This figure shows a base turn heading advisory of 100 degrees for ASE 243.  This is denoted by the cyan “H100” in the third visible line of the FDB of ASE 243.  Heading advisory information timeshares with the sequence number advisory information.  The cyan diamond identifies the location where the advisory needs to be issued by the controller to the pilot.  This heading of 100 degrees will assist the controller in spacing ASE 243 precisely behind EGF 695.

Figure5	Combined Speed and Heading Advisories Using Color

In any busy air traffic control environment, workload and frequency congestion are primary considerations.  It is often necessary for controllers to issue both speed and heading control instructions in close proximity to one another.  It is desirable to combine transmissions in order to reduce workload and frequency congestion.  Human factors research will be conducted to determine when controllers issue combined advisories vs. independent advisories.  A different type of symbol, representing a combined advisory may be incorporated into the symbology if necessary.

Figure 5  illustrates aFAST-generated speed and heading advisories using color.  Active FAST has generated a speed advisory of 190 knots for ASE 243.  This is denoted by the orange “190” in the third visible line of the FDB of ASE 243.  The orange dot identifies the location where the advisory needs to be issued by the controller to the pilot.  This speed of 190 knots will assist the controller in spacing ASE 243 precisely behind EGF 695.  This speed will synchronize the arrival stream.  Active FAST has also generated a base turn heading advisory of 100 degrees for ASE 243.  This is denoted by the cyan “H100” in the third visible line of the FDB of ASE 243.  The cyan diamond identifies the location where the advisory needs to be issued by the controller to the pilot.  This heading of 100 degrees will also assist the controller in spacing ASE 243 precisely behind EGF 695.  Since these two advisories are in close proximity, it is assumed that the controller will issue both during the same transmission.

Figure 6	Trajectory Quicklook Using Color

In order to generate advisories, aFAST calculates the trajectories of each arrival aircraft.  A byproduct of this calculation is that these trajectories can be displayed to the controllers.  In order to help formulate a plan of action, the controller may choose to see what routes and speeds are being calculated by aFAST.

Figure 6 illustrates a trajectory being displayed for AAL 1808.  The route in white shows the aFAST-calculated two-dimensional path.  The orange advisories along the path (S210 and S190) indicate where the speed instructions should be issued.  The cyan advisories along the path (H360 and H090) indicate where the heading instructions should be issued.  This trajectory may change as the data on this aircraft and other aircraft are updated via radar.  Once advisories are displayed, they are “frozen” and cannot be changed.   However, non-displayed advisory points can be varied.

- FUNCTIONAL FLOW

Figure 7   illustrates the detailed functional flow of  aFAST operating in the TRACON and depicts the functional interfaces with external data sources.  The input/output sources, appearing in double boxes, are shown in the figure.  The major functions within aFAST are:

- Data Acquisition and Processing

- Data Formatting  and Distribution

- Trajectory Generation

- Arrival Planning

- Advisory Generation

- Conflict Detection

- Display Message Processing

The narrative contained in the following section provides adequate description for the aFAST functional flow (see Figure 7 ) and for the aFAST Software architecture (see Figure 8 ).

Figure 7  aFAST Functional Flow

The external interfaces required for aFAST include:

- Host Computer System - To receive flight data and radar tracks from the ARTCC's HCS via an interface device.

- Terminal Automation System – To receive flight data, radar tracks, and controller entries from the Terminal Automation System via an interface device.  This includes interfacing with the terminal color display hardware.

The additional external interfaces that are preferred for aFAST include:

- Integrated Terminal Weather System (ITWS) - To receive low altitude wind and storm motion data from ITWS via an interface device.

- Surface Decision Support Tools – To exchange information with surface decision support tools in order to optimize the queuing of departures.

- Other atmospheric data - To receive high altitude wind, temperature, and air pressure data as a function of position and altitude.

The aFAST system is divided into nine software modules: the Input Source Manager (ISM), the Communications Manager (CM), the Weather Data Acquisition Daemon (WDAD), the Weather Data Processing Daemon (WDPD), the Route Analyzer (RA), the Profile Selector Active (PFSA), the Trajectory Synthesizer (TS), the Timeline Graphical User Interface (TGUI), and the PGUI.  The ISM controls the flow of information from all external ATC data sources, specifically the en-route Host Computer System (HCS) and the Automated Radar Terminal System (ARTS) computers.  The CM controls the flow of information between the aFAST modules and manages system start-up and shutdown procedures.  The WDAD and WDPD retrieve and process weather information for both ARTCC and TRACON airspace.  Weather information provided by RUC is sufficient for scheduling aircraft.  However, for tactical advisories such as aFAST, higher resolution wind information is required.  ITWS provides an appropriate resolution of weather information.  The RA generates and analyzes predicted possible routes for each aircraft involved in the scheduling process.  The TS computes predicted 4D trajectories by combining these aircraft routes, the current weather information, and the aircraft’s performance model. The RA, in conjunction with the TS, produces 4D trajectories and ETAs spanning a range of possible paths for each aircraft.  From this set of possible flight paths for each aircraft, the PFSA generates an efficient conflict-free schedule and the corresponding advisories required to meet this schedule.  The PGUI provides the TRACON traffic managers with a comprehensive view of the traffic control information being generated by aFAST and being displayed to the TRACON controllers.  Similarly, the TGUI provides the TRACON traffic managers with the means to impose traffic management constraints on the system, based on aFAST-generated information.

The PFSA module is the most significant difference between aFAST and pFAST.  In pFAST, there is a similar profile selector module (PFS).  However, PFS does not guarantee “conflict-free” trajectories.  Passive FAST schedules aircraft such that an efficient flow of traffic is balanced between the adapted runways.  In doing this, pFAST attempts to ensure a conflict-free trajectory.  In rare cases where the most efficient plan has unresolved conflicts, pFAST will not attempt to recalculate a new conflict-free plan.  It is assumed that controllers will be able to resolve individual conflicts by using speed, heading, and altitude instructions.  Active FAST is more tactical than pFAST.  Since speed and heading advisories are generated, safety requires that these advisories be conflict free (in order to validate this, Active FAST must be able to perform efficiently and conflict-free in a closed loop environment). In addition, the selected software architecture allows all aircraft trajectories and schedules to be updated within the radar update cycle.

Figure 8	aFAST Software Architecture

APPENDIX A:  BIBLIOGRAPHY

- National Aeronautics and Space Administration; Decision Support Tools of the Advanced Air Transportation Technologies Project; May 2000

- Federal Aviation Administration, US Department of Transportation, Washington DC; National Airspace System Architecture Version 4.0; January 1999

- National Aeronautics and Space Administration, Ames Research Center; CTAS - Final Approach Spacing Tool (FAST);  July 2000      http://ctas.arc.nasa.gov/project_description/fast.html

- National Aeronautics and Space Administration, Ames Research Center; Center TRACON Automation System – FAST Fact Sheet; April 2000

- Robinson III, J. E., D. R. Isaacson; A Concurrent Sequencing, and Deconfliction Algorithm for Terminal Area Air Traffic Control; AIAA Guidance, Navigation, and Control Conference, Denver, CO; August 2000

- Quinn, C., J. E. Robinson III; A Human Factors Evaluation of Active Final Approach Spacing Tool Concepts; 3rd USA/Europe Air Traffic Management R&D Seminar, Napoli, Italy; June 2000

- Mueller, K. T., J. E. Robinson III; Final Approach Spacing Tool (FAST) Velocity Accuracy Performance Analysis, AIAA Guidance, Navigation, and Control Conference, Boston, MA; August 1998

- Robinson III, J. E., T. J. Davis, and D. R. Isaacson; Fuzzy Reasoning-Based Sequencing of Arrival Aircraft in the Terminal Area; AIAA Guidance, Navigation and Control Conference, New Orleans, LA; August 1997

- Lee, K. K. and T. J. Davis; The Development of the Final Approach Spacing Tool(FAST): A Cooperative Controller-Engineer Design Approach; Journal of Control Engineering Practice, Vol. 4, No. 8, pp. 1161-1168; August 1996

- Lee, K. K., and T.J. Davis; The Development of the Final Approach Spacing Tool (FAST): A Cooperative Controller-Engineer Design Approach, NASA TM 110359; August 1995 and Proceedings the Fifth IFAC Symposium on Automated Systems Based on Human Skill; September 1995

- Krzeczowski, K.J., T.J.Davis, H.Erzberger, I. Lev-Ram, and C.P. Bergh; Knowledge-Based Scheduling of Arrival Aircraft in the Terminal Area; Proceedings of the AIAA Guidance, Navigation, and Control Conference, Paper No. AIAA-95-3366, Baltimore, MD; August 1995

- Slattery, R.A.; Terminal Area Trajectory Synthesis for Air Traffic Control Automation; submitted to the American Control Conference; June 1995

- Bergh, C.P., K.J. Krzeczowski, and T.J. Davis; TRACON Aircraft Arrival Planning and Optimization through Spatial Constraint Satisfaction; Air Traffic Control Quarterly, Vol. 3, No. 2; 1995

- Davis, T.J., K.J. Krzeczowski, and C. Bergh; The Final Approach Spacing Tool; IFAC Thirteenth Symposium on Automatic Control in Aerospace, Palo Alto, CA; September 1994

- Credeur, L., W.R. Capron, G.W. Lohr, D.J. Crawford, D.A. Tang, and W.G. Rodgers, Jr.; A Comparison of Final Approach Spacing Aids for Terminal ATC Automation; Air Traffic Control Quarterly, Vol. 1(2) 135-178; 1993

- Davis, T.J., H. Erzberger, S.M. Green, and W. Nedell; Design and Evaluation of an Air Traffic Control Final Approach Spacing Tool; Journal of Guidance, Control and Dynamics, Vol. 14, No. 4; July/August 1991

- NASA: Beyond Free Flight Phase 1 Tools; NASA Office of Aero-Space Technology

- Smith, Colin, National Air Traffic Services Ltd, England; FINAL APPROACH SPACING TOOL; December 1998

- Credeur, L., W.R. Capron, G.W. Lohr, D.J. Crawford, D.A. Tang, and W.G. Rodgers, Jr.; Final-Approach Spacing Aids (FASA) Evaluation for Terminal-Area, Time-Based Air Traffic Control; NASA Technical Paper 3399; December 1993

- Davis, T.J., H. Erzberger, and S.M. Green; Simulator Evaluation of the Final Approach Spacing Tool; American Control Conference; San Diego, CA; May 1990; NASA Technical Memorandum 102807; 1990

- Davis, T.J., H. Erzberger, and H. Bergeron; Design of a Final Approach Spacing Tool for TRACON Air Traffic Control; NASA Technical Memorandum 102229; Ames Research Center, 1989

- Erzberger, H., and Nedell, W., “Design of Automated System for Management of Arrival Traffic,” NASA TM-102201, June 1989.

- “Center TRACON Automation System Build 2 Operational Description Document,” MIT Lincoln Laboratory, July 1997.

- Swenson, H. N., Hoang, T., Engelland, S., Vincent, D., Sanders, T., Sanford, B., Heere, K., “Design and Operational Evaluation of the Traffic Management Advisor at the Fort Worth Air Route Traffic Control Center”, 1st USA/Europe Air Traffic Management Research & Development Seminar, Saclay, France, June 1997

- Davis, T. J., Erzberger, H., Green, S. M., Nedell, W., “Design and Evaluation of an Air Traffic Control Final Approach Spacing Tool”, Journal of Guidance, Control, and Dynamics, Vol. 14, No. 4, pp. 848-854.

- “Center-TRACON Automation System (CTAS) Build 2 Computer-Human Interface (CHI) Requirements Specification,” MIT Lincoln Laboratory, August 1998.

- Quinn, C., Zelenka, R. E., “ATC/Air Carrier Collaborative Arrival Planning”, 2nd USA/Europe Air Traffic Management Research & Development Seminar, Orlando, FL, December 1998.

- Davis, T. J., Isaacson, D. R., Robinson, J. E. III, den Braven, W., Lee, K. K., Sanford, B., “Operational Field Test Results of the Final Approach Spacing Tool”, Proceedings of the IFAC 8th Symposium on Transportation Systems, Chania, Greece, June 1997.

- Isaacson, D. R., Davis, T. J., Robinson J. E. III, “Knowledge-based Runway Assignment for Arrival Aircraft in the Terminal Area”, AIAA Guidance, Navigation, and Control Conference, New Orleans, LA, August 1997.

- Zelenka, R. E., Beatty, R., Engelland, S., “Preliminary Results of the Impact of CTAS Information on Airline Operational Control”, AIAA-98-4481.

- Slattery, R., “Examination of Possible Future Terminal Area Procedures”, AIAA Guidance, Navigation, and Control Conference, San Diego, CA, July 1996.

- Lee, K. K., Sanford, B., Slattery, R., “The Human Factors of FMS Usage in the Terminal Area”, AIAA Modeling and Simulation Technologies Conference, New Orleans, LA, August 1997.

- Hinton, D. A., “Aircraft Vortex Spacing System (AVOSS) Conceptual Design”, NASA TM 110184, August 1995.

- Clarke, J. B., Hansman, R. J.,  "Systems Analysis of Noise Abatement Procedures Enabled by Advanced Flight Guidance Technology," AIAA-97-0490, Presented at the 35th Aerospace Sciences Meeting, Reno, Nevada, January 6-9, 1997.

- Welsch, Jerry D.,  Andrews, John W., "An Examination of Prior aFAST Benefits Analysis Studies - Interim Report; MIT/LL 92PM-AATT-0002, December 1, 1999

- Welsch, Jerry D., Andrews, John W., "Final Approach Spacing Tool Benefits Final Report", MIT/LL 92PM-AATT-0009, September 15, 2000

# Text boxes

G

EGF695

18R E120

5

H

H

J

EGF520

17C  E120

5

J

NWA270

17L MD80

3

G

AAL1109

18R  MD80

4

H

ASE243

18R SF34

6     190

H

DAL1105

18R A320

7

H

AAL444

17L  MD80

4

G

DAL1253

17C  MD80

7

E

ASE437

17L  SF34

5

E

Speed Advisory

G

EGF695

18R E120

5

H

H

J

EGF520

17C  E120

5

J

NWA270

17L MD80

3

G

AAL1109

18R  MD80

4

H

ASE243

18R SF34

H100

H

DAL1105

18R A320

7

H

AAL444

17L  MD80

4

G

DAL1253

17C  MD80

7

E

ASE437

17L  SF34

5

E

Heading

Advisory

E

G

EGF695

18R E120

5

H

H

J

EGF520

17C  E120

5

J

NWA270

17L MD80

3

G

AAL1109

18R  MD80

4

H

ASE243

18R SF34

H100 190

H

DAL1105

18R A320

7

H

AAL444

17L  MD80

4

G

DAL1253

17C  MD80

7

E

ASE437

17L  SF34

5

E

Combined

Advisory

G

EGF695

18R E120

5

H

H

AAL1808

18R MD80

8

W

J

EGF520

17C  E120

5

J

NWA270

17L MD80

3

G

AAL1109

18R  MD80

4

H

ASE243

18R SF34

6

H

DAL1105

18R A320

7

H

AAL444

17L  MD80

4

G

DAL1253

17C  MD80

7

E

ASE437

17L  SF34

5

E

# Trajectory Quick Look

H090

H360

S190

H150

S210