MSFC Problem Reporting and Corrective Action (PRACA) System

WHOLE RECORD REPORT( + ADDENDUM)

| MSFC Record # A09937 | In-Flight Anomaly Number -- | Contractor Report Number E-097 | JSC# -- | KSC# -- |
| --- | --- | --- | --- | --- |
| Problem Title ORIFICE MISIDENTIFIED |
| EICN# -- | ELEMENT ET | Contractor MMMSS | FSCM# -- | FCRIT 1R |
| HCRIT -- | Sys_Lvl Y | Misc Codes A (4) B C D E (X) F G H I J K L M N O |
| HARDWARE EIM | NOMENCLATURE ORIFICE FITTING | PART# 80931003756-033 | SER/LOT# N/A | MANUFACTURER PLASTIC FAB |
| HARDWARE LRU | NOMENCLATURE LH2 ULL FEED THRU | PART# 80931003779 | SER/LOT# N/A | MANUFACTURER MMC |
| HARDWARE NCA | NOMENCLATURE ORIFICE FITTING | PART# 80931003756-033 | SER/LOT# N/A | MANUFACTURER PLASTIC FAB |
| Test/Operation L - FLD | Prevailing Condtion S - SHIPPING | F / U F | Fail Mode UC - UNSAT | Cause MAW - MFG-ASY-WORK |
| System ELECTRICAL | Defect MT - TYPE W | Material D - DIE | Work Contact J. ADAMS | Fail Date 01/30/1986 |
| Received at MSFC 02/21/1986 | Date Isolated -- | FMEA Reference 3.1.2.9 | IFA: Mission Phase -- | Mission Elapsed Time -- |
| Location MAF | Symptom UC - UNSAT | Time Cycle -- |
| Effectivity Text LWT-16, 20, 21, 22, 24 AND SUBS |
| Vehicle Effectivity Codes |
| Vehicle 1 -- | Vehicle 2 -- | Vehicle 3 -- | Vehicle 4 -- | Vehicle 5 -- |
| Mission Effectivity Codes |
| Mssn 1 -- | Mssn 2 -- | Mssn 3 -- | Mssn 4 -- | Mssn 5 -- |
| Estimated Completion Dates |
| MSFC Approved Defer Until Date -- | Contractor Req Defer Until Date -- | LVL 3 Close -- | Remark / Action -- |
| Investigation / Resolution Summary |
| Last MSFC Update 10/07/1987 | CN RSLV SBMT 07/18/1986 | Defer Date -- | Add Date -- | R/C Codes 2 - MFG -- -- |
| Assignee |
| Design W. COBB | Chief Engineer -- | S & MA R. JACKSON | Project M. PESSIN | Project MGR -- |
| Approval |
| Design W. COBB | Chief Engineer -- | S & MA R. JACKSON | Project M. PESSIN | Project MGR -- |
| PAC Assignee G. MILLER | PAC Review Complete GM | MSFC Closure Date 08/08/1986 | Status C - CLOSED | F/A Completion -- |
| Problem Type -- | SEV -- | Program Name -- | REVL -- | OPRINC -- |
| FUNC MOD -- | Software Effectivity -- -- -- -- -- | Software Fail CD -- | SUBTYPE -- | Software Closure CD -- |
| RES PERSON L2 -- | Approval Signature L3 -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Contractor Status Summary |
| Reliability/Quality Assurance Concerns, Recommendations: |
| Problem Description REF: MARS T-89570 AND DC&R E-86-001 ORIFICE FITTINGS, P/N'S 80931003756-033 AND -034, HAD BEEN MISIDENTIFIED BY THE MANUFACTURER THE SMALLER ORIFICES, P/N -033, ARE USED ON THE PRESSURE INLET FITTINGS OF BOTH THE LH2 AND LOX ULLAGE PRESSURE TRANSDUCERS. THE LARGE ORIFICES, P/N -034, HAD BEEN LABELLED AS -033. THE ORIFICE FITTINGS ARE USED IN BOTH THE LOX AND LH2 FLIGHT ULLAGE PRESSURE TRANSDUCER INSTALLATIONTO PROTECT THE TRANSDUCERS FROM ACOUSTIC NOISE. THE PARTS ARE NOT DESIGNED TO BE INTERCHANGEABLE |
| Contractor Investigation/Resolution 2/21/86 - MISIDENTIFICATION OF PARTS WAS VENDOR ERROR. EXACT CAUSES AND CIRCUMSTANCES ARE UNDER INVESTIGATION. 3/3/86 CONSTRAINTS - LWT'S 16, 20, 21, 24 THRU 31, AND MPTA. EFFECTIVITIES - LWT'S 16, 20, 21, 22 AND 24, AND SUBS. 3/3/86 BACKGROUND - WHILE PACKAGING A SHIPMENT OF BOTH TYPES OF ORIFICE FITTINGS TO BE SENT TO KSC, IT WAS DISCOVERED THAT SOME OF THE PARTS WERE MISIDENTIFIED ON THE IDENTIFICATION CARDS WITH THE PARTS. SOME 80931003756-033 ORIFICES WERE IDENTIFIED AS -034 AND VICE VERSA. THE DISCREPANT PARTS WERE DOCUMENTED ON MARS T-89570. THE ORIFICE FITTINGS ARE USED IN THE INSTALLATIONS OF BOTH THE LOX AND LH2 ULLAGE PRESSURE TRANS- DUCERS, PART NUMBER PD7400098. THE TRANSDUCERS PROVIDE SIGNALS WHICH ARE USED TO CONTROL THE PRESSURIZATION OF THE ET IN FLIGHT. THE ORIFICES REDUCE THE INTENSITY OF THE ACOUSTIC ENERGY WHICH REACHES THE PRESSURE SENSING CAPSULES OF THE TRANSDUCERS. THE HIGH ACOUSTIC ENERGY LEVELS, WHICH OCCUR DURING THE PROPELLANT LOADING CYCLE OF THE ET PRIOR TO LAUNCH, MAY CAUSE EXCESSIVE WEAR OF THE TRANSDUCERS UNLESS THEY ARE PROPERLY PROTECTED. EACH -033 ORIFICE FITTING HAS TWO .014-INCH DIAMETER HOLES IN IT. THE -033 ORIFICES ARE INSTALLED DIRECTLY ON THE #4 MALE, FLARED TUBE, PRESSURE SENSE PORT FITTING OF EACH TRANSDUCER. THE SENSE PORT FITTING OF EACH TRANSDUCER MATES WITH A FLEXIBLE HOSE. THE OTHER END OF EACH FLEXIBLE HOSE MATES WITH A #4 MALE, FLARED TUBE, BULKHEAD FEEDTHROUGH FITTING ON THE TANK WALL. EACH FEEDTHROUGH FITTING HAS A -034 ORIFICE FITTING INSTALLED ON IT. THE -034 ORIFICE FITTING HAS TWO .029-INCH DIAMETER HOLES IN IT THE ORIFICE FITTINGS, -033 AND -034, ARE SO SIMILAR IN APPEARANCE AND THE HOLES SO SMALL THAT IT IS DIFFICULT TO TELL THEM APART VISUALLY UNLESS TWO DIFFERENT PART NUMBER FITTINGS ARE AVAILABLE FORSIDE-BY-SIDE COMPARISON. THE PARTS ARE NOT TRACEABLE NOR ARE THEY MARKED IN ANY WAY FOR IDENTI- FICATION. THE INDIVIDUAL PACKAGE FOR EACH PART CONTAINS A "CLEANING STATUS AND IDENTIFICATION" CARDWHICH IS STAMPED BY THE VENDOR AND MMC QC SOURCE INSPECTION. 3/3/86 INVESTIGATION (PLANNED) - A. MMC PROCUREMENT QUALITY, DEPARTMENT 3761, IS INVESTIGATING THE CIRCUMSTANCES WHICH LED TO THE MISIDENTIFICATION OF THE ORIFICES. ECD IS 3-21-86. B. ITEM OPEN ELECTRICAL ENGINEERING, DEPARTMENT 3513, WITH THE SUPPORT OF PROJECT PLANNING, DEPARTMENT 3860, WILL PERFORM TESTS TO DETERMINE THE EFFECTS OF THE VARIOUS POSSIBLE INCORRECT INSTALLATIONS OF THE ORIFICES ON THE PERFORMANCE OF THE TRANSDUCERS. IT IS POSSIBLE THAT INCORRECT INSTALLATIONS STILL PROVIDE A PROPERLY FUNCTIONING SYSTEM. IF THIS PROVES TO BE THE CASE, IT WILL PROVIDE RATIONALE TO ACCEPT LWT'S 16, 20, 21, 22 AND 24 THROUGH 31 WITHOUT INSPECTION/REPLACEMENT OF THE ORIFICES. ECD IS 5-16-86. CORRECTIVE ACTIONS (PRELIMINARY/PLANNED) - A. SCAR 3761-86-035 HAS BEEN ISSUED TO THE VENDOR, PLASTIC FABRICATING. ECD IS 3-21-86. B. THE RECEIVING ACCEPTANCE PLAN USED AT MAF HAS BEEN REVISED. THE ORIFICE HOLE SIZE IS NOW INSPECTED PRIOR TO ACCEPTANCE OF THE PARTS. C. DC&R E-86-001 WAS ISSUED TO REINSPECT ALL ORIFICES IN MAF INVENTORY STORES FOR HOLE SIZE DISCREPANT PARTS WERE REIDENTIFIED PER MARS T-89570 DISPOSITION QUANTITY INSPECTED: 107 EACH QUANTITY DEFECTIVE: 53 EACH D. THE INSTALLATION KIT FOR LWT-32, P/N 80931043800-020, HAD BEEN ISSUED TO PRODUCTION IN BUILDING 420. ALL ORIFICE FITTINGS IN THE KIT WERE DOCUMENTED AS "SUSPECT" ON MARS T-79085 AND REINSPECTED. MISIDENTIFIED PARTS WERE RELABELLED PER MARS DISPOSITION AND RETURNED TO MAF INVENTORY STORES. THE ORIFICES INSTALLED ON LWT-32 WERE DRAWN FROM INVENTORY STORES WHEN THE MARS WAS WRITTEN AND HAD BEEN INSPECTED PER DC&R E-86-001. QUANTITY INSPECTED: 16 EACH QUANTITY DEFECTIVE: 7 EACH E. THE FINAL ASSEMBLY STOCK ROOM, WHERE THE INSTALLATION KITS FOR THE ORIFICES ARE STAGED, HAD ONLY ONE KIT OF PARTS IN STOCK. THE KIT FOR LWT-33 HAD THE ORIFICES REMOVED AND DOCUMENTED ON MARS T-88170 AS "SUSPECT", AND REPLACEMENT PARTS WERE DRAWN FROM INVENTORY STORES WHICH HAD BEEN INSPECTED PER DC&R E-86-001. THE PARTS ON THE MARS WERE REINSPECTED AND REIDENTIFIED AS NECESSARY. QUANTITY INSPECTED: 16 EACH QUANTITY DEFECTIVE: 7 EACH F. DC&R E-86-004 IS BEING ISSUED TO REQUIRE THE REPLACEMENT OF ALL ORIFICES ON LWT'S 16, 20, 21, 22, 24 THRU 31 AND MPTA. G. RELIABILITY ASSURANCE, DEPARTMENT 3741, IN CONJUNCTION WITH LOGISTICS OFFSITE SUPPORT, DEPARTMENT 3543, HAS GENERATED TWO ACTION REQUESTS TO REQUIRE THE RETURN OF "GOVERNMENT PROPERTY" ORIFICE FITTINGS IN SPARE PARTS STORAGE TO MAF FOR REINSPECTION. AR M6010 WAS ISSUED TO KSC. AR MV6011 WAS ISSUED TO VAFB. NSTL IS BEING HANDLED ON STANDARD SHIPPING DOCUMENTATION. ECD IS 3-7-86. H. PROJECT PLANNING, DEPARTMENT 3052, IN CONJUNCTION WITH MATERIAL OPERATIONS, DEPARTMENT 3860, ARE COORDINATING ACTIONS TO PROCURE SUFFICIENT SPARE ORIFICE FITTINGS TO SUPPORT PRODUCTION AND REINSPECTION EFFORTS. ECD 4-11-86 CLEARANCE OF EFFECTIVITES - A. LWT'S 16, 20, 21, 22 AND 24 THROUGH 31 CONSTRAINT TO FLIGHT. DC&R E-86-004 IS BEING ISSUED TO REQUIRE THE REMOVAL OF ALL INSTALLED ORIFICES AND REPLACEMENT WITH REINSPECTED PARTS. NOTE: IF TESTING PROVIDES DEFINITIVE PROOF THAT INCORRECT ORIFICES HAVE NO DETRIMENTAL EFFECT UPON TRANSDUCER OPERATION, THE DC&R WORK WILL BE HALTED. B. MPTA CONSTRAINT TO PROPELLANT LOADING/ENGINE RUN. DC&R E-86-004 IS BEING ISSUED TO REQUIRE THE REMOVAL OF ALL INSTALLED ORIFICES AND REPLACEMENT WITH REINSPECTED PARTS. C LWT-32/SUBSEQUENT THERE ARE NO CONSTRAINTS. ALL HARDWARE HAS BEEN PROPERLY IDENTIFIED PRIOR TO INSTALLATION ON ET'S. 3/20/86 PRB STATUS - MISIDENTIFIED ORIFICES HAVE BEEN PURGED FROM MMC STORES. ALL KSC AND MPTL SPARES HAVE BEEN BROUGHT BACK TO MMC FOR INSPECTION. TESTS ARE BEING DONE TO SEE WHAT THE ACTUAL EFFECT OF USING WRONG ORIFICE SIZES WOULD BE. THESE TESTS TO BE DONE BEFORE NOSE CONES ARE REMOVED FROM DELIVERED TANKS IN ORDER TO CHECK INSTALLED ORIFICES. ECD HAS NOT BEEN DETERMINED. 4/17/86 PRB STATUS - VENDOR'S PROCESSES AND PROCEDURES WERE CHECKED AND FOUND TO BE ADEQUATE TO PRECUDE OCCURRENCE OF THIS PROBLEM VENDOR HAS NO EXPLANATION OTHER THAN CALLING THIS OCCURRENCE AN ISOLATED QUALITY ESCAPE. TESTS TO DETERMINE EFFECT OF USING WRONG SIZE ORIFICE ARE COMPLETE BUT HAVE NOT BEEN EVALUATED. ECD HAS NOT BEEN DETERMINED. 5/15/86 PRB STATUS - LOADS AND DYNAMICS ARE TO PERFORM TESTS TO DETERMINE THE EFFECTS OF INCORRECT ORIFICE INSTALLATION. THE EXACT CAUSE/CIRCUMSTANCES ARE UNDER INVESTIGATION; HOWEVER, CONTROL OF ALL ORIFICES IN THE SYSTEM ARE NOW IN PLACE. 6/19/86 PRB STATUS - TEST RESULTS INDICATED NO DIFFERENCE IN OPERATION DUE TO ORIFICE SIZE. CAPS CLOSURE BEING PREPARED. ECD IS 7-15-86. 6/19/86 PRB STATUS - TEST RESULTS INDICATED NO DIFFERENCE IN OPERATION DUE TO ORIFICE SIZE. CAPS CLOSURE BEING PREPARED. ECD IS 7-15-86. 7/23/86 FALURE INVESTIGATION - A. THE ORIFICE FITTINGS ARE USED IN THE INSTALLATIONS OF BOTH THE LH2 AND LO2 ULLAGE PRESSURE TRANSDUCERS, PART NUMBER PD7400098. THE TRANSDUCERS PROVIDE SIGNALS WHICH ARE USED TO CONTROL THE PRESSURIZATION OF THE ET IN FLIGHT. THE ORIFICES REDUCE THE INTENSITY OF THE ACOUSTIC ENERGY WHICH REACHES THE PRESSURE SENSING CAPSULES OF THE TRANSDUCERS. THE HIGH ACOUSTIC ENERGY LEVELS, WHICH OCCUR DURING THE PROPELLANT LOADING CYCLE OF THE ET PRIOR TO LAUNCH, MAY CAUSE EXCESSIVE WEAR OF THE TRANSDUCERS UNLESS THEY ARE PROPERLY PROTECTED EACH -033 ORIFICE FITTING HAS TWO .014-INCH DIAMETER HOLES IN IT. THE -033 ORIFICES ARE INSTALLED DIRECTLY ON THE #4 MALE, FLARED TUBE, PRESSURE SENSE PORT FITTING OF EACH TRANSDUCER. THE SENSE PORT FITTING OF EACH TRANSDUCER MATES WITH A FLEXIBLE HOSE. THE OTHER END OF EACH FLEXIBLE HOSE MATES WITH A #4 MALE, FLARED TUBE, BULKHEAD FEEDTHROUGH FITTING ON THE TANK WALL. EACH FEEDTHROUGH FITTING HAS A -034 ORIFICE FITTING INSTALLED ON IT. THE -034 ORIFICE FITTING HAS TWO .029-INCH DIAMETER HOLES IN IT. THE ORIFICE FITTINGS, -033 AND -034, ARE SO SIMILAR IN APPEARANCE AND THE HOLES SO SMALL THAT IT IS DIFFICULT TO TELL THEM APART VISUALLY UNLESS TWO DIFFERENT PART NUMBER FITTINGS ARE AVAILABLE FOR SIDE-BY-SIDE COMPARISON. THE PARTS ARE NOT TRACEABLE NOR ARE THEY MARKED IN ANY WAY FOR IDENTIFICATION. THE INDIVIDUAL PACKAGE FOR EACH PART CONTAINS A "CLEANING STATUS AND IDENTIFICATION" CARD WHICH IS STAMPED BY THE VENDOR AND MMC QC SOURCE INSPECTION. WHILE PACKAGING A SHIPMENT OF BOTH TYPES OF ORIFICE FITTINGS TO BE SENT TO KSC, IT WAS DIS- COVERED THAT SOME OF THE PARTS WERE MISIDENTIFIED ON THE IDENTIFICATION CARD WITH THE PARTS. SOME 80931003756-033 ORIFICES WERE IDENTIFIED AS -034 AND VICE VERSA. THE DISCREPANT PARTS WERE DOCUMENTED ON MARS T-89570. B. THE CORRECTIVE ACTIONS FOR THE MISIDENTIFIED ORIFICES INCLUDED THE REINSPECTION OF ALL PARTS IN STOCK AT MAF AS WELL AS IN GOVERNMENT POSSESSION AT THE LAUNCH SITES. WHILE REINSPECTING THE P/N 80931003756-033 ORIFICES RETURNED FROM KSC, IT WAS DISCOVERED THAT SOME OF THE HOLES WERE NOT CLEANLY DEBURRED, AS REQUIRED BY THE ENGINEERING DRAWING. REINSPECTION OF THE 38 LIKE PARTS IN MAF INVENTORY STORES FOR BURRS FOUND 34 DEFECTIVE PARTS. C. MMC PROCUREMENT QUALITY INVESTIGATED THE MISIDENTIFICATION PROBLEM. THEY WERE UNABLE TO IDENTIFY THE TIME AND PLACE WHERE THE ERROR OCCURRED HOWEVER, ALL MCC AND VENDOR PERSONNEL INVOLVED WERE MADE AWARE OF THE PROBLEM AND INSTRUCTED ON THE IMPORTANCE OF PERFORMING A THOROUGH VISUAL INSPECTION TO VERIFY PART CONFIGURATION. REFERENCE MEMORANDUM FROM J. KING, DATED 4-30-86. D. LOADS AND DYNAMICS, DEPARTMENT 3524, AND ELECTRICAL ENGINEERING, DEPARTMENT 3513, PERFORMED TESTS TO DETERMINE THE EFFECTS OF THE VARIOUS POSSIBLE INSTALLATIONS OF ORIFICES AND BURRED HOLES UPON THE RESPONSE RATE OF THE PRESSURE TRANSDUCERS AND THE LEVEL OF ACOUSTIC ENERGY REACHING THEM. IT WAS CONCLUDED THAT NO DELETERIOUS EFFECTS WOULD RESULT FROM THE USE OF ONE SIZE OF ORIFICE WHERE THE OTHER WAS CALLED FOR OR FROM THE USE OF -033 ORIFICES WITH BURRS AROUND THE HOLES. REFERENCE INTEROFFICE MEMORANDUMS 3513-86-049, 3524-86-216, 3522/P-86-020 AND 3522/P-86-047. 7/23/86 CORRECTIVE ACTIONS (IMPLEMENTED) - A. THE RECEIVING ACCEPTANCE PLAN USED AT MAF WAS REVISED ON FEBRUARY 6, 1986, TO REQUIRE VERIFICATION OF HOLE SIZE B. SUPPLIER CORRECTIVE ACTION REQUEST 3761-86-035 WAS ISSUED TO THE VENDOR, PLASTIC FABRICATING, FOR THE MISIDENTIFIED PARTS. THE VENDOR ATTRIBUTED THE PROBLEM TO THE SUBCONTRACTOR, QUALITY CONTROLLED CLEANING, WHICH CLEANS AND PACKAGES THE PARTS. QUALITY CONTROLLED CLEANING WAS WARNED THAT THE PARTS WERE FLIGHT CRITICAL AND THAT EXTREME CARE SHOULD BE USED WHEN PROCESSING THEM. C. SUPPLIER CORRECTIVE ACTION REQUEST 3761-86-088 WAS ISSUED TO THE VENDOR, PLASTIC FABRICATING, FOR THE BURRS AROUND THE HOLES OF THE -033 PARTS. THE VENDOR ATTRIBUTED THE PROBLEMS TO THE SUBCONTRACTOR WHICH DRILLS THE HOLES. THE SUBCONTRACTOR ADDED A CAUTION NOTE TO THEIR PLANNING TO PREVENT A RECURRENCE. PLASTIC FABRICATING'S INSPECTION SHEETS WERE ALSO CHANGED TO INCLUDE AN INSPECTION FOR BURRS. D. DC&R E-86-001 WAS ISSUED TO REINSPECT ALL ORIFICES IN MAF INVENTORY STORES FOR HOLE SIZE DISCREPANT PARTS WERE REIDENTIFIED PER MARS T-89570 DISPOSITION QUALITY INSPECTED: 107 EACH QUANTITY DEFECTIVE: 53 EACH E. THE INSTALLATION KIT FOR LWT-32, P/N 80931043800-020, HAD BEEN ISSUED TO PRODUCTION IN BUILDING 420. ALL ORIFICE FITTINGS IN THE KIT WERE DOCUMENTED AS "SUSPECT" ON MARS T-79085 AND RE- INSPECTED FOR HOLE SIZE. MISIDENTIFIED PARTS WERE RELABELLED PER MARS DISPOSITION AND RETURNED TO MAF INVENTORY STORES. THE ORIFICES INSTALLED ON LWT-32 WERE DRAWN FROM INVENTORY STORES WHEN THE MARS WAS WRITTEN AND HAD BEEN INSPECTED PER DC&R E-86-001. QUANTITY INSPECTED: 16 EACH QUANTITY DEFECTIVE: 7 EACH F. THE FINAL ASSEMBLY STOCK ROOM, WHERE THE INSTALLATION KITS FOR THE ORIFICES ARE STAGED, HAD ONLY ONE KIT OF PARTS IN STOCK. THE KIT FOR LWT-33 HAD THE ORIFICES REMOVED AND DOCUMENTED ON MARS T-88170 AS "SUSPECT", AND REPLACEMENT PARTS WERE DRAWN FROM INVENTORY STORES WHICH HAD BEEN INSPECTED PER DC&R E-86-001 THE PARTS ON THE MARS WERE INSPECTED FOR HOLE SIZE AND REIDENTIFIED AS NECESSARY. QUANTITY INSPECTED: 16 EACH QUANTITY DEFECTIVE: 12 EACH G ALL ORIFICE FITTINGS IN STOCK AT KSC WERE RETURNED TO MAF AND REINSPECTED FOR HOLE SIZE. QUANTITY INSPECTED: 56 EACH QUANTITY DEFECTIVE: 10 EACH DURING THE REINSPECTION FOR HOLE SIZE, IT WAS NOTED THAT SOME OF THE -033 PARTS HAD BURRS AROUND THE HOLES. ALL -033 PARTS IN THE LOT WERE THEN INSPECTED FOR BURRS. REFERENCE MARS T-90056 QUANTITY INSPECTED: 32 EACH QUANTITY DEFECTIVE: 8 EACH H. ALL ORIFICE FITTINGS IN STOCK AT NSTL WERE RETURNED TO MAF FOR REINSPECTION REFERENCE MARS T-90057. TOTAL QUANTITY OF PARTS: 14 EACH QUANTITY MISIDENTIFIED: 11 EACH QUANTITY OF -033 PARTS: 8 EACH QUANTITY WITH BURRS: 1 EACH I. UPON DISCOVERY OF -033 ORIFICES WITH BURRS AROUND THE HOLES, ALL -033 PARTS IN MAF INVENTORY STORES WERE REINSPECTED FOR BURRS. REFERENCE MARS T-90073. QUANTITY INSPECTED: 38 EACH QUANTITY DEFECTIVE: 34 EACH J. ALL ORIFICE FITTINGS IN STOCK AT VAFB WERE RETURNED TO MAF AND REINSPECTED FOR HOLE SIZE AND BURRS. QUANTITY INSPECTED: 4 EACH QUANTITY DEFECTIVE: 0 EACH K. DC&R E-86-004 WAS WRITTEN IN ANTICIPATION OF THE NEED TO SUPPORT FLIGHTS BEFORE THE TESTING OF THE VARIOUS ORIFICE DEFECTS COULD BE COMPLETED. THE DC&R WOULD HAVE REPLACED ORIFICES ON FLIGHT VEHICLES AND MPTA. DUE TO THE DELAY IN TH FLIGHT PROGRAM, TESTING WAS COMPLETED BEFORE THE NEXT FLIGHT. THE DC&R HAS BEEN CANCELLED. 7/23/86 RESOLUTION - BASED ON THE FAILURE INVESTIGATION AND CORRECTIVE ACTIONS DESCRIBED ABOVE, THE RESOLUTION TO THE PROBLEM IS AS FOLLOWS: THE ORIFICE FITTINGS WERE FOUND TO HAVE TWO TYPES OF DEFECTS AS THE RESULT OF VENDOR ERROR: - THE PART NUMBERS OF SOME ORIFICES WERE INCORRECT, THAT IS THE P/N OF THE SMALLER SIZE HAD BEEN ASSIGNED LARGER SIZE AND VICE VERSA. - SOME OF THE SMALLER ORIFICES, THE -033, HAD BURRS ON THE EDGES OF THE HOLES THE ENTIRE STOCK SYSTEM WAS CLEARED BY REINSPECTION AND REIDENTIFICATION OF MISIDENTIFIED PARTS. ENGINEERING TESTS FOUND THAT NEITHER THE MISIDENTIFICATION OF THE PARTS NOR THE BURRS WOULD DEGRADE THE PERFORMANCE OF SYSTEM IN WHICH THE ORIFICES ARE INSTALLED THEREFORE, NO INSPECTION OR REPLACE-MENT WAS REQUIRED FOR COMPLETED INSTALLATIONS ON ET'S. CORRECTIVE ACTION WAS OBTAINED AT THE VENDOR ADDITIONAL INSPECTIONS WERE ADDED TO THE MAF RECEIVING INSPECTION PLAN TO DETECT SIMILAR FUTURE QUALITY ESCAPES AT THE VENDOR. CLEARANCE OF EFFECTIVES - LWTS 16, 20, 21, 22, 24/SUBSEQUENT AND MPTA NO CONSTRAINT NO COMBINATION OF ORIFICES WILL INCREASE THE ACOUSTIC LEVEL AT THE TRANSDUCERS ABOVE THAT OF THE DRAWING INSTALLATION. BURRS ON THE HOLES OF -033 PARTS WIL NOT IMPAIR OPERATION. NO FURTHER RECURRENCE CONTROL IS NECESSARY. RECOMMEND THIS PROBLEM REPORT BE CLOSED |
| MSFC Response/Concurrence |

MSFC Problem Reporting and Corrective Action (PRACA) System

ASSESSMENT ADDENDUM REPORT

| MSFC Report# A09937 | IFA# -- | Contractor RPT# E-097 | JSC# -- | KSC# -- | EICN# -- |
| --- | --- | --- | --- | --- | --- |
| Asmnt Part# 80931003756-033 | Asmnt Part Name ORIFICE FITTING | Asmnt Serial/Lot# N/A |
| HCRIT CD -- | FCRIT CD 1R | CAUSE CD MAW - MFG-ASY-WORK | FAIL MODE UC - UNSAT |
| Asmnt FMEA 3.4.1.1 | Asmnt FM 1 | FMEA CSE AA | FMEA SCSE N/A |
| Asmnt FMEA -- | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Asmnt FMEA -- | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Correlated Part# -- | Correlated Part# -- | Correlated Part# -- |
| Associated LRU# -- | Associated LRU# -- | Associated LRU# -- |
| MAJOR DESIGN CHANGES |
| APRV DATE -- | DESCRIPTION OF CHANGES -- |
| ASSESSMENT TEXT |