POLAR Spacecraft Status As of: Tues 21 Aug 07, 12:00 EST

(Changes from last week in bold border)

| Subsystem/ Component | NOAA-15K AM: 17:49=AN GAC data only | NOAA-16L PM: 15:04=AN GAC&LAC data | NOAA-17M AM: 22:23=AN GAC&LAC data | NOAA-18N PM 13:49=AN GAC & LAC data |
| --- | --- | --- | --- | --- |
| LAUNCHED | 05/13/98 | 09/21/00 | 6/24/02 | 5/20/05 |
| CNTL OBP | OBP2 | OBP2 | OBP2 | OBP2 |
| BUS | B-BUS XSU-1 | B-BUS XSU-1: TOAR444 | B-BUS XSU-1 | B-BUS XSU-1 |
| BUS VETO | NO | NO | NO | NO |
| ADACS | Nominal Mode Rgmode=Monitor Gyro-3 Off 6/26/00 Gyro chans=AAB N2 Low PSI invalid | RGYRO Mode Estimate Y-ROLL Rgmode=PASSIVE Gyros-1 & 3 Inop/Off Gyro chans XA-ZB Pitch wheel bias 2400 Gyro2 safe macro | Nominal Mode Rgmode=Monitor Gyro-3 Off 6/10/04 Gyro chans=AAB GAS Enabled Dec 05 | Nominal Mode Gyro-A MIMU-2 Z-wheel -Pitch TOAR 447 Z-momentum transition complete Pitch Torquer again active |
| RXO | PRI daily bias -8 mS -500 mS 12/31/05 | PRI Daily Bias –5.5 mS -1500 mS 31Dec05 | PRI Daily Bias –3 mS -1500 mS 31Dec05 | PRI No daily bias -1500 mS 31Dec05 |
| CLOCK DIV | 2 | 2 | 2 | 2 |
| MIRP | External Synch Rephase 0730 daily | External Sync Rephase each orbit | External Sync Rephase Enabled | External Synch Rephase Enabled |
| TIP SIDE | 2 (since 4/3/03) 3 channels inop | 2 since 4/18/05 (analog drifting?) | 2 Swapped 9/20/06 | 1 Analog telem drifting |
| Recorders (DTR, SSR) | DTRs 1, 2, 3, 4 Safestate 1B EOT | DTRs 1, 2, 3, 4A Safestate 3A 4B STIP only | DTR 1,3,4 / SSR 2 Safestate=SSR 2B 4A Pressure leak | SSRs 1,2,3,4,5 Safestate=5B Current spikes |
| VTX (APT data) | #1 ON As of 19 June 07 | OFF / INOP since 11/15/00 | #2 ON 137.62 MHZ | #1 ON 137.1 MHZ As of 16 Aug 07 |
| BTX | #1 137.35 MHZ | #2 137.77 MHZ | #2 137.77 MHZ | #1 137.35 MHZ |
| STX 1 = rcp 1698.0 mhz 2 = lcp 1702.5 mhz 3= rcp 1707.0 mhz 4= rcp 2247.5 mhz | 2-Omni HRPT 2 Omni=rcp Power TOAR 446 4-Playback 1,2,3-Degraded | 2 – HRPT 1– Playback 4 off INOP-10 Aug 2007 3 low power INOP -10 Aug 2007 | 3 – HRPT TOAR424 low power 2 & 1 Playback STX-1 Power drop STX-4 no modulation | 1 - HRPT 3 - Playback 2-Playback 4-Test & Standby |
| POWER (Array offset and CANT angle, charge & V/T rates, eclipse states and sun angle) | Array Off -45 Since 1/25/01 Full Sun Sun Angle 13 Uptrend to 18 early Jan 07 Batts 1-3= LRC V/T=7/9 SA CANT=37 degs | Array Off -40 Since 7/16/02 Eclipse all year Sun Angle 34 Steady trend Batts 1-3= LRC V/T=4/8 SA CANT=22 degs Transitioning to full sun S/C in Sept 07 BVR Phase Control auton swap 7/19/07 | Array Off. –40 Since 1/29/04 Eclipse all year Sun Angle at 66 Steady trend Batts 1-3= LRC V/T= 4/8 SA CANT=37 degs | Array Off. -40 Since 6/6/05 Eclipse all year Sun Angle 63 uptrend to 65 on 1 Jan 07 Batts 1-3=LRC Batts 1-3 V/T=4/8 SA CANT=22 BVR Phase Control auton swap 3/29/06 & 1/4/07 |
| AVHRR | Nominal Channel 3B only Occasional minor scan motor instabilities | Nominal Recent SM current increases TCE24 OFF 4/14/04 Channel 3B only | Nominal 3A-B switch enabled Previous scan motor current mini surges | Nominal Channel 3B only Scan motor current drop 29 Aug 06 |
| AMSU-A1 | Operational Ch14 inoperative Ch11 inoperative | Operational Primary PLLO chans 9-14 bias shift. Backup PLLO inop. Channel 9-14 noise | OFF/INOP Since 10/30/03 Survival heat on. | Nominal Full Scan mode |
| `AMSU-A2 | Nominal | Nominal | Nominal | Nominal |
| AMSU-B | Operational Bias in All Chans. Degraded Chan-3 | Operational Space Position-3 Chan-8 degradation | Nominal | Replaced by MHS |
| HIRS | NOMINAL FW Abrupt return to nominal 7/12/05 After years of minor and major current surges FW mode=Hi Powr | NOMINAL New all time high filter motor current reached 9/17/06. Imagery occasionally exhibits high levels of radiometric noise | NOMINAL 1 Pixel cross-track misalignment. | Operational Filter Heat OFF. LW channel 1-12 noise TOAR 448 Loose LWIR lens. LW imagery erratic. |
| MHS/MIU |  |  |  | Nominal Fly Wheel Motor Current Spiking but not alarming since 27 Dec 06 Entered Motor Spin State on 27 March 07 |
| MSU |  |  |  |  |
| SSU |  |  |  |  |
| DCS RFI investigation | Nominal | Nominal Pseudo message turned on 1/5/06 | Nominal | Nominal DRU’s 1-7 On DRU8 inop/off |
| SARR | Operational A-Side, AGC Mode Intermittent failures for 243MHz A&B | Operational Mode =AA A-side, AGC Mode (B-side in FG mode) 243 MHz = INOP. | Nominal A-side All AGC Mode | Nominal A-Side All AGC Mode Since 15 Aug 05 |
| SARP | Nominal RCVR B/W = 2 | Nominal RCVR B/W = 2 | Nominal | Nominal A-side 23 May05 |
| SEM | Nominal E-CDEM-HVPS=2 P-CDEM-HVPS=0 | Nominal E-CDEM-HVPS=6 P-CDEM-HVPS=5 27 Jun 0615:30z | Nominal E-CDEM-HVPS=2 P-CDEM-HVPS=4 27 June 06 16:00z | Nominal Elec-CH-HVPS=1 27 June 06 17:00z Prot-CH-HVPS=0 |
| SBUV |  | Operational Degraded Ozone data Backup Diffuser inop Primary Diffuser deployment problem TOAR 426 AMSU EMI causing erratic Behavior in PMT cathod, range 3 | Nominal Anode Mode Plan sweep mode Standard Ops TOAR 463 sun glint IBSL test performed 12 Sept 06 Grating motor investigation | Nominal Anode mode since 6 July 05 13:30z Electronics turnoff taken out of STESM safestate table TOAR 462 sun glint |
| SADPOS |  | ON Enabled MFactor50% Timer = 12 mins | ON ENABLED Timer = 12mins | ON Enabled Timer =12 mins |
| THERMAL Heaters, louvers TCE’s | TCE26 & 15H Telem valid TOAR 432 closed TCE24L&25L (HIRS & AVHRR) failed 5/13/98 RCE thermostat failed 5/13/98 Spacecraft in thermal uptrend | Nominal TCE24 OFF 4/14/05 (AVHRR H&L) HIRS Filter heater turned OFF 1/18/05 | TCE3H Batt 2A heater failed ON, turned off 8/26/03 AMSU-A1 survival heaters on 10/29/03 | All TCE’s active HIRS filter heater turned OFF 9/28/06 |

COMMENTS/CHANGES:

MISC:	 Planning for a partial solar eclipse on 11 Sep 2007 is being planned.

NOAA-15:	There were relatively no changes to the NOAA-15 payload health situation during the past week.  N-15 has come out of summer eclipse season.  EPS in nominal

No new updates on #2 gyro since last week.  Latest yaw updates are shown in Figures 1.

NOAA-16: 	There was relatively no change in the performance of the NOAA-16 payload subsystems during the past week and the rest of the spacecraft subsystems were also nominal during this time.

No updates in the STX-3 & 4 issues.  A test for both STX-3 & 4s are being planned, no firm date yet.

A request from NASA has been made to move the SA from -40 to -35 so the shunts are always on to possibly avoid the spikes on the recorders.  An evaluation and a date for move is TBD.  NOAA-16 will be in full sunlight beginning in mid-September.  This is the first time ever it will not be eclipsing.

NOAA-17: 	There was relatively no change in the performance of the NOAA-17 payload subsystems during the past week. The HIRS filter wheel period noise calmed down this week.

No updates or conclusion were reached about the Attitude disturbance on 17 July 2007.  The investigation continues.

NOAA-18:	There were relatively no changes to the NOAA-18 health situation during the past week.  MHS DC offsets is still being investigated.

The VTX was switched from side 2 to 1 on 16 Aug 2007 at 14:43.

MetOp A:	No significant changes reported on the NOAA instruments on MetOp.  The HRPT transmitter failure investigation continues.

Trend Observations (NOAA Instruments)

·       All housekeeping telemetry and science data were stable during this reporting period.

·       HIRS Filter Wheel resyncs have remained at the same approximate rate as reported last week (approximately once every 93 seconds).

Anomalies

·        AR8360, “HIRS Scan Mirror Temperature Out-of-Limits”:  Anomalous temperature telemetry was observed between August 6-8, but has returned to nominal since then.  There was also a correlation observed between jumps in the Scan Mirror Temperature telemetry and slight drops in the Patch Power.  This is currently under investigation by ITT.  An ARB with EUMETSAT and NOAA is planned for Thursday, August 23, at 16:00 CET.

·         AR8154, “HRPT SSPA-A Failure”:  Investigations continued on trying to isolate the cause of the HRPT SSPA failure.  An ARB was held on August 20 to review the latest test results.  The breadboard tests at Tesat have agreed well with in-orbit measurements.  The investigation is circling in on a transistor that is used twice in the SSPA:  the CLY38 transistor.  The observed behavior (8-10 dB lower RF power) would be consistent with one of the two resistors having a short circuit.  The same resistor is used in the MSG (Meteosat Second Generation) design, where a similar in-orbit SSPA failure occurred.  Astrium, Tesat and EUMETSAT are considering another in-orbit test later this week, if they can improve the measurement resolution in order to determine whether the RF power reduction is truly 10 dB (to confirm the CLY38 transistor as the failed component).  Tesat also took the action to use some available MSG modules and expose them to additional radiation testing (to investigate whether an SEU/SET or IESD susceptibility is present).  The HRPT will remain OFF until further notice (no near term plans for switching ON with the redundant chain) .

Operations Performed

·         The SEM IFCs were run on Tuesday, August 14, with the TED IFC starting at 08:07:37 UTC and the MEPED IFC starting at 08:08:57 UTC.

Operations Planned

·         The SEM IFCs will be run again on their weekly schedule (Tuesday, Aug 21).

Notes: Figure 1has been omitted for web listing.