Site Specific Hydrologic Predictor (SSHP)

Reference Guide

Release: OB6

Last Updated 2/1/06

NWS

Office of Hydrologic Development

Hydrology Laboratory

1. Introduction	5

1.1 Purpose	5

1.2 Changes From Previous Version (OB5 version)	5

1.2.2 User Interface Changes	5

1.2.3 Database Changes	5

2. Overview	5

Figure 2.1 SSHP Overview	6

3. Interactive Application	7

Figure 3.1 SSHP Application	8

4. Precipitation Data	9

4.1 SSHP MAP Preprocessor	9

Figure 4.1 MAP Preprocessor	10

4.2 Precipitation Input Options	11

5. SSHP Data Transfer	12

5.1 Transferred Data Description	12

Figure 5.1 Data Transfer Process	13

5.2 Invocation Description	14

5.2.1 Sending Side (RFC)	14

5.2.2 Receiving Side (at each targeted WFO)	15

5.3 Cleanup	16

5.4 Example XML Data Transfer Control File:	16

6.  Local SAC-SMA State Updater	19

Figure 6.1 SAC-SMA State Updater	19

7. System Setup	21

7.1 RFC Setup	21

7.1.1 OFS Setup	21

7.1.2 Data Transfer	21

7.2 WFO Setup	21

7.2.1 Static Data Setup (for API-MKC and SAC-SMA)	21

7.2.2 Data Generally Transferred from RFC	22

7.2.3 Token Settings	22

7.2.4 Cron Job	22

7.2.5 Adding an SSHPConfig record	22

8. Forecast Adjustment	24

8.1 Description	24

8.2 Details	24

8.2.1  Pairing	24

8.2.2  Interpolation	24

8.2.3  Blending	24

Appendix A:    Directories and Files	26

1. Directories and File Locations	26

1.1 Application Scripts and Executable Files	26

1.2 Log Files	26

1.3 Application Setup Files	26

1.4 Data Transfer Directories	27

2. Script and Executable Descriptions	27

Appendix B – SSHP AppsDefaults Tokens	29

Appendix C – RFC Segment Definition Example	31

Appendix D – Science Background	34

Appendix E – Calibration and State Maintenance	36

1. Model Parameter Calibration Options	36

2. Model State Maintenance Options	37

Appendix F – SSHP Database Tables	39

Appendix G - Unit Hydrograph Editor Guide	44

1. Introduction	44

2.   Table Modification	44

3.   Data Contents and Usage	44

3.1 UnitGraph Table in IHFS	44

4. Editing	45

4.1 Adding A Record In Memory	45

4.2 Removing A Record In Memory	45

4.3 Modifying A Record In Memory	45

4.4 Saving Changes To Database	45

4.5 Deleting Unitgraphs From Database	45

4.6 Importing and Exporting Hydrographs	46

4.7 Sorting	46

4.8 Viewing	46

4.9 Screen Shot	47

Document Notes

This document is the reference guide for the SSHP application and its associated utility programs.  It is intended to provide sufficient technical information to allow the SSHP application to be configured for operation at a field site, whether it is a WFO or an RFC.  While the application’s primary purpose is to provide WFOs with a forecasting tool for fast-responding streams, RFCs may also wish to run the application, in order to help configure and monitor the system as used by the WFOs, and to have easy access to models run at a 1-hour time step.  This document will refer to the office that uses the application, as the “WFO”.  Substitute “RFC” if appropriate.

## 1. Introduction

### 1.1 Purpose

The Site Specific Hydrologic Predictor (SSHP) is an application that is designed to run at a WFO in order to provide streamflow forecasts for headwater points of streams which respond quickly to precipation.  Since the 6-hour time step used by most RFC models is too long to be effective for these fast-responding streams, SSHP uses a 1-hour time step for its model computations.

### 1.2 Changes From Previous Version (OB5 version)

There are no feature changes for the OB6 version (compared with OB5).

### 1.2.2 User Interface Changes

There are no user interface changes to the OB6 version

### 1.2.3 Database Changes

The database accessed has been changed from INFORMIX to PostgreSQL.

## 2. Overview

The SSHP subsystem consists of the SSHP interactive application, the SSHP MAP preprocessor, the data transfer components, and the SAC-SMA state updater.   The application is the most visible part of  the SSHP subsystem.  The application produces streamflow forecasts for headwater forecast points and can use either the API-MKC or the SAC-SMA rainfall-runoff models, configurable by forecast point.  It requires a unit hydrograph and rating curve for each forecast point.

The application relies on the other parts of the subsystem for putting essential data into the IHFS database. The MAP preprocessor puts basin-average observed QPE time series into the database.  The data transfer components transfer SAC-SMA states and parameters from the RFC to the WFO and store them in the database.  Finally, the optional SAC-SMA state updater can be used to keep SAC-SMA states current in cases where no state update has been sent from the RFC to the WFO.  Each of the components discussed above is discussed below in greater detail.

### Figure 2.1 SSHP Overview

## 3. Interactive Application

The SSHP interactive application provides the following functionality using its various GUIs.

1. Configuration of model preferences and settings, including a choice of rainfall-runoff models.

2.  Creation of forecast hydrograph using either the SAC-SMA or API-MKC rainfall-runoff 	models.

3. Graphical and tabular editing of the precipitation time series.  As soon as the data is edited, the

forecast model is rerun and the new hydrograph is displayed.

4. Graphical and tabular editing and viewing of the forecast hydrograph.  Note:  if the forecast 	model is rerun, this data is overwritten.

5.  Tabular viewing of the potential evapotranspiration time series (if used).

6.  Tabular editing of monthly ET-demand curve and PE-adjustment factors.

7.  Saving of forecast height and discharge time series.  The time series are saved in the IHFS database and are accessible to the other WHFS applications.

8.  Tabular and graphical viewing of prior computed runoff time series and the current computed 	runoff time series.

9.  Modification of model states and parameters through the Analysis Window’s user interface.

### Figure 3.1 SSHP Application

## 4. Precipitation Data

### 4.1 SSHP MAP Preprocessor

In the standard configuration, the SSHP MAP Preprocessor is executed with MPE/Fieldgen scripts (run_mpe_fieldgen, rerun_mpe_fieldgen, and run_mpe_whfs).  The MAP Preprocessor reads the best estimate xmrg files and computes MAP for configured basins.  The MAP values for the basins are placed into the ArealObs table with pe = ‘PP’, dur = 1 hour, and ts = “PM”.  The application, though, only reads observed QPE from the ArealObs table.  So, if some other process were to take the place of the current preprocessor, the precipitation data source could be different.  This might be necessary in offices in which the MPE application is not used.  Also, the OB4 version of the application will read QPF from the ArealFcst table, looking for pe = “PP”, dur = 1 hour, and a ts starting with “F”.  The application determines the type/source to use based on the ts_rank as stored in the IngestFilter table (editable in HydroBase).  The SSHP does NOT place any mean areal QPF data in this table, it simply reads it.

### Figure 4.1 MAP Preprocessor

### 4.2 Precipitation Input Options

If the SSHP MAP Preprocessor is not appropriate for use at a particular WFO, then some other means of populating the database with mean areal QPE should be devised.  Note: if a different MAP preprocessor is being used, the “Run MAP Preprocessor” button in the Control Window should not be clicked by a user, since it will invoke the standard MAP Preprocessor.

## 5. SSHP Data Transfer

In order to keep the SAC-SMA model states up-to-date and to provide other necessary input data, the data transfer process moves data from the OFS database at an RFC to the

IHFS database at a WFO.  The transfer process is executed once per day, after the forecast model run at the RFC has completed.

### 5.1 Transferred Data Description

| Description | Data Source at RFC | Destination table at WFO in IHFS DB |
| --- | --- | --- |
| SAC-SMA state variables | OFS DB | SacSmaState |
| SAC-SMA parameters | OFS DB | SacSmaParams |
| MAPE adjustment values (12 monthly values) OR ET-demand curve (12 monthly values) | OFS DB | MonthlyValues |
| Prior Computed Runoff | OFS DB | FcstDischarge |
| MAPE Time Series (optional) | OFS DB | FcstOther |

### Figure 5.1 Data Transfer Process

### 5.2 Invocation Description

### 5.2.1 Sending Side (RFC)

1)  Once per day, cron at an RFC invokes run_SSHP_data_transfer, which extracts data from OFS flat files and sends an XML data file (via the AWIPS Message Handling System) to each WFO.  The WFOs, OFS segment ids, and WFO forecast points involved are configured in the control file:

/awips/hydroapps/whfs/local/data/app/sshp/SSHPTransfer.xml file.  See control file format below.

On the sending side, some intermediate files will have been created in:

/awips/hydroapps/whfs/local/data/sshp_transfer/ofs_extract_text

/awips/hydroapps/whfs/local/data/sshp_transfer/ofs_extract_xml

2) run_SSHP_data_transfer starts

java ohd.hseb.sshp.messaging.SshpDataTransferMgr

which then calls:

2.1) run_SSHP_ofs_extract (script to call sshp_ofs_extract.LX) on segment ids as defined in the SSHPTransfer.xml file.   This creates files in 	/awips/hydroapps/whfs/local/data/sshp_transfer/ofs_extract_text

2.1) ohd.hseb.sshp.messaging.XmlSacEncoder (within same Java process) which creates 	one xml data file per targeted WFO in /awips/hydroapps/whfs/local/data/sshp_transfer/ofs_extract_xml

2.3) run_SSHP_data_send

copies the extracted files to 						/awips/hydroapps/whfs/local/data/sshp_transfer/outgoing

invokes distributeProduct and sends the data files over the AWIPS WAN

via the Message Handling System (MHS)

### 5.2.2 Receiving Side (at each targeted WFO)

Upon receipt of a HYDRO_MODEL_DATA message, MHS invokes /awips/hydroapps/whfs/bin/process_hydro_model_data,  which copies the received data files to /awips/hydroapps/whfs/local/data/sshp_transfer/incoming

and uses ssh to invoke run_SSHP_data_decoder on a PX machine.  The script

run_SSHP_data_decoder invokes java ohd.hseb.sshp.messaging.XmlSacDecoder which then posts the data to the IHFS database.  After the data file has been processed, it is moved to /awips/hydroapps/whfs/local/data/sshp_transfer/ingest_xml..

### 5.3 Cleanup

The standard WHFS mechanisms for file and database cleanup are used with SSHP.

purge_files will delete old files from:

/awips/hydroapps/whfs/local/data/sshp_transfer/ingest_xml

/awips/hydroapps/whfs/local/data/sshp_transfer/ofs_extract_text

/awips/hydroapps/whfs/local/data/sshp_transfer/ofs_extract_xml

db_purge will delete old records from the following tables:

FcstDischarge

FcstOther

ArealObs

### 5.4 Example XML Data Transfer Control File:

standard location:

/awips/hydroapps/wfo/local/data/app/sshp/SSHPTransfer.xml

<?xml version="1.0" encoding="ISO-8859-1"?>

<SSHPTransfer>

<wfo>

<name>SJU</name>

<mhsId>SJU</mhsId>

<productId>KSJURRMALR</productId>

<fcstPoint>

<ofsSegmentId>RPOP4</ofsSegmentId>

<ihfsLocId>RPOP4</ihfsLocId>

<ihfsBasinId>RPOP4</ihfsBasinId>

<sendMapeTimeseries>NO</sendMapeTimeseries>

</fcstPoint>

<fcstPoint>

<ofsSegmentId>CAGP4</ofsSegmentId>

<ihfsLocId>CAGP4</ihfsLocId>

<ihfsBasinId>CAGP4</ihfsBasinId>

<sendMapeTimeseries>NO</sendMapeTimeseries>

</fcstPoint>

</wfo>

<wfo>

<name>ABC</name>

<mhsId>ABC</mhsId>

<productId>KABCRRMALR</productId>

<fcstPoint>

<ofsSegmentId>DEFV1</ofsSegmentId>

<ihfsLocId>DEFV1</ihfsLocId>

<ihfsBasinId>DEFV1</ihfsBasinId>

<sendMapeTimeseries>NO</sendMapeTimeseries>

</fcstPoint>

<fcstPoint>

<ofsSegmentId>GHIV1</ofsSegmentId>

<ihfsLocId>GHIV1</ihfsLocId>

<ihfsBasinId>GHIV1</ihfsBasinId>

<sendMapeTimeseries>NO</sendMapeTimeseries>

</fcstPoint>

</wfo>

</SSHPTransfer>

Element descriptions:

<SSHPTransfer> - mandatory root node

<wfo>  -  For each WFO to which the RFC wants to send data, there will be 1 WFO element.  It will contain the following sub-elements:   <name>, <mhsId>, <productId>, and <fcstPoint>.  There may be multiple <fcstPoint> elements.

<name> -  The abbreviated name of the WFO.

<mhsId> - The AWIPS Message Handling System Id for the WFO.

<productId> - The Product Id to use with distributeProduct.

<fcstPoint>  - The element that represents the information used to

pull data out of OFS and send it with the correct information to the WFO.

It contains the sub-elements:  <ofsSegmentId>, <ihfsLocId>, 					<ihfsBasinId>, <sendMapeTimeseries>.

<ofsSegmentId>  - Contains the name of the OFS segment from which data will be

extracted for this particular forecast point.

<ihfsLocId>  - Contains the location id of the forecast point as stored in the WFO’s

IHFS database.

<ihfsBasinId> - Contains the basin id associated with the forecast point as stored in the

WFO’s IHFS database.  The MAPE data will be associated with this basinId.  This should be the same basinId used for the MAP basin at the

WFO.

<sendMapeTimeseries> - contains values (YES or NO).  Determines if the data

extraction program will attempt to extract MAPE time series data.  If so, then there will be an MAPE time series sent along with Monthly Adjustment factors.   If not, then an MAPE demand curve will be sent.

Configuration Instructions:

Edit the file, putting in only the forecast points for which the RFC wants to extract data from OFS and send to the WFO (or back to the RFC, if the RFC is going to run SSHP).  Make sure that all of the XML elements are properly fill out, keeping in mind that each WFO has its own <wfo> element with potentially multiple <fcstPoint> subelements.

## 6.  Local SAC-SMA State Updater

### Figure 6.1 SAC-SMA State Updater

Although it is not recommended to use it, the SSHP subsystem includes a utility, run_SSHP_SAC_state_update, that may be run in the background.  It is useful only in cases in which the WFO is using the SAC-SMA model and either the RFC does not intend to send state updates to the WFO, or there is a temporary problem which is interrupting the provision of the daily update.   If the policy of the office is to execute this utility, it should be run daily.  In order for a forecast point’s SAC-SMA states to be updated locally, the checkbox labelled “Update Model States” in the SSHP Configuration Dialog must be checked and the preferred rainfall-runoff model must be “SAC-SMA”.  The local state updater will check the database for a state for each locally updateable (see above requirements) forecast point with a valid time that is not older than the number of hours (the default exporation hours value is 25 hours) encoded into the script.  If a site that is configured to be updated does not have a new enough state in the database, then the local state updater will run the SAC-SMA model in the background for the number of hours (the default hours forward value is -2) relative to the latest hour and save the state in the database.  No forecast will be saved.

There are currently no tokens for the expiration hours or the hours forward, so any customization must be done in the run_SSHP_SAC_state_update script itself.

## 7. System Setup

### 7.1 RFC Setup

For WFOs that are NOT going to use the SAC-SMA rainfall-runoff model, SSHP does not require any special data transfer.  The use of the API-MKC requires FFH data, generally delivered through SHEF.  The following describes what is necessary to set up the SAC-SMA data transfer.  More data transfer details are available in Section 5.

### 7.1.1 OFS Setup

In a standard configuration, the RFC will need to define, run, and maintain segments for the forecast points that are to be modelled at the WFO using the SAC-SMA rainfall-runoff model.  Data from these segments are to be transferred to the WFO.     Please see Appendix C – RFC Segment Definition Example, Appendix D – Science Background, and Appendix E – Calibration and State Maintenance for more details.

### 7.1.2 Data Transfer

The RFC will need to edit the data transfer control file: /awips/hydroapps/whfs/local/data/app/sshp/ SSHPTransfer.xml

For details on editing/creating this file, see Section 5.4.

The RFC will need to add an entry in their crontab file to execute /awips/hydroapps/whfs /bin/run_SSHP_data_transfer once per day after the OFS model run.

### 7.2 WFO Setup

### 7.2.1 Static Data Setup (for API-MKC and SAC-SMA)

The following tables must have entries properly defined in the IHFS database at the WFO.

Location – the basic table defining a location

Riverstat – preferably including the threshold runoff value

Unitgraph - 1 – hour unit hydrograph

Rating – includes an entry for each rating curve point

RatingShift  - should have 0 or 1 active shifts at a time

SSHPConfig  - see Adding an SSHPConfig record below

### 7.2.2 Data Generally Transferred from RFC

The following tables must have entries defined in the IHFS database at the WFO.	 Typically, this data will be sent from the RFC and posted to the database.

SacSmaState – state of SAC-SMA model

SacSmaParams –SAC-SMA  parameters

FcstOther – (optional)  - MAPE time series, uses physical element  = ‘EA’

MonthlyValues  - MAPE Monthly Values or adjustment factors, uses  						physical element  = ‘EA’

FcstDischarge  - Prior Computed Runoff time series - stored in uses physical element =  “QB”, dur = 1001 (1-hour),  and ts = “FZ”

### 7.2.3 Token Settings

In order to run the MAP Preprocessor automatically with the MPE/Fieldgen scripts, the sshp_invoke_map_preprocess token needs to be set to ON.  The default is ON..

### 7.2.4 Cron Job

If the WFO chooses to have SAC-SMA states updated locally, in the event that RFC state transfers fail or are not desired, the run_SSHP_SAC_state_update script should be initiated by cron once per day.  If the WFO receives RFC state transfers and is using this for backup purposes, then the time of the execution should be 1 hour or more after the expected data transfer.  This script may be started on the HP machines, but will then use ssh to execute on a px machine.  If it is started on a Linux machine, it will execute on that machine.

Note:  Starting run_SSHP_SAC_state_update will only have an effect on the SAC-SMA states stored in the database if:

1.  The location is configured in SSHPConfig to auto update AND

2.  The database does not contain a recent (< 25 hours old) record for the associated basin id  in 	the SacSmaState table.

### 7.2.5 Adding an SSHPConfig record

Each modeled site should be configured in the IHFS database.

To configure a location, from the SSHP Control Window, press the “Configure...” button.  The SSHPConfig Dialog will appear.  The SSHPConfig Dialog contains the settings as described below:

Location Id  - The key field.

Basin id  - The basin for which the areal data is to be used.

Model Preference – (Preferred Rainfall-Runoff Model)  -

Allowed values:  API-MKC or SAC-SMA

Determines what is the default rainfall-runoff model to start with for a particular location when starting the application.  This setting, along with the auto state update toggle,  is also used when running the SacStateUpdater, to determine the stations for which to check for recently updated model states.  The SacStateUpdater does not update states of locations which have a preferred rainfall-runoff model other that the SAC-SMA.

Use Adjustment?

Allowed values: (true or false)

Sets whether the model will have the adjustment feature toggled on when the AnalysisWindow is launched for this particular location id.

Adjustment Method

Allowed values:  DIFF or  RATIO.

Sets the interpolation method to use for the Forecast Adjustment feature.

Blending Hours  - Sets the number of hours for the default length of the blending portion of the Adjustment feature.  The length of blending hours can be changed in the AnalysisWindow.

SAC-SMA Settings

Update states Locally

Allowed values: (true or false)

If the preferred rainfall-runoff model is SAC-SMA, the option tells the SacStateUpdater to update the SAC-SMA model states in the event that the preferred source of state data has not successfully sent within 25 hours (a 1 hour grace time over 24 hours is allowed).  This option has no effect if the preferred rainfall-runoff model is other than SAC-SMA.

Data Source Preference

Allowed values: LOCAL or RFC

Indicates the preferred source of SAC-SMA state and parameter values.  This option has no effect if the preferred rainfall-runoff model is other than SAC-SMA.

Use ET-Demand Curve

Allowed values: (true or false)

A SAC-SMA setting which indicates to the model if it should use the monthly ET demand curve or (alternatively) use an MAPE time series for input.

## 8. Forecast Adjustment

### 8.1 Description

SSHP contains an automated forecast adjustment feature similar to the NWSRFS Adjust-Q operation.  The purpose of this feature is to bring forecasts in line with observed data.  The feature can be configured via the SSHP Config Dialog to be initially on or off (on a site-by-site basis) in the AnalysisWindow. Within the AnalysisWindow, the feature be toggled on or off manually.  In the Config Dialog, the interpolation method (DIFFERENCES or RATIOS) and the number of blending hours can be set.  The time windows for pairing (70 min) and interpolation (3 hours) are fixed.   In the AnalysisWindow, there is the ability to choose the last time to consider observations in the adjustment computation.

### 8.2 Details

The forecast adjustment feature has 3 types of adjustments that can be applied, pairing, interpolation, and blending.  Forecast values are first paired with observed points, leftover forecast values are interpolated between the 2 sets of paired values if within the time window for interpolation, and then any other values within the blending time window are blended forward and backward if possible.

### 8.2.1  Pairing

Forecast values and observed values are paired up if they are within the time window for pairing (see above Description) and are the best match.  The forecast values are corrected to equal the paired observed value.

### 8.2.2  Interpolation

Any non-paired forecast value adjustments may be interpolated if the previous and next paired values are within the interpolation time window.  The values are interpolated using either RATIOs or DIFFERENCES.   The ratio discussed is the ratio of the observed value and forecast value from a pair of observed and forecast values (see above).   If the RATIO technique is configured to be used for the site and the both ratios (of the observed and forecast values in each pair) are less than or equal to 5.0 and the difference between the two ratios is less than or equal to 2.0, an interpolated ratio will be used to adjust the original forecast value.  Otherwise, an interpolated difference will be used to adjust the original forecast value.

### 8.2.3  Blending

When a forecast value cannot be paired with an observed value and it cannot be interpolated (either because of a lack of a previous or later pair of values, or the two pairs of values are too far apart in time), then blending is attempted.  If available, the adjustment value for the previous pair of observed and forecast values is applied in the forward direction with a linear fade-out time that is set in the user interface and is called blending hours.  The adjustment amount reduces to zero in blending hours.   The same adjustment is applied in the reverse direction if a value has not been paired or interpolated and it has a pair of observed and forecast values that occurs later in time than the forecast value.  This is known as a backward blend.  Generally, though, at the end of a forecast, there are no observed values and so those forecast values are blended forward only.

# Appendix A:    Directories and Files

### 1. Directories and File Locations

### 1.1 Application Scripts and Executable Files

directory:  /awips/hydroapps/whfs/bin

run_SiteSpecific

run_SSHP_data_transfer

run_SSHP_data_decode

run_SSHP_data_send

run_SSHP_MAP_preprocess

run_SSHP_ofs_extract

run_SSHP_SAC_state_update

process_hydro_model_data

SiteSpecific.jar

sshp_ofs_extract.LX

### 1.2 Log Files

directory:  /awips/hydroapps/whfs/local/data/log/sshp

MAPPreprocessor.log

MAPPreprocessor.stdout.log

MAPPreprocessor.stdout2.log

SSHP.log

SacStateUpdate.log

SacStateUpdate.stdout.log

SshpDataTransferMgr.log

SshpDataTransferMgr.stdout.log

SshpDataSender.log

SacXMLDecoder.log

### 1.3 Application Setup Files

directory:  /awips/hydroapps/whfs/local/data/app/sshp

SSHPTransfer.xml

### 1.4 Data Transfer Directories

The following directories exist at the RFC and the WFO.  An RFC may wish to send the extracted OFS to itself, in which case, the directories labelled “applies to WFO” will also apply to the RFC.

/awips/hydroapps/whfs/local/data/sshp_transfer

Applies to RFC:

/awips/hydroapps/whfs/local/data/sshp_transfer/ofs_extract_text

/awips/hydroapps/whfs/local/data/sshp_transfer/ofs_extract_xml

awips/hydroapps/whfs/local/data/sshp_transfer/outgoing

Applies to WFO:

/awips/hydroapps/whfs/local/data/sshp_transfer/ingest _xml /awips/hydroapps/whfs/local/data/sshp_transfer/incoming

### 2. Script and Executable Descriptions

SiteSpecific.jar - contains all of the Java classes for the application and the other processes.

run_SiteSpecific  - starts current version of the application

run_SiteSpecific_API  - starts old version of the application

run_SSHP_data_decode  - normally called from process_hydro_model_data

run_SSHP_data_transfer - main script for starting the data transfer process from RFC to WFO

run_SSHP_MAP_preprocess - invoked by MPE/Fieldgen scripts

run_SSHP_ofs_extract - invokes sshp_ofs_extract.LX

run_SSHP_SAC_state_update - Calculates local updates of SAC-SMA states for sites that are configured to be updated locally.    Useful when RFC state updates not available

run_SSHP_data_send - sends processed XML file to WFO via MHS.Uses distributeProduct.

sshp_ofs_extract.LX  - uses OFS routines to extract data from OFS flat file database

process_hydro_model_data - invoked by AWIPS Message Handling System (MHS) upon 				message receipt

# Appendix B – SSHP AppsDefaults Tokens

sshp_java_process_host    =  px1f

This token contains the host name of the machine on which the MAPPreprocessor,

the SacXmlDecoder, and the SacStateUpdater will run.

sshp_invoke_map_preprocess  =  ON

This token is a switch to determine whether or not to run the SSHP MAPPreprocessor when the MPE/Fieldgen scripts (run_mpe_fieldgen and rerun_mpe_fieldgen) are invoked.  If this is set to ON (default is ON), the SSHP MAPPreprocessor will be initiated in the background.  If run_SSHP_MAP_preprocess is executed on the HP machines, it will use ssh (secure shell) to invoke run_SSHP_MAP_preprocess on a Linux machine.

rfcwide_xmrg_dir = /awips/hydroapps/precip_proc/local/data/mpe/qpe

This token identifies the directory location for the gridded best estimate QPE files to be used by the MAPPreprocessor.

sshp_fcst_ts token = FZ

This controls the default value of the forecast’s type/source value in the Save Forecast Height/Discharge Dialogs.

sshp_initial_forecast_length  = 24

This token sets the default length in hours of a forecast for all forecast points.   The “live” value can be changed in the Analysis Window.

sshp_max_forecast_length =  120

This token sets the maximum length of a forecast for all forecast points.   This sets the maximum value of the forecast length in hours available to the user of the user interface.

sshp_sac_update_expiration_hours = 25

After the SAC-SMA model state is older than this number of hours, the SAC State Updater will

run the model and save the state.

sshp_sac_update_hours_forward = -2

When the SAC State Updater runs, it will run from the time of the last valid state to the current time plus the value of this token.  In this example, since the value is negative, the time will actually be 2 hours before the current time rounded back to the top of the hour.

The following are tokens defined in national .Apps_defaults (all are directories). DO NOT CHANGE.

local_data_sshp_dir       : $(whfs_local_data_dir)/sshp_transfer

sshp_control_dir          : $(whfs_local_data_dir)/app/sshp

sshp_ofs_extract_text_dir : $(local_data_sshp_dir)/ofs_extract_text

sshp_ofs_extract_xml_dir  : $(local_data_sshp_dir)/ofs_extract_xml

sshp_ingest_xml_dir       : $(local_data_sshp_dir)/ingest_xml

sshp_incoming_dir         : $(local_data_sshp_dir)/incoming

sshp_outgoing_dir         : $(local_data_sshp_dir)/outgoing

sshp_log_dir              : $(whfs_log_dir)/sshp

# Appendix C – RFC Segment Definition Example

Provided By SERFC, MAY 2004

___________________________________________________________

For the SAC-SMA Site Specific Model:

The INFL., SSTG, QINE, SMZC and ROCL time series were all set to be OUTPUT.

Filesize and Filecrat will have to be reviewed to assure that these time series can be output.

1-hr Unit hydrographs will have to be defined and sent to the WFO.

Rating Curves will also have to be supplied to the WFO.

___________________________________________________________

Here is an example of a segment that was defined on a 1-hr interval:

RESEGDEF

IDENTIFIER  CAGP4        18.24     66.01

TITLE     RIO GRANDE DE LOIZA

UPSTREAM

DOWNSTREAM

DEF-TS

CAGP4      MAPX    1            INPUT         FPDB

CAGP4      MAPX

CAGP4      INFW    1            OUTPUT        FPDB

CAGP4      INFW     18.24     66.01     GRANDE DE LOIZA-CAGU

CAGP4      SQIN    1            INTERNAL

CAGP4      STG     1            INPUT         FPDB

CAGP4      STG

CAGP4      QIN     1            INTERNAL

CAGP4      SSTG    1            OUTPUT        FPDB

CAGP4      SSTG     18.24     66.01     GRANDE DE LOIZA-CAGU

CAGP4      QINE    1            OUTPUT        FPDB

CAGP4      QINE     18.24     66.01     GRANDE DE LOIZA-CAGU

CAGP4      SMZC    1            OUTPUT        FPDB

CAGP4      SMZC     18.24     66.01     GRANDE DE LOIZA-CAGU

CAGP4      ROCL    1            OUTPUT        FPDB

CAGP4      ROCL     18.24     66.01     GRANDE DE LOIZA-CAGU

END

SAC-SMA     CAGP4

GRANDE DE LOIZA-CAGU         1  CAGP4    MAPX       CAGP4    INFW

0  CAGP4     CAGP4                 1    1

1.0001.000 15.0 15.00.3000.0400.3000.000    00.000

95.0 3.00  90. 80.0 170.0.225.01200.1000.300 0.00

3.003.003.003.403.403.804.204.204.003.603.303.00

3.1  0.0  73.  0.1  53.  60.    0

FFG         CAGP4

CAGP4    AREA CAGP4               0 0.00 0.00

CAGP4    SAC-SMA   CAGP4

CLEAR-TS

CAGP4    SQIN    1

UNIT-HG     CAGP4

GRANDE DE LOIZA-CAGU           89.8   16     CARRY ENGL     0.000

CAGP4    INFW    1  CAGP4    SQIN    1

6900.0   10000.0   11000.0   10000.0    8000.0    4000.0    2200.0

1500.0    1220.0     900.0     750.0     500.0     400.0     300.0

200.0     100.0

0.0007    0.0007    0.0007    0.0007    0.0007    0.0008    0.0008

0.0007    0.0007    0.0008    0.0008    0.0008    0.0007    0.0014

0.0009

STAGE-Q     CAGP4B

GRANDE DE LOIZA-CAGU  CAGP4            1 RDCO

CAGP4    STG     1  CAGP4    QIN     1

1.37        2.     -0.04         0

ADJUST-Q    CAGP4

GRANDE DE LOIZA-CAGU    1    0    0

CAGP4      QIN     1

CAGP4      SQIN    1

CAGP4      QINE

500

1

STAGE-Q     CAGP4C

GRANDE DE LOIZA-CAGU  CAGP4            2 RDCO

CAGP4    SSTG    1  CAGP4    QINE    1

1.37        2.      0.00         0

PLOT-TUL    CAGP4

1    1  101    0  100    1    1    5    3    I    -    0    0    0

0   25    F    U    M  CAGP4       0    0    0

XMP   SSTG     QIN

CAGP4     MAPX LIST      F5.2,       1

CAGP4     SSTG LIST      F7.1,       1

CAGP4     QIN  PLOT O                1

CAGP4     QINE BOTH A    F9.0,       1

CAGP4     SQIN PLOT S                1

END

STOP

# Appendix D – Science Background

Sacramento Model and the Site Specific Hydrologic Prediction Tool

Mike Smith

February 6, 2004

- Overview

The Sacramento Soil Moisture Accounting Model (SAC-SMA) is being added to the Site Specific Hydrologic Prediction tool to complement the existing Antecedent Precipitation Index (API) rainfall/runoff model.  In SSHP, the SAC-SMA will be run at a 1-hour time step.  The parameters used by the basins need to be created for that time step and the actual forecast basin size.  The goal of this approach is to apply the SAC-SMA at the spatial and temporal scale for which the forecasts are to be issued. This is to avoid the documented scale sensitivities of the both the SAC-SMA model parameters and states and the resulting problems of modeling a ‘parent’ basin in OFS at a 6-hour time step and using those parameters and states to run the SSHP at an interior sub-basin at an hourly time step.  The model will be executed continuously so as to have the best estimate of the initial states at run time.

- Scope

This document covers aspects of the SAC-SMA application only and is not intended to describe all functional components of the SSHP tool.

3. Model Set-up, Parameterization, and Calibration

We identify two cases for the use of the SAC-SMA version: gaged and ungaged basins. However, it is anticipated that the predominant usage of this application will be in gaged basins and run at a one-hour time step.

3.1 Gaged basins.

In this use case, the model is applied to a watershed that is gaged and may or may not coincide to a basin being forecasted by the RFC using the Operational Forecast System (OFS), usually at a 6-hour time step. Here, there is the possibility that the SAC-SMA and unit hydrographs (UHG) can be calibrated against observed streamflow data.  Typical calibration procedures can be applied to derive the optimum values of the SAC-SMA parameters.

3.1.1 SAC-SMA Parameterization

Initial values of the SAC-SMA for the SSHP application can be obtained from several sources. First, the RFC can apply calibrated SAC-SMA parameters from the corresponding OFS basin if the two coincide or if the basin to be modeled is a sub-basin of the OFS basin.  Or, initial parameters may be defined using the hydrograph analysis techniques described in the calibration manual developed by Eric Anderson (Anderson, 2002). Finally, the user can select the initial SAC-SMA parameter estimates developed by Koren et al. (2000) and available via the Calibration Assistance Program (CAP).

3.1.2 Unit Hydrograph

In the application to gaged basins, a UHG can also be derived and calibrated. (The user is referred to Chapter 7-6 in Anderson, 2002 for a discussion of UHG derivation). An initial UHG can be developed through traditional analysis of observed hydrographs. Or, the user can adopt the UHG from the OFS basin and make the required adjustments for any changes in drainage area or time step (e.g., S-Curve analysis). The UHG derivation options within IHABBS may also be used.  An emerging and promising approach is to use a UHG derivation tool developed as part of the variational assimilation research being performed in the Hydrology Lab. At the time of this writing, this tool is being tested at several RFC’s.

3.1.3 Calibration

Given that the SSHP is applied to a gaged basin, parameter calibration can take place. The Manual-Expert calibration steps described in detail in Anderson (2002) should be followed to calibrate the SAC-SMA parameters and the UHG. A calibration time series of precipitation can be derived from radar data using the MAPX calibration preprocessor and basin boundary information. The calibration MAP preprocessor may be used to derive a one-hour MAP time series if the reporting rain gage density is sufficient for such an area.

3.2 Ungaged Basins

In this use case, the SAC-SMA SSHP model is applied to an ungaged location and cannot be calibrated. However, the model is set up and run continuously at the spatial and temporal scale for which forecasts are to be issued.

3.2.1 SAC-SMA Parameterization

Here, it is recommended that the initial soils-based parameters derived by Koren et al. (2000) and available via CAP be used.  Given the basin boundary coordinates, CAP may be used to derive spatially-lumped SAC-SMA parameters.

3.2.2 Unit Hydrograph

For an ungaged application, the UHG for the SAC-SMA model can be derived using synthetic methods in IHABBS or by appropriately scaling a UHG from a downstream point.

4. Model States and Execution

In either the gaged or ungaged application, the SAC-SMA is run continuously.  Precipitation estimates that are quality controlled are used to execute the model in order to maintain the best possible states.  At the time of forecasting, the user obtains the most recent saved state variables and observed rainfall to run the model up to the current time. The SSHP tool is then used with user-defined forecast precipitation to generate forecasts into the future. Depending on the time of day, it may not be possible to quality control the observed precipitation data before running the model from the last carryover date to the current time. In such cases, the SAC-SMA can be re-run from the same carryover date once quality controlled precipitation estimates are available so as to maintain the best possible state variables.

A future enhancement to the SAC-SMA SSHP tool would be to incorporate the variational assimilation method to develop the most appropriate state variables.  Current research in HL shows that variational assimilation is very promising.

5.  References

Anderson, E.A., 2002. Calibration of Conceptual Models for Use in River Forecasting. Hydrology Lab, available at: http://www.nws.noaa.gov/oh/hrl/calb/calibration1102/main.htm

Koren, V., I., Smith, M., Wang, D., and Zhang, Z., 2000. Use of soil property data in the derivation of conceptual rainfall-runoff model parameters. Preprints: 15th Conference on Hydrology, Long Beach, CA, American Meteorological Society, 10-14 January, 103-106.

# Appendix E – Calibration and State Maintenance

WFO use of the Sacramento model introduces issues that do not apply to use of the API models.  The major issues are those of parameter calibration and model state maintenance.  Parameter calibration is an issue because SSHP will be running the Sacramento model at a 1-hour time step.  Studies of the Sacramento model using different spatial and temporal scales indicate that the 6-hour parameters for a large parent basin modeled at an RFC are not necessarily transferable to a smaller, interior basin targeted for hourly simulations at a WFO using SSHP.  To avoid uncertainties and problems caused by crossing time/space scales, the SAC-SMA runs in continuous mode (as is done in OFS) at the space scale of the target basin with a 1-hour time step.  The following table displays some options for addressing this issue.

### 1. Model Parameter Calibration Options

| Option Name | Steps To Obtain Model Parameters for SSHP Basin |
| --- | --- |
| Pure Calibration | 1. Calibrate the SSHP basin for 1 hour time step. 2. Develop 1-hour Unit Hydrograph for the SSHP basin. |
| Partial Calibration | 1. Calibrate the parent basin for 1-hour time step operation. 2. Generate a priori parameters with CAP for both the parent and child basins. 3. Apply a ratio of the parameters obtained from CAP to the calibrated parent basin’s parameters to obtain parameters for the SSHP (child) basin. 4. Develop a 1-hour Unit Hydrograph for the SSHP (child) basin. |
| No calibration | 1. Generate a priori parameters with CAP for the SSHP basin. 2. Develop a 1-hour Unit Hydrograph for the SSHP basin. |

Issues regarding model state maintenance also appear with the usage of the Sacramento model at a WFO.  The various options differ in the degree of participation and interaction between RFC and WFO.  In the RFC- managed options, the model states can be updated using RFC information, and this requires more RFC involvement.  The WFO-managed options put the responsibility for state management at the WFO.  This option requires that the model at the WFO be run for each hour, so that the state variables remain current.  A possible near-future upgrade to the SSHP in the state maintenance area is the addition of VAR functionality which would continuously adjust state variables to optimize the model output.  This would create another type of WFO-managed state maintenance.  Presumably, this version could recover faster from out-of-date model state information.

### 2. Model State Maintenance Options

| Option Name | Option Description |
| --- | --- |
| RFC – managed with OFS | RFC models the same basin at 1-hour time step in OFS and regularly updates WFO’s model state stored at the WFO. The SSHP would update states locally at the WFO in between RFC updates. Those local state updates could be overridden by an RFC state update. |
| RFC –managed without OFS | RFC models the same basin at 1-hour time step using Site Specific at the RFC and regularly updates WFO model state. The SSHP updates state locally at the WFO in between RFC updates. Those local state updates could be overridden by an RFC state update. |
| RFC -managed with VAR (future?) | RFC models the same basin at 1-hour time step using Site Specific at the RFC and regularly updates WFO model state. The RFC uses VAR and sends hourly state updates to the WFO. |
| WFO -managed | The WFO runs the model for each hour and maintains its own state. |
| WFO-managed with VAR (future?) | The WFO runs the model for each hour and maintains its own state. VAR adjusts the state parameters regularly to optimize forecast. |

As shown above, the SSHP application is capable of maintaining its own state in the IHFS database using newly incorporated tables, but this is not expected to be the standard mode of operation.    SSHP has the ability to have its model state and even model parameters be updated with data provided by the RFC.  The use of this RFC-to-WFO update capability is expected to be the most common mode of operation.  Updates from RFC to WFO are handled by an automated process (running at the RFC) to extract data from OFS and send the data (via the AWIPS WAN) to the WFO.  At the WFO, the updated model state and model parameters (if changed) are stored in the IHFS database.   The prior computed runoff is stored. Also stored are the MAPE monthly adjustment values or ET-demand curve, and the MAPE time series (if applicable).

# Appendix F – SSHP Database Tables

1.  SSHPConfig

Holds configuration data for model configuration by forecast point.

TABLE DEFINITION:

lid             char(8)       		not null,

basin_id        char(8)        		not null,

postingtime     datetime year to second 	not null,

model_pref      char(20)    			not null,

auto_process    char(1)          		not null,

source_pref     char(20)    			not null,

use_static_evap char(1)          		not null,

use_blend       char(1)				not null,

blend_method    char(20)                  not null,

blend_hours	    integer				not null

lid

Location Id of the forecast point.

basin_id

Id of the basin.

postingtime

Time of posting of this record

model_pref

The rainfall runoff model that is preferred for SSHP startup

auto_process

Y or N to update states locally if RFC update not available or desired.

source_pref – (“RFC” or “LOCAL”)

If  auto_process is “Y”, the local SAC-SMA state updater checks for recent state updates from the preferred source.

use_static_evap

If “Y” then the ET-DEMAND curve is used, otherwise the MAPE time series will be used.

use_blend

The Forecast Adjustment feature default value for the  AnalysisWindow.

The name should be changed to use_adjustment.

blend_method

The interpolation method of the Forecast Adjustment feature.

blend_hours

The number of hours for the blend portion of the Forecast Adjustment feature.

2. MonthlyValues

Used in SSHP to hold the daily mean (by month) ET-Demand curve values or adjustment factors to the MAPE time series.

TABLE DEFINITION:

lid             char(8)   not null,

pe              char(2)  not null,

dur             smallint           not null,

ts              char(2)  not null,

extremum        char(1)  not null,

adjustment      char(1)     not null,

postingtime     datetime year to second  not null,

jan_value       float not null,

feb_value       float not null,

mar_value       float not null,

apr_value       float not null,

may_value       float not null,

jun_value       float not null,

jul_value       float not null,

aug_value       float not null,

sep_value       float not null,

oct_value       float not null,

nov_value       float not null,

dec_value       float not null

3. SacSmaState

Used in SSHP to hold the updates of the SAC-SMA model states.

TABLE DEFINITION:

basin_id        char(8)   not null,

source          char(20)  not null,

validtime       datetime year to second not null,

basistime       datetime year to second not null,

postingtime     datetime year to second not null,

uztwc           float not null,

uzfwc           float not null,

lztwc           float not null,

lzfsc           float not null,

lzfpc           float not null,

adimc           float not null

4.  SacSmaParams

Used in SSHP to hold the updates of the SAC-SMA parameters.

TABLE DEFINITION:

basin_id        char(8)   not null,

source          char(20)  not null,

validtime       datetime year to second not null,

postingtime     datetime year to second not null,

uztwm           float not null,

uzfwm           float not null,

uzk             float not null,

pctim           float not null,

adimp           float not null,

riva            float not null,

zperc           float not null,

rexp            float not null,

lztwm           float not null,

lzfsm           float not null,

lzfpm           float not null,

lzsk            float not null,

lzpk            float not null,

pfree           float not null,

rserv           float not null,

side            float not null,

peadj           float not null,

pxadj           float not null,

efc             float not null

5.  Other Tables

The following are well-established IHFS tables used by SSHP.  Please refer to IHFS database documentation for more details.

ContingencyValue

Input : Used by  API-MKC for FFH values.

FcstDischarge

Input: Prior Computed Runoff time series. Basin ID is stored as the lid.

Output: Forecast discharge time series for forecast point.

FcstHeight

Output: Forecast height time series for forecast point.

Height

Input:  Used for observed height time series and to calculate baseflow for API-MKC.

FcstOther

Input:  MAPE time series.  The basin id is stored as the lid.

ArealFcst

Input:  Basin QPF time series.  The basin id is stored as the lid.

ArealObs

Input:  Processed 1-hour basin MAP QPE time series.  The basin id is stored in the lid.

Unitgraph

Input: Contains Unit hydrograph.

Rating

Input: Contains raw (unshifed) rating curve data points.

RatingShift:

Input:  Contains records for rating shifts.

LineSegs:

Input:  Used by MAP Preprocess to compute basin-average QPF.

IngestFilter:

Input and Output:   SacXmlDecoder adds a record to allow for data ingest if a record 		does not exist 	for a particular forecast point.

# Appendix G - Unit Hydrograph Editor Guide

## 1. Introduction

In OB5, the Site-Specific Hydrologic Predictor added the Unit-Hydrograph Editor.

This editor is also available through HydroBase.   During the OB5 system release, the IHFS table UnitGraph was changed to add a column and alter its primary key.  This document describes these changes and some of their impacts.

## 2.   Table Modification

The column "model" (char(10))  was added to UnitGraph before the existing column "dur".  For previously existing rows, the "model" column is initially set to "ANY". The primary key was changed to (lid, area_id, model, dur, ordinal) and and index was added (lid, area_id, model, dur).  This means that a given location might be associated with more than one area.  Also, the same lid, area_id combination may have more than one unithydrograph associated with it.  There might be a unithydrograph than is calibrated for the API-MKC and one that is calibrated for the SAC-SMA rainfall-runoff model.

## 3.   Data Contents and Usage

### 3.1 UnitGraph Table in IHFS

| Column Name | Key Column? | Type | Description | Sample Content |
| --- | --- | --- | --- | --- |
| lid | YES | Char(8) | Handbook 5 Location Id | BLUO2 |
| area_id | YES | Char(8) | Area (Basin) Identifier | BLUO2H or BLUO2 (may be same as lid) |
| model | YES | Char (20) | rainfall-runoff model for which this may be used | ANY or API-MKC or SAC-SMA |
| dur | YES | integer | duration code |  |
| ordinal | YES | integer | time period number |  |
| discharge | NO | 8 byte float | discharge value in CFS |  |

The SSHP uses the data in the UnitGraph table.   In order to be used by SSHP, each forecast point must be configured in SshpConfig and the lid, basin_id combination found there must match the lid, area_id found in UnitGraph.  The contents of the new “model” column (as entered from this editor) may be “ANY”, “API-MKC”, or “SAC-SMA”.   The SSHP will find the closest match available for use with the selected rainfall-runoff model. “ANY” is a wildcard and will be used if the specific model type is not available.   “ANY” is the value to which the “model” column was automatically set in the OB4 to OB5 database conversion.  This way, the user could continue to use the SSHP without having to enter new rows in the UnitGraph table.

## 4. Editing

In either HydroBase or SSHP, call up the Unit Hydrograph Editor for a particular

location id (lid).   Follow the appropriate steps below to alter the unit hydrograph in WORKING MEMORY.     After you are satisfied with your changes, press the Save button, or your changes will be lost when you close the editor!

### 4.1 Adding A Record In Memory

To add a record, fill in the area id, model, duration, ordinal, and discharge text boxes or option menus.  Press Add button.   If the ordinal already exists for that unit hydrograph, an error message dialog will appear.

### 4.2 Removing A Record In Memory

To remove a record, click on the single record to remove and then press the Remove button.  A confirmation window will appear, press Yes to remove, No to keep the record.

### 4.3 Modifying A Record In Memory

To modify a record, change the discharge value and press the Modify button.  No confirmation dialog will appear and the discharge value will have been changed.

### 4.4 Saving Changes To Database

All operations on a record-by-record basis (adding, removing, modifying records) are performed only IN MEMORY ONLY.  To save the changes to the database, press the Save button.  When any of the records is modified,  the text on the Save  button changes to remind the user that changes will need to saved to be made permanent.

### 4.5 Deleting Unitgraphs From Database

To delete an entire unit hydrograph from the database, in the tabular section, click on a record that belongs to the unit hydrograph, then click on the Delete button.  A confirmation dialog will appear.  The confirmation dialog will include the data values that describe the unit hydrograph to be deleted.  Press YES to confirm, NO to decline.

### 4.6 Importing and Exporting Hydrographs

Importing a hydrograph is useful when the user wants to avoid using the editor to enter records one at a time. If the the file to import conflicts with what is already in the database, or is otherwise faulty, an error dialog will appear.   If unsure of the valid format of the UHG file, enter a small unit hydrograph and export it.  The user can export a hydrograph to a file by pressing the Export button. Exported files may be modified by hand and then imported into the database by pressing the Import button.

### 4.7 Sorting

In order to make editing easier, the rows of the tabular section can be sorted by clicking on the column header.  Clicking again on a column header reverses its sort order from ascending to descending or vice versa.   For example, to sort by discharge, click on the word “Discharge” at the top of the column.  Click again to reverse the sort order.

The program remembers previous requests to sort by a particular column and honors those requests when possible.  To order by ordinal, model, and area id at the same time, click on the column headers for ordinal, model, and area id in that order.

### 4.8 Viewing

To the right of the tabular section, is the graphical section.  To select the unit hydrograph to graph, click on the unit hydrograph descriptor in the small table below the graph.  To select more than one unit hydrograph, hold down the shift key and click on a descriptor.

The graphical section displays what is IN MEMORY, not necessarily what is in the database.   Remember to SAVE unit hydrographs that you want to keep.

### 4.9 Screen Shot