| BUS SAFETY INSPECTION CHECKLIST |  | 10. PRE-USE INSPECTION | ٱREJECTED |
| --- | --- | --- | --- |
|  |  | MILES: ___________ DATE__________ TIME________ |
| 1. INCIDENT NAME/NUMBER | 2. ORDER/REQUEST NUMBER |  | INSPECTOR NAME:________________________________ TITLE__________________ PRINT |
| 3. OWNER/VENDOR NAME & COMPANY NUMBER |  | ٱACCEPTED |
| 4. AGREEMENT, PO, CONTRACT NO. | 5. EXPIRES |  | MILES: ___________ DATE__________ TIME________ |
| 6. MAKE | 7. MODEL, TYPE |  | VENDOR SIGNATURE:______________________________ TITLE__________________ PRINT |
| 8. SERIAL NO./VIN | 9. LICENSE NO. |  | INSPECTOR NAME:__________________________________ TITLE__________________ PRINT |
| * Safety Items, Do Not Accept Until Repaired | Pre-Use | Release |  | Bus Specialty Requirements | Yes | No |
|  | Yes | No | Yes | No |  |  |  |  |
| 1. DOT inspection in previous 12 mths when required * |  |  |  |  |  | 1. PERSONAL PROTECTIVE EQUIPMENT (PPE): Flame Resistant Clothing, Boots, Gloves, Hardhat & Fire Shelter. |  |  |
| 2. Gauges and lights * |  |  |  |  |  |  |  |  |
| 3. Seat belts * |  |  |  |  |  |  |  |  |
| 4. Glass and mirrors * |  |  |  |  |  | 2. SAFETY CAGE: Nets WILL NOT be accepted. |  |  |
| 5. Wipers and horn * |  |  |  |  |  |  |  |  |
| 6. Clutch pedal: proper adjustment, ¾” free travel |  |  |  |  |  | 3. EMERGENCY DOORS: Marked with 1-inch letters and identified with a red electric lamp that works when lights are needed. 393.92 1. No emergency exit sign over rear door (if cage in rear) 2. If required roof hatch minimum size is 13”X17” 3. All exits shall be properly labeled |  |  |
| 7. Cooling system: check radiator and hoses |  |  |  |  |  |  |  |  |
| 8. Oil level/condition: full and clean |  |  |  |  |  |  |  |  |
| 9. Battery: check for corrosion, loose terminals, tie downs |  |  |  |  |  |  |  |  |
| 10. Fuel system * |  |  |  |  |  |  |  |  |
| 11. Electrical system: alternator and starter working |  |  |  |  |  |  |  |  |
| 12. Engine running: check for knocks and leaks |  |  |  |  |  |  |  |  |
| 13. Transmission: check for leaks |  |  |  |  |  | 4. DRIVE SHAFT PROTECTION: Must have at least one guard or bracket at the end of the shaft that would prevent whipping of the shaft in the event of failure. |  |  |
| 14. Steering (See specialty items) * |  |  |  |  |  |  |  |  |
| 15. Tie rods, ball joints: check for looseness or bent * |  |  |  |  |  |  |  |  |
| 16. Lubrication: check for dry fittings |  |  |  |  |  |  |  |  |
| 17. Brakes (See specialty items) * |  |  |  |  |  | 5. EXHAUST SYSTEM: Gas Powered Buses: Tailpipe will exit at or within 6” forward of the rear most part of the bus. Diesel Buses: Tailpipe will exit within 15” of the rear most part of the bus or to the rear of all doors or windows designed to be opened except windows designed to open solely as emergency exits 393.83 No exhaust leaks will be tolerated, no temp repairs. |  |  |
| 18. Drive line/U-joints: check for looseness |  |  |  |  |  |  |  |  |
| 19. Springs and shocks * |  |  |  |  |  |  |  |  |
| 20. Differential: check for leaks |  |  |  |  |  |  |  |  |
| 21. Exhaust system (See specialty items) * |  |  |  |  |  |  |  |  |
| 22. Frame * |  |  |  |  |  |  |  |  |
| 23. Tire and wheels: ¼” front, 3/16” rear tread required * |  |  |  |  |  |  |  |  |
| 24. Accessories: jack, lug wrench, mounted spare |  |  |  |  |  | 6. SPARE TIRE: Full size, mounted on wheel required on all buses: tire must be secured. |  |  |
| 25. Body and interior condition: describe & locate damage on back side of form |  |  |  |  |  |  |  |  |
|  |  |  |  |  |  | 7. STEERING SYSTEM: 393.209 See table in CFR book for maximum steering lash allowed. Gear box, u-joints, ball joints and tie rods must be in good condition. Power steering systems will NOT have ANY leaks. Belts in good condition, steering wheel spokes may not be cracked or missing. |  |  |
| 26. Emergency Equipment required:___Fire Extinguisher ____Spare fuses ____Reflectors ____Chock Blocks * |  |  |  |  |  |  |  |  |
| 27. Operator(s) properly licensed: State______ License No.________________ Class_____ Endorsements________Med Cert Exp Date____________ |  |  |  |  |  |  |  |  |
|  |  | 8. BRAKES: Parking brake must hold, air brakes must meet front protection regs and have low air warning devices and working air pressure gauge. Slack adjusters must be properly adjusted. Brake lining will conform to specs. NO leaks of air or fluid allowed. |  |  |
| 11. RELEASE INSPECTION MILES_________________ DATE___________________ TIME________________ VENDOR SIGNATURE:________________________________TITLE______________________________ INSPECTOR NAME:_____________________________________TITLE_______________________________ Print |  |  |  |  |
|  |  | COMMENTS: |