| Livestock Manure Storage Assessment Worksheet |
| --- |
| Ground & Surface Water Contaminants - Nutrients, Organics & Pathogens |
| Rating Item | Low Risk 4 Points | Low-Mod Risk 3 Points | Mod-High Risk 2 Points | High Risk 1 Point | Score |
| 1. No on-farm storage facilities | Wastes hauled off farm for proper storage and disposal |  |  | Daily spreading of livestock wastes |  |
| 2. On-farm storage Manure stack and/or | Manure stack covered; on impermeable surface; rainfall and runoff diverted; built to NRCS standards. | Manure covered; on low permeable soil; rainfall and runoff diverted. | Manure partially covered; on slightly permeable soils; some runoff collected. | Manure not covered; runoff not collected. |  |
| Liquid/Slurry storage | Concrete, clay lined, or other liquid tight design; designed and built to NRCS standards; properly maintained; no cracks and leaks. | Earthen structure built to NRCS standards and properly maintained. | Not designed to NRCS standards; on slightly permeable soils; poorly maintained, some evidence of cracks and leaks. | Not designed to NRCS standards; on permeable soils; not maintained; leaks and cracks. |  |
| 3. Storage volume | Not full at end of rainy season; if liquid/slurry adequate capacity to hold 25-year, 24-hour storm; solids removed to avoid loss of storage capacity. | Not full at end of rainy season; if liquid/slurry not adequate capacity to hold 25-year, 24-hour storm. | Storage facility requires occasional emptying during the rainy season; if liquid/slurry not adequate capacity to hold 25-year, 24-hour storm. | Storage facility requires regular emptying during the rainy season; if liquid/slurry not adequate capacity to hold 25-year, 24-hour storm. |  |
| 4. Storage location | Manure stack or earthen pond located more than 500 feet from well, stream, pond, or drainageway. Or Liquid/slurry storage located more than 200 feet from well, stream, pond, or drainageway or has emergency containment dike for accidential spills or leaks. | Manure stack or earthen pond located between 250-500 feet from well, stream, pond, or drainageway. Or Liquid/slurry storage located betwen 100-200 feet from well, stream, pond, or drainageway | Manure stack or earthen pond located less than 250 feet downslope from well, stream, pond, or drainageway. Or Liquid/slurry storage located more than 100 feet downslope from well, stream, pond, or drainageway | Manure stack or earthen pond located less than 250 feet upslope from well, stream, pond, or drainageway. Or Liquid/slurry storage located 100 feet from upslope well, stream, pond, or drainageway |  |
| Livestock Waste Storage Rating for Ground & Surface Waters | Accumulative Score (sum of above ratings) |  |
|  | Average Score (sum of ratings / number of items rated) |  |
| Overall Risk Rating- |  |

Ratings:	3.6-4=Low risk, 2.6-3.5=Low to moderate risk, 1.6-2.5=Moderate to high risk, 1-1.5=High Risk

Source: Modification of Oregon Home*A*Syst, EM 8546, Worksheet #7, Livestock Waste Storage

| Livestock Yard Management Assessment Worksheet |
| --- |
| Ground & Surface Water Contaminants – Nutrients, Organics & Pathogens |
| Rating Item | Low Risk 4 Points | Low-Moderate Risk 3 Points | Mod-High Risk 2 Points | High Risk 1 Point | Score |
| 1. Location | More than 200 feet from well and more than 500 feet from stream, pond, or drainageway | Between 100-200 feet of well and between 250-500 feet from stream, pond, or drainageway | Between 50-100 feet of well and between 100-250 feet from stream, pond, or drainageway | Less than 50 feet of well and less than 100 feet from stream, pond, or drainageway |  |
| 2. Livestock water source | Stock water in troughs, with overflow diverted to wastewater system | Stock water in troughs with overflow diverted from lot area. Stock excluded from streams or ditches. | Live water fenced, with stock water provided in water gap. | Stock water provided by live stream or irrigation ditch. |  |
| 3. Surface water diversion | All upslope and roof water diverted. Diversion and gutters well maintained. | Most upslope surface and roof water diverted. Diversions and gutters occasionally maintained. | No surface water diverted. Some roof water collected and redirected. Gutters and diversions not maintained. | All water (surface and roof water) runs through the yard. |  |
| 4. Lot runoff control system | No yard runoff. Fully covered area or runoff from surfaced lot directed to waste storage facility. | All runoff collected from compacted, earthen lot. Solids mounded and collected or stored. | Most of lot runoff diverted to filter strip and collected. Some solids removed. | Lot runoff uncontrolled. Solids rarely collected. |  |
| 5. Yard cleaning and scraping | No yard (animals confined) | Every month or two lot smoothed, leveled, and regularly shaped. | Quarterly. Lot rough and irregular in shape. | Rarely. Lot poorly sited and developed for cleaning and scraping. |  |
| 6. Dairy cow concentration on yard | No yard. Confined to barn, roofed yard or pasture. | 75 sf/a or more on fenced, curbed concrete pad and/or 400 sf/a on graded earthen surface. More than 1800 sf/a in exercise area. | 50 sf/a or more on concrete pad and/or 200-300 sf/a on earthen surface. More than 1200 sf/a in exercise area. | Some concrete, less than 50 sf/a and less than 200 sf/a on earthen surface. |  |
| 7. Dairy replacements concentration | No yard. Confined to barn, roofed yard, or pasture. | More than 40 sf/a on fenced, curbed concrete pad and/or more than 150 sf/a on earthen yard. | 40-20 sf/a on concrete and/or 75-150 sf/a on earthen surface. | Less than 75 sf/a on earth. |  |
| 8. Beef feeder concentrations | No yard. Confined to barn. | Barn and/or paved lot more than 50 sf/a. Earthen lot with mound more than 300 sf/a, or without mound more than 500 sf/a. | No shelter. Paved lot with 30-50 sf/a. Earthen lot with mound 150-300 sf/a or earthen without mound 250-500 sf/a. | Paved less than 30 sf/a. Earthen less than 250 sf/a. |  |
| 9. Beef cows/heifers concentrations | Barn, roofed yard, or pasture. | Barn with paved lot more than 60 sf/a. Earthen with mound 400 sf/a or without mound 600 sf/a. | Paved lot more than 30 sf/a. Earthen with mound 200-400 sf/a or without mound 300-600 sf/a. | Paved less than 30 sf/a. Earthen without mound less than 200 sf/a. |  |
| 10. Sheep/ewes concentrations | No yard. Confined to barn, roofed yard, or pasture. | Barn and paved lot more than 20 sf/a. Earthen more than 40 sf/a. | Barn and paved lot 15-20 sf/a. Earthen 25-40 sf/a. | Barn and paved lot less than 15 sf/a. Earthen less than 25 sf/a. |  |
| 11. Feeder lambs concentrations | No yard. Confined to barn, roofed yard, or pasture. | Barn and paved lot more than 10 sf/a. Earthen more than 25 sf/a. | Barn and paved lot 5-10 sf/a. Earthen 10-25 sf/a. | Barn and paved lot less than 5 sf/a. Earthen less than 10 sf/a. |  |
| Hogs/sows Concentrations | No yard. Confined to barn. | Shed and paved lot more than 30 sf/a. | Shed and earthen lot more than 10 sf/a | Shed and earthen lot less than 10 sf/a. |  |
| 13. Horses concentrations | No yard. Confined to barn, roofed yard, or pasture. | Earthen exercise lot more than 2,500 sf/a. | Earthen exercise lot 1,000-2,500 sf/a. | Earthen exercise lot less than 1,000 sf/a |  |
| 14. Poultry concentrations | No lot. In building. | . | Earthen lot of more than 4 sf/a. | Earthen lot of less than 4 sf/a. |  |
| Livestock Yard Rating | Accumulative Score (sum of above ratings) |  |
|  | Average Score (sum of ratings / number of items rated) |  |
| Overall Rating- |  |

Ratings:	3.6-4=Low risk, 2.6-3.6=Low to moderate risk, 1.6-2.5=Moderate to high risk, 1-1.5=High Risk

Note:  sf/a = square feet per animal

Source: Modification of Oregon Home*A*Syst, EM 8546, Worksheet #8, Livestock Yards Management